## Slide 1: 18-447 Computer Architecture Lecture 24: Memory Scheduling
Prof. Onur Mutlu
Presented by Justin Meza
Carnegie Mellon University
Spring 2014, 3/31/2014

## Slide 2: Last Two Lectures
Main Memory
  Organization and DRAM Operation
  Memory Controllers
DRAM Design and Enhancements
  More Detailed DRAM Design: Subarrays
  RowClone and In-DRAM Computation
  Tiered-Latency DRAM
Memory Access Scheduling
  FR-FCFS – row-hit-first scheduling

## Slide 3: Today
Row Buffer Management Policies
Memory Interference (and Techniques to Manage It)
  With a focus on Memory Request Scheduling

## Slide 4: Review: DRAM Scheduling Policies (I)
FCFS (first come first served)
  Oldest request first
FR-FCFS (first ready, first come first served)
  1. Row-hit first
  2. Oldest first
  Goal: Maximize row buffer hit rate  maximize DRAM throughput
  Actually, scheduling is done at the command level
    Column commands (read/write) prioritized over row commands (activate/precharge)
    Within each group, older commands prioritized over younger ones

## Slide 5: Review: DRAM Scheduling Policies (II)
A scheduling policy is essentially a prioritization order
Prioritization can be based on
  Request age
  Row buffer hit/miss status
  Request type (prefetch, read, write)
  Requestor type (load miss or store miss)
  Request criticality
    Oldest miss in the core?
    How many instructions in core are dependent on it?

## Slide 6: Row Buffer Management Policies
Open row
  Keep the row open after an access
  + Next access might need the same row  row hit
  -- Next access might need a different row  row conflict, wasted energy
Closed row
  Close the row after an access (if no other requests already in the request buffer need the same row)
  + Next access might need a different row  avoid a row conflict
  -- Next access might need the same row  extra activate latency
Adaptive policies
  Predict whether or not the next access to the bank will be to the same row

## Slide 7: Open vs. Closed Row Policies
Policy | First access | Next access | Commands needed for next access
Open row | Row 0 | Row 0 (row hit) | Read
Open row | Row 0 | Row 1 (row conflict) | Precharge + Activate Row 1 + Read
Closed row | Row 0 | Row 0 – access in request buffer (row hit) | Read
Closed row | Row 0 | Row 0 – access not in request buffer (row closed) | Activate Row 0 + Read + Precharge
Closed row | Row 0 | Row 1 (row closed) | Activate Row 1 + Read + Precharge

## Slide 8: Memory Interference and Scheduling in Multi-Core Systems

## Slide 9: Review: A Modern DRAM Controller

## Slide 10: Review: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 11: Scheduling Policy for Single-Core Systems
A row-conflict memory access takes significantly longer than a row-hit access
Current controllers take advantage of the row buffer
FR-FCFS (first ready, first come first served) scheduling policy
  1. Row-hit first
  2. Oldest first
  Goal 1: Maximize row buffer hit rate  maximize DRAM throughput
  Goal 2: Prioritize older requests  ensure forward progress
Is this a good policy in a multi-core system?

## Slide 12: Trend: Many Cores on Chip
Simpler and lower power than a single large core
Large scale parallelism on chip
IBM Cell BE 8+1 cores
Intel Core i7 8 cores
Tilera TILE Gx
100 cores, networked
IBM POWER7
8 cores
Intel SCC
48 cores, networked
Nvidia Fermi
448 “cores”
AMD Barcelona
4 cores
Sun Niagara II
8 cores

## Slide 13: Many Cores on Chip
What we want:
  N times the system performance with N times the cores
What do we get today?

## Slide 14: (Un)expected Slowdowns in Multi-Core
Low priority
High priority
(Core 0)
(Core 1)
Moscibroda and Mutlu, “Memory performance attacks: Denial of memory service
in multi-core systems,” USENIX Security 2007.
Notes: What kind of performance do we expect when we run two applications on a multi-core system? To answer this question, we performed an experiment. We took two applications we cared about, ran them together on different cores in a dual-core system, and measured their slowdown compared to when each is run alone on the same system. This graph shows the slowdown each app experienced. (DATA explanation…)
Why do we get such a large disparity in the slowdowns?
Is it the priorities? No. We went back and gave high priority to gcc and low priority to matlab. The slowdowns did not change at all. Neither the software or the hardware enforced the priorities.
Is it the contention in the disk? We checked for this possibility, but found that these applications did not have any disk accesses in the steady state. They both fit in the physical memory and therefore did not interfere in the disk.
What is it then? Why do we get such large disparity in slowdowns in a dual core system?
I will call such an application a “memory performance hog”
Now, let me tell you why this disparity in slowdowns happens.
Is it that there are other applications or the OS interfering with gcc, stealing its time quantums? No.

## Slide 15: Uncontrolled Interference: An Example
CORE 1
CORE 2
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
DRAM
Bank 0
DRAM
Bank 1
DRAM
Bank 2
Shared DRAM
Memory System
Multi-Core
Chip
unfairness
INTERCONNECT
stream
random
DRAM
Bank 3
Notes: -In a multi-core chip, different cores share some hardware resources. In particular, they share the DRAM memory system. The shared memory system consists of this and that.
When we run matlab on one core, and gcc on another core, both cores generate memory requests to access the DRAM banks. When these requests arrive at the DRAM controller, the controller favors matlab’s requests over gcc’s requests. As a result, matlab can make progress and continues generating memory requests. These requests are again favored by the DRAM controller over gcc’s requests. Therefore, gcc starves waiting for its requests to be serviced in DRAM whereas matlab makes very quick progress as if it were running alone.
Why does this happen? This is because the algorithms employed by the DRAM controller are unfair.
But, why are these algorithms unfair? Why do they unfairly prioritize matlab accesses?
To understand this, we need to understand how a DRAM bank operates.
Almost all systems today contain multi-core chips
Multi-core systems consist of multiple on-chip cores and caches
Cores share the DRAM memory system
DRAM memory system consists of
  DRAM banks that store data (multiple banks to allow parallel accesses)
  DRAM memory controller that mediates between cores and DRAM memory
    It schedules memory operations generated by cores to DRAM
This talk is about exploiting the unfair algorithms in the memory controllers to perform denial of service to running threads
To understand how this happens, we need to know about how each DRAM bank operates

## Slide 16: A Memory Performance Hog
// initialize large arrays A, B
for (j=0; j<N; j++) {
index = rand();
A[index] = B[index];
…
}
STREAM
Sequential memory access
Very high row buffer locality (96% hit rate)
Memory intensive
RANDOM
Random memory access
Very low row buffer locality (3% hit rate)
Similarly memory intensive
// initialize large arrays A, B
for (j=0; j<N; j++) {
index = j*linesize;
A[index] = B[index];
…
}
streaming
random
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: Streaming through memory by performing operations on two 1D arrays.
Sequential memory access
Each access is a cache miss (elements of array larger than a cache line size)  hence, very memory intensive
Link to the real code…

## Slide 17: What Does the Memory Hog Do?
Row Buffer
Row decoder
Column mux
Data
Row 0
T0: Row 0
Row 0
T1: Row 16
T0: Row 0
T1: Row 111
T0: Row 0
T0: Row 0
T1: Row 5
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
Memory Request Buffer
T0: STREAM
T1: RANDOM
Row size: 8KB, cache block size: 64B
128 (8KB/64B) requests of T0 serviced before T1
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: Pictorially demonstrate how stream denies memory service to rdarray
Stream continuously accesses columns in row 0 in a streaming manner (streams through a row after opening it)
In other words almost all its requests are row-hits
RDarray’s requests are row-conflicts (no locality)
The DRAM controller reorders streams requests to the open row over other requests (even older ones) to maximize DRAM throughput
Hence, rdarray’s requests do not get serviced as long as stream is issuing requests at a fast-enough rate
In this example, the red thread’s request to another row will not get serviced until stream stops issuing a request to row 0
With those parameters, 128 requests of stream would be serviced before 1 from rdarray
As row-buffer size increases, which is the industry trend, this problem will become more severe
This is not the worst case, but it is easy to construct and understand
  Stream falls off the row buffer at some point
I leave it to the listeners to construct a case worse than this (it is possible)

## Slide 18: Effect of the Memory Performance Hog
1.18X slowdown
2.82X slowdown
Results on Intel Pentium D running Windows XP
(Similar results for Intel Core Duo and AMD Turion, and on Fedora Linux)
Slowdown
Chart: 
| STREAM | gcc
Column1 | 1.23 | 2.91
Chart: 
| STREAM | Virtual PC
Column1 | 1.21 | 2.59
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.
Notes: RANDOM was given higher OS priority in the experiments

## Slide 19: Problems due to Uncontrolled Interference
Unfair slowdown of different threads
Low system performance
Vulnerability to denial of service
Priority inversion: unable to enforce priorities/SLAs
Cores make
very slow
progress
Memory performance hog
Low priority
High priority
Slowdown
Main memory is the only shared resource

## Slide 20: Problems due to Uncontrolled Interference
Unfair slowdown of different threads
Low system performance
Vulnerability to denial of service
Priority inversion: unable to enforce priorities/SLAs
Poor performance predictability (no performance isolation)
Uncontrollable, unpredictable system

## Slide 21: Inter-Thread Interference in Memory
Memory controllers, pins, and memory banks are shared
Pin bandwidth is not increasing as fast as number of cores
  Bandwidth per core reducing
Different threads executing on different cores interfere with each other in the main memory system
Threads delay each other by causing resource contention:
  Bank, bus, row-buffer conflicts  reduced DRAM throughput
Threads can also destroy each other’s DRAM bank parallelism
  Otherwise parallel requests can become serialized

## Slide 22: Effects of Inter-Thread Interference in DRAM
Queueing/contention delays
  Bank conflict, bus conflict, channel conflict, …
Additional delays due to DRAM constraints
  Called “protocol overhead”
  Examples
    Row conflicts
    Read-to-write and write-to-read delays
Loss of intra-thread parallelism
  A thread’s concurrent requests are serviced serially instead of in parallel

## Slide 23: Problem: QoS-Unaware Memory Control
Existing DRAM controllers are unaware of inter-thread interference in DRAM system
They simply aim to maximize DRAM throughput
  Thread-unaware and thread-unfair
  No intent to service each thread’s requests in parallel
  FR-FCFS policy: 1) row-hit first, 2) oldest first
    Unfairly prioritizes threads with high row-buffer locality
    Unfairly prioritizes threads that are memory intensive (many outstanding memory accesses)

## Slide 24: Solution: QoS-Aware Memory Request Scheduling
How to schedule requests to provide
  High system performance
  High fairness to applications
  Configurability to system software
Memory controller needs to be aware of threads
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 25: Stall-Time Fair Memory Scheduling
Onur Mutlu and Thomas Moscibroda, "Stall-Time Fair Memory Access Scheduling for Chip Multiprocessors" 40th International Symposium on Microarchitecture (MICRO),
pages 146-158, Chicago, IL, December 2007. Slides (ppt)
STFM Micro 2007 Talk

## Slide 26: The Problem: Unfairness
Vulnerable to denial of service
Unable to enforce priorities or service-level agreements
Low system performance
Uncontrollable, unpredictable system

## Slide 27: How Do We Solve the Problem?
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
Goal: Threads sharing main memory should experience similar slowdowns compared to when they are run alone  fair scheduling
  Also improves overall system performance by ensuring cores make “proportional” progress
Idea: Memory controller estimates each thread’s slowdown due to interference and schedules requests in a way to balance the slowdowns
Mutlu and Moscibroda, “Stall-Time Fair Memory Access Scheduling for Chip Multiprocessors,” MICRO 2007.

## Slide 28: Stall-Time Fairness in Shared DRAM Systems
A DRAM system is fair if it equalizes the slowdown of equal-priority threads relative to when each thread is run alone on the same system
DRAM-related stall-time: The time a thread spends waiting for DRAM memory
STshared: DRAM-related stall-time when the thread runs with other threads
STalone: DRAM-related stall-time when the thread runs alone
Memory-slowdown = STshared/STalone
  Relative increase in stall-time
Stall-Time Fair Memory scheduler (STFM) aims to equalize Memory-slowdown for interfering threads, without sacrificing performance
  Considers inherent DRAM performance of each thread
  Aims to allow proportional progress of threads
Notes: Memory-slowdown is the relative increase in the DRAM-related stall-time due to interference from other threads
For example, if a thread’s DRAM related stall time is 1 hour when running alone, and its stall-time is 2 hours when it runs together with other threads,
Its memory-slowdown is said to be 2.
Give an example at the end: If a thread waits for DRAM 1 hour running by itself and this increases to 2 hours (its slowdown is 2), then a thread that waits for DRAM 2 hours, should now wait for DRAM 4 hours.
Each thread experiences the same slowdown compared to its baseline DRAM performance
The amount of time a thread spends waiting for DRAM memory
Extra time a thread requires to run because DRAM access is not instant
PROPORTIONALITY: Each thread makes the same amount of progress relative to its baseline performance. This is consistent with priority based scheduling mechanisms that allocate the same time quantum for equal-priority threads.
We define two values to compute slowdown.
Proportional slowdown (proportionate progress)
  Fairness notion similar to SMT [Cazorla, IEEE Micro’04][Luo, ISPASS’01], SoEMT [Gabor, Micro’06], and shared caches [Kim, PACT’04]

## Slide 29: STFM Scheduling Algorithm [MICRO’07]
For each thread, the DRAM controller
  Tracks STshared
  Estimates STalone
Each cycle, the DRAM controller
  Computes Slowdown = STshared/STalone for threads with legal requests
  Computes unfairness = MAX Slowdown / MIN Slowdown
If unfairness < 
  Use DRAM throughput oriented scheduling policy
If unfairness ≥ 
  Use fairness-oriented scheduling policy
    (1) requests from thread with MAX Slowdown first
    (2) row-hit first , (3) oldest-first
Notes: Except for pathological cases, best achievable unfairness value is 1
Maximizes DRAM throughput if it cannot improve fairness
WORK CONSERVING: Does not waste useful bandwidth to improve fairness
    If a request does not interfere with any other, it is scheduled

## Slide 30: How Does STFM Prevent Unfairness?
Row Buffer
Data
Row 0
T0: Row 0
Row 0
T1: Row 16
T0: Row 0
T1: Row 111
T0: Row 0
T0: Row 0
T1: Row 5
T0: Row 0
T0: Row 0
T0: Row 0
T0 Slowdown
T1 Slowdown
1.00
1.00
1.00
Unfairness
1.03
1.03
1.06
1.06

1.05
1.03
1.06
1.03
1.04
1.08
1.04
1.04
1.11
1.06
1.07
1.04
1.10
1.14
1.03
Row 16
Row 111
Notes: A pictorial example of how our solution prevents stream from being a memory performance hog
Our technique requires the DRAM controller to keep track of slowdowns for each thread and the unfairness value based on these slowdowns
Alpha parameter (maximum tolerable unfairness until the fairness-oriented scheduling policy kicks in) is set to 1.05 in this example
As stream’s requests are prioritized over rdarray’s, rdarray’s slowdown increases and hence unfairness increases
Once unfairness crosses the alpha value, our algorithm kicks in and uses the fairness-oriented scheduling policy
This policy prioritizes requests from the thread with the maximum slowdown (rdarray – thread 1)
Hence, rdarray’s requests do not indefinitely starve
Servicing rdarray’s request increases stream’s slowdown and keeps in check rdarray’s slowdown (thus reduces unfairness)
Therefore, when unfairness becomes tolerable again, our algorithm switches back to the baseline scheduling policy to maximize throughput (i.e. it schedules stream’s row hit requests first, and then the oldest requests)

## Slide 31: STFM Pros and Cons
Upsides:
  First algorithm for fair multi-core memory scheduling
  Provides a mechanism to estimate memory slowdown of a thread
  Good at providing fairness
  Being fair can improve performance
Downsides:
  Does not handle all types of interference
  (Somewhat) complex to implement
  Slowdown estimations can be incorrect

## Slide 32: Parallelism-Aware Batch Scheduling
Onur Mutlu and Thomas Moscibroda, "Parallelism-Aware Batch Scheduling: Enhancing both
Performance and Fairness of Shared DRAM Systems” 35th International Symposium on Computer Architecture (ISCA),
pages 63-74, Beijing, China, June 2008. Slides (ppt)
PAR-BS ISCA 2008 Talk

## Slide 33: Another Problem due to Interference
Processors try to tolerate the latency of DRAM requests by generating multiple outstanding requests
  Memory-Level Parallelism (MLP)
  Out-of-order execution, non-blocking caches, runahead execution
Effective only if the DRAM controller actually services the multiple requests in parallel in DRAM banks
Multiple threads share the DRAM controller
DRAM controllers are not aware of a thread’s MLP
  Can service each thread’s outstanding requests serially, not in parallel
Notes: Modern processors try to amortize the latency of DRAM requests by generating multiple outstanding requests
This concept is called memory-level parallelism.
Many techniques, such as OOO, non-blocking caches and runahead execution, are designed or used to tolerate long memory latencies by exploiting memory-level parallelism
These latency tolerance techniques are effective only if the DRAM controller actually services the multiple requests of a thread in parallel in DRAM banks
This is true in a single-threaded system since only one thread has exclusive access to all DRAM banks.
However, in a multi-core system, multiple threads share the DRAM controller.
Unfortunately, existing DRAM controllers are not aware of each thread’s memory level parallelism
As a result they can service each thread’s outstanding requests serially, not in parallel
Let’s take a look at why this happens.
-----------------------------------------
Assuming requests are to different banks
In a single core system this is fine because only one thread has exclusive access to all DRAM banks.
However, in a multi-core system, multiple threads shared the DRAM controller.
Unfortunately, DRAM controllers are unaware of a thread’s MLP. As a result, because threads can interfere with each other in the DRAM system, they can service each thread’s requests serially instead of in parallel.
Let’s take a look at why this happens.

## Slide 34: Bank Parallelism of a Thread
Thread A: Bank 0, Row 1
Thread A: Bank 1, Row 1
Bank access latencies of the two requests overlapped
Thread stalls for ~ONE bank access latency
Thread A :
Bank 0
Bank 1
Compute
2 DRAM Requests
Bank 0
Stall
Compute
Bank 1
Single Thread:
Notes: I will demonstrate this pictorially with an example.
Let’s say a thread A executes until it encounters 2 DRAM requests caused by two of its load instructions. These requests are sent to the DRAM controller. And, the controller services them by first scheduling the request to Bank 0 and then scheduling the request to Bank 1. While the requests are being serviced in parallel in the banks, the thread stalls (waiting for the data). Once the servicing of the requests completes, the thread can continue execution.
Since the requests were serviced in parallel in the two banks, bank access latencies of the two requests are overlapped. As a result, the thread stalls for approximately one bank access latency, instead of two bank access latencies.

## Slide 35: Bank Parallelism Interference in DRAM
Compute
Compute
2 DRAM Requests
Bank 0
Bank 1
Thread A: Bank 0, Row 1
Thread B: Bank 1, Row 99
Thread B: Bank 0, Row 99
Thread A: Bank 1, Row 1
A :
Compute
2 DRAM Requests
Bank 0
Stall
Bank 1
Baseline Scheduler:
B:
Compute
Bank 0
Stall
Bank 1
Stall
Stall
Bank access latencies of each thread serialized
Each thread stalls for ~TWO bank access latencies
Notes: What happens when we run two of these threads together in a dual-core system? Again, both threads execute until each encounters 2 DRAM requests. These requests are sent to the DRAM controller. Assume they arrive in the order shown. And the controller services them in the order they arrive.
The controller first takes Thread A’s request to Bank 0 and schedules it. It then schedules Thread B’s request to Bank 1. While these two requests are serviced in parallel, both threads stall.
Once the first request to Bank 0 is done, the controller takes Thread B’s request to bank 0 and schedules it. And it takes Thread A’s request to Bank 1 and schedules it. While these two requests are serviced in parallel, both threads stall.
Once the requests are complete, the threads continue computation.
In this case, because the threads’ requests interfered with each other in the DRAM system, the bank access latencies of each thread were serialized because the requests were serialized. As a result both threads stall for two bank access latencies instead of 1, which is what each thread experienced when running alone.
This is because the DRAM controller did not try to preserve the bank parallelism of each thread.

## Slide 36: Parallelism-Aware Scheduler
2 DRAM Requests
Bank 0
Bank 1
Thread A: Bank 0, Row 1
Thread B: Bank 1, Row 99
Thread B: Bank 0, Row 99
Thread A: Bank 1, Row 1
A :
2 DRAM Requests
Parallelism-aware Scheduler:
B:
Compute
Bank 0
Stall
Compute
Bank 1
Stall
2 DRAM Requests
A :
Compute
2 DRAM Requests
Bank 0
Stall
Compute
Bank 1
B:
Compute
Bank 0
Stall
Compute
Bank 1
Stall
Stall
Baseline Scheduler:
Compute
Bank 0
Stall
Compute
Bank 1
Saved Cycles
Average stall-time: ~1.5 bank access latencies
Notes: Can we do better than this? Let me describe what a parallelism aware scheduler would do.
This is the same example. The two threads compute until they each generate 2 DRAM requests, which arrive at the controller in the same order as before. The controller first takes Thread A’s request to Bank 0 and schedules it. But then, instead of servicing the requests in their arrival order, it realizes there is another request from Thread A to Bank 1 and if it schedules that one back to back with Thread A’s previous request, thread A’s request latencies would be overlapped.
Therefore, the controller takes Thread A’s request to Bank 1 and schedules it. While these two requests are serviced in parallel in the banks, both threads stall.
Once the request to Bank 0 is complete, the controller takes Thread B’s request to Bank 0 and schedules it. Later, it schedules Thread B’s request to Bank 1. While these two requests are being serviced, Thread B stalls (because it does not have the data it needs), but thread A can do useful computation! This is because its requests were serviced in parallel in the banks, instead of serially, and the thread has all the data it needs to do useful computation. As a result, the execution time of Thread A reduces compared to the baseline scheduler that was not aware of the threads’ bank parallelism.
Overall system throughput also improves because the average stall-time of the threads is 1.5 bank access latencies instead of 2. Instead of stalling, cores can make progress executing their instruction streams.

## Slide 37: Parallelism-Aware Batch Scheduling (PAR-BS)
Principle 1: Parallelism-awareness
  Schedule requests from a thread (to different banks) back to back
  Preserves each thread’s bank parallelism
  But, this can cause starvation…
Principle 2: Request Batching
  Group a fixed number of oldest requests from each thread into a “batch”
  Service the batch before all other requests
  Form a new batch when the current one is done
  Eliminates starvation, provides fairness
  Allows parallelism-awareness within a batch
Bank 0
Bank 1
T1
T1
T0
T0
T2
T2
T3
T3
T2
T2
T2
Batch
T0
T1
T1
  Mutlu and Moscibroda, “Parallelism-Aware Batch Scheduling,” ISCA 2008.
Notes: Parallelism aware batch scheduling uses two key principles. The first principle is parallelism awareness. As I showed you before, a thread’s bank parallelism is improved by scheduling requests from a thread to different banks back to back. Unfortunately, doing this greedily can cause starvation because a thread whose requests are continuously scheduled back to back can keep on generating more requests and therefore deny service to other threads that are waiting to access the same bank.
  To avoid this, we use a second principle, called request batching. With this, the controller groups a fixed number of oldest requests from each thread into a “batch”. And, it services the batch before all other requests. It forms a new batch when the current one is done.
  Batching eliminates starvation of requests and threads, and provides fairness. It also allows parallelism of each thread to be optimized for within a batch.
  Let’s take a look at how this works pictorially.
  Multiple threads send requests to the DRAM controller. The controller groups these requests into a batch. Once a batch is formed any newly arriving requests are not included in the batch. Within the batch, the controller schedules each thread’s requests in parallel. It first takes TX’s requests and schedules them in parallel. Then it takes TY’s requests and schedules them in parallel. Note that incoming requests from T3 that are outside the batch are not serviced. Once all requests in the batch are serviced in a parallelism-aware manner, the controller forms a new batch with the requests in the memory request buffer.

## Slide 38: PAR-BS Components
Request batching
Within-batch scheduling
  Parallelism aware
Notes: PAR-BS has two components, which I will describe in more detail. The first is request batching. Aside from guaranteeing starvation freedom and providing fairness, a batch provides a flexible substrate that enables aggressive scheduling optimizations (within the batch).
The second component is the within-batch scheduling component. Within a batch, any DRAM scheduling policy can be employed. And, this policy can be very aggressive and possibly unfair in the global sense. Because the overlying batching scheme ensures forward progress in each thread. In fact, we use a globally unfair shortest job first scheduling policy within a batch, to optimize each thread’s bank parallelism.

## Slide 39: Request Batching
Each memory request has a bit (marked) associated with it
Batch formation:
  Mark up to Marking-Cap oldest requests per bank for each thread
  Marked requests constitute the batch
  Form a new batch when no marked requests are left
Marked requests are prioritized over unmarked ones
  No reordering of requests across batches: no starvation, high fairness
How to prioritize requests within a batch?
Notes: To implement batching, Each memory request has a bit (called the marked bit) associated with it
When a batch is formed, the controller marks up to a Marking-Cap pending requests per bank for each thread. Marked requests constitute the batch. A new batch is formed when no marked requests are left.
  The key idea is that marked requests are always prioritized over unmarked ones. Hence, there is no reordering of requests across batches: As a result, there is no starvation, and a high degree of fairness.
  But how does the controller prioritize requests within a batch?

## Slide 40: Within-Batch Scheduling
Can use any existing DRAM scheduling policy
  FR-FCFS (row-hit first, then oldest-first) exploits row-buffer locality
But, we also want to preserve intra-thread bank parallelism
  Service each thread’s requests back to back
Scheduler computes a ranking of threads when the batch is formed
  Higher-ranked threads are prioritized over lower-ranked ones
  Improves the likelihood that requests from a thread are serviced in parallel by different banks
    Different threads prioritized in the same order across ALL banks
HOW?
Notes: Within a batch, the controller can use any existing DRAM scheduling policy. For example, the baseline FR-FCFS policy is very good at exploiting row buffer locality.
However, in addition to exploiting row-buffer locality, we also want to preserve intra-thread bank parallelism. As I showed you before, this can be accomplished by servicing each thread’s requests back to back
To do so, the DRAM scheduler computes a ranking of threads when the batch is formed
And it prioritizes requests that belong to higher-ranked threads over those that belong to lower ranked ones
  This Improves the likelihood that requests from a thread are serviced in parallel by different banks
  Because Different threads prioritized in the same order (the RANK ORDER) across ALL banks
But how does the scheduler compute this ranking?

## Slide 41: How to Rank Threads within a Batch
Ranking scheme affects system throughput and fairness
Maximize system throughput
  Minimize average stall-time of threads within the batch
Minimize unfairness (Equalize the slowdown of threads)
  Service threads with inherently low stall-time early in the batch
  Insight: delaying memory non-intensive threads results in high slowdown
Shortest stall-time first (shortest job first) ranking
  Provides optimal system throughput [Smith, 1956]*
  Controller estimates each thread’s stall-time within the batch
  Ranks threads with shorter stall-time higher
* W.E. Smith, “Various optimizers for single stage production,” Naval Research Logistics Quarterly, 1956.
Notes: The thread ranking scheme affects system throughput and fairness
A good ranking scheme should achieve two objectives.
First, it should maximize system throughput
Second, it should minimize unfairness; in other words it should balance the slowdown of the threads compared to when each is run alone.
These two objectives call for the same ranking scheme, as I will show soon.
Maximizing system throughput is achieved by minimizing the average stall-time of the threads within the batch (as I showed in the earlier example). By minimizing the average stall time, we maximize the amount of time the system spends on computation rather than waiting for DRAM accesses.
Minimizing unfairness is achieved by servicing threads with inherently low stall-time early in the batch, The insight is that if a thread has low stall time to begin with (if it is not intensive) delaying that thread would result in very high slowdown compared to delaying a memory-intensive thread.
To achieve both objectives, we use the “shortest job first” principle. Shortest job first scheduling has been proven to provide the optimal throughput in generalized machine scheduling theory. The controller estimates each thread’s stall-time within the batch (assuming the thread is run alone). And, it ranks a thread higher if the thread has a short stall time.

## Slide 42: Shortest Stall-Time First Ranking
Maximum number of marked requests to any bank (max-bank-load)
  Rank thread with lower max-bank-load higher (~ low stall-time)
Total number of marked requests (total-load)
  Breaks ties: rank thread with lower total-load higher
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
 | max-bank-load | total-load
T0 | 1 | 3
T1 | 2 | 4
T2 | 2 | 6
T3 | 5 | 9
Ranking:
T0 > T1 > T2 > T3
Notes:     How is this exactly done? The controller keeps track of two values for each thread. First, the maximum number of marked requests from the thread to any bank. This is called max-bank-load. A lower value of this correlates with low stall time (and less memory intensiveness). As a result the scheduler ranks a thread with lower max-bank-load higher than a thread with higher max-bank load.
    If the max-bank-load of the two threads are equal, the scheduler uses another value it keeps track of to break the ties. It keeps the total number of requests in the batch from each thread. This is called total-load. If a thread has lower total-load it is less intensive, therefore it is ranked higher.
    Let’s take a look at these concepts with an example. Assume these are the requests within the batch.
    T0 has at most 1 request to any bank, so its max-bank-load is 1. Its total-load is 3 since it has total 3 marked requests.
    T1 has at most 2 requests to any bank so its max-bank-load is 2. Its total load is 6.
    T2 similarly has a max-bank-load of 2, but its total load is higher.
    Finally, T3 has a maximum of 5 requests to Bank 3. Therefore, its max-bank load is 5.
    Because T1 has the smallest max-bank-load, it is ranked highest. The scheduler ranks T1 higher than T2 because T1 has fewer total requests. The most memory intensive thread, T2 is ranked the lowest.
    ----------------------------
    Insight: Memory-intensive threads can be delayed more within a batch since their baseline stall-time is high
    How do you break the ties? A thread with lower total-load is ranked higher
    Goal: Finish non-intensive threads first and fill in the gaps in parallelism as much as possible
    Shortest job first within a batch might seem unfair, but remember the batch boundaries. Less intensive threads will be penalized across batches because if their requests are not marked, they cannot be serviced. Shortest job first balances this delay caused to the less intensive threads
Thread 0 has at most one request to any bank
Thread 1 has at most 2: it has two requests to Bank 0.
Thread 2 has at most 2 as well.
Thread 3 has max number of requests to Bank 3 (5 reqs)

## Slide 43: Example Within-Batch Scheduling Order
7
5
3
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
Baseline Scheduling
Order (Arrival order)
PAR-BS Scheduling
Order
T2
T3
T1
T0
Bank 0
Bank 1
Bank 2
Bank 3
T3
T3
T1
T3
T2
T2
T1
T2
T1
T0
T2
T0
T3
T2
T3
T3
T3
T3
T0 | T1 | T2 | T3
4 | 4 | 5 | 7
AVG: 5 bank access latencies
AVG: 3.5 bank access latencies
Stall times
T0 | T1 | T2 | T3
1 | 2 | 4 | 7
Stall times
Time
1
2
4
6
Ranking: T0 > T1 > T2 > T3
1
2
3
4
5
6
7
Time
Notes: How does this ranking affect the scheduling order? Let’s take a look at this pictorially.
First, let’s look at the baseline scheduler. I will show the time at which the requests are serviced, where time is expressed abstractly in terms of bank access latency. In the baseline scheduler, the batched requests are serviced in their arrival order. As a result, the last request of T0 is serviced after 4 bank access latencies, the last request of T1 is also serviced after 4 bank access latencies. Consequently, the average stall time of the threads is approximately 5 bank access latencies within this batch of requests.
If we use PAR-BS to rank the threads, the scheduler will prioritize requests based on their thread-rank order, which I showed before. It prioritizes T0’s requests first (as shown in the ranking order). As a result, T0’s requests complete after 1 bank access latency. T1’s requests are serviced after 2 bank access latencies. T2’s requests are serviced after 4 bank access latencies.
Note that the bank parallelism of each thread is preserved as much as possible. Because of this, the average stall time reduces by 30%. Thus, system throughput improves.
Also note that, to keep this example simple, I assumed there are no row-buffer hits. A more complicated example with row-buffer hits is provided in the paper, and I encourage you to look at it.
--------------------------------------
Time is in bank access latencies (note that this is an approximation to demonstrate the idea… real DRAM system is much more complex than this…)
Last request from a thread is scheduled at TIME

## Slide 44: Putting It Together: PAR-BS Scheduling Policy
PAR-BS Scheduling Policy
  (1) Marked requests first
  (2) Row-hit requests first
  (3) Higher-rank thread first (shortest stall-time first)
  (4) Oldest first
Three properties:
  Exploits row-buffer locality and intra-thread bank parallelism
  Work-conserving
    Services unmarked requests to banks without marked requests
  Marking-Cap is important
    Too small cap: destroys row-buffer locality
    Too large cap: penalizes memory non-intensive threads
Mutlu and Moscibroda, “Parallelism-Aware Batch Scheduling,” ISCA 2008.
Batching
Parallelism-aware
within-batch
scheduling
Notes: The resulting scheduling policy of our mechanism is based on four simple prioritization rules.
Marked requests are prioritized over others. This is the batching component.
Within a batch, row-hit requests are prioritized over others to exploit row-buffer locality (as in FR-FCFS). Then, higher-ranked threads’ requests are prioritized over lower ranked threads’ requests (to preserve each thread’s bank parallelism). Finally all else being equal, older requests are prioritized over others.
This scheduling policy has three properties.
First, it exploits both row-buffer locality and intra-thread bank parallelism. I assumed no row buffer hits in the previous example, to keep it simple, but this is taken into account in our scheduling algorithm. There is a balance between exploiting row buffer locality and bank parallelism, and our scheduling algorithm tries to achieve this balance. An example with row hits is provided in the paper.
Second, it is work conserving. It services unmarked requests in banks without marked requests.
Third, and I will not go into much detail on this, Marking-Cap is the most important parameter. Remember that the Marking-Cap determines how many requests from each thread to each bank can be admitted into a batch. If the cap is too small, too few requests from each thread are admitted into the batch. As a result, a thread’s row buffer locality cannot be exploited. If the cap is too large too many requests from intensive threads enter the batch, which slows down non-intensive threads.
Many other similar trade-offs are analyzed in the paper and I encourage you to read it.

## Slide 45: Hardware Cost
<1.5KB storage cost for
  8-core system with 128-entry memory request buffer
No complex operations (e.g., divisions)
Not on the critical path
  Scheduler makes a decision only every DRAM cycle
Notes: The implementation of PAR-BS is relatively simple. It requires three pieces of logic. Marking logic and thread ranking logic are utilized only when a new batch is formed. Extensions to request prioritization logic are needed to take into account the marked status and the thread-rank of each request.
There are no complex operations and the logic is not on the critical path of execution.
Our implementation requires less than 1.5KB storage cost within a reasonably large system with 8 cores.
More details are provided in the paper.

## Slide 46: Unfairness on 4-, 8-, 16-core Systems
Unfairness = MAX Memory Slowdown / MIN Memory Slowdown [MICRO 2007]
Notes: This graph compares the five schedulers in terms of unfairness averaged over all workloads run on the 4, 8, and 16 core systems. Unfairness is computed as the max memory slowdown in the system divided by the minimum memory slowdown in the system. PAR-BS reduces unfairness significantly compared to the best previous scheduler, STFM, on all systems.
We conclude that the combination of batching and shortest stall-time first within batch scheduling provides good fairness without the need to explicitly estimate each thread’s slowdown and adjust scheduling policy based on that.

## Slide 47: System Performance
Notes: This graph compares the system performance provided by the five schedulers. Performance is normalized to that of the baseline FR-FCFS scheduler. PAR-BS also improves system performance compared to the best previous scheduler, STFM, on all systems. In the 4-core system, PAR-BS provides an 8.3% performance improvement. The main reason is that PAR-BS improves each thread’s bank level parallelism: as a result, it reduces the average stall time per each request by 7.1% in the four core system (from 301 cycles to 281 cycles)

## Slide 48: PAR-BS Pros and Cons
Upsides:
  First scheduler to address bank parallelism destruction across multiple threads
  Simple mechanism (vs. STFM)
  Batching provides fairness
  Ranking enables parallelism awareness
Downsides:
  Implementation in multiple controllers needs coordination for best performance  too frequent coordination since batching is done frequently
  Does not always prioritize the latency-sensitive applications