## Slide 1: 18-447 Computer Architecture Lecture 14: Out-of-Order Execution (Dynamic Instruction Scheduling)
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2014, 2/19/2014

## Slide 2: Announcements
Lab due Friday (Feb 21)
Homework 3 due next Wednesday (Feb 26)
Exam coming up (before Spring Break)

## Slide 3: Reminder: Lab Late Day Policy Adjustment
Your total late days have increased to 7
Each late day beyond all exhausted late days costs you 15% of the full credit of the lab

## Slide 4: Reminder: A Note on Testing Your Code
Testing is critical in developing any system
You are responsible for creating your own test programs and ensuring your designs work for all possible cases
That is how real life works also…
  Noone gives you all possible test cases, workloads, users, etc. beforehand

## Slide 5: Lab 2 Grade Distribution
Chart: Lab 2 Grade Distribution
| 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
 | 11 | 0 | 0 | 0 | 0 | 0 | 2 | 5 | 4 | 18 | 1

## Slide 6: Lab 2 Statistics
MAX 99.62
MIN 62.74
MEDIAN 92.59
MEAN 89.26
STD 10.21

## Slide 7: HW 2 Grade Distribution
Chart: HW 2 Grade Distribution
| 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
 | 1 | 0 | 1 | 0 | 0 | 4 | 2 | 3 | 5 | 22 | 4

## Slide 8: HW 2 Statistics
MAX 100
MIN 0
MEDIAN 92.98
MEAN 81.98
STD 24.82

## Slide 9: Readings for Past Few Lectures (I)
P&H Chapter 4.9-4.11
Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proceedings of the IEEE, 1995
  More advanced pipelining
  Interrupt and exception handling
  Out-of-order and superscalar execution concepts
McFarling, “Combining Branch Predictors,” DEC WRL Technical Report, 1993.
Kessler, “The Alpha 21264 Microprocessor,” IEEE Micro 1999.

## Slide 10: Readings for Past Few Lectures (II)
Smith and Plezskun, “Implementing Precise Interrupts in Pipelined Processors,” IEEE Trans on Computers 1988 (earlier version in ISCA 1985).

## Slide 11: Readings Specifically for Today
Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proceedings of the IEEE, 1995
  More advanced pipelining
  Interrupt and exception handling
  Out-of-order and superscalar execution concepts
Kessler, “The Alpha 21264 Microprocessor,” IEEE Micro 1999.

## Slide 12: Readings for Next Lecture
SIMD Processing
Basic GPU Architecture
Other execution models: VLIW, Dataflow
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.
Fatahalian and Houston, “A Closer Look at GPUs,” CACM 2008.
Stay tuned for more readings…

## Slide 13: Maintaining Precise State
Reorder buffer
History buffer
Future register file
Checkpointing
Readings
  Smith and Plezskun, “Implementing Precise Interrupts in Pipelined Processors,” IEEE Trans on Computers 1988 and ISCA 1985.
  Hwu and Patt, “Checkpoint Repair for Out-of-order Execution Machines,” ISCA 1987.

## Slide 14: Registers versus Memory
So far, we considered mainly registers as part of state
What about memory?
What are the fundamental differences between registers and memory?
  Register dependences known statically – memory dependences determined dynamically
  Register state is small – memory state is large
  Register state is not visible to other threads/processors – memory state is shared between threads/processors (in a shared memory multiprocessor)

## Slide 15: Maintaining Speculative Memory State: Stores
Handling out-of-order completion of memory operations
  UNDOing a memory write more difficult than UNDOing a register write. Why?
  One idea: Keep store address/data in reorder buffer
    How does a load instruction find its data?
  Store/write buffer: Similar to reorder buffer, but used only for store instructions
    Program-order list of un-committed store operations
    When store is decoded: Allocate a store buffer entry
    When store address and data become available: Record in store buffer entry
    When the store is the oldest instruction in the pipeline: Update the memory address (i.e. cache) with store data

## Slide 16: Out-of-Order Execution (Dynamic Instruction Scheduling)

## Slide 17: An In-order Pipeline
Problem: A true data dependency stalls dispatch of younger instructions into functional (execution) units
Dispatch: Act of sending an instruction to a functional unit
F
D
E
R
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Cache miss
W

## Slide 18: Can We Do Better?
What do the following two pieces of code have in common (with respect to execution in the previous design)?
Answer: First ADD stalls the whole pipeline!
  ADD cannot dispatch because its source registers unavailable
  Later independent instructions cannot get executed
How are the above code portions different?
  Answer: Load latency is variable (unknown until runtime)
  What does this affect? Think compiler vs. microarchitecture
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R9, R9
LD R3  R1 (0)
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R9, R9

## Slide 19: Preventing Dispatch Stalls
Multiple ways of doing it
You have already seen THREE:
  1. Fine-grained multithreading
  2. Value prediction
  3. Compile-time instruction scheduling/reordering
What are the disadvantages of the above three?
Any other way to prevent dispatch stalls?
  Actually, you have briefly seen the basic idea before
    Dataflow: fetch and “fire” an instruction when its inputs are ready
  Problem: in-order dispatch (scheduling, or execution)
  Solution: out-of-order dispatch (scheduling, or execution)

## Slide 20: Out-of-order Execution (Dynamic Scheduling)
Idea: Move the dependent instructions out of the way of independent ones
  Rest areas for dependent instructions: Reservation stations
Monitor the source “values” of each instruction in the resting area
When all source “values” of an instruction are available, “fire” (i.e. dispatch) the instruction
  Instructions dispatched in dataflow (not control-flow) order
Benefit:
  Latency tolerance: Allows independent instructions to execute and complete in the presence of a long latency operation

## Slide 21: In-order vs. Out-of-order Dispatch
In order dispatch + precise exceptions:
Out-of-order dispatch + precise exceptions:
16 vs. 12 cycles
F
D
W
E
E
E
E
R
F
D
E
R
W
F
IMUL R3  R1, R2
ADD R3  R3, R1
ADD R1  R6, R7
IMUL R5  R6, R8
ADD R7  R3, R5
D
E
R
W
F
D
E
R
W
F
D
E
R
W
F
D
W
E
E
E
E
R
F
D
STALL
STALL
E
R
W
F
D
E
E
E
E
STALL
E
R
F
D
E
E
E
E
R
W
F
D
E
R
W
WAIT
WAIT
W

## Slide 22: Enabling OoO Execution
1. Need to link the consumer of a value to the producer
  Register renaming: Associate a “tag” with each data value
2. Need to buffer instructions until they are ready to execute
  Insert instruction into reservation stations after renaming
3. Instructions need to keep track of readiness of source values
  Broadcast the “tag” when the value is produced
  Instructions compare their “source tags” to the broadcast tag  if match, source value becomes ready
4. When all source values of an instruction are ready, need to dispatch the instruction to its functional unit (FU)
  Instruction wakes up if all sources are ready
  If multiple instructions are awake, need to select one per FU

## Slide 23: Tomasulo’s Algorithm
OoO with register renaming invented by Robert Tomasulo
  Used in IBM 360/91 Floating Point Units
  Read: Tomasulo, “An Efficient Algorithm for Exploiting Multiple Arithmetic Units,” IBM Journal of R&D, Jan. 1967.
What is the major difference today?
  Precise exceptions: IBM 360/91 did NOT have this
  Patt, Hwu, Shebanow, “HPS, a new microarchitecture: rationale and introduction,” MICRO 1985.
  Patt et al., “Critical issues regarding HPS, a high performance microarchitecture,” MICRO 1985.
Variants used in most high-performance processors
  Initially in Intel Pentium Pro, AMD K5
  Alpha 21264, MIPS R10000, IBM POWER5, IBM z196, Oracle UltraSPARC T4, ARM Cortex A15

## Slide 24: Two Humps in a Modern Pipeline
Hump 1: Reservation stations (scheduling window)
Hump 2: Reordering (reorder buffer, aka instruction window or active window)
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
E
O
R
D
E
R
S
C
H
E
D
U
L
E
TAG and VALUE Broadcast Bus
in order
out of order
in order

## Slide 25: General Organization of an OOO Processor
  Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proc. IEEE, Dec. 1995.

## Slide 26: Tomasulo’s Machine: IBM 360/91
FP FU
FP FU
from memory
load
buffers
from instruction unit
FP registers
store buffers
to memory
operation bus
reservation
stations
Common data bus

## Slide 27: Register Renaming
Output and anti dependencies are not true dependencies
  WHY? The same register refers to values that have nothing to do with each other
  They exist because not enough register ID’s (i.e. names) in the ISA
The register ID is renamed to the reservation station entry that will hold the register’s value
  Register ID  RS entry ID
  Architectural register ID  Physical register ID
  After renaming, RS entry ID used to refer to the register
This eliminates anti- and output- dependencies
  Approximates the performance effect of a large number of registers even though ISA has a small number

## Slide 28: Tomasulo’s Algorithm: Renaming
Register rename table (register alias table)
R0
R1
R2
R3
tag
value
valid?
R4
R5
R6
R7
R8
R9
1
1
1
1
1
1
1
1
1
1

## Slide 29: Tomasulo’s Algorithm
If reservation station available before renaming
  Instruction + renamed operands (source value/tag) inserted into the reservation station
  Only rename if reservation station is available
Else stall
While in reservation station, each instruction:
  Watches common data bus (CDB) for tag of its sources
  When tag seen, grab value for the source and keep it in the reservation station
  When both operands available, instruction ready to be dispatched
Dispatch instruction to the Functional Unit when instruction is ready
After instruction finishes in the Functional Unit
  Arbitrate for CDB
  Put tagged value onto CDB (tag broadcast)
  Register file is connected to the CDB
    Register contains a tag indicating the latest writer to the register
    If the tag in the register file matches the broadcast tag, write broadcast value into register (and set valid bit)
  Reclaim rename tag
    no valid copy of tag in system!

## Slide 30: An Exercise
Assume ADD (4 cycle execute), MUL (6 cycle execute)
Assume one adder and one multiplier
How many cycles
  in a non-pipelined machine
  in an in-order-dispatch pipelined machine with imprecise exceptions (no forwarding and full forwarding)
  in an out-of-order dispatch pipelined machine imprecise exceptions (full forwarding)
MUL R3  R1, R2
ADD R5  R3, R4
ADD R7  R2, R6
ADD R10  R8, R9
MUL R11  R7, R10
ADD R5  R5, R11
F
D
E
W

## Slide 31: Exercise Continued

## Slide 32: Exercise Continued

## Slide 33: Exercise Continued
MUL R3  R1, R2
ADD R5  R3, R4
ADD R7  R2, R6
ADD R10  R8, R9
MUL R11  R7, R10
ADD R5  R5, R11

## Slide 34: How It Works

## Slide 35: Cycle 0

## Slide 36: Cycle 2

## Slide 37: Cycle 3

## Slide 38: Cycle 4

## Slide 39: Cycle 7

## Slide 40: Cycle 8

## Slide 41: An Exercise, with Precise Exceptions
Assume ADD (4 cycle execute), MUL (6 cycle execute)
Assume one adder and one multiplier
How many cycles
  in a non-pipelined machine
  in an in-order-dispatch pipelined machine with reorder buffer (no forwarding and full forwarding)
  in an out-of-order dispatch pipelined machine with reorder buffer (full forwarding)
MUL R3  R1, R2
ADD R5  R3, R4
ADD R7  R2, R6
ADD R10  R8, R9
MUL R11  R7, R10
ADD R5  R5, R11
F
D
E
R
W

## Slide 42: Out-of-Order Execution with Precise Exceptions
Idea: Use a reorder buffer to reorder instructions before committing them to architectural state
An instruction updates the register alias table (essentially a future file) when it completes execution
An instruction updates the architectural register file when it is the oldest in the machine and has completed execution

## Slide 43: Out-of-Order Execution with Precise Exceptions
Hump 1: Reservation stations (scheduling window)
Hump 2: Reordering (reorder buffer, aka instruction window or active window)
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
E
O
R
D
E
R
S
C
H
E
D
U
L
E
TAG and VALUE Broadcast Bus
in order
out of order
in order

## Slide 44: Enabling OoO Execution, Revisited
1. Link the consumer of a value to the producer
  Register renaming: Associate a “tag” with each data value
2. Buffer instructions until they are ready
  Insert instruction into reservation stations after renaming
3. Keep track of readiness of source values of an instruction
  Broadcast the “tag” when the value is produced
  Instructions compare their “source tags” to the broadcast tag  if match, source value becomes ready
4. When all source values of an instruction are ready, dispatch the instruction to functional unit (FU)
  Wakeup and select/schedule the instruction

## Slide 45: Summary of OOO Execution Concepts
Register renaming eliminates false dependencies, enables linking of producer to consumers
Buffering enables the pipeline to move for independent ops
Tag broadcast enables communication (of readiness of produced value) between instructions
Wakeup and select enables out-of-order dispatch