## Slide 1: 18-447 Computer Architecture Lecture 22: Main Memory
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2013, 3/26/2014

## Slide 2: Announcements
Homework 5 due date pushed out by two days
  March 28 is the new due date
Get started early on Lab 5
  Due April 6
Upcoming events that I encourage you all to attend
  Computer Architecture Seminars on Memory (April 3)
  Carnegie Mellon Cloud Workshop (April 4)

## Slide 3: Computer Architecture Seminars
Seminars relevant to many topics covered in 447
  Caching
  DRAM
List of past and upcoming seminars are here:
  https://www.ece.cmu.edu/~calcm/doku.php?id=seminars:seminars
You can subscribe to receive Computer Architecture related event announcements here:
  https://sos.ece.cmu.edu/mailman/listinfo/calcm-list

## Slide 4: Upcoming Seminar on DRAM (April 3)
April 3, Thursday, 4pm, this room (CIC Panther Hollow)
Prof. Rajeev Balasubramonian, Univ. of Utah
Memory Architectures for Emerging Technologies and Workloads
  The memory system will be a growing bottleneck for many workloads running on high-end servers. Performance improvements from technology scaling are also expected to decline in the coming decade. Therefore, new capabilities will be required in memory devices and memory controllers to achieve the next big leaps in performance and energy efficiency. Some of these capabilities will be inspired by emerging workloads (e.g., in-memory big-data, approximate computing, co-scheduled VMs), some will be inspired by new memory technologies (e.g., 3D stacking). The talk will discuss multiple early-stage projects in the Utah Arch lab that focus on DRAM parameter variation, near-data processing, and memory security.

## Slide 5: Cloud Workshop All Day on April 4
http://www.industry-academia.org/event-carnegie-mellon-cloud-workshop.html
You need to register to attend. Gates 6115. Many talks:
Keynote: Prof. Onur Mutlu – Carnegie Mellon – "Rethinking Memory System Design for Data-Intensive Computing"
Prof. Rajeev Balasubramonian – Utah – “Practical Approaches to Memory Security in the Cloud”
Bryan Chin – Cavium – “Head in the Clouds - Building a Chip for Scale-out Computing”
Dr. Joon Kim - SK Hynix – “The Future of NVM Memories”
Prof. Andy Pavlo - Carnegie Mellon – “OLTP on NVM: YMMV"
Dr. John Busch – SanDisk – “The Impact of Flash Memory on the Future of Cloud Computing”
Keynote: Prof. Greg Ganger – Carnegie Mellon – “Scheduling Heterogeneous Resources in Cloud Datacenters”
Paul Rad – Rackspace – “OpenStack-Based High Performance Cloud Architecture”
Charles Butler – Ubuntu – “Cloud Service Orchestration with JuJu”
Prof. Mor Harchol-Balter - Carnegie Mellon – “Dynamic Power Management in Data Centers”
Prof. Eric Xing – Carnegie Mellon – “Petuum: A New Platform for Cloud-based Machine Learning to Efficiently Solve Big Data Problems”
Majid Bemanian – Imagination Technologies – “Security in the Cloud and Virtualized Mobile Devices”
Robert Broberg – Cisco – “Cloud Security Challenges and Solutions”

## Slide 6: Cloud Career Fair on April 4
http://www.industry-academia.org/event-carnegie-mellon-cloud-workshop.html
Gates 6121, 11am-3pm
Runs in Room 6121 in parallel to the Tech Forum, from 11am to 3PM. IAP members will have informational/recruiting tables on site. During the breaks in the technical presentations and lunch, the Tech Forum attendees can network on lining up an internship or that first full-time engineering job. Students who are only interested and/or able to attend the Career Fair are welcome to do so, but please indicate this specific interest on your registration application (see the “Register Here” button below).

## Slide 7: Enabling High Bandwidth Memories

## Slide 8: Multiple Instructions per Cycle
Can generate multiple cache/memory accesses per cycle
How do we ensure the cache/memory can handle multiple accesses in the same clock cycle?
Solutions:
  true multi-porting
  virtual multi-porting (time sharing a port)
  multiple cache copies
  banking (interleaving)

## Slide 9: Handling Multiple Accesses per Cycle (I)
True multiporting
  Each memory cell has multiple read or write ports
  + Truly concurrent accesses (no conflicts on read accesses)
  -- Expensive in terms of latency, power, area
  What about read and write to the same location at the same time?
    Peripheral logic needs to handle this

## Slide 10: Peripheral Logic for True Multiporting

## Slide 11: Peripheral Logic for True Multiporting

## Slide 12: Handling Multiple Accesses per Cycle (II)
Virtual multiporting
  Time-share a single port
  Each access needs to be (significantly) shorter than clock cycle
  Used in Alpha 21264
  Is this scalable?

## Slide 13: Handling Multiple Accesses per Cycle (III)
Cache
Copy 1
Multiple cache copies
  Stores update both caches
  Loads proceed in parallel
Used in Alpha 21164
Scalability?
  Store operations form a bottleneck
  Area proportional to “ports”
Port 1
Load
Store
Port 1
Data
Cache
Copy 2
Port 2
Load
Port 2
Data

## Slide 14: Handling Multiple Accesses per Cycle (III)
Banking (Interleaving)
  Bits in address determines which bank an address maps to
    Address space partitioned into separate banks
    Which bits to use for “bank address”?
  + No increase in data store area
  -- Cannot satisfy multiple accesses
  to the same bank
  -- Crossbar interconnect in input/output
Bank conflicts
  Two accesses are to the same bank
  How can these be reduced?
    Hardware? Software?
Bank 0:
Even
addresses
Bank 1:
Odd
addresses

## Slide 15: General Principle: Interleaving
Interleaving (banking)
  Problem: a single monolithic memory array takes long to access and does not enable multiple accesses in parallel
  Goal: Reduce the latency of memory array access and enable multiple accesses in parallel
  Idea: Divide the array into multiple banks that can be accessed independently (in the same cycle or in consecutive cycles)
    Each bank is smaller than the entire memory storage
    Accesses to different banks can be overlapped
  A Key Issue: How do you map data to different banks? (i.e., how do you interleave data across banks?)

## Slide 16: Further Readings on Caching and MLP
Required: Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2006.
Glew, “MLP Yes! ILP No!,” ASPLOS Wild and Crazy Ideas Session, 1998.
Mutlu et al., “Runahead Execution: An Effective Alternative to Large Instruction Windows,” IEEE Micro 2003.

## Slide 17: Main Memory

## Slide 18: Main Memory in the System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 19: The Memory Chip/System Abstraction

## Slide 20: Review: Memory Bank Organization
Read access sequence:
1. Decode row address & drive word-lines
2. Selected bits drive bit-lines
• Entire row read
3. Amplify row data
4. Decode column address & select subset of row
• Send to output
5. Precharge bit-lines
• For next access

## Slide 21: Review: SRAM (Static Random Access Memory)
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m diff pairs
2n
n
m
1
row select
bitline
_bitline
n+m
Read Sequence
  1. address decode
  2. drive row select
  3. selected bit-cells drive bitlines
  (entire row is read together)
  4. diff. sensing and col. select
  (data is ready)
  5. precharge all bitlines
  (for next read or write)
Access latency dominated by steps 2 and 3
Cycling time dominated by steps 2, 3 and 5
  step 2 proportional to 2m
  step 3 and 5 proportional to 2n

## Slide 22: Review: DRAM (Dynamic Random Access Memory)
row enable
_bitline
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m
2n
n
m
1
RAS
CAS
A DRAM die comprises
of multiple such arrays
Bits stored as charges on node capacitance (non-restorative)
  bit cell loses charge when read
  bit cell loses charge over time
Read Sequence
  1~3 same as SRAM
  4. a “flip-flopping” sense amp amplifies and regenerates the bitline, data bit is mux’ed out
  5. precharge all bitlines
Refresh: A DRAM controller must periodically read all rows within the allowed refresh time (10s of ms) such that charge is restored in cells

## Slide 23: Review: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 24: Some Fundamental Concepts (I)
Physical address space
  Maximum size of main memory: total number of uniquely identifiable locations
Physical addressability
  Minimum size of data in memory can be addressed
  Byte-addressable, word-addressable, 64-bit-addressable
  Microarchitectural addressability depends on the abstraction level of the implementation
Alignment
  Does the hardware support unaligned access transparently to software?
Interleaving

## Slide 25: Some Fundamental Concepts (II)
Interleaving (banking)
  Problem: a single monolithic memory array takes long to access and does not enable multiple accesses in parallel
  Goal: Reduce the latency of memory array access and enable multiple accesses in parallel
  Idea: Divide the array into multiple banks that can be accessed independently (in the same cycle or in consecutive cycles)
    Each bank is smaller than the entire memory storage
    Accesses to different banks can be overlapped
  A Key Issue: How do you map data to different banks? (i.e., how do you interleave data across banks?)

## Slide 26: Interleaving

## Slide 27: Interleaving Options

## Slide 28: Some Questions/Concepts
Remember CRAY-1 with 16 banks
  11 cycle bank latency
  Consecutive words in memory in consecutive banks (word interleaving)
  1 access can be started (and finished) per cycle
Can banks be operated fully in parallel?
  Multiple accesses started per cycle?
What is the cost of this?
  We have seen it earlier (today)
Modern superscalar processors have L1 data caches with multiple, fully-independent banks; DRAM banks share buses

## Slide 29: The Bank Abstraction

## Slide 30
Rank

## Slide 31: The DRAM Subsystem

## Slide 32: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 33: The DRAM Bank Structure

## Slide 34: Page Mode DRAM
A DRAM bank is a 2D array of cells: rows x columns
A “DRAM row” is also called a “DRAM page”
“Sense amplifiers” also called “row buffer”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for activate command

## Slide 35: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 36: The DRAM Chip
Consists of multiple banks (2-16 in Synchronous DRAM)
Banks share command/address/data buses
The chip itself has a narrow interface (4-16 bits per read)

## Slide 37: 128M x 8-bit DRAM Chip

## Slide 38: DRAM Rank and Module
Rank: Multiple chips operated together to form a wide interface
All chips comprising a rank are controlled at the same time
  Respond to a single command
  Share address and command buses, but provide different data
A DRAM module consists of one or more ranks
  E.g., DIMM (dual inline memory module)
  This is what you plug into your motherboard
If we have chips with 8-bit interface, to read 8 bytes in a single access, use 8 chips in a DIMM

## Slide 39: A 64-bit Wide DIMM (One Rank)

## Slide 40: A 64-bit Wide DIMM (One Rank)
Advantages:
  Acts like a high-capacity DRAM chip with a wide interface
  Flexibility: memory controller does not need to deal with individual chips
Disadvantages:
  Granularity: Accesses cannot be smaller than the interface width

## Slide 41: Multiple DIMMs
Advantages:
  Enables even higher capacity
Disadvantages:
  Interconnect complexity and energy consumption can be high

## Slide 42: DRAM Channels
2 Independent Channels: 2 Memory Controllers (Above)
2 Dependent/Lockstep Channels: 1 Memory Controller with wide interface (Not Shown above)

## Slide 43: Generalized Memory Structure

## Slide 44: Generalized Memory Structure

## Slide 45: The DRAM Subsystem The Top Down View

## Slide 46: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 47: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 48: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM

## Slide 49: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 50: Rank
Rank 0 (Front)
Rank 1 (Back)
Data <0:63>
CS <0:1>
Addr/Cmd
<0:63>
<0:63>
Memory channel

## Slide 51: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 52: Breaking down a Chip
Chip 0
<0:7>
8 banks
Bank 0
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 53: Breaking down a Bank
Bank 0
<0:7>
row 0
row 16k-1
...
2kB
1B
1B (column)
1B
Row-buffer
1B
...
<0:7>

## Slide 54: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 55: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Channel 0
DIMM 0
Rank 0
Mapped to

## Slide 56: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 57: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 58: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 59: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 1
. . .

## Slide 60: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
. . .
8B

## Slide 61: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
A 64B cache block takes 8 I/O cycles to transfer.
During the process, 8 columns are read sequentially.
. . .

## Slide 62: Latency Components: Basic DRAM Operation
CPU → controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
Controller → DRAM transfer time
DRAM bank latency
  Simple CAS (column address strobe) if row is “open” OR
  RAS (row address strobe) + CAS if array precharged OR
  PRE + RAS + CAS (worst case)
DRAM → Controller transfer time
  Bus latency (BL)
Controller to CPU transfer time

## Slide 63: Multiple Banks (Interleaving) and Channels
Multiple banks
  Enable concurrent DRAM accesses
  Bits in address determine which bank an address resides in
Multiple independent channels serve the same purpose
  But they are even better because they have separate data buses
  Increased bus bandwidth
Enabling more concurrency requires reducing
  Bank conflicts
  Channel conflicts
How to select/randomize bank/channel indices in address?
  Lower order bits have more entropy
  Randomizing hash functions (XOR of different address bits)

## Slide 64: How Multiple Banks/Channels Help

## Slide 65: Multiple Channels
Advantages
  Increased bandwidth
  Multiple concurrent accesses (if independent channels)
Disadvantages
  Higher cost than a single channel
    More board wires
    More pins (if on-chip memory controller)

## Slide 66: Address Mapping (Single Channel)
Single-channel system with 8-byte memory bus
  2GB memory, 8 banks, 16K rows & 2K columns per bank
Row interleaving
  Consecutive rows of memory in consecutive banks
  Accesses to consecutive cache blocks serviced in a pipelined manner
Cache block interleaving
    Consecutive cache block addresses in consecutive banks
    64 byte cache blocks
    Accesses to consecutive cache blocks can be serviced in parallel
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits

## Slide 67: Bank Mapping Randomization
DRAM controller can randomize the address mapping to banks so that bank conflicts are less likely
Column (11 bits)
3 bits
Byte in bus (3 bits)
XOR
Bank index (3 bits)

## Slide 68: Address Mapping (Multiple Channels)
Where are consecutive cache blocks?
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C

## Slide 69: Interaction with VirtualPhysical Mapping
Operating System influences where an address maps to in DRAM
Operating system can influence which bank/channel/rank a virtual page is mapped to.
It can perform page coloring to
  Minimize bank conflicts
  Minimize inter-application interference [Muralidhara+ MICRO’11]
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Page offset (12 bits)
Physical Frame number (19 bits)
Page offset (12 bits)
Virtual Page number (52 bits)
VA
PA
PA

## Slide 70: Memory Controllers

## Slide 71: DRAM versus Other Types of Memories
Long latency memories have similar characteristics that need to be controlled.
The following discussion will use DRAM as an example, but many scheduling and control issues are similar in the design of controllers for other types of memories
  Flash memory
  Other emerging memory technologies
    Phase Change Memory
    Spin-Transfer Torque Magnetic Memory
  These other technologies can place other demands on the controller

## Slide 72: DRAM Controller: Functions
Ensure correct operation of DRAM (refresh and timing)
Service DRAM requests while obeying timing constraints of DRAM chips
  Constraints: resource conflicts (bank, bus, channel), minimum write-to-read delays
  Translate requests to DRAM command sequences
Buffer and schedule requests to improve performance
  Reordering, row-buffer, bank, rank, bus management
Manage power consumption and thermals in DRAM
  Turn on/off DRAM chips, manage power modes

## Slide 73: DRAM Controller: Where to Place
In chipset
  + More flexibility to plug different DRAM types into the system
+ Less power density in the CPU chip
On CPU chip
  + Reduced latency for main memory access
  + Higher bandwidth between cores and controller
    More information can be communicated (e.g. request’s importance in the processing core)

## Slide 74: A Modern DRAM Controller (I)

## Slide 75: A Modern DRAM Controller (II)

## Slide 76: DRAM Scheduling Policies (I)
FCFS (first come first served)
  Oldest request first
FR-FCFS (first ready, first come first served)
  1. Row-hit first
  2. Oldest first
  Goal: Maximize row buffer hit rate  maximize DRAM throughput
  Actually, scheduling is done at the command level
    Column commands (read/write) prioritized over row commands (activate/precharge)
    Within each group, older commands prioritized over younger ones

## Slide 77: DRAM Scheduling Policies (II)
A scheduling policy is essentially a prioritization order
Prioritization can be based on
  Request age
  Row buffer hit/miss status
  Request type (prefetch, read, write)
  Requestor type (load miss or store miss)
  Request criticality
    Oldest miss in the core?
    How many instructions in core are dependent on it?