## Slide 1: 18-447 Computer Architecture Lecture 27: Prefetching
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2014, 4/9/2013

## Slide 2: Announcements
No office hours today
Graded homework and labs
  You can find grade distributions on the website
Lab 6: Memory Hierarchy Due April 20
HW 6: Due today!
HW 7: Will be out soon.
  Please do the homework to prepare for Midterm II
Midterm II: April 23 – start preparing now
  Similar in format and spirit to Midterm I. Solve past midterms.

## Slide 3: Suggestions for Midterm II
Solve past midterms (and finals) on your own…
  And, check your solutions vs. the online solutions
  Questions will be similar in spirit
http://www.ece.cmu.edu/~ece447/s14/doku.php?id=exams
http://www.ece.cmu.edu/~ece447/s13/doku.php?id=exams
Do Homework 7
Study and internalize the lecture material well.
Do the readings that are required.

## Slide 4: Lab 4 Statistics
MAX 100
MIN 67.79
MEDIAN 96.16
MEAN 91.32
STD 9.92

## Slide 5: Lab 4 Grade Distribution
Chart: Lab 4 Grade Distribution
| 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 4 | 4 | 10 | 7

## Slide 6: Lab 4 Extra Credit (Branch Performance)
Bailey Forrest -- bcforres (0.858209405)
Aaron Reyes -- areyes (0.821014754)
Jeremie Kim -- jeremiek (0.74389269)
Xiang Lin -- xianglin (0.701012488)
Clement Loh -- changshl (0.69833888)

## Slide 7: Lab 6: Memory Hierarchy
Due Sunday (April 20)
Cycle-level modeling of L2 cache and DRAM-based main memory
Extra credit: Prefetching
  Design your own hardware prefetcher to improve system performance

## Slide 8: Last Lecture
Memory Latency Tolerance
Runahead Execution and Enhancements
  Efficient Runahead Execution
  Address-Value Delta Prediction

## Slide 9: Today
Basics of Prefetching
Advanced Prefetching

## Slide 10: Tolerating Memory Latency

## Slide 11: Cache Misses Responsible for Many Stalls
512KB L2 cache, 500-cycle DRAM latency, aggressive stream-based prefetcher
Data averaged over 147 memory-intensive benchmarks on a high-end x86 processor model
L2 Misses

## Slide 12: Review: Memory Latency Tolerance Techniques
Caching [initially by Wilkes, 1965]
  Widely used, simple, effective, but inefficient, passive
  Not all applications/phases exhibit temporal or spatial locality
Prefetching [initially in IBM 360/91, 1967]
  Works well for regular memory access patterns
  Prefetching irregular access patterns is difficult, inaccurate, and hardware-intensive
Multithreading [initially in CDC 6600, 1964]
  Works well if there are multiple threads
  Improving single thread performance using multithreading hardware is an ongoing research effort
Out-of-order execution [initially by Tomasulo, 1967]
  Tolerates irregular cache misses that cannot be prefetched
  Requires extensive hardware resources for tolerating long latencies
  Runahead execution alleviates this problem (as we will see in a later lecture)

## Slide 13: Prefetching

## Slide 14: Outline of Prefetching Lectures
Why prefetch? Why could/does it work?
The four questions
  What (to prefetch), when, where, how
Software prefetching
Hardware prefetching algorithms
Execution-based prefetching
Prefetching performance
  Coverage, accuracy, timeliness
  Bandwidth consumption, cache pollution
Prefetcher throttling (if we get to it)
Issues in multi-core (if we get to it)

## Slide 15: Prefetching
Idea: Fetch the data before it is needed (i.e. pre-fetch) by the program
Why?
  Memory latency is high. If we can prefetch accurately and early enough we can reduce/eliminate that latency.
  Can eliminate compulsory cache misses
  Can it eliminate all cache misses? Capacity, conflict?
Involves predicting which address will be needed in the future
  Works if programs have predictable miss address patterns

## Slide 16: Prefetching and Correctness
Does a misprediction in prefetching affect correctness?
No, prefetched data at a “mispredicted” address is simply not used
There is no need for state recovery
In contrast to branch misprediction or value misprediction

## Slide 17: Basics
In modern systems, prefetching is usually done in cache block granularity
Prefetching is a technique that can reduce both
  Miss rate
  Miss latency
Prefetching can be done by
  hardware
  compiler
  programmer

## Slide 18: How a HW Prefetcher Fits in the Memory System

## Slide 19: Prefetching: The Four Questions
What
  What addresses to prefetch
When
  When to initiate a prefetch request
Where
  Where to place the prefetched data
How
  Software, hardware, execution-based, cooperative

## Slide 20: Challenges in Prefetching: What
What addresses to prefetch
  Prefetching useless data wastes resources
    Memory bandwidth
    Cache or prefetch buffer space
    Energy consumption
    These could all be utilized by demand requests or more accurate prefetch requests
  Accurate prediction of addresses to prefetch is important
    Prefetch accuracy = used prefetches / sent prefetches
How do we know what to prefetch
  Predict based on past access patterns
  Use the compiler’s knowledge of data structures
Prefetching algorithm determines what to prefetch

## Slide 21: Challenges in Prefetching: When
When to initiate a prefetch request
  Prefetching too early
    Prefetched data might not be used before it is evicted from storage
  Prefetching too late
    Might not hide the whole memory latency
When a data item is prefetched affects the timeliness of the prefetcher
Prefetcher can be made more timely by
  Making it more aggressive: try to stay far ahead of the processor’s access stream (hardware)
  Moving the prefetch instructions earlier in the code (software)

## Slide 22: Challenges in Prefetching: Where (I)
Where to place the prefetched data
  In cache
    + Simple design, no need for separate buffers
    -- Can evict useful demand data  cache pollution
  In a separate prefetch buffer
    + Demand data protected from prefetches  no cache pollution
    -- More complex memory system design
    - Where to place the prefetch buffer
    - When to access the prefetch buffer (parallel vs. serial with cache)
    - When to move the data from the prefetch buffer to cache
    - How to size the prefetch buffer
    - Keeping the prefetch buffer coherent
Many modern systems place prefetched data into the cache
  Intel Pentium 4, Core2’s, AMD systems, IBM POWER4,5,6, …

## Slide 23: Challenges in Prefetching: Where (II)
Which level of cache to prefetch into?
  Memory to L2, memory to L1. Advantages/disadvantages?
  L2 to L1? (a separate prefetcher between levels)
Where to place the prefetched data in the cache?
  Do we treat prefetched blocks the same as demand-fetched blocks?
  Prefetched blocks are not known to be needed
    With LRU, a demand block is placed into the MRU position
Do we skew the replacement policy such that it favors the demand-fetched blocks?
  E.g., place all prefetches into the LRU position in a way?

## Slide 24: Challenges in Prefetching: Where (III)
Where to place the hardware prefetcher in the memory hierarchy?
  In other words, what access patterns does the prefetcher see?
  L1 hits and misses
  L1 misses only
  L2 misses only
Seeing a more complete access pattern:
  + Potentially better accuracy and coverage in prefetching
  -- Prefetcher needs to examine more requests (bandwidth intensive, more ports into the prefetcher?)

## Slide 25: Challenges in Prefetching: How
Software prefetching
  ISA provides prefetch instructions
  Programmer or compiler inserts prefetch instructions (effort)
  Usually works well only for “regular access patterns”
Hardware prefetching
  Hardware monitors processor accesses
  Memorizes or finds patterns/strides
  Generates prefetch addresses automatically
Execution-based prefetchers
  A “thread” is executed to prefetch data for the main program
  Can be generated by either software/programmer or hardware

## Slide 26: Software Prefetching (I)
Idea: Compiler/programmer places prefetch instructions into appropriate places in code
  Mowry et al., “Design and Evaluation of a Compiler Algorithm for Prefetching,” ASPLOS 1992.
Prefetch instructions prefetch data into caches
Compiler or programmer can insert such instructions into the program

## Slide 27: X86 PREFETCH Instruction
microarchitecture
dependent
specification
different instructions
for different cache
levels

## Slide 28: Software Prefetching (II)
Can work for very regular array-based access patterns. Issues:
  -- Prefetch instructions take up processing/execution bandwidth
  How early to prefetch? Determining this is difficult
    -- Prefetch distance depends on hardware implementation (memory latency, cache size, time between loop iterations)  portability?
    -- Going too far back in code reduces accuracy (branches in between)
  Need “special” prefetch instructions in ISA?
    Alpha load into register 31 treated as prefetch (r31==0)
    PowerPC dcbt (data cache block touch) instruction
  -- Not easy to do for pointer-based data structures
for (i=0; i<N; i++) {
__prefetch(a[i+8]);
__prefetch(b[i+8]);
sum += a[i]*b[i];
}
while (p) {
__prefetch(pnext);
work(pdata);
p = pnext;
}
while (p) {
__prefetch(pnextnextnext);
work(pdata);
p = pnext;
}
Which one is better?

## Slide 29: Software Prefetching (III)
Where should a compiler insert prefetches?
  Prefetch for every load access?
    Too bandwidth intensive (both memory and execution bandwidth)
  Profile the code and determine loads that are likely to miss
    What if profile input set is not representative?
  How far ahead before the miss should the prefetch be inserted?
    Profile and determine probability of use for various prefetch distances from the miss
      What if profile input set is not representative?
      Usually need to insert a prefetch far in advance to cover 100s of cycles of main memory latency  reduced accuracy

## Slide 30: Hardware Prefetching (I)
Idea: Specialized hardware observes load/store access patterns and prefetches data based on past access behavior
Tradeoffs:
  + Can be tuned to system implementation
  + Does not waste instruction execution bandwidth
  -- More hardware complexity to detect patterns
  - Software can be more efficient in some cases

## Slide 31: Next-Line Prefetchers
Simplest form of hardware prefetching: always prefetch next N cache lines after a demand access (or a demand miss)
  Next-line prefetcher (or next sequential prefetcher)
  Tradeoffs:
    + Simple to implement. No need for sophisticated pattern detection
    + Works well for sequential/streaming access patterns (instructions?)
    -- Can waste bandwidth with irregular patterns
    -- And, even regular patterns:
    - What is the prefetch accuracy if access stride = 2 and N = 1?
    - What if the program is traversing memory from higher to lower addresses?
    - Also prefetch “previous” N cache lines?

## Slide 32: Stride Prefetchers
Two kinds
  Instruction program counter (PC) based
  Cache block address based
Instruction based:
  Baer and Chen, “An effective on-chip preloading scheme to reduce data access penalty,” SC 1991.
  Idea:
    Record the distance between the memory addresses referenced by a load instruction (i.e. stride of the load) as well as the last address referenced by the load
    Next time the same load instruction is fetched, prefetch last address + stride

## Slide 33: Instruction Based Stride Prefetching
What is the problem with this?
  Hint: how far can this get ahead? How much of the miss latency can the prefetch cover?
  Initiating the prefetch when the load is fetched the next time can be too late
    Load will access the data cache soon after it is fetched!
  Solutions:
    Use lookahead PC to index the prefetcher table (decouple frontend of the processor from backend)
    Prefetch ahead (last address + N*stride)
    Generate multiple prefetches
Load Inst. | Last Address | Last | Confidence
PC (tag) | Referenced | Stride | 
……. | ……. | …… | 
Load
Inst
PC

## Slide 34: Cache-Block Address Based Stride Prefetching
Can detect
  A, A+N, A+2N, A+3N, …
  Stream buffers are a special case of cache block address based stride prefetching where N = 1
    Read the Jouppi paper
    Stream buffer also has data storage in that paper (no prefetching into cache)
Address tag | Stride | Control/Confidence
……. | …… | 
Block
address

## Slide 35: Stream Buffers (Jouppi, ISCA 1990)
Each stream buffer holds one stream of sequentially prefetched cache lines
On a load miss check the head of all stream buffers for an address match
  if hit, pop the entry from FIFO, update the cache with data
  if not, allocate a new stream buffer to the new miss address (may have to recycle a stream buffer following LRU policy)
Stream buffer FIFOs are continuously topped-off with subsequent cache lines whenever there is room and the bus is not busy
FIFO
FIFO
FIFO
FIFO
DCache
Memory interface

## Slide 36: Stream Buffer Design

## Slide 37: Stream Buffer Design

## Slide 38: Prefetcher Performance (I)
Accuracy (used prefetches / sent prefetches)
Coverage (prefetched misses / all misses)
Timeliness (on-time prefetches / used prefetches)
Bandwidth consumption
  Memory bandwidth consumed with prefetcher / without prefetcher
  Good news: Can utilize idle bus bandwidth (if available)
Cache pollution
  Extra demand misses due to prefetch placement in cache
  More difficult to quantify but affects performance

## Slide 39: Prefetcher Performance (II)
Prefetcher aggressiveness affects all performance metrics
Aggressiveness dependent on prefetcher type
For most hardware prefetchers:
  Prefetch distance: how far ahead of the demand stream
  Prefetch degree: how many prefetches per demand access
Predicted Stream
Predicted Stream
X
Access Stream
Pmax
Prefetch Distance
Pmax
Very Conservative
Pmax
Middle of the Road
Pmax
Very Aggressive
P
Prefetch Degree
X+1
1 2 3

## Slide 40: Prefetcher Performance (III)
How do these metrics interact?
Very Aggressive Prefetcher
  Well ahead of the load access stream
  Hides memory access latency better
  More speculative
  + Higher coverage, better timeliness
  -- Likely lower accuracy, higher bandwidth and pollution
Very Conservative Prefetcher
  Closer to the load access stream
  Might not hide memory access latency completely
  Reduces potential for cache pollution and bandwidth contention
  + Likely higher accuracy, lower bandwidth, less polluting
  -- Likely lower coverage and less timely

## Slide 41: Prefetcher Performance (IV)

## Slide 42: Prefetcher Performance (V)
  Srinath et al., “Feedback Directed Prefetching: Improving the Performance and Bandwidth-Efficiency of Hardware Prefetchers“, HPCA 2007.
48%
 29%

## Slide 43: Feedback-Directed Prefetcher Throttling (I)
Idea:
  Dynamically monitor prefetcher performance metrics
  Throttle the prefetcher aggressiveness up/down based on past performance
  Change the location prefetches are inserted in cache based on past performance
High Accuracy
Not-Late
Polluting
Decrease
Late
Increase
Med Accuracy
Not-Poll
Late
Increase
Polluting
Decrease
Low Accuracy
Not-Poll
Not-Late
No Change
Decrease

## Slide 44: Feedback-Directed Prefetcher Throttling (II)
  Srinath et al., “Feedback Directed Prefetching: Improving the Performance and Bandwidth-Efficiency of Hardware Prefetchers“, HPCA 2007.
  Srinath et al., “Feedback Directed Prefetching: Improving the Performance and Bandwidth-Efficiency of Hardware Prefetchers“, HPCA 2007.
11%
13%

## Slide 45: How to Prefetch More Irregular Access Patterns?
Regular patterns: Stride, stream prefetchers do well
More irregular access patterns
  Indirect array accesses
  Linked data structures
  Multiple regular strides (1,2,3,1,2,3,1,2,3,…)
  Random patterns?
  Generalized prefetcher for all patterns?
Correlation based prefetchers
Content-directed prefetchers
Precomputation or execution-based prefetchers

## Slide 46: Markov Prefetching (I)
Consider the following history of cache block addresses
  A, B, C, D, C, E, A, C, F, F, E, A, A, B, C, D, E, A, B, C, D, C
After referencing a particular address (say A or E), are some addresses more likely to be referenced next
A
B
C
D
E
F
1.0
.33
.5
.2
1.0
.6
.2
.67
.6
.5
.2
Markov
Model

## Slide 47: Markov Prefetching (II)
Idea: Record the likely-next addresses (B, C, D) after seeing an address A
  Next time A is accessed, prefetch B, C, D
  A is said to be correlated with B, C, D
Prefetch up to N next addresses to increase coverage
Prefetch accuracy can be improved by using multiple addresses as key for the next address: (A, B)  (C)
(A,B) correlated with C
Joseph and Grunwald, “Prefetching using Markov Predictors,” ISCA 1997.
Cache Block Addr |  | Prefetch | Confidence | …. | Prefetch | Confidence
(tag) |  | Candidate 1 |  | …. | Candidate N | 
……. |  | ……. | …… | .… | ……. | ……
 |  |  |  | …. |  | 
Cache
Block
Addr

## Slide 48: Markov Prefetching (III)
Advantages:
  Can cover arbitrary access patterns
    Linked data structures
    Streaming patterns (though not so efficiently!)
Disadvantages:
  Correlation table needs to be very large for high coverage
    Recording every miss address and its subsequent miss addresses is infeasible
  Low timeliness: Lookahead is limited since a prefetch for the next access/miss is initiated right after previous
  Consumes a lot of memory bandwidth
    Especially when Markov model probabilities (correlations) are low
  Cannot reduce compulsory misses

## Slide 49: Content Directed Prefetching (I)
A specialized prefetcher for pointer values
Cooksey et al., “A stateless, content-directed data prefetching mechanism,” ASPLOS 2002.
Idea: Identify pointers among all values in a fetched cache block and issue prefetch requests for them.
+ No need to memorize/record past addresses!
+ Can eliminate compulsory misses (never-seen pointers)
-- Indiscriminately prefetches all pointers in a cache block
How to identify pointer addresses:
  Compare address sized values within cache block with cache block’s address  if most-significant few bits match, pointer

## Slide 50: Content Directed Prefetching (II)
x40373551
L2
DRAM
…
…
=
=
=
=
=
=
=
=
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
x80011100
Generate Prefetch
Virtual Address Predictor
X80022220
22220
X800
11100
x800

## Slide 51: Making Content Directed Prefetching Efficient
Hardware does not have enough information on pointers
Software does (and can profile to get more information)
Idea:
  Compiler profiles and provides hints as to which pointer addresses are likely-useful to prefetch.
  Hardware uses hints to prefetch only likely-useful pointers.
Ebrahimi et al., “Techniques for Bandwidth-Efficient Prefetching of Linked Data Structures in Hybrid Prefetching Systems,” HPCA 2009.

## Slide 52: Efficient CDP – An Example
HashLookup(int Key) {
…
for (node = head ; node -> Key != Key;
Struct node{
int Key;
int * D1_ptr;
int * D2_ptr;
node * Next;
}
node = node -> Next;
if (node) return node->D1;
}
…
Key
D2
Key
D1
D2
Key
D1
D2
…
Key
D1
D2
Key
D1
D2
D1
) ;
Key
Example from mst

## Slide 53: Efficient CDP – An Example
=
=
=
=
=
=
=
=
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
Virtual Address Predictor
Key
Next
Key
Next
Cache Line Addr
…
Key
D2
Key
D1
D2
Key
D1
D2
…
…
Key
D1
D2
D1
D2
D1
D1_ptr
D2_ptr
D1_ptr
D2_ptr
Key

## Slide 54: Efficient CDP – An Example
HashLookup(int Key) {
…
for (node = head ;
node = node -> Next;
if (node)
}
) ;
…
Key
D2
D1
D2
Key
D1
D2
…
Key
D1
D2
Key
D1
D2
D1
node -> Key != Key;
return node -> D1;
Key

## Slide 55: Efficient CDP – An Example
…
=
=
=
=
=
=
=
=
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
Virtual Address Predictor
Key
D1_ptr
D2_ptr
Next
Key
D1_ptr
D2_ptr
Next
Cache Line Addr
Key
D1
D2
Key
D1
D2
Key
D1
D2
…
…
Key
D1
D2
Key
D1
D2
[31:20]