## Slide 1: 18-447 Computer Architecture Lecture 31: Asymmetric Multi-Core
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2014, 4/30/2014

## Slide 2: Lab 7: Multi-Core Cache Coherence
Due May 2; Last submission accepted on May 9, 11:59pm
Cycle-level modeling of the MESI cache coherence protocol
Since this is the last lab
  An automatic extension of 7 days granted for everyone
  No other late days accepted

## Slide 3: A Note on Testing Your Own Code
We provide the reference simulator to aid you
Do not expect it to be given, and do not rely on it much
In real life, there are no reference simulators
The architect designs the reference simulator
The architect verifies it
The architect tests it
The architect fixes it
The architect makes sure there are no bugs
The architect ensures the simulator matches the specification

## Slide 4: Lab 7 Grading
Lab 7 is worth 5% of your entire course grade
3% of this is my gift to each of you 
2% of this you can earn by getting a grade between 0/100 and 40/100 (if you submit)
An additional 3% will be extra credit you can earn by getting a grade between 40/100 and 100/100 (if you submit)
Lab 7 grade is calculated as
  Effect on total course grade = 3% + [5% * grade/100]
  Everyone gets 3% on the lab without even submitting it
  Those who submit the lab can get the remaining 2% and up to 3% more extra credit.

## Slide 5: Final Exam: May 6
May 6, 8:30-11:30am, Hamerschlag Hall B103
Comprehensive (over all topics in course)
Three cheat sheets allowed
We might have a review session
Remember this is 25% of your grade
  I will take into account your improvement over the course
  Know all concepts, especially the previous midterm concepts
  Same advice as before for Midterms I and II

## Slide 6: A Note on 742, Research, Jobs
I am teaching Parallel Computer Architecture next semester (Fall 2014)
  Deep dive into many topics we covered
  And, many topics we did not cover
  Research oriented with an open-ended research project
  Cutting edge research and topics in HW/SW interface
If you are enjoying 447 and are doing well, you can take it
 no need to have taken 640/740
 talk with me
If you are excited about Computer Architecture research or looking for a job/internship in this area
 talk with me

## Slide 7: Course Evaluations (due May 12)
Due May 12
Please do not forget to fill out the course evaluations
  http://www.cmu.edu/hub/fce/
Your feedback is very important
I read these very carefully, and take into account every piece of feedback
  And, improve the course for the future
Please take the time to write out feedback
  State the things you liked, topics you enjoyed, and what we can improve on
  Don’t just say “the course is hard” because you knew that form the very beginning!

## Slide 8: Last Lecture
Wrap up cache coherence
  VI  MSI  MESI  MOESI  ?
  Directory vs. snooping tradeoffs
  Scaling the directory based protocols
Interconnects
  Why important?
  Topologies
  Routing algorithms
  Handling contention
  On-chip interconnects

## Slide 9: Today
Evolution of multi-core systems
Handling serial and parallel bottlenecks better
Heterogeneous multi-core systems

## Slide 10: Multi-Core Design

## Slide 11: Many Cores on Chip
Simpler and lower power than a single large core
Large scale parallelism on chip
IBM Cell BE 8+1 cores
Intel Core i7 8 cores
Tilera TILE Gx
100 cores, networked
IBM POWER7
8 cores
Intel SCC
48 cores, networked
Nvidia Fermi
448 “cores”
AMD Barcelona
4 cores
Sun Niagara II
8 cores

## Slide 12: With Many Cores on Chip
What we want:
  N times the performance with N times the cores when we parallelize an application on N cores
What we get:
  Amdahl’s Law (serial bottleneck)
  Bottlenecks in the parallel portion

## Slide 13: Caveats of Parallelism
Amdahl’s Law
  f: Parallelizable fraction of a program
  N: Number of processors
  Amdahl, “Validity of the single processor approach to achieving large scale computing capabilities,” AFIPS 1967.
Maximum speedup limited by serial portion: Serial bottleneck
Parallel portion is usually not perfectly parallel
  Synchronization overhead (e.g., updates to shared data)
  Load imbalance overhead (imperfect parallelization)
  Resource sharing overhead (contention among N processors)
Speedup =
1
+
1 - f
f
N

## Slide 14: The Problem: Serialized Code Sections
Many parallel programs cannot be parallelized completely
Causes of serialized code sections
  Sequential portions (Amdahl’s “serial part”)
  Critical sections
  Barriers
  Limiter stages in pipelined programs
Serialized code sections
  Reduce performance
  Limit scalability
  Waste energy

## Slide 15: Example from MySQL
Open database tables
Perform the operations
….
Critical Section
Parallel
Access Open Tables Cache
Chart: 



SCMP | 1 | 3.1009 | 4.5502 | 5.4912 | 5.9668 | 5.399 | 3.9177
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 3.1009 | 4.5502 | 5.4912 | 5.9668 | 5.399 | 3.9177
ACS | 1.841 | 3.1306 | 4.7201 | 6.4589 | 6.9731 | 7.4453 | 7.4756
Chip Area (cores)
Speedup
Today
Asymmetric
Notes: I show an example from the MySQL database. Each database thread first>>>
opens the database tables it requires, and >>>
then processes the transaction >>>
While independent transactions can proceed in parallel, opening the tables requires accessing a shared data structure called the Open Table Caches. The open tables cache is a 2-dimensional a linked data structure accesses to which are difficult to parallelize. >>>
Thus the accesses are encapsulated in a critical section.>>>

## Slide 16: Demands in Different Code Sections
What we want:
In a serialized code section  one powerful “large” core
In a parallel code section  many wimpy “small” cores
These two conflict with each other:
  If you have a single powerful core, you cannot have many cores
  A small core is much more energy and area efficient than a large core

## Slide 17: “Large” vs. “Small” Cores
Out-of-order
Wide fetch e.g. 4-wide
Deeper pipeline
Aggressive branch predictor (e.g. hybrid)
Multiple functional units
Trace cache
Memory dependence speculation
In-order
Narrow Fetch e.g. 2-wide
Shallow pipeline
Simple branch predictor (e.g. Gshare)
Few functional units
Large Core
Small Core
Large Cores are power inefficient: e.g., 2x performance for 4x area (power)

## Slide 18: Large vs. Small Cores
Grochowski et al., “Best of both Latency and Throughput,” ICCD 2004.

## Slide 19: Meet Large: IBM POWER4
Tendler et al., “POWER4 system microarchitecture,” IBM J R&D, 2002.
Another symmetric multi-core chip…
But, fewer and more powerful cores

## Slide 20: IBM POWER4
2 cores, out-of-order execution
100-entry instruction window in each core
8-wide instruction fetch, issue, execute
Large, local+global hybrid branch predictor
1.5MB, 8-way L2 cache
Aggressive stream based prefetching

## Slide 21: IBM POWER5
  Kalla et al., “IBM Power5 Chip: A Dual-Core Multithreaded Processor,” IEEE Micro 2004.

## Slide 22: Meet Small: Sun Niagara (UltraSPARC T1)
Kongetira et al., “Niagara: A 32-Way Multithreaded SPARC Processor,” IEEE Micro 2005.

## Slide 23: Niagara Core
4-way fine-grain multithreaded, 6-stage, dual-issue in-order
Round robin thread selection (unless cache miss)
Shared FP unit among cores

## Slide 24: Remember the Demands
What we want:
In a serialized code section  one powerful “large” core
In a parallel code section  many wimpy “small” cores
These two conflict with each other:
  If you have a single powerful core, you cannot have many cores
  A small core is much more energy and area efficient than a large core
Can we get the best of both worlds?

## Slide 25: Performance vs. Parallelism
Assumptions:
1. Small cores takes an area budget of 1 and has performance of 1
2. Large core takes an area budget of 4 and has performance of 2

## Slide 26: Tile-Large Approach
Tile a few large cores
IBM Power 5, AMD Barcelona, Intel Core2Quad, Intel Nehalem
+ High performance on single thread, serial code sections (2 units)
- Low throughput on parallel program portions (8 units)
Large core
Large core
Large
core
Large core
“Tile-Large”

## Slide 27: Tile-Small Approach
Tile many small cores
Sun Niagara, Intel Larrabee, Tilera TILE (tile ultra-small)
+ High throughput on the parallel part (16 units)
- Low performance on the serial part, single thread (1 unit)
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
“Tile-Small”

## Slide 28: Can we get the best of both worlds?
Tile Large
+ High performance on single thread, serial code sections (2 units)
- Low throughput on parallel program portions (8 units)
Tile Small
+ High throughput on the parallel part (16 units)
- Low performance on the serial part, single thread (1 unit), reduced single-thread performance compared to existing single thread processors
Idea: Have both large and small on the same chip  Performance asymmetry

## Slide 29: Asymmetric Multi-Core

## Slide 30: Asymmetric Chip Multiprocessor (ACMP)
Provide one large core and many small cores
+ Accelerate serial part using the large core (2 units)
+ Execute parallel part on small cores and large core for high throughput (12+2 units)
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Large
core
ACMP
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
“Tile-Small”
Large core
Large core
Large
core
Large core
“Tile-Large”

## Slide 31: Accelerating Serial Bottlenecks
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Large
core
ACMP Approach
Single thread  Large core

## Slide 32: Performance vs. Parallelism
Assumptions:
1. Small cores takes an area budget of 1 and has performance of 1
2. Large core takes an area budget of 4 and has performance of 2

## Slide 33: ACMP Performance vs. Parallelism
33
Large core
Large core
Large
core
Large core
“Tile-Large”
Large Cores | 4 | 0 | 1
Small Cores | 0 | 16 | 12
Serial Performance | 2 | 1 | 2
Parallel Throughput | 2 x 4 = 8 | 1 x 16 = 16 | 1x2 + 1x12 = 14
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
“Tile-Small”
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Large
core
ACMP
Area-budget = 16 small cores

## Slide 34: Caveats of Parallelism, Revisited
Amdahl’s Law
  f: Parallelizable fraction of a program
  N: Number of processors
  Amdahl, “Validity of the single processor approach to achieving large scale computing capabilities,” AFIPS 1967.
Maximum speedup limited by serial portion: Serial bottleneck
Parallel portion is usually not perfectly parallel
  Synchronization overhead (e.g., updates to shared data)
  Load imbalance overhead (imperfect parallelization)
  Resource sharing overhead (contention among N processors)
Speedup =
1
+
1 - f
f
N

## Slide 35: Accelerating Parallel Bottlenecks
Serialized or imbalanced execution in the parallel portion can also benefit from a large core
Examples:
  Critical sections that are contended
  Parallel stages that take longer than others to execute
Idea: Dynamically identify these code portions that cause serialization and execute them on a large core

## Slide 36: Accelerated Critical Sections
M. Aater Suleman, Onur Mutlu, Moinuddin K. Qureshi, and Yale N. Patt, "Accelerating Critical Section Execution with Asymmetric Multi-Core Architectures" Proceedings of the 14th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), 2009

## Slide 37: Contention for Critical Sections
0
Critical Section
Parallel
Idle
12 iterations, 33% instructions inside the critical section
P = 1
P = 3
P = 2
P = 4
1
2
3
4
5
6
7
8
9
10
11
12
33% in critical section
Notes: For simplicity lets assume that when run as a single thread, each database transaction spends 33% of its time inside the critical section and 75% of its time executing the parallel portion. >>>
I show execution of 16 transactions on a single core. The red represent the critical sections and the grey represent the non-critical section code.>>>
With 2 cores, overall execution time is halved >>>
With 4 cores, the execution time is again halved however note that the critical section is being run at all times. Thus, performance has become critical section limited ..>>>
Further increasing the cores to 8, does not reduce execution time. >>>
Thus critical sections reduce performance and limit scalability.

## Slide 38: Contention for Critical Sections
0
Critical Section
Parallel
Idle
12 iterations, 33% instructions inside the critical section
P = 1
P = 3
P = 2
P = 4
1
2
3
4
5
6
7
8
9
10
11
12
Accelerating critical sections increases performance and scalability
Critical Section Accelerated by 2x
Notes: However, I can accelerate the critical section. When we accelerate the critical section execution by 2x, the time inside the critical section reduces to half. I use blue to show the accelerated critical section. At one core, the overall execution time reduces. >>>
Similarly execution time also reduces at 2, 3, and 4 cores. >>>
Most notably, due to the shorter critical sections, performance no longer saturates at 4 cores. Instead, execution time continues to reduce until 4 cores.

## Slide 39: Impact of Critical Sections on Scalability
Contention for critical sections leads to serial execution (serialization) of threads in the parallel program portion
Contention for critical sections increases with the number of threads and limits scalability
MySQL (oltp-1)
Chart: 



SCMP | 1 | 3.1009 | 4.5502 | 5.4912 | 5.9668 | 5.399 | 3.9177
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 3.1009 | 4.5502 | 5.4912 | 5.9668 | 5.399 | 3.9177
ACS | 1.841 | 3.1306 | 4.7201 | 6.4589 | 6.9731 | 7.4453 | 7.4756
Chip Area (cores)
Speedup
Today
Asymmetric

## Slide 40: A Case for Asymmetry
Execution time of sequential kernels, critical sections, and limiter stages must be short
It is difficult for the programmer to shorten these serialized sections
  Insufficient domain-specific knowledge
  Variation in hardware platforms
  Limited resources
Goal: A mechanism to shorten serial bottlenecks without requiring programmer effort
Idea: Accelerate serialized code sections by shipping them to powerful cores in an asymmetric multi-core (ACMP)

## Slide 41: An Example: Accelerated Critical Sections
Idea: HW/SW ships critical sections to a large, powerful core in an asymmetric multi-core architecture
Benefit:
  Reduces serialization due to contended locks
  Reduces the performance impact of hard-to-parallelize sections
  Programmer does not need to (heavily) optimize parallel code  fewer bugs, improved productivity
Suleman et al., “Accelerating Critical Section Execution with Asymmetric Multi-Core Architectures,” ASPLOS 2009, IEEE Micro Top Picks 2010.
Suleman et al., “Data Marshaling for Multi-Core Architectures,” ISCA 2010, IEEE Micro Top Picks 2011.
Notes: SHOW a picture of ACMP and shipping…
Aater’s picture…

## Slide 42: Accelerated Critical Sections
EnterCS()
  PriorityQ.insert(…)
LeaveCS()
Onchip-Interconnect
Critical Section Request Buffer (CSRB)
1. P2 encounters a critical section (CSCALL)
2. P2 sends CSCALL Request to CSRB
3. P1 executes Critical Section
4. P1 sends CSDONE signal
Core executing critical section
P4
P3
P2
P1
Notes: To accelerate critical sections, the large core is augmented with a critical section request buffer or CSRB. >>>
When a small core encounters a critical section, it ships to the large core. The large core completes the ciritcal section and notifies the requesting core.
For example, When P2 encounters a critical sections,>>>
its sends a request to the large core and becomes idle.>>>
The request is buffered at the CSRB and>>>
is serviced by the large core at the first opportunity.>>>
The large core sends a CSDONE signal when it has completed the critical section. At this point, P2 resumes execution.
42

## Slide 43: Accelerated Critical Sections (ACS)
Suleman et al., “Accelerating Critical Section Execution with Asymmetric Multi-Core Architectures,” ASPLOS 2009.
A = compute()
LOCK X
result = CS(A)
UNLOCK X
print result
Small Core
Small Core
Large Core
A = compute()
CSDONE Response
CSCALL Request
Send X, TPC, STACK_PTR, CORE_ID
PUSH A
CSCALL X, Target PC
…
…
…
Acquire X
POP A
result = CS(A)
PUSH result
Release X
CSRET X
TPC:
POP result
print result
…
…
…
…
…
…
…
Waiting in Critical Section Request Buffer (CSRB)

## Slide 44: False Serialization
ACS can serialize independent critical sections
Selective Acceleration of Critical Sections (SEL)
  Saturating counters to track false serialization
CSCALL (A)
CSCALL (A)
CSCALL (B)
Critical Section Request Buffer (CSRB)
4
4
A
B
3
2
5
To large core
From small cores
Notes: While executing the critical sections on the large core accelerates their execution, ACS can serialize the execution of independent critical sections. Independent critical sections protect disjoint data and can execute concurrently in conventional systems. Since ACS sends all critical sections to the large core, their execution can get serialized. WE call this false serialization. To reduce the effect of false serialization,
we implement a mechanism to selectively disable the acceleration of critical sections which are experiencing false serialization. We call it SEL.
To implement SEL, we add a table of saturating counters to the CSRB which track false serialization. For simplicity, assume there is one counter for every independent critical section. A counter is incremented when the critical section experiences false serialization and decremented otherwise.
For example, consider a system with two critical sections A and B and an empty CSRB.
A CSCALL for critical section A arrives. Since there are no other entries, there is no false serialization, so
the counter corresponding to critical section A is decremented.
While the first call is still in progress, another CSCALL for A arrives. Again, there is NO false serialization since CSCALL for A would have waited for the first instance of critical section A even in the conventional system.
Thus counter for A is again decremented.
Now a CSCALL for B is enters the CSRB. Since B now has to wait for critical section A, which it should NOT. We say that B is experiencing false serialization and
increment its counter.
When a counter reaches its maximum value, acceleration for that critical section is disabled and conventional locking is used for its execution from there on.

## Slide 45: ACS Performance Tradeoffs
Pluses
  + Faster critical section execution
  + Shared locks stay in one place: better lock locality
  + Shared data stays in large core’s (large) caches: better shared data locality, less ping-ponging
Minuses
  - Large core dedicated for critical sections: reduced parallel throughput
  - CSCALL and CSDONE control transfer overhead
  - Thread-private data needs to be transferred to large core: worse private data locality

## Slide 46: ACS Performance Tradeoffs
Fewer parallel threads vs. accelerated critical sections
  Accelerating critical sections offsets loss in throughput
  As the number of cores (threads) on chip increase:
    Fractional loss in parallel performance decreases
    Increased contention for critical sections makes acceleration more beneficial
Overhead of CSCALL/CSDONE vs. better lock locality
  ACS avoids “ping-ponging” of locks among caches by keeping them at the large core
More cache misses for private data vs. fewer misses for shared data
Notes: ACS dedicates the large core for execution of critical sections which could otherwise be used for executing additional threads. This reduces peak parallel throughput. However, we find that in critical section intensive workloads this is not a problem since the benefit obtained by accelerating of critical sections offsets the loss in peak parallel throughput.
Moreover, we observe that this problem will be further reduce as the number of cores on the chip increase for two reasons.
First, the fraction of throughput lost due to ACS decreases. For example, loosing 4 cores in a 64-core system will be a much smaller loss than loosing 4 cores in a 8-core system.
Second, contention for critical sections increases as the number of concurrent threads increase. When contention is high, accelerating the critical sections not only reduces the critical section execution time BUT also the waiting time for contending threads. Thereby making the acceleration even more beneficial.
ACS also incurs the overhead of sending CSCALL and CSDONE signals.
This overhead is similar to the conventional systems because in conventional systems lock acquire operations often generate a cache miss and the lock variable is brought from another core. In ACS, since all critical sections execute on one LARGE core, the lock variables stay resident in its cache which saves cache misses. Thus, overall, ACS has similar latency.
In ACS the input arguments to the critical section must be transferred from the cache of the small core to the cache of the large core. Let me explain this trade-off with an example.

## Slide 47: Cache Misses for Private Data
Private Data: NewSubProblems
Shared Data: The priority heap
PriorityHeap.insert(NewSubProblems)
Puzzle Benchmark
Notes: Consider this critical section from the puzzle benchmark. This critical sections protects a priority heap. The input argument is the node to be inserted on the heap.
The priority heap is the Shared data which is data protected by the critical sections and private data is the incoming node to be inserted.
During execution, multiple nodes of the heap are touched to find the right place to insert the incoming private data. In conventional systems, the shared data usually moves from cache-to-cache as different cores modify it inside critical sections. The private data is usually available locally. In ACS, since all critical sections execute on the large core, the shared data stays resident AT the large and does not move from cache to cache. However, private data has to be brought in from the small requesting core to execute the critical section.

## Slide 48: ACS Performance Tradeoffs
Fewer parallel threads vs. accelerated critical sections
  Accelerating critical sections offsets loss in throughput
  As the number of cores (threads) on chip increase:
    Fractional loss in parallel performance decreases
    Increased contention for critical sections makes acceleration more beneficial
Overhead of CSCALL/CSDONE vs. better lock locality
  ACS avoids “ping-ponging” of locks among caches by keeping them at the large core
More cache misses for private data vs. fewer misses for shared data
  Cache misses reduce if shared data > private data
This problem can be solved

## Slide 49: ACS Comparison Points
Conventional locking
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Large
core
ACMP
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Large
core
ACS
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
Small core
SCMP
Conventional locking
Large core executes Amdahl’s serial part
Large core executes Amdahl’s serial part and critical sections
Notes: In our experiments we simulated three configurations.
First, A symmetric CMP or SCMP with all small cores. The numbers of cores is equal to the chip area and conventional locks are used for critical sections.
Second, an ACMP with one large core and remaining small cores. The large core takes the area of 4 small cores. The large core is used to execute Amdahl’s bottleneck. Critical Sections are executed using conventional locking.
Third, ACS, which is an ACMP with a CSRB and support for accelerating critical sections. In ACS, the Amdahl’s bottleneck as well as the critical sections execute on the large core.
The large core replceas four small cores. When chip area increases, we increase the number of small cores in all three confgiurations. At area 16, the SCMP has 16 small cores and the ACMP and ACS has 1 large core and 12 small cores. At area 32, the SCMP has 32 small cores and ACMP and ACS have 1 large core and 28 small cores.
We use the ACMP as our baseline.

## Slide 50: Accelerated Critical Sections: Methodology
Workloads: 12 critical section intensive applications
  Data mining kernels, sorting, database, web, networking
Multi-core x86 simulator
  1 large and 28 small cores
  Aggressive stream prefetcher employed at each core
Details:
  Large core: 2GHz, out-of-order, 128-entry ROB, 4-wide, 12-stage
  Small core: 2GHz, in-order, 2-wide, 5-stage
  Private 32 KB L1, private 256KB L2, 8MB shared L3
  On-chip interconnect: Bi-directional ring, 5-cycle hop latency

## Slide 51: ACS Performance
Equal-area comparison Number of threads = Best threads
Chip Area = 32 small cores SCMP = 32 small cores ACMP = 1 large and 28 small cores
269 180 185
Coarse-grain locks
Fine-grain locks

## Slide 52: Equal-Area Comparisons
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 2.7874 | 2.369 | 2.0853 | 1.8461 | 1.4486 | 1.2089
ACMP | 1.6096 | 2.768 | 2.3457 | 2.0982 | 1.7972 | 1.4721 | 1.2759
ACS | 1.606 | 2.9533 | 2.8213 | 2.7064 | 2.5748 | 2.4526 | 2.1977
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 1.1458 | 1.1471 | 1.1285 | 1.1039 | 1.0451 | 0.9879
ACMP | 2.2956 | 2.4163 | 2.209 | 2.1294 | 2.0336 | 1.9099 | 1.747
ACS | 2.2925 | 2.5528 | 2.6598 | 2.6737 | 2.6425 | 2.6232 | 2.5347
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 2.6017 | 2.8059 | 2.3995 | 2.0104 | 1.3235 | 1.0144
ACMP | 2.2644 | 2.5701 | 2.7652 | 2.2258 | 1.7098 | 1.2053 | 0.9084
ACS | 2.2612 | 2.9495 | 3.9682 | 3.9855 | 3.655 | 2.9419 | 2.4096
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 1.7435 | 2.1047 | 1.9538 | 1.7833 | 1.823 | 1.8924
ACMP | 1.722 | 2.1333 | 2.2717 | 2.1047 | 1.9538 | 1.7828 | 1.862
ACS | 1.7192 | 3.0115 | 3.4064 | 4.1725 | 4.809 | 5.5459 | 6.0383
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 2.7874 | 2.369 | 2.0853 | 1.8461 | 1.4486 | 1.2089
ACMP | 1.6096 | 2.768 | 2.3457 | 2.0982 | 1.7972 | 1.4721 | 1.2759
ACS | 1.606 | 2.9533 | 2.8213 | 2.7064 | 2.5748 | 2.4526 | 2.1977
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 3.4178 | 4.6398 | 5.3483 | 7.6793 | 8.0406 | 8.1884
ACMP | 1.9785 | 3.3581 | 4.1479 | 4.823 | 7.0395 | 7.8384 | 9.183
ACS | 1.9741 | 3.1079 | 4.5331 | 5.8125 | 8.9718 | 10.4681 | 12.399
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 2.7475 | 2.7485 | 2.6792 | 2.6439 | 2.5398 | 2.4472
ACMP | 1.0619 | 2.366 | 2.8337 | 2.7351 | 2.6967 | 2.5574 | 2.4847
ACS | 1.0619 | 4.4602 | 5.1412 | 5.1328 | 5.1242 | 5.1408 | 5.1691
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 3.2573 | 5.3076 | 6.0964 | 7.0564 | 7.111 | 6.8937
ACMP | 1.1843 | 2.0748 | 3.8756 | 5.5328 | 6.6299 | 7.643 | 7.5889
ACS | 1.1839 | 3.3459 | 5.3486 | 7.3722 | 8.2556 | 8.7135 | 8.4629
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 3.1009 | 4.5502 | 5.4912 | 5.9668 | 5.399 | 3.9177
ACMP | 1.841 | 3.2843 | 4.4047 | 5.7197 | 6.2272 | 5.4377 | 4.6047
ACS | 1.841 | 3.1306 | 4.7201 | 6.4589 | 6.9731 | 7.4453 | 7.4756
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 3.2331 | 5.5182 | 6.3488 | 7.4295 | 7.0684 | 5.0469
ACMP | 1.8574 | 3.3207 | 5.3037 | 6.2144 | 7.1436 | 6.8139 | 6.4971
ACS | 1.8574 | 3.2783 | 5.746 | 7.2078 | 9.2149 | 9.5317 | 7.9959
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 1.0162 | 1.1798 | 1.6524 | 1.9567 | 2.1513 | 2.4747
ACMP | 1.0398 | 1.0484 | 1.2086 | 1.5729 | 1.9212 | 2.1253 | 2.4374
ACS | 1.0398 | 1.0084 | 1.2112 | 1.6315 | 2.1882 | 2.3861 | 2.8053
Chart: 
| 1.0 | 4.0 | 8.0 | 12.0 | 16.0 | 24.0 | 32.0
SCMP | 1 | 3.0116 | 4.3871 | 5.9208 | 6.6481 | 6.896 | 6.9711
ACMP | 2.8503 | 3.0122 | 4.7865 | 6.8903 | 7.1032 | 8.2281 | 9.0471
ACS | 2.8477 | 3.0444 | 5.428 | 6.6922 | 7.0494 | 8.7541 | 9.5836
Speedup over a small core
Chip Area (small cores)
(a) ep
(b) is
(c) pagemine
(d) puzzle
(e) qsort
(f) tsp
(i) oltp-1
(i) oltp-2
(h) iplookup
(k) specjbb
(l) webcache
(g) sqlite
Number of threads = No. of cores
------ SCMP
------ ACMP
------ ACS
Notes: Now we will compare SCMP, ACMP, and ACS as the chip area increases. The X-axis is chip area and the Y-axis shows speedup over a SINGLE small core. The green line shows ACS, the red line shows the ACMP, and blue line shows the SCMP. Here we set the number of threads equal to the number of available cores.
As you can see, critical sections severely limit the scalability of some benchmarks. For example, performance of PageMine saturates at only 8 threads. Notice that the peak speedup of ACS is higher than both ACMP and SCMP and ACS does not saturate until 12 threads.
More importantly, In case of puzzle and oltp-1, while the ACMP and SCMP show poor scalability ACS significantly improves scalability as well as speedup.
In all, ACS improves scalability in 7 out of the 12 workloads.

## Slide 53: ACS Summary
Critical sections reduce performance and limit scalability
Accelerate critical sections by executing them on a powerful core
ACS reduces average execution time by:
  34% compared to an equal-area SCMP
  23% compared to an equal-area ACMP
ACS improves scalability of 7 of the 12 workloads
Generalizing the idea: Accelerate all bottlenecks (“critical paths”) by executing them on a powerful core

## Slide 54: Bottleneck Identification and Scheduling
Jose A. Joao, M. Aater Suleman, Onur Mutlu, and Yale N. Patt, "Bottleneck Identification and Scheduling in Multithreaded Applications" Proceedings of the 17th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), London, UK, March 2012.

## Slide 55: BIS Summary
Problem: Performance and scalability of multithreaded applications are limited by serializing synchronization bottlenecks
  different types: critical sections, barriers, slow pipeline stages
  importance (criticality) of a bottleneck can change over time
Our Goal: Dynamically identify the most important bottlenecks and accelerate them
  How to identify the most critical bottlenecks
  How to efficiently accelerate them
Solution: Bottleneck Identification and Scheduling (BIS)
  Software: annotate bottlenecks (BottleneckCall, BottleneckReturn) and implement waiting for bottlenecks with a special instruction (BottleneckWait)
  Hardware: identify bottlenecks that cause the most thread waiting and accelerate those bottlenecks on large cores of an asymmetric multi-core system
Improves multithreaded application performance and scalability, outperforms previous work, and performance improves with more cores

## Slide 56: Bottlenecks in Multithreaded Applications
Definition: any code segment for which threads contend (i.e. wait)
Examples:
Amdahl’s serial portions
  Only one thread exists  on the critical path
Critical sections
  Ensure mutual exclusion  likely to be on the critical path if contended
Barriers
  Ensure all threads reach a point before continuing  the latest thread arriving is on the critical path
Pipeline stages
  Different stages of a loop iteration may execute on different threads, slowest stage makes other stages wait  on the critical path

## Slide 57: Observation: Limiting Bottlenecks Change Over Time
A=full linked list; B=empty linked list
repeat
Lock A
Traverse list A
Remove X from A
Unlock A
Compute on X
Lock B
Traverse list B
Insert X into B
Unlock B
until A is empty
Lock A is limiter
Lock B is limiter
32 threads

## Slide 58: Limiting Bottlenecks Do Change on Real Applications
MySQL running Sysbench queries, 16 threads

## Slide 59: Previous Work on Bottleneck Acceleration
Asymmetric CMP (ACMP) proposals [Annavaram+, ISCA’05] [Morad+, Comp. Arch. Letters’06] [Suleman+, Tech. Report’07]
Accelerated Critical Sections (ACS) [Suleman+, ASPLOS’09, Top Picks’10]
Feedback-Directed Pipelining (FDP) [Suleman+, PACT’10 and PhD thesis’11]
No previous work
 can accelerate all types of bottlenecks or  adapts to fine-grain changes in the importance of bottlenecks
Our goal:
general mechanism to identify and accelerate performance-limiting bottlenecks of any type

## Slide 60: Bottleneck Identification and Scheduling (BIS)
Key insight:
  Thread waiting reduces parallelism and is likely to reduce performance
  Code causing the most thread waiting  likely critical path
Key idea:
  Dynamically identify bottlenecks that cause the most thread waiting
  Accelerate them (using powerful cores in an ACMP)

## Slide 61: Bottleneck Identification and Scheduling (BIS)
Annotate bottleneck code
Implement waiting
for bottlenecks
Measure thread waiting cycles (TWC) for each bottleneck
Accelerate bottleneck(s) with the highest TWC
Binary containing BIS instructions
Compiler/Library/Programmer
Hardware

## Slide 62: Critical Sections: Code Modifications
while cannot acquire lock
Wait loop for watch_addr
acquire lock
…
release lock
…
BottleneckCall bid, targetPC
…
targetPC: while cannot acquire lock
Wait loop for watch_addr
acquire lock
…
release lock
BottleneckReturn bid
BottleneckWait bid, watch_addr
…
…
Used to keep track of waiting cycles
Used to enable acceleration

## Slide 63: Barriers: Code Modifications
…
BottleneckCall bid, targetPC
enter barrier
while not all threads in barrier
BottleneckWait bid, watch_addr
exit barrier
…
targetPC: code running for the barrier
…
BottleneckReturn bid

## Slide 64: Pipeline Stages: Code Modifications
BottleneckCall bid, targetPC
…
targetPC: while not done
while empty queue
BottleneckWait prev_bid
dequeue work
do the work …
while full queue
BottleneckWait next_bid
enqueue next work
BottleneckReturn bid

## Slide 65: Bottleneck Identification and Scheduling (BIS)
Annotate bottleneck code
Implement waiting
for bottlenecks
Measure thread waiting cycles (TWC) for each bottleneck
Accelerate bottleneck(s) with the highest TWC
Binary containing BIS instructions
Compiler/Library/Programmer
Hardware

## Slide 66: BIS: Hardware Overview
Performance-limiting bottleneck identification and acceleration are independent tasks
Acceleration can be accomplished in multiple ways
  Increasing core frequency/voltage
  Prioritization in shared resources [Ebrahimi+, MICRO’11]
  Migration to faster cores in an Asymmetric CMP
Large core
Small
core
Small
core
Small
core
Small
core
Small
core
Small
core
Small
core
Small
core
Small
core
Small
core
Small
core
Small
core

## Slide 67: Bottleneck Identification and Scheduling (BIS)
Annotate bottleneck code
Implement waiting
for bottlenecks
Measure thread waiting cycles (TWC) for each bottleneck
Accelerate bottleneck(s) with the highest TWC
Binary containing BIS instructions
Compiler/Library/Programmer
Hardware

## Slide 68: Determining Thread Waiting Cycles for Each Bottleneck
Small Core 1
Large Core 0
Small Core 2
Bottleneck
Table (BT)
…
BottleneckWait x4500
bid=x4500, waiters=1, twc = 0
bid=x4500, waiters=1, twc = 1
bid=x4500, waiters=1, twc = 2
BottleneckWait x4500
bid=x4500, waiters=2, twc = 5
bid=x4500, waiters=2, twc = 7
bid=x4500, waiters=2, twc = 9
bid=x4500, waiters=1, twc = 9
bid=x4500, waiters=1, twc = 10
bid=x4500, waiters=1, twc = 11
bid=x4500, waiters=0, twc = 11
bid=x4500, waiters=1, twc = 3
bid=x4500, waiters=1, twc = 4
bid=x4500, waiters=1, twc = 5

## Slide 69: Bottleneck Identification and Scheduling (BIS)
Annotate bottleneck code
Implement waiting
for bottlenecks
Measure thread waiting cycles (TWC) for each bottleneck
Accelerate bottleneck(s) with the highest TWC
Binary containing BIS instructions
Compiler/Library/Programmer
Hardware

## Slide 70: Bottleneck Acceleration
Small Core 1
Large Core 0
Small Core 2
Bottleneck
Table (BT)
…
Scheduling Buffer (SB)
bid=x4700, pc, sp, core1
Acceleration
Index Table (AIT)
BottleneckCall x4600
Execute locally
BottleneckCall x4700
bid=x4700 , large core 0
Execute remotely
AIT
bid=x4600, twc=100
bid=x4700, twc=10000
BottleneckReturn x4700
bid=x4700 , large core 0
bid=x4700, pc, sp, core1
 twc < Threshold
 twc > Threshold
Execute locally
Execute remotely

## Slide 71: BIS Mechanisms
Basic mechanisms for BIS:
  Determining Thread Waiting Cycles 
  Accelerating Bottlenecks 
Mechanisms to improve performance and generality of BIS:
  Dealing with false serialization
  Preemptive acceleration
  Support for multiple large cores

## Slide 72: Hardware Cost
Main structures:
  Bottleneck Table (BT): global 32-entry associative cache, minimum-Thread-Waiting-Cycle replacement
  Scheduling Buffers (SB): one table per large core, as many entries as small cores
  Acceleration Index Tables (AIT): one 32-entry table per small core
Off the critical path
Total storage cost for 56-small-cores, 2-large-cores < 19 KB

## Slide 73: BIS Performance Trade-offs
Faster bottleneck execution vs. fewer parallel threads
  Acceleration offsets loss of parallel throughput with large core counts
Better shared data locality vs. worse private data locality
  Shared data stays on large core (good)
  Private data migrates to large core (bad, but latency hidden with Data Marshaling [Suleman+, ISCA’10])
Benefit of acceleration vs. migration latency
  Migration latency usually hidden by waiting (good)
  Unless bottleneck not contended (bad, but likely not on critical path)

## Slide 74: Evaluation Methodology
Workloads: 8 critical section intensive, 2 barrier intensive and 2 pipeline-parallel applications
  Data mining kernels, scientific, database, web, networking, specjbb
Cycle-level multi-core x86 simulator
  8 to 64 small-core-equivalent area, 0 to 3 large cores, SMT
  1 large core is area-equivalent to 4 small cores
Details:
  Large core: 4GHz, out-of-order, 128-entry ROB, 4-wide, 12-stage
  Small core: 4GHz, in-order, 2-wide, 5-stage
  Private 32KB L1, private 256KB L2, shared 8MB L3
  On-chip interconnect: Bi-directional ring, 2-cycle hop latency

## Slide 75: BIS Comparison Points (Area-Equivalent)
SCMP (Symmetric CMP)
  All small cores
ACMP (Asymmetric CMP)
  Accelerates only Amdahl’s serial portions
  Our baseline
ACS (Accelerated Critical Sections)
  Accelerates only critical sections and Amdahl’s serial portions
  Applicable to multithreaded workloads (iplookup, mysql, specjbb, sqlite, tsp, webcache, mg, ft)
FDP (Feedback-Directed Pipelining)
  Accelerates only slowest pipeline stages
  Applicable to pipeline-parallel workloads (rank, pagemine)

## Slide 76: BIS Performance Improvement
Optimal number of threads, 28 small cores, 1 large core
BIS outperforms ACS/FDP by 15% and ACMP by 32%
BIS improves scalability on 4 of the benchmarks
barriers, which ACS cannot accelerate
limiting bottlenecks change over time
ACS
FDP

## Slide 77: Why Does BIS Work?
Coverage: fraction of program critical path that is actually identified as bottlenecks
  39% (ACS/FDP) to 59% (BIS)
Accuracy: identified bottlenecks on the critical path over total identified bottlenecks
  72% (ACS/FDP) to 73.5% (BIS)
Fraction of execution time spent on predicted-important bottlenecks
Actually critical

## Slide 78: BIS Scaling Results
Performance increases with:
1) More small cores
  Contention due to bottlenecks increases
  Loss of parallel throughput due to large core reduces
2) More large cores
  Can accelerate independent bottlenecks
  Without reducing parallel throughput (enough cores)
2.4%
6.2%
15%
19%

## Slide 79: BIS Summary
Serializing bottlenecks of different types limit performance of multithreaded applications: Importance changes over time
BIS is a hardware/software cooperative solution:
  Dynamically identifies bottlenecks that cause the most thread waiting and accelerates them on large cores of an ACMP
  Applicable to critical sections, barriers, pipeline stages
BIS improves application performance and scalability:
  Performance benefits increase with more cores
Provides comprehensive fine-grained bottleneck acceleration with no programmer effort

## Slide 80: We did not cover the remaining slides. These are for your benefit.

## Slide 81: Handling Private Data Locality: Data Marshaling
M. Aater Suleman, Onur Mutlu, Jose A. Joao, Khubaib, and Yale N. Patt, "Data Marshaling for Multi-core Architectures" Proceedings of the 37th International Symposium on Computer Architecture (ISCA), pages 441-450, Saint-Malo, France, June 2010.

## Slide 82: Staged Execution Model (I)
Goal: speed up a program by dividing it up into pieces
Idea
  Split program code into segments
  Run each segment on the core best-suited to run it
  Each core assigned a work-queue, storing segments to be run
Benefits
  Accelerates segments/critical-paths using specialized/heterogeneous cores
  Exploits inter-segment parallelism
  Improves locality of within-segment data
Examples
  Accelerated critical sections, Bottleneck identification and scheduling
  Producer-consumer pipeline parallelism
  Task parallelism (Cilk, Intel TBB, Apple Grand Central Dispatch)
  Special-purpose cores and functional units
Notes: Accelerate critical paths
Ship computation to data (A segmenting approach)

## Slide 83: Staged Execution Model (II)
LOAD X
STORE Y
STORE Y
LOAD Y
….
STORE Z
LOAD Z
….
Notes: Let me demonstrate the staged execution model pictorially. Assume that we have this contiguous chunk of code. I show only loads and stores since they are relevant to our work.

## Slide 84: Staged Execution Model (III)
LOAD X
STORE Y
STORE Y
LOAD Y
….
STORE Z
LOAD Z
….
Segment S0
Segment S1
Segment S2
Split code into segments
Notes: This figure shows the same chunk of code split into three segments, S0, S1, S2.
This split can be done statically and dynamically, and it is not the focus of our paper. However, I will soon show you two paradigms that split the code in different ways.

## Slide 85: Staged Execution Model (IV)
Core 0
Core 1
Core 2
Work-queues
Instances of S0
Instances of S1
Instances of S2
Notes: Once the split is done, each segment is assigned to a different core (this assignment can be done statically or dynamically, and again has been covered in previous work).
The work queue of each core contains the segments to be executed in that core.
In this example, S0 is executed in core 0, S1 executed in core 1, and so on.
*** Usually, to preserve locality and take advantage of customization, a segment is executed in one core.
*** This also preserves the locality of data that is commonly touched by instances of S0, S1, and S2 (intra-segment data, or shared data among instances of the same segment).

## Slide 86
LOAD X
STORE Y
STORE Y
LOAD Y
….
STORE Z
LOAD Z
….
Core 0
Core 1
Core 2
S0
S1
S2
Staged Execution Model: Segment Spawning
Notes: A segment that is executing on one core spawns another segment on another core, which in turn can spawn another segment in another core. These segments may need to communicate with each other because a later segment may need the data produced by a previous segment.
Segment spawning:
OLD:
When these segment runs on three cores P0, P1 and P2, core>>>
P1 incurs a cache miss to fetch Y and >>>
P2 incurs a cache miss to fetch Z
We cnan avoid these misses by shipping the data required by a segment to the core where the segment will run.

## Slide 87: Staged Execution Model: Two Examples
Accelerated Critical Sections [Suleman et al., ASPLOS 2009]
  Idea: Ship critical sections to a large core in an asymmetric CMP
    Segment 0: Non-critical section
    Segment 1: Critical section
  Benefit: Faster execution of critical section, reduced serialization, improved lock and shared data locality
Producer-Consumer Pipeline Parallelism
  Idea: Split a loop iteration into multiple “pipeline stages” where one stage consumes data produced by the next stage  each stage runs on a different core
    Segment N: Stage N
  Benefit: Stage-level parallelism, better locality  faster execution
Notes: Let me give you two concrete examples of staged execution models. I will extensively use these examples to show the benefits of data marshaling.

## Slide 88: Problem: Locality of Inter-segment Data
LOAD X
STORE Y
STORE Y
LOAD Y
….
STORE Z
LOAD Z
….
Transfer Y
Transfer Z
S0
S1
S2
Core 0
Core 1
Core 2
Cache Miss
Cache Miss
Notes: The problem is that when segments execute on different cores, they may need data produced by previous segments.
In this example, when S1 is executing Load to address Y on Core 1, it will incur a cache miss on the cache block containing Y because Core 0 was the last writer to that block.
If there is an inter-segment cache miss, the core that executes the segment will stall (or progress more slowly).
These intra-segment communication misses reduce the performance potential of staged execution.

## Slide 89: Problem: Locality of Inter-segment Data
Accelerated Critical Sections [Suleman et al., ASPLOS 2010]
  Idea: Ship critical sections to a large core in an ACMP
  Problem: Critical section incurs a cache miss when it touches data produced in the non-critical section (i.e., thread private data)
Producer-Consumer Pipeline Parallelism
  Idea: Split a loop iteration into multiple “pipeline stages”  each stage runs on a different core
  Problem: A stage incurs a cache miss when it touches data produced by the previous stage
Performance of Staged Execution limited by inter-segment cache misses
Notes: Let’s quickly take a look at what these misses look like in the two models we have discussed.
Remember in ACS, the critical sections are shipped to a large core. This means that the thread-private data that is produced outside the critical section and consumed inside it needs to be transferred to the large core when the critical section needs this data.
Similarly, in pipeline parallelism, …
…
But what is the effect of such cache misses on overall performance?

## Slide 90: What if We Eliminated All Inter-segment Misses?

## Slide 91: Talk Outline
Problem and Motivation
How Do We Get There: Examples
Accelerated Critical Sections (ACS)
Bottleneck Identification and Scheduling (BIS)
Staged Execution and Data Marshaling
Thread Cluster Memory Scheduling (if time permits)
Ongoing/Future Work
Conclusions

## Slide 92: Terminology
LOAD X
STORE Y
STORE Y
LOAD Y
….
STORE Z
LOAD Z
….
Transfer Y
Transfer Z
S0
S1
S2
Inter-segment data: Cache block written by one segment and consumed by the next segment
Generator instruction: The last instruction to write to an inter-segment cache block in a segment
Core 0
Core 1
Core 2
Notes: Let me first introduce some terminology. >>>
We call the data which is written by one segment and read by the next segment, inter-segment data >>>
In our example, Y and Z are intersegment data. >>>
We call the last instruction to modify intersegment data in a segment a generator. >>>
For example, The instructions which store Y and Z are generator instructions. >>>

## Slide 93: Key Observation and Idea
Observation: Set of generator instructions is stable over execution time and across input sets
Idea:
  Identify the generator instructions
  Record cache blocks produced by generator instructions
  Proactively send such cache blocks to the next segment’s core before initiating the next segment
Suleman et al., “Data Marshaling for Multi-Core Architectures,” ISCA 2010, IEEE Micro Top Picks 2011.
Notes: We made a key observation that lead to the development of data marshaling. We found that across a wide variety of workloads …
Based on this observation, the basic idea is data marshaling is as follows:

## Slide 94: Data Marshaling
Identify generator instructions
Insert marshal instructions
Record generator-
produced addresses
Marshal recorded
blocks to next core
Binary containing generator prefixes & marshal Instructions
Compiler/Profiler
Hardware
Notes: DM consists of two components: Compiler and Hardware.

## Slide 95: Data Marshaling
Identify generator instructions
Insert marshal instructions
Record generator-
produced addresses
Marshal recorded
blocks to next core
Binary containing generator prefixes & marshal Instructions
Hardware
Compiler/Profiler
Notes: The job of the compiler is twofolds.

## Slide 96: Profiling Algorithm
LOAD X
STORE Y
STORE Y
LOAD Y
….
STORE Z
LOAD Z
….
Mark as Generator Instruction
Inter-segment data
Notes: The algorithm runs the program as a single thread and instruments all memory instructions.
Every time an instruction modifies a cache block, the algorithm stores the instruction’s IP as the last-writer of the cache block.
Every time a segment reads a cache block whose last writer is from previous segment, i.e., the data is inter-segment data, the last-writer is added to the generator set.
SPEND LESS TIME

## Slide 97: Marshal Instructions
LOAD X
STORE Y
G: STORE Y
MARSHAL C1
LOAD Y
….
G:STORE Z
MARSHAL C2
0x5: LOAD Z
….
When to send (Marshal)
Where to send (C1)
Notes: In addition to marking the generators, the compiler/library must also insert >>>
a Marshal instruction at the end of every segment.
The instruction informs the hardware that it is time to marshal the lines and the argument to the instruction tells it where the lines should be marshaled to.
(Inserted just before the point where the next segment is initiated)
If segments are not statically scheduled to the cores, the compiler would insert the segment id as argument to the MARSHAL instruction. This segment ID is later bound to a physical core ID via the runtime library or the hardware.
Marshal instructions can come free depending on SE model
SPEND LESS TIME
Binding between segment ID and core ID… accomplished by the runtime library or can be done with hardware dynamically as well if HW scheduling is employed.

## Slide 98: DM Support/Cost
Profiler/Compiler: Generators, marshal instructions
ISA: Generator prefix, marshal instructions
Library/Hardware: Bind next segment ID to a physical core
Hardware
  Marshal Buffer
    Stores physical addresses of cache blocks to be marshaled
    16 entries enough for almost all workloads  96 bytes per core
  Ability to execute generator prefixes and marshal instructions
  Ability to push data to another cache

## Slide 99: DM: Advantages, Disadvantages
Advantages
  Timely data transfer: Push data to core before needed
  Can marshal any arbitrary sequence of lines: Identifies generators, not patterns
  Low hardware cost: Profiler marks generators, no need for hardware to find them
Disadvantages
  Requires profiler and ISA support
  Not always accurate (generator set is conservative): Pollution at remote core, wasted bandwidth on interconnect
    Not a large problem as number of inter-segment blocks is small
Notes: Pollution at remote core

## Slide 100: Accelerated Critical Sections with DM
100
Small Core 0
Marshal Buffer
Large Core
LOAD X
STORE Y
G: STORE Y
CSCALL
LOAD Y
….
G:STORE Z
CSRET
Cache Hit!
L2 Cache
L2 Cache
Data Y
Addr Y
Critical Section
Notes: 100

## Slide 101: Accelerated Critical Sections: Methodology
Workloads: 12 critical section intensive applications
  Data mining kernels, sorting, database, web, networking
  Different training and simulation input sets
Multi-core x86 simulator
  1 large and 28 small cores
  Aggressive stream prefetcher employed at each core
Details:
  Large core: 2GHz, out-of-order, 128-entry ROB, 4-wide, 12-stage
  Small core: 2GHz, in-order, 2-wide, 5-stage
  Private 32 KB L1, private 256KB L2, 8MB shared L3
  On-chip interconnect: Bi-directional ring, 5-cycle hop latency

## Slide 102: DM on Accelerated Critical Sections: Results
168 170
8.7%
Notes: I show the speedup of ACMP over SCMP where both of them employ data marshaling. DM improves performance by 8% for critical section-limited workloads and by 16% for pipeline workloads. In both cases, I also show an unrealistic ideal configuration where all misses to private and inter-stage data are artificially converted into hits. Notice that DM gets very close to this unrealistic ideal configuration.

## Slide 103: Pipeline Parallelism
103
Core 0
Marshal Buffer
Core 1
LOAD X
STORE Y
G: STORE Y
MARSHAL C1
LOAD Y
….
G:STORE Z
MARSHAL C2
0x5: LOAD Z
….
Cache Hit!
L2 Cache
L2 Cache
Data Y
Addr Y
S0
S1
S2
Notes: 103
To implement DM, Each core is augmented with a >>>
Marshal Buffer. The marshal buffer stores the addresses of the cache lines to be marshaled. >>>
Every time a core encounters a Generator instruction, it enqueues the address of the cache line being written by the instruction in the marshal buffer. >>>
When a core hits a critical section, it ships al the lines pointed to by the marshal buffer entries to the large core. The large core encounters hits when it needs to access this data.

## Slide 104: Pipeline Parallelism: Methodology
Workloads: 9 applications with pipeline parallelism
  Financial, compression, multimedia, encoding/decoding
  Different training and simulation input sets
Multi-core x86 simulator
  32-core CMP: 2GHz, in-order, 2-wide, 5-stage
  Aggressive stream prefetcher employed at each core
  Private 32 KB L1, private 256KB L2, 8MB shared L3
  On-chip interconnect: Bi-directional ring, 5-cycle hop latency

## Slide 105: DM on Pipeline Parallelism: Results
16%
Notes: I show the speedup of ACMP over SCMP where both of them employ data marshaling. DM improves performance by 8% for critical section-limited workloads and by 16% for pipeline workloads. In both cases, I also show an unrealistic ideal configuration where all misses to private and inter-stage data are artificially converted into hits. Notice that DM gets very close to this unrealistic ideal configuration.

## Slide 106: DM Coverage, Accuracy, Timeliness
High coverage of inter-segment misses in a timely manner
Medium accuracy does not impact performance
  Only 5.0 and 6.8 cache blocks marshaled for average segment

## Slide 107: Scaling Results
DM performance improvement increases with
  More cores
  Higher interconnect latency
  Larger private L2 caches
Why? Inter-segment data misses become a larger bottleneck
  More cores  More communication
  Higher latency  Longer stalls due to communication
  Larger L2 cache  Communication misses remain
Notes: Relative performance impact of inter-segment data cache misses increases with all three parameters

## Slide 108: Other Applications of Data Marshaling
Can be applied to other Staged Execution models
  Task parallelism models
    Cilk, Intel TBB, Apple Grand Central Dispatch
  Special-purpose remote functional units
  Computation spreading [Chakraborty et al., ASPLOS’06]
  Thread motion/migration [e.g., Rangan et al., ISCA’09]
Can be an enabler for more aggressive SE models
  Lowers the cost of data migration
    an important overhead in remote execution of code segments
  Remote execution of finer-grained tasks can become more feasible  finer-grained parallelization in multi-cores

## Slide 109: Data Marshaling Summary
Inter-segment data transfers between cores limit the benefit of promising Staged Execution (SE) models
Data Marshaling is a hardware/software cooperative solution: detect inter-segment data generator instructions and push their data to next segment’s core
  Significantly reduces cache misses for inter-segment data
  Low cost, high-coverage, timely for arbitrary address sequences
  Achieves most of the potential of eliminating such misses
Applicable to several existing Staged Execution models
  Accelerated Critical Sections: 9% performance benefit
  Pipeline Parallelism: 16% performance benefit
Can enable new models very fine-grained remote execution

## Slide 110: A Case for Asymmetry Everywhere
Onur Mutlu, "Asymmetry Everywhere (with Automatic Resource Management)" CRA Workshop on Advancing Computer Architecture Research: Popular Parallel Programming, San Diego, CA, February 2010. Position paper

## Slide 111: The Setting
Hardware resources are shared among many threads/apps in a many-core based system
  Cores, caches, interconnects, memory, disks, power, lifetime, …
Management of these resources is a very difficult task
  When optimizing parallel/multiprogrammed workloads
  Threads interact unpredictably/unfairly in shared resources
Power/energy is arguably the most valuable shared resource
  Main limiter to efficiency and performance

## Slide 112: Shield the Programmer from Shared Resources
Writing even sequential software is hard enough
  Optimizing code for a complex shared-resource parallel system will be a nightmare for most programmers
Programmer should not worry about (hardware) resource management
  What should be executed where with what resources
Future cloud computer architectures should be designed to
  Minimize programmer effort to optimize (parallel) programs
  Maximize runtime system’s effectiveness in automatic shared resource management

## Slide 113: Shared Resource Management: Goals
Future many-core systems should manage power and performance automatically across threads/applications
Minimize energy/power consumption
While satisfying performance/SLA requirements
  Provide predictability and Quality of Service
Minimize programmer effort
  In creating optimized parallel programs
Asymmetry and configurability in system resources essential to achieve these goals

## Slide 114: Asymmetry Enables Customization
Symmetric: One size fits all
  Energy and performance suboptimal for different phase behaviors
Asymmetric: Enables tradeoffs and customization
  Processing requirements vary across applications and phases
  Execute code on best-fit resources (minimal energy, adequate perf.)
C4
C4
C5
C5
C4
C4
C5
C5
C2
C3
C1
Asymmetric
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
Symmetric

## Slide 115: Thought Experiment: Asymmetry Everywhere
Design each hardware resource with asymmetric, (re-)configurable, partitionable components
  Different power/performance/reliability characteristics
  To fit different computation/access/communication patterns

## Slide 116: Thought Experiment: Asymmetry Everywhere
Design the runtime system (HW & SW) to automatically choose the best-fit components for each workload/phase
  Satisfy performance/SLA with minimal energy
  Dynamically stitch together the “best-fit” chip for each phase

## Slide 117: Thought Experiment: Asymmetry Everywhere
Morph software components to match asymmetric HW components
  Multiple versions for different resource characteristics

## Slide 118: Many Research and Design Questions
How to design asymmetric components?
  Fixed, partitionable, reconfigurable components?
  What types of asymmetry? Access patterns, technologies?
What monitoring to perform cooperatively in HW/SW?
  Automatically discover phase/task requirements
How to design feedback/control loop between components and runtime system software?
How to design the runtime to automatically manage resources?
  Track task behavior, pick “best-fit” components for the entire workload

## Slide 119: Exploiting Asymmetry: Simple Examples
Execute critical/serial sections on high-power, high-performance cores/resources [Suleman+ ASPLOS’09, ISCA’10, Top Picks’10’11, Joao+ ASPLOS’12]
  Programmer can write less optimized, but more likely correct programs

## Slide 120: Exploiting Asymmetry: Simple Examples
Execute streaming “memory phases” on streaming-optimized cores and memory hierarchies
  More efficient and higher performance than general purpose hierarchy

## Slide 121: Exploiting Asymmetry: Simple Examples
Partition memory controller and on-chip network bandwidth asymmetrically among threads [Kim+ HPCA 2010, MICRO 2010, Top Picks 2011] [Nychis+ HotNets 2010] [Das+ MICRO 2009, ISCA 2010, Top Picks 2011]
  Higher performance and energy-efficiency than symmetric/free-for-all

## Slide 122: Exploiting Asymmetry: Simple Examples
Have multiple different memory scheduling policies; apply them to different sets of threads based on thread behavior [Kim+ MICRO 2010, Top Picks 2011] [Ausavarungnirun, ISCA 2012]
  Higher performance and fairness than a homogeneous policy

## Slide 123: Exploiting Asymmetry: Simple Examples
Build main memory with different technologies with different characteristics (energy, latency, wear, bandwidth) [Meza+ IEEE CAL’12]
  Map pages/applications to the best-fit memory resource
  Higher performance and energy-efficiency than single-level memory
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)