## Slide 1: 18-447 Computer Architecture Lecture 23: Memory Management
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2015, 3/27/2015

## Slide 2: Where We Are in Lecture Schedule
The memory hierarchy
Caches, caches, more caches
Virtualizing the memory hierarchy: Virtual Memory
Main memory: DRAM
Main memory control, scheduling
Memory latency tolerance techniques
Non-volatile memory
Multiprocessors
Coherence and consistency
Interconnection networks
Multi-core issues (e.g., heterogeneous multi-core)

## Slide 3: Required Reading (for the Next Few Lectures)
Onur Mutlu, Justin Meza, and Lavanya Subramanian, "The Main Memory System: Challenges and Opportunities" Invited Article in Communications of the Korean Institute of Information Scientists and Engineers (KIISE), 2015.
http://users.ece.cmu.edu/~omutlu/pub/main-memory-system_kiise15.pdf

## Slide 4: Required Readings on DRAM
DRAM Organization and Operation Basics
  Sections 1 and 2 of: Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
  http://users.ece.cmu.edu/~omutlu/pub/tldram_hpca13.pdf
  Sections 1 and 2 of Kim et al., “A Case for Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
  http://users.ece.cmu.edu/~omutlu/pub/salp-dram_isca12.pdf
DRAM Refresh Basics
  Sections 1 and 2 of Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012. http://users.ece.cmu.edu/~omutlu/pub/raidr-dram-refresh_isca12.pdf

## Slide 5: Memory Interference and Scheduling in Multi-Core Systems

## Slide 6: Review: A Modern DRAM Controller

## Slide 7: (Un)expected Slowdowns in Multi-Core
Low priority
High priority
(Core 0)
(Core 1)
Moscibroda and Mutlu, “Memory performance attacks: Denial of memory service
in multi-core systems,” USENIX Security 2007.
Notes: What kind of performance do we expect when we run two applications on a multi-core system? To answer this question, we performed an experiment. We took two applications we cared about, ran them together on different cores in a dual-core system, and measured their slowdown compared to when each is run alone on the same system. This graph shows the slowdown each app experienced. (DATA explanation…)
Why do we get such a large disparity in the slowdowns?
Is it the priorities? No. We went back and gave high priority to gcc and low priority to matlab. The slowdowns did not change at all. Neither the software or the hardware enforced the priorities.
Is it the contention in the disk? We checked for this possibility, but found that these applications did not have any disk accesses in the steady state. They both fit in the physical memory and therefore did not interfere in the disk.
What is it then? Why do we get such large disparity in slowdowns in a dual core system?
I will call such an application a “memory performance hog”
Now, let me tell you why this disparity in slowdowns happens.
Is it that there are other applications or the OS interfering with gcc, stealing its time quantums? No.

## Slide 8: Memory Scheduling Techniques
We covered
  FCFS
  FR-FCFS
  STFM (Stall-Time Fair Memory Access Scheduling)
  PAR-BS (Parallelism-Aware Batch Scheduling)
  ATLAS
  TCM (Thread Cluster Memory Scheduling)
There are many more …
See your required reading (Section 7):
  Mutlu et al., “The Main Memory System: Challenges and Opportunities,” KIISE 2015.

## Slide 9: Other Ways of Handling Memory Interference

## Slide 10: Fundamental Interference Control Techniques
Goal: to reduce/control inter-thread memory interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling

## Slide 11: Observation: Modern Systems Have Multiple Channels
A new degree of freedom
Mapping data across multiple channels
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 12: Data Mapping in Current Systems
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Causes interference between applications’ requests
Page
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 13: Partitioning Channels Between Applications
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Page
Eliminates interference between applications’ requests
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 14: Overview: Memory Channel Partitioning (MCP)
Goal
  Eliminate harmful interference between applications
Basic Idea
  Map the data of badly-interfering applications to different channels
Key Principles
  Separate low and high memory-intensity applications
  Separate low and high row-buffer locality applications
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 15: Key Insight 1: Separate by Memory Intensity
High memory-intensity applications interfere with low memory-intensity applications in shared memory channels
Map data of low and high memory-intensity applications
to different channels
1
2
3
4
5
Channel 0
Bank 1
Channel 1
Bank 0
Conventional Page Mapping
Red App
Blue App
Time Units
Core
Core
Bank 1
Bank 0
Channel Partitioning
Red App
Blue App
Channel 0
Time Units
1
2
3
4
5
Channel 1
Core
Core
Bank 1
Bank 0
Bank 1
Bank 0
Saved Cycles
Saved Cycles

## Slide 16: Key Insight 2: Separate by Row-Buffer Locality
High row-buffer locality applications interfere with low
row-buffer locality applications in shared memory channels
Conventional Page Mapping
Channel 0
Bank 1
Channel 1
Bank 0
R1
R0
R2
R3
R0
R4
Request Buffer State
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
R0
Channel 0
R1
R2
R3
R0
R4
Request Buffer State
Channel Partitioning
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Saved
Cycles
Map data of low and high row-buffer locality applications to different channels

## Slide 17: Memory Channel Partitioning (MCP) Mechanism
1. Profile applications
2. Classify applications into groups
3. Partition channels between application groups
4. Assign a preferred channel to each application
5. Allocate application pages to preferred channel
Hardware
System Software
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 18: Interval Based Operation
time
Current Interval
Next Interval
1. Profile applications
2. Classify applications into groups
3. Partition channels between groups
4. Assign preferred channel to applications
5. Enforce channel preferences

## Slide 19: Observations
Applications with very low memory-intensity rarely access memory  Dedicating channels to them results in precious memory bandwidth waste
They have the most potential to keep their cores busy  We would really like to prioritize them
They interfere minimally with other applications  Prioritizing them does not hurt others

## Slide 20: Integrated Memory Partitioning and Scheduling (IMPS)
Always prioritize very low memory-intensity applications in the memory scheduler
Use memory channel partitioning to mitigate interference between other applications
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 21: Hardware Cost
Memory Channel Partitioning (MCP)
  Only profiling counters in hardware
  No modifications to memory scheduling logic
  1.5 KB storage cost for a 24-core, 4-channel system
Integrated Memory Partitioning and Scheduling (IMPS)
  A single bit per request
  Scheduler prioritizes based on this single bit
Muralidhara et al., “Memory Channel Partitioning,” MICRO’11.

## Slide 22: Performance of Channel Partitioning
1%
5%
Chart: Normalized System Performance
|
FRFCFS | 1
ATLAS | 1.012
TCM | 1.061
MCP | 1.071
IMPS | 1.1108
7%
11%
Better system performance than the best previous scheduler
at lower hardware cost
Averaged over 240 workloads

## Slide 23: Combining Multiple Interference Control Techniques
Combined interference control techniques can mitigate interference much more than a single technique alone can do
The key challenge is:
  Deciding what technique to apply when
  Partitioning work appropriately between software and hardware

## Slide 24: Fundamental Interference Control Techniques
Goal: to reduce/control inter-thread memory interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling

## Slide 25: Source Throttling: A Fairness Substrate
Key idea: Manage inter-thread interference at the cores (sources), not at the shared resources
Dynamically estimate unfairness in the memory system
Feed back this information into a controller
Throttle cores’ memory access rates accordingly
  Whom to throttle and by how much depends on performance target (throughput, fairness, per-thread QoS, etc)
  E.g., if unfairness > system-software-specified target then throttle down core causing unfairness & throttle up core that was unfairly treated
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS’10, TOCS’12.

## Slide 26: Fairness via Source Throttling (FST) [ASPLOS’10]
26
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
(limit injection rate and parallelism)
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
⎪
⎨
⎪
⎧
⎩
Slowdown Estimation
Time
Interval 1
Interval 2
Interval 3
Runtime Unfairness
Evaluation
Dynamic
Request Throttling

## Slide 27: Core (Source) Throttling
Idea: Estimate the slowdown due to (DRAM) interference and throttle down threads that slow down others
  Ebrahimi et al., “Fairness via Source Throttling: A Configurable and High-Performance Fairness Substrate for Multi-Core Memory Systems,” ASPLOS 2010.
Advantages
  + Core/request throttling is easy to implement: no need to change the memory scheduling algorithm
  + Can be a general way of handling shared resource contention
  + Can reduce overall load/contention in the memory system
Disadvantages
  - Requires interference/slowdown estimations  difficult to estimate
  - Thresholds can become difficult to optimize  throughput loss

## Slide 28: Fundamental Interference Control Techniques
Goal: to reduce/control interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling
Idea: Pick threads that do not badly interfere with each other to be scheduled together on cores sharing the memory system

## Slide 29: Interference-Aware Thread Scheduling
An example from scheduling in clusters (data centers)
Clusters can be running virtual machines

## Slide 30: Virtualized Cluster
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
How to dynamically schedule VMs onto hosts?
Distributed Resource Management (DRM) policies
Notes: In a virtualized cluster, we have a set of physical hosts, and many virtual machines.
One key question to manage the virtualized cluster is how to dynamic scheduling the virtual machines onto the physical hosts?
To achieve high resource utilization and energy savings, virtualized systems usually employ distributed resource management (DRM) policies to solve this problem.

## Slide 31: Conventional DRM Policies
Core0
Core1
Host
LLC
DRAM
App
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
VM
App
Memory Capacity
CPU
Based on operating-system-level metrics
e.g., CPU utilization, memory capacity demand
Notes: Could will map them in this manner.
Conventional DRM policies, usually make the mapping decision based on operating-system level metrics, such as CPU utilization, memory capacity, and fit the virtual machines into physical hosts dynamically.
Here is an example, let’s use the height to indicate the CPU utilization and the width to indicate the memory capacity demand. If we have four virtual machines like this, we can fit them into the two hosts.

## Slide 32: Microarchitecture-level Interference
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VMs within a host compete for:
  Shared cache capacity
  Shared memory bandwidth
Can operating-system-level metrics capture the microarchitecture-level resource interference?
Notes: However, another key aspect that impact the virtual machines performance is the microarchitecture-level interference.
Virtual machines within a host compete at:
1) …
VMs will evict each other’s data from the last level cache, causing an increase in memory access latency, thus resulting in performance degradation.
2) …
VMs’ memory requests also contend at the different components of main memory, such as channels, ranks, and banks. Also resulting in performance degradation.
One question raised here is: can the operating-system-level metrics reflect the micro-architecture-level resources interference?

## Slide 33: Microarchitecture Unawareness
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
VM | Operating-system-level metrics | 
 | CPU Utilization | Memory Capacity
 | 92% | 369 MB
 | 93% | 348 MB
App
App
STREAM
gromacs
Microarchitecture-level metrics | 
LLC Hit Ratio | Memory Bandwidth
2% | 2267 MB/s
98% | 1 MB/s
VM
App
Memory Capacity
CPU
Notes: Could possibly map VM to Host in this manner. NO topology
Starved.
We profiled many benchmarks and found many of them exhibit the similar CPU utilization and memory capacity demand. Take the STREAM and gromacs for example, their cpu utilization and memory capacity demand are similar.
If we use conventional DRM to schedule them, this is a possible mapping. The two STREAM running on the same host.
However, although the cpu and memory usage are similar, the microarchitecture-level resource are totally different. STREAM…
Gromacs …
Thus in this mapping, this host may already experiencing heavily contention.

## Slide 34: Impact on Performance
Chart: IPC (Harmonic Mean)
| IPC (Harmonic Mean)
Conventional DRM | 0.30788
with Microarchitecture Awareness | 0.45937
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
App
STREAM
gromacs
VM
App
Memory Capacity
CPU
SWAP
Notes: Although the conventional DRM policies now aware of microarchitecture level contention, how much benefit will we get if we considering them?
We did an experiment use the STREAM and groamcs benchmark. When two STREAM are locate on the same host, the harmonic mean of IPC across all the VMs are 0.30.

## Slide 35: Impact on Performance
Chart: IPC (Harmonic Mean)
| IPC (Harmonic Mean)
Conventional DRM | 0.30788
with Microarchitecture Awareness | 0.45937
49%
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
Core0
Core1
Host
LLC
DRAM
VM
App
VM
App
App
STREAM
gromacs
VM
App
Memory Capacity
CPU
We need microarchitecture-level interference awareness in DRM!
Notes: However, after we migrate STREAM to the other host and migrate gromacs back. The performance is improved by nearly fifty percentage.
Which indicate that we need microarchitecture-level interference awareness in distributed resource management.

## Slide 36: A-DRM: Architecture-aware DRM
Goal: Take into account microarchitecture-level shared resource interference
  Shared cache capacity
  Shared memory bandwidth
Key Idea:
  Monitor and detect microarchitecture-level shared resource interference
  Balance microarchitecture-level resource usage across cluster to minimize memory interference while maximizing system performance
Notes: A-DRM takes into account two main sources of interference at the microarchitecture-level,
shared last level cache capacity and
memory bandwidth.
The key idea of A-DRM is to monitors the microarchitecture-level resource usage, and balance it across the cluster.

## Slide 37: A-DRM: Architecture-aware DRM
OS+Hypervisor
VM
App
VM
App
A-DRM: Global Architecture –aware Resource Manager
Profiling Engine
Architecture-aware
Interference Detector
Architecture-aware
Distributed Resource Management (Policy)
Migration Engine
Hosts
Controller
CPU/Memory Capacity
Profiler
Architectural Resource
•••
Architectural Resources
Notes: In addition to conventional DRM, A-DRM add
1) an architectural resource profiler at each host
We add two … to the Controller.
1) An architecture-aware
interference detector is invoked at each scheduling
interval to detect microarchitecture-level shared resource
interference.
2) Once such interference is detected, the architecture-aware DRM policy is used to determine VM migrations to mitigate the detected interference.

## Slide 38: More on Architecture-Aware DRM
Optional Reading
Wang et al., “A-DRM: Architecture-aware Distributed Resource Management of Virtualized Clusters,” VEE 2015.
  http://users.ece.cmu.edu/~omutlu/pub/architecture-aware-distributed-resource-management_vee15.pdf

## Slide 39: Interference-Aware Thread Scheduling
Advantages
  + Can eliminate/minimize interference by scheduling “symbiotic applications” together (as opposed to just managing the interference)
  + Less intrusive to hardware (no need to modify the hardware resources)
Disadvantages and Limitations
  -- High overhead to migrate threads between cores and machines
  -- Does not work (well) if all threads are similar and they interfere

## Slide 40: Summary: Fundamental Interference Control Techniques
Goal: to reduce/control interference
1. Prioritization or request scheduling
2. Data mapping to banks/channels/ranks
3. Core/source throttling
4. Application/thread scheduling
Best is to combine all. How would you do that?

## Slide 41: Handling Memory Interference In Multithreaded Applications

## Slide 42: Multithreaded (Parallel) Applications
Threads in a multi-threaded application can be inter-dependent
  As opposed to threads from different applications
Such threads can synchronize with each other
  Locks, barriers, pipeline stages, condition variables, semaphores, …
Some threads can be on the critical path of execution due to synchronization; some threads are not
Even within a thread, some “code segments” may be on the critical path of execution; some are not

## Slide 43: Critical Sections
Enforce mutually exclusive access to shared data
Only one thread can be executing it at a time
Contended critical sections make threads wait  threads causing serialization can be on the critical path
Each thread:
loop {
Compute
lock(A)
Update shared data
unlock(A)
}
N
C

## Slide 44: Barriers
Synchronization point
Threads have to wait until all threads reach the barrier
Last thread arriving to the barrier is on the critical path
Each thread:
loop1 {
Compute
}
barrier
loop2 {
Compute
}

## Slide 45: Stages of Pipelined Programs
Loop iterations are statically divided into code segments called stages
Threads execute stages on different cores
Thread executing the slowest stage is on the critical path
loop {
Compute1
Compute2
Compute3
}
A
B
C
A
B
C

## Slide 46: Handling Interference in Parallel Applications
Threads in a multithreaded application are inter-dependent
Some threads can be on the critical path of execution due to synchronization; some threads are not
How do we schedule requests of inter-dependent threads to maximize multithreaded application performance?
  Idea: Estimate limiter threads likely to be on the critical path and prioritize their requests; shuffle priorities of non-limiter threads to reduce memory interference among them [Ebrahimi+, MICRO’11]
  Hardware/software cooperative limiter thread estimation:
    Thread executing the most contended critical section
    Thread executing the slowest pipeline stage
    Thread that is falling behind the most in reaching a barrier

## Slide 47: Prioritizing Requests from Limiter Threads
47
Critical Section 1
Barrier
Non-Critical Section
Waiting for Sync or Lock
Thread D
Thread C
Thread B
Thread A
Time
Barrier
Time
Barrier
Thread D
Thread C
Thread B
Thread A
Critical Section 2
Critical Path
Saved Cycles
Limiter Thread:
D
B
C
A
Most Contended Critical Section:
1
Limiter Thread Identification

## Slide 48: More on Parallel Application Memory Scheduling
Optional reading
Ebrahimi et al., “Parallel Application Memory Scheduling,” MICRO 2011.
  http://users.ece.cmu.edu/~omutlu/pub/parallel-memory-scheduling_micro11.pdf

## Slide 49: More on DRAM Management and DRAM Controllers

## Slide 50: DRAM Power Management
DRAM chips have power modes
Idea: When not accessing a chip power it down
Power states
  Active (highest power)
  All banks idle
  Power-down
  Self-refresh (lowest power)
State transitions incur latency during which the chip cannot be accessed

## Slide 51: DRAM Refresh

## Slide 52: DRAM Refresh
DRAM capacitor charge leaks over time
The memory controller needs to refresh each row periodically to restore charge
  Read and close each row every N ms
  Typical N = 64 ms
Downsides of refresh
-- Energy consumption: Each refresh consumes energy
  -- Performance degradation: DRAM rank/bank unavailable while refreshed
  -- QoS/predictability impact: (Long) pause times during refresh
  -- Refresh rate limits DRAM capacity scaling

## Slide 53: DRAM Refresh: Performance
Implications of refresh on performance
  -- DRAM bank unavailable while refreshed
  -- Long pause times: If we refresh all rows in burst, every 64ms the DRAM will be unavailable until refresh ends
Burst refresh: All rows refreshed immediately after one another
Distributed refresh: Each row refreshed at a different time, at regular intervals

## Slide 54: Distributed Refresh
Distributed refresh eliminates long pause times
How else can we reduce the effect of refresh on performance/QoS?
Does distributed refresh reduce refresh impact on energy?
Can we reduce the number of refreshes?

## Slide 55: Refresh Today: Auto Refresh
Columns
Rows
Row Buffer
DRAM CONTROLLER
DRAM Bus
BANK 0
BANK 1
BANK 2
BANK 3
A batch of rows are
periodically refreshed
via the auto-refresh command
Notes: The DRAM system consists of the DRAM banks, the DRAM bus, and the DRAM memory controller. DRAM banks store the data in physical memory. There are multiple DRAM banks to allow multiple memory requests to proceed in parallel.
Each DRAM bank has a 2-dimensional structure, consisting of rows by columns. Data can only be read from a “row buffer”, which acts as a cache that “caches” the last accessed row. As a result, a request that hits in the row buffer can be serviced much faster than a request that misses in the row buffer.
Existing DRAM controllers take advantage of this fact. To maximize DRAM throughput, these controllers prioritize row-hit requests over other requests in their scheduling. All else being equal, they prioritize older accesses over younger accesses. This policy is called the FR-FCFS policy. Note that this scheduling policy is designed for maximizing DRAM throughput and does not distinguish between different threads’ requests at all.
-----------------------------
Explain bank operation at a high level
- An access that is to the row in the row buffer takes a shorter time than to an access that is to another row.
Multiple banks put together to allow for multiple requests to be serviced in parallel
The DRAM controller treats each bank as an independent entity
In each bank, the DRAM controller optimizes for improving row buffer locality to improve DRAM throughput
- It prioritizes row-hit requests over other requests and all else being equal, older requests over younger requests. It is not aware of the different threads accessing it.
The DRAM controller does not coordinate accesses to different banks.
As a result requests of different threads can be serviced in different banks even though a single thread’s requests might be outstanding to multiple banks

## Slide 56: Refresh Overhead: Performance
8%
46%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 57: Refresh Overhead: Energy
15%
47%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 58: Problem with Conventional Refresh
Today: Every row is refreshed at the same rate
Observation: Most rows can be refreshed much less often without losing data [Kim+, EDL’09]
Problem: No support in DRAM for different refresh rates per row

## Slide 59: Retention Time of DRAM Rows
Observation: Only very few rows need to be refreshed at the worst-case rate
Can we exploit this to reduce refresh operations at low cost?

## Slide 60: Reducing DRAM Refresh Operations
Idea: Identify the retention time of different rows and refresh each row at the frequency it needs to be refreshed
(Cost-conscious) Idea: Bin the rows according to their minimum retention times and refresh rows in each bin at the refresh rate specified for the bin
  e.g., a bin for 64-128ms, another for 128-256ms, …
Observation: Only very few rows need to be refreshed very frequently [64-128ms]  Have only a few bins  Low HW overhead to achieve large reductions in refresh operations
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 61: RAIDR: Mechanism
1. Profiling: Profile the retention time of all DRAM rows
 can be done at DRAM design time or dynamically
2. Binning: Store rows into bins by retention time
 use Bloom Filters for efficient and scalable storage
3. Refreshing: Memory controller refreshes rows in different bins at different rates
 probe Bloom Filters to determine refresh rate of a row
1.25KB storage in controller for 32GB DRAM memory

## Slide 62: 1. Profiling

## Slide 63: 2. Binning
How to efficiently and scalably store rows into retention time bins?
  Use Hardware Bloom Filters [Bloom, CACM 1970]
Bloom, “Space/Time Trade-offs in Hash Coding with Allowable Errors”, CACM 1970.

## Slide 64: Bloom Filter
[Bloom, CACM 1970]
Probabilistic data structure that compactly represents set membership (presence or absence of element in a set)
Non-approximate set membership: Use 1 bit per element to indicate absence/presence of each element from an element space of N elements
Approximate set membership: use a much smaller number of bits and indicate each element’s presence/absence with a subset of those bits
  Some elements map to the bits other elements also map to
Operations: 1) insert, 2) test, 3) remove all elements
Bloom, “Space/Time Trade-offs in Hash Coding with Allowable Errors”, CACM 1970.

## Slide 65: Bloom Filter Operation Example
Bloom, “Space/Time Trade-offs in Hash Coding with Allowable Errors”, CACM 1970.

## Slide 66: Bloom Filter Operation Example

## Slide 67: Bloom Filter Operation Example

## Slide 68: Bloom Filter Operation Example

## Slide 69: Bloom Filter Operation Example

## Slide 70: Bloom Filters

## Slide 71: Bloom Filters: Pros and Cons
Advantages
  + Enables storage-efficient representation of set membership
  + Insertion and testing for set membership (presence) are fast
  + No false negatives: If Bloom Filter says an element is not present in the set, the element must not have been inserted
  + Enables tradeoffs between time & storage efficiency & false positive rate (via sizing and hashing)
Disadvantages
  -- False positives: An element may be deemed to be present in the set by the Bloom Filter but it may never have been inserted
  Not the right data structure when you cannot tolerate false positives
Bloom, “Space/Time Trade-offs in Hash Coding with Allowable Errors”, CACM 1970.

## Slide 72: Benefits of Bloom Filters as Refresh Rate Bins
False positives: a row may be declared present in the Bloom filter even if it was never inserted
  Not a problem: Refresh some rows more frequently than needed
No false negatives: rows are never refreshed less frequently than needed (no correctness problems)
Scalable: a Bloom filter never overflows (unlike a fixed-size table)
Efficient: No need to store info on a per-row basis; simple hardware  1.25 KB for 2 filters for 32 GB DRAM system

## Slide 73: Use of Bloom Filters in Hardware
Useful when you can tolerate false positives in set membership tests
See the following recent examples for clear descriptions of how Bloom Filters are used
  Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.
  Seshadri et al., “The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing,” PACT 2012.

## Slide 74: 3. Refreshing (RAIDR Refresh Controller)

## Slide 75: 3. Refreshing (RAIDR Refresh Controller)
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 76: RAIDR: Baseline Design
Refresh control is in DRAM in today’s auto-refresh systems
RAIDR can be implemented in either the controller or DRAM

## Slide 77: RAIDR in Memory Controller: Option 1
Overhead of RAIDR in DRAM controller:
1.25 KB Bloom Filters, 3 counters, additional commands issued for per-row refresh (all accounted for in evaluations)

## Slide 78: RAIDR in DRAM Chip: Option 2
Overhead of RAIDR in DRAM chip:
Per-chip overhead: 20B Bloom Filters, 1 counter (4 Gbit chip)
Total overhead: 1.25KB Bloom Filters, 64 counters (32 GB DRAM)

## Slide 79: RAIDR: Results and Takeaways
System: 32GB DRAM, 8-core; SPEC, TPC-C, TPC-H workloads
RAIDR hardware cost: 1.25 kB (2 Bloom filters)
Refresh reduction: 74.6%
Dynamic DRAM energy reduction: 16%
Idle DRAM power reduction: 20%
Performance improvement: 9%
Benefits increase as DRAM scales in density

## Slide 80: DRAM Refresh: More Questions
What else can you do to reduce the impact of refresh?
What else can you do if you know the retention times of rows?
How can you accurately measure the retention time of DRAM rows?
Recommended reading:
  Liu et al., “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms,” ISCA 2013.

## Slide 81: More Readings on DRAM Refresh
  Liu et al., “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms,” ISCA 2013.
  http://users.ece.cmu.edu/~omutlu/pub/dram-retention-time-characterization_isca13.pdf
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.
  http://users.ece.cmu.edu/~omutlu/pub/dram-access-refresh-parallelization_hpca14.pdf