## Slide 1: 18-447 Computer Architecture Lecture 33: Interconnection Networks
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2015, 4/27/2015

## Slide 2: Logistics
Lab 7 and Lab 8
Final Exam
Midterm II scores
Course grades so far
Course evaluations
740 next semester
Plans for Wed and Fri lectures

## Slide 3: Lab 6 Extra Credit
2.5% Ashish Shrestha (ashresth)
2.5% Amanda Marano (amarano)
2.5% Pete Ehrett (wpe)
2.0% Jared Choi (jaewonch)
2.0% Akshai Subramanian (avsubram)
2.0% Sohil Shah (sohils)
2.0% Raghav Gupta (raghavg)
1.5% Kais Kudrolli (kkudroll)

## Slide 4: Lab 7
Abstract, cycle-level modeling of the memory hierarchy
  L2 Cache and Main Memory Controllers
  A key part of all modern computing systems today
You can submit until May 1 and still get full credit
Feel free to submit the Extra Credit portion as well
  Prefetching
  You can get up to 2% of course grade as extra credit
Remember: The goal is for you to learn…

## Slide 5: Extra Credit Lab 8: Multi-Core Cache Coherence
Completely extra credit (all get 5% for free; can get 5% more)
Last submission accepted on May 10, 11:59pm; no late submissions
Cycle-level modeling of the MESI cache coherence protocol

## Slide 6: Midterm 2 Grade Distribution
AVG = 152
Median = 154
STDDEV = 37
Max = 240
Min = 61

## Slide 7: Midterm 2 Grade Distribution (%)
AVG = 45
Median = 45
STDDEV = 40
Max = 71
Min = 18

## Slide 8: Final Exam: May 5
May 5, 5:30-8:30pm, Location: BH A51
Comprehensive (over all topics in course)
Three cheat sheets allowed
We will (likely) have a review session on Friday
Remember this is 22% of your grade
  I will take into account your improvement over the course
  Know all concepts, especially the previous midterm concepts
  Same advice as before for Midterms I and II

## Slide 9: Course Grades So Far
AVG = 57
Median = 58
STDDEV = 6.5
Max = 66
Min = 43
Max_possible = 71
Max_possible + EC = 87.15
Notes: I will guarantee at least the following grades:
A: 90-100
B: 80-90
C: 70-80
D: 60-70
R: 0-60
I may lower the lowest point of a grade range, but not raise them.

## Slide 10: A Note on 740, Research, Jobs/Internships
I am teaching 740 next semester (Fall 2015)
  Lectures M, W 7:30-9:20pm
  Recitations T 7:30-9:20pm
If you are enjoying 447 and are doing well, you can take it
 feel free to talk with me
If you are excited about Computer Architecture research or looking for a job/internship in this area
 talk with me

## Slide 11: More on 740
740 is the next course in sequence
Time: Lect. MW 7:30-9:20pm, Rect. T 7:30-9:20pm
Content:
  Lectures: More advanced, with a different perspective
  Recitations: Delving deeper into papers, advanced topics
  Readings: Many fundamental and research readings; will do many reviews
  Project: More open ended research project. Proposal  milestones  final poster and presentation
    Done in groups of 1-3
    Focus of the course is the project and critical reviews of readings
  Exams: lighter and fewer
  Homeworks: None

## Slide 12: Course Evaluations (due May 11)
Due May 11, 11:59pm
Please do not forget to fill out the course evaluations
  http://www.cmu.edu/hub/fce/
Your feedback is very important
I read these very carefully, and take into account every piece of feedback
  And, improve the course for the future
Please take the time to write out feedback
  State the things you liked, topics you enjoyed, what you think the course contributed to your learning, what we can improve on
  Please don’t just say “the course is hard and fast paced”
    Because you knew that from the very beginning!

## Slide 13: Extra Credit for Course Evaluations
0.25% extra credit for everyone in the class if more than 90% (i.e., 25) of you fill out the evaluations

## Slide 14: Plan for Wed and Fri Sessions This Week
Wednesday: Informal Q&A Session
  Location: Porch
  Tentative format: Fun, information, food
  Come with questions (about comp arch/systems, and anything else)
  We will have food
Friday: Final Exam Review
  Location: HH 1107
  Tentative format: TAs will go over Midterms I and II and answer your questions

## Slide 15: Where We Are in Lecture Schedule
The memory hierarchy
Caches, caches, more caches
Virtualizing the memory hierarchy: Virtual Memory
Main memory: DRAM
Main memory control, scheduling
Memory latency tolerance techniques
Non-volatile memory
Multiprocessors
Coherence and consistency
In-memory computation and predictable performance
Multi-core issues (e.g., heterogeneous multi-core)
Interconnection networks

## Slide 16: Interconnection Network Basics

## Slide 17: Where Is Interconnect Used?
To connect components
Many examples
  Processors and processors
  Processors and memories (banks)
  Processors and caches (banks)
  Caches and caches
  I/O devices
Interconnection network

## Slide 18: Why Is It Important?
Affects the scalability of the system
  How large of a system can you build?
  How easily can you add more processors?
Affects performance and energy efficiency
  How fast can processors, caches, and memory communicate?
  How long are the latencies to memory?
  How much energy is spent on communication?

## Slide 19: Interconnection Network Basics
Topology
  Specifies the way switches are wired
  Affects routing, reliability, throughput, latency, building ease
Routing (algorithm)
  How does a message get from source to destination
  Static or adaptive
Buffering and Flow Control
  What do we store within the network?
    Entire packets, parts of packets, etc?
  How do we throttle during oversubscription?
  Tightly coupled with routing strategy

## Slide 20: Topology
Bus (simplest)
Point-to-point connections (ideal and most costly)
Crossbar (less costly)
Ring
Tree
Omega
Hypercube
Mesh
Torus
Butterfly
…

## Slide 21: Metrics to Evaluate Interconnect Topology
Cost
Latency (in hops, in nanoseconds)
Contention
Many others exist you should think about
  Energy
  Bandwidth
  Overall system performance

## Slide 22: Bus
All nodes connected to a single link
+ Simple + Cost effective for a small number of nodes
+ Easy to implement coherence (snooping and serialization)
- Not scalable to large number of nodes (limited bandwidth, electrical loading  reduced frequency)
- High contention  fast saturation
0
1
2
3
4
5
6
7

## Slide 23: Point-to-Point
Every node connected to every other
with direct/isolated links
+ Lowest contention
+ Potentially lowest latency
+ Ideal, if cost is no issue
-- Highest cost
O(N) connections/ports
per node
O(N2) links
-- Not scalable
-- How to lay out on chip?
0
1
2
3
4
5
6
7

## Slide 24: Crossbar
Every node connected to every other with a shared link for each destination
Enables concurrent transfers to non-conflicting destinations
Could be cost-effective for small number of nodes
+ Low latency and high throughput
- Expensive
- Not scalable  O(N2) cost
- Difficult to arbitrate as N increases
Used in core-to-cache-bank
networks in
- IBM POWER5
- Sun Niagara I/II
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 25: Another Crossbar Design
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 26: Sun UltraSPARC T2 Core-to-Cache Crossbar
High bandwidth interface between 8 cores and 8 L2 banks & NCU
4-stage pipeline: req, arbitration, selection, transmission
2-deep queue for each src/dest pair to hold data transfer request

## Slide 27: Bufferless and Buffered Crossbars
Output
Arbiter
Output
Arbiter
Output
Arbiter
Output
Arbiter
Flow
Control
Flow
Control
Flow
Control
Flow
Control
NI
NI
NI
NI
Buffered
Crossbar
0
1
2
3
NI
NI
NI
NI
Bufferless
Crossbar
0
1
2
3
+ Simpler arbitration/ scheduling
+ Efficient support for variable-size packets
- Requires N2 buffers

## Slide 28: Can We Get Lower Cost than A Crossbar?
Yet still have low contention compared to a bus?
Idea: Multistage networks

## Slide 29: Multistage Logarithmic Networks
Idea: Indirect networks with multiple layers of switches between terminals/nodes
Cost: O(NlogN), Latency: O(logN)
Many variations (Omega, Butterfly, Benes, Banyan, …)
Omega Network:
conflict

## Slide 30: Multistage Networks (Circuit Switched)
A multistage network has more restrictions on feasible concurrent Tx-Rx pairs vs a crossbar
But more scalable than crossbar in cost, e.g., O(N logN) for Butterfly
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 crossbar

## Slide 31: Multistage Networks (Packet Switched)
Packets “hop” from router to router, pending availability of the next-required switch and buffer
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 router

## Slide 32: Aside: Circuit vs. Packet Switching
Circuit switching sets up full path before transmission
  Establish route then send data
  Noone else can use those links while “circuit” is set
  + faster arbitration
  -- setting up and bringing down “path” takes time
Packet switching routes per packet in each router
  Route each packet individually (possibly via different paths)
  If link is free, any packet can use it
  -- potentially slower --- must dynamically switch
  + no setup, bring down time
  + more flexible, does not underutilize links

## Slide 33: Switching vs. Topology
Circuit/packet switching choice independent of topology
It is a higher-level protocol on how a message gets sent to a destination
However, some topologies are more amenable to circuit vs. packet switching

## Slide 34: Another Example: Delta Network
Single path from source to destination
Each stage has different routers
Proposed to replace costly crossbars as processor-memory interconnect
Janak H. Patel ,“Processor-Memory Interconnections for Multiprocessors,” ISCA 1979.
8x8 Delta network

## Slide 35: Another Example: Omega Network
Single path from source to destination
All stages are the same
Used in NYU Ultracomputer
Gottlieb et al. “The NYU Ultracomputer - Designing an MIMD Shared Memory Parallel Computer,” IEEE Trans. On Comp., 1983.

## Slide 36: Ring
Each node connected to exactly two other nodes. Nodes form a continuous pathway such that packets can reach any node.
+ Cheap: O(N) cost
- High latency: O(N)
- Not easy to scale
- Bisection bandwidth remains constant
Used in Intel Haswell,
Intel Larrabee, IBM Cell,
many commercial systems today
Notes: KSR machine, Hector

## Slide 37: Unidirectional Ring
Single directional pathway
Simple topology and implementation
  Reasonable performance if N and performance needs (bandwidth & latency) still moderately low
  O(N) cost
  N/2 average hops; latency depends on utilization
R
0
R
1
R
N-2
R
N-1
2
2x2 router

## Slide 38: Bidirectional Rings
Multi-directional pathways, or multiple rings
+ Reduces latency
+ Improves scalability
- Slightly more complex injection policy (need to select which ring to inject a packet into)

## Slide 39: Hierarchical Rings
+ More scalable
+ Lower latency
- More complex

## Slide 40: More on Hierarchical Rings
Rachata+, “Design and Evaluation of Hierarchical Rings with Deflection Routing,” SBAC-PAD 2014.
  http://users.ece.cmu.edu/~omutlu/pub/hierarchical-rings-with-deflection_sbacpad14.pdf
Discusses the design and implementation of a mostly-bufferless hierarchical ring

## Slide 41: Mesh
Each node connected to 4 neighbors (N, E, S, W)
O(N) cost
Average latency: O(sqrt(N))
Easy to layout on-chip: regular and equal-length links
Path diversity: many ways to get from one node to another
Used in Tilera 100-core
And many on-chip network
prototypes
Notes: e.g. Tile64

## Slide 42: Torus
Mesh is not symmetric on edges: performance very sensitive to placement of task on edge vs. middle
Torus avoids this problem
+ Higher path diversity (and bisection bandwidth) than mesh
- Higher cost
- Harder to lay out on-chip
- Unequal link lengths

## Slide 43: Torus, continued
Weave nodes to make inter-node latencies ~constant

## Slide 44: Trees
Planar, hierarchical topology
Latency: O(logN)
Good for local traffic
+ Cheap: O(N) cost
+ Easy to Layout
- Root can become a bottleneck
Fat trees avoid this problem (CM-5)
Fat Tree

## Slide 45: CM-5 Fat Tree
Fat tree based on 4x2 switches
Randomized routing on the way up
Combining, multicast, reduction operators supported in hardware
  Thinking Machines Corp., “The Connection Machine CM-5 Technical Summary,” Jan. 1992.

## Slide 46: Hypercube
“N-dimensional cube” or “N-cube”
Latency: O(logN)
Radix: O(logN)
#links: O(NlogN)
+ Low latency
- Hard to lay out in 2D/3D
0000
0101
0100
0001
0011
0010
0110
0111
1000
1101
1100
1001
1011
1010
1110
1111
Notes: Popular in early message-passing computers (e.g., intel iPSC, NCUBE)

## Slide 47: Caltech Cosmic Cube
64-node message passing machine
Seitz, “The Cosmic Cube,” CACM 1985.

## Slide 48: Interconnection Network Basics
Topology
  Specifies the way switches are wired
  Affects routing, reliability, throughput, latency, building ease
Routing (algorithm)
  How does a message get from source to destination
  Static or adaptive
Buffering and Flow Control
  What do we store within the network?
    Entire packets, parts of packets, etc?
  How do we throttle during oversubscription?
  Tightly coupled with routing strategy

## Slide 49: Handling Contention
Two packets trying to use the same link at the same time
What do you do?
  Buffer one
  Drop one
  Misroute one (deflection)
Tradeoffs?

## Slide 50: Bufferless Deflection Routing
Destination
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.1
1Baran, “On Distributed Communication Networks.” RAND Tech. Report., 1962 / IEEE Trans.Comm., 1964.
New traffic can be injected
whenever there is a free
output link.

## Slide 51: Bufferless Deflection Routing
Input buffers are eliminated: packets are buffered in pipeline latches and on network links
North
South
East
West
Local
North
South
East
West
Local
Deflection Routing Logic
Input Buffers

## Slide 52: Routing Algorithm
Three Types
  Deterministic: always chooses the same path for a communicating source-destination pair
  Oblivious: chooses different paths, without considering network state
  Adaptive: can choose different paths, adapting to the state of the network
How to adapt
  Local/global feedback
  Minimal or non-minimal paths

## Slide 53: Deterministic Routing
All packets between the same (source, dest) pair take the same path
Dimension-order routing
  First traverse dimension X, then traverse dimension Y
  E.g., XY routing (used in Cray T3D, and many on-chip networks)
+ Simple
+ Deadlock freedom (no cycles in resource allocation)
- Could lead to high contention
- Does not exploit path diversity

## Slide 54: Deadlock
No forward progress
Caused by circular dependencies on resources
Each packet waits for a buffer occupied by another packet downstream

## Slide 55: Handling Deadlock
Avoid cycles in routing
  Dimension order routing
    Cannot build a circular dependency
  Restrict the “turns” each packet can take
Avoid deadlock by adding more buffering (escape paths)
Detect and break deadlock
  Preemption of buffers

## Slide 56: Turn Model to Avoid Deadlock
Idea
  Analyze directions in which packets can turn in the network
  Determine the cycles that such turns can form
  Prohibit just enough turns to break possible cycles
Glass and Ni, “The Turn Model for Adaptive Routing,” ISCA 1992.

## Slide 57: Oblivious Routing: Valiant’s Algorithm
An example of oblivious algorithm
Goal: Balance network load
Idea: Randomly choose an intermediate destination, route to it first, then route from there to destination
  Between source-intermediate and intermediate-dest, can use dimension order routing
+ Randomizes/balances network load
- Non minimal (packet latency can increase)
Optimizations:
  Do this on high load
  Restrict the intermediate node to be close (in the same quadrant)

## Slide 58: Adaptive Routing
Minimal adaptive
  Router uses network state (e.g., downstream buffer occupancy) to pick which “productive” output port to send a packet to
  Productive output port: port that gets the packet closer to its destination
  + Aware of local congestion
  - Minimality restricts achievable link utilization (load balance)
Non-minimal (fully) adaptive
  “Misroute” packets to non-productive output ports based on network state
  + Can achieve better network utilization and load balance
  - Need to guarantee livelock freedom

## Slide 59: On-Chip Networks
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc
  Buses and crossbars are not scalable
Packet switched
2D mesh: Most commonly used topology
Primarily serve cache misses and memory requests
Notes: One commonly proposed solution is on-chip network (NoC), which allows cores to communicate with a packet switched substrate.
Here is a figure showing an on-chip network that uses a 2d-mesh topology which
is commonly used due to its low layout complexity.
This is also the topology we used for our evaluations, but our mechanism is also applicable to other topologies.
In most multi-core systems, NoC primarily serves cache misses and memory requests.