## Slide 1: bot
Manini Amin, Joseph Wang, Karen Johnson

## Slide 2: Immediate Disaster Information
How can we quickly report the number of victims in an area to first responders?
Key Features:
Detection of humans
Obstacle detection & avoidance
Areas:
Embedded systems: machinery
Signals: Image processing
Software: Detection algorithm

## Slide 3: General Approach
1) Send SOS_bot room layout
2) SOS_bot navigates room and sends images back
3) Detect people in images from SOS_bot

## Slide 4: Challenges
Pathfinding & Obstacle Avoidance
  Traverse room to interest points to take images
  Only outline of room is known
  Obstacles may be placed around the room
Unideal situations
  Overlapping images
  Camera wobble
  People may not be fully visible
  Varying lighting conditions
Machine Learning model designed and implemented by us

## Slide 5: Requirements
Fast and accurate machine learning
  70% mAP on ImageNet dataset
  Computation time < 5s per image on laptop CPU
  Maximum error of +-2 when counting the number of people
Efficient pathfinding
  Determine best path between interest points
  Take best path around obstacle
  May not be more than 2 feet off from an interest point at arrival to a point
  Distance traveled may not be 20% more than calculated optimal distance with obstacles
High image quality
  Resolution must be at least 1080p
  Minimal quality loss from when photo is taken to when it is received
Notes: mAP - mean Average Precision

## Slide 6: Solution Approach- Hardware Components
iRobot create 2
Raspberry pi 3 - Model B
Ultrasonic sensors (HC-SR04)
Raspberry Pi Camera Module V2

## Slide 7: Movement
Occupancy Grid Map
Object Detection from Sensors-> relay to Pi
- serial port connection
Object avoidance
Still photo- sent over wifi to local computer

## Slide 8: People Detection
Deep Learning Approach
Based on Faster RCNN
Implement using Pytorch
ImageNet Database
Trained on Amazon Web Services
Deployed on laptop
Notes: 952K Image Net pics for Person Class
Our model will be based on the pre existing Faster RCNN (Region based Convolutional Neural Networks) as we prefer higher accuracy for our model. Furthermore, we are not aiming to achieve real time detection as can be accomplished by other single shot detector models.

## Slide 9: Obstacle Course
Built by us
Known grid layout
Interest points
Randomly place obstacles
Randomly place people of varying heights/positions
People may not be fully visible
Range of lighting conditions
SOS_bot must traverse this room to an interest point
Neural net must accurately detect the number of people

## Slide 10: Verification Methods
Number of collisions with obstacles
Distance away from point of interest at arrival to point
Distance traveled vs optimal path distance
Photo clarity
Model inference speed
Number of people detected vs actual number of people

## Slide 11: Division of Labor
Karen
  Putting SOS_bot together
  Roomba path planning
  Obstacle Course Design
Manini
  Model Implementation and Design
  Model Testing and Parameter Tuning
Joseph
  Model Design
  Obstacle Avoidance
  User Interface

## Slide 12: Schedule
Notes: Basic Movement - first week
Obstacle avoidance- end of february- early march
Deep learning - April 1st
Obstacle Course - Early April
Bot fully assembled - april 6th
testing - month