## Slide 1
The Bluetooth Audio Rejiggering Instrument (B.A.R.I.)
Team D0: Adam Quinn, Xingran Du, Sam Rainey
Product Pitch
B.A.R.I. is a Bluetooth-enabled audio effects pedal, the first of its kind. With a low price point (< $100 at volume), small form factor, and the ability to connect to any standard Bluetooth speaker, B.A.R.I. enables casual musicians to easily jam with their friends or practice anywhere, without having to buy (and lug around!) bulky audio equipment.
Despite its accessible price point, B.A.R.I. is the only effects unit to offer Bluetooth compatibility, and is highly capable, featuring not only both true-analog and digital audio effects but also dual input channels. B.A.R.I. accepts input from either microphone (XLR) or instrument (1/4”) cables to the same audio channel, enabling a wide range of use cases.
System Architecture
System Description
System Evaluation
Battery
Main Board
Rotary Encoder w/ Button
B.A.R.I - Components View
System Block Diagram
Metric | Result | Pass | Subsystem
Response Latency | ~50ms | ✓ | UI
State Update Time | ~200ms | ✓ | UI
Processing Latency | 1.3ms | ✓ | Microcontroller
Bluetooth Range | 6m | ✓ | RF Module
Effects Implemented | Overdrive, Delay, EQ | ✓ | Analog and Digital Effects
Max Current Draw | 150 mA | ✓ | Power
Est. Battery Life | 10 hrs | ✓ | Power
B.A.R.I - Product Photo
LCD Display
XLR/1/4”
Inputs
Footswitch
Pre-amplifier Circuit
(*prototype version only)
Bluetooth
Module
USB Connector
to Bluetooth Module
LCD Display
Power Switch
Key Specifications
Preamplifier Distortion
(not to exceed)