## Slide 1
Key
Traveling Mind: EEG Controlled Game
Team D4: Chris Liu, Lavender Jiang, Eryn Qian
Product Pitch
Our team develops a mind controlled game, where users fight waves of zombies as the lone peashooter. The system reads user’s brainwave signals via a EEG headset and identifies the control intentions - shoot or hold - from the signal patterns. The software stack could be used in other scenarios too, e.g. enabling people with locomotor disabilities to seamlessly command the compute agents.
Our system is thoroughly tested by 3 different users and after some training, 2 of them are able to survive the game for more than 20s and effectively assert their control intentions for more than 3s.
System Architecture
System Description
System Evaluation
Emotiv Brainware
Denoiser
FIR Bandpass Filter
4 - 35 Hz
Ocular Artifact Removal
EMD
Bluetooth
Emotiv App
LSL
Neural Network
Layer n, n in {1,2,3,4}
Temporal Conv2D for n=1
Batch Normalization
Channel-wise Conv2D
ELU Activation
Dropout
Maxpool for n>1
Flatten + Activation
User Interface
Calibrate
Start
End
Off-the-Shelf
from Emotiv
Software Module
Software Submodule
Processing Computer
EEG Headset
Real-time
control directives
Calibration
data
Calibration
Start Game
Raw EEG data
Starting Screen
NN Sublayer
Table 1: System Test
Test Category | Test Name | Result / Criterion | Pass
Denoising | Ocular Effect Removal | Blinking Spikes Look Attenuated | Y
Denoising | Fidelity of Cleaned Signal | 0.83 / > 0.65 | Y
Denoising | Latency | 0.0035s / <0.01s | Y
Neural Network | Max Binary Classification Accuracy | ~80% / >70% | Y
Neural Network | Latency | 0.05s / <0.1s | Y
UI Rendering | Latency | 0.012s / <0.1s | Y
Green: UI workflow
Black: Data flow
Table 2: User Test
Test Subject | Test Name | Result / Criterion | Pass
Chris | Shoot Peas | 3s / 3s | Y
Chris | Not Shoot | 3s / 3s | Y
Chris | Survive | 20s / 20s | Y
Tianyi | Shoot Peas | 3s / 3s | Y
Tianyi | Not Shoot | ~1s / 3s | N
Tianyi | Survive | ~17s / 20s | N
Eryn | Shoot Peas | 3s / 3s | Y
Eryn | Not Shoot | 3s / 3s | Y
Eryn | Survive | 20s / 20s | Y