## Slide 1
conFFTi — FPGA music synthesizer
Team D8: Michelle Chang, Hongrun Zhou, Jiuling Zhou
Product Pitch
conFFTi is a digital music synthesizer implemented on an FPGA.
It accepts real-time input from a MIDI keyboard, generates and processes audio signals, and outputs 44.1kHz, 16-bit, 2 channel signals through an audio DAC.
conFFTi has a very low latency of 3.3ms, minimal shape distortion of less than 1%, and low frequency distortion of less than 10 cents across notes from C0 to C6.
System Architecture
System Description
System Evaluation
4-note polyphony
  Play up to 4 musical notes at the same time!
8 waveforms to select from the FPGA switches
  Basic waveforms: square, triangle, sine
  Special wavetables: violin, viola, cello, trumpet, french horn
ADSR
  Adjust attack, decay, release and sustain levels via keyboard knobs
Pulse width modulation (PWM)
  Adjust waveform duty cycle via keyboard knob
Unison detune
  Thicken the sound by adjusting keyboard knob
Record and cycle
  Hold down the record key, play up to 4 notes
  Press play button to loop the recording
DE2-115 Cyclone IV FPGA
Latency (including DAC) | 3.30ms
Latency (except DAC) | 940us
Fig. A. Latency from MIDI to DAC is below the 10ms requirement and is undetectable by human ears
ubld.it MIDI breakout board
UDA1334
I2S DAC
Launchkey Novation MINI MkIII
Fig. C. Pitch deviation across all octaves measured in cents; Notes above C6 are not meeting the requirement of less than 10 cents
Fig. B. Shape distortion for signals of different periods;
1% deviation requirement met for all signals