## Slide 1
Tartan’s Gambit
Team E0: Lillie Widmayer, Luis Ortega, Juan Cortes
Product Pitch
Tartan’s Gambit is an integrated software and hardware system that enables a user to play a physical game of chess with a remote opponent via a web application. Due to the pandemic, it can be difficult to see people in person, and an in-person game of chess cannot be played while maintaining 6-feet of social distance. Hence, we have created Tartan’s Gambit. One player makes moves via a web application while the other player makes moves on a physical chessboard with actual pieces. The moves made in the real world are detected using computer vision and are translated to be reflected on the web application. The moves made by the web player are communicated to the gantry system which performs the web player’s move on the physical board world.
System Architecture
System Description
System Evaluation
Hardware Block Diagram
Arduino
Raspberry Pi
Camera
CNC Shield
12V Input Voltage + GND
12V Stepper
A4988 Driver
5V Stepper
A4988 Driver
12V Stepper
A4988 Driver
GND 5V Input Voltage
Coolant EN Pin
5V Input Voltage + GND
USB Serial
9g Servo
Legend
Claw
X-Y Gantry
Software Flow Diagram
Raspberry Pi
12V Steppers
Arduino
Chessboard
Front View of Entire System
Camera
Servo
5V Stepper
Claw
Elevator
Height Stands
Elevator Gripper Close Up
Servo
Claw
Guide
Rails
Grip Pads
Pulley
5V Stepper
Yarn
Free Gear
Requirements | How it is Met
Remote play | Physical and virtual boards communicate via http requests and sockets.
Synchronous board states | Webserver synchronised with the physical board every 5 seconds
Low false positives from move detection | OpenCV pauses calculations while movement is occurring within its field of view
Gantry does not interfere with other pieces | Each piece is lifted above the height of the tallest piece (King) before commencing any XY movement
High accuracy of move detection | OpenCV bases the location of the moves on where the center of the pieces lie, minimizing edge cases
No turns detected if player decides not to place a moved piece | The OpenCV will not report and forward moves to the webserver if only one square is calculated to have been involved
Requirements Met
Accuracy Test Chart