## Slide 1
Anywhere Piano
Team B6: Lee Poirier, Nish Nilakantan, Caroline Liu
18-500 Capstone Design, Spring 2023
Electrical and Computer Engineering Department
Carnegie Mellon University
System Architecture
Product Pitch
Problem
Music composition and arrangement requires using a piano (not portable & lacks accessibility). Online synthesizers are not user-friendly & robust, and lack pressure-controlled volume.
Solution
User will wear a glove of sensors, play notes on a printed piano key layout, use phone camera CV to detect notes, and desktop for UI.
http://course.ece.cmu.edu/~ece500/projects/s23-teamb6/
System Description
System Evaluation
Conclusions & Additional Information
Interface Subsystem
Computer Vision Subsystem
Gloves Subsystem
Calibration screen, Camera view of Keyboard
Further Design Extensions
Synth Engine
  MIDI Capabilities
More Volume Levels
  Increase thresholding accuracy
Interface
  Pedal capabilities
  More accurate resonance for loud + soft notes
Left Hand:
Arduino BLE Nano
5x MD 30-60 Pressure Sensor
3x AA Batteries
Right Hand:
Arduino BLE Nano
5xMD 30-60 Pressure Sensor
3x AA Batteries
49 Keys
Mount to hold phone directly above user
Contour Detection
Warp Homography
Manual Points
Finger Identification
Localization
Media Pipe
Accesses stream from phone camera
Bluetooth information
Send and receive information
Multiple notes through speaker output
Key Identification
Thresholding
Edge Detection
Segmentation
Test | Method | Goal | Result
Warp Consistency | 25 Test Images | 95% | 80%
Key Segmentation | 25 Test Images, with successful warp | 95% | 84%
Key Identification | 25 Test Images, with successful warp | 100% | 84%
Multi-Note Volume Comparison | Play 48 successive notes and compare decibel output <1-2 dB difference | 9/10 notes -> 90% accuracy | 100%
Multi-Note Volume Threshold | Play 48 “loud” notes and check they don’t overpower the speaker (go above 70 dB) | 9/10 notes -> 90% accuracy | 100%
Note Accuracy | Play all notes and compare with tuner | 48/49 notes -> 98% accuracy | 100%
Edge Cases | Use one finger to play between two notes 10 times to make sure ties are correctly broken | 9/10 notes -> 90% accuracy | 100%
Design Tradeoff | Before | After | Rationale
Resistors | 68K Ohm | 10K Ohm | Wider range of volume outputs
Microcontroller | STM32 + HC-05 | Arduino BLE Nano | Bluetooth already integrated
App UI | Phone | Desktop PC | Can’t see user interface from phone. No need to convert code to C++ for apple phones.
Finger Identification | Colored Fiducials | Mediapipe | Faster, effective, and more reliable
Camera Angle | 45 degrees | Top-Down view | Easier for warping and ring light more stable
Table 1: Tests, verification, validation + results
Table 2: Design Trade-offs
Fig 5: App Interface
Fig 4: Computer Vision
Fig 3: Paper Keyboard
Fig 2: Gloves
Fig 1: Phone+ Camera