## Slide 1
Fall 2023
Lecture 15: Sparsity
Credit: Brandon Lucia

## Slide 2: Today: Sparse Problems
What is a sparse problem? Why are they called “sparse”?
What makes sparse problems hard?
Roofline performance modeling
Hardware and software strategies for optimizing sparse problems
(with acknowledgements to Vignesh Balaji, CMU ECE PhD 2021, now at Nvidia for contributions to this material)

## Slide 3: Graph Processing Problems are Sparse Problems
Path Planning
Social network analysis
Protein-Protein Interaction
The canonical examples of sparse problems are graph processing applications.

## Slide 4: Machine Learning Problems are Sparse Problems
Graph Convolutional Networks
Data Mining

## Slide 5: What does a graph processing program look like?
for e in EL: dstData[e.dst] =
f(srcData[e.src],dstData[e.dst])
dstData srcData
stores vertex property information
if srcData == dstData, updating in-place;
often “swap” srcData & dstData from 1 iteration to the next iteration

## Slide 6: What does a graph processing program look like?
PageRank(-ish){
for e in EL: rank_n[e.dst] =
rank_nminus1[e.src] + rank_n[e.dst]
}
dstData srcData
rank_n is a webpage’s rank in this iteration,
rank_nminus1 is rank_n from the last iteration

## Slide 7: Graph Analytics can be mapped to Sparse Linear Algebra

## Slide 8: Graph Analytics can be mapped to Sparse Linear Algebra

## Slide 9: Graph Analytics can be mapped to Sparse Linear Algebra

## Slide 10: How do graph applications correspond to linear algebra?
Src
Dst

## Slide 11: How do graph applications correspond to linear algebra?
Src
Dst
1
Initial xi vector is starting vertex for BFS.
=
1
1
T
Matrix-transpose-vector product is one BFS iteration
ATxi = xi+1

## Slide 12: How do graph applications correspond to linear algebra?
Src
Dst
1
Initial xi vector is starting vertex for BFS.
=
1
T
Matrix-transpose-vector product is one BFS iteration
ATxi = xi+1
xi
xi+1
Initial xi+1 is vertices reachable from xi
A Transpose
1

## Slide 13: How do graph applications correspond to linear algebra?
Src
Dst
1
=
1
T
Matrix transpose vector product is one BFS iteration
ATxi = xi+1
The next iteration is computed by performing the next matrix
xi
xi+1
transpose vector product
1
1
1

## Slide 14: How do graph applications correspond to linear algebra?
Src
Dst
=
1
T
Matrix transpose vector product is one BFS iteration
ATxi = xi+1
The next iteration is computed by performing the next matrix
xi
xi+1
1
1
1
transpose vector product
1
1
1
1

## Slide 15: How do graph applications correspond to linear algebra?
Src
Dst
=
1
T
Matrix transpose vector product is one BFS iteration
ATxi = xi+1
The next iteration is computed by performing the next matrix
xi
xi+1
1
1
1
transpose vector product
1
1
1
1
1
1
1
1
1
1
1
1
=
Search done when no new vertices added (or all
visited)

## Slide 16: How do graph applications correspond to linear algebra?
Src
Dst
=
1
T
Turns out that other graph applications also correspond to roughly this formulation if you change the operations you use (min/+ instead of +/*) or consider weighted edges
ATxi = xi+1
SSSP, BFS, PageRank, Connected-Components, Betweenness-Centrality,
triangle counting… BFS is a representative sparse problem.
xi
xi+1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
=
Search done when no new vertices added (or all
visited)

## Slide 17: Nobody EVER uses the adjacency matrix!
Src
Dst
Why would the Adjacency Matrix not be used?

## Slide 18: Nobody EVER uses the adjacency matrix!
Src
Dst
Reasons Adjacency Matrix is never used:
Sparsity: % of Non-Zero Entries ~ 10-5
Total Size: 32M nodes => (32M * 32M) = 1PB

## Slide 19: Compressed Sparse Data Structures for Feasible Memory Size
Src
Dst
Offsets Array (OA)
Neighbors Array (NA)
Compressed Sparse Row (CSR)
Outgoing Neighbors
2 | 1 | 1 | 2 | 1
Vertex Property Array i.e., srcData / dstData
Often we will leave the vertex property array implicitly defined when we talk about sparse structures, but it is always there

## Slide 20: Compressed Sparse Data Structures for Feasible Memory Size
20
Src
Dst
Offsets Array (OA)
Compressed Sparse Row (CSR)
Outgoing Neighbors
Neighbors Array (NA)
EdgeList sorted by SrcIDs
OA indexed by vertex ID of src of edge Value in OA is offset into NA
start index for edges w/ src == vertex i = OA[i]
#edges with src == vertex i = OA[i+1] – OA[i]
Dense encoding of sparse structure
index is src id

## Slide 21: Compressed Sparse Data Structures for Feasible Memory Size
21
Src
Dst
Offsets Array (OA)
Compressed Sparse Row (CSR)
Outgoing Neighbors
Compressed Sparse Column (CSC)
Incoming Neighbors
Neighbors Array (NA)
EdgeList sorted by DstIDs
The CSC is the transpose of the CSR
Offsets Array (OA)
Neighbors Array (NA)
EdgeList sorted by SrcIDs

## Slide 22: Building the CSR / CSC from a Graph’s Edge List
for e in EL: neigh_count[e.dst]++; /*e.src*/
2 | 1 | 1 | 2 | 1
neigh_count

## Slide 23: Building the CSR / CSC from a Graph’s Edge List
for e in EL: neigh_count[e.dst]++; /*e.src*/
2 | 1 | 1 | 2 | 1
neigh_count
neigh_count_dup
sum = 0
for i in 0 .. |V|: tmp = neigh_count[i]
neigh_count[i] = sum; neigh_count_dup[i] = sum; sum += tmp
2 | 1 | 1 | 2 | 1

## Slide 24: Building the CSR / CSC from a Graph’s Edge List
for e in EL: neigh_count[e.dst]++; /*e.src*/
2 | 1 | 1 | 2 | 1
neigh_count
sum = 0
for i in 0 .. |V|: tmp = neigh_count[i]
neigh_count[i] = sum; //OA neigh_count_dup[i] = sum; sum += tmp
0 | 2 | 3 | 4 | 6
OA (also OA_dup)

## Slide 25: Building the CSR / CSC from a Graph’s Edge List
for e in EL:
neigh_ind = OA[e.src] NA[neigh_ind] = e.dst OA[e.src]++ /*sacrificial OA*/
//i.e., NA[ OA[e.src]++ ] = e.dst
0 | 2 | 3 | 4 | 6
OA (also OA_dup)
0 | 2 | 3 | 4 | 6
1 | 2 | 0 | 0 | 0 | 2 | 0
OA_dup
NA
Completed CSC

## Slide 26: Compressed Representations ⇒ Irregular Memory Accesses
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
Pull (CSC Traversal)
OA
NA
CSC
26
from source vertex
dstData
srcData
0 1 2 3 4
e.g., current rank of page I,
e.g., current shortest path
5 | 20 | 10 | 2 | 1
Pull traversal performs irregular read operations that lack locality
i.e., xi+1

## Slide 27: Compressed Representations ⇒ Irregular Memory Accesses
Src
Dst
for src in G:
for dst in out_neighs(src):
dstData[dst] += srcData[src]
Push (CSR Traversal)
OA
NA
dstData
srcData
0 1 2 3 4
e.g., current rank of page I,
5 | 20 | 10 | 2 | 1
Push traversal performs irregular write operations that lack locality
i.e., xi+1
CSR
e.g., current shortest path
from source vertex

## Slide 28: Compressed Representations ⇒ Irregular Memory Accesses
0 1 2 3 4
srcData 5 20 10 2 1
e.g., current rank of page I,
Src
Dst
for src in G:
for dst in out_neighs(src):
dstData[dst] += srcData[src]
Push (CSR Traversal)
OA
NA
Push traversal performs irregular write operations that lack locality
i.e., xi+1
Irregular Data Footprint >> LLC Size
Size of srcData ~ 256MB (32M vertices * 8B)
CSR
e.g., current shortest path
from source vertex
dstData

## Slide 29: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
Running on RMAT27 Graph w/ 35MB LLC
Why such bleak cache performance? Consequence of bleak cache performance?

## Slide 30: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
0 | 0 | 0 | 0 | 0
Dst coordinate of edge is index in dstData:
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Running on RMAT27
Graph w/ 35MB LLC
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
totally input dependent & random!!!

## Slide 31: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
0 | 0 | 0 | 0 | 0
0
miss
Dst coordinate of edge is index in dstData:
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Running on RMAT27
Graph w/ 35MB LLC
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
totally input dependent & random!!!

## Slide 32: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
0 0
0 | 0 | 0 | 0 | 0
miss
Dst coordinate of edge is index in dstData:
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Running on RMAT27
Graph w/ 35MB LLC
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
totally input dependent & random!!!

## Slide 33: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
0 0
0 | 0 | 0 | 0 | 0
(You get lucky sometimes)
hit
Dst coordinate of edge is index in dstData:
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Running on RMAT27
Graph w/ 35MB LLC
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
totally input dependent & random!!!

## Slide 34: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
0 | 0 | 0 | 0 | 0
0
miss
0
Dst coordinate of edge is index in dstData:
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Running on RMAT27
Graph w/ 35MB LLC
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
totally input dependent & random!!!

## Slide 35: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
0 | 0 | 0 | 0 | 0
miss
0
0
Dst coordinate of edge is index in dstData:
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Running on RMAT27
Graph w/ 35MB LLC
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
totally input dependent & random!!!

## Slide 36: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
0 | 0 | 0 | 0 | 0
miss
0 0
Dst coordinate of edge is index in dstData:
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Running on RMAT27
Graph w/ 35MB LLC
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
totally input dependent & random!!!

## Slide 37: Irregular Accesses Lead to Poor Locality
LLC Miss Rate (%)
0 | 0 | 0 | 0 | 0
miss
0 0
Dst coordinate of edge is index in dstData:
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Running on RMAT27
Graph w/ 35MB LLC
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
totally input dependent & random!!!

## Slide 38: Irregular Accesses Lead to Poor Locality
Cycles stalled on DRAM / Total Cycles
LLC Miss Rate (%)
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
Cache miss latency cannot be hidden by anything else in the program. Each miss incurs DRAM latency!

## Slide 39: Irregular Accesses Lead to Poor Locality
Cycles stalled on DRAM / Total Cycles
LLC Miss Rate (%)
Problem: Sparse representations make processing large graphs feasible, but
graph processing still entails a large working set with poor locality
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;

## Slide 40: Even Building the CSR / CSC is an Irregular Access Pattern!
for e in EL: neigh_count[e.dst]++;
2 | 1 | 1 | 2 | 1
neigh_count
Why is this irregular?

## Slide 41: Even Building the CSR / CSC is an Irregular Access Pattern!
for e in EL: neigh_count[e.dst]++; /*e.src*/
2 | 1 | 1 | 2 | 1
neigh_count
Updates to the neigh_count array are to random elements determined by order of edges in edge list

## Slide 42: Even Building the CSR / CSC is an Irregular Access Pattern!
Why is the NA update part irregular?
for e in EL:
NA[ OA[e.src]++ ] = e.dst
0 | 2 | 3 | 4 | 6
1 | 2 | 0 | 0 | 0 | 2 | 0
OA
NA
Completed CSC

## Slide 43: Even Building the CSR / CSC is an Irregular Access Pattern!
Updates to NA based on EL order & OA[e.src] NA[ OA[e.src]++ ] = e.dst
for e in EL:
NA[ OA[e.src]++ ] = e.dst
0 | 2 | 3 | 4 | 6
1 | 2 | 0 | 0 | 0 | 2 | 0
OA
NA
Completed CSC

## Slide 44: Roofline Performance Analysis of Graph Applications
44

## Slide 45: The Roofline Model
45
Throughput (operations per second)
Operational Intensity
(operations per byte)
Compute-
Bound
Peak ops/s
Memory-
Bound
GFLOPS = Giga-Floating
Point Operations Per Second
Yes, this is not a proper acronym

## Slide 46: The Roofline Model
46
Throughput
(GFLOP/s)
Operational Intensity
(FLOPS/Byte)
Memory-
Bound
Compute-
Bound
Peak FLOPS
App 2
App 1
What does Roofline help us understand about a program?

## Slide 47: The Roofline Model
Throughput
(GFLOP/s)
Memory-
Bound
Compute-
Bound
Peak FLOPS
App 2
App 1
What does Roofline help us
understand about a program?
Tell us what limits performance & how close to peak an app is.
Operational Intensity
(FLOPS/Byte)

## Slide 48: The Roofline Model
Throughput
(GFLOP/s)
Memory-
Bound
Compute-
Bound
Peak FLOPS
App 2
App 1
“Ridge point” is a property of a particular machine
What does Roofline help us
understand about a program?
Tell us what limits performance & how close to peak an app is.
Operational Intensity
(FLOPS/Byte)

## Slide 49: The Roofline Model
49
Throughput
(GFLOP/s)
Operational Intensity
(FLOPS/Byte)
Memory-
Bound
Compute-
Bound
Peak FLOPS
App 2
App 1
As a program does more operations per byte, memory has more time to deliver next byte, relieving Mem BW pressure & increasing compute pressure
“Ridge point” is a property of a particular machine

## Slide 50: The Roofline Model
50
Throughput
(GFLOP/s)
Operational Intensity
(FLOPS/Byte)
Memory-
Bound
Compute-
Bound
Peak FLOPS
App 2
“Ridge point” is a property of a particular machine
App 1
What is this point?
As a program does more operations per byte, memory has more time to deliver next byte, relieving Mem BW pressure & increasing compute pressure

## Slide 51: The Roofline Model
51
Throughput
(GFLOP/s)
Operational Intensity
(FLOPS/Byte)
Memory-
Bound
Compute-
Bound
Peak FLOPS
App 2
App 1
What is this point?
As a program does more operations per byte, memory has more time to deliver next byte, relieving Mem BW pressure & increasing compute pressure
Compare App1 and App2. What are they doing differently from one another?

## Slide 52: Operational Intensity of Irregular Graph Applications
for e in EL:
dstData[e.dst] += srcData[e.src]
What is the operational intensity of a random update kernel like this one?

## Slide 53: Operational Intensity of Irregular Graph Applications
for e in EL:
dstData[e.dst] += srcData[e.src]
What is the operational intensity of a random update kernel like this one?
Operations per byte:

## Slide 54: Operational Intensity of Irregular Graph Applications
for e in EL:
dstData[e.dst] += srcData[e.src]
What is the operational intensity of a random
update kernel like this one?
Operations per byte:
Operations: 1 addition
Bytes to Load: 8B for edge, 4B srcData, 4B dstData
Operational Intensity = 1 / (8+4+4) = 1/16

## Slide 55: Graph Applications are Memory-Bound
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak FLOPS
250
Operational Intensity
(FLOPS/Byte)
1/16

## Slide 56: Graph Applications are Memory-Bound
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak FLOPS
250
1/16
DRAM BW utilization in graph apps is ~50%
Operational Intensity
(FLOPS/Byte)
Why would we have spare BW capacity to go to memory and not use it?

## Slide 57: Graph Applications are Memory-Bound
57
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak FLOPS
250
Operational Intensity
(FLOPS/Byte)
1/16
DRAM BW utilization in graph apps is ~50%
Why would we have spare BW capacity to go to memory and not use it?
Don’t know what to fetch
next (no temporal
locality), can’t use extra stuff we fetch (no spatial locality). Limited ability to send more memory requests (limited mem. parallelism).

## Slide 58: Graph Applications are Memory-Bound
58
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak FLOPS
250
Operational Intensity
(FLOPS/Byte)
1/16
How to improve BW utilization?
Option #1: Improve Locality →
Reduce Bytes moved → Improve OI

## Slide 59: Graph Applications are Memory-Bound
59
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak
FLOPS
250
Operational Intensity
(FLOPS/Byte)
1/16
Option #1: Improve Locality →
Reduce Bytes moved → Improve OI
Option #2: Improve Memory to handle more parallel requests
How to improve BW utilization?

## Slide 60: Operational Intensity of Irregular Graph Applications
for e in EL:
dstData[e.dst] += srcData[e.src]
Ideal Best Possible Operational Intensity?
Operations per byte: Operations: 1 addition Bytes to Load: Operational Intensity =

## Slide 61: Ideal Operational Intensity of Irregular Graph Applications
for e in EL:
dstData[e.dst] += srcData[e.src]
Ideal Best Possible Operational Intensity?
Operations per byte:
Operations: 1 addition
Bytes to Load: 8B for edge, 0B srcData, 0B dstData
Operational Intensity = 1 / (8+0+0) = 1/8

## Slide 62: Improving Operational Intensity (OI) by Improving Locality
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak FLOPS
250
1/16 1/8
Operational Intensity
(FLOPS/Byte)

## Slide 63: Improving Operational Intensity (OI) by Improving Locality
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak FLOPS
250
1/16 1/8
Locality wins: If we can operate out of cache, higher ceiling & more leftward ridge point.
Why is cache BW > DRAM BW?
Operational Intensity
(FLOPS/Byte)

## Slide 64: Improving Operational Intensity (OI) by Improving Locality
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak FLOPS
Locality wins: If we can operate out of cache, higher ceiling & more leftward ridge point.
250
Why is cache BW > DRAM BW?
Smaller SRAM caches much faster.
1/16
1/8
Operational Intensity
(FLOPS/Byte)

## Slide 65: Improving Operational Intensity (OI) by Improving Locality
Throughput
(GFLOP/s)
Memory- Bound
Compute- Bound
Peak FLOPS
Locality wins: If we can operate out of cache, higher ceiling & more leftward ridge point.
Key Question: So how do we improve locality, to reduce data movement from memory, to increase OI, and move to peak performance?
250
Why is cache BW > DRAM BW?
Smaller SRAM caches much faster.
1/16
1/8
Operational Intensity
(FLOPS/Byte)

## Slide 66: What did we just learn?
Sparse problems are ones that manipulate large, mostly-zero matrices
Sparsity makes caching a useful part of the matrix hard
Roofline model shows how close to peak perf. an app is
(with acknowledgements to Vignesh Balaji, CMU ECE PhD 2021, now at Nvidia for contributions to this material)