## Slide 1
Fall 2023
Lecture 16: Sparsity, cont
Credit: Brandon Lucia

## Slide 2: Today: Sparse Problems
Hardware and software strategies for optimizing sparse problems
(with acknowledgements to Vignesh Balaji, CMU ECE PhD 2021, now at Nvidia for contributions to this material)

## Slide 3: Propagation Blocking: Optimizing Sparse Irregular Writes to Improve Cache Locality

## Slide 4: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
67
0 | 0 | 0 | 0 | 0
Recall: irregular accesses into
vertex data array based on
e.dst which are essentially random
Bad for the cache: the size of the domain of vertex data array entries is |V|, but the
cache holds only |C| << |V| entries
|Domain| = |V| = 5 vertices
|Cache| = 2 vertices

## Slide 5: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
68
0 | 0 | 0 | 0 | 0
Recall: irregular accesses into
vertex data array based on
e.dst which are essentially random
Bad for the cache: the size of the domain of vertex data array entries is |V|, but the
cache holds only |C| << |V| entries
|Domain| = |V| = 5 vertices
|Cache| = 2 vertices
Key idea in propagation blocking: Limit the domain of updates to a sub-space of vertices,
V*, so that |V*| <= |C| and do multiple sub-spaces of V*s, so that all V*s together = V

## Slide 6: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Create “Bins” that hold input elements (edges
from the edge list)
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
0 1
2 0
1 0
0 2
2 3
0 3
0 4

## Slide 7: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
0 1
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Execute the kernel for one bin at a time
2 0
1 0
0 2
2 3
0 3
0 4

## Slide 8: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
0 1
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Execute the kernel for one bin at a time
2 0
1 0
0 2
2 3
0 3
0 4
0

## Slide 9: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
0 1
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Execute the kernel for one bin at a time
2 0
1 0
0 2
2 3
0 3
0 4
0 0

## Slide 10: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
0 1
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Execute the kernel for one bin at a time
2 0
1 0
0 2
2 3
0 3
0 4
0 0
hit

## Slide 11: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
0 1
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Execute the kernel for one bin at a time
2 0
1 0
0 2
2 3
0 3
0 4
0 0

## Slide 12: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
0 1
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Execute the kernel for one bin at a time
2 0
1 0
0 2
2 3
0 3
0 4
0 0

## Slide 13: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Execute the kernel for one bin at a time
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
0 1
2 0
1 0
0 2
2 3
0 3
0 4
0 0
hit

## Slide 14: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
0 | 0 | 0 | 0 | 0
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
How to decide how many vertices go in
each of your Propagation Blocker’s bins?
Bin 0:
dst 0-1
Bin 1:
dst 2-3
Bin 2:
dst 4-5
0 1
2 0
1 0
0 2
2 3
0 3
0 4
0 0
hit

## Slide 15: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
78
0 | 0 | 0 | 0 | 0
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Match destinations per bin to number of vertices worth of dstData that can fit in cache at one time
Bin 0:
dst 0-2
Bin 1:
dst 3-5
0 1
2 0
1 0
0 2
2 3
0 3
0 0 0
hit
0 4

## Slide 16: Propagation Blocking: Performance Analysis
79
0 | 0 | 0 | 0 | 0
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Traverse the edge list twice instead of once
Bin 0:
dst 0-2
Bin 1:
dst 3-5
0 1
2 0
1 0
0 2
2 3
0 3
0 4
0 0 0
All locations written fit in cache! Compulsory misses on dstData[] only: all the rest hit.
hit
Binning
Bin Read

## Slide 17: Propagation Blocking: Performance Analysis
80
0 | 0 | 0 | 0 | 0
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Traverse the edge list twice instead of once
Bin 0:
dst 0-2
Bin 1:
dst 3-5
0 1
2 0
1 0
0 2
2 3
0 3
0 4
0 0 0
All locations written fit in cache! Compulsory misses on dstData[] only: all the rest hit.
hit
Binning
Bin Read
What about the performance of reading the edge list during binning?

## Slide 18: Propagation Blocking: Performance Analysis
81
0 | 0 | 0 | 0 | 0
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Usually save a little space in cache for
Traverse the edge list twice instead of once streaming edge list data. Easy to cache.
Bin 0:
dst 0-2
Bin 1:
dst 3-5
0 1
2 0
1 0
0 2
2 3
0 3
0 4
0
0
0
Binning
Bin Read
What about propagation blocking for irregular reads?
Streaming
Random Access, but always in cache

## Slide 19: Propagation Blocking
PropagationBlocking_EdgeCount(EdgeList E){
Bins B[];
for edge in E{
add_to_bin( find_bin(edge) )
}
for bin in B{ for e in bin{
dstData[e.dst]++
}
}
}
Application of Propagation Blocking for Graph Applications (Page Rank only, at first) discovered in 2017
(Prior work on “radix partitioning” applied the idea to other domains, but not graphs)

## Slide 20: Cache Locality determines Overall Performance What about better replacement policies?
83

## Slide 21: Existing Replacement Policies Are Insufficient
Lower is Better

## Slide 22: Existing Replacement Policies Are Insufficient
State-of-the-Art
Policies
Lower is Better

## Slide 23: Existing Replacement Policies Are Insufficient
State-of-the-Art
Policies
Marginal Benefit over LRU
Lower is Better

## Slide 24
Existing Replacement Policies Are Insufficient
Marginal Benefit over LRU
Lower
is State-of-the-
Better Art
🏆 Policies
87
Problem: Heuristics used by SOTA policies fail to capture the complex reuse patterns of graph data

## Slide 25: Is It Possible To Do Better Cache Replacement?
E1
...
Enew
Elements
in Cache
Element To Be Inserted
E2
Ek
Belady’s MIN Replacement Policy

## Slide 26: Is It Possible To Do Better Cache Replacement?
E1
...
Enew
Elements
in Cache
Element To Be Inserted
E2
Ek
Belady’s MIN Replacement Policy
Time
Next
References

## Slide 27: Is It Possible To Do Better Cache Replacement?
E1
...
Enew
Elements
in Cache
Element To Be Inserted
E2
Ek
Evict the element accessed furthest in the future
Belady’s MIN Replacement Policy
Time
Next
References

## Slide 28: Is It Possible To Do Better Cache Replacement?
E1
...
Enew
Elements
in Cache
Element To Be Inserted
E2
Ek
Evict the element accessed furthest in the future
Belady’s MIN Replacement Policy
Time
Next
References
Recall: Prescience required. Problem?

## Slide 29: Is It Possible To Do Better Cache Replacement? YES!
E1
...
Enew
Elements
in Cache
Element To Be Inserted
E2
Ek
Evict the element accessed furthest in the future
Time
Key Observation: The Graph’s Transpose Efficiently Encodes Future Accesses 92
Belady’s MIN Replacement Policy
Prescience is a flawed requirement: any hope?

## Slide 30: Key Graph Application Property That Enables Belady’s OPT
93

## Slide 31: Key Graph Application Property That Enables Belady’s OPT
94
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
Pull Execution (CSC Traversal)
OA
NA
CSC

## Slide 32: Key Graph Application Property That Enables Belady’s OPT
95
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
OA
NA
CSC
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
0
D1
D1
. . .
Time
CurrDs Irregular Data Stream tD0
D0
Pull Execution (CSC Traversal)

## Slide 33: Key Graph Application Property That Enables Belady’s OPT
96
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
OA
NA
CSC
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
0
D1
D1
. . .
Time
Key Property: Dst-IDs are like timestamps for irregular accesses
CurrDs Irregular Data Stream
tD0
D0
Pull Execution (CSC Traversal)

## Slide 34: Key Graph Application Property That Enables Belady’s OPT
97
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
OA
NA
CSC
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
0
D1
D1
. . .
Time
CurrDs Irregular Data Stream
tD0
D0
Key Property: Dst-IDs are like timestamps for irregular accesses
Pull Execution (CSC Traversal)

## Slide 35: Key Graph Application Property That Enables Belady’s OPT
98
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
OA
NA
CSC
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
0
D1
D1
. . .
Time
CurrDs Irregular Data Stream
tD0
D0
Key Property: Dst-IDs are like timestamps for irregular accesses
Pull Execution (CSC Traversal)

## Slide 36: Key Graph Application Property That Enables Belady’s OPT
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
OA
NA
CSC
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
0
D1
D1
. . .
Time
srcData[S2] is accessed at D0 ⇒ D1 ⇒ D3
CurrDs Irregular Data Stream
tD0
D0
Key Property: Dst-IDs are like timestamps for irregular accesses
Pull Execution (CSC Traversal)

## Slide 37: Using The Graph’s Transpose For Optimal Replacement

## Slide 38: Using The Graph’s Transpose For Optimal Replacement
Src
Dst
for dst in G:
for src in in_neighs(dst): dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
. . .
Time
CurrDs Irregular Data Stream tD0
D0 D0 D1 D1
Assumptions:
One srcData elem per line
Only irregular data enters the cache
2-way Set-Associative
Pull Execution (CSC Traversal)

## Slide 39: Using The Graph’s Transpose For Optimal Replacement
102
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
. . .
Time
2-way Set-Associative
CurrDs Irregular Data Stream
tD0
D0 D0 D1 D1
Pull Execution (CSC Traversal)

## Slide 40: Using The Graph’s Transpose For Optimal Replacement
103
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
. . .
Time
srcData[S1]
2-way Set-Associative
CurrDs Irregular Data Stream
tD0
D0 D0 D1 D1
Pull Execution (CSC Traversal)

## Slide 41: Using The Graph’s Transpose For Optimal Replacement
104
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
1
. . .
Time
srcData[S1]
srcData[S2]
2-way Set-Associative
CurrDs Irregular Data Stream
tD0
D0 D0 D1
Pull Execution (CSC Traversal)

## Slide 42: Using The Graph’s Transpose For Optimal Replacement
105
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
1
D
1
. . .
Time
srcData[S1]
srcData[S2]
2-way Set-Associative
Which line should we evict?:
srcData[S1]
srcData[S2]
CurrDs Irregular Data Stream
tD0
D0
D0
Pull Execution (CSC Traversal)

## Slide 43: Using The Graph’s Transpose For Optimal Replacement
106
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
1
D
1
. . .
Time
srcData[S1]
srcData[S2]
2-way Set-Associative
Which line should we evict?:
srcData[S1] (nextRef @ D4)
srcData[S2]
D0
D4
Out-Neigh(S1):
CurrDs Irregular Data Stream
tD0
D0
D0
CS R
Pull Execution (CSC Traversal)

## Slide 44: Using The Graph’s Transpose For Optimal Replacement
107
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
1
D
1
. . .
Time
srcData[S1]
srcData[S2]
2-way Set-Associative
Which line should we evict?:
srcData[S1] (nextRef @ D4)
srcData[S2] (nextRef @ D1)
D0 | D1 | D3
Out-Neigh(S2):
CurrDs Irregular Data Stream
tD0
D0
D0
CS R
Pull Execution (CSC Traversal)

## Slide 45: Using The Graph’s Transpose For Optimal Replacement
108
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
1
D
1
. . .
Time
srcData[S1]
srcData[S2]
2-way Set-Associative
Which line should we evict?:
srcData[S1] (nextRef @ D4) ✔️
srcData[S2] (nextRef @ D1)
CurrDs Irregular Data Stream
tD0
D0
D0
Pull Execution (CSC Traversal)

## Slide 46: Using The Graph’s Transpose For Optimal Replacement
109
Src
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
D
1
D
1
. . .
Time
srcData[S1]
srcData[S2]
2-way Set-Associative
Which line should we evict?:
srcData[S1] (nextRef @ D4) ✔️
srcData[S2] (nextRef @ D1)
CurrDs Irregular Data Stream
tD0
D0
D0
Pull Execution (CSC Traversal)
Key Question: how to query next
reference while running the program?

## Slide 47: For a pull execution (CSC-traversal), the transpose (CSR) contains all the necessary OPT replacement information
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] +=
Src srcData[src]
D0 srcData[S1]
D0 srcData[S2]
D0 srcData[S4]
D1 srcData[S2]
D1 srcData[S3]
110
. . .
Using The Graph’s Transpose For Optimal Replacement
Pull Execution (CSC Traversal)
CurrDs Irregular Data t Stream
Which line should we evict?: Time
srcData[S1] ● srcData[S1] (nextRef @ D4)
✔️
● srcData[S2] (nextRef @ D1)
srcData[S2]
2-way Set-Associative

## Slide 48: For a pull execution (CSC-traversal), the transpose (CSR) contains all the necessary OPT replacement information
Dst
for dst in G:
for src in in_neighs(dst):
dstData[dst] +=
Src srcData[src]
D0 srcData[S1]
D0 srcData[S2]
D0 srcData[S4]
D1 srcData[S2]
D1 srcData[S3]
111
. . .
Using The Graph’s Transpose For Optimal Replacement
Pull Execution (CSC Traversal)
CurrDs Irregular Data t Stream
Which line should we evict?: Time
srcData[S1] ● srcData[S1] (nextRef @ D4)
✔️
● srcData[S2] (nextRef @ D1)
srcData[S2]
2-way Set-Associative
For a push execution (CSR-traversal), the transpose (CSC) contains all the necessary OPT replacement information

## Slide 49: Transpose-based OPT (T-OPT) Provides Large Gains

## Slide 50: Transpose-based OPT (T-OPT) Provides Large Gains
1.7X
🏆

## Slide 51: Transpose-based OPT (T-OPT) Incurs Overheads
Src
Dst
Finding Next References Using The Transpose
114
Set-Associative Cache
SrcData[S2]

## Slide 52: Transpose-based OPT (T-OPT) Incurs Overheads
115
Src
Dst
Set-Associative Cache
Finding Next References Using The Transpose
SrcData[S2]
OA
NA
CSR (Transpose)
DRAM Access overhead
Transpose accesses are irregular

## Slide 53: Transpose-based OPT (T-OPT) Incurs Overheads
Src
Dst
Set-Associative Cache
Finding Next References Using The Transpose
SrcData[S2]
OA
NA
CSR (Transpose)
DRAM Access overhead
Runtime Traversal overhead
D0
D1
Out-Neigh(S2):
D3
Need to scan neighbors 116

## Slide 54: Transpose-based OPT (T-OPT) Incurs Overheads
117
Src
Dst
Set-Associative Cache
Finding Next References Using The Transpose
SrcData[S2]
DRAM Access overhead
Question: How do we retrieve the next reference information from the graph’s transpose
without all the cost of traversing the graph?
Runtime Traversal overhead

## Slide 55: Main Technique: Use Quantization To Compress The Transpose
Src
Dst
OA
NA
srcData[S2] Accessed at:
D0 ⇒ D1 ⇒ D3
CSR
(Transpose)
118

## Slide 56: Main Technique: Use Quantization To Compress The Transpose
OA
NA
Dst
Divide execution into coarse-grained epochs
Src
srcData[S2] Accessed at:
D0 ⇒ D1 ⇒ D3
CSR
(Transpose)
119

## Slide 57: Main Technique: Use Quantization To Compress The Transpose
OA
NA
Dst
Divide execution into coarse-grained epochs
Src
srcData[S2] Accessed at:
E0 ⇒ E1
srcData[S2] Accessed at:
D0 ⇒ D1 ⇒ D3
CSR
(Transpose)
120

## Slide 58: Main Technique: Use Quantization To Compress The Transpose
121
OA
NA
CSR
(Transpose)
Dst
Divide execution into coarse-grained epochs
Src
srcData[S2] Accessed at:
E0 ⇒ E1
No. of epochs ⬇ ⇒ Next Ref Quantization ⬆
(accuracy vs metadata size trade-off)
srcData[S2] Accessed at:
D0 ⇒ D1 ⇒ D3

## Slide 59: Main Technique: Use Quantization To Compress The Transpose
122
OA
NA
CSR
(Transpose)
Dst
Divide execution into coarse-grained epochs
Src
Rereference Matrix
(Quantized Transpose)
Quantization enables
compression of transpose data
Size the reref matrix to fit in cache!

## Slide 60: P-OPT Improves Cache Locality

## Slide 61: P-OPT Improves Cache Locality
P-OPT results are only 12% away from the Ideal

## Slide 62: P-OPT’s LLC Miss Reductions Directly Translate To Speedups
P-OPT provides up to 1.56x speedup over LRU. What does this tell us about LRU?
125

## Slide 63: What did we just learn?
Sparse problems are ones that manipulate large, mostly-zero matrices
Sparsity makes caching a useful part of the matrix hard
Roofline model shows how close to peak perf. an app is
Propagation blocking bins updates making irregular data fit in cache
P-OPT is a practical implementation of Belady’s OPT for graphs
(with acknowledgements to Vignesh Balaji, CMU ECE PhD 2021, now at Nvidia for contributions to this material)

## Slide 64: Takeaways
127
P-OPT achieves close to ideal performance (quantization can be an effective tool in making a design practical)
    Creative thinking can provide solutions when hardware can be customized, e.g. lossy compression (epochs) and other-than-LRU prediction (transpose)