## Slide 1: CMU 18-344: Computer Systems and the Hardware/Software Interface Fall 2021, Prof. Brandon Lucia

## Slide 2: Recap: Sparse Problems
What is a sparse problem? Why are they called “sparse”?
What makes sparse problems hard?
Roofline performance modeling
Hardware and software strategies for optimizing sparse problems

## Slide 3: Graph Processing Problems are Sparse Problems
Path Planning
Social network analysis
Protein-Protein Interaction
The canonical examples of sparse problems are graph processing applications.

## Slide 4: What does a graph processing program look like?
for e in EL: dstData[e.dst] =
f(srcData[e.src],dstData[e.dst])
dstData srcData
stores vertex property information
if srcData == dstData, updating in-place;
often “swap” srcData & dstData from 1 iteration to the next iteration

## Slide 5: How do graph applications correspond to linear algebra?
Search done when no new vertices added (or all visited)
5
Src
Dst
=
1
T
ATx = x
i i+1
Turns out that other graph applications also correspond to roughly this formulation if you change the operations you use (min/+ instead of +/*) or consider weighted edges
xi
xi+1
1
1
1
SSSP, BFS, PageRank, Connected-Components, Betweenness-Centrality, triangle counting… BFS is a representative sparse problem.
1
1
1
1
1
1
1
1
1
1
1
1
=

## Slide 6: Compressed Sparse Data Structures for Feasible Memory Size
6
Src
Dst
Offsets Array (OA)
Neighbors Array (NA)
Compressed Sparse Row (CSR)
Outgoing Neighbors
2 | 1 | 1 | 2 | 1
Vertex Property Array i.e., srcData / dstData
Often we will leave the vertex property array implicitly deﬁned when we talk about sparse structures, but it is always there

## Slide 7: Compressed Representations ⇒ Irregular Memory Accesses
Src
Dst
for src in G:
for dst in out_neighs(src): dstData[dst] += srcData[src]
Push (CSR Traversal)
OA
NA
CSR
7
dstData
srcData
0 1 2 3 4
e.g., current rank of page I, e.g., current shortest path from source vertex
5 | 20 | 10 | 2 | 1
Push traversal performs irregular write operations that lack locality
i.e., xi+1

## Slide 8: Irregular Accesses Lead to Poor Locality
Right Figure from “Optimizing Cache Performance for Graph Analytics” ArXiv v1;
Cycles stalled on DRAM / Total Cycles
LLC Miss Rate (%)
Problem: Sparse representations make processing large graphs feasible, but graph processing still entails a large working set with poor locality
8

## Slide 9: Even Building the CSR / CSC is an Irregular Access Pattern!
for e in EL: neigh_count[e.dst]++; /*e.src*/
2 | 1 | 1 | 2 | 1
neigh_count
Updates to the neigh_count array are to random elements determined by order of edges in edge list

## Slide 10: Even Building the CSR / CSC is an Irregular Access Pattern!
Updates to NA based on EL order & OA[e.src] NA[ OA[e.src]++ ] = e.dst
for e in EL:
NA[ OA[e.src]++ ] = e.dst
0 | 2 | 3 | 4 | 6
1 | 2 | 0 | 0 | 0 | 2 | 0
OA
NA
Completed CSC

## Slide 11: Graph Applications are Memory-Bound
11
Throughput
(GFLOP/s)
Compute-Bo und
Memory-Bou nd
Peak FLOPS
Peak Mem BW
250
Operational Intensity
(FLOPS/Byte)
1/16
DRAM BW utilization in graph apps is ~50%
Why would we have spare BW capacity to go to memory and not use it?

## Slide 12: Improving Operational Intensity (OI) by Improving Locality
12
Throughput
(GFLOP/s)
Operational Intensity
(FLOPS/Byte)
Compute-Bo und
Memory-Bou nd
Peak FLOPS
250
1/16 1/8
Peak Cache BW
Peak Mem BW
Locality wins: If we can operate out of cache, higher ceiling & more leftward ridge point.
Why is cache BW > DRAM BW?
Smaller SRAM caches much faster.
Key Question: So how do we improve locality, to reduce data movement from memory, to increase OI, and move to peak performance?

## Slide 13: Propagation Blocking: Optimizing Sparse Irregular Writes to Improve Cache Locality

## Slide 14: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
14
0 | 0 | 0 | 0 | 0
Recall: irregular accesses into vertex data array based on
e.dst which are essentially random
Bad for the cache: the size of the domain of vertex data array entries is |V|, but the
cache holds only |C| << |V| entries
|Domain| = |V| = 5 vertices
|Cache| = 2 vertices

## Slide 15: Propagation Blocking: Reorganize Input to Make Memory Being Randomly Written Fit in Cache
15
0 | 0 | 0 | 0 | 0
Recall: irregular accesses into vertex data array based on
e.dst which are essentially random
Bad for the cache: the size of the domain of vertex data array entries is |V|, but the
cache holds only |C| << |V| entries
|Domain| = |V| = 5 vertices
|Cache| = 2 vertices
Key idea in propagation blocking: Limit the domain of updates to a sub-space of vertices,
V*, so that |V*| <= |C| and do multiple sub-spaces of V*s, so that all V*s together = V

## Slide 16: Propagation Blocking: Performance Analysis
16
0 | 0 | 0 | 0 | 0
dstData
Remember: dstData[e.dst] ++
and e.dst is random, from edge list
Usually save a little space in cache for
Traverse the edge list twice instead of once streaming edge list data. Easy to cache.
Bin 1:
dst 0-2
Bin 1:
dst 3-5
0 | 1
2 | 0
1 0 | 
0 2
2 3
0 3
0 4
0
0
0
Binning
Bin Read
What about the performance of reading the edge list during binning?
Streaming
Random Access, but always in cache

## Slide 17: Propagation Blocking
PropagationBlocking_EdgeCount(EdgeList E){
Bins B[];
for edge in E{
add_to_bin( find_bin(edge) )
}
for bin in B{ for e in bin{
dstData[e.dst]++
}
}
}
Application of Propagation Blocking for Graph Applications (Page Rank only, at first) discovered in 2017 (Prior work on “radix partitioning” applied the idea to other domains, but not graphs)

## Slide 18: Using The Graph’s Transpose For Optimal Replacement
18
Src
Dst
for dst in G:
for src in in_neighs(dst): dstData[dst] += srcData[src]
srcData[S1]
srcData[S2]
srcData[S4]
srcData[S2]
srcData[S3]
1
. . .
Time
srcData[S1]
srcData[S2]
2-way Set-Associative
Which line should we evict?:
srcData[S1] (nextRef @ D4)
srcData[S2] (nextRef @ D1)
CurrDs Irregular Data Stream
tD0
D0 D0 D1 D
Pull Execution (CSC Traversal)

## Slide 19: Transpose-based OPT (T-OPT) Provides Large Gains
19
1.7X

## Slide 20: Main Technique: Use Quantization To Compress The Transpose
20
OA
NA
CSR
(Transpose)
Dst
Divide execution into coarse-grained epochs
Src
Rereference Matrix
(Quantized Transpose)
Quantization enables compression of transpose data

## Slide 21: P-OPT Improves Cache Locality
21
P-OPT results are only 12% away from the Ideal

## Slide 22: P-OPT’s LLC Miss Reductions Directly Translate To Speedups
22
P-OPT provides up to 1.56x speedup over LRU

## Slide 23: Today: Parallel Computer Architectures
Why do we have mainly parallel computers
How do we make caches work with parallelism
Memory consistency models & ordering
Implementing synchronization

## Slide 26
14 nm process
11 metal layers
~1,750,000,000 transistors
~9.19 mm x ~11.08 mm
~101.83 mm² die size
4 CPU cores + 24 GPU EUs

## Slide 27
14 nm process
11 metal layers
~1,750,000,000 transistors
~9.19 mm x ~11.08 mm
~101.83 mm² die size
4 CPU cores + 24 GPU EUs
Shared memory multi-threading

## Slide 28
14 nm process
682.6 mm² die size
76 CPU cores
7,100,000,000 transistors

## Slide 29
Parallel hardware + parallelizable software are a direct application of
Amdahl’s Law
Multi-core parallelism was the primary way to keep performance scaling alive once single-thread performance hit the
wall
Question: How to we architect a
programmable parallel computer
system?

## Slide 30: “Coherence seeks to make the caches of a shared-memory system as functionally invisible as the caches in a single-core system. Correct coherence ensures that a programmer cannot
determine whether and where a system has caches by analyzing the results of loads and stores.”
Excerpt from “Primer on Memory Consistency and Cache Coherence” Mark Hill, 2011

## Slide 31: Cache Coherence

## Slide 32
CPU 1
CPU 2
CPU 3
W
r X=1 |  | 
$ |  | 
$
W
r X=2 |  | 
 | $ | 
Rd X=?
What is the behavior of this parallel program? (X initially 0)

## Slide 33
CPU 1
CPU 2
CPU 3
W
r X=1 |  | 
$ |  | 
$
W
r X=2 |  | 
 | $ | 
Rd X=?
Wr X=1
Wr X=2
Rd X=2
Wr X=1
Wr X=2
Rd X=1 Rd X=0
Wr X=1
Wr X=2

## Slide 34
CPU 1
CPU 2
CPU 3
$
X
++ |  | 
 | $ | 
Rd X=?
What about this example? (X initially 0)
X
++ |  | 
$ |  | 

## Slide 35: CPU 1
CPU 2
CPU 3
X
++ |  | 
$ |  | 
$
X
++ |  | 
 | $ | 
Rd X=?
X++
X++
Rd X=2
X++
X++
Rd X=2
X++
X++
Rd X=1
(and the symmetric case)

## Slide 36
CPU 1
CPU 2
CPU 3
$
X
++ |  | 
 | $ | 
Rd X=?
What assumptions are we making about the system to produce the results 0, 1, and 2?
X
++ |  | 
$ |  | 

## Slide 37
CPU 1
CPU 2
CPU 3
$
X
++ |  | 
 | $ | 
Rd X=?
We assume the updates see one anothers’ results! (Why wouldn’t they?)
X
++ |  | 
$ |  | 

## Slide 38: CPU 1
CPU 2
CPU 3
X
$
X
++ |  | 
 | X=0 | 
Rd X=?
X
++ |  | 
=0 |  | 
X++
X++
Rd X=?
Memory: X=0 CPU1: X=1 CPU2: X=1
Reality: X=2 (?!)
$[X]=1
$[X]=1
So what the heck do we do now?

## Slide 39: CPU 1
CPU 2
CPU 3
X
$
X
++ |  | 
 | X=0 | 
Rd X=?
X
++ |  | 
=0 |  | 
X++
X++
Rd X=?
Memory: X=0 CPU1: X=1 CPU2: X=1
Reality: X=2 (?!)
$[X]=1
$[X]=1
Never let this happen. Caches should be coherent.
“coherence ensures that a programmer cannot determine whether and where a system has caches by analyzing the results of loads and stores”

## Slide 40: Informally Defining Coherence
“Coherence serializes all reads with all updates to the same location by different CPUs/caches, so that each read sees the result of the most recent update by any other”
“Single Writer/Multiple Reader (SWMR) Invariant
+
Data-Value Invariant”

## Slide 41: Epoch Model
$[X]=0
Read/Write X++
Epoch for CPU1 $[X]=1
$[X]=1
Read/WriteX++
Epoch for CPU2$[X]=2
Epoch for all
$[X]=2
Read-onlyRd X=?
$[X]=2
Rd X=?
$[X]=2 $[X]=2
Yay! Corresponds to reality!

## Slide 42: Epoch Model
$[X]=0
Read/Write X++
Epoch for CPU1 $[X]=1
$[X]=1
Read/WriteX++
Epoch for CPU2$[X]=2
Epoch for all
$[X]=2
Read-onlyRd X=?
$[X]=2
Rd X=?
$[X]=2 $[X]=2
Yay! Corresponds to reality!
R/W vs. R-O Epochs directly enforce SWMR
Epoch transitions assume data-value invariant

## Slide 43: What do we need to implement the Epoch Model?
Need to add concept of R/W epoch vs. R-O epoch
Need to add gadget that correctly moves data between epochs

## Slide 44: Cache Coherence Protocol
Add state to each cache line saying whether it is R-O or R/W
Add protocol actions to move lines from state to state based on (1)local memory operations; and (2)other CPUs’ memory operations
Add support to get data from (1)local cache; (2)a remote cache; or (3)main memory, depending on line’s protocol state

## Slide 45: High-level sketch of protocol in action
$[X]=0
Read/Write X++
Epoch for CPU1 $[X]=1
$[X]=1
Read/WriteX++
Epoch for CPU2$[X]=2
Epoch for all
$[X]=2
Read-onlyRd X=?
$[X]=2
Rd X=?
$[X]=2
$[X]=2
(1) CPU1 says “I am is writing X”
Others relinquish cached copies of X
and reply “OK go for it” <enter R/W epoch>
(ditto (1) for CPU2)
CPU1 replies “I have X. Use my copy or get it from memory after I write it back”
(2)
(3)
(ditto (3) for CPU 2) (5)
CPU3 says “I want to read only”
(4)Others reply “OK, we all agree
not to write without saying so”
<enter R-O epoch>

## Slide 46: Cache Coherence Protocol
Per-line coherence states
M
S
I

## Slide 47: Cache Coherence Protocol
Modified (R/W)
Shared (R-O)
Invalid (inaccessible)

## Slide 48: Cache Coherence Protocol Local operations perspective
M
S
I
Locally perform a read
[send requests to share to other CPUs]
Locally perform a write [send invalidations to other CPUs]
Locally perform a write
[send invalidations to other CPUs]
Locally perform a read
Locally perform a read or write

## Slide 49: Cache Coherence Protocol Remote operations perspective
M
S
I
Incoming Invalidation [reply with invalidation acknowledgement]
Incoming request to share [reply with data or write back]
Incoming Invalidation
[reply with invalidation acknowledgement]

## Slide 50: Can we design another state?
M
S
I
?
What should we optimize?

## Slide 51: Can we design another state?
M
S
I
Exclusive Read-only
(Benefit: no invalidation required
to transition from E->M, like from S->M)

## Slide 52: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
Snoopy Coherence
Shared bus for coherence messages

## Slide 53: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
Invalidate X++

## Slide 54: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
X++
Ack
Ack

## Slide 55: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
=1 |  | 
(M)X
Entering CPU1’s write epoch
X++

## Slide 56: Implementing the Protocol
CPU 1 CPU 2 CPU 3
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
=1 |  | 
(M)X $
X++
RdReq Rd X=?

## Slide 57: Implementing the Protocol
CPU 1 CPU 2 CPU 3
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
=1 |  | 
(M)X $
Got it: X=1 X++
Rd X=?
Don’t have it

## Slide 58: Implementing the Protocol
CPU 1 CPU 2 CPU 3
X=1
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
=1 |  | 
(S) X (S)
X++
Rd X=?
Entering R-O epoch

## Slide 59: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
What sucks about Snoopy?

## Slide 60: Implementing the Protocol
CPU 1 CPU 2 CPU 3
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
$
Shared bus
Bus limits scalability due to congestion and complex message arbitration

## Slide 61
Intel Sandybridge Multiprocessor: bi-directional ring network

## Slide 62
Skylake Xeon 2017 2D mesh

## Slide 63: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
Directory-based
Sharers of X
(Effectively) Point to Point Links

## Slide 64: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
Directory-based
Sharers of X

## Slide 65: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
Directory-based
Sharers of X
X++
Who has X?

## Slide 66: Implementing the Protocol
CPU 1 CPU 2 CPU 3
$
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
$ |  | 
Directory-based
Sharers of X
X++
No one does! Proceed!

## Slide 67: Implementing the Protocol
CPU 1 CPU 2 CPU 3
X=1
X
++ |  | 
 | X=1 | 
X Rd X=?
++ |  | 
$ |  | 
Directory-based
Sharers of X
X++
Rd X=?
X++
CPUs 2 and 3 do.
Send them Invalidates!

## Slide 68: Implementing the Protocol
CPU 1 CPU 2 CPU 3
X $
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
=1 |  | 
Benefit: No broadcast on shared bus
Sharers of X

## Slide 69: Implementing the Protocol
CPU 1 CPU 2 CPU 3
X $
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
=1 |  | 
Drawbacks?
Sharers of X
X++

## Slide 70: Implementing the Protocol
CPU 1 CPU 2 CPU 3
X $
X
++ |  | 
 | $ | 
X Rd X=?
++ |  | 
=1 |  | 
Centralized directory won’t scale (In Practice: Distribute Directory)
Sharers of X
Sharers of Y

## Slide 71: Optimization: Non-binding Prefetch
CPU 1 CPU 2 CPU 3
R
d X |  | 
 | X | 
Rd X |  | 
 | X | 
P
F X |  | 
$ |  | 
Prefetch instruction preemptively changes coherence state
Sharers of X
CPU 2
CPU 3

## Slide 72: Optimization: Non-binding Prefetch
CPU 1 CPU 2 CPU 3
X
R
d X |  | 
 | $ | 
Rd X |  | 
 | $ | 
P X
…F X =1 |  | 
=1 |  | 
Benefit?
Owner of X
CPU 2
CPU 3
CPU 1

## Slide 73: Optimization: Speculation
CPU 1 CPU 2
CPU 3
Rd X |  | 
 | $ | 
R
d X |  | 
 | $ | 
i
Speculative operations that squash behave like non-binding pre-fetch
: taken
speculative
f(C) BP X=1 |  | 
X | s | 
Owner of X
CPU 2
CPU 3
CPU 1

## Slide 74
“computers execute operations in a different order than is specified by the program. A correct execution is achieved if the results produced are the same as would be produced by executing the program steps in order. For a multiprocessor computer, such a correct execution by each processor does not guarantee the correct execution of the entire program.”
Excerpt from “How to Make a Multiprocessor Computer That Correctly Executes Multiprocess Program”
LESLIE LAMPORT, 1979

## Slide 75
“The memory consistency model of a shared-memory system specifies the order in which memory operations will appear to execute to the programmer. The memory consistency model affects the process of writing parallel programs and forms an integral part of the entire system, including the architecture, the compiler, and the programming
language.”
Excerpt from “Recent Advances in Memory Consistency Models for Hardware Shared-Memory Systems”
Sarita Adve, et al, 1999

## Slide 76: Memory Consistency

## Slide 77: Memory Consistency Model
Informal Definition:
“Defines the value a read operation may read at each point during the execution”
“Defines the set of legal observable orders of memory operations during an execution”
“Defines which reorderings of memory operations are permitted”

## Slide 78: Coherence is Ordering
Wr X
Wr X
Coherence defines the set of legal orders of accesses to a single memory location
Wr X
Wr X
OR

## Slide 79: Consistency is Ordering
Wr X
Wr Y
Consistency defines the set of legal orders of accesses to multiple memory locations
Wr X
Wr Y
OR

## Slide 80: Sequential Consistency (SC) The simplest, most intuitive memory consistency model
Two Invariants to SC:
Invariant #1: Instructions are executed in program order
Invariant #2:
All processors agree on a total order of executed instructions

## Slide 81: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution

## Slide 82: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X

## Slide 83: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y

## Slide 84: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y

## Slide 85: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y Rd X

## Slide 86: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y Rd X Rd X

## Slide 87: Why is SC Important?
Wr X Rd Y Wr Y Rd X Rd X
Rd Y Wr X
Rd X Rd X Wr Y
SC is the most complex model that we can ask
programmers to think about.
Intuitive (SC)Weird (not SC)
Wr X
Rd Y
Rd X
Wr Y Rd X
SC prohibits all reordering of instructions (Invariant 1)

## Slide 88: Why are Instructions Reordered?
Examples? When does it matter? When does it not matter?

## Slide 89: Reordering #1: Write Buffers
M
CPU |  | 
 |  | Wri
M |  | 
CPU can read its write buffer, but not others’
Buffered writes eventually end up in coherent shared memory
Coherent
CPU
te Buffer
Write Buffer

## Slide 90: Reordering #1: Write Buffers
X=1
r1=Y
Y=1
r2=X
M
M |  | 
Program Initially X == Y == 0
Is r1==r2==0
a valid result?

## Slide 91: Reordering #1: Write Buffers
X=1
r1=Y
Y=1
r2=X
M
M |  | 
Program Initially X == Y == 0
Is r1==r2==0
a valid result?
r1 == r2 == 0 is not SC, but it can happen with write buffers

## Slide 92: Reordering #1: Write Buffers
Execution
r1=Y
Program Initially X == Y == 0
Y=1
r2=X
M |  | 
X=1 |  | 
M |  | 

## Slide 93: Reordering #1: Write Buffers
Execution
r1=Y
r2=X
Y=1 |  | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 94: Reordering #1: Write Buffers
Execution
r1=Y
r2=X
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 95: Reordering #1: Write Buffers
Program Initially X == Y == 0
r2=X
Execution
Y= |  | 
 | 1 | 
M |  | 
r1=Y |  | 
X= |  | 
 | 1 | 
M |  | 

## Slide 96: Reordering #1: Write Buffers
Execution
r2=X |  | 
Y= |  | 
 | 1 | 
M |  | 
r1=Y |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 97: Reordering #1: Write Buffers
Execution
r1=Y [r1 <- 0]
r2=X |  | 
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 98: Reordering #1: Write Buffers
Execution r1=Y [r1 <- 0] r2=X [r2 <- 0]
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 99: Reordering #1: Write Buffers
Execution r1=Y [r1 <- 0] r2=X [r2 <- 0]
M
M |  | 
Program Initially X == Y == 0
Y=1
X=1 (Not SC!)
WBs let reads finish before older writes

## Slide 100: Reordering #2: Write Combining
Coalescing Write Buffer
Program X,Z in same $ line
X=1 Y=1 Z=1
4 word cache line

## Slide 101: Reordering #2: Write Combining
Coalescing Write Buffer
Program X,Z in same $ line
X=1 Y=1 Z=1
X=1

## Slide 102: Reordering #2: Write Combining
Coalescing Write Buffer
Program X,Z in same $ line
X=1 Y=1 Z=1
X=1
Y=1

## Slide 103: Reordering #2: Write Combining
Coalescing Write Buffer
Program X,Z in same $ line
X=1 Y=1 Z=1
X=1
Y=1
Z=1

## Slide 104: Reordering #2: Write Combining
X=1
Y=1
Z=1
Coalescing Write Buffer Coalescing Write Buffer
Y=1
X=1 Z=1
Combining the write to X & Z saves bandwidth, but reorders Z=1 and Y=1

## Slide 105: Reordering #3: Interconnect
Execution
X=1 Y=1
r1=X [r1 <- 1]
r2=Y [r2 <- 0] r3=Y [r3 <- 1] r4=X [r4 <- 0]
Program
X=1 r1=X Y=1 r2=Y
r3=Y r4=X
X=1
Y=1
Y=1
X=1
Variable time cost traversing routed on-chip network

## Slide 106: Reordering #4: Compilers
X = 0
for (1 .. 100)
X = 1
print X
X = 0
X = 1
for (1 .. 100)
print X
X = 0
Hoisted!
The compiler hoists the write out of the loop, permitting new (non-SC) results (e.g., “1 0 0 0 0 0 0...”)

## Slide 107: When is Reordering a Problem? When Executions Aren’t SC

## Slide 108: When is an Execution Not SC? When a memory operation happens before itself
Execution r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1 Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph

## Slide 109: When is an Execution Not SC? When a memory operation happens before itself
Execution r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1 Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
Program Order HB Edge

## Slide 110: When is an Execution Not SC? When a memory operation happens before itself
Execution r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1 Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
Program Order HB Edge Causal Order HB Edge

## Slide 111: When is an Execution Not SC? When a memory operation happens before itself
Execution r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1 Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
If there is a cycle in the happens-before graph, the execution is not SC

## Slide 112: When is an Execution Not SC? When a memory operation happens before itself
X=1
Happens-Before Graph
Y=1 r1=X r3=Y
r2=Y r4=X
If there is a cycle in the happens-before graph, the execution is not SC
Execution X=1 Y=1
r1=X [r1 <- 1]
r2=Y [r2 <- 0] r3=Y [r3 <- 1] r4=X [r4 <- 0]

## Slide 113: So... are Computers Wrong?!
SC is how programmers think.
SC prohibits all reordering of instructions
WBs let reads finish before older writes Combining writes saves bandwidth but reorders writes

## Slide 114
Relaxed Memory Consistency
Relaxed Memory Models permit reorderings, unlike SC

## Slide 115: x86-TSO (intel x86s) “The Write Buffer Memory Model”
r1=Y X=1
r1=Y
Total Store Order - loads may complete before older stores to different locations complete.
Relaxes W->R order

## Slide 116: PSO(SPARC) “The Write Combining Memory Model”
X=1 Z=1 Y=1 Z=1
Partial Store Order - loads and stores may complete before older stores to different locations complete.
Relaxes W->W order

## Slide 117: In General
X=1 Z=1 Y=1 Z=1
r1=Y X=1
r1=Y
W->R W->W
r1=Y r2=X
r1=Y
R->R
Y=1 r2=X
Y=1
R->W
Starting with PSO and relaxing R->R and R->W yields Weak Ordering or Release Consistency (alpha)
Depending on the implementation

## Slide 118: SC and Relaxed Consistency
SC is required for correctness and programmer sanity
+
Reordering is required* for performance
Goal: Ensure SC executions while permitting Relaxed Consistency reorderings
*Usually; the MIPS memory model is SC (surprising!)

## Slide 119: How to ensure SC, but permit reordering?

## Slide 120: Synchronization Prevents Reordering
X=1
Memory fences are another type of synchronization
r1=Y
Memory Fence
Reordering prevented
r1=Y
Fence implementation depends on reordering implementation
TSO: Stall reads until write buffer is empty

## Slide 121: Synchronization For Real Programmers
r1=Y X=1
r1=Y
Direct use of fences possible, but inadvisable. USE A LIBRARY.
Lock Unlock
Memory fences are wrapped up in locks, etc.
Reordering prevented

## Slide 122: Data Races
Y=1
Lock Unlock
Synchronization imposes happens-before on otherwise unordered operations
Data Race: Unordered operations to the same memory location, at least one a write
HB Order: Data race prevented
Lock
r1=Y
Unlock

## Slide 123: Memory Models across the System Stack
Language
Compiler
Architecture
Java/C++: SC for
data-race-free programs
Conservative with reordering when d-r-f can’t be proved
Usually very weak for max optimization (lots of reordering)
Note: fences from “above” ensure SC