## Slide 1
Fall 2023
Lecture 18: Synchronization and Transactional Memory
Credit: Brandon Lucia

## Slide 2: Synchronization and its Implementation

## Slide 3: Review: Synchronization Can Prevent Operation Reordering
X=1
Memory Fence
Memory fences are one type of synchronization
r1=Y
Reordering prevented
r1=Y
Fence implementation depends on reordering implementation

## Slide 4: Review: Synchronization For Real Programmers
Y=1
r1=Y
Memory fences are wrapped up in locks, etc.
Reordering prevented
Unlock
r1=Y
Direct use of fences can be tricky and you will usually use a library
Lock

## Slide 5: Data Races
Y=1
Lock Unlock
Synchronization imposes happens-before on otherwise unordered operations
r1=Y
Unlock
Data Race: Unordered operations to the same memory location, at least one write.
Data race prevented
Lock

## Slide 6: Fences are for (Preventing Re-)Ordering to Avoid Data Races & Ensure Correct Executions
Thread 0 |  |  | Thread 1
r1=Y X=1 | Fence |  | r2=X Y=1 Fence
r1=Y |  |  | r2=X
We will see later that this program can produce very strange results if not sychronized

## Slide 7: Fences are for (Preventing Re-)Ordering to Avoid Data Races & Ensure Correct Executions
Thread 0
r1=X r1++ X=r1
Fence
Thread 1
What happens with this program? Where can we put the fence?
r2=X r2++ X=r2

## Slide 8: Fences are for (Preventing Re-)Ordering to Avoid Data Races & Ensure Correct Executions
r1++
X=r1
Fence
Thread 0
r1=X
Thread 1
r2=X
How about fences everywhere? Does this fix our problem?
r2++
X=r2
Fence
Fence
Fence

## Slide 9: Some programs also require atomicity
r1=X r1++ X=r1
Fence
Thread 0
Thread 1
Fences don’t provide atomicity, but we have other primitives that we can use for atomic operations
r2=X r2++ X=r2
Defining Atomicity:
Given a critical region that requires atomic execution by multiple different threads, all threads’ executions of the region were atomic if the resulting execution is equivalent to some serialization of the atomic regions.

## Slide 10: Some programs also require atomicity
r1=X r1++ X=r1
Serialization #1
r2=X r2++ X=r2
Defining Atomicity:
Given a critical region that requires atomic execution by multiple different threads, all threads’ executions of the region were atomic if the resulting execution is equivalent to some serialization of the atomic regions.
r1=X r1++ X=r1
Serialization #2
r2=X r2++ X=r2

## Slide 11: Mutual exclusion (mutex) locks enforce atomicity (and ordering)
r1=X r1++ X=r1
Thread 0
Thread 1
r2=X r2++ X=r2
Lock Behavior:
A thread acquires a lock L, does stuff while holding L, and then releases lock L.
If a thread tries to acquire L while L is held, the thread keeps trying to acquire L until L is unheld, when its attempt to acquire succeeds.
Lock L
Unlock L
Lock L
Unlock L

## Slide 12: SpinLocks are one implementation of synchronization
r1=X r1++ X=r1
Thread 0
Thread 1
r2=X r2++ X=r2
Lock L
Lock L
Unlock L Unlock L
spinlock(L){
while( sync_bool_compare_and_swap(&L,0,1) == 0 ){
/*do nothing; pause here on some systems*/
}
}
unlock(L){ L = 0; sync_synchronize(); /*mem fence*/ }

## Slide 13: SpinLocks are one implementation of synchronization
spinlock(L){
while( sync_bool_compare_and_swap(&L,0,1) == 0 ){
/*do nothing; pause here on some systems*/
}
}
unlock(L){ L = 0; sync_synchronize(); /*mem fence*/ }
Turtles all the way down?

## Slide 14: SpinLocks are one implementation of synchronization
spinlock(L){
while( sync_bool_compare_and_swap(&L,0,1) == 0 ){
/*do nothing; pause here on some systems*/
}
}
unlock(L){ L = 0; sync_synchronize(); /*mem fence*/ }
175b: | 48 | 8b | 02 |  |  | mov | (%rdx),%rax //load L into %rax
175e: | 48 | 8d | 48 | 01 |  | lea | 0x1(%rax),%rcx //add 1 to %rax, into %rcx
1762: | f0 | 48 | 0f | b1 | 0a | lock | cmpxchg %rcx,(%rdx) //compare & exchange
1767: | 75 | f2 |  |  |  | jne | 175b //loop to mov if cmpxchg fails

## Slide 15: SpinLocks are one implementation of synchronization
spinlock(L){
while( sync_bool_compare_and_swap(&L,0,1) == 0 ){
/*do nothing; pause here on some systems*/
}
}
unlock(L){ L = 0; sync_synchronize(); /*mem fence*/ }
1762: f0 48 0f b1 0a
//if (%rdx) == %rax{
lock cmpxchg %rcx,(%rdx) (%rdx) = %rcx }
Implemented directly in the machine microarchitecture. Even if multiple threads executing, hardware guarantees no inter-thread interactions

## Slide 16: SpinLocks are one implementation of synchronization
spinlock(L){
while( sync_bool_compare_and_swap(&L,0,1) == 0 ){
/*do nothing; pause here on some systems*/
}
}
unlock(L){ L = 0; sync_synchronize(); /*mem fence*/ }
1890:
0f ae f0
mfence Fence

## Slide 17: Lock ordering matters
x++ y++
Thread 0
Lock LX
Lock LY
Thread 1
x++ y++
Lock Ordering:
If you manipulate more than one piece of data in a critical region, you will need to acquire the locks in the same order for all critical regions or face deadlock
Unlock LX Unlock LY
Unlock LX Unlock LY
Lock LX Lock LY
x++ y++
Unlock LY
Unlock LX
Lock LY Lock LX

## Slide 18: Directly Using Compare and Swap
r1=X r1++ X=r1
Thread 0
Thread 1
r2=X r2++ X=r2
Lock L
Unlock L
Lock L
Unlock L
Thread 0
Thread 1
r1 = x + 1
_cas(&x,x,r1)
r2 = x + 1
_cas(&x,x,r2)
How general is a CAS operation for implementing critical regions that need to execute atomically? What are the limitations on a CAS operation?

## Slide 19: Fetch and Add – Further Specializing Atomics
r1=X r1++ X=r1
Thread 0
Thread 1
r2=X r2++ X=r2
Lock L
Unlock L
Lock L
Unlock L
Thread 0
Thread 1
_fna(&x,1)
_fna(&x,1)
1707: f0 48 83 04 d0 01 lock addq $0x1,(%rax,%rdx,8)
How much less general than compare and swap?
sync_fetch_and_add(x,1);

## Slide 20: Transactional Memory – Further Generalizing Atomics
r1=X r1++ X=r1
Thread 0
Thread 1
r2=X r2++ X=r2
Lock L
Unlock L
Lock L
Unlock L
Thread 0
Thread 1
r1 = x + 1
_cas(&x,x,r1)
r2 = x + 1
_cas(&x,x,r2)
Limited by single location that can be updated using a CAS. What if we want to update 3 (or n) different locations (without using a lock)?

## Slide 21: Transactional Memory – Further Generalizing Atomics
r1=X
r1++ X=r1 r2=Y Y++ Y=r2
Thread 0
Lock L
Thread 1 Thread 0 Thread 1
Lock L
r3=X
r3++ X=r3 r2=Y Y++ Y=r2
Unlock L
Unlock L
r1 = x + 1
_cas(&x,x,r1) r2 = y + 1
_cas(&y,y,r2)
How about using multiple CAS operations?
r3 = x + 1
_cas(&x,x,r3) r4 = y + 1
_cas(&y,y,r4)

## Slide 22: Transactional Memory – Further Generalizing Atomics
r1=X
r1++ X=r1 r2=Y Y++ Y=r2
Thread 0
Lock L
Thread 1 Thread 0 Thread 1
Lock L
r3=X
r3++ X=r3 r2=Y Y++ Y=r2
Unlock L
Unlock L
r1 = x + 1
_cas(&x,x,r1) r2 = y + 1
_cas(&y,y,r2)
How about using multiple CAS operations?
Problem: Need atomicity across CAS ops.
r3 = x + 1
_cas(&x,x,r3) r4 = y + 1
_cas(&y,y,r4)

## Slide 23: Transactional Memory: Atomicity for “n-CAS”
Thread 0
Thread 1
xbegin()
r1 = x | + | 1
r2 = y | + | 1
x = r1 |  | 
y = r2 |  | 
xend() |  | 
Transaction attempts to execute atomically, as if protected by a lock
xbegin()
r1 = x | + | 1
r2 = y | + | 1
x = r1 |  | 
y = r2 |  | 
xend() |  | 
xbegin() starts a transaction xend() ends the transaction started by the most recent xbegin()

## Slide 24: Transactional Memory: Atomicity for “n-CAS”
Thread 0
Thread 1
xbegin() r1 = x + 1 r2 = y + 1 x = r1
y = r2
ABORT
Transaction aborts if another thread accesses a location accessed in transaction (or if explicitly aborted)
y = 17

## Slide 25: Transactional Memory: Atomicity for “n-CAS”
Thread 0
Thread 1
xbegin() r1 = x + 1 r2 = y + 1 x = r1
y = r2
ABORT?
Transaction aborts if another thread accesses a location accessed in transaction (or if explicitly aborted)
… = y

## Slide 26: Transactional Memory: Atomicity for “n-CAS”
Thread 0
Thread 1
xbegin() r1 = x + 1 r2 = y + 1 x = r1
y = r2
ABORT?
Transaction aborts if another thread reads a location written by the transaction or writes a location
accessed by the transaction (“Conflicting” accesses)
… = y

## Slide 27: Transactional Memory: Atomicity for “n-CAS”
Thread 0
Thread 1
xbegin() r1 = x + 1 r2 = y + 1 x = r1 ABORT
Reads don’t conflict and
transactions can read-share data
… = y

## Slide 28: What do we do if we have repeated aborts?
Thread 0
Thread 1
xbegin() r1 = x + 1 r2 = y + 1 x = r1 ABORT
xbegin() r1 = x + 1 r2 = y + 1 x = r1 ABORT
xbegin() r1 = x + 1 r2 = y + 1 x = r1 ABORT
xbegin() r1 = x + 1 r2 = y + 1 x = r1 ABORT
xbegin() r1 = x + 1 r2 = y + 1 x = r1
xbegin() r1 = x + 1 r2 = y + 1 x = r1
These threads are contending for memory locations causing repeated aborts.
How to deal with contention in a transactional memory system?

## Slide 29: Lock-based Fallback Path
if(xbegin()==OK){ rlk = read_spinlock(L) r1 = x + 1
r2 = y + 1 x = r1 xend()
}else{
//fallback lock(L) r1 = x+1 r2 = y+1 x = r1
y = r2 unlock(L)
}
Add a fallback path & abort handling code Fallback should use spinlocks, not TM. Why? TM case needs to read spinlock lock word. Why? In fallback, can do arbitrary code.
Can also retry TM version repeatedly before giving up and running fallback. Up to you the programmer what sequence to follow.
Precise Intel TSX syntax is available in the lab handout and tm.h in the lab release files.

## Slide 30: What do we do if we have repeated aborts?
Thread 0
Thread 1
xbegin() r1 = x + 1 r2 = y + 1 x = r1 ABORT
xbegin() r1 = x + 1 r2 = y + 1 x = r1 ABORT
xbegin() r1 = x + 1 r2 = y + 1 x = r1
y = r2
xend()
xbegin() r1 = x + 1 r2 = y + 1
These threads are contending for memory locations causing repeated aborts.
How to deal with contention in a transactional memory system?
Random delay for contention avoidance

## Slide 31: A Note About Lock-based Fallback Paths
for(i = 0..MAX_TRIES){
if(xbegin()){
…; xend(); goto done;
}//abort code here
}
//Fallback code here
lock(Lx); lock(Ly);
r1 = x+1 r2 = y+1 x = r1 y = r2
unlock(Lx); unlock(Ly);
}
done:
//continue
Run your transaction some number of times (MAX_TRIES)
If you commit once, skip past your fallback. Often use ‘goto’…
Locks are tricky in code like this: which locks do you need to
acquire? Often need to acquire them all before you make accesses associated with locks.

## Slide 32: Implementation sketch of TM
LL33$$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | Add TM bit to each cache block Blocks accessed in transaction mark bit All transactional state must fit in cache. |  |  |  | 
 | Set 0 | Line |  |  |  |  |  |  |  |  |  | 
 | Set 1 |  |  |  |  |  |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | TM | Valid | Dirty | Tag | 32 bytes data
 | Set 3 |  |  |  |  |  |  |  |  |  |  | 

## Slide 33: Tracking TM conflicts using coherence msgs
CPU 1 CPU 2 CPU 3
X++
X++ Rd X=?
$ $ $
Invalidate X++
An incoming access request for a block with its TM bit set leads to a conflict and a transactional abort

## Slide 34: Reasons a transaction might abort
Too many blocks with their TM bits set leaves no room for more TM blocks
  Too many defined as “more blocks w/ TM bits set than blocks in a way”
Conflict with another transaction or non-transactional access
  identified through incoming coherence traffic
Explicit xabort() instruction when transactional code concludes transaction is not useful
Other, unspecified, but arbitrary conditions left up to the microarchitects
  I speculate that these are related to internal buffers of fixed capacity

## Slide 35: Why is this reordering situation a problem?
Thread 0 |  |  | Thread 1
r1=Y X=1 | Fence |  | r2=X Y=1 Fence
r1=Y |  |  | r2=X
Reordering independent memory operations that access different locations

## Slide 36
“computers execute operations in a different order than is specified by the program. A correct execution is achieved if the results produced are the same as would be produced by executing the program steps in order. For a multiprocessor computer, such a correct execution by each processor does not guarantee the correct execution of the entire program.”
Excerpt from “How to Make a Multiprocessor Computer That Correctly Executes Multiprocess Program”
LESLIE LAMPORT, 1979

## Slide 37
“The memory consistency model of a shared-memory system specifies the order in which memory operations will appear to execute to the programmer. The memory consistency model affects the process of writing parallel programs and forms an integral part of the entire system, including the architecture, the compiler, and the programming language.”
Excerpt from “Recent Advances in Memory Consistency Models for Hardware Shared-Memory Systems”
Sarita Adve, et al, 1999

## Slide 38: Memory Consistency

## Slide 39: Memory Consistency Model
Informal Definition:
“Defines the value a read operation may read at each point during the execution”
“Defines the set of legal observable orders of memory operations during an execution”
“Defines which reorderings of memory operations are permitted”

## Slide 40: Coherence is Ordering
Wr X
Wr X
Coherence defines the set of legal orders of accesses to a single memory location
Wr X
Wr X
OR

## Slide 41: Consistency is Ordering
Wr X
Wr Y
Consistency defines the set of legal orders of accesses to multiple memory locations
Wr X
Wr Y
OR

## Slide 42: Sequential Consistency (SC) The simplest, most intuitive memory consistency model
Two Invariants to SC:
Invariant #1: Instructions are executed in program order
Invariant #2:
All processors agree on a total order of executed instructions

## Slide 43: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution

## Slide 44: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X

## Slide 45: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y

## Slide 46: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y

## Slide 47: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y Rd X

## Slide 48: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y Rd X Rd X

## Slide 49: Why is SC Important?
Wr X Rd Y Wr Y Rd X Rd X
Rd Y
Wr X
Rd X Rd X Wr Y
SC is the most complex model that we can ask
programmers to think about.
Intuitive (SC) Weird (not SC)
Wr X
Rd Y
Rd X
Wr Y Rd X
SC prohibits all reordering of instructions (Invariant 1)

## Slide 50: Real hardware does not enforce SC
https://developer.arm.com/documentation/den0024/a/Memory-Ordering
The ARMv8 Memory Model:

## Slide 51: Reordering #1: Write Buffers
CPU can read its write
buffer, but not others’
Coherent
Buffered writes eventually end up in coherent shared memory
CPU |  | 
 |  | Wri
M |  | 
CPU |  | 
 |  | Wri
M |  | 
te Buffer
te Buffer

## Slide 52: Reordering #1: Write Buffers
X=1
r1=Y
Y=1
r2=X
M
M |  | 
Program
Initially X == Y == 0
Is r1==r2==0
a valid result?

## Slide 53: Reordering #1: Write Buffers
X=1
r1=Y
Y=1
r2=X
M
M |  | 
Program Initially X == Y == 0
Is r1==r2==0
a valid result?
r1 == r2 == 0 is not SC, but it can happen with write buffers

## Slide 54: Reordering #1: Write Buffers
Execution
r1=Y
Program
Initially X == Y == 0
Y=1
r2=X
M |  | 
X=1 |  | 
M |  | 

## Slide 55: Reordering #1: Write Buffers
Execution
r1=Y
r2=X
Y=1 |  | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program
Initially X == Y == 0

## Slide 56: Reordering #1: Write Buffers
Execution
r1=Y
r2=X
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program
Initially X == Y == 0

## Slide 57: Reordering #1: Write Buffers
Program
Initially X == Y == 0
r2=X
Execution
Y= |  | 
 | 1 | 
M |  | 
r1=Y |  | 
X= |  | 
 | 1 | 
M |  | 

## Slide 58: Reordering #1: Write Buffers
Execution
r2=X |  | 
Y= |  | 
 | 1 | 
M |  | 
r1=Y |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 59: Reordering #1: Write Buffers
Execution
r1=Y [r1 <- 0]
r2=X |  | 
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 60: Reordering #1: Write Buffers
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program
Initially X == Y == 0

## Slide 61: Reordering #1: Write Buffers
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
M
M |  | 
Program
Initially X == Y == 0
Y=1
X=1 (Not SC!)
WBs let reads finish before older writes

## Slide 62: Reordering #2: Write Combining
Coalescing Write Buffer
Program X,Z in same $ line
X=1 Y=1 Z=1
4 word cache line

## Slide 63: Reordering #2: Write Combining
Coalescing Write Buffer
X=1 |  |  |  | 
Program X,Z in same $ line
X=1 Y=1 Z=1

## Slide 64: Reordering #2: Write Combining
X=1 |  |  |  | 
 |  |  | Y=1 | 
Coalescing Write Buffer
Program X,Z in same $ line
X=1 Y=1 Z=1

## Slide 65: Reordering #2: Write Combining
Coalescing Write Buffer
X=1 |  |  |  | 
 |  |  | Y=1 | 
 | Z=1 |  |  | 
Program X,Z in same $ line
X=1 Y=1 Z=1

## Slide 66: Reordering #2: Write Combining
X=1 |  |  |  | 
 |  |  | Y=1 | 
 | Z=1 |  |  | 
Coalescing Write Buffer Coalescing Write Buffer
X=1 | Z=1 |  |  | 
 |  |  | Y=1 | 
Combining the write to X & Z saves bandwidth, but reorders Z=1 and Y=1

## Slide 67: Reordering #3: Interconnect
Execution
X=1
Y=1 r1=X [r1 <- 1] r2=Y [r2 <- 0]
r3=Y [r3 <- 1] r4=X [r4 <- 0]
Program
X=1 r1=X Y=1
r2=Y
r3=Y
r4=X
X=1
Y=1
Y=1
X=1
Variable time cost traversing routed on-chip network

## Slide 68: Reordering #4: Compilers
X = 0
for (1 .. 100)
X = 1
print X
X = 0
X = 1
for (1 .. 100)
print X
X = 0
Hoisted!
The compiler hoists the write out of the loop,
permitting new (non-SC) results (e.g., “1 0 0 0 0 0 0...”)

## Slide 69: When is an Execution Not SC? When a memory operation happens before itself
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1
Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph

## Slide 70: When is an Execution Not SC? When a memory operation happens before itself
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1
Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
Program Order HB Edge

## Slide 71: When is an Execution Not SC? When a memory operation happens before itself
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1 Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
Program Order HB Edge Causal Order HB Edge

## Slide 72: When is an Execution Not SC? When a memory operation happens before itself
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1
Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
If there is a cycle in the happens-before graph, the execution is not SC

## Slide 73: When is an Execution Not SC? When a memory operation happens before itself
X=1
Happens-Before Graph
Y=1 r1=X r3=Y
r2=Y r4=X
If there is a cycle in the happens-before graph, the execution is not SC
Execution
X=1 Y=1
r1=X [r1 <- 1]
r2=Y [r2 <- 0] r3=Y [r3 <- 1] r4=X [r4 <- 0]

## Slide 74: Two Design Constraints at Odds
SC is how programmers think, but restricts all reordering
Reordering allows optimization, but leads to unintuitive non-SC behavior.

## Slide 75
Relaxed Memory Consistency
Relaxed Memory Models permit reorderings, unlike SC

## Slide 76: x86-TSO (intel x86s) “The Write Buffer Memory Model”
r1=Y X=1
r1=Y
Total Store Order - loads may complete before older stores to different locations complete.
Relaxes W->R order

## Slide 77: PSO(SPARC) “The Write Combining Memory Model”
X=1 Z=1 Y=1 Z=1
Partial Store Order - loads and stores may complete before older stores to different locations complete.
Relaxes W->W order

## Slide 78: In General
X=1 Z=1 Y=1 Z=1
r1=Y X=1
r1=Y
W->R W->W
r1=Y r2=X
Y=1
r2=X
r1=Y Y=1
R->R R->W
Starting with PSO and relaxing R->R and R->W yields Weak Ordering or Release Consistency (alpha)
Depending on the implementation

## Slide 79: Implementing Synchronization for Weak Memory Models
What does synchronization have to do to prevent SC violations?
  Flush WB, prevent coalescing/bypassing, impose ordering in network, prevent compiler reorderings
What does synchronization have to do to prevent other kinds of problems?
  Enforce mutually exclusive execution by different threads of critical region, force threads to wait at barriers, enforce wait/notify discipline

## Slide 80: SC and Relaxed Consistency
SC is required for correctness and programmer sanity
+
Reordering is required* for performance
Goal: Ensure SC executions while permitting Relaxed Consistency reorderings
*Usually; MIPS memory model is SC

## Slide 81: Memory Models across the System Stack
Language
Compiler
Architecture
Java/C++: SC for data-race- free programs
Conservative with reordering when d-r-f can’t be proved
Usually very weak for max optimization (lots of reordering)
Note: fences from
“above” ensure SC

## Slide 82: What did we just learn?
Concurrency and parallelism, from the bottom to the top
Coherence and consistency are both memory ordering principles
Synchronization exists to spare you data-races and non-SC executions
Transactional memory is a powerful sync primitive in many x86 CPUs