## Slide 1
Fall 2023
Lecture 4: ISAs: The RISC-V ISA
Credit: Brandon Lucia

## Slide 2: What is a Computer Architecture?
Building up to our first architecture
Defining the ISA: Architecture vs. Microarchitecture
RISC vs. CISC ISAs
RISCV ISA

## Slide 3: Recap: What is a Computer Architecture?
Building up to our first architecture
Defining the ISA: Architecture vs. Microarchitecture
RISC vs. CISC ISAs
RISCV ISA

## Slide 4: Basic Architecture: State + processing elements
Maintain State (sequential logic)
Process (combinational logic)
control
ALU/processing
state

## Slide 5: Building up to our first architecture: ALU
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output: A op B

## Slide 6: A “single-cycle” design
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+
Clock
Key Idea:
Single-cycle design goes from reading an instruction out of memory all the way to writing results back to registers before the next clock edge.

## Slide 7: Where is the HW/SW Interface?
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
Branch: PC Source Select

## Slide 8: Big Idea: Instruction Bits are Control Signals
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Binary encoded: signals
directly interface to datapath
Reg 1
Reg 2
Reg 3
Reg 4
x

## Slide 9: Architecture vs. Microarchitecture
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA defines the architecture of the machine
A microarchitecture implements the features of the architecture

## Slide 10: Architecture vs. Microarchitecture
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 2
Reg 1
Reg 3
Reg 4
+
For a given architecture there are many perfectly good microarchitectural implementations
Architecture:
Register-register ALU ops, registers numbering 0-4
x
Microarchitecture:
One ALU containing an adder; multiply w/ iterated addition, physical register file with registers numbering 0-4
ALU
SRAM Bank #1 SRAM Bank #2
Register File
Microarchitecture:
Two SRAM banks storing regs based on parity
Architecture:
Sequentially-numbered, general-purpose registers

## Slide 11: ISA Design and Diving into RISCV-RV32I
What makes an ISA?
The basics of the RISCV-RV32I ISA
  A modern ISA engineered with clear goals from first principles
More microarchitectural concepts
  Control hazards & branch prediction
  Pipelining our microarchitecture & instruction-level parallelism

## Slide 12: What should go in the ISA?
Reduced Instruction Set Computer
Simple primitives:
Let software compose complex operations
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Complex Instruction Set Computer
Simple & complex operations:
Hardware provides complex functionality
Many operations:
Often several ways to do the same thing
Register and memory operands:
Operations may directly manipulate memory

## Slide 13: What should go in the ISA?
Reduced Instruction Set Computer
Simple primitives:
Let software compose complex operations
Complex Instruction Set Computer
Simple & complex operations:
Hardware must support complex functionality
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Register and memory operands:
Operations may directly manipulate memory
Many operations:
Often several ways to do the same thing
Many cases to map to control signals in microarchitecture
rd = M[imm] rd = M[reg]
rd = M[reg + imm] rd = M[PC + imm]
Plus all of these combinations
Few cases to map to control signals in microarchitecture

## Slide 14: What should go in the ISA?
Reduced Instruction Set Computer
Complex Instruction Set Computer
Simple primitives:
Let software compose complex operations
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Simple & complex operations:
Hardware must support complex functionality
Register and memory operands:
Operations may directly manipulate memory
Many operations:
Often several ways to do the same thing
What are the pros and cons of each?
How does RISC vs. CISC affect the microarchitecture,
compiler, program, programmer?

## Slide 15: Principles of ISA Design
General Principles
Regularity – “Law of least astonishment”
Orthogonality – keep separable concerns separate Composability – regular, orthogonal ops combine easily
Specific Principles
One vs. All – precisely one way to do it, or all ways should be possible
Primitives, not solutions – solve by coding, compiling, & synthesizing
“Blatant opinions” (matters of taste)
Addressing – not limited to simple arrays, etc.
Environment Support – exceptions, processes, debugging, etc
Deviations – deviate from these rules only in implementation-specific ways

## Slide 16: RISCV ISA
We will learn about ISA design by learning about RISCV
Modern, full-featured RISC ISA
Developed in the last decade at UC Berkeley
  The fifth in a sequence of RISC ISAs originating in the 80s
  https://riscv.org/technical/specifications/
  The RISC-V Instruction Set Manual, Volume I: BaseUser-Level ISA, Waterman et al, 2011
Goals
  Open-source
  Free
  Simple, but full-featured; avoids “over-architecting” for a particular uArch style (FPGA, ASIC,…)
  Extensible through extension specifications and variants
  Support heterogeneous & parallel systems efficiently
  Support 32- and 64-bit variants efficiently
  Fully virtualizable
  Supports (but does not require) IEEE 754 Floating Point

## Slide 17: RISCV Variants & extensions
L,B,J,T,P,V – Extra weird stuff (read the spec)
RV32I & RV64I are base integer ISA versions M – Support for HW Multiply & Divide Basic Operations
F – Support for single-precision Float D – Support for double-precision Float Q – Support for quad-precision Float Floating Point
A – Support for Atomic instructions RVWMO – Memory Consistency Model Concurrency

## Slide 18: RISCV Variants & extensions
RV32I & RV64I are base integer ISA versions
XLEN: how many bits in a register?
Memory: 2^XLEN bytes
Word: 4B, Doubleword: 8B, Halfword: 2B
Insn 1
Insn 2
Insn 3
Insn 4
…
32-bit instructions in base encoding

## Slide 19: RISCV-RV32I Specification
32 Registers x0-x31 + PC register
x0 is always zero
x1 is the return address (by convention)
x2 is the stack pointer (by convention)
x5 is used as an “alternate link” register (by convention)
  E.g., Implementing exceptions / long jumps in software
(Micro)architectural implications of this ISA choice?

## Slide 20: RISCV-RV32I Specification
32 Registers x0-x31 + PC register
x0 is always zero
x1 is the return address (by convention)
x2 is the stack pointer (by convention)
x5 is used as an “alternate link” register (by convention)
  E.g., Implementing exceptions / long jumps in software
(Micro)architectural implications of this ISA choice?
  Why not 16 registers? [RV32-E has 16 regs; why?]
  Why not 16-bit instructions?
  Power / Energy?
  Compilation & optimization?

## Slide 21: Exercise: What about variable insn/reg size?
What defines instruction size? Why? What defines register size? Why?
Can we support multiple instruction sizes? Why would we support multiple sizes?
How to support different sizes? Benefits & drawbacks?

## Slide 22: Exercise: What about variable insn/reg size?
What defines instruction size? Why? What defines register size? Why?
  ISA defines insn size. Lacking extensions, RV32I & RV64I both 32-bit insn
  ISA variant defines reg size. Programmer must know, datapath must implement; must be ISA-level spec.
Can we support multiple instruction sizes? Why would we support multiple sizes?
  Can we? Yes. Why? Code size optimization, longer constant immediates, longer jumps
How to support different sizes? Benefits & drawbacks?
  Two options. Option 1: RVC (riscv-compressed) – 16-bit ops blowup at decode into 32bit ones.
Code size optimization. Longer jumps possible.
  Option 2: steal some ISA bits to indicate variable width: 11 for 32, 011111 for 48, 0111111 for 64
  Costs? Increased decode complexity. Need to figure out how big instruction word is and where important signals are in the instruction word based on size.

## Slide 23: RISCV-RV32I Specification
Four base instruction encoding formats
  R(egister), I(mmediate), S(tore), U(pper Immediate)
  Mnemonics are non-binding and formats get flexibly used

## Slide 24: RISCV-RV32I Specification
Four base instruction encoding formats
  R(egister), I(mmediate), S(tore), U(pper Immediate)
  Mnemonics are non-binding and formats get flexibly used
R-Type: 2 register input operands, 1 register output operand, opcode type, and function selection bits

## Slide 25: RISCV-RV32I Specification
Four base instruction encoding formats
  R(egister), I(mmediate), S(tore), U(pper Immediate)
  Mnemonics are non-binding and formats get flexibly used
I-Type: 1 register input operands, 1 immediate input operand, 1 register output operand,
opcode type, and function selection bits

## Slide 26: RISCV-RV32I Specification
Four base instruction encoding formats
  R(egister), I(mmediate), S(tore), U(pper Immediate)
  Mnemonics are non-binding and formats get flexibly used
S-Type: 2 register input operands, 1 immediate input operand, [0 output operands], Opcode type, and function selection bits

## Slide 27: RISCV-RV32I Specification
Four base instruction encoding formats
  R(egister), I(mmediate), S(tore), U(pper immediate)
  Mnemonics are non-binding and formats get flexibly used
U-Type: 1 immediate input operand, 1 register output operand, opcode selection bits

## Slide 28: Example: R-type Arithmetic Operations
0000000 | 00101 | 00110 | 000 | 00111 | 0110011
OP
https://metalcode.eu/2019-12-06-rv32i.html

## Slide 29: Example: R-type Arithmetic Operations
0000000 | 00101 | 00110 | 000 | 00111 | 0110011
x7 = x5 + x6
OP
ADD reg x7
reg x6
reg x5
Func 7 = 0
https://metalcode.eu/2019-12-06-rv32i.html

## Slide 30: Example: R-type Arithmetic Operations
0100000 | 00101 | 00110 | 000 | 00111 | 0110011
x7 = x5 - x6
OP
SUB reg x7
reg x6
reg x5
Func 7 = 32
https://metalcode.eu/2019-12-06-rv32i.html

## Slide 31: Example: R-type Arithmetic Operations
0000000 | 00101 | 00110 | 110 | 00111 | 0110011
x7 = x5 | x6
OP
OR reg x7
reg x6
reg x5
Func 7 = 0
https://metalcode.eu/2019-12-06-rv32i.html

## Slide 32: Example: I-type Reg/Imm Arithmetic Operations
0000 0000 1001 | 00110 | 010 | 00111 | 0100011
x7 = x5 << 9
OP-IMM
reg x7
SLTI
reg x6
Func 7 = 0

## Slide 33: Example: S-type Store Operations
0100000 | 00101 | 00110 | 010 | 00111 | 0100011
M[x6 + offset] = x5 (4-bytes stored)
STORE
imm[4:0]
word
reg x6
reg x5
imm[11:5]
value
addr base
Base + offset: Why? Seem familiar?
width
offset
offset

## Slide 34: Example: S-type Store Operations
0100000 | 00101 | 00110 | 001 | 00111 | 0100011
M[x6 + offset] = x5 (2-bytes stored)
STORE
width imm[4:0]
half- word
reg x6
reg x5
imm[11:5]
value
addr base
Base + offset: Why? Seem familiar?
offset
offset

## Slide 35: What type are Load instructions?
What information do we need to encode for a load instruction?

## Slide 36: Load operations are I-Type Instructions

## Slide 37: Example: U-type Upper Immediate Operations
0000 0000 1000 1111 1111 | 00111 | 0110111
x7 = (2303 << 12)
LUI (Load Upper Immediate)
reg x7
20-bit Upper Immediate
What in the world is this instruction type used for?
= 2303

## Slide 38: Example: U-type Upper Immediate Operations
0000 0000 1000 1111 1111 | 00111 | 0010111
x7 = PC + (2303 << 12)
AUIPC (Add Upper Imm to PC)
reg x7
20-bit Upper Immediate
Why bring the PC into the picture?
= 2303

## Slide 39: Control Flow: Jump-and-link
0000 0000 100 | 00111 | 000 | 01000 | 1100111
x8=PC+4;
jump to ((base+offset) & 0xfffffffe)
Jump & Link (Register)
reg x7
Immediate
reg x8
Save PC+4
base
offset

## Slide 40: Control Flow: Call Jump-and-link
0000 0000 100 | 00111 | 000 | 01000 | 1100111
x8=PC+4;
jump to ((base+offset) & 0xfffffffe)
Jump & Link (Register)
reg x7
Immediate
reg x8
Save PC+4
base
offset
Why the mask?

## Slide 41: Control Flow: Compare & Branch
0 000000 | 00111 | 01000 | 101 | 1000 0 | 1100011
If(x8 >= x7) PC=PC + 16
Branch
reg x7
Imm[12,10:5]
reg x8 BGE
Where is bit 0?
Imm[4:1,11]
Imm: PC-relative branch target

## Slide 42: Design Goals Behind Instruction Encoding
Why are all of the immediate bits all over the place?
Why are the immediates apparently different sizes?
Why are some immediate bits left unspecified?

## Slide 43: Design Goals Behind Instruction Encoding
Why are all of the immediate bits all over the place?

## Slide 44: Design Goals Behind Instruction Encoding
Why are all of the immediate bits all over the place?
  Instruction decode is expensive & always performance critical
  Registers always in same place makes decoder simpler

## Slide 45: Fixed register position, simple decode logic
Instruction
Decode
Instruction
Fetch
000001 01010 00011 000 00010 00000001

## Slide 46: Fixed register position, simple decode logic
Instruction
Decode
Instruction
Fetch
000001 00100 01111 000 01000 00000001

## Slide 47: Design Goals Behind Instruction Encoding
Why are the immediates apparently different sizes?
12 bits
12 bits
32* bits

## Slide 48: Design Goals Behind Instruction Encoding
Why are the immediates apparently different sizes?
  Different immediates have different uses!
  E.g., 12-bits are enough for PC-relative jump targets
12 bits
12 bits
32* bits

## Slide 49: Design Goals Behind Instruction Encoding
Why are some immediate bits left unspecified?

## Slide 50: Design Goals Behind Instruction Encoding
Why are some immediate bits left unspecified?
  To make large (like, 32-bit) values in a 32-bit insn., need to leave stuff out
  E.g., LUI: store high order bits of a large constant into a register

## Slide 51: Implications of Control Flow Design
Benefits & limitations of PC-relative offsets?

## Slide 52: Implications of Control Flow Design
Benefits & limitations of PC-relative offsets?
  Compact encoding
  Easy to support position independent code (PIC) if all jumps PC-relative
  Limited reach for jump targets

## Slide 53: Implications of Control Flow Design
Benefits of combined compare & branch?

## Slide 54: Implications of Control Flow Design
Benefits of combined compare & branch?
  No management of implicit (& explicit) condition codes like x86, ARM, SPARC…
  Higher code density, reduced instruction fetch traffic,
  Execution reaches branch sooner in instruction stream allowing earlier prediction

## Slide 55: Other Design Dissiderata
Differences from x86 (for better and for worse)
  No complex addressing modes
  No conditional move (like x86 cmov) or predicated execution
  Much smaller basic ISA implementation (http://ref.x86asm.net/coder.html)
Memory Model Considerations (more on this toward end of semester)
  Alignment Issues: “The base ISA supports misaligned accesses, but these might run extremely slowly depending on the implementation. Furthermore, naturally aligned loads and stores are guaranteed to execute atomically, whereas misaligned loads and stores might not, and hence require additional synchronization to ensure
atomicity.”
  Memory Consistency Model: “We chose a relaxed memory model to allow high performance from simple machine implementations, however a completely relaxed memory model is too weak to support programming language memory models and so the memory model is being tightened.” [this point is basically the riscv team apologizing for having punted on concurrency to begin with and walking back to something that makes sense]

## Slide 56: What kind of ISA are we studying?
Maintain State (sequential logic)
Process (combinational logic)
control
ALU/processing
state

## Slide 57: RISCV is a “Register / Register” ISA
control
ALU/processing
state – inputs & outputs are in register file
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output:
A op B
Reg 1
Reg 2
Reg 3
Reg 4
Register File

## Slide 58: RISCV is a “Register / Register” ISA
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output
Register
Control
Input A Register Control
Input B Register Control
Memory
Unit
ld: data
Data Memory
st: data
ld/st: address
state – inputs & outputs are in register file Register / Register? we have memory tho?

## Slide 59: Alternative: “Register / Memory” ISA
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output
Register
Control
Input A Register Control
Input B Register Control
Memory
Unit
ld: data
Data Memory
st: data
ld/st: address
state – inputs & outputs are in register file Register / Register? we hhaavvee mmeemmoorryy tho?
Zero or one inputs comes from memory in a R/M architecture
Example Register / Memory architectures?

## Slide 60: Alternative: Stack Machine Architecture
control
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output: A op B
stored at stack top
Implicit arguments A & B come from top two stack positions
Stack
(Access memory via
ld/st to stack top)
state – in/out operands from stack only. there are no registers in this architecture!

## Slide 61: Alternative: Stack Machine Architecture
control
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output: A op B
stored at stack top
Stack
Implicit arguments A & B come from top two stack positions
state – in/out operands from stack only. there are no registers in this architecture!
Memory is weird: push <addr> loads
<addr> and pushes to stack top, pop
<addr> stores stack top to <addr>
push (0xabc) push (0xac0) addw
push (0x123)
push $10 //imm. 10 mulw
addw
pop (0xdeadbeef)
What does this do?

## Slide 62: Alternative: Stack Machine Architecture The Z4 digital computer (1942 + later)
control
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output: A op B
stored at stack top
Stack
Implicit arguments A & B come from top two stack positions
state – in/out operands from stack only. there are no registers in this architecture!
Memory is weird: push <addr> loads
<addr> and pushes to stack top, pop
<addr> stores stack top to <addr>
push (0xabc) push (0xac0) addw
push (0x123)
push $10 //imm. 10 mulw
addw
pop (0xdeadbeef)
What does this do?

## Slide 63: Alternative: Stack Machine Architecture The Java Virtual Machine is a stack machine
state – in/out operands from stack only. there are no registers in this architecture!
Memory is weird: push <addr> loads
<addr> and pushes to stack top, pop
<addr> stores stack top to <addr>
push (0xabc) push (0xac0) addw
push (0x123)
push $10 //imm. 10 mulw
addw
pop (0xdeadbeef)
What does this do?

## Slide 64: Alternative: Accumulator Machine Architecture
control
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B: imm. or mem.
Output: A op B
stored in A
Accumulator
Implicit argument A always comes from accumulator
state – no registers, implicit argument is A (the accumulator), other arg is imm. / mem.
Memory is less weird: load (0xabc) puts the contents of 0xabc in A, store (0xabc) puts A into memory at 0xabc
load (0xabc) add (0xac0) store (0xf00) load (0x123) mul 10
add (0xf00)
store (0xdeadbeef)
What does this do?

## Slide 65: IBM 701 (ca. 1952)
control
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B: imm. or mem.
Output: A op B
stored in A
Accumulator
Implicit argument A always comes from accumulator
state – no registers,
implicit argument is A
(the accumulator), other
arg is imm. / mem.
Memory is less weird: load (0xabc) puts the contents of 0xabc in A, store (0xabc) puts A into memory at 0xabc
load (0xabc) add (0xac0) store (0xf00) load (0x123) mul 10
add (0xf00)
store (0xdeadbeef)
What does this do?

## Slide 66: What did we just learn?
A deep-ish dive into the RISCV ISA as a vehicle for learning about ISA design
A look at how ISA design choices influence other aspects of the
system’s design
How to we cross the hardware/software interface to go from software to hardware

## Slide 67: What to think about next?
More microarchitectural concepts (next time)
  Pipelining our microarchitecture & instruction-level parallelism
  Control hazards & branch prediction
Caches as a microarchitectural optimization (next next time)
  Implementation of cache hierarchies
  Cache design tradeoffs
Performance Evaluation (looking forward)
  Design spaces, Pareto Frontiers, and design space exploration