## Slide 1
Fall 2023
Lecture 19: Consistency and Coherency
Credit: Brandon Lucia

## Slide 2
“The memory consistency model of a shared-memory system specifies the order in which memory operations will appear to execute to the programmer. The memory consistency model affects the process of writing parallel programs and forms an integral part of the entire system, including the architecture, the compiler, and the programming language.”
Excerpt from “Recent Advances in Memory Consistency Models for Hardware Shared-Memory Systems”
Sarita Adve, et al, 1999

## Slide 3: Memory Consistency

## Slide 4: Memory Consistency Model
Informal Definition:
“Defines the value a read operation may read at each point during the execution”
“Defines the set of legal observable orders of memory operations during an execution”
“Defines which reorderings of memory operations are permitted”

## Slide 5: Coherence is Ordering
Wr X
Wr X
Coherence defines the set of legal orders of accesses to a single memory location
Wr X
Wr X
OR

## Slide 6: Consistency is Ordering
Wr X
Wr Y
Consistency defines the set of legal orders of accesses to multiple memory locations
Wr X
Wr Y
OR

## Slide 7: Sequential Consistency (SC) The simplest, most intuitive memory consistency model
Two Invariants to SC:
Invariant #1: Instructions are executed in program order
Invariant #2:
All processors agree on a total order of executed instructions

## Slide 8: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution

## Slide 9: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X

## Slide 10: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y

## Slide 11: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y

## Slide 12: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y Rd X

## Slide 13: The SC “Switch”
Wr X
Rd Y
Wr Y
Rd X
Rd X
Execution
Wr X Rd Y Wr Y Rd X Rd X

## Slide 14: Why is SC Important?
Wr X Rd Y Wr Y Rd X Rd X
Rd Y
Wr X
Rd X Rd X Wr Y
SC is the most complex model that we can ask
programmers to think about.
Intuitive (SC) Weird (not SC)
Wr X
Rd Y
Rd X
Wr Y Rd X
SC prohibits all reordering of instructions (Invariant 1)

## Slide 15: Real hardware does not enforce SC
https://developer.arm.com/documentation/den0024/a/Memory-Ordering
The ARMv8 Memory Model:

## Slide 16: Reordering #1: Write Buffers
CPU can read its write
buffer, but not others’
Coherent
Buffered writes eventually end up in coherent shared memory
CPU |  | 
 |  | Wri
M |  | 
CPU |  | 
 |  | Wri
M |  | 
te Buffer
te Buffer

## Slide 17: Reordering #1: Write Buffers
X=1
r1=Y
Y=1
r2=X
M
M |  | 
Program
Initially X == Y == 0
Is r1==r2==0
a valid result?

## Slide 18: Reordering #1: Write Buffers
X=1
r1=Y
Y=1
r2=X
M
M |  | 
Program Initially X == Y == 0
Is r1==r2==0
a valid result?
r1 == r2 == 0 is not SC, but it can happen with write buffers

## Slide 19: Reordering #1: Write Buffers
Execution
r1=Y
Program
Initially X == Y == 0
Y=1
r2=X
M |  | 
X=1 |  | 
M |  | 

## Slide 20: Reordering #1: Write Buffers
Execution
r1=Y
r2=X
Y=1 |  | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program
Initially X == Y == 0

## Slide 21: Reordering #1: Write Buffers
Execution
r1=Y
r2=X
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program
Initially X == Y == 0

## Slide 22: Reordering #1: Write Buffers
Program
Initially X == Y == 0
r2=X
Execution
Y= |  | 
 | 1 | 
M |  | 
r1=Y |  | 
X= |  | 
 | 1 | 
M |  | 

## Slide 23: Reordering #1: Write Buffers
Execution
r2=X |  | 
Y= |  | 
 | 1 | 
M |  | 
r1=Y |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 24: Reordering #1: Write Buffers
Execution
r1=Y [r1 <- 0]
r2=X |  | 
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program Initially X == Y == 0

## Slide 25: Reordering #1: Write Buffers
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
Y= |  | 
 | 1 | 
M |  | 
X= |  | 
 | 1 | 
M |  | 
Program
Initially X == Y == 0

## Slide 26: Reordering #1: Write Buffers
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
M
M |  | 
Program
Initially X == Y == 0
Y=1
X=1 (Not SC!)
WBs let reads finish before older writes

## Slide 27: Reordering #2: Write Combining
Coalescing Write Buffer
Program X,Z in same $ line
X=1 Y=1 Z=1
4 word cache line

## Slide 28: Reordering #2: Write Combining
Coalescing Write Buffer
X=1 |  |  |  | 
Program X,Z in same $ line
X=1 Y=1 Z=1

## Slide 29: Reordering #2: Write Combining
X=1 |  |  |  | 
 |  |  | Y=1 | 
Coalescing Write Buffer
Program X,Z in same $ line
X=1 Y=1 Z=1

## Slide 30: Reordering #2: Write Combining
Coalescing Write Buffer
X=1 |  |  |  | 
 |  |  | Y=1 | 
 | Z=1 |  |  | 
Program X,Z in same $ line
X=1 Y=1 Z=1

## Slide 31: Reordering #2: Write Combining
X=1 |  |  |  | 
 |  |  | Y=1 | 
 | Z=1 |  |  | 
Coalescing Write Buffer Coalescing Write Buffer
X=1 | Z=1 |  |  | 
 |  |  | Y=1 | 
Combining the write to X & Z saves bandwidth, but reorders Z=1 and Y=1

## Slide 32: Reordering #3: Interconnect
Execution
X=1
Y=1 r1=X [r1 <- 1] r2=Y [r2 <- 0]
r3=Y [r3 <- 1] r4=X [r4 <- 0]
Program
X=1 r1=X Y=1
r2=Y
r3=Y
r4=X
X=1
Y=1
Y=1
X=1
Variable time cost traversing routed on-chip network

## Slide 33: Reordering #4: Compilers
X = 0
for (1 .. 100)
X = 1
print X
X = 0
X = 1
for (1 .. 100)
print X
X = 0
Hoisted!
The compiler hoists the write out of the loop,
permitting new (non-SC) results (e.g., “1 0 0 0 0 0 0...”)

## Slide 34: When is an Execution Not SC? When a memory operation happens before itself
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1
Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph

## Slide 35: When is an Execution Not SC? When a memory operation happens before itself
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1
Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
Program Order HB Edge

## Slide 36: When is an Execution Not SC? When a memory operation happens before itself
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1 Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
Program Order HB Edge Causal Order HB Edge

## Slide 37: When is an Execution Not SC? When a memory operation happens before itself
Execution
r1=Y [r1 <- 0] r2=X [r2 <- 0]
X=1
Y=1
X=1
r1=Y
Y=1
r2=X
Happens-Before Graph
If there is a cycle in the happens-before graph, the execution is not SC

## Slide 38: When is an Execution Not SC? When a memory operation happens before itself
X=1
Happens-Before Graph
Y=1 r1=X r3=Y
r2=Y r4=X
If there is a cycle in the happens-before graph, the execution is not SC
Execution
X=1 Y=1
r1=X [r1 <- 1]
r2=Y [r2 <- 0] r3=Y [r3 <- 1] r4=X [r4 <- 0]

## Slide 39: Two Design Constraints at Odds
SC is how programmers think, but restricts all reordering
Reordering allows optimization, but leads to unintuitive non-SC behavior.

## Slide 40
Relaxed Memory Consistency
Relaxed Memory Models permit reorderings, unlike SC

## Slide 41: x86-TSO (intel x86s) “The Write Buffer Memory Model”
r1=Y X=1
r1=Y
Total Store Order - loads may complete before older stores to different locations complete.
Relaxes W->R order

## Slide 42: PSO(SPARC) “The Write Combining Memory Model”
X=1 Z=1 Y=1 Z=1
Partial Store Order - loads and stores may complete before older stores to different locations complete.
Relaxes W->W order

## Slide 43: In General
X=1 Z=1 Y=1 Z=1
r1=Y X=1
r1=Y
W->R W->W
r1=Y r2=X
Y=1
r2=X
r1=Y Y=1
R->R R->W
Starting with PSO and relaxing R->R and R->W yields Weak Ordering or Release Consistency (alpha)
Depending on the implementation

## Slide 44: Implementing Synchronization for Weak Memory Models
What does synchronization have to do to prevent SC violations?
  Flush WB, prevent coalescing/bypassing, impose ordering in network, prevent compiler reorderings
What does synchronization have to do to prevent other kinds of problems?
  Enforce mutually exclusive execution by different threads of critical region, force threads to wait at barriers, enforce wait/notify discipline

## Slide 45: SC and Relaxed Consistency
SC is required for correctness and programmer sanity
+
Reordering is required* for performance
Goal: Ensure SC executions while permitting Relaxed Consistency reorderings
*Usually; MIPS memory model is SC

## Slide 46: Memory Models across the System Stack
Language
Compiler
Architecture
Java/C++: SC for data-race- free programs
Conservative with reordering when d-r-f can’t be proved
Usually very weak for max optimization (lots of reordering)
Note: fences from
“above” ensure SC

## Slide 47: What did we just learn?
Coherence and consistency are both memory ordering principles
Understanding the memory model is compelling to understanding the execution and correctness of the program