## Slide 1
Fall 2023
Lecture 3: Computer Architecture Basics
Credit: Brandon Lucia

## Slide 2: What did we talk about last time?
Hardware vs. software tradeoffs
von Neumann vs. Harvard architecture and the beginnings of a design space
An optimization exercise by example
Amdahl’s Law (and Gustafson’s Law, by contrast)

## Slide 3: Hardware/software boundary

## Slide 4: Our first hw/sw interface: The Von Neumann Computing Model
Program
Data
Unified Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
John von Neumann’s Big Idea:
Programs are data.

## Slide 5: Optimizing our Harvard Architecture
Program
Data
Instruction Bus
(32-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1:
x
=
y
+
z
I2: a = b * c
I3: r = s + t
32bits
64bits
With a one word (8 byte) bus:
1 data write cycle simultaneous with 1 data read cycles simultaneous with 1 instruction read cycle
per arithmetic operation
1 cycle per instruction!

## Slide 6: How about changing the code?
Program
Data
Instruction Bus
(128-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1:
I2:
I3:
I4:
if (x==0) a = b * 2 y = z + w q = n + m
Restructure code, increase likelihood to execute
Avoid needless fetch of non-executing code
Q: What if x is most often non-zero?
I5: //else
I6: a = b * 4 I7: y = z + w I8: q = n + m
Compiler!
I1:
I2:
I3:
I4:
I5:
I6:
I7:
I8:
y = z + w q = n + m if (x==0) a = b * 2
//else
a = b * 4
//other
//stuff

## Slide 7: Amdahl’s Law
100% of execution time
45% - Memory Accesses 20% - Control Flow 17.5% - Integer 12.5% - Fetch
5% - Floating
Point
Amdahl’s Law:
optimized time = [ 1-p x time / 1.0 ] + [ p x time / speedup ] Or equivalently:
speedup = 1 / [ (1 – p) / 1.0 + p / speedup ]

## Slide 8: Amdahl’s Law Speedup
optimizable
part (p)
Optimized speedup for optimizable part
>100x
optimized part speedup?
80%
optimizable? max speedup 5x!

## Slide 9: Another view of the world: Gustaffson’s Law
100% of execution energy
Memory Accesses
Control Flow
Integer
Fetch
Floating Point
Idea: find an optimizable part of your system and make it bigger If we know that memory is optimizable, why not optimize more and do more memory accesses?

## Slide 10: Another view of the world: Gustafson’s Law
Gustafson’s Law: Sequential part does not grow as optimizable part grows. Can always add more optimizable part and make sequential part matter less
Assume that we can scale up # of parallel mem operations, N
Assume that we can scale input to use all N parallel memops
data_size = 10 data[data_size] = {…} if(…){ }
…//18 more of these conditionals if(…){ }
for d in 0..data_size{ d++ }
data_size = 100000 data[data_size] = {…} if(…){ }
…//18 more of these conditionals if(…){ }
#parallel[N=1000]
for d in 0..data_size{ d++ }
Gustaffson!

## Slide 11: Another view of the world: Gustafson’s Law
85% - Memory Accesses
Gustafson’s Law for overall speedup with speedup factor of N:
(assume) Optimized time = T = 1
Unoptimized time = T’ = (1-p)T + pT*N = (1-p) + pN
Scaled Speedup = T’ / T = (1-p) + pN

## Slide 12: Another view of the world: Gustafson’s Law
85% - Memory Accesses
Gustafson’s Law for overall speedup with speedup factor of N:
(assume) Optimized time = T = 1
Unoptimized time = T’ = (1-p)T + pT*N = (1-p) + pN Scaled Speedup = T’ / T = (1-p) + pN
Scale parallel memory accesses, N, up to 1000? Scaled Speedup = 1-p + 1000p = 999p + 1 Scaled Speedup = 999 * 0.85 + 1 = 850x

## Slide 13: What is a Computer Architecture?
Building up to our first architecture
Defining the ISA: Architecture vs. Microarchitecture
RISC vs. CISC ISAs
RISCV ISA

## Slide 14: Our CPU from last time is incomplete
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
What’s missing?

## Slide 15: Basic Architecture: State + processing elements
Maintain State (sequential logic)
Process (combinational logic)
control
ALU/processing
state

## Slide 16: Building up to our first architecture: ALU
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output: A op B

## Slide 17: Building up to our first architecture: ALU
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output: A op B
Design choice – what operations do we support here?

## Slide 18: Basic Architecture: State + processing elements
Maintain State (sequential logic)
control
ALU/processing
state
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output:
A op B

## Slide 19: Basic Architecture: State + processing elements
control
ALU/processing
state
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output:
A op B
Reg 1
Reg 2
Reg 3
Reg 4
Register File

## Slide 20: Building up to our first architecture: ALU + Registers
Opcode select
op = [+, -, x, /]
Output register select
Input A register select Input B register select
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A
Register
Control
Input B Register Control

## Slide 21: Building up to our first architecture: ALU + Registers
Opcode select
op = [+, -, x, /]
Output register select
Input A register select Input B register select
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A
Register
Control
Input B Register Control
Stateful Elements plus control required to access them, providing inputs to operations and storing outputs of operations

## Slide 22: Building up to our first architecture: ALU + Registers
Opcode select
op = [+, -, x, /]
Output register select
Input A register select Input B register select
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A
Register
Control
Input B Register Control
Design choice – how many stateful elements / registers do we support?
Need to activate control logic to select right register for a particular operation. How?
Registers are named & explicit. Implication of explicit names?

## Slide 23: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Instruction gets decoded into signals that control the other parts of the system (more on encoding / decoding in a few slides)

## Slide 24: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Instruction memory holds all of the bits of all of the instructions that we might ever use to control other units.
Design choice: Need to think about where we put this memory (and its hierarchy of caches)

## Slide 25: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Instruction fetch logic refers to PC, loads instruction from instruction memory and sends to decode.
Design choices: how much to fetch at once?
What to fetch next (not always obvious)?

## Slide 26: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Remember our fetch optimization from last time? That would go here. Specialized instruction memory access logic. (Physical memory may be the same, though)

## Slide 27: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Sequential Control:
Each cycle, update the PC by adding 4.
Implication for software of our current design?

## Slide 28: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Decoding a fetched operation breaks it from a blob of bits into a set of signals that we can use to configure the rest of the units in this diagram
Key Idea: What we encode here has implications for other units and software layers above the instruction definition level.
Mechanism of decoding and content of encoded/decoded instructions are orthogonal concepts. How? vs what?.

## Slide 29: Building up to our first architecture: Memory
Reg 1
Reg 2
Reg 3
Reg 4
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory
Unit
Op select
op = [ld,st]
Data
Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register Control
Input B Register Control
Memory Unit
ld: data
Data Memory
st: data
ld/st: address

## Slide 30: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Decoded instruction now needs to select: ALU op or Mem op?

## Slide 31: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Here: address assumed to come from register directly

## Slide 32: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Reality: ALU may crunch reg vals to generate address
Address mode bits from decoded instruction
Address bits from register

## Slide 33: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Design choice:
How many ways do we have to compute an address? How many ways should we have?
Guess at implications of more ways?
Address mode bits from decoded instruction
Address bits from register

## Slide 34: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
state

## Slide 35: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Are register files and memory two varieties of the same basic thing?

## Slide 36: Building up to our first architecture: Branching
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC Source Select
PC+4
+

## Slide 37: Building up to our first architecture: Branching
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
4
+
Input A Input B
Register Register
Control Control
In A reg select In B reg select
Register File
Input A Input B Reg 1
Output Reg 2
Op select Register
op = [+, -, x, /] ALU Control Reg 3
Out reg select ALU: output C Reg 4
Op select Memory ld: data st: data
op = [ld,st] Unit ld/st: address
Data Memory
Branch Target Address Offset
MUX
PC Source Select
PC+4
PC
If PC Source Select not asserted PC=PC+4
If PC Source Select asserted PC=PC+off
+
Program
Memory

## Slide 38: Building up to our first architecture: Branching
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC Source Select
PC+4
+
Where does our branch target offset originate?
Alternative design choices? How are each of those used in code?

## Slide 39: Building up to our first architecture: Branching
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC Source Select
PC+4
+
How do we decide taken vs. not
taken via PC Source Select?

## Slide 40: Building up to our first architecture: Branching
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
Branch: PC Source Select
Design Choice:
ALU output determines PC source select when branch condition evaluates Alternative Design?

## Slide 41: A Complete (but slightly messy) RISCV-ish Datapath
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+

## Slide 42: A “single-cycle” design
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+
Clock

## Slide 43: A “single-cycle” design
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+
Clock
Key Idea:
Single-cycle design goes from reading an instruction out of memory all the way to writing results back to registers before the next clock edge.

## Slide 44: Thinking about latency: ALU Operations
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Address mode bits from decoded instruction
Address bits from register
ALU Operation Latency:
Circuit delay of ALU operations is (mostly) low.
Why?
Program Counter(PC)
4
+
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+

## Slide 45: Thinking about latency: ALU Operations
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Address mode bits from decoded instruction
Address bits from register
ALU Operation Latency:
Circuit delay of ALU operations is (mostly) low.
Sum of delay of 5 or 6 units depending on impl.
Need to fetch, decode, register access (in 1), reg access (in 2), ALU function, register writeback
Program Counter(PC)
4
+
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+

## Slide 46: Thinking about latency: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Address mode bits from decoded instruction
Address bits from register
Memory Latency:
Memory accesses are pretty slow. Why?
Program Counter(PC)
4
+
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+

## Slide 47: Thinking about latency: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Address mode bits from decoded instruction
Address bits from register
Sum of delay of 7 or 8 units depending on counting Need to fetch, decode, register access (addr part 1), reg access (addr part 2), alu (addr gen), memory unit, memory bank, register write
Program Counter(PC)
4
+
Branch Target Address Offset
Memory Latency – Critical Path:
Memory accesses are pretty slow in our datapath.
MUX
Branch: PC Source Select
PC+4
+

## Slide 48: Implication of operation latencies?
Single-cycle design means that the cycle time for the system is
defined by the latency of the longest-latency operation
In our case, that would be the memory latency (and ALU latency has some slack from the cycle time)
If every operation is not a memory operation, then we have over- provisioned the cycle time of the system

## Slide 49: Where is the HW/SW Interface in the Datapath?
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
Branch: PC Source Select

## Slide 50: Where is the HW/SW Interface?
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
This is where software begins!
Branch: PC Source Select

## Slide 51: Instruction memory holds software
Instruction
Decode
Instruction
Fetch
???

## Slide 52: Big Idea: Instruction Bits are Control Signals
Instruction
Decode
Instruction
Fetch
Input Register 1
Input Register 2
Output Register
Operation Type
PC Source Select
Jump Target
…

## Slide 53: Big Idea: Instruction Bits are Control Signals
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00001000 | 00001001 | 00000001

## Slide 54: Big Idea: Instruction Bits are Control Signals
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Binary encoded: signals
directly interface to datapath
Reg 1
Reg 2
Reg 3
Reg 4
x

## Slide 55: Instruction Set Architecture
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Binary encoded: signals
directly interface to datapath
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA defines the architecture of the machine
Any implementation of the architecture must support the features exposed through the ISA (why?)

## Slide 56: Architecture vs. Microarchitecture
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA defines the architecture of the machine
A microarchitecture implements the features of the architecture

## Slide 57: Architecture vs. Microarchitecture
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA defines the architecture of the machine
A microarchitecture implements the features of the architecture
Architecture:
Register-register ALU ops, registers numbering 0-4
Microarchitecture:
One ALU containing a multiplier,
physical register file with registers numbering 0-3
ALU
x

## Slide 58: Architecture vs. Microarchitecture
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 1
Reg 2
Reg 3
Reg 4
+
For a given architecture there are many perfectly good microarchitectural implementations
Architecture:
Register-register ALU ops, registers numbering 0-4
x
Microarchitecture:
One ALU containing an adder; multiply w/ iterated addition, physical register file with registers numbering 0-3
ALU

## Slide 59: Architecture vs. Microarchitecture
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 2
Reg 1
Reg 3
Reg 4
+
For a given architecture there are many perfectly good microarchitectural implementations
Architecture:
Register-register ALU ops, registers numbering 0-4
x
Microarchitecture:
One ALU containing an adder; multiply w/ iterated addition, physical register file with registers numbering 0-3
ALU
SRAM Bank #1 SRAM Bank #2
Register File
Microarchitecture:
Two SRAM banks storing regs based on parity
Architecture:
Sequentially-numbered, general-purpose registers

## Slide 60: Instruction Set Architecture
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Binary encoded: signals
directly interface to datapath
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA is the vocabulary of the machine
The ISA/vocabulary determines the types of programs/sentences that it is possible to write

## Slide 61: What should go in the ISA?
Reduced Instruction Set Computer
Simple primitives:
Let software compose complex operations
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Complex Instruction Set Computer
Simple & complex operations:
Hardware provides complex functionality
Many operations:
Often several ways to do the same thing
Register and memory operands:
Operations may directly manipulate memory

## Slide 62: What should go in the ISA?
Reduced Instruction Set Computer
Simple primitives:
Let software compose complex operations
Complex Instruction Set Computer
Simple & complex operations:
Hardware must support complex functionality
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Register and memory operands:
Operations may directly manipulate memory
Many operations:
Often several ways to do the same thing
Many cases to map to control signals in microarchitecture
rd = M[imm] rd = M[reg]
rd = M[reg + imm] rd = M[PC + imm]
Plus all of these combinations
Few cases to map to control signals in microarchitecture

## Slide 63: What should go in the ISA?
Reduced Instruction Set Computer
Complex Instruction Set Computer
Simple primitives:
Let software compose complex operations
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Simple & complex operations:
Hardware must support complex functionality
Register and memory operands:
Operations may directly manipulate memory
Many operations:
Often several ways to do the same thing
What are the pros and cons of each?
How does RISC vs. CISC affect the microarchitecture,
compiler, program, programmer?

## Slide 64: Principles of ISA Design
General Principles
Regularity – “Law of least astonishment”
Orthogonality – keep separable concerns separate Composability – regular, orthogonal ops combine easily
Specific Principles
One vs. All – precisely one way to do it, or all ways should be possible
Primitives, not solutions – solve by coding, compiling, & synthesizing
“Blatant opinions” (matters of taste)
Addressing – not limited to simple arrays, etc.
Environment Support – exceptions, processes, debugging, etc
Deviations – deviate from these rules only in implementation-specific ways

## Slide 65: What did we just learn?
Computer architectures define the HW/SW interface through the ISA
There is a difference between architecture and microarchitecture
Many valid microarch. implementations of an architecture exist
RISC vs. CISC architectures are extrema on a spectrum
Principles of ISA design (Wulf)

## Slide 66: What to think about next?
The basics of the RISCV-RV32I ISA and some other hw/sw interfaces
More microarchitectural concepts
  Pipelining our microarchitecture & instruction-level parallelism
  Control hazards & branch prediction