## Slide 1
Fall 2023
Lecture 6: Control Hazards and Branch Prediction
Credit: Brandon Lucia

## Slide 2: Recap: Pipelined Datapath Microarchitecture
Understanding pipelining as a general microarchitectural optimization
Data hazards and their effect on the pipelined microarchitectural datapath
Forwarding as a mitigation for data hazards in a pipelined architecture

## Slide 3: A Simple Pipelined Processor Datapath
ALU
Input Read Reg A
ALU: output C data Memop: Effective Addr. Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read Register A & B Select
Input Read Reg B
Write Reg C Data
+
Instruction PC+4 Branch Target
Branch Target
Branch Target Offset
Instruction PC + 4
Branch Target
AAddddrr Reg A
Data Reg B
(Ld Only)
RReeaadd DDaattaa CC
Read Data C (Ld Only)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select [Ld/St]
Instruction Fetch
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back

## Slide 4: Types of Data Hazards
sub x6 x5 x4 lw x16 0xabc
Read-After-Write (RAW) Write-After-Read (WAR)
sub x8 x16 x4
add x12 x6 x14 lw
x16 0xabc
Write-After-Write (WAW)
Only Read-After-Write (RAW) hazards are possible in our simple pipeline
lw x6 0xabc
add x16 x6 x14 sub x6 x5 x4
add x12 x6 x14

## Slide 5: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14 reads the value of x6 sub x6 x5 x4
add x12 x6 x14 lw x16 0xabc
from
Read-After-Write (RAW) Hazard:
Input register does not contain updated data during register read cycle due to yet-to-be-completed register writeback from older instruction
x6 gets written back here 2 cycles later!

## Slide 6: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14

## Slide 7: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
add x12 x6 x14 sub x6 x5 x4

## Slide 8: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14
stall

## Slide 9: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14
stall
stall

## Slide 10: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
add x12 x6 x14
stall
stall

## Slide 11: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
stall
add x12 x6 x14

## Slide 12: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
add x12 x6 x14

## Slide 13: How do we avoid the stall cycles?
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14
stall
stall

## Slide 14: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14
Value of x6 is available after sub Executes
We can forward the value to the add!

## Slide 15: Forwarding to avoid a pipeline RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
Value of x6 is available from EX/MEM pipeline register!
add x12 x6 x14 sub x6 x5 x4
“x6”
We can forward the value in the EX/MEM pipeline register from the sub back to Execute to act as the input operand for the add

## Slide 16: Forwarding to avoid a pipeline RAW Hazard
Fetch
Decode
Execute Memory
Register Write-Back
Can also forward if there are intervening instructions
add x12 x6 x14 add x9 x8 x7 sub x6 x5 x4
“x6”
Can forward the value in the MEM/WB pipeline register from the sub back to Execute for the add (going around the unrelated operation now in the memory stage)

## Slide 17: Immediately preceding & dependent on load = stall
Fetch
Decode
Execute
Memory
Register Write-Back
lw x6 0xabc
add x12 x6 x14
lw x6 0xabc add x12 x6 x14
Value of x6 is available from Memory!
We can forward the value in Memory’s pipeline register
from the lw back to Execute’s input for the add
(Still requires stalling…)
stall

## Slide 18: Adding Forwarding Support
ALU
ALU: output C data Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read Register A & B Select
Input Read Reg B
Write Reg C Data
+
Instruction PC+4 Branch Target
PC Source Select (1 if branch taken)
Branch Target
Branch Target Offset
Instruction PC + 4
Read
Data C
Read Data C (Ld)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select
[Ld/St]
Instruction Fetch
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
Branch Target
Mem/WB to Exec Forward
Ex/Mem to Exec
Forward
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
Input Read Reg A
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B

## Slide 19: Exception Handling
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
invalid ins
sw x6 (x14)
sw x0 (x13)
Basic Exception Idea: Nuke everything that started after the current instruction, finish everything that started before the current instruction, jump to exception handler
Exception!

## Slide 20: Today: More Pipelined Microarchitecture
Quick recap of pipeline mechanics
Introduction to structural hazards
Introduction to control hazards on branches
Simple approaches to handling control hazards
Branch prediction for handling control hazards

## Slide 21: Pipeline Control Signals

## Slide 22: Control signals also pipelined through stages
ALU
Input Read Reg A
ALU: output C data
Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read
Registe
A & B Select
Input Read Reg B
Read Regs A & B Data Write Register C Select
Write Register C Data
Write Reg C Data ALU
Branch Target Offset
+
Instruction PC+4 Branch Target
Branch Target
I
P
r
O
o
nstruction C + 4
Branch Target
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
MemRead/ MemWrite
Instruction Fetch
Instr. Decode Execute
Memory
Register Write-Back
IF/
ID
ID/
EX
EX/ Mem
Mem
/WB Write Reg C Data
PC Source Select (1 if branch taken)
Wr Data
Write Reg C Data Mem

## Slide 23: Which pipeline control signals get set where?
Instruction Memory
Instruction Fetch
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
C
Si
R R A S
Read Regs A & B Data Write Register C Select
Write Register C Data
Write Reg C Data ALU
Branch
Instruction PC+4 Branch Target
Branch Target
I
P
r
O
o
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
Instruction Fetch
Instr. Decode Execute
Memory
Register Write-Back
IF/
ID
Target AAddddrr Data
Offset Branch Target RReegg AA Reg B ontrol nstruction + (Ld Only)
gnals C + 4
Cont. Memory
ead Sigs.: Unit RReeaadd
egiste Input Input Op. DaDattaa CC
ID/ EX/ Select
& B Read Read [Ld/St]
elect EX Reg A Reg B Mem Data
Memory
Control Signals:
p select ALU
p = [+, -, x, /]
ALU: output C data Branch: PC Source Select
Mem
/WB Write Reg C Data
PC Source Select (1 if branch taken)
Instruction Fetch:
Instruction memory read control always asserted
PC write enable always asserted
no special control signal pipelining here
Write Reg C Data Mem

## Slide 24: Which pipeline control signals get set where?
In Re Re
Instruction Memory
Instruction Fetch
Control Signal
p select
p = [+, -, x, /]
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read
Registe
A & B Select
Read Regs A & B Data Write Register C Select
Write Register C Data
Write Reg C Data ALU
Branch Target Offset
+
Instruction PC+4 Branch Target
Branch Target
I
P
r
O
o
nstruction C + 4
r
ack
utput/Read
g Select
Write Reg C Select
Instruction Fetch
Instr. Decode Execute
Memory
Register Write-Back
IF/
ID
ID/
EX
AAddddrr Data Output/Read O
Branch Target RReegg AA Reg B Reg C Data Re (Ld Only)
Cont. Memory Registe
Sigs.:
Op. Unit RReeaadd Writeb
put Input EX/ Select DaDattaa CC
ad Read [Ld/St] Mem
g A Reg B Mem Data /WB Write
Memory Reg C
s: Data
ALU
ALU: output C data Branch: PC Source Select
PC Source Select (1 if branch taken)
Instruction Decode ( / Register Read):
In RISCV, source registers always in same location in all
instruction formats.
No special control signal pipelining here either.
Write Reg C Data Mem

## Slide 25: Recall: R-type Arithmetic Operations
0100000 | 00101 | 00110 | 000 | 00111 | 0110011
x7 = x5 - x6
OP
SUB reg x7
reg x6
reg x5
Func 7 = 32
https://metalcode.eu/2019-12-06-rv32i.html

## Slide 26: Which pipeline control signals get set where?
ALU
Input Read Reg A
ALU: output C data
Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read
Registe
A & B Select
Read Regs A & B Data Write Register C Select
Write Register C Data
Write Reg C Data ALU
Branch Target Offset
+
Branch Target
I
P
r
Branch Target
Instruction Fetch
Instr. Decode Execute
Memory
Register Write-Back
IF/
ID
ID/
EX
EX/ Me
AAddddrr Data Output/Read Output/Read
RReegg AA Reg B Reg C Data Reg Select (Ld Only)
Cont. Memory Register
Sigs.:
Op. Unit RReeaadd Writeback
DaDattaa CC
Select
m [Ld/St] Mem
Data /WB Write Write
Memory Reg C Reg C
Data Select
Immed.
Input Read Reg B
ALU Src
Select
Sign Extend
Execute / Address Generation:
ALU Op Select: selects the ALU operation
ALU Src Select: (previously omitted, added here)
selects between read register B and a sign-extended
immediate extracted from the bits of the instruction
Instruction C + 4
PC Source Select (1 if branch taken)
Instruction PC+4 Branch Target
Write Reg C Data Mem

## Slide 27: Which pipeline control signals get set where? PC Source Select
a
Branch: PC Source Select
Instr Me
Instr Fetc
Memory
Unit
Data
Memory
4
+
PC
Write Reg C Data ALU
Branch
Instruction PC+4 Branch Target
I
P
r
O
o
AAddddrr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
EX/ Mem
Mem
/WB Write Reg C Data
d.
Target
Offset Branch Target
Branch Control nstruction + Imme
Target Signals C + 4
X PC Source Input Sign
Select Read Read Extend
IF/ Registe ID/ Input Reg B
uction A & B Read ALU Src
h ID Select EX Reg A Select
Control Signals:
Reg 1 p select ALU
uction Reg 2 p = [+, -, x, /]
mory Reg 3 ALU: output C dat
Memory ( / Branch Resolution):
MU PC Source Select: Set to 1 if instruction is a branch and
branch taken (e.g., if ALU output is 0)
MemRead: Use incoming address from Ex stage as a
read address
MemWrite: Use incoming address from Ex stage as a
write address
Wr Data
Write Reg C Data Mem
MemRead/ MemWrite

## Slide 28: Which pipeline control signals get set where? PC Source Select
RReeaadd DDaattaa CC
a
Branch: PC Source Select
Instr Me
Instr Fetc
Memory
Unit
Data
Memory
4
+
MU
PC
Write Reg C Data ALU
Branch
Instruction PC+4 Branch Target
I
P
r
O
o
AAddddrr
Write Reg C Data Mem
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
EX/ Mem
Mem
/WB Write Reg C Data
d.
Target
Offset Branch Target
Branch Control nstruction + Imme
Target Signals C + 4
X PC Source Input Sign
Select Read Read Extend
IF/ Registe ID/ Input Reg B
uction A & B Read ALU Src
h ID Select EX Reg A Select
Control Signals:
Reg 1 p select ALU
uction Reg 2 p = [+, -, x, /]
mory Reg 3 ALU: output C dat
Writeback:
MemOrALU: Select whether ALU result (from Ex) or
data from memory (from Mem) writes to register file
RegWrite: Enables register file write
Write Reg Select: Use instruction bits to choose write
register
Wr Data
MemRead/ MemWrite

## Slide 29: Which pipeline control signals get set where? PC Source Select
ALU: output C data Branch: PC Source Select
Instruction
Memory
Instruction Fetch
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Control
Signal
Read
Regist
A & B
Select
Write Reg C Data ALU
Branch Target Offset
+
Instruction PC+4 Branch Target
Branch Target
I
nstruction
Branch Target
AAddddrr
aadd ttaa CC
Write Reg C Data Mem
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
IF/
ID
Mem
/WB Write Reg C Data
Wr Data
Immed.
s PC + 4
Input Sign Memory
Read Extend Unit RRee er ID/ Input Reg B EX/ DaDa
Read
EX Reg A ALU Src Mem Data
Select
Memory
Control Signals:
Op select ALU MemRead/
op = [+, -, x, /] MemWrite
Takeaway point on pipeline control:
Need to route signals to a pipeline stage (from the
decoded instruction, or from an earlier stage)
and
need to have sufficient signals available to control
units in a pipeline stage.

## Slide 30: More on Pipeline Hazards Structural Hazards Control Hazards

## Slide 31: Structural Hazards
ALU: output C data Branch: PC Source Select
Instruction
Memory
Instruction Fetch
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Sourc
Select
Reg 3
Write Reg C Data ALU
Instruction PC+4 Branch Target
Branch Target
I
P
r
O
o
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
MemRead/ MemWrite
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
Branch
Target
Offset Branch Target
Control nstruction +
Signals C + 4
e
Read
IF/ Registe ID/ Input Input EX/
A & B Read Read
ID Select EX Reg A Reg B Mem
Control Signals:
Reg 1 p select ALU
Reg 2 p = [+, -, x, /]
Mem
/WB Write Reg C Data
PC Source Select (1 if branch taken)
Wr Data
Write Reg C Data Mem
Observation:
We have two memories, one for data, one for
instructions.

## Slide 32: Structural Hazards
ALU
Input Read Reg A
ALU: output C data
Branch: PC Source Select
Unified Memory 1 rd / 1wr
Instruction Fetch
Control Signals:
p select
p = [+, -, x, /]
Memory
Unit
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Control Signals
Read
Registe
A & B Select
Input Read Reg B
Write Reg C Data ALU
Branch Target Offset
+
Instruction PC+4 Branch Target
Branch Target
I
P
r
O
o
nstruction C + 4
Branch Target
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
IF/
ID
ID/
EX
EX/ Mem
Mem
/WB Write Reg C Data
PC Source Select (1 if branch taken)
Wr Data
Write Reg C Data Mem
What happens when we make
this small change?

## Slide 33: Structural Hazards
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
sw x6 (x14)
sub x6 x5 x4 sw x0 (x13)
Load occupies unified memory read port
Fetch is blocked with no access to read port
stall
No software or clever architectural mitigation. Need two memories or two memory ports.

## Slide 34: Control Hazards
beq | x16 | x12 PC+12
sub | x6 | x5 x4
add | x12 | x6 x14
add | x12 | x7 x9
Branch-induced Control Hazard

## Slide 35: Example: Pipelined Execution w/ Branch
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
Problem: What to fetch next?
beq x16 x12 PC+12
sub x6 x5 x4 add x12 x6 x14 add x12 x7 x9
?

## Slide 36: Example: Pipelined Execution w/ Branch Option #1: Stall on Branch
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
stall
stall
Proposal: We know the next PC only after beq finishes Ex (What signals do we need to determine next PC? )

## Slide 37: Determining the Next PC in the Pipeline
ALU
Input Read Reg A
ALU: output C data
Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Input Read Reg B
Read Regs A & B Data Write Register C Select
Write Register C Data
Write Reg C Data ALU
Instruction PC+4 Branch Target
Branch Target
I
P
O
o
Branch
Target
Offset Branch Target nstruction +
C + 4
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
MemRead/ MemWrite
Instruction Fetch
Instr. Decode Execute
Memory
Register Write-Back
IF/
ID
ID/
EX/ Mem
Mem
/WB Write Reg C Data
PC Source Select (1 if branch taken)
Wr Data
Write Reg C Data Mem
Control
Signals
Read
Register EX
A & B
Select

## Slide 38: Example: Pipelined Execution w/ Branch Option #1: Stall on Branch
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
stall
stall
2 pipeline bubbles per branch!
sub x6 x5 x4

## Slide 39: Example: Pipelined Execution w/ Branch Option #1: Stall on Branch
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
stall
stall
2 pipeline bubbles per branch!
Can we do better than 2 bubbles?
sub x6 x5 x4

## Slide 40: Proposal: Resolve the branch target and branch taken/not taken outcome earlier than beq in Mem.
Early Branch Resolution
ALU
Input Read Reg A
ALU: output C data
Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Input Read Reg B
Read Regs A & B Data Write Register C Select
Write Register C Data
Write Reg C Data ALU
Instruction PC+4 Branch Target
Branch Target
I
P
O
o
Branch
Target
Offset Branch Target nstruction +
C + 4
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
MemRead/ MemWrite
Instruction Fetch
Instr. Decode Execute
Memory
Register Write-Back
IF/
ID
ID/
EX/ Mem
Mem
/WB Write Reg C Data
PC Source Select (1 if branch taken)
Wr Data
Write Reg C Data Mem
Control
Signals
Read
Register EX
A & B
Select

## Slide 41: Early Branch Resolution
ALU
Input
Read Reg A
ALU: output C data
Instruction Memory
Instruction Fetch
Control Signals:
O
o
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Input
Read
Reg B
Write Reg C Data ALU
Instruction PC+4
Branch Target
Branch Target
Branch
Target Offset
Instruction +
PC + 4
Branch
Target
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
MemRead/ MemWrite
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
IF/
ID
ID/
EX/ Mem
Mem
/WB Write Reg C Data
Wr Data
Control
Signals
Read
Register EX
A & B
Select
PC Source Select (1 if branch taken)
Key Idea: Move Branch Target logic to ID and add forwarding path for PC Source
Select from Ex for IF to use in same cycle.
Write Reg C Data Mem
Fairly aggressive optimization in MIPS: resolve branch in EX in first half of cycle, use PC Src Select in second half of cycle in IF to fetch the correct instruction. Could limit clock frequency…

## Slide 42: Example: Pipelined Execution w/ Early Resolution
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
Problem: What to fetch next?
beq | x16 | x12 PC+12
sub | x6 | x5 x4
add | x12 | x6 x14
add | x12 | x7 x9
?

## Slide 43: Example: Pipelined Execution w/ Early Resolution
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
stall
We know the next PC when beq is in Ex

## Slide 44: Example: Pipelined Execution w/ Early Resolution
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
stall
1 pipeline bubble per branch!
sub x6 x5 x4

## Slide 45: Example: Pipelined Execution w/ Early Resolution
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
stall
Can we do even better than 1 stall per branch?
sub x6 x5 x4

## Slide 46: MIPS-style Delayed Branch Execution
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
stall
Branch takes an extra cycle to resolve, so how about just fetching some instruction in the “delay slot”?
sub x6 x5 x4
Branch Delay Slot

## Slide 47: Filling Branch Delay Slots
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
Only useful if branch ends up resolving not-taken Otherwise, need to erase the effects of the sub when branch finally resolves
Branch Delay Slot filled w/ not-taken instruction
sub x6 x5 x4
beq x16 x12 PC+12 sub x6 x5 x4
add x12 x6 x14 add x12 x7 x9

## Slide 48: Filling Branch Delay Slots
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
Branch Delay Slot filled w/ taken instruction
add x12 x7 x9
beq x16 x12 PC+12 sub x6 x5 x4
add x12 x6 x14 add x12 x7 x9
Only useful if branch ends up resolving taken Otherwise, need to erase the effects of the add when branch finally resolves

## Slide 49: Filling Branch Delay Slots
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
Why is it OK for the compiler to reorder the mul and the beq in this instance?
Branch Delay Slot filled w/ other independent insn
mul x8 x15 x1
mul x8 x15 x1 beq x16 x12 PC+12 sub x6 x5 x4
add x12 x6 x14
beq x16 x12 PC+12 mul x8 x15 x1 sub x6 x5 x4
add x12 x6 x14
add x12 x7 x9 add x12 x7 x9
Compiler reorders code to fill slot

## Slide 50: Filling Branch Delay Slots
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
Why is it OK for the compiler to reorder the mul and the beq in this instance?
Data-independent and control-equivalent
We will come back to compiler reordering in a few lectures
Compiler knows about branch delay slot (it is architectural)
Branch Delay Slot filled w/ other independent insn
mul x8 x15 x1
mul x8 x15 x1 beq x16 x12 PC+12 sub x6 x5 x4
add x12 x6 x14
add x12 x7 x9
mul x8 x15 x1 sub x6 x5 x4 add x12 x6 x14 add x12 x7 x9
Compiler reorders code to fill slot
beq x16 x12 PC+12

## Slide 51: Filling Branch Delay Slots
Fetch
Decode
Execute
Memory
Register Write-Back
beq | x16 | x12 PC+12
nop |  | 
sub | x6 | x5 x4
add | x12 | x6 x14
add beq x16 x12 PC+12 | x12 | x7 x9
Not really sure what to put in the delay slot. Cannot (or do not want to) slot in taken/not-taken conditional next instructions… No data-independent, control-equivalent ops to put in slot
Branch Delay Slot
filled w/ nop
nop

## Slide 52: RISCV does not have/allow/require delay slots
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
stall
sub x6 x5 x4
Branch Delay Slot
From the RISCV RV32I Spec: “Control transfer instructions in RV32I do not have architecturally visible delay slots.”
What is “architecturally visible”?
Why do they ban delayed branches at the ISA level?

## Slide 53: Why do they ban delayed branches at the ISA level?
“For their first microprocessor with a 5-stage pipeline, this indecision could have caused a one clock-cycle stall of the pipeline. MIPS-32 solved this problem by redefining branch to occur in the instruction after the next one. Thus, the following instruction is always executed. The job of the programmer or compiler writer was to put something useful into the delay slot. Alas, this “solution” didn’t help later MIPS-32 processors with many more pipeline stages (hence many more instructions fetched before the branch outcome is computed), but it made life harder for MIPS-32 programmers, compiler writers, and processor designers ever after, since incremental ISAs demand backwards compatibility (see Section 1.2). In addition, it makes the MIPS-32 code much harder to understand (see Figure 2.10 on page 29 ). While architects shouldn’t put features that help just one implementation at a point in time, they also shouldn’t put in features that hinder some implementations.”
The RISC-V Reader: An Open Architecture Atlas [Beta edition, 0.0.1] 099924910X, 9780999249109
https://dokumen.pub/the-risc-v-reader-an-open-architecture-atlas-beta-edition-001-099924910x-9780999249109.html

## Slide 54: Branch Prediction to avoid control hazards
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
Fetch the best guess if we know which way is most likely
beq | x16 | x12 PC+12
sub | x6 | x5 x4
add | x12 | x6 x14
add | x12 | x7 x9
?

## Slide 55: Branch Prediction to avoid control hazards
Fetch
Decode
Execute
Memory
Register Write-Back
beq x16 x12 PC+12
Fetch the best guess if we know which way is most likely
beq | x16 | x12 PC+12
sub | x6 | x5 x4
add | x12 | x6 x14
add | x12 | x7 x9
?
How to guess about which way
a branch is most likely to resolve?

## Slide 56: There is “typical” branch behavior
beq x16 x12 PC+12 sub x6 x5 x4
add x12 x6 x14
add x12 x7 x9
sub x6 x5 x4 add x12 x6 x14 add x12 x7 x9
beq x16 x12 PC-12
What will these programs tend to do?

## Slide 57: There is “typical” branch behavior
beq x16 x12 PC+12 sub x6 x5 x4
add x12 x6 x14
add x12 x7 x9
sub x6 x5 x4 add x12 x6 x14 add x12 x7 x9
beq x16 x12 PC-12
Forward and backward branches have different characteristics
2/3 of all branches are taken in general
Backward branch: 80% taken
Most branch instructions jump forward

## Slide 58: Statically defined hints about branches?
beq.t90 x16 x12 PC+12 sub x6 x5 x4
add x12 x6 x14
add x12 x7 x9
From the RISCV RV32I Spec:
“We considered but did not include static branch hints in the instruction encoding. These can reduce the pressure on dynamic predictors, but require more instruction encoding space and software profiling for best results, and can result in poor performance if
production runs do not match profiling runs.”
sub x6 x5 x4 add x12 x6 x14 add x12 x7 x9
beq.nt90 x16 x12 PC-12
From the Intel's manual:
"Branch hint prefixes (2EH, 3EH) allow a program to give a hint to the processor about the most likely code path for a branch. Use these prefixes only with conditional branch instructions (Jcc).“ From the internet:
“gcc is right to not generate the prefix, as they have no effect for all processors since the Pentium 4.”

## Slide 59: Dynamically predicting branch behavior
Fetch
Decode
Execute
Memory
Register Write-Back
0x100: beq x16 x12 PC+0xC
Branch Predictor
Outcome: taken
Target: 0x10C

## Slide 60: Dynamically predicting branch behavior
Fetch
Decode
Execute
Memory
Register Write-Back
0x100: beq x16 x12 PC+0xC
Branch Predictor
Outcome:
Target:
0x10C: sub x6 x5 x4
A dynamic branch predictor is a circuit that learns the likely outcome of a branch and keeps a record of its past target computations
Guess what happens after the current instruction and run speculatively.
Fetch the predicted instruction (sub,
here) and start executing with no delay.

## Slide 61: Speculation entails guessing about what’s next
Fetch
Decode
Execute
Memory
Register Write-Back
Branch Predictor
Outcome:
Target:
sub x6 x5 x4 beq x16 x12 PC+0xC
Question: What do we do on a misprediction (also known as a branch mis-speculation)?
Resolved not taken
0x100
Predicted taken
0x10C
Fetch more…
0x110
lw x6 0xabc

## Slide 62: Recovering from branch misprediction
Fetch
Decode
Execute
Memory
Register Write-Back
Resolved not taken
0x100
beq x16 x12 PC+0xC
Branch Predictor
Outcome:
Target:
Incorrectly predicted taken
nop nop
Recovery: Zero all control signals (nop) & reset PC to PC+4 of beq
Recovery from mis-speculation entails wasted work in the pipeline. What about other state? Register file? Anything else might end up corrupted by speculative execution? Main cost? How cost scales?

## Slide 63: Dynamically predicting branch behavior
Fetch
Decode
Execute
Memory
Register Write-Back
0x100: beq x16 x12 PC+0xC
Branch Predictor
Outcome:
Target:
0x10C: sub x6 x5 x4
Question: where does the branch predictor live in our pipeline?

## Slide 64: Branch Predictor in the pipeline
ALU
Input
Read Reg A
ALU: output C data
Instruction Memory
Instruction Fetch
Control Signals:
O
o
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Input
Read
Reg B
Write Reg C Data ALU
Instruction PC+4 Branch Target
Branch Target
Branch
Target Offset
Instruction +
PC + 4
Branch
Target
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
MemRead/ MemWrite
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
IF/
ID
ID/
EX/ Mem
Mem
/WB Write Reg C Data
Wr Data
Write Reg C Data Mem
Control
Signals
Read
Register EX
A & B
Select
PC Source Select (1 if branch taken)
Key Idea: Add predictor to fetch stage, allowing continuous fetch
Branch Predictor
Branch
Predictor
Outcome:
Branch Target:

## Slide 65: Dynamically predicting branch behavior
Branch Predictor
Outcome:
Target:
Branch Address
Predictors learn from past behavior
Need to predict branch outcome: 0/1
Need to “predict” branch target: PC
Need to validate prediction
Need to update predictor
Many different types of predictor

## Slide 66: Predicting Branch Outcomes
0x100: beq x16 x12 PC+0xC
Branch Address
What info do we have?
Outcome: taken
Branch Predictor

## Slide 67: Predicting Branch Outcomes
Branch Predictor
Branch Address
0x100: beq x16 x12 PC+0xC
Outcome: taken
What info do we have?
History of prior branch outcomes
0x100: 111111111011111111101111111110…

## Slide 68: Predicting Branch Outcomes
Branch Predictor
Branch Address
0x100: beq x16 x12 PC+0xC
Outcome: taken
What info do we have?
History of prior branch outcomes
For every branch in the program
Hardware idea: keep history in table and choose most likely outcome
0x100: 111111111011111111101111111110…
0x10E: 111001111011111111101100000110…
0x200: 000000000011111111100000000000…
0x210: 100011111011110001101111000110…
0x214: 000000000000000000000000000000…
0x220: 111000000010000000001000000000…

## Slide 69: Proposal: Store predictor state in fetch stage with prediction logic
Branch Predictor in the pipeline
ALU
Input
Read Reg A
ALU: output C data
Instruction Memory
Instruction Fetch
Control Signals:
O
o
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Input
Read
Reg B
Write Reg C Data ALU
Instruction PC+4 Branch Target
Branch Target
Branch
Target Offset
Instruction +
PC + 4
Branch
Target
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
MemRead/ MemWrite
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
IF/
ID
ID/
EX/ Mem
Mem
/WB Write Reg C Data
Wr Data
Write Reg C Data Mem
Control
Signals
Read
Register EX
A & B
Select
PC Source Select (1 if branch taken)
0x100: 111111111011111O1u11t10c1o11m11e1:1110…
0x10E: B1r1a10n0c1h111011111111101100000110…
0x200: 000000000011111B1r11a10n0c00h0000000…
0x210:Pr1e00d0i1c1t1o1r1011110T0a01r10g1e11t10:00110…
0x214: 000000000000000000000000000000…
0x220: 111000000010000000001000000000…
Branch Predictor
Problems with this design?

## Slide 70: Predicting Branch Outcomes
Branch Predictor
Branch Address
Outcome: taken
Making branch history implementable
Idea 1: Hash table from PC to entry
Eliminates table size = #branch insns.
Branch History Table (BHT)
hash()
0x100
Branch PC

## Slide 71: Predicting Branch Outcomes
Branch Predictor
Branch Address
Predicted Outcome: T/NT
Making branch history implementable
Idea 2: Concise history of outcomes
Eliminates entry size = #branch executions
Branch History Table (BHT)
hash()
0x100
10
00
00
11
Branch PC
01
10
00
11
NT
NT
NT
NT
T
Two-bit saturating counter branch predictor
T T T

## Slide 72: Bimodal BHT Branch Predictor (Lab 1)
Branch Predictor
Branch Address
Predicted Outcome: T/NT
Making branch history implementable
Idea 2: Concise history of outcomes
Eliminates entry size = #branch executions
Branch History Table (BHT)
hash()
0x100
10
00
00
11
Branch PC
01
10
00
11
NT
NT NT NT
Example history - 0x100: 1010110110110110…
T
Two-bit saturating counter branch predictor
T T T

## Slide 73: Bimodal BHT Branch Predictor
[“Combining Branch Predictors”, McFarling ’93]

## Slide 74: Predicting Branch Outcomes
Limitations of 2-bit BHT branch prediction
Limitation 1: branch interference due to hash table collisions
Limitation 2: single-branch decision making misses correlation How to handle each of these problems?
Branch History Table (BHT)
hash()
0x100
10
00
00
11
Branch PC
01
10
00
11
NT
NT NT NT
Example history - 0x100: 1010110110110110…
T
Two-bit saturating counter branch predictor
T T T

## Slide 75: Avoiding collisions
Example history - 0x100: 1010110110110110…
Large table size (e.g., 16k entries) avoids collisions
Each entry is small, making total cost tolerable (e.g., 32kb)
Large enough table and collisions do not limit prediction accuracy
Branch History Table (BHT)
hash()
0x100
Branch PC
01
10
00
11
NT
NT NT NT
T
Two-bit saturating counter branch predictor
T T T
10
00
00
11
16k Entries
. . .

## Slide 76: Catching correlated branches
There are correlation of the outcomes of consecutive branches
The outcome of the third branch is correlated with the first two
Our per-branch predictor cannot capture this common pattern
Branch History Table (BHT)
hash()
0x100
Branch PC
10
00
00
11
16k Entries
. . .
if(a | == | 1){ | a=0 | }
if(b | == | 1){ | b=0 | }
if(a | != | b){ | ... | }

## Slide 77: Two-Level Branch Predictor (Option for Lab 1): GAp (Global Adaptive w/ per-address table)
Track history of outcomes of all branches executed in GHT
Use PC to select which PHT to use
Use global pattern history to index into PHT
Use PHT entry’s 2-bit counter to predict outcome
After each branch resolves, updated predictor in per-address
pattern history table & shift its outcome (T=1, NT=0) into GHT
Per-address “pattern history table”
hash()
0x100
10 | 00
00 | 00
00 | 00
11 | 11
Branch PC
16k Entries
. . .
if(a | == | 1){ | a=0 | }
if(b | == | 1){ | b=0 | }
if(a | != | b){ | ... | }
. . .
11
11
00
11
10010110
Global History Table

## Slide 78: Global Index Sharing Predictor
Index sharing predictor tracks local history in global context concisely
XOR GHT with branch PC to select BHT
Use 2-bit counter in BHT to make prediction for branch in GHT context
XOR maps branches & contexts that matter to different BHTs
Gshare combining addr bits with history bits often better
Branch History Table (BHT)
xor
0x100
Branch PC
10
00
00
11
16k Entries
. . .
if(a | == | 1){ | a=0 | }
if(b | == | 1){ | b=0 | }
if(a | != | b){ | ... | }
10010110
Global History Table

## Slide 79: Local/Global Correlating Predictor (Optional for Lab 1): PAg (Per-Address Adaptive global history table)
Per-PC Branch History Table
Use per-branch history to index into a global, shared table of
predictors. Per-PC branch history table stores history for that branch only, not global history.
Use PC to select which BHT to use
Use branch history to index into global PHT
Use PHT entry’s 2-bit counter to predict outcome
0x100
Branch PC
if(a == 1){ a=0 }
if(b == 1){ b=0 } if(a != b){ ... }
11
11
00
11
10010110
10010110
10010110
10010110
. . .
. . .
Global Pattern History Table
hash()
n entries
(256 entries here)
log n bits
(8 bits here)

## Slide 80
(Choose best option)
Quantifying Predictor Accuracy

## Slide 81: Dynamically predicting branch behavior
Fetch
Decode
Execute
Memory
Register Write-Back
0x100: beq x16 x12 PC+0xC
Branch Predictor
Target: 0x10C
Need to predict branch target
Target gets resolved only in Decode, which leads to 1-cycle stall
Predict outcome and target both in Fetch & avoid all stalls

## Slide 82: Branch Target Buffer Implementation
Branch Target Buffer
hash()
0x1a2100
BranchID
1a2ABC
1A210C
Branch Tag
Tag
Target
1A22EE
1A2112
1A2
Target: 0x1A210C
Branch Target Buffer (BTB) logs branch target
BTB is associative memory table indexed by branch PC low order bits
Need tag because some PCs do not point to branches
Associative memory can be set-, fully-associative or direct-mapped
Branch PC = Tag + ID

## Slide 83: Putting it all together: A Gshare branch predictor + BTB
Branch Target Buffer
hash()
0x1a2100
BranchID
1a2ABC
1A210C
Branch Tag
Tag
Target
1A22EE
1A2112
1A2
Target: 0x1A210C
Branch History Table (BHT)
xor
0x100
Branch PC
10
00
00
11
16k Entries
. . .
10010110
Global History Table
Outcome: Taken
Branch predictors resolve branches in the fetch stage avoiding stalls
Need misprediction detection logic added to decode stage
Need logic to flush instructions on predicted path after misprediction
Flushed instructions are effectively stalls in the pipeline, but worse: wasted work.

## Slide 84: Branch Predictor in the pipeline
ALU
Input
Read Reg A
ALU: output C data
Instruction Memory
Instruction Fetch
Control Signals:
O
o
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Input
Read
Reg B
Write Reg C Data ALU
Instruction PC+4 Branch Target
Branch Target
Branch
Target Offset
Instruction +
PC + 4
Branch
Target
Addr
RReeaadd DDaattaa CC
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
MemRead/ MemWrite
Instruction Fetch
Reg 4
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
IF/
ID
ID/
EX/ Mem
Mem
/WB Write Reg C Data
Wr Data
Write Reg C Data Mem
Control
Signals
Read
Register EX
A & B
Select
PC Source Select (1 if branch taken)
Branch Predictor
.
.
.

## Slide 85: What did we just learn?
Control hazards introduce stalls because on a branch the pipeline
doesn’t know what to fetch next
Single stall cycle with early branch resolution (in Decode)
Branch delay slots and static prediction do OK, but still need stalls and nops often
Dynamic Branch Prediction uses per-branch information and global branch outcome history information to predict outcomes and targets
Branch predictor accuracies are in the 90+% in a lot of cases (you will see these figures in Lab 1)

## Slide 86: What to think about next?
Caches as a microarchitectural optimization (next time)
  Implementation of cache hierarchies
  Cache design tradeoffs
Performance Evaluation (next next time)
  Design spaces, Pareto Frontiers, and design space exploration