## Slide 1
Fall 2023
Lecture 9: Introduction to Performance Evaluation
Credit: Brandon Lucia

## Slide 2: Today: Performance Evaluation
Performance evaluation basics: metrics, measurement, comparisons
Benchmarks and benchmarking
The curse of averages: means, variance, distributions
Selecting the right metric along which to compare two systems
Defining a design space
Pareto Frontiers and Pareto Optimality of a design
Design space exploration and design iteration

## Slide 3: How good is this architecture?
ALU
ALU: output C data
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data Memory
4
+
MUX
Branch Target
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control
Signals
Read Register A & B Select
Input Read Reg B
Write Reg C Data
Branch Target
Read
Data C
Read Data C (Ld)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select
[Ld/St]
Instruction Fetch
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
Exec/Exec Forward
Mem/Mem Forward
Mem/Exec Forward
WB/Exec Forward
Instruction PC+4
WB/Mem Forward
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
Input Read Reg A
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
Branch
Target
+
Offset
Instruction PC + 4
Branch
Target
Branch
Outcome Logic
PC
Source Select
Reg A Reg B
.
.
.
Branch Predictor
Outcome
Target

## Slide 4: How good is this architecture?
ALU
ALU: output C data
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data Memory
4
+
MUX
Branch Target
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control
Signals
Read Register A & B Select
Input Read Reg B
Wr Writ
ite Register C Select
e Register C Data
Write Reg C Data
Branch Target
Read
Data C
Read Data C (Ld)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select
[Ld/St]
Instruction Fetch
Instr. Decode Execute
Read Regs A & B Data
Memory
Register Write-Back
Exec/Exec Forward
Mem/Mem Forward
Mem/Exec Forward
WB/Exec Forward
Instruction PC+4
WB/Mem Forward
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
Input Read Reg A
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
Branch
Target
+
Offset
Instruction PC + 4
Branch
Target
Branch
Outcome Logic
PC
Source Select
Reg A Reg B
.
.
.
Branch Predictor
Outcome
Target
Key Question: Good relative to what?

## Slide 5: Which architecture is better?

## Slide 6: Which architecture is better?
Key Question: What defines “good”?

## Slide 7: Intel Core i7-4960X
17.1mm
15mm
Area: 257 mm^2 22nm process tech. 3.6GHz

## Slide 8: Intel Pentium 4
35mm
35mm
Area: 1225 mm^2 180nm process tech. 1.8GHz

## Slide 9: Intel Pentium Pro / Klamath Falls
14mm
14mm
Area: 194.8 mm^2 280nm process tech. 0.3GHz

## Slide 10: Comparing Processor Designs
Area
(mm^2)
1225
257
194
What do we learn from this comparison?
257
194
Area: 194.8 mm2
280nm tech
0.3GHz
Area: 1225 mm2
180nm tech
1.8GHz
Area: 257 mm2 22nm process tech. 3.6GHz

## Slide 11: Comparing Processor Designs
Process
Normalized Area (mm^2)
1.21
19.14
257
Now what do we learn? What did we change?
Process normalization example:
180nm / 22nm = ~8x
35mm / 8x = 4.375 // 1225 = 35*35
4.375 * 4.375 = 19.14 //half-square dim.
Area: 194.8 mm2
280nm tech
0.3GHz
Area: 1225 mm2
180nm tech
1.8GHz
Area: 257 mm2 22nm process tech. 3.6GHz

## Slide 12: Comparing Processor Designs
Process
Normalized Area (mm^2)
1.21
19.14
257
Process normalization example:
180nm / 22nm = ~8x
35mm / 8x = 4.375
4.375 * 4.375 = 19.14 //half-square dim.
The metric you use should suit the comparison
Area: 194.8 mm2
280nm tech
0.3GHz
Area: 1225 mm2
180nm tech
1.8GHz
Area: 257 mm2 22nm process tech. 3.6GHz

## Slide 13: Comparing Processor Designs
Normalized
Process- Normalized Area (mm^2)
1.0x
212.4x
Normalize the results to the most logical
option in your data set
15.8x
The relative value is most important in comparisons
7.5M Transistors 42M Transistors
1.9B Transistors
Wow! 212.4x more complexity
than a Pentium Pro!
Area: 194.8 mm2
280nm tech
0.3GHz
Area: 1225 mm2
180nm tech
1.8GHz
Area: 257 mm2 22nm process tech. 3.6GHz

## Slide 14: There are lots of metrics to choose from
Performance:
  Run time or “latency” (seconds to get a result)
  Throughput (results per second)
  Instructions per Cycle (IPC) or Cycles per Instruction (CPI)
Energy:
  Total energy
  Power (avg. or peak) [we will come back to this one….]
  Area (absolute or normalized)
Efficiency:
  Performance per power (GigaOperations Per Second Per Watt: GOPS/W)
  Operations per Joule (1W = 1J/s, so multiply by J/s, then by 1s)
  Throughput per unit area (results per second per mm2)

## Slide 15: There are lots of metrics to choose from
Cache-specific:
  Cache Misses per Kilo-Instruction
  Cache Misses per Kilo-Memory-Instruction
  Cache Misses per Cache Access
  Average Memory Access Time
Control-specific:
  Branch prediction accuracy
  Branch Mispredictions per Kilo-Instruction
Memory-specific:
  Data throughput (GB/s)
  Memory Latency (seconds per random byte)

## Slide 16: Measuring a System’s Performance
Get a system that you want to measure and clean it up and isolate it from everything else in the world
Find a workload that you can run on your system and
that will produce a meaningful result
Choose an appropriate baseline system to which to
compare your results to understand their relative merit

## Slide 17: Measure your baseline…

## Slide 18: …measure your system…

## Slide 19: …and compare the results
Normalized Run Time
1.0x
0.74x
baseline ref baseline ref ref baseline
These are equivalent results, with different presentations
Speedup
1.36x
1.0x
Run Time (s)
8.2s
6.0s

## Slide 20: Choosing your measurement workload The “Benchmark Problem”

## Slide 21
What are we looking for in a benchmark program?
Representative of typical workloads for system
Runs long enough to measure precisely
Runs in reasonable time for repeated trials
Runs with deterministic metric values
Runs w/ no excessively large inputs or I/O
Runs with no human intervention

## Slide 22: Benchmark Suites
The Standard Performance Evaluation Corporation
Founded 1988 by workstation computer manufacturers
Goal: eliminate hype misinformation, replace hype with hard data,
eliminate “apples-to-oranges” comparison of computer systems
Methodology: provide standardized suite of source code that a benchmarker (a human) can compile for their system, tune for best results, and run for an official benchmark performance score comparable to others.
Updates benchmark suite periodically to keep it in line with the market, i.e. the workloads driving the sales.

## Slide 23: What are these benchmark programs?

## Slide 24: MLPerf (“MLCommons”) Benchmarks

## Slide 25: What are these benchmark programs?

## Slide 26: Allows us to compare different machines?
What is this axis showing?

## Slide 27: SPEC Baselines to a Reference Machine
Oracle Sun Fire V490
Competitive 2000s-era server
4-Socket UltraSPARC IV architecture 64GB Max Memory Capacity
Last shipped April 2009
For SPEC2017, this machine represents 1.0 SPECMarks Why compare to some random machine from 2001?

## Slide 28: Allows us to compare arbitrary machines!
SPECMarks: Normalized throughput relative to Sun Fire V490
Oracle Sun Fire V490
Competitive 2000s-era server
4

## Slide 29: The SPEC Reference Machine Challenge
A current competitor won’t fly
  It is an industry benchmark.
  Do you want your machine to be the slow 1.0?
  Do you want everyone talking about a competitor’s product as if it is the current gold standard
An unfamiliar machine is an unintuitive metric
An imaginary machine is worse
An older machine may be poorly suited for current workloads
  It isn’t just ops/sec.
  Consider a modern large working set workload run on an older machine with a smaller cache. How does one compare?
A recent “venerable workhorse” may be the best option

## Slide 30: A Few Other Presently Relevant Benchmarks
Cloudsuite
  Data center works (may be a little less relevant than a few years ago)
MLPerf
  Cloud-based training and inference performance
GAP Code (Berkeley)
  Data center works (may be a little less relevant than a few years ago)
It is sometimes appropriate to propose a new benchmark tuned to emerging concerns, but results are typically also reported for well-accepted benchmark(s) until the research community understands the proposed benchmark, observes a critical mass of research data based upon it, and accepts its relevance.

## Slide 31: Lies, Damned Lies, and Statistics (Twain/Diraeli)
Comparing to the wrong thing can make anything look good
  Comparing an improvement of a feature to the absence of a feature, e.g. a new branch predictor to none at all vs comparing it to a well-accepted best-of-class
Comparing in a nonsensical environment can make anything look good
  Workload too large for cache on reference machine
  Comparing single core to multicore and letting bus traffic interfere
Choosing a benchmark not relevant to the audience or problem
  E.g., just a SPEC benchmark, when the use case is a novel workload for which the chosen benchmark, though well accepted for other purposes, is not relevant.
Managing the data
  Cherry-picking runs (when there is environmental interference)
  Not excluding outliers (when there is environmental interference)
  Averaging or otherwise summarizing inappropriately

## Slide 32: Practical Normalized Performance Measurement
Speedup
1.36x
1.0x
ref
baseline
Userspace Run Time (s)
8.2s
6.0s
baseline
ref
Choose appropriate baseline system
  Not going to use Oracle Sun Fire V490 unless you’re
submitting to SPEC
Select a highly optimized baseline
  Avoid “Straw Man” comparisons
Select a comparable baseline
  Avoid “apples-to-oranges” comparisons

## Slide 33: Single Number Performance Summaries
Speedup
perlbench
gcc
mcf
xalan
omnetpp
x264
deepsjeng
leela
SPEC2017
Average
What is the meaning of this bar over here?

## Slide 34: On Computing Averages: Options

## Slide 35: Amean – Good for averaging times
Averages all data points equally. Sums them up and divides by number of fata points
Good for times.

## Slide 36: Geometric Mean – good for speedups
Program 1: 0.5x speedup Program 2: 2.0x speedup
Average speedup: 1.0 (one is half as fast, one is twice as fast)
Amean(0.5,2.0) = (0.5+2.0) / 2 = 2.5 / 2 = 1.25x
Gmean(0.5,2.0) = sqrt(0.5 * 2.0) = Sqrt(1.0) = 1.0
See the problem?

## Slide 37: Harmonic Mean – Good for rates
F() has N instructions
N instructions at 60GOPS
N same instructions at 20GOPS
Total time = N/60 + N/20 = N/15; N=60 -> 4s.
Amean: (60GOPS + 20 GOPS) / 2 = 40GOPS
Total time using Amean: 2N / 40; N = 60 -> 120/40 = 3s (incorrect)
Hmean: Avg GOPS = Total Instructions / Sum of per-call times =
2N / (N/60 + N/20) = 2 / (1/60 + 1/20) = 2 / (1 / 15) = 30 GOPS
Total time using Hmean: 2N / 30; N = 60 -> 120/30 = 4s (correct)

## Slide 38: The problem with single-number performance summaries by example
Benchmark #1 Userspace
Run Time (s)
12s
3s
baseline
ref
Benchmark #2 Userspace
Run Time (s)
600s
300s
baseline
ref

## Slide 39: Thinking in ratios
Benchmark #1 Userspace
Run Time (s)
12s
3s
baseline ref
Speedup = 12s / 3s = 4x
Benchmark #2 Userspace
Run Time (s)
600s
300s
baseline ref
Speedup = 600s / 300s = 2x
Unweighted Average Speedup (gmean of speedups) = sqrt(4x * 2x) = 2.82x (No benchmark is more important or prevalent than any other in the wild despite differences in time during tests – unweighted average.)
Time-weighted Average Speedup (amean of times) = 612s / 303s = 2.02x (Runtime of each test indicates its
prevalence/importance in the wild. Tests that run longer count for more – weighted average. This only makes sense if workloads balance out in this proportion in the wild. Otherwise can weight by prevalence, etc. )

## Slide 40: Isolating your measurement environment

## Slide 41: Isolating your measurement environment
First check the basics (like no one is gamin’ on the rig)

## Slide 42: Unintuitive Sources of Performance Interference

## Slide 43
blucia@Nuugaatsiaq:~$ env SHELL=/bin/bash
PINPATH=/home/blucia/cvsandbox/pin/pin-3.18-98332-gaebd7b1e6-gcc-linux
WSL_DISTRO_NAME=Ubuntu-20.04
NAME=Nuugaatsiaq PWD=/home/blucia LOGNAME=blucia MOTD_SHOWN=update-motd HOME=/home/blucia LANG=C.UTF-8
WSL_INTEROP=/run/WSL/632_interop
LS_COLORS=rs=0:di=01;34:ln=01;36:mh=00:pi=40;33:so=01;35:do=01;35:bd=40;33;01:cd=40;33;01:or=40;31;01:mi=00:su=37;41:sg=30;43:ca=30;41:tw=30;42:ow=34;42:st=3
7;44:ex=01;32:*.tar=01;31:*.tgz=01;31:*.arc=01;31:*.arj=01;31:*.taz=01;31:*.lha=01;31:*.lz4=01;31:*.lzh=01;31:*.lzma=01;31:*.tlz=01;31:*.txz=01;31:*.tzo=01;3
1:*.t7z=01;31:*.zip=01;31:*.z=01;31:*.dz=01;31:*.gz=01;31:*.lrz=01;31:*.lz=01;31:*.lzo=01;31:*.xz=01;31:*.zst=01;31:*.tzst=01;31:*.bz2=01;31:*.bz=01;31:*.tbz
=01;31:*.tbz2=01;31:*.tz=01;31:*.deb=01;31:*.rpm=01;31:*.jar=01;31:*.war=01;31:*.ear=01;31:*.sar=01;31:*.rar=01;31:*.alz=01;31:*.ace=01;31:*.zoo=01;31:*.cpio
=01;31:*.7z=01;31:*.rz=01;31:*.cab=01;31:*.wim=01;31:*.swm=01;31:*.dwm=01;31:*.esd=01;31:*.jpg=01;35:*.jpeg=01;35:*.mjpg=01;35:*.mjpeg=01;35:*.gif=01;35:*.bm p=01;35:*.pbm=01;35:*.pgm=01;35:*.ppm=01;35:*.tga=01;35:*.xbm=01;35:*.xpm=01;35:*.tif=01;35:*.tiff=01;35:*.png=01;35:*.svg=01;35:*.svgz=01;35:*.mng=01;35:*.p cx=01;35:*.mov=01;35:*.mpg=01;35:*.mpeg=01;35:*.m2v=01;35:*.mkv=01;35:*.webm=01;35:*.ogm=01;35:*.mp4=01;35:*.m4v=01;35:*.mp4v=01;35:*.vob=01;35:*.qt=01;35:*. nuv=01;35:*.wmv=01;35:*.asf=01;35:*.rm=01;35:*.rmvb=01;35:*.flc=01;35:*.avi=01;35:*.fli=01;35:*.flv=01;35:*.gl=01;35:*.dl=01;35:*.xcf=01;35:*.xwd=01;35:*.yuv
=01;35:*.cgm=01;35:*.emf=01;35:*.ogv=01;35:*.ogx=01;35:*.aac=00;36:*.au=00;36:*.flac=00;36:*.m4a=00;36:*.mid=00;36:*.midi=00;36:*.mka=00;36:*.mp3=00;36:*.mpc
=00;36:*.ogg=00;36:*.ra=00;36:*.wav=00;36:*.oga=00;36:*.opus=00;36:*.spx=00;36:*.xspf=00;36: PIN_ROOT=/home/blucia/cvsandbox/pin/pin-3.18-98332-gaebd7b1e6-gcc-linux PIN_HOME=/home/blucia/cvsandbox/pin/pin-3.18-98332-gaebd7b1e6-gcc-linux LESSCLOSE=/usr/bin/lesspipe %s %s
TERM=xterm-256color
LESSOPEN=| /usr/bin/lesspipe %s USER=blucia DISPLAY=172.17.80.1:0
SHLVL=1 WSLENV=
XDG_DATA_DIRS=/usr/local/share:/usr/share:/var/lib/snapd/desktop PROJECT_ROOT=/home/blucia/cvsandbox/panic PATH=/home/blucia/.local/bin:/home/blucia/cvsandbox/pin/pin-3.18-98332-gaebd7b1e6-gcc-
linux:/home/blucia/.local/bin/:/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin:/usr/games:/usr/local/games:/mnt/c/Program Files/WindowsApps/CanonicalGroupLimited.Ubuntu20.04onWindows_2004.2021.610.0_x64 79rhkp1fndgsc:/mnt/c/WINDOWS/system32:/mnt/c/WINDOWS:/mnt/c/WINDOWS/System3 2/Wbem:/mnt/c/WINDOWS/System32/WindowsPowerShell/v1.0/:/mnt/c/WINDOWS/System32/OpenSSH/:/mnt/c/Program Files (x86)/PDFtk Server/bin/:/mnt/c/Program Files/MIT/Kerberos/bin:/mnt/c/Program Files/OpenAFS/Common:/mnt/c/Program Files/OpenAFS/Client/Program:/mnt/c/Users/bluci/AppData/Local/Microsoft/WindowsApps:/snap/bin
HOSTTYPE=x86_64
RISCV=/home/blucia/cvsandbox/panic-riscv-tools/riscv-tools
_=/usr/bin/env blucia@Nuugaatsiaq:~$

## Slide 44
blucia@Nuugaatsiaq:~$ env SHELL=/bin/bash
PINPATH=/home/blucia/cvsandbox/pin/pin-3.18-98332-gaebd7b1e6-gcc-linux
WSL_DISTRO_NAME=Ubuntu-20.04
NAME=Nuugaatsiaq PWD=/home/blucia LOGNAME=blucia MOTD_SHOWN=update-motd HOME=/home/blucia LANG=C.UTF-8
WSL_INTEROP=/run/WSL/632_interop
LS_COLORS=rs=0:di=01;34:ln=01;36:mh=00:pi=40;33:so=01;35:do=01;35:bd=40;33;01:cd=40;33;01:or=40;31;01:mi=00:su=37;41:sg=30;43:ca=30;41:tw=30;42:ow=34;42:st=3
7;44:ex=01;32:*.tar=01;31:*.tgz=01;31:*.arc=01;31:*.arj=01;31:*.taz=01;31:*.lha=01;31:*.lz4=01;31:*.lzh=01;31:*.lzma=01;31:*.tlz=01;31:*.txz=01;31:*.tzo=01;3
1:*.t7z=01;31:*.zip=01;31:*.z=01;31:*.dz=01;31:*.gz=01;31:*.lrz=01;31:*.lz=01;31:*.lzo=01;31:*.xz=01;31:*.zst=01;31:*.tzst=01;31:*.bz2=01;31:*.bz=01;31:*.tbz
=01;31:*.tbz2=01;31:*.tz=01;31:*.deb=01;31:*.rpm=01;31:*.jar=01;31:*.war=01;31:*.ear=01;31:*.sar=01;31:*.rar=01;31:*.alz=01;31:*.ace=01;31:*.zoo=01;31:*.cpio
=01;31:*.7z=01;31:*.r .gif=01;35:*.bm
p=01;35:*.pbm=01;35:
z=01;31:*.cab=01;31:*.wim=01;31:*.swm=01;31:*.dwm=01;31:*.esd=01;31:*.jpg=01;35:*.jpeg=01;35:*.mjpg=01;35:*.mjpeg=01;35:*
*.pgm=01;35:*.ppm=01;35:*.tga=01;35:*.xbm=01;35:*.xpm=01;35:*.tif=01;35:*.tiff=01;35:*.png=01;35:*.svg=01;35:*.svgz=01;35:
*.mng=01;35:*.p
cx=01;35:*.mov=01;35:*.mpg=01;35:*.mpeg=01;35:*.m2v=01;35:*.mkv=01;35:*.webm=01;35:*.ogm=01;35:*.mp4=01;35:*.m4v=01;35:*.mp4v=01;35:*.vob=01;35:*.qt=01;35:*. nuv=01;35:*.wmv=01;35:*.asf=01;35:*.rm=01;35:*.rmvb=01;35:*.flc=01;35:*.avi=01;35:*.fli=01;35:*.flv=01;35:*.gl=01;35:*.dl=01;35:*.xcf=01;35:*.xwd=01;35:*.yuv
=01;35:*.cgm=01;35:*.emf=01;35:*.ogv=01;35:*.ogx=01;35:*.aac=00;36:*.au=00;36:*.flac=00;36:*.m4a=00;36:*.mid=00;36:*.midi=00;36:*.mka=00;36:*.mp3=00;36:*.mpc
=00;36:*.ogg=00;36:*.ra=00;36:*.wav=00;36:*.oga=00;36:*.opus=00;36:*.spx=00;36:*.xspf=00;36: PIN_ROOT=/home/blucia/cvsandbox/pin/pin-3.18-98332-gaebd7b1e6-gcc-linux PIN_HOME=/home/blucia/cvsandbox/pin/pin-3.18-98332-gaebd7b1e6-gcc-linux LESSCLOSE=/usr/bin/lesspipe %s %s
TERM=xterm-256color
esspipe %s
USER=blucia
DISPLAY=172.17.80.1:0
SHLVL=1 WSLENV=
XDG_DATA_DIRS=/usr/local/share:/usr/share:/var/lib/snapd/desktop PROJECT_ROOT=/home/blucia/cvsandbox/panic PATH=/home/blucia/.local/bin:/home/blucia/cvsandbox/pin/pin-3.18-98332-gaebd7b1e6-gcc-
linux:/home/blucia/.local/bin/:/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin:/usr/games:/usr/local/games:/mnt/c/Program Files/WindowsApps/CanonicalGroupLimited.Ubuntu20.04onWindows_2004.2021.610.0_x64 79rhkp1fndgsc:/mnt/c/WINDOWS/system32:/mnt/c/WINDOWS:/mnt/c/WINDOWS/System3 2/Wbem:/mnt/c/WINDOWS/System32/WindowsPowerShell/v1.0/:/mnt/c/WINDOWS/System32/OpenSSH/:/mnt/c/Program Files (x86)/PDFtk Server/bin/:/mnt/c/Program Files/MIT/Kerberos/bin:/mnt/c/Program Files/OpenAFS/Common:/mnt/c/Program Files/OpenAFS/Client/Program:/mnt/c/Users/bluci/AppData/Local/Microsoft/WindowsApps:/snap/bin
HOSTTYPE=x86_64
RISCV=/home/blucia/cvsandbox/panic-riscv-tools/riscv-tools
_=/usr/bin/env blucia@Nuugaatsiaq:~$
int execvpe(const char *file, char *const argv[], char *const envp[]);
LESSOPEN=| /usr/bin/l Every process includes an environment that takes up some memory in its address space

## Slide 45: The size of your Unix environment can bias your measurements!
(It can change alignment of data on the stack, changing cache conflicts, etc.)

## Slide 46: The order in which you link libraries affects optimizability (O2 vs. O3)
(Changing locations changes alignment w.r.t. cache conflicts, as very nuanced things such as branch prediction, alignment within buffers/queues, etc.)

## Slide 47: Measurement bias effects may exceed the scale of actual effects
Setup randomization: Semi-systematic randomization of address layout, environment, and other factors

## Slide 48: It may be impossible to entirely isolate
Real world benchmarking is most relevant to the real world
It is also most subject to environmental interference
One can’t eliminate every aspect of environment, e.g. OS activity
It may be that the best one can do is to clean up as much as possible and then exclude outliers.
Even comparing only user time ignores the impact of side-effects

## Slide 49: What did we just learn?
Performance Evaluation
  What does it mean to evaluate a system?
  How to compare two systems?
  How to do a performance experiment?
  Measurement pitfalls & metrics
  Single-number performance summaries
  Averages
  Measurement bias sources

## Slide 50: What to think about next?
Performance Evaluation (next time)
  Design spaces, Pareto Frontiers, and design space exploration
Miscellaneous (micro)architectural tricks & optimizations (future)
  Vector processors, SIMD/SIMT, dataflow