## Slide 1: Energy-minimal Computing Edge architectures for extreme efficiency
Brandon Lucia - Carnegie Mellon University - Challenges of Intermittent Computing
2

## Slide 2: Existing architectures are extremely inefficient
Control/Communication
Instruction energy* breakdown:
Useful compute (10%)
>90%
*Horowitz ISSCC 2014 + measured values
Extreme Edge Computing Goal:
increase energy-efficiency and preserve programmability

## Slide 3: Where does all the energy go in existing computer architectures?
Fetch/Decode (40-50%) | Register file (20%) | Other control | Useful compute (10%)
Something is fundamentally wrong here:
Instruction energy* breakdown:
ASICs/Accelerators would improve this, but forfeit programmability
*Horowitz ISSCC 2014 + measured values

## Slide 4: Fundamental extreme edge trade-offs High Programmability
High Performance
Low Power
Opportunity for the
extreme edge
Well-studied
(GPUs, OOO, SIMD)
Well-studied (ASICs)

## Slide 5: Fundamental extreme edge trade-offs High Programmability
High Performance
Low Power
Opportunity for the extreme edge
Manic
x
SNAFU
x
Well-studied (GPUs, OOO, SIMD)
Well-studied (ASICs)
RipTide
x
Key Idea:
Different architecture, different set of tradeoffs
Extreme edge applications demand programmable & energy- minimal architectures

## Slide 6: MANIC: Extreme Edge Vector-dataflow processor
Reduce instruction supply energy + VRF energy
Maintain high-degree of programmability to support future kernels
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector- Dataflow |  |  | 
7

## Slide 7: Scalar execution model
for i in 0...3: load r0, &a[i] mul r1, r0, r0 add r2, r1, r0 store &b[i], r2
load
mul
add
store
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector
Vector-
Dataflow
Example Program
register
load
register
Dataflow
mul
register
add
register
store
Control-flow
Related: MSP430, ARM M0
8

## Slide 8: Scalar execution model
for i in 0...3: load r0, &a[i] mul r1, r0, r0 add r2, r1, r0 store &b[i], r2
load
mul
add
store
Dataflow
add
register
store
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector
Vector-
Dataflow
Example Program
register
load
register
mul
register
Dataflow
Control-flow

## Slide 9: Scalar execution model
for i in 0...3: load r0, &a[i] mul r1, r0, r0 add r2, r1, r0 store &b[i], r2
load
mul
add
store
Dataflow
store
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector
Vector- Dataflow
Example Program
register
load
register
mul
register
register
add
Dataflow
Control-flow

## Slide 10: Scalar execution model
for i in 0...3: load r0, &a[i] mul r1, r0, r0 add r2, r1, r0 store &b[i], r2
load
mul
add
store
Dataflow
register
load
register
mul
register
add
register
store
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector
Vector-
Dataflow
Repeat fetches + decodes
Read and write
to RF
Example Program
Dataflow
Control-flow

## Slide 11: Scalar execution is inefficient
Memory | DCache access | ICache access | Compute + Control
Energy wasted on instruction & data supply

## Slide 12: Vector execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector |  |  | 
Vector-
Dataflow
Example Program
vload:
vmul: v[0] v[1] v[2]
Vector Register
vadd: v[0] v[1] v[2]
Vector Register
vstore: v[0] v[1] v[2]
v[1]
v[0]
v[2]
Vector Register
Dataflow
Control-flow

## Slide 13: Vector execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector |  |  | 
Vector-
Dataflow
Example Program
vload:
vmul:
v[1]
v[0]
v[2]
vadd: v[0] v[1] v[2]
Vector Register
vstore: v[0] v[1] v[2]
Vector Register
v[1]
v[0]
v[2]
Vector Register
Dataflow
Control-flow

## Slide 14: Vector execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector |  |  | 
Vector-
Dataflow
Example Program
vload:
vmul:
vadd:
vstore: v[0] v[1] v[2]
Vector Register
v[1]
v[0]
v[2]
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
Vector Register
Dataflow
Control-flow

## Slide 15: Vector execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector |  |  | 
Vector-
Dataflow
Example Program
Read and write to VRF
vload: | v[0] | v[1] | v[2]
 |  | Vector Register | 
vmul: | v[0] | v[1] | v[2]
 |  | Vector Register | 
vadd: | v[0] | v[1] Vector Register | v[2]
vstore: | v[0] | v[1] | v[2]
Dataflow
Control-flow

## Slide 16: Vector pays huge energy cost for VRF writes
Memory | DCache access | ICache access | Compute + Control
Vector
Memory | DCache access | ICache | Compute + Control | Vector register file

## Slide 17: MANIC’s Vector-dataflow execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Vector
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector- Dataflow |  |  | 
Example Program
Vector Register
vload:
v[0]
vmul: v[0]
vadd: v[0]
vstore: v[0]
V
v[1] v[2]
v[1] v[2]
v[1] v[2]
v[1] v[2]
ector Register
Dataflow
Control-flow

## Slide 18: MANIC’s Vector-dataflow execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Vector
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector- Dataflow |  |  | 
Example Program
Vector Register
vload:
vmul:
v[0]
vadd: v[0]
vstore: v[0]
V
v[1] v[2]
v[1] v[2]
v[1] v[2]
v[1] v[2]
ector Register
v[0]
Dataflow
Control-flow

## Slide 19: MANIC’s Vector-dataflow execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Vector
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector- Dataflow |  |  | 
Example Program
Vector Register
vload:
vmul:
vadd:
v[0]
v[0]
vstore: v[0]
V
v[1] v[2]
v[1] v[2]
v[1] v[2]
v[1] v[2]
ector Register
v[0]
Dataflow
Control-flow

## Slide 20: MANIC’s Vector-dataflow execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Vector
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector- Dataflow |  |  | 
Example Program
Vector Register
V
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[1] v[2]
v[1] v[2]
v[1] v[2]
v[1] v[2]
ector Register
v[0]
v[0]
Dataflow
Control-flow

## Slide 21: MANIC’s Vector-dataflow execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Vector
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector- Dataflow |  |  | 
Example Program
Vector Register
Vector Register
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[1]
v[1]
v[1]
v[2]
v[2]
v[2]
v[2]
v[0]
v[0]
v[1]
Dataflow
Control-flow

## Slide 22: MANIC’s Vector-dataflow execution
vload v0, &a vmul v1, v0, v0 vadd v2, v1, v0 vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Scalar
Vector
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Vector- Dataflow |  |  | 
Example Program
Vector Register
Vector Register
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[0]
v[0]
v[1]
v[1]
v[1]
v[1]
v[2]
v[2]
v[2]
v[2]
Dataflow
Forwarding
Dataflow
Control-flow

## Slide 23: Vector-dataflow reduces energy without costing programmability
Memory | DCache access | ICache access | Compute + Control
Vector-dataflow execution
  Vector execution reduces instructions fetched
  Dataflow execution eliminates VRF reads
Software support to eliminate VRF writes
Vector
Memory | DCache access | ICache | Compute + Control | Vector register file
Memory | DCache access | ICache | Compute + Control | 
Dataflow
Vector register file

## Slide 24: MANIC is an energy-minimal computer architecture implementing vector-dataflow
RISC-V
Scalar Core
2KB
I$
4KB D$
I2C
4KB VRF
Boot ROM
64KB SRAM
256KB MRAM
Main Memory
MANIC
Arbiter
Arbiter
GPIO
IO Bus
Block diagram
Implementation Characteristics
Complete standalone system
Scalar, Vector & MANIC designs
Intel 22nm bulk FinFet (HVT)
Embedded MRAM
SRAM, logic, MRAM power isolated

## Slide 25: Evaluating MANIC’s efficiency in a silicon prototype
Intel 22nm FinFET 8 metal layers, MANIC +
Vector + Scalar, 256kB MRAM + 64kB SRAM
Evaluation Goals: Energy characterization
of first ever vector-dataflow chip.
MANIC
MRAM
MRAM
Core Logic
$ + VRF
SRAM
Operational Characteristics:
Frequency: 4-50MHz Voltage: 0.4-1.0V
Power: 19.1uW Efficiency: 256 GOPS/W
Key Result: Power low & efficiency high enough to run on tiny solar panel indoors

## Slide 26: More Pretty Chip Micrographs Courtesy CMU’s Nanofabrication Laboratory & their electron microscope
MANIC
Scalar |  | 
Caches |  | 
SRAM |  | 
 | MANIC | 
MRAM |  | 

## Slide 27: Can we do even better? Let’s eliminate all instruction control & caching costs!
Memory | DCache access | ICache access | Compute + Control
Vector
Memory | DCache access | ICache | Compute + Control | Vector register file
Dataflow
Memory | DCache access | ICache | Compute + Control | 
Memory
Coarse-grained Reconfigurable Array Architectures
Compute
Key idea: architecture eliminates instruction & control overheads

## Slide 28: CGRA Overview
Processing elements (PE) connected by Network-on-Chip (NoC)
  Heterogenous PE capability
  Connections configured by software compiler
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
M M M M
r
r
r
r

## Slide 29: CGRA Overview
Collection of processing elements (PE) connected via NoC
  Configure PE once, use many times: no instruction fetch/control costs
  Data move directly PE to PE: no RF/VRF/Cache costs
  Stream data through fabric: Reduced memory costs
dot_product():
vload v0, &a
vload v1, &b
vmul v2, v0, v1
vredsum v3, v2
vstore &c, v3
Vector assembly
Extract
3
4
5
1 2
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r r r r r
M M M M
r r r r r
S C B
r r r r
S B
r r r
S
r r
1 2 5
3 4
Schedule
Nearly all energy for actually useful computation!

## Slide 30: RipTide CGRA
T
C
>
+
CF
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
CF
R
R
R
R
St
R
R
R
R
A
R
R
R
R
A
R
R
R
R
St
R
R
R
R
M
R
R
R
R
M
R
R
R
R
A
R
R
R
R
A
R
R
R
R
A
R
R
R
R
A
R
R
R
R
CF
R
R
R
R
CF
R
R
R
R
A
R
R
R
R
A
R
R
R
R
A
R
R
R
R
A
R
R
R
R
M
R
R
R
R
M
R
R
R
R
St
R
R
R
R
A
R
R
R
R
A
R
R
R
R
St
R
R
R
R
CF
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
R
R
R
R
M CF
R
R
R
R
RISC-V
Scalar Core
CGRA
Control
CGRA
Configurator
Memory
Memory
Memory
Memory
M
M
St
CF
A
Memory
Multiplier
Stream
Arithmetic Control-flow
CF-modules

## Slide 31: CGRAs provide efficiency & programmability Dataflow compiler support avoids the need for programmer acrobatics
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R R R R
R R R R
R R R R
R R R R
T
C
>
+
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) { z[j] = 0;
}
z[j] += b[j];
}
}
}
Dataflow
Compiler
Optimized Dataflow Graph
C code
RipTide CGRA
R
R

## Slide 32: Dataflow Architecture

## Slide 33: Dataflow Architecture: Dataflow Program Graphs
Conditional operations represented as dataflow
if( x > 3 ){ x += 2 }
else{ x -= 1 }
y = x * 4
Loop represented as dataflow
while( x
x -= 3
}
> 0 ){
Initial value

## Slide 34: Dataflow: “Activity Template” implementation

## Slide 35: Dataflow: Processing Element & Interconnect Arch.
Processing Element Architecture
Processing Element Interconnection Architecture
Question: what do we need to specify
in this ISA?

## Slide 36: Dataflow: MIT Dataflow Architecture
What is the main difference in this architecture versus the
“basic” architecture on the previous slide?

## Slide 37: Dataflow: The Riptide Ordered Dataflow Machine

## Slide 38: Dataflow: The Riptide ISA
What program constructs do the carry and
invariant ISA ops support?
What does the order ISA op do?
What program construct(s) does the
stream ISA op support?

## Slide 39: Background: What is a Dataflow Machine?

## Slide 40: Dataflow ISA matches CGRA Architecture Dataflow compiler efficiently targets reconfigurable dataflow architecture!
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R R R R
R R R R
R R R R
R R R R
T
C
>
+
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) { z[j] = 0;
}
z[j] += b[j];
}
}
}
Dataflow
Compiler
Optimized Dataflow Graph
C code
RipTide CGRA
R
R

## Slide 41: Intermediate representation for dataflow compilation

## Slide 42: Steering Sends Values Only Where They Are Needed
Steering instead of predication Avoids evaluating both sides of branch like predication does

## Slide 43: Control-flow Operators Handle Loop-Carried Dependences
Generate fresh value tokens for loop carried dependences and loop-invariant values

## Slide 44: Memory Ordering Gates Maintain Memory Consistency
Enforce logical time ordering of concurrent memory operations

## Slide 45: Memory Ordering Reduction Analysis
Existing memory ordering analyses rely on transitive reduction of ordering graph
Dataflow ordering reduction requires path sensitivity or cuts required orders.

## Slide 46: Stream Gates Optimize Patterned Address Computation
Generate new address value token every cycle according to affine(-ish) function established in program

## Slide 47: End-to-end compilation flow

## Slide 48: Energy-Minimal Network-on-Chip Tricks: No Buffers & Control-Flow in NoC
Multi-hop, bufferless NoC
Buffer on every link Buffers @ producer
Control-flow in the NoC
Control-flow operations are numerous, but simple
 Wasteful to assign to PEs
C
r
B
M
r
Allows broadcast to multiple consumers w/out duplication
S
S
S
S
r
r
r
r
B
r
r
r
r
S
r
r
r
S
r
r
r
r
r
r
r
r
C B
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
M M M M
r
r
r
r
r
Duplicates data in
multiple buffers
v.
Switch
Router
Switch
Switch
Router
CF-Modules

## Slide 49: Riptide vs. COTS Extreme Edge MCUs
Energy savings Speedup

## Slide 50: Evaluating compute options for the extreme edge
HMB010 BLE
System overview:

## Slide 51: Evaluating compute options for the extreme edge
HMB010 Scalar BLE
System overview:

## Slide 52: Evaluating compute options for the extreme edge
HMB010 Riptide BLE
System overview:

## Slide 53: Evaluating compute options for the extreme edge
HMB010 ASIC BLE
System overview:

## Slide 54: That was “Ordered Dataflow”
Axiom: Tokens proceed through the graph in the order of their generation
How do we ensure that tokens flow through the dataflow graph in order?

## Slide 55: What about allowing token reordering?
“Tagged-token dataflow architectures”
Two issues: Latency & Synchronization
Latency: time between when operation is issued and when completes
Synchronization: need to assure data properly written before read
ld
Memory
t=0
t=?
(Memory) Latency: when can I
expect my value to come back?
Synchronization: which
value should I use?

## Slide 57: Tagged-token Dataflow Architecture
Token matching: synchronization of out-of-order inputs, using i-struc5t9s
I-structures: latency-tolerant memory
I-fetch send rd tok w/ addr+continuation
P: read & run; A/W: queue
I-store: send wr tok to populate table
A/W are non-blocking (why?)
I-allocate: make storage for fetch/stores

## Slide 58: Parallelism is a resource congestion problem
I structure
Synchronization: which value should I use? Many options accumulating over time

## Slide 59: Varieties of Dataflow Execution

## Slide 60: Varieties of Dataflow Execution