## Slide 1
Fall 2023
Lecture 5: Pipelines and Hazards
Credit: Brandon Lucia

## Slide 2: Pipelined Microarchitectural Implementation
Pipelining for Instruction-Level Parallelism (ILP)
Pipelined microarchitecture design sketch
Control hazards
Branch prediction for dealing with control hazards

## Slide 3: Pipelining in the abstract: A laundry efficiency problem
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project

## Slide 4: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed
Private Laundry Room Model: only one
person at a time allowed in laundry room

## Slide 5: Pipelining in the abstract: A laundry efficiency problem
To be washed
Time = 0
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 6: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 7: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 8: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 9: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 10: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 11: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 12: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 13: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 14: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 15: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 16: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 17: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed
Time = 12

## Slide 18: Pipelining in the abstract: A laundry efficiency problem
To be washed
Done being washed
Analysis: With 3 resources ( ,
, ) and 3 units of
work ( , , ) our laundry took 12 units of time
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project

## Slide 19: Pipelining in the abstract: A laundry efficiency problem
To be washed
Done being washed
Analysis: With 3 resources ( ,
, ) and 3 units of
work ( , , ) our laundry took 12 units of time
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
12 units of time?
Why 12 units of time vs 9 units of time overall?
Why 4 units of time per load vs 3 units of time?
                Processors and their workings are triggered devices.
                It takes 4 triggers for the dirty laundry pile to be washed, dried, folded, and available.

## Slide 20: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed
Let’s redesign our laundry room to make it more efficient

## Slide 21: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed
Shared Laundry Room: single laundry task uses single machine at a time, not entire room. Multiple roommates allowed in at once.

## Slide 22: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 23: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 24: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 25: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed

## Slide 26: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed
Time = 5

## Slide 27: Pipelining in the abstract: A laundry efficiency problem
To be washed
Done being washed
Analysis: With 3 resources ( ,
, ) and 3 units of
work ( , , ) our laundry took 6 units of time
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project

## Slide 28: Pipelining in the abstract: A laundry efficiency problem
Vs.
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
General observations about private laundry room model vs. shared laundry room model?

## Slide 29: Pipelining in the abstract: A laundry efficiency problem
Vs.
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
General observations about private laundry room model vs. shared laundry room model?
Using machines in parallel in the shared laundry model
At time step 3 (“steady state”) all machines are active
Private model: always leaving 2/3 of laundry machines idle, despite laundry yet to wash!

## Slide 30: Pipelining in the abstract: A laundry efficiency problem
To be washed
Art attribution: Andrejs Kirma from the Noun ProjectKoson Rattanaphan from the Noun Project, Symbolon from the Noun Project
Done being washed
Shared Laundry Room: single laundry task uses single machine at a time, not entire room. Multiple roommates allowed in at once.
30min
60min
15min
Improving Pipeline Performance
If you could make washing take only 15 minutes what would be the impact upon throughput?
What if you could make ironing take only 10 minutes?
What if you could make drying take 45 minutes? Why is that different?
Hint: What (stage) limits the throughput? Why?

## Slide 31: Let’s do some grouping together of functionality
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
Branch: PC Source Select
Data
Memory

## Slide 32: Let’s do some grouping together of functionality
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
Branch: PC Source Select
Data
Memory

## Slide 33: Let’s do some grouping together of functionality
ALU
Input Read Reg A
ALU: output C data Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read Register A & B Select
Input Read Reg B
+
Instruction PC+4 Branch Target
Branch Target
Branch Target Offset
Instruction PC + 4
Branch Target
AAddddrr Reg A
Data Reg B
(Ld Only)
RReeaadd DDaattaa CC
Read Data C (Ld Only)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Read Regs A & B Data
Write Register C Select Write Register C Data
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select [Ld/St]

## Slide 34: A Simple 5-Stage Pipelined Processor Datapath
ALU
Input Read Reg A
ALU: output C data Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read Register A & B Select
Input Read Reg B
+
Instruction PC+4 Branch Target
Branch Target
Branch Target Offset
Instruction PC + 4
Branch Target
AAddddrr Reg A
Data Reg B
(Ld Only)
RReeaadd DDaattaa CC
Read Data C (Ld Only)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Read Regs A & B Data
Write Register C Select Write Register C Data
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select [Ld/St]
Instruction Fetch
Instr. Decode
Execute
Memory
Register Write-Back

## Slide 35: What about an alternative decomposition?
ALU
Input Read Reg A
ALU: output C data Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read Register A & B Select
Input Read Reg B
+
Instruction PC+4 Branch Target
Branch Target
Branch Target Offset
Instruction PC + 4
Branch Target
AAddddrr Reg A
Data Reg B
(Ld Only)
RReeaadd DDaattaa CC
Read Data C (Ld Only)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Read Regs A & B Data
Write Register C Select Write Register C Data
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select [Ld/St]
Instruction Fetch
Instr. Decode
Execute
Memory
Register Write-Back

## Slide 36: 4-stage? Pro / con?
ALU
Input Read Reg A
ALU: output C data Branch: PC Source Select
Instruction Memory
ode
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read Register A & B Select
Input Read Reg B
+
Instruction PC+4 Branch Target
PC Source Select (1 if branch taken)
Branch Target
Branch Target Offset
Instruction PC + 4
Branch Target
AAddddrr Reg A
Data Reg B
(Ld Only)
RReeaadd DDaattaa CC
Read Data C (Ld Only)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Read Regs A & B Data
Write Register C Select Write Register C Data
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select [Ld/St]
Instruction Fetch and Decode
Execute
Memory
Register Write-Back

## Slide 37: What does ALU op do in Mem? Memop in EX?
ALU
Input Read Reg A
ALU: output C data Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read Register A & B Select
Input Read Reg B
+
Instruction PC+4 Branch Target
Branch Target
Branch Target Offset
Instruction PC + 4
Branch Target
AAddddrr Reg A
Data Reg B
(Ld Only)
RReeaadd DDaattaa CC
Read Data C (Ld Only)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Read Regs A & B Data
Write Register C Select Write Register C Data
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select [Ld/St]
Instruction Fetch
Instr. Decode
Execute
Memory
Register Write-Back

## Slide 38: Cost of pipelining:
Need to register state between pipeline stages
ALU
Input Read Reg A
ALU: output C data Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read
Registe
A & B Select
Input Read Reg B
Branch Target Offset
+
Instruction PC+4 Branch Target
PC Source Select (1 if branch taken)
Branch Target
I
P
r
O
o
nstruction C + 4
Branch Target
AAddddrr Reg A
Data Reg B
(Ld Only)
RReeaadd DDaattaa CC
Read Data C (Ld Only)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
[Ld/St]
Instruction Fetch
Instr. Decode
Execute
Memory
Register Write-Back
IF/
ID
ID/
EX
Cont. Sigs.: Op.
EX/ Select
Mem
Mem
/WB Write Reg C Data
Read Regs A & B Data
Write Register C Select Write Register C Data
Write Reg C Data

## Slide 39: Cost of pipelining:
Need to register state between pipeline stages
ALU
Input Read Reg A
ALU: output C data Branch: PC Source Select
Instruction Memory
Instruction Fetch
Read Regs A & B Da
ta
Control Signals:
p select
p = [+, -, x, /]
Memory
Unit
Data
Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read
Registe
A & B Select
Input Read Reg B
Branch Target Offset
+
Instruction PC+4 Branch Target
PC Source Select (1 if branch taken)
Branch Target
I
P
r
O
o
nstruction C + 4
Branch Target
AAddddrr Reg A
Data Reg B
(Ld Only)
RReeaadd DDaattaa CC
Read Data C (Ld Only)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Select
[Ld/St]
Instruction Fetch
Instr. Decode Execute
Memory
Register Write-Back
IF/
ID
ID/
EX
Cont. Sigs.: Op.
EX/ Select
Mem
Mem
/WB Write Reg C Data
Pipeline Registers
Write Register C Select
Write Register C Data
Write Reg C Data

## Slide 40: Need to store state between pipeline stages
4
Memory
Unit
Input
Instruction Read
Fetch Reg A Data
Memory
Control Signals:
select ALU
Instruction = [+, -, x, /]
Memory ALU: output C data
Branch: PC Source Select
Read Regs A & B Data
+
PC Source Select (1 if branch taken)
PC
Branch
Target
Instruction PC+4 Branch Target
I
P
r
O
o
AAddddrr
Data
Read Data C (Ld Only)
Output/Read
Output/Read
Offset Branch Target RReegg AA Reg B Reg C Data Reg Select
Branch Control nstruction + (Ld Only)
Target Signals C + 4
MUX PC Source Cont. Register
Sigs.:
Select Read Op. RReeaadd Writeback
IF/ Registe ID/ Input EX/ Select DaDattaa CC
A & B Read [Ld/St] Mem
ID Select EX Reg B Mem /WB Write Write
Reg C Reg C
Data Select
Reg 1 p
Reg 2 p
Reg 3
Reg 4
Instruction Fetch Instr. Decode Execute Memory Register Write-Back
Write Register C Select Write Register C Data
Write Reg C Data
What do we need to preserve in these pipeline registers?

## Slide 41: Need to store state between pipeline stages
4
Memory
Unit
Input
Instruction Read
Fetch Reg A Data
Memory
Control Signals:
select ALU
Instruction = [+, -, x, /]
Memory ALU: output C data
Branch: PC Source Select
Read Regs A & B Data
+
PC Source Select (1 if branch taken)
PC
Branch
Target
Instruction PC+4 Branch Target
I
P
r
O
o
AAddddrr
Data
Read Data C (Ld Only)
Output/Read
Output/Read
Offset Branch Target RReegg AA Reg B Reg C Data Reg Select
Branch Control nstruction + (Ld Only)
Target Signals C + 4
MUX PC Source Cont. Register
Sigs.:
Select Read Op. RReeaadd Writeback
IF/ Registe ID/ Input EX/ Select DaDattaa CC
A & B Read [Ld/St] Mem
ID Select EX Reg B Mem /WB Write Write
Reg C Reg C
Data Select
Reg 1 p
Reg 2 p
Reg 3
Reg 4
Instruction Fetch Instr. Decode Execute Memory Register Write-Back
Write Register C Select Write Register C Data
Write Reg C Data
What do we need to preserve in these pipeline registers?
For Example -- Store instruction: IF/ID:

## Slide 42: Need to store state between pipeline stages
4
Memory
Unit
Input
Instruction Read
Fetch Reg A Data
Memory
Control Signals:
select ALU
Instruction = [+, -, x, /]
Memory ALU: output C data
Branch: PC Source Select
Read Regs A & B Data
+
PC Source Select (1 if branch taken)
PC
Branch
Target
Instruction PC+4 Branch Target
I
P
r
O
o
AAddddrr
Data
Read Data C (Ld Only)
Output/Read
Output/Read
Offset Branch Target RReegg AA Reg B Reg C Data Reg Select
Branch Control nstruction + (Ld Only)
Target Signals C + 4
MUX PC Source Cont. Register
Sigs.:
Select Read Op. RReeaadd Writeback
IF/ Registe ID/ Input EX/ Select DaDattaa CC
A & B Read [Ld/St] Mem
ID Select EX Reg B Mem /WB Write Write
Reg C Reg C
Data Select
Reg 1 p
Reg 2 p
Reg 3
Reg 4
Instruction Fetch Instr. Decode Execute Memory Register Write-Back
Write Register C Select Write Register C Data
Write Reg C Data
What do we need to preserve in these pipeline registers?
For Example -- Store instruction: IF/ID: 32-bit instruction + 32-bit PC+4 result
ID/EX:

## Slide 43: Need to store state between pipeline stages
4
Memory
Unit
Input
Instruction Read
Fetch Reg A Data
Memory
Control Signals:
select ALU
Instruction = [+, -, x, /]
Memory ALU: output C data
Branch: PC Source Select
Read Regs A & B Data
+
PC Source Select (1 if branch taken)
PC
Branch
Target
Instruction PC+4 Branch Target
I
P
r
O
o
AAddddrr
Data
Read Data C (Ld Only)
Output/Read
Output/Read
Offset Branch Target RReegg AA Reg B Reg C Data Reg Select
Branch Control nstruction + (Ld Only)
Target Signals C + 4
MUX PC Source Cont. Register
Sigs.:
Select Read Op. RReeaadd Writeback
IF/ Registe ID/ Input EX/ Select DaDattaa CC
A & B Read [Ld/St] Mem
ID Select EX Reg B Mem /WB Write Write
Reg C Reg C
Data Select
Reg 1 p
Reg 2 p
Reg 3
Reg 4
Instruction Fetch Instr. Decode Execute Memory Register Write-Back
Write Register C Select Write Register C Data
Write Reg C Data
What do we need to preserve in these pipeline registers?
For Example -- Store instruction: IF/ID: 32-bit instruction + 32-bit PC+4 result
ID/EX: address parts (base/offset) & value to store Ex/Mem:

## Slide 44: Need to store state between pipeline stages
4
Memory
Unit
Input
Instruction Read
Fetch Reg A Data
Memory
Control Signals:
select ALU
Instruction = [+, -, x, /]
Memory ALU: output C data
Branch: PC Source Select
Read Regs A & B Data
+
PC Source Select (1 if branch taken)
PC
Branch
Target
Instruction PC+4 Branch Target
I
P
r
O
o
AAddddrr
Data
Read Data C (Ld Only)
Output/Read
Output/Read
Offset Branch Target RReegg AA Reg B Reg C Data Reg Select
Branch Control nstruction + (Ld Only)
Target Signals C + 4
MUX PC Source Cont. Register
Sigs.:
Select Read Op. RReeaadd Writeback
IF/ Registe ID/ Input EX/ Select DaDattaa CC
A & B Read [Ld/St] Mem
ID Select EX Reg B Mem /WB Write Write
Reg C Reg C
Data Select
Reg 1 p
Reg 2 p
Reg 3
Reg 4
Instruction Fetch Instr. Decode Execute Memory Register Write-Back
Write Register C Select Write Register C Data
Write Reg C Data
What do we need to preserve in these pipeline registers?
For Example -- Store instruction: IF/ID: 32-bit instruction + 32-bit PC+4 result
ID/EX: address parts (base/offset) & value to store Ex/Mem: computed addr & value to store Mem/WB:

## Slide 45: Need to store state between pipeline stages
4
Memory
Unit
Input
Instruction Read
Fetch Reg A Data
Memory
Control Signals:
select ALU
Instruction = [+, -, x, /]
Memory ALU: output C data
Branch: PC Source Select
Read Regs A & B Data
+
PC Source Select (1 if branch taken)
PC
Branch
Target
Instruction PC+4 Branch Target
I
P
r
O
o
AAddddrr
Data
Read Data C (Ld Only)
Output/Read
Output/Read
Offset Branch Target RReegg AA Reg B Reg C Data Reg Select
Branch Control nstruction + (Ld Only)
Target Signals C + 4
MUX PC Source Cont. Register
Sigs.:
Select Read Op. RReeaadd Writeback
IF/ Registe ID/ Input EX/ Select DaDattaa CC
A & B Read [Ld/St] Mem
ID Select EX Reg B Mem /WB Write Write
Reg C Reg C
Data Select
Reg 1 p
Reg 2 p
Reg 3
Reg 4
Instruction Fetch Instr. Decode Execute Memory Register Write-Back
Write Register C Select Write Register C Data
Write Reg C Data
What do we need to preserve in these pipeline registers?
For Example -- Store instruction: IF/ID: 32-bit instruction + 32-bit PC+4 result
ID/EX: address parts (base/offset) & value to store Ex/Mem: computed addr & value to store Mem/WB: nothing

## Slide 46: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
add x7 x8 x9

## Slide 47: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
add x7 x8 x9
lw x12 (x15)

## Slide 48: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
sw x0 (x13)

## Slide 49: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
sub x6 x5 x4 sw x0 (x13)

## Slide 50: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
sub x6 x5 x4 sw x0 (x13)
sw x6 (x14)

## Slide 51: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
sub x6 x5 x4 sw x0 (x13)
sw x6 (x14)

## Slide 52: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
sub x6 x5 x4 sw x0 (x13)
sw x6 (x14)
Key Idea:Pipelining unlocks
Instruction Level Parallelism (ILP)
one of the great ideas in computer architecture
Practical Implications of adding ILP to the system?

## Slide 53: Pipeline Diagram Illustrates Parallelism
sub x6 x5 x4
sw x6 (x14)
sw x0 (x13)
lw x12 (x15)
IF
ID
EX/AG
ID
IF
Mem
EX/AG
ID
IF
WB
Mem
EX/AG
ID
IF
IF
WB
Mem
EX/AG
ID
WB
Mem
EX/AG
WB
Time (Cycles)
1
2
3
4
5
6
7
8
add x31 x30 x29
Mem
WB

## Slide 54: Pipeline Diagram Illustrates Parallelism
sub x6 x5 x4
sw x6 (x14)
sw x0 (x13)
lw x12 (x15)
IF
ID
EX/AG
ID
IF
Mem
EX/AG
ID
IF
IF
WB
Mem
EX/AG
ID
WB
Mem
EX/AG
WB
Time (Cycles)
1
2
3
4
6
7
 | 5
 | WB
Me | m
EX | /AG
 | ID
 | IF
8
Parallelism Factor = 5!
Question:
What is this machine’s rate
of Instructions per Cycle?
add x31 x30 x29
Mem
WB

## Slide 55: Pipeline Diagram Illustrates Parallelism
sub x6 x5 x4
sw x6 (x14)
sw x0 (x13)
IF
ID
EX/AG
ID
IF
Mem
EX/AG
ID
IF
IF
WB
Mem
EX/AG
ID
WB
Mem
EX/AG
Time
1
2
3
4
6
7
 | 5
 | WB
Me | m
EX | /AG
 | ID
 | IF
8
Pipeline Drain
Parallelism Factor = 5!
Question:
What is this machine’s rate
of Instructions per Cycle?
lw x12 (x15)
WB
x29Pipeline Fill
add x31 x30
Mem
WB

## Slide 56: Pipeline Diagram: Single Cycle Design
sub x6 x5 x4
sw x6 (x14)
sw x0 (x13)
lw x12 (x15)
IF
ID
EX/AG
Mem
WB
Clock Cycle
1
IF | ID | EX/AG | Mem | WB
IF | ID | EX
2
3
Parallelism Factor = 1
Question:
What is this machine’s rate
of Instructions per Cycle?

## Slide 57
IF
ID
EX/AG
Mem
WB
IF
ID
EX/AG
Mem
WB
IF
ID
EX/AG
Mem
WB
IF
ID
EX/AG
Mem
WB
IF | ID | EX/AG | Mem | WB
IF | ID | EX/AG | Mem | WB
What gives? IPC is 1 for both and each
instruction’s latency is still 5ns.
5ns
5ns
IF
ID
EX/AG
Mem
WB

## Slide 58
IF
ID
EX/AG
Mem
WB
IF
ID
EX/AG
Mem
WB
IF
ID
EX/AG
Mem
WB
IF
ID
EX/AG
Mem
WB
IF | ID | EX/AG | Mem | WB
IF | ID | EX/AG | Mem | WB
5ns
5ns
IF
ID
EX/AG
Mem
WB
What gives? IPC is 1 in both cases!
Key Idea: Pipelined Instruction Throughput is higher.
Shorter clock period + parallelism = 1 completed instruction per ns even though each instruction takes 5ns to complete
Instructions/Cycle
Vs
Instructions/Second
5ns = (up to) 25(*) stages of work
vs
5ns = 5 stages of work
* 15 here due to pipeline filling

## Slide 59: Iron Law of Computer Performance
instructions
/ program
cycles /
instruction
seconds
/ cycle
X
X

## Slide 60: Iron Law of Computer Performance
instructions
/ program
cycles /
instruction
seconds
/ cycle
X
X
Question: what term does pipelining optimize? how else might we approach optimization in light of this performance expression?

## Slide 61: Pipelining Code Example
p = 0xabc; x = y – z m = *p;
t = x + w;
What is interesting about this short program?
sub x6 x5 x4 lw x16 0xabc add x12 x6 x14

## Slide 62: Pipelining Code Example
sub x6 x5 x4 lw x16 0xabc add x12 x6 x14
What happens to x6 as we execute this code?

## Slide 63: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4

## Slide 64: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
lw x16 0xabc sub x6 x5 x4

## Slide 65: Example: Pipelined Execution
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14 reads the value of x6 sub x6 x5 x4
add x12 x6 x14 lw x16 0xabc
from
Read-After-Write (RAW) Hazard:
Input register does not contain updated data during register read cycle due to yet-to-be-completed register writeback from older instruction
x6 gets written back here 2 cycles later!

## Slide 66: Types of Data Hazards
sub x6 x5 x4 lw x16 0xabc
Read-After-Write (RAW) Write-After-Read (WAR)
sub x8 x16 x4
add x12 x6 x14 lw
x16 0xabc
Write-After-Write (WAW)
Only Read-After-Write (RAW) hazards are possible in our simple pipeline
lw x6 0xabc
add x16 x6 x14 sub x6 x5 x4
add x12 x6 x14

## Slide 67: lw x6 0xabc sub x6 x5 x4 add x12 x6 x14
Types of Data Hazards
Write-After-Write (WAW)
Fetch
Decode
Execute
Memory
Register Write-Back
Memory
Memory
lw x6 0xabc

## Slide 68: lw x6 0xabc sub x6 x5 x4 add x12 x6 x14
Types of Data Hazards
Write-After-Write (WAW)
Fetch
Decode
Execute
Memory
Register Write-Back
Memory
Memory
lw x6 0xabc
sub x6 x5 x4

## Slide 69: lw x6 0xabc sub x6 x5 x4 add x12 x6 x14
Types of Data Hazards
Write-After-Write (WAW)
Fetch
Decode
Execute
Memory
Register Write-Back
Memory
Memory
lw x6 0xabc
sub x6 x5 x4

## Slide 70: lw x6 0xabc sub x6 x5 x4 add x12 x6 x14
Types of Data Hazards
Write-After-Write (WAW)
lw x6 0xabc
Fetch
Decode
Execute
Memory
Register Write-Back
Memory
Memory
sub x6 x5 x4

## Slide 71: lw x6 0xabc sub x6 x5 x4 add x12 x6 x14
Types of Data Hazards
Write-After-Write (WAW)
lw x6 0xabc
Fetch
Decode
Execute
Memory
Register Write-Back
Memory
Memory
sub x6 x5 x4

## Slide 72: lw x6 0xabc sub x6 x5 x4 add x12 x6 x14
Types of Data Hazards
Write-After-Write (WAW)
Multi-cycle latency memory op
lw x6 0xabc lw x6 0xabc lw x6 0xabc
Fetch
Decode
Execute
Memory
Register Write-Back
Memory
Memory
sub x6 x5 x4 sub x6 x5 x4
Non-mem-op, single memory cycle
Earlier lw instruction finishes after later sub instruction. Both write x6. Wrong final value in x6. Explicitly handled with logic to maintain ordering in processors that allow this behavior (not our datapath)

## Slide 73: sub x8 x16 x4 add x16 x6 x14 lw x11 0xabc
Types of Data Hazards
Write-After-Read (WAR)
Fetch
Decode
Execute
Memory
Register Write-Back
Stalled at decode/reg. read
(why? wait a few lectures & more in 447)
sub x8 x16 x4
add x16 x6 x14
Completes quickly and writes reg.
Later add instruction writes x16 before earlier
sub instruction reads x16. sub sees wrong value!

## Slide 74: What can we do about these data hazards?
sub x6 x5 x4 lw x16 0xabc
Read-After-Write (RAW) Write-After-Read (WAR)
sub x8 x16 x4
add x12 x6 x14 lw
x16 0xabc
Write-After-Write (WAW)
Only Read-After-Write (RAW) hazards are possible in our simple pipeline
lw x6 0xabc
add x16 x6 x14 sub x6 x5 x4
add x12 x6 x14

## Slide 75: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14 reads the value of x6 sub x6 x5 x4
add x12 x6 x14 lw x16 0xabc
from
Read-After-Write (RAW) Hazard:
Input register does not contain updated data during register read cycle due to yet-to-be-completed register writeback from older instruction
x6 gets written back here 2 cycles later!

## Slide 76: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14

## Slide 77: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
add x12 x6 x14 sub x6 x5 x4

## Slide 78: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14
stall

## Slide 79: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14
stall
stall

## Slide 80: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
add x12 x6 x14
stall
stall

## Slide 81: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
stall
add x12 x6 x14

## Slide 82: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
add x12 x6 x14

## Slide 83: How do we avoid the stall cycles?
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14
stall
stall

## Slide 84: Example: Pipelined Execution w/ RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
sub x6 x5 x4
add x12 x6 x14
Value of x6 is available after sub Executes
We can forward the value to the add!

## Slide 85: Forwarding to avoid a pipeline RAW Hazard
Fetch
Decode
Execute
Memory
Register Write-Back
Value of x6 is available from Execute!
add x12 x6 x14 sub x6 x5 x4
“x6”
We can forward the value in the EX/MEM pipeline register from the sub back to Execute to act as the input operand for the add

## Slide 86: Forwarding to avoid a pipeline RAW Hazard
Fetch
Decode
Execute Memory
Register Write-Back
Can also forward if there are intervening instructions
add x12 x6 x14 add x9 x8 x7 sub x6 x5 x4
“x6”
We can forward the value in the MEM/WB pipeline register from the sub back to Execute to act as the input operand for the add (going around the unrelated operation in the memory stage)

## Slide 87: Pipeline Can Forward Between Different Stages
Fetch
Decode
Execute
Memory
Register Write-Back
lw x6 0xabc
add x12 x6 x14
lw x6 0xabc add x12 x6 x14
Value of x6 is available from Memory!
We can forward the value in Memory’s pipeline register
from the lw back to Execute’s input for the add
(Still requires stalling…)
stall

## Slide 88: Adding Forwarding Support
ALU
ALU: output C data Branch: PC Source Select
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data Memory
4
+
MUX
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control Signals
Read Register A & B Select
Input Read Reg B
Write Reg C Data
+
Instruction PC+4 Branch Target
PC Source Select (1 if branch taken)
Branch Target
Branch Target Offset
Instruction PC + 4
Read
Data C
Read Data C (Ld)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select
[Ld/St]
Instruction Fetch
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
Branch Target
Exec/Exec Forward
Mem/Exec Forward
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
Input Read Reg A
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B

## Slide 89: Question: What is time in a pipelined system?
Fetch
What if one of our instructions were to throw an
exception (e.g., illegal instruction in decode or page fault on a memop)?
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
sub x6 x5 x4 sw x0 (x13)
sw x6 (x14)

## Slide 90: Exception Handling
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
invalid ins
sw x6 (x14)
sw x0 (x13)
Exception!
What if one of our instructions were to throw an
exception (e.g., illegal instruction in decode or page fault on a memop)?

## Slide 91: Exception Handling
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
invalid ins
sw x6 (x14)
sw x0 (x13)
Basic Exception Idea: Nuke everything that started after the current instruction, finish everything that started before the current instruction, jump to exception handler
Exception!

## Slide 92: Exception Handling
Fetch
Decode
Execute
Memory
Register Write-Back
lw x12 (x15) add x7 x8 x9
BNE <ehreg>
sw x6 (x14)
sw x0 (x13)
Basic Exception Idea: Nuke everything that started after the current instruction, finish everything that started before the current instruction, jump to exception handler, no new insns
Exception!
Exception Handler
Exception Reason
stall

## Slide 93: What did we just learn?
Basics of pipelining as a first technique for Instruction-level parallelism
Datapath decomposition to support pipelined execution
Hazards and their impediment to pipelined execution
Forwarding in the pipeline to avoid stalling on data hazards

## Slide 94: What to think about next?
More microarchitectural concepts (next time)
  Control hazards & branch prediction
Caches as a microarchitectural optimization (next time)
  Implementation of cache hierarchies
  Cache design tradeoffs
Performance Evaluation (next next time)
  Design spaces, Pareto Frontiers, and design space exploration