## Slide 1
Fall 2025
Lecture 11: Design Space Exploration
Credit: Brandon Lucia

## Slide 2: Today: Design Space Exploration
Defining the design space of a hardware or software system
Pareto Frontiers and optimizing within a design space
Applied Performance Evaluation
  Finding the best performing design under constraints

## Slide 3: Defining a design space
A design space is a set of possible incarnations of a system
A design space is defined over a set of parameters
A point in the design space is a concrete system with a concrete value for each of the design space’s parameters
Design spaces exist to allow systematic exploration of a collection of possible designs, like architectures.

## Slide 4: Example: Branch Predictor Design Space
Branch Target Buffer
hash()
0x1a2100
BranchID
1a2ABC
1A210C
Branch Tag
Tag
Target
1A22EE
1A2112
1A2
Target: 0x1A210C
Branch History Table (BHT)
xor
0x100
Branch PC
10
00
00
11
16k Entries
. . .
10010110
Global History Table
Outcome: Taken
What are the parameters /
dimensions of this branch predictor’s design?

## Slide 5: Example: Branch Predictor Design Space
Branch Target Buffer
hash()
0x1a2100
BranchID
1a2ABC
1A210C
Branch Tag
Tag
Target
1A22EE
1A2112
1A2
Target: 0x1A210C
Branch History Table (BHT)
xor
0x100
Branch PC
10
00
00
11
16k Entries
. . .
10010110
Global History Table
Outcome: Taken
GHT size
BHT # entries GHT/PC hash func BHT entry size BranchID hash BTB # entries
BTB assoc

## Slide 6: These parameters are the dimensions of a design space vector
GHT size
BHT # entries GHT/PC hash func BHT entry size BranchID hash BTB # entries
BTB assoc
Sg Nb Hp Sb Hb Nt At

## Slide 7: Example: Branch Predictor Design Space
Branch Target Buffer
hash()
0x1a2100
BranchID
1a2ABC
1A210C
Branch Tag
Tag
Target
1A22EE
1A2112
1A2
Target: 0x1A210C
Branch History Table (BHT)
xor
0x100
Branch PC
10
00
00
11
16k Entries
. . .
10010110
Global History Table
Outcome: Taken
Sg Nb Hp Sb Hb Nt At
8
16k
xor()
2
hash()
4
1

## Slide 8: Example: Branch Predictor Design Space
Branch Target Buffer
hash()
0x1a2100
BranchID
1a2ABC
1A210C
Branch Tag
1A22EE
1A2112
1A2
Target: 0x1A210C
Branch History Table (BHT)
xor
0x100
Branch PC
10
00
00
11
1k Entries
. . .
1001011001000111
Global History Table
Outcome: Taken
Sg Nb Hp Sb Hb Nt At
16
1k
xor()
2
hash()
8
2
Tag
Target
Tag
Target

## Slide 9: Can find a good design by measuring points in the design space
Run Time (s)
7s
3s
8
16k xor() 2
hash()
4
1
16
1k xor() 2
hash() 8
2
Faster design!

## Slide 10: Can find a good design by measuring points in the design space
Run Time (s)
7s
3s
8
16k xor() 2
hash() 4
1
16
1k xor() 2
hash()
8
2
Faster design!
Run Energy (J)
2J
5J
8
16k xor()
hash()
4
1
16
1k xor() 2
hash() 8
2
Low2 er energy
Side Q: Why might this particular
design have lower energy?

## Slide 11: Is one of these better?
Run Time (s)
7s
3s
8
16k xor() 2
hash() 4
1
16
1k xor() 2
hash()
8
2
Faster design!
Run Energy (J)
2J
5J
8
16k xor()
hash()
4
1
16
1k xor() 2
hash() 8
2
Low2 er energy

## Slide 12: Plotting the design space: Geometric view of design dimensions
Sg Nb Hp Sb Hb Nt At
Sg
Nb
Nt
8
16k xor() 2
hash() 4
1
16
1k xor() 2
hash()
8
2

## Slide 13: Plotting the design space: Geometric view of design dimensions
Sg Nb Hp Sb Hb Nt At
Sg
Nb
Nt
8
16k xor() 2
hash() 4
1
16
1k xor() 2
hash()
8
2
Limited medium: too many dimensions to render visually Limited interpretability: what does position mean?
Can be helpful for clustering designs if non-obvious

## Slide 14: Plotting the design space: Geometric view of figures of merit
Time Energy
Time
Energy
8
16k xor() 2
hash() 4
1
16
1k xor() 2
hash() 8
2
Simple medium: can easily render multiple FoMs & designs Limited view of designs: points do not show design info Benefit: allows comparing designs in multiple dimensions
FoM = “Feature of Merit”, i.e. an attribute we care about.

## Slide 15: Plotting many designs to study a tradeoff
Time
Energy
8
16k xor() 2
hash() 4
1
16
1k xor() 2
hash()
8
2
What can we learn from this plot?

## Slide 16: Plotting many designs to study a tradeoff
Time
Energy
More energy,
same time
Time
Energy
More time,
same energy

## Slide 17: Which points in this plot are optimal?
Time
Energy
More energy,
same time
Time
Energy
More time,
same energy

## Slide 18: Pareto Optimality of Design Alternatives
Time
Energy
Vilfredo Pareto
Pareto Optimality:
A design is optimal if no change leads to improvement in one dimension without a loss in at least one other dimension

## Slide 19: Pareto Optimality of Design Alternatives
Time
Energy
Time
Energy
All other points offer a level of performance in one dimension which can be had, or more, at a lower cost in the other dimension.

## Slide 20: Design Consequence of Pareto Optimality
Never select designs other than at the frontier, at least without motivation outside of plot.
Any design anywhere other than at the frontier can achieve the same or better performance at a lower cost w.r.t. the plotted dimensions.
This level of energy efficiency can be had at a lower cost along the frontier
This point is strictly better, right?
Time
Energy

## Slide 21: Design Consequence of Pareto Optimality
Time
Energy
Time
Energy
How do we choose from between
these Pareto Optimal alternatives?

## Slide 22: Worthwhile Options Are Along the Pareto Frontier
Time
Need low energy (battery powered maybe?)
How do we choose from between these Pareto Optimal alternatives?
Need to decide what matters to you!
Want to strike a balance of performance and
energy consumption (not make anyone too mad)
Need high performance (for latency requirement)
Energy

## Slide 23: Design Space Exploration
Applied Performance Evaluation to find the best feasible system
  Define a system’s important design parameters
  Define a system’s figure(s) of merit
  Define a set of constraints on the feasibility of a binding of design parameters
  Choose a feasible parameter setting and measure its merit
  Iterate until satisfied:
    If this system is better than the last one, keep it. If worse, discard it.
    Choose a parameter and change it

## Slide 24: Design Space Exploration
Applied Performance Evaluation to find the best feasible system
  Define a system’s important design parameters
  Define a system’s figure(s) of merit
  Define a set of constraints on the feasibility of a binding of design parameters
  Choose a feasible parameter setting and measure its merit
  Iterate until satisfied:
    If this system is better than the last one, keep it. If worse, discard it.
    Choose a parameter and change it

## Slide 25: Constraining your design space
Branch Target Buffer
hash()
0x1a2100
BranchID
1a2ABC
1A210C
Branch Tag
Tag
Target
1A22EE
1A2112
1A2
Target: 0x1A210C
Branch History Table (BHT)
xor
0x100
Branch PC
10
00
00
11
16k Entries
. . .
10010110
Global History Table
Outcome: Taken
Physical design constraints Max BP power = 4mW
Max BTB associativity = 2
Max memory (BTB+BHT) = 20kB
Designs candidates are often described as needing to “Make PPA”:
Power
Performance
Area

## Slide 26: Design Space Exploration
Applied Performance Evaluation to find the best feasible system
  Define a system’s important design parameters
  Define a system’s figure(s) of merit
  Define a set of constraints on the feasibility of a binding of design parameters
  Choose a feasible parameter setting and measure its merit
  Iterate until satisfied:
    If this system is better than the last one, keep it. If worse, discard it.
    Choose a parameter and change it
    Random restarts to search different sub-spaces

## Slide 27: Systematically fill out your design space
Time
Energy
8
16k xor() 2
hash()
4
1
8
12k xor() 2
hash()
4
1
8
88kk xor() 22
hash() 4
1
8
4k xor() 2
hash() 4
1
Choose a dimension to start exploring Experiments to get time/energy (or other FoM) Change dimensions when way off frontier

## Slide 28: Systematically fill out your design space
Time
Energy
8
16k xor() 2
hash()
4
1
8
12k xor() 2
hash()
4
1
8
88kk xor() 22
hash() 4
1
8
4k xor() 2
hash() 4
1
As you start plotting different designs’ points, you will discover which dimensions matter to your space (What do we learn from these labeled points?)

## Slide 29: Example of Design Space Optimization The Q100 Database Acceleration Architecture
Cutting edge database query hardware accelerator
“GPU for SQL & Database operations”
Architecture built up of a collection of special computing tiles in hardware
Each tile runs a particular kind of database operation
Tiles connected by configurable wires that can be set up to make circuits to do a database query
(Includes one of the best design space
explorations I’ve encountered in a research paper)

## Slide 30: Design Space Constraints The Q100 Database Acceleration Architecture
Design space optimization problem statement:
Choose the right mixture of tiles to have the best performance and power without using too much area or limiting frequency

## Slide 31: Design Space Constraints The Q100 Database Acceleration Architecture
Design space optimization problem statement:
Choose the right mixture of tiles to have the best performance and power without using too much area or limiting frequency

## Slide 32: Design Space Constraints The Q100 Database Acceleration Architecture
Design space optimization problem statement:
Choose the right mixture of tiles to have the best performance and power without using too much area or limiting frequency

## Slide 33: Design Space Constraints The Q100 Database Acceleration Architecture
Design space optimization problem statement:
Choose the right mixture of tiles to have the best performance and power without using too much area or limiting frequency
Estimate area w.r.t. a reasonable baseline.
In the original work, they compared to a contemporary server processor, the Intel E5620 Xeon. The comparison included all of the connecting wires, buffers, etc.

## Slide 34: Design Space Constraints The Q100 Database Acceleration Architecture
Design space optimization problem statement:
Choose the right mixture of tiles to have the best performance and power without using too much area or limiting frequency

## Slide 35: Design Space Constraints The Q100 Database Acceleration Architecture
Design space optimization problem statement:
Choose the right mixture of tiles to have the best performance and power without using too much area or limiting frequency

## Slide 36: Design Space Constraints The Q100 Database Acceleration Architecture
Design space optimization problem statement:
Choose the right mixture of tiles to have the best performance and power without using too much area or limiting frequency

## Slide 37: Q100 Pareto Frontier
Pareto plot from a research paper on the Q100 Database accelerator by Wu et al, ASPLOS 2014
How did they select magenta points?
What other points might they have selected?
What is the value in seeing all these points?
“Pareto Design” as used in the paper means the design that maximizes (runtime) performance per watt.
Although there were designs with nominally better runtime, the goal of the paper was to select three options for further study. The two options with a nominally better runtime were only negligibly better but at a much higher cost in terms of energy, rendering them less interesting to the authors.

## Slide 38: Results of Design Space Exploration
Final results show idealized design and results that include adding in costs related to the on-chip network and memory access bandwidth

## Slide 39: Heat Plots Can Be Used to Explore 2D Space
Here heat plots are used to show the communication bandwidth needed between tiles and which design elements exceed a reference threshold.

## Slide 40: Q100 Takeaways / What did we just learn
Practical application of design space exploration
Defined design space based on tiles and connections between tiles
Defined constraints and optimization goals based on power, area, frequency
Runs experiments to produce Pareto Frontier with performance and power as main design dimension
Final designs come from Pareto Frontier – fast, balanced, low-power
Compare design to characteristics of known baseline (Xeon)

## Slide 41: What to think about next?
Miscellaneous (micro)architectural tricks & optimizations (future)
  Super-scalar Out-of-Order
  VLIW
  Vector processors / SIMD
  SIMT/GPU