## Slide 1
Fall 2025
Lecture 13: Virtual Memory
Credit: Brandon Lucia

## Slide 2: Today (& Next Time): Virtual Memory
Basic dimensions of a virtual memory system: paging, protections, process isolation, address mapping
Working through operation of a virtual memory system example, including page fault handling and page table walking
Start looking at hardware support for virtual memory (TLB)

## Slide 3: What is virtualization?

## Slide 4: Virtualization - Purpose
Expose abstraction of abundant resource despite limited resource
Expose abstraction of uniform resource despite heterogeneity of resource
Expose abstraction of isolated resource despite sharing of resource

## Slide 5: Virtualization – What resources?
Entire machines (VMMs)
Storage (Disk controllers / Flash controllers)
Memory (Virtual Memory)
Network connectivity / bandwidth (Software-defined Networks)

## Slide 6: Memory Virtualization

## Slide 7: Virtual Memory – Abstraction of Abundance
0xFFFF
0xFFFF 0xFFFF
Entire Address Range Available
Entire Address Range Available
Entire Address Range Available
X
0x0000
0x0000
0x0000
Process 1
Process 2
Process 3
X
X
X

## Slide 8: Virtual Memory – Abstraction of Uniformity
0xFFFF
0xFFFF 0xFFFF
Contiguous Address Range Available
Contiguous Address Range Available
Contiguous Address Range Available
X X
0x0000
0x0000
0x0000
Process 1
Process 2
Process 3

## Slide 9: Virtual Memory – Abstraction of Isolation*
0xFFFF
0xFFFF 0xFFFF
Unshared
Address Range Available
Unshared
Address Range Available
Unshared
Address Range Available
X
0x0000
0x0000
0x0000
Process 1
Process 2
Process 3
X

## Slide 10: Virtual Memory – Thinking about mechanism
0xFFFF
0x0000
0x0000
Process 1
Process 2
0xFFFF
sw 0xEFFF
sw 0xEFFF
First obvious problem:
Two processes access same location
violates isolation abstraction

## Slide 11: Virtual Memory – Thinking about Mechanism
0xFFFF
0x0000
0x0000
Process 1
Process 2
0xFFFF
sw 0xFFFF
…
sw 0x1000
sw 0xEFFF
…
sw 0x0000
First obvious problem:
Two processes access same location
violates isolation abstraction
Second obvious problem:
Two processes access #bytes > total memory size
violates abundance abstraction (and isolation)

## Slide 12: First Attempt: Static Partitioning [Opal, SASOS, bare-metal micros]
0xFFFF
Process 1
stack
0xFFFF
Statically partitioning the address space
violates abundance and uniformity (but not isolation)
Process 2
stack
Process 1
code
Process 2 code
Process 2 heap
0x0000
0x0000
Process 1
Process 2
Process 2 heap

## Slide 13: First Attempt: Static Partitioning
0xFFFF
Process 1
stack
Process 2
0x0000
0xFFFF
Process 2 heap
0x0000
Statically partitioning the address space
violates abundance and uniformity
Also need to be sure that neither process will go and
mess around with the other process’ address ranges
Process 1
Process 2
stack
Process 1
code
Process 2 code
Process 2 heap

## Slide 14: First Attempt: Static Partitioning
0xFFFF 0xFFFF
Statically partitioning the address space
Need to be sure that neither process will go and mess around with the other process’ address ranges (isolation)
Need to use increasingly tiny partitions per process (abundance)
Need to know where your tiny partition starts so you
can use it (uniformity)
. . .
0x0000
0x0000
cess 1
Process n-1
Process n

## Slide 15: First Attempt: Static Partitioning
0xFFFF 0xFFFF
Statically partitioning the address space
Need to be sure that neither process will go and mess around with the other process’ address ranges (isolation)
Need to use increasingly tiny partitions per process (abundance)
Need to know where your tiny partition starts so you
can use it (uniformity).
Machine code can never refer to an address without knowing mix of other programs running on machine & where process loaded (uniformity, isolation)
. . .
0x0000
0x0000
cess 1
Process n-1
Process n

## Slide 16: Second Attempt: Segmented Memory [8086, IBM AS/400]
0x7FFF
Process 1
stack
0x0000
Process 1
Process 1
code
Process 2 heap
Process 1 stack
0x0000
0x7FFF
Process 2
Process 1
code
Process 2 heap
Active Segment
Segment 1
0/1
Segment 0

## Slide 17: Second Attempt: Segmented Memory
Process 1 stack
0x0000
0x7FFF
Process 2
Process 1 code
Process 2
heap
e Segment
Segment 1
0/1
Segment up the memory address space and switch
segments
Benefit: Limited address size can address more memory (switch segment, another 16b space). Abstraction of abundance.
Benefit: Processes can choose a segment and use predictable addresses off of that segment. Abstraction of uniformity.
Benefit: If processes use independent segments, no interference.
Caveat: 8086 & others did not check permissions,
segments could overlap. (isolation, abundance…)
Caveat: need to select segment; how to choose
which? (uniformity)

## Slide 18: Second Attempt: Segmented Memory
0xFFFF
Process 1 stack
0x0000
Process 1
Process 1 code
Process 2
heap
Active Segment
2^16 segs
Abstraction of abundance, uniformity in segment relative
addressing, and the ability to address a very large address space is a key advantage of segmentation in memory
Segment 0 Segment 1 Segment 2 Segment 3 Segment 4
. . .
Each segment only needs 16bit addresses, combined with a single 16bit segment reg, have 4GB addressed.
Why did they not just use 32bit addresses instead?

## Slide 19: Virtual Memory: Software Dynamic Address Translation (and Permission Checking)
0x7FFF
Process 1
stack
0x0000
Process 1
Process 1 code
Process 2 heap
Physical Memory
Process 1 stack
0x0000
0x7FFF
Process 2
Process 1 code
Process 2 heap
Permissions Check
Translate

## Slide 20: Virtual Memory: Software Dynamic Address Translation and Permission Checking
Physical Memory
Process
Key ideas behind virtual memory:
Physical memory acts like a cache of data that are mapped into process address space
Accesses always refer to VAs and VM translates them to usable physical addresses
Mapping makes a virtual address range accessible & unmapped regions are inaccessible
Virtual memory happens at granularity of pages
(i.e., 4kB chunks of memory)
Page table entry per page contains: (1) is it in physical memory? (2) at what address? (3) with what access permissions?

## Slide 21: Virtual Memory: Software Dynamic Address Translation and Permission Checking
Physical Memory
Process
On every memory access, translate memory address from virtual address to physical address
Benefit: Arbitrary hierarchy of memories / storage can back program data Abstraction of abundance.
Benefit: All processes have identical linear virtual address space that can use predictable addresses always. Abstraction of uniformity.
Benefit: Per-process address space are private by
default. Abstraction of isolation.
Caveat: need mechanism for mapping data in
Caveat: translation & permissions are dynamic
Caveat: translation granularity (i.e., page size) is a system-wide parameter

## Slide 22: Mapping Data Into Virtual Address Space

## Slide 23: Virtual Memory: Mapping Data into Virtual
Address Space
64-bit Address
Space 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
0x00000000
4GB of
a.out
Hard Drive / Backing Storage
Define a new operation map(data, size, mode)
Physical Memory
0x0000000000000000
Process
Data: ID of file on disk to map into address space (or “anonymous” for blank memory) Size: How many bytes in the address space to map
Mode: Readable, writeable, executable
Semantics of map: Mapped addresses in virtual address space become accessible and if file-
backed, correspond to file’s data
What does it mean to “become accessible”?

## Slide 24: Virtual Memory: Mapping Data into Virtual
Address Space
64-bit Address
Space 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
0x00000000
4GB of
a.out
Hard Drive / Backing Storage
Define a new operation
map(addr, data, size, mode)
Physical Memory
0x0000000000000000
Process
Data: file descriptor to map into address space
(or “anonymous” for just memory)
Size: How many bytes to map
Mode: Readable, writeable, executable
Semantics of map: Mapped addresses in virtual
address space become accessible and if file-
backed, correspond to file’s data
What does it mean to “become accessible”? executing memory access to address in range is no longer illegal; corresponds to data, either file or anonymous buffer

## Slide 25: Virtual Memory: Mapping Data into Virtual
Address Space
unmapped
mapped (a.out)
unmapped
64-bit Address
Space 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive /
int fd; open(/foo/bar/baz/a.out);
Map(0x1000, fd, 7500 Bytes, RWX)
Backing Storage
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Update translation function
Update permissions entry
Reserve virtual address range
DO NOT move data anywhere
Translate
Permissions Check
0x1000
0x3000

## Slide 26: Virtual Memory: Accessing Data Mapped into the Virtual Address Space 0xFFFFFFFFFFFFFFFF
mapped (a.out)
0xFFFFFFFF
a.out
Hard Drive /
Access to unmapped region:
Attempt to translate address
Find unmapped: Segmentation Fault.
Access to mapped region:
Attempt to translate address, find mapped
Check permissions
Locate data
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
segfault
sw 0x2500
Backing Storage
0x00000000
4GB of
Physical Memory
sw 0x3500
0x0000000000000000
Process

## Slide 27: Virtual Memory: Shared Mapping of File-backed Data into Address Space by Multiple Processes
0xFFFFFFFFFFFFFFFF
mapped (a.out)
0xFFFFFFFF
0x00000000
4GB of
a.out
Hard Drive / Backing Storage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0xFFFFFFFFFFFFFFFF
mapped
(a.out)
0x2500
unmapped
unmapped
0x4500
STILL DO NOT move data! (shared read mapping)
int fd; open(/foo/bar/baz/a.out);
Map(0x1000, fd, 7500 Bytes, RX)
Physical Memory
0x0000000000000000
Process 1
0x0000000000000000
Process 2
int fd; open(/foo/bar/baz/a.out);
Map(0x2500, fd, 7500 Bytes, RX)

## Slide 28: Virtual Memory: Shared Mapping of Anonymous Data into Address Space by Multiple Processes
0xFFFFFFFFFFFFFFFF
mapped (anon)
0xFFFFFFFF
0x00000000
4GB of
a.out
Hard Drive / Backing Storage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0xFFFFFFFFFFFFFFFF
mapped
(anon)
0x2500
unmapped
unmapped
0x4500
Can share non-file-backed memory w/ memfd_create; all refs close? mem disappears
int fd = memfd_create(/usr/mem, …)
Map(0x1000, fd, 7500 Bytes, RX)
Physical Memory
0x0000000000000000
Process 1
0x0000000000000000
Process 2
int fd = memfd_create(/usr/mem);
Map(0x2500, fd, 7500 Bytes, RX)

## Slide 29: Page Granularity for Translation (& Permissions)

## Slide 30: Virtual Memory: Translation & Permissions at Page Granularity 0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
unmapped
Page 0x1000 mapped
(a.out) Page 0x2000
unmapped
0xFFFFFFFF
0x00000000
4GB of
Physical Memory
a.out
Hard Drive / Backing Storage
Still not talking about getting actual data yet; first need to translate (we will talk about how data moves in a few slides)
Translation happens at page granularity
Pages are usually 2^12 = 4096 bytes
Memory access:
Look up translation for page virtual address
Find & fetch data after translation
Translate
Permissions Check
0x1000
0x3000
0x2000

## Slide 31: Virtual Memory: Translation and Finding Data Outcome #1: Page Not in Physical Memory 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Translate
Permissions Check
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
“Translate Virtual Page Number
0x2000, please!” 0x1000
Hard Drive /
Backing Storage
unmapped
lw 0x2500
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory

## Slide 32: Virtual Memory: Translation and Finding Data Outcome #1: Page Not in Physical Memory 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Translate
Permissions Check
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
VM:
“Mapped, but not in physical memory!”
Hard Drive /
Backing Storage
unmapped
lw 0x2500
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory
?
“Translate Virtual Page Number
0x2000, please!” 0x1000

## Slide 33: Virtual Memory: Translation and Finding Data Outcome #1: Page Not in Physical Memory 0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
0xFFFFFFFF
0x00000000
4GB of
Physical Memory
a.out
Hard Drive / Backing Storage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
lw 0x2500
VM:
“Page Fault.
Try again.”
Virtual Memory
“Demand Paging” – bring into physical memory on first access
VM:
“Translation updated. Page in memory for future accesses.
Move page from disk into memory on access:
“demand paging”

## Slide 34: Virtual Memory: Translation and Finding Data Outcome #2: Page in Physical Memory 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Translate
Permissions Check
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
“Translate Virtual Page Number
0x2000, please!” 0x1000
Hard Drive /
Backing Storage
unmapped
lw 0x2500
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory

## Slide 35: Virtual Memory: Translation and Finding Data Outcome #2: Page in Physical Memory 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Translate
Permissions Check
0x1000
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
VM:
“Translated:
0x2000 =>
0xF000”
VM:
“Virtual 0x2000 corresponds to Physical Page Number 0xF000”
Hard Drive /
Backing Storage
unmapped
lw 0x2500
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory

## Slide 36: Virtual Memory: Translation and Finding Data Outcome #2: Page in Physical Memory 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive / Backing Storage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
lw 0x2500
MEM:
lw 0xF500
CPU Memory Unit: “Data at physical page number 0xF000, physical page offset
0x500, please”
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory
0xF500
0xF000

## Slide 37: Virtual Memory: Translation and Finding Data Outcome #2: Page in Physical Memory 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive / Backing Storage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
lw 0x2500
MEM:
lw 0xF500
Memory Hierarchy:
“Data at 0xF500:
<data>”
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory

## Slide 38: The Translation Function & Its Use

## Slide 39: Virtual Memory: The Translation Function Page Table Stores Translation for Paged-In Data 0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
0xFFFFFFFF
a.out
Hard Drive / Backing Storage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x2500
Virtual Memory
0x2000
0xF000
VPN
PPN
Page Table
Page
Table
Entry
0x00000000
4GB of
Physical Memory
PPN: Physical Page Number VPN: Virtual Page Number

## Slide 40: Virtual Memory: The Translation Function Page Table Holds Disk Location for Paged-Out Data
0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive /
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x2500
0x2000
Paged Out:
/swap/a.out
Page Table
VPN PPN
Page
Table
Entry
Backing Storage
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory

## Slide 41: Virtual Memory: The Translation Function Page Table Holds No Entry for Unmapped Data 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive /
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x7522
0x2000
Paged Out:
/swap/a.out
VPN
PPN
Page Table
Page Table Entry
0x7000
No Entry!
???????
SegFault delivered to program
Backing Storage
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory

## Slide 42: Physical Memory as a Cache of Data on Disk: Cache Miss Means Page Fault (1/2) 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive /
Translate
Permissions Check
0x1000
0x3000
0x2000
unmapped
Page 0x1000 mapped
(a.out) Page 0x2000
unmapped
sw 0x2522
0x2000
Paged Out:
/swap/a.out
Page Table
VPN PPN
Page
Table
Entry
Backing Storage
0x00000000
4GB of
Physical Memory
“Demand Paging” – bring into physical memory on first access
0x0000000000000000
Process
Virtual Memory

## Slide 43: Physical Memory as a Cache of Data on Disk: Cache Miss Means Page Fault (2/2) 0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive /
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x2522
0x2000
0x1E000
Page Table
VPN PPN
Page
Table
Entry
0x1E000
Backing Storage
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Virtual Memory

## Slide 44: Virtual Memory Translation Algorithmically
vmTranslate(vaddr){
//Compute Virtual Page Number & Virtual Page Offset
//from vaddr assuming 2^12 page size
(VPN,VPO) = (vaddr[63:12],vaddr[11:0])
PPN = PT.lookup(VPN)
if PPN == UNMAPPED:
kill(SIGSEGV)
else if PPN == PAGEDOUT@<diskloc>: MMU.pageIn(VPN,PPN,<diskloc>) // move diskloc data to
// phys @ PPN, update PTE for VPN
MMU.raiseInterrupt(PAGE_FAULT, …)
//Semantics of interrupt: replay instruction that caused interrupt
//In Lab 3 emulation: page data in, record page fault
else
return PPN //PTE contained usable VPN; hooray! MMU tells CPU the PPN
}

## Slide 45: Permissions Checking

## Slide 46: Permissions Checking Happens with Page Translation (Compare access type to permissions) 0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
0xFFFFFFFF
0x00000000
4GB of
Physical Memory
a.out
Hard Drive / Backing Storage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x2522
Virtual Memory
0x2000
0x1E000
Page Table
VPN PPN
0x1E000
Perms
R

## Slide 47: Page Cache Placement / Replacement

## Slide 48: Physical Memory as a Cache of Data on Disk: Cache Placement / Replacement Policy
a.out
?
Hard Drive /
Backing Storage
0x00000000
4GB of
Physical Memory
Acts as cache for disk
0xFFFFFFFF
Placement Policy? Where to put a new page?

## Slide 49: Physical Memory as a Cache of Data on Disk: Cache Placement / Replacement Policy
0xFFFFFFFF
a.out
Fully Associative
Hard Drive /
Backing Storage
0x00000000
4GB of
Physical Memory
Acts as cache for disk
Placement Policy:
Fully associative – need flexibility to put any page anywhere in physical memory via arbitrary mapping function. Next available location works fine.
Replacement Policy?

## Slide 50: Physical Memory as a Cache of Data on Disk: Cache Placement / Replacement Policy
0xFFFFFFFF
a.out
?
Hard Drive /
Backing Storage
0x00000000
4GB of
Physical Memory
Acts as cache for disk
Placement Policy:
Fully associative – need flexibility to put any page anywhere in physical memory via arbitrary mapping function. Next available location works fine.
Replacement Policy?

## Slide 51: Physical Memory as a Cache of Data on Disk: Cache Placement / Replacement Policy
0xFFFFFFFF
0x00000000
4GB of
a.out
Hard Drive / Backing Storage
?
so you can focus on translation & mapping
Physical Memory
Acts as cache for disk
Placement Policy:
Fully associative – need flexibility to put any page anywhere in physical memory via arbitrary mapping function. Next available location works fine.
Replacement Policy:
Can be complicated…
Variants of LRU & approximations
Not Recently Used (like Bit-PLRU)
Not Frequently Used
Re-reference-Distance-Based Policies
In Lab 3 we handle placement & replacement

## Slide 52: Page Tables: Another Look at the Translation Function

## Slide 53: Page Translation and Its Implementation
Page Table
 |  |  |  |  | PPN |  | Perms/Flags |  |  | 
 |  |  | VPN |  |  |  |  |  |  | 
 |  |  | 0x2000 |  | 0x123000 |  |  | RW |  | 
 |  |  | 0x3000 |  | Paged Out: /swap/a.out |  |  | RWX |  | 
 |  |  | … |  |  |  |  |  |  | 
 |  |  | 0xF000 |  | 0xFFF0F000 |  |  |  | RW | 
 |  |  | … |  |  |  |  |  |  | 
 | 0x |  | 126F000 |  | 0x11212000 |  |  |  | R | 
 |  |  | … |  |  |  |  |  |  | 
0xFFFFFFF |  |  | FF000 |  | 0x45454000 |  |  |  | R / COW | 
Table stores 2^36 entries in it for virtual pages 0x000000000000 up to 0xFFFFFFFFF000
which span the entire
48-bit address space.
Implementation Issues?
VPN
VPO
PPN
PPO
Translate
36 bits 12 bits
Page Table Entry – 6 Bytes
12 bits
PPN
Perms/Flags
36 bits
36 bits
12 bits
Q: Why can store flags in
lower 12 bits of PTE?
48-bit Virtual Address (like AMD)

## Slide 54: Page Translation and Its Implementation
Page Table
 |  |  |  |  | PPN |  | Perms/Flags |  |  | 
 |  |  | VPN |  |  |  |  |  |  | 
 |  |  | 0x2000 |  | 0x123000 |  |  | RW |  | 
 |  |  | 0x3000 |  | Paged Out: /swap/a.out |  |  | RWX |  | 
 |  |  | … |  |  |  |  |  |  | 
 |  |  | 0xF000 |  | 0xFFF0F000 |  |  |  | RW | 
 |  |  | … |  |  |  |  |  |  | 
 | 0x |  | 126F000 |  | 0x11212000 |  |  |  | R | 
 |  |  | … |  |  |  |  |  |  | 
0xFFFFFFF |  |  | FF000 |  | 0x45454000 |  |  |  | R / COW | 
Table stores 2^36 entries in it for virtual pages 0x000000000000 up to 0xFFFFFFFFF000
which span the entire
48-bit address space.
Dense, linear table stores 2^36 * 6B PTEs: 550.8GB of Page Tables
Most PTEs Empty!!!
VPN
VPO
PPN
PPO
Translate
36 bits 12 bits
Page Table Entry – 6 Bytes
12 bits
PPN
Perms/Flags
36 bits
36 bits
12 bits
48-bit Virtual Address (like AMD)

## Slide 55: Hierarchical Page Tables
Page Table Entry – 6 Bytes
Page Table Addr or PPN
Perms/Flags
36 bits
12 bits
PTAddr
PTAddr
…
2^9 PTEs
PTAddr
PTAddr
…
2^9 PTEs
PTAddr
…
2^9 PTEs
…
PTAddr
…
…
PTAddr
…
2^9 PTEs
2^9 PTEs
PTAddr
…
2^9 PTEs
PPN
…
PPN
…
…
PPN
…
Multi-level / hierarchical page tables are enormously more space efficient. If an entire sub-tree of addresses in hierarchy of tables contain no mapped VAs, then entire tables not stored anywhere in memory!
…
…
…
…
PTAddr
…
PTAddr

## Slide 56: Translation Using Hierarchical Page Tables
48-bit Virtual Address
9 bits
12 bits
L1 PT Offset | L2 PT Offset | L3 PT Offset | L4 PT Offset | VPO
9 bits
9 bits
9 bits
PTAddr
…
PTAddr
Register CR3 Page Table Base
PTAddr
PTAddr
…
…
PTAddr
…
PPN
…
L1 PTab
L2 PTab
L3 PTab
L4 PTab
PPN
PPO

## Slide 57: Mapping Using Hierarchical Page Tables
48-bit Virtual Address
9 bits
12 bits
L1 PT Offset | L2 PT Offset | L3 PT Offset | L4 PT Offset | VPO
9 bits
9 bits
9 bits
PTAddr
…
PTAddr
Register CR3 Page Table Base
PTAddr
PTAddr
…
…
PTAddr
…
Paged Out
…
L1 PTab
L2 PTab
L3 PTab
L4 PTab
L1 Table Always Exists
Table not allocated? Create & fill entry
Initialize PPN to show paged out.

## Slide 58: (New) Intel 57-bit Virtual, 52-bit Physical, 5-level Translation Using Hierarchical Page Tables (2019)
57-bit Virtual Address
9 bits
12 bits
9 bits
9 bits
9 bits
PTAddr
…
PTAddr
Register CR3 Page Table Base
PTAddr
PTAddr
…
…
PTAddr
…
PPN
…
L1 PTab
L2 PTab L3 PTab
Why not do something with those top 7 bits?
L4 PTab
PPN
PPO
PTAddr
…
PTAddr
L0 PTab
9 bits
Reserved | L0 PT Offset | L1 PT Offset | L2 PT Offset | L3 PT Offset | L4 PT Offset | VPO
7 bits

## Slide 59: (New) Intel 57-bit Virtual, 52-bit Physical, 5-level Translation Using Hierarchical Page Tables (2019)
57-bit Virtual Address
9 bits
12 bits
9 bits
9 bits
9 bits
PTAddr
…
PTAddr
Register CR3 Page Table Base
PTAddr
PTAddr
…
…
PTAddr
…
PPN
…
L1 PTab L2 PTab L3 PTab L4 PTab
PPN
PPO
PTAddr
…
PTAddr
L0 PTab
9 bits
Reserved | L0 PT Offset | L1 PT Offset | L2 PT Offset | L3 PT Offset | L4 PT Offset | VPO
7 bits
Why not do something with those top 7 bits?
Intel checks that addresses are “canonical”, meaning sign extended to 64 bits & if not, then
SEGFAULT. Allows future architecturs to use 64b addrs if they want to!

## Slide 60: What part of the pipeline manipulates the page tables?
ALU
ALU: output C data
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
Data Memory
4
+
MUX
Branch Target
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control
Signals
Read Register A & B Select
Input Read Reg B
Write Reg C Data
Branch Target
Read
Data C
Read Data C (Ld)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select
[Ld/St]
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
Exec/Exec Forward
Mem/Mem Forward
Mem/Exec Forward
WB/Exec Forward
Instruction PC+4
WB/Mem Forward
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
Input Read Reg A
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
Branch
Target
+
Offset
Instruction PC + 4
Branch
Target
Branch
Outcome Logic
PC
Source Select
Reg A Reg B
.
.
.
Branch Predictor
Outcome
Target
Instruction Fetch

## Slide 61: MMU has fast access to memory and TLB for translation
ALU
ALU: output C data
Instruction Memory
Instruction Fetch
Control Signals:
Op select
op = [+, -, x, /]
Memory
Unit
4
+
MUX
Branch Target
PC Source Select (1 if branch taken)
PC
PC Source Select
Reg 1
Reg 2
Reg 3
Reg 4
Control
Signals
Read Register A & B Select
Input Read Reg B
Write Reg C Data
Branch Target
Read
Data C
Read Data C (Ld)
Register
Writeback
Output/Read Reg C Data
Output/Read Reg Select
Write Reg C Data
Write Reg C Select
Cont. Sigs.: Op. Select
[Ld/St]
Data
Memory
Instr. Decode Execute
Read Regs A & B Data Write Register C Select
Write Register C Data
Memory
Register Write-Back
Exec/Exec Forward
Mem/Mem Forward
Mem/Exec Forward
WB/Exec Forward
Instruction PC+4
WB/Mem Forward
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
Input Read Reg A
MUX
WB/Ex Fwd
Ex/Ex Fwd Mem/Ex Fwd
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
Branch
Target
+
Offset
Instruction PC + 4
Branch
Target
Branch
Outcome Logic
PC
Source Select
Reg A Reg B
.
.
.
Branch Predictor
Outcome
Target
Instruction Fetch
MMU
+ TLB
Key idea: page table walk entails extra memory operations not extra memory instructions

## Slide 62: Performance and Storage Overhead Analysis of Translation with Page Tables

## Slide 63: Page Tables Stored in Virtual Memory and Paged in and out Like Other Data
First level page table always in physical memory at address in Register CR3. Other levels of page table can be paged out to make space for other data.
All paged & page table data moves through cache hierarchy like any other data
0xFFFFFFFF
0x00000000
4GB of
Physical Memory
Acts as cache for disk
PTAddr
…
PTAddr
PPTTAAddddrr
…
Register CR3
PTAddr
… …
PTAddr
PTAddr
…
Perm s/Fla gs
1
2
b i t s
P
T A
d d r
P T A
d d
r
…
2
^ 9
P T
Es
P T A
d d
rP T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
…
P T A
d d r
…
…
2
^ 9
P T
Es
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P P N
…
P P N
…
…
P P N
…
…
…
…
…
P T A
d d r
P T A
d d r
…
Question: How much space overhead to store hierarchical vs. linear page tables?
Question: How much time overhead to access hierarchical vs. linear page tables?

## Slide 64: Space Overhead Analysis of Page Tables
12 bits
PTAddr
PTAddr
…
PTAddr
PTAddr
…
2^9 PTEs
2^9 PTEs
…
PTAddr
…
PTAddr
…
…
PTAddr
…
2^9 PTEs
2^9 PTEs
2^9 PTEs
PPN
…
PPN
…
…
PPN
…
…
…
…
…
PTAddr
…
PTAddr
512sETP^92
PTEs
8bytes / PTE (sign extend to 64-bit word size)
PTAddr
…
PTAddr
How much space for tables vs. mapped data? Compared to linear?
PPN
4 Levels of Page Tables

## Slide 65: Space Overhead Analysis of Page Tables
12 bits
PTAddr
PTAddr
…
PTAddr
PTAddr
…
2^9 PTEs
2^9 PTEs
…
PTAddr
…
PTAddr
…
…
PTAddr
…
2^9 PTEs
2^9 PTEs
2^9 PTEs
PPN
…
PPN
…
…
PPN
…
…
…
…
…
PTAddr
…
PTAddr
512sETP^92
PTEs
8bytes / PTE (sign extend to 64-bit word size)
PTAddr
…
PTAddr
Table Size = Page Size
2^3 bytes / PTE * 2^9 PTEs / Table = 2^12 = 4kB / Table
Pictured Example page tables size:
9 * 4kB = 36kB of page tables
Possible to map every page in last level PT:
4 last level tables exist * 512 entries * 4kB / page = 2^23B mappable with just these page tables
Overhead:
36kB / 2^23B = 36kB / 2^13kB = 0.004x overhead
Linear page tables:
550GB of page tables
With 2^23B of data to map, 65565x overhead
PPN
4 Levels of Page Tables

## Slide 66: Performance Analysis of Page Tables
12 bits
PTAddr
PTAddr
…
2^9 PTEs
PTAddr
PTAddr
…
2^9 PTEs
2^9 PTEs
…
PTAddr
…
PTAddr
…
…
PTAddr
…
2^9 PTEs
2^9 PTEs
2^9 PTEs
PPN
…
PPN
…
…
PPN
…
…
…
…
…
PTAddr
…
PTAddr
PTAddr
…
PTAddr
PPN
What is the time cost per memory access to use a hierarchical page table structure?
sw 0x2000

## Slide 67: Performance Analysis of Page Tables
12 bits
PTAddr
PTAddr
…
2^9 PTEs
PTAddr
PTAddr
…
2^9 PTEs
2^9 PTEs
…
PTAddr
…
PTAddr
…
…
PTAddr
…
2^9 PTEs
2^9 PTEs
2^9 PTEs
PPN
…
PPN
…
…
PPN
…
…
…
…
…
PTAddr
…
PTAddr
PTAddr
…
PTAddr
PPN
What is the time cost per memory access to use a hierarchical
page table structure?
sw 0x2000
Plus four more memory accesses:
one memory access per page table level
three of which levels may be swapped out / page fault
all of which can be a cache miss
Worst case time overhead:
Word at 0x2000 is an L1 cache hit, all page table data except first level table misses in cache & page faults
1 cycle L1 hit becomes 3 cache misses & 3 page faults (DRAM
~20 cycles) = 60-100 (or more) cycles overhead on 1 cycle L1 hit
Minimum(-ish) Overhead:
Access to word at 0x2000 (L1 miss, say), all page table accesses
hit in cache & no page faults
3 cycle L1 miss becomes 3 cache hits and a cache miss (1 cycle cache hits) = 3 cycles overhead on 3 cycle L1 miss
Time Overhead Summary: Worst: >60-100x overhead Best: ~2x overhead

## Slide 68: Hierarchical Page Tables Trade Time to Save Space
12 bits
PTAddr
PTAddr
…
2^9 PTEs
PTAddr
PTAddr
…
2^9 PTEs
2^9 PTEs
…
PTAddr
…
PTAddr
…
…
PTAddr
…
2^9 PTEs
2^9 PTEs
2^9 PTEs
PPN
…
PPN
…
…
PPN
…
…
…
…
…
PTAddr
…
PTAddr
PTAddr
…
PTAddr
PPN
Space Savings:
From 65565x space overhead
to a 0.001x space overhead
Time overhead:
From 2x constant time overhead to a variable overhead that can be upwards of 100x!
Key Insight:
Use microarchitectural support in the form of a Translation Lookaside Buffer to eliminate the time cost of most translations

## Slide 69: Translation Lookaside Buffers: Hardware Support for Caching Page Address Translations

## Slide 70: Translation Lookaside Buffer: Basic Idea (Hit)
0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
0xFFFFFFFF
0x00000000
4GB of Physical Memory
t
e /
rage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x2522
Virtual Memory
0x2000
0x1E000
VPN
PPN
Page Table
0x1E000
TLB: On-core Hardware
Cache of Translations

## Slide 71: Translation Lookaside Buffer: Basic Idea (Hit)
0xFFFFFFFF
t
e /
rage
0x00000000
4GB of Physical Memory
0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
Permissions Check
Translate
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x2522
y
Page Table
VPN PPN
0x2000 0x1E000
0x1E000
Virtual Memor
TLB: On-core Hardware
Cache of Translations
Awesome property of the TLB:
On a TLB Hit, no need to run translation function, access
page tables, traverse page table hierarchy, experience a page
fault, access the page table again, and return a translation
Translation stays core-local, zero extra memory accesses

## Slide 72: Translation Lookaside Buffer: Basic Idea
0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
0xFFFFFFFF
0x00000000
4GB of Physical Memory
t
e /
rage
Translate
Permissions Check
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x2522
Virtual Memory
0x2000
0x1E000
VPN
PPN
Page Table
0x1E000
TLB Miss (4): cache
0x2000 => 0x1E000 in TLB
TLB: Translation
Cache

## Slide 73: Translation Lookaside Buffer: Basic Idea (Hit)
0xFFFFFFFF
t
e /
rage
0x00000000
4GB of Physical Memory
0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
Permissions Check
Translate
0x1000
unmapped
unmapped
0x3000
0x2000
Page 0x1000 mapped
(a.out) Page 0x2000
sw 0x2522
y
Page Table
VPN PPN
0x2000 0x1E000
0x1E000
Virtual Memor
TLB: On-core Hardware
Cache of Translations
On the next access to same page:
TLB Hit! Subsequent accesses to
same page amortize cost of page
table “walk”

## Slide 74: Hardware Support for Virtual Memory: Translation Lookaside Buffers in Intel Core i7
Separate L1 data & instruction (L1) TLB
Size? Reach? Why i-TLB larger?
Unified (L2) TLB
512 entries: total size? total reach?

## Slide 75: Hardware Support for Virtual Memory: Translation Lookaside Buffers in Intel Core i7
Separate L1 data & instruction (L1) TLB
Size: 64 * 8B = 512B; 128 * 8B = 1024B
Data Reach: 64 * 4kB = 256kB data Code Reach: 128 * 4kB = 512kB code
Unified (L2) TLB
Size: 512 * 8B = 4kB
Reach: 512 * 4kB = 2^21 = 2MB code+data
Awesome Property of the TLB:
With a 3MB-ish working set of data + code, can run
without ever running virtual memory translation

## Slide 76: Hardware Support for Virtual Memory: Translation Lookaside Buffers in Intel Core i7
Separate L1 data & instruction (L1) TLB
Size: 64 * 8B = 512B; 128 * 8B = 1024B
Data Reach: 64 * 4kB = 256kB data Code Reach: 128 * 4kB = 512kB code
Unified (L2) TLB
Size: 512 * 8B = 4kB
Reach: 512 * 4kB = 2^21 = 2MB code+data
Awesome Property of the TLB?
What if my working set is, like, 58GB?
Question: How do we increase TLB Reach?

## Slide 77: Revisiting the Assumption of Page Granularity
0xFFFFFFFFFFFFFFFF
0x0000000000000000
Process
unmapped
Page 0x40000000
0xFFFFFFFF
0x00000000
4GB of
Physical Memory
a.out
Hard Drive / Backing Storage
What if a page were large (2MB) or huge (1GB)?
Translate
Permissions Check
0x40000000
0x80000000
1GB of data

## Slide 78: Hardware Support for Virtual Memory: Translation Lookaside Buffers in Intel Core i7
Separate L1 data & instruction (L1) TLB
Size: 64 * 8B = 512B; 128 * 8B = 1024B
Max Data Reach: 64 * 1GB = 64GB data Code Reach: 128 * 4kB = 512kB code Implication of this TLB organization
Unified (L2) TLB
Size: 512 * 8B = 4kB
Max Reach: 512 * 1GB = 512GB code+data
Awesome Property of the TLB!
Huge pages make reach of L1TLB be 64GB!

## Slide 79: Increasing Page Size to Increase TLB Reach
unmapped
Page 0x40000000
0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
0x00000000
4GB of
a.out
Hard Drive / Backing Storage
Moder Oses support large pages and huge pages via mmap (& other ways).
IA-64 (Itanium) had 8 page
sizes 4kB – 256MB
Can mix different page sizes
w/ hardware support
Translate
Permissions Check
0x40000000
0x80000000
mmap((void*)0x0, |  |  | 
round_to_huge_page_size(n * sizeof(T)), |  |  | 
PROT_READ ¦ PROT_WRITE, |  |  | 
MAP_PRIVATE ¦ MAP_ANONYMOUS ¦MAP_HUGETLB, |  |  | 
Physical Memory
0x0000000000000000
Process
1GB of data
-1, 0));

## Slide 80: Increasing Page Size to Increase TLB Reach
unmapped
Page 0x40000000
0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
0x00000000
4GB of
a.out
Hard Drive / Backing Storage
“Transparent” huge pages allow the OS to promote a normal page to HUGE status
Translate
Permissions Check
0x40000000
0x80000000
1GB of data
Physical Memory
0x0000000000000000
Process
madvise(..., MADV_HUGEPAGE);
Not guaranteed to Huge-ify.
If aligned more likely to be huge
int posix_memalign(void **memptr,
size_t alignment, size_t size);

## Slide 81: Increasing Page Size to Increase TLB Reach
unmapped
Page 0x40000000
0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive /
Translate
Permissions Check
0x40000000
0x80000000
1GB of data
Backing Storage
0x00000000
4GB of
Physical Memory
0x0000000000000000
Process
Risks / Costs of Increasing Page Size?

## Slide 82: Increasing Page Size to Increase TLB Reach
unmapped
Page 0x40000000
0xFFFFFFFFFFFFFFFF
0xFFFFFFFF
a.out
Hard Drive / Backing Storage
Translate
Permissions Check
0x40000000
0x80000000
1GB of data
0x00000000
4GB of
Physical Memory
Use at your own risk! Try it out!
0x0000000000000000
Process
Risks / Costs of Increasing Page
Size?
High cost to page in/out on page fault (eek!)
Wasting memory if hugeness is useless
Internal page fragmentation
Need HW to track page sizes
Potential for programmer error w/ changing sizes
High cost to zero a page

## Slide 83: How Do Virtual Memory and Caching Interact?

## Slide 84: Recall: Physically separate cache data & tags
L3$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
0x01111111111111110000000001010011
tag bits
set index
block offset
L3$
Set 0
Set 1
Set 2
Set 3
tag 1
tag 2
tag 3
Way 0
Way 1
Way 2
Way 3
tag 0
Cache Tag Array
Cache Data Array

## Slide 85: Recall:
Physically separate cache data & tags
L3$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
0x01111111111111110000000001010011
tag bits
set index
block offset
L3$
Set 0
Set 1
Set 2
Set 3
tag 1
tag 2
tag 3
Way 0
Way 1
Way 2
Way 3
tag 0
Question: Virtual or Physical Address?
Cache Tag Array
Cache Data Array

## Slide 86: Physical Cache: Translate First Then Access Cache
L3
$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
Virtual Address 0x01111111111111110000000001010011
3
$
L
3
$
S
e t
0
S
e t
1
S
e t 2
S
e t
3
W
ay
0
W
ay
ta1g 1
W
ay
ta2g 2
W
ay
ta3g 3
Cache Data Array
Cache Tag Array
Perm s/Fla gs
1
2
b i t s
P
T A
d d r
P T A
d d
r
…
2
^ 9
P T
Es
P T A
d d
rP T A
d d r
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
…
P T A
d d
r
… …
2
^ 9
P T
Es
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P P N
…
P P N
…
…
P P N
…
… …
…
…
…
P T A
d d
r
P T A
d d r
…
Translate
Physical Address
tag
VPN
Tag bits change with translation b/c cache uses physical addresses but page offset bits stay same
PPN PPO
0x01100001111011100001001101010011
VPO
Issues with the physical cache approach?

## Slide 87: Physical Cache: Translate First Then Access Cache (PIPT: Physically Indexed, Physically Tagged)
L3
$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
Virtual Address 0x01111111111111110000000001010011
3
$
L
3
$
S
e t
0
S
e t
1
S
e t 2
S
e t
3
W
ay
0
W
ay
ta1g 1
W
ay
ta2g 2
W
ay
ta3g 3
Cache Data Array
Cache Tag Array
Perm s/Fla gs
1
2
b i t s
P
T A
d d r
P T A
d d
r
…
2
^ 9
P T
Es
P T A
d d
rP T A
d d r
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
…
P T A
d d r
… …
2
^ 9
P T
Es
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P P N
…
P P N
…
…
P P N
…
… …
…
…
…
P T A
d d r
P T A
d d r
…
Translate
Physical Address
tag
VPN
Tag bits change with translation b/c cache uses physical addresses but page offset bits stay same
PPN PPO
0x01100001111011100001001101010011
VPO
Issues with the physical cache approach?
Translation is on the L1 critical path!
Even w/ TLB hit, increases L1 hit time
Limits cycle time & performance

## Slide 88: Virtual Cache: Access Cache Then Translate (VIVT: Virtually Indexed, Virtually Tagged)
L3
$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
3
$
L
3
$
S
e t
0
S
e t
1
S
e t 2
S
e t
3
W
ay
0
W
ay
ta1g 1
W
ay
ta2g 2
W
ay
ta3g 3
Perm s/Fla gs
1
2
b i t s
P
T A
d d r
P T A
d d
r
…
2
^ 9
P T
Es
P T A
d d
rP T A
d d r
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
…
P T A
d d r
… …
2
^ 9
P T
Es
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P P N
…
P P N
…
…
P P N
…
… …
…
…
…
P T A
d d r
P T A
d d r
…
Translate
0x01100001111011100001001101010011
Physical Address
Virtual Address 0x01111111111111110000000001010011
tag
VPN
PPN PPO
VPO
Benefits of the virtual cache approach?
Parallelize cache lookup & translate Costs of the virtual cache approach?
Synonyms & homonyms
Cache Data Array
Cache Tag Array
To: lower caches & memory

## Slide 89: Virtual Caches: The Synonym Problem
L3
$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
0x01111111111111110000111000010010
3
$
L
3
$
S
e t
0
S
e t
1
S
e t 2
S
e t
3
W
ay
0
W
ay
ta1g 1
W
ay
ta2g 2
W
ay
ta3g 3
Perm s/Fla gs
1
2
b i t s
P
T A
d d r
P T A
d d
r
…
2
^ 9
P T
Es
P T A
d d
rP T A
d d r
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
…
P T A
d d
r
… …
2
^ 9
P T
Es
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P P N
…
P P N
…
…
P P N
…
… …
…
…
…
P T A
d d
r
P T A
d d r
…
Translate
0x01100001111011100001001101010011
Process 1:
Physical Address
PPN PPO
Virtual Address 1 VPN VPO
0x01111111111111110000000000110011
Process 2:
Virtual Address 1 VPN
VPO
Problem: two VAs refer to the same PA. Cached
Cache Data Array
Cache Tag Array
To: lower caches & memory
separately, in memory as a single block.

## Slide 90: Virtual Caches: The Homonym Problem
L3
$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
0x01111111111111110000011000010011
3
$
L
3
$
S
e t
0
S
e t
1
S
e t 2
S
e t
3
W
ay
0
W
ay
ta1g 1
W
ay
ta2g 2
W
ay
ta3g 3
Perm s/Fla gs
1
2
b i t s
P
T A
d d r
P T A
d d
…
2
^ 9
P T
Es
P T A
d d
rP T A
d d r
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
…
P T A
d d
r
…
…
2
^ 9
P T
Es
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P P N
…
P P N
…
…
P P N
…
… …
…
…
…
P T A
d d r
P T A
d d rr
…
Translate
Process 1:
Physical Address 1
Virtual Address 1 VPN VPO
0x01111111111111110000000000110011
Process 2:
Virtual Address 2 VPN
VPO
0x01100001111011100001001101010011
Physical Address 2
0x0100000011111000001001101010011
Problem: Same VA refers to two different PAs. Same
block in cache, but distinct in memory.
Cache Data Array
Cache Tag Array
To: lower caches & memory

## Slide 91: Virtually Indexed, Physically Tagged Caches
L3
$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
3
$
L
3
$
S
e t
0
S
e t
1
S
e t 2
S
e t
3
W
ay
0
W
ay
ta1g 1
W
ay
ta2g 2
W
ay
ta3g 3
Cache Data Array
Cache Tag Array
Perm s/Fla gs
1
2
b i t s
P
T A
d d r
P T A
d d
r
…
2
^ 9
P T
Es
P T A
d d
rP T A
d d r
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
…
P T A
d d
r
… …
2
^ 9
P T
Es
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P P N
…
P P N
…
…
P P N
…
… …
…
…
…
P T A
d d
r
P T A
d d r
…
Translate
Virtual Address 0x01111111111111110000000001010011
Physical Address
tag
VPN
Use index bits from VPO and
use tag bits from PPN. Overlap set indexing w/ translation
PPN PPO
0x01100001111011100001001101010011
VPO
For what cache organizations does VIPT work?

## Slide 92: Virtually Indexed, Physically Tagged Caches
L3
$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
3
$
L
3
$
S
e t
0
S
e t
1
S
e t 2
S
e t
3
W
ay
0
W
ay
ta1g 1
W
ay
ta2g 2
W
ay
ta3g 3
Cache Data Array
Cache Tag Array
Perm s/Fla gs
1
2
b i t s
P
T A
d d r
P T A
d d
r
…
2
^ 9
P T
Es
P T A
d d
rP T A
d d r
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P T A
d d r
…
…
P T A
d d
r
… …
2
^ 9
P T
Es
2
^ 9
P T
Es
P T A
d d r
…
2
^ 9
P T
Es
P P N
…
P P N
…
…
P P N
…
… …
…
…
…
P T A
d d
r
P T A
d d r
…
Translate
Virtual Address 0x01111111111111110000000001010011
Physical Address
tag
VPN
Use index bits from VPO and
use tag bits from PPN. Overlap set indexing w/ translation
PPN PPO
0x01100001111011100001000001010011
VPO
Cache geometries compatible with VIPT:
Requires #VPO bits > #cache block offset + #cache set index bits (why?)
Page size > block size * (cachesize / assoc = #sets)

## Slide 93: Virtual Caches vs. Physical Caches
Virtual Cache: uses virtual address to do cache lookups
Physical Cache: uses physical address to do cache lookups
Virtually-Indexed, Physically-Tagged (VIPT): uses virtual set index bits to do set lookup, uses physical tag bits to do tag comparison

## Slide 94: What did we just learn?
Virtual memory, from the ground up
Partitioning & segmentation: partial solutions
Dynamic, software mapping, translation, and permissions checking
Page tables & hierarchical page tables
TLBs for accelerating translation
Caches & VM together