## Slide 1
Fall 2023
Lecture 3: Computer Architecture Basics
Credit: Brandon Lucia

## Slide 2: What did we talk about last time?
Hardware vs. software tradeoffs
von Neumann vs. Harvard architecture and the beginnings of a design space
An optimization exercise by example
Amdahl’s Law (and Gustafson’s Law, by contrast)

## Slide 3: What is a Computer Architecture?
Building up to our first architecture
Defining the ISA: Architecture vs. Microarchitecture
RISC vs. CISC ISAs
RISCV ISA

## Slide 4: Recall: The Von Neumann Computing Model
Program
Data
Unified Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
John von Neumann’s Big Idea:
Programs are data.

## Slide 5: Recall: the Harvard Architecture
Program
Data
Instruction Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Data Bus
Split bus architecture provides simultaneous access to program and to data

## Slide 6: Either Way: Our CPU from last time is incomplete
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
What’s missing?

## Slide 7: Basic Architecture: State + processing elements
Maintain State (sequential logic)
Process (combinational logic)
control
ALU/processing
state

## Slide 8: Building up to our first architecture: ALU
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output: A op B

## Slide 9: Building up to our first architecture: ALU
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output: A op B
Design choice – what operations do we support here?

## Slide 10: Basic Architecture: State + processing elements
Maintain State (sequential logic)
control
ALU/processing
state
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output:
A op B

## Slide 11: Basic Architecture: State + processing elements
control
ALU/processing
state
Opcode selector
op = [+, -, x, /]
ALU
Input A
Input B
Output:
A op B
Reg 1
Reg 2
Reg 3
Reg 4
Register File

## Slide 12: Building up to our first architecture: ALU + Registers
Opcode select
op = [+, -, x, /]
Output register select
Input A register select Input B register select
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A
Register
Control
Input B Register Control

## Slide 13: Building up to our first architecture: ALU + Registers
Opcode select
op = [+, -, x, /]
Output register select
Input A register select Input B register select
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A
Register
Control
Input B Register Control
Stateful Elements plus control required to access them, providing inputs to operations and storing outputs of operations

## Slide 14: Building up to our first architecture: ALU + Registers
Opcode select
op = [+, -, x, /]
Output register select
Input A register select Input B register select
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A
Register
Control
Input B Register Control
Design choice – how many stateful elements / registers do we support?
Need to activate control logic to select right register for a particular operation. How?
Registers are named & explicit. Implication of explicit names?

## Slide 15: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Instruction gets decoded into signals that control the other parts of the system (more on encoding / decoding in a few slides)

## Slide 16: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Instruction memory holds all of the bits of all of the instructions that we might ever use to control other units.
Design choice: Need to think about where we put this memory (and its hierarchy of caches)

## Slide 17: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Instruction fetch logic refers to PC, loads instruction from instruction memory and sends to decode.
Design choices: how much to fetch at once?
What to fetch next (not always obvious)?

## Slide 18: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Remember our fetch optimization from last time? That would go here. Specialized instruction memory access logic. (Physical memory may be the same, though)

## Slide 19: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Sequential Control:
Each cycle, update the PC by adding 4.
Implication for software of our current design?

## Slide 20: Building up to our first architecture: Control
Input A
Input B
ALU
Output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register
Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
Out reg select
4
+
Decoding a fetched operation breaks it from a blob of bits into a set of signals that we can use to configure the rest of the units in this diagram
Key Idea: What we encode here has implications for other units and software layers above the instruction definition level.
Mechanism of decoding and content of encoded/decoded instructions are orthogonal concepts. How? vs what?.

## Slide 21: Building up to our first architecture: Memory
Reg 1
Reg 2
Reg 3
Reg 4
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory
Unit
Op select
op = [ld,st]
Data
Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register Control
Input A Register Control
Input B Register Control
Memory Unit
ld: data
Data Memory
st: data
ld/st: address

## Slide 22: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Decoded instruction now needs to select: ALU op or Mem op?

## Slide 23: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Here: address assumed to come from register directly

## Slide 24: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Reality: ALU may crunch reg vals to generate address
Address mode bits from decoded instruction
Address bits from register

## Slide 25: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Design choice:
How many ways do we have to compute an address? How many ways should we have?
Guess at implications of more ways?
Address mode bits from decoded instruction
Address bits from register

## Slide 26: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
state

## Slide 27: Building up to our first architecture: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Are register files and memory two varieties of the same basic thing?

## Slide 28: Building up to our first architecture: Branching
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC Source Select
PC+4
+

## Slide 29: Building up to our first architecture: Branching
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
4
+
Input A Input B
Register Register
Control Control
In A reg select In B reg select
Register File
Input A Input B Reg 1
Output Reg 2
Op select Register
op = [+, -, x, /] ALU Control Reg 3
Out reg select ALU: output C Reg 4
Op select Memory ld: data st: data
op = [ld,st] Unit ld/st: address
Data Memory
Branch Target Address Offset
MUX
PC Source Select
PC+4
PC
If PC Source Select not asserted PC=PC+4
If PC Source Select asserted PC=PC+off
+
Program
Memory

## Slide 30: Building up to our first architecture: Branching
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC Source Select
PC+4
+
Where does our branch target offset originate?
Alternative design choices? How are each of those used in code?

## Slide 31: Building up to our first architecture: Branching
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC Source Select
PC+4
+
How do we decide taken vs. not
taken via PC Source Select?

## Slide 32: Building up to our first architecture: Branching
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
Branch: PC Source Select
Design Choice:
ALU output determines PC source select when branch condition evaluates Alternative Design?

## Slide 33: A Complete (but slightly messy) RISCV-ish Datapath
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+

## Slide 34: A “single-cycle” design
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+
Clock

## Slide 35: A “single-cycle” design
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+
Clock
Key Idea:
Single-cycle design goes from reading an instruction out of memory all the way to writing results back to registers before the next clock edge.

## Slide 36: Thinking about latency: ALU Operations
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Address mode bits from decoded instruction
Address bits from register
ALU Operation Latency:
Circuit delay of ALU operations is (mostly) low.
Why?
Program Counter(PC)
4
+
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+

## Slide 37: Thinking about latency: ALU Operations
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Address mode bits from decoded instruction
Address bits from register
ALU Operation Latency:
Circuit delay of ALU operations is (mostly) low.
Sum of delay of 5 or 6 units depending on impl.
Need to fetch, decode, register access (in 1), reg access (in 2), ALU function, register writeback
Program Counter(PC)
4
+
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+

## Slide 38: Thinking about latency: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Address mode bits from decoded instruction
Address bits from register
Memory Latency:
Memory accesses are pretty slow. Why?
Program Counter(PC)
4
+
Branch Target Address Offset
MUX
Branch: PC Source Select
PC+4
+

## Slide 39: Thinking about latency: Memory
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Address mode bits from decoded instruction
Address bits from register
Sum of delay of 7 or 8 units depending on counting Need to fetch, decode, register access (addr part 1), reg access (addr part 2), alu (addr gen), memory unit, memory bank, register write
Program Counter(PC)
4
+
Branch Target Address Offset
Memory Latency – Critical Path:
Memory accesses are pretty slow in our datapath.
MUX
Branch: PC Source Select
PC+4
+

## Slide 40: Implication of operation latencies?
Single-cycle design means that the cycle time for the system is
defined by the latency of the longest-latency operation
In our case, that would be the memory latency (and ALU latency has some slack from the cycle time)
If every operation is not a memory operation, then we have over- provisioned the cycle time of the system

## Slide 41: Where is the HW/SW Interface in the Datapath?
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
Branch: PC Source Select

## Slide 42: Where is the HW/SW Interface?
Input A
Input B
ALU
ALU: output C
Reg 1
Reg 2
Reg 3
Reg 4
Register File
Output Register
Control
Input A Register Control
Input B Register Control
Instruction
Memory
Instruction Decode
Instruction
Fetch
Program Counter(PC)
In A reg select In B reg select
Op select
op = [+, -, x, /]
Out reg select
4
+
Memory Unit
Op select
op = [ld,st]
ld: data
Data Memory
st: data
ld/st: address
Branch Target Address Offset
MUX
PC+4
+
This is where software begins!
Branch: PC Source Select

## Slide 43: Instruction memory holds software
Instruction
Decode
Instruction
Fetch
???

## Slide 44: Big Idea: Instruction Bits are Control Signals
Instruction
Decode
Instruction
Fetch
Input Register 1
Input Register 2
Output Register
Operation Type
PC Source Select
Jump Target
…

## Slide 45: Big Idea: Instruction Bits are Control Signals
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00001000 | 00001001 | 00000001

## Slide 46: Big Idea: Instruction Bits are Control Signals
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Binary encoded: signals
directly interface to datapath
Reg 1
Reg 2
Reg 3
Reg 4
x

## Slide 47: Instruction Set Architecture
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Binary encoded: signals
directly interface to datapath
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA defines the architecture of the machine
Any implementation of the architecture must support the features exposed through the ISA (why?)

## Slide 48: Architecture vs. Microarchitecture
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA defines the architecture of the machine
A microarchitecture implements the features of the architecture

## Slide 49: Architecture vs. Microarchitecture
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA defines the architecture of the machine
A microarchitecture implements the features of the architecture
Architecture:
Register-register ALU ops, registers numbering 0-4
Microarchitecture:
One ALU containing a multiplier,
physical register file with registers numbering 0-3
ALU
x

## Slide 50: Architecture vs. Microarchitecture
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 1
Reg 2
Reg 3
Reg 4
+
For a given architecture there are many perfectly good microarchitectural implementations
Architecture:
Register-register ALU ops, registers numbering 0-4
x
Microarchitecture:
One ALU containing an adder; multiply w/ iterated addition, physical register file with registers numbering 0-3
ALU

## Slide 51: Architecture vs. Microarchitecture
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Reg 2
Reg 1
Reg 3
Reg 4
+
For a given architecture there are many perfectly good microarchitectural implementations
Architecture:
Register-register ALU ops, registers numbering 0-4
x
Microarchitecture:
One ALU containing an adder; multiply w/ iterated addition, physical register file with registers numbering 0-3
ALU
SRAM Bank #1 SRAM Bank #2
Register File
Microarchitecture:
Two SRAM banks storing regs based on parity
Architecture:
Sequentially-numbered, general-purpose registers

## Slide 52: Instruction Set Architecture
Instruction
Decode
Instruction
Fetch
Input Register 1 | Input Register 2 | Output Register | Operation Type
00000100 | 00000011 | 00000010 | 00000001
Register r4 | Register r3 | Register r2 | Multiply
Binary encoded: signals
directly interface to datapath
Reg 1
Reg 2
Reg 3
Reg 4
x
The ISA is the vocabulary of the machine
The ISA/vocabulary determines the types of programs/sentences that it is possible to write

## Slide 53: What should go in the ISA?
Reduced Instruction Set Computer
Simple primitives:
Let software compose complex operations
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Complex Instruction Set Computer
Simple & complex operations:
Hardware provides complex functionality
Many operations:
Often several ways to do the same thing
Register and memory operands:
Operations may directly manipulate memory

## Slide 54: What should go in the ISA?
Reduced Instruction Set Computer
Simple primitives:
Let software compose complex operations
Complex Instruction Set Computer
Simple & complex operations:
Hardware must support complex functionality
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Register and memory operands:
Operations may directly manipulate memory
Many operations:
Often several ways to do the same thing
Many cases to map to control signals in microarchitecture
rd = M[imm] rd = M[reg]
rd = M[reg + imm] rd = M[PC + imm]
Plus all of these combinations
Few cases to map to control signals in microarchitecture

## Slide 55: What should go in the ISA?
Reduced Instruction Set Computer
Complex Instruction Set Computer
Simple primitives:
Let software compose complex operations
Register operands:
Decouple functionality from memory accesses
Few total operations:
Usually only one way to do something
Simple & complex operations:
Hardware must support complex functionality
Register and memory operands:
Operations may directly manipulate memory
Many operations:
Often several ways to do the same thing
What are the pros and cons of each?
How does RISC vs. CISC affect the microarchitecture,
compiler, program, programmer?

## Slide 56: Principles of ISA Design
General Principles
Regularity – “Law of least astonishment”
Orthogonality – keep separable concerns separate Composability – regular, orthogonal ops combine easily
Specific Principles
One vs. All – precisely one way to do it, or all ways should be possible
Primitives, not solutions – solve by coding, compiling, & synthesizing
“Blatant opinions” (matters of taste)
Addressing – not limited to simple arrays, etc.
Environment Support – exceptions, processes, debugging, etc
Deviations – deviate from these rules only in implementation-specific ways

## Slide 57: What did we just learn?
Computer architectures define the HW/SW interface through the ISA
There is a difference between architecture and microarchitecture
Many valid microarch. implementations of an architecture exist
RISC vs. CISC architectures are extrema on a spectrum
Principles of ISA design (Wulf)

## Slide 58: What to think about next?
The basics of the RISCV-RV32I ISA and some other hw/sw interfaces
More microarchitectural concepts
  Pipelining our microarchitecture & instruction-level parallelism
  Control hazards & branch prediction