## Slide 1
Fall 2025
Lecture 7: Caches and the Memory Hierarchy
Credit: Brandon Lucia

## Slide 2: Today: Caches and the Memory Hierarchy
Introduction to caches and cache organization
Caches in the memory hierarchy
Cache implementation choices
Cache hardware optimizations
Software-managed caches & scratchpad memories

## Slide 3: Memory is a big list of M bytes
Byte 2
Byte 1
Byte 0
. . .
Byte M
Fetch
Decode
Execute
Memory
Register Write-Back
lw x6 0xC
. . .
Byte 0xF Byte 0xE Byte 0xD Byte 0xC

## Slide 4: Memory is conceptually far away from CPU
Byte 2
Byte 1
Byte 0
. . .
Byte M
lw x6 0xC
. . .
Byte 0xF Byte 0xE Byte 0xD Byte 0xC
Memory
Unit
Read Data C
Cont. Sigs.: Op. Select [Ld/St]
Memory
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
What does this “distance” entail for a
hardware / software interface?

## Slide 5: Memory is conceptually far away from CPU
Byte 2
Byte 1
Byte 0
. . .
Byte M
lw x6 0xC
. . .
Byte 0xF Byte 0xE Byte 0xD Byte 0xC
Memory
Unit
Read Data C
Cont. Sigs.: Op. Select [Ld/St]
Memory
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
What does this “distance” entail for a hardware / software
interface?
Need to be judicious with lw & sw
Compiler & programmer must carefully lay out memory
Worth spending hardware resources to optimize
Need hardware and software to co-optimize data re-use
Data movement is a fundamental limit on speed & energy

## Slide 6: Memory hierarchy: large & slow vs. small & fast
Byte 2
Byte 1
Byte 0
. . .
Byte M
lw x6 0xC
. . .
Byte 0xF Byte 0xE Byte 0xD Byte 0xC
Memory
Unit
Read Data C
Cont. Sigs.: Op. Select
[Ld/St]
Memory
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
Byte M2
Byte M1
Capacity inversely proportional to access cost
M > M3 > M2 > M1
L1D$
LL11II$$
L3$
Byte M3
L2$
Byte I1

## Slide 7: Recall: Memory Hierarchy from 18x13
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(SSD/Disk)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers.
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 8: Recall from 18x13: The Working Set
The data that is presently being use is called the Working Set.
Imagine you are working on 18x13. Your working set might include:
  The lab handout
  A terminal window for editing
  A terminal window for debugging
  A browser window for looking up man pages
If you changed tasks, you’d probably hide those windows and open new ones
The data computer programs use works the same way.

## Slide 9: Recall from 18x13: Guesstimating the Working Set
How does the memory system (cache logic) know the working set?
  This is tricky. There is no way it can really know what data the program needs or will need soon.
  It could even be totally dynamic, based upon input.
It approximates it using a simple heuristic called locality:
  Temporal locality: Data used recently is likely to be used again in the near future (local in time).
  Spatial locality: Data near the data used recently is likely to be used soon (local in space, e.g. address space).
The memory system will bring and keep the Most Recently Used (MRU) data and data near it in memory to the higher layers while evicting the Least Recently Used (LRU) data to the lower layers.

## Slide 10: What’s New Since 18x13?
We want to think about a cache built natively in real hardware vs a software simulation of a cache
The 18x13 cache was a software simulation of a somewhat ideal LRU cache
Consider how you built an LRU cache simulator in 18x13:
  A linked list- based queue?
  A copy-to-shift array-based queue?
Time for the “18-240 Thinking Cap”: Consider the implementation of LRU in hardware
  Can the 18x13 approach be translated to real hardware in a practical way?

## Slide 11: Locality is the key to cache performance
Spatial Locality
Temporal Locality
Why do we see locality? What are some examples of each?

## Slide 12: Memory hierarchy: Unified vs. Split ICache & DCache
Byte 2
Byte 1
Byte 0
. . .
Byte M
lw x6 0xC
. . .
Byte 0xF Byte 0xE Byte 0xD Byte 0xC
Memory
Unit
Read Data C
Cont. Sigs.: Op. Select
[Ld/St]
Memory
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
Byte M2
Byte M1
L1 Instruction & L1 Data cache often separate (why?)
Lower levels of cache are unified (why?)
L1D$
LL11II$$
L3$
Byte M3
L2$
Byte I1

## Slide 13: Review: Anatomy of a set-associative cache
L3$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
Valid | Dirty | Tag | B bytes data
Anatomy of a Line
Typical Parameters
Line contains 16-64 bytes of data
1-8 number of sets
1 set contains all lines? All sets contain 1 line? Total size varies by level: L1: 1kB – 32kB
L3: a few kB – 48MB

## Slide 14: Review: Accessing the cache
L3$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
Valid | Dirty | Tag | 32 bytes data
Total cache size = 32B x 4 sets x 4 ways = 512B
Step 1: Partitioning the address
lb x6 0x7fff0053
set index
0x01111111111111110000000001010011
tag bits
block offset

## Slide 15: Review: Accessing the cache
L3$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
Step 2: Select the set
lb x6 0x7fff0053
set index
0x01111111111111110000000001010011
tag bits
block offset
set 2

## Slide 16: Review: Accessing the cache - Hit
L3$L3$
Set 1 Set 0
Set 2
Set 3
Way 0 Way 1 Way 2 Way 3
Line
Step 3: Check valid, compare tags
lb x6 0x7fff0053
tag bits
block offset
1,0,0x7fff10,…
Valid | Dirty | Tag | 32 bytes data
1,0,0x000000,…
1,1,0x001e00,…
1,1,0x7fff00,…
Tag match, valid
set index
0x01111111111111110000000001010011

## Slide 17: Review: Accessing the cache - Hit
LL33$$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
1,1,0x7fff00,…
Memory Unit
Read Data C
Cont. Sigs.: Op. Select
[Ld/St]
Memory
MUX
MUX
Addr Reg A
WB/Mem Fwd
MUX
Data Reg B
WB/Mem Fwd
Cache
Controller
0x01111111111111110000000001010011
block offset
= byte 19
lb
Single Byte of Data @ 0x7fff0053
Step 4: Fetch cache block for memory unit via cache controller

## Slide 18: Review: Accessing the cache - Miss
L3$L3$
Set 1 Set 0
Set 2
Set 3
Way 0 Way 1 Way 2 Way 3
Line
Step 3: Check valid, compare tags
lb x6 0x7fff0053
set index
0x01111111111111110000000001010011
tag bits
block offset
1,0,0x7fff10,…
Valid | Dirty | Tag | 32 bytes data
1,0,0x000000,…
1,1,0x001e00,…
0,1,0x7fff00,…
No tag match, or invalid

## Slide 19: Review: Accessing the cache - Miss
L3$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
1,0,0x7fff00,…
ache ontroller
0011
fset
9
Byte 2
Byte 1
Byte 0
. . .
Byte M
. . .
32 Byte Block
@ 0x7fff0000

## Slide 20: Review: Accessing the cache - Miss
LL33$$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
1,0,0x7fff00,…
Memory Unit
Read Data C
Cont. Sigs.: Op. Select
[Ld/St]
Memory
MUX
MUX
Addr Reg A
WB/Mem Fwd
MUX
Data Reg B
WB/Mem Fwd
Cache
Controller
0x01111111111111110000000001010011
block offset
= byte 19
lb
Single Byte of Data @ 0x7fff0053
Step 5: Fetch cache block for memory unit via cache controller

## Slide 21: Why do we miss in the cache?

## Slide 22: Why do we miss in the cache?
The 3 C’s of misses
  Compulsory
  Conflict
  Capacity

## Slide 23: Why miss? Compulsory misses
First access to any block of memory is always a miss; these misses are compulsory

## Slide 24: Why miss? Capacity misses
Working set of program contains more data than can be cached at one time.
By the pigeonhole principle caching all data requires missing at least once

## Slide 25: Why miss? Conflict misses
Multiple blocks of memory map to the same location in the cache and conflict, even if there is still some empty space in the cache
L3$

## Slide 26: How many bits in tag/index/offset?
L3$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
Valid | Dirty | Tag | 32 bytes data
Total cache size = 32B x 4 sets x 4 ways = 512B
lb x6 0x7fff0053
set index
0x01111111111111110000000001010011
tag bits
block offset
Why these numbers of bits?

## Slide 27: How many bits in tag/index/offset?
L3$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
Valid | Dirty | Tag | 32 bytes data
Total cache size = 32B x 4 sets x 4 ways = 512B
lb x6 0x7fff0053
set index
0x01111111111111110000000001010011
tag bits
block offset
Enough block offset bits to count block bytes Enough set index bits to count the sets
All left-over bits are tag bits
Question: what do tag bits mean?

## Slide 28: How many sets should your cache have?
L3$L3$
Set 1 Set 0
Set 2
Set 3
Way 0 Way 1 Way 2 Way 3
Line
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,1,0x7fff00,…
#Ways parallel tag matches per lookup
Set Associative Cache Design Procedure
Select total cache size
Select implementable #ways
cache size = #sets x #ways x #block_bytes
4.#sets = cache size / (#ways x #block_bytes)
What is an implementable # of ways?

## Slide 29: What is an implementable # ways?
L3$L3$
Set 1 Set 0
Set 2
Set 3
Way 0 Way 1 Way 2 Way 3
Line
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,1,0x7fff00,…
n-way set associative cache:
Need n parallel comparators for tag match

## Slide 30: What is an implementable # ways?
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,1,0x7fff00,…
Fully-associative cache:
# comparators = # lines in entire cache
L3$
Line

## Slide 31: What is an implementable # ways?
L3$
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,1,0x7fff00,…
Direct mapped cache:
1 comparator because each set
contains a single line

## Slide 32: Physical implementation separates data & tags
L3$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
0x01111111111111110000000000010011
tag bits
set index
block offset
L3$
Set 0
Set 1
Set 2
Set 3
tag 1
tag 2
tag 3
Way 0
Way 1
Way 2
Way 3
tag 0
Cache Data Array
Cache Tag Array

## Slide 33: Sequential Tag Lookup & Data Lookup
L3$
Set 0
Set 1
Set 2
Way 0
Way 1
Way 2
Way 3
Line
0x01111111111111110000000000010011
tag bits
set index
block offset
L3$
Set 0
Set 1
Set 3
Set 3 Set 2
tag 1
tag 2
tag 3
Way 0
Way 1
Way 2
Way 3
tag 0
Cache Data Array
Cache Tag Array
Sequentially access tag array first, then access the data array using the result of the tag lookup.
Question: Can you think of an alternative scheme to optimize tag/data lookup?
2-bit way select
2-bit set
select
2-bit set
select
4-bit block select

## Slide 34: Parallel Tag Lookup & Data Lookup
L3$
Set 0
Set 1
Set 2
Way 0
Way 3
Line
0x01111111111111110000000000010011
tag bits
set index
block offset
L3$
Set 0
Set 1
Set 3
Set 3 Set 2
tag 1
tag 2
tag 3
Way 0
Way 1
Way 2
Way 3
tag 0
Cache Data Array
Cache Tag Array
Fetch all ways in set in parallel with tag matching and use the way index of tag to select the one data block that was fetched.
Question: Pros & cons of parallel lookup?
Block Select
2-bit way
select
2-bit set select

## Slide 35: Way Prediction: Cost Like Sequential, Performance
Like Parallel Tag Lookup
L3$
Set 0
Set 1
Set 2
Way 1
Way 0 Way 2 Way 3
Line
0
x01111111111111110000000000010011
tag bits
set index
block offset
L3$
Set 0
Set 1
Set 3
Set 3 Set 2
tag 1
tag 2
tag 3
Way 0
Way 1
Way 2
Way 3
tag 0
Cache Data Array
Send some tag bits and set index bits to fast way predictor, output of which is 4-bit block select, like in sequential. Fetch way of matched tag and send to prediction validation logic. If correct predict: use block. If incorrect predict: discard block and refetch.
Cache Tag Array
2-bit
way
select
2-bit set
select
2-bit set select
4-bit block select
way
predictor
Prediction validator
?

## Slide 36
Moritz Lipp, Vedad Hadžić, Michael Schwarz, Arthur Perais, Clémentine Maurice, and Daniel Gruss. 2020. Take A Way: Exploring the Security Implications of AMD's Cache Way Predictors. In Proceedings of the 15th ACM Asia Conference on Computer and Communications Security (ASIA CCS '20). Association for Computing Machinery, New York, NY, USA, 813–825. https://doi.org/10.1145/3320269.3384746

## Slide 37: Cost of Associativity
Read Latency = 83.4307ps
Tag Read Latency = 293.516ps Write Latency = 83.1343ps
Tag Write Latency = 226.518ps
Read Bandwidth = 480.942GB/s Write Bandwidth = 500.715GB/s
Tag Read Dynamic Energy = 1.01651pJ Tag Write Dynamic Energy = 0.758075pJ
$ ./destiny config/SRAM_512_1_256.cfg
$ ./destiny config/SRAM_512_4_256.cfg
Read Latency = 55.4943ps Tag Read Latency = 277.84ps Write Latency = 54.7831ps
Tag Write Latency = 212.575ps
Read Bandwidth = 674.493GB/s Write Bandwidth = 633.944GB/s
Tag Read Dynamic Energy = 0.281324pJ Tag Write Dynamic Energy = 0.222833pJ
512 Bytes, 256-bit (32B) lines, 4-way
512 Bytes, 256-bit (32B) lines, 1-way
Higher associativity avoids conflict misses at an additional cost in hit latency & energy

## Slide 38
Write Policies - Allocation
Byte 2
Byte 1
Byte 0
Byte M
. . . . . .
sb x6 0x7fff0053
Memory
Unit
Read
Data C
Cont. Sigs.: Op. Select
[Ld/St]
Memory
MUX
MUX
Addr Reg A
WB/Mem Fwd
MUX
Data Reg B
WB/Mem Fwd
LL33$$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
Write-Allocate: Stores go to cache
Write-No-Allocate: Stores do not go to cache
?

## Slide 39: Write Policies - Propagation
Byte 2
Byte 1
Byte 0
. . . . . .
Byte M
sb x6 0x7fff0053
Memory
Unit
Read
Data C
Cont. Sigs.: Op. Select [Ld/St]
Memory
MUX
MUX
Addr Reg A
WB/Mem Fwd
MUX
Data Reg B
WB/Mem Fwd
LL33$$ |  | Way 0 | Way 1 | Way 2 | Way 3 |  | 
 | Set 0 | Line |  |  |  |  | 
 | Set 1 |  |  |  |  |  | 
 | Set 2 |  |  |  |  |  | 
 | Set 3 |  |  |  |  |  | 
Write-Back: Wait until line evicted to writeback Write-Through: Writeback immediately on store
When?

## Slide 40: Recall 18x13: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
a: 2
E
b:200
E
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 41: Recall 18x13: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
a: 2
E
b:200
E
print 200
b:200
S
b:200
S
print 2
a:2
S
a: 2
S
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
When cache sees request for one of its E-tagged blocks
  Supply value from cache (Note: value in memory may be stale)
  Set tag to S

## Slide 42: Recall 18x13: Typical Multicore Processor
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core n-1
…
L3 unified cache
(shared by all cores)
Main memory
Propagation Policy v. Multicore Cache Coherency
What is required for a snooping?
How does propagation policy facilitate or impede this?
What does this suggest about cache policy by level?

## Slide 43: Cache Hierarchy Performance Measurement

## Slide 44: Average Memory Access Time (AMAT): Measuring the performance of a memory hierarchy
Byte 2
Byte 1
Byte 0
. . .
Byte M
lw x6 0xC
. . .
Byte 0xF Byte 0xE Byte 0xD Byte 0xC
Memory
Unit
Read Data C
Cont. Sigs.: Op. Select
[Ld/St]
Memory
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
Byte M2
Byte M1
Compute the time taken by the average access based on miss rate, hit latency, and miss penalty at each level
L1D$
LL11II$$
L3$
Byte M3
L2$
Byte I1

## Slide 45: Average Memory Access Time (AMAT): Measuring the performance of a memory hierarchy
Byte 1
Byte 0
Byte 2
. . .
7.5ns
Latency
lw x6 0xC
. . .
Byte 0xF Byte 0xE Byte 0xD Byte 0xC
Memory
Unit
Read Data C
Cont. Sigs.: Op. Select [Ld/St]
Memory
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
Compute the time taken by the average access based on miss rate, hit latency, and miss penalty at each level
L1$
L2$
L3$
Miss rate = 0.1 Access time = 322ps Miss time = 305ps
1MB,
8way
4kB,
4way
64kB,
8way
Miss rate = 0.02 Access time = 461ps Miss time = 395ps
Miss rate = 0.01 Hit time = 1.28ns Miss time = 485ps

## Slide 46: Average Memory Access Time (AMAT): Measuring the performance of a memory hierarchy
Byte 1
Byte 0
Byte 2
. . .
lw x6 0xC
. . .
Byte 0xF Byte 0xE Byte 0xD Byte 0xC
Memory
Unit
Read Data C
Cont. Sigs.: Op. Select [Ld/St]
Memory
MUX
MUX
WB/Mem Fwd
Mem/Mem Fwd Addr Reg A
MUX
WB/Mem Fwd
Mem/Mem Fwd
Data Reg B
AMAT = L1HitRate x L1AccTime + L1MissRate x ( L1MissTime + L2HitRate x L2AccTime + L2MissRate x ( L2MissTime + L3HitRate x L3AccTime + L3MissRate x ( L3MissTime +
DRAM Latency ) ) )
L1$
L2$
L3$
Miss rate = 0.1 Access time = 322ps Miss time = 305ps
1MB,
8way
4kB,
4way
64kB,
8way
Miss rate = 0.02 Access time = 461ps Miss time = 395ps
Miss rate = 0.01 Hit time = 1.28ns Miss time = 485ps
7.5ns
Latency

## Slide 47: Computing the AMAT 1/2/4/23 90% hits
Miss rate = 0.1 Access time = 322ps (1 cycle @ 3GHz) Miss time = 305ps
Miss rate = 0.02 Access time = 461ps (2 cycles @ 3GHz) Miss time = 395ps
Miss rate = 0.01 Hit time = 1.28ns (4 cycles @ 3GHz) Miss time = 485ps
0.322ns x 0.9 + 0.1 x (0.305ns +
0.461ns x 0.98 + 0.02 x (0.395ns +
1.28ns x 0.99 + 0.01 x (0.485ns +
7.5ns) ) )
DRAM Latency
7.5ns (CAS latency) (23 cycles @ 3GHz)
1 x 0.9 + 0.1 x (1 +
2 x 0.98 + 0.02 x (2 +
4 x 0.99 + 0.01 x (2 +
23) ) )
AMAT in Seconds
AMAT in Cycles

## Slide 48: Computing the AMAT
Miss rate = 0.1 Access time = 322ps Miss time = 305ps
Miss rate = 0.02 Access time = 461ps Miss time = 395ps
Miss rate = 0.01 Hit time = 1.28ns Miss time = 485ps
DRAM Latency
7.5ns (CAS latency)
cycles

## Slide 49: Computing the AMAT – 2/5/10/30 90% hits
Miss rate = 0.1
Access time = 2 cycles Miss time = 2 cycles
Miss rate = 0.02 Access time = 5 cycles Miss time = 5 cycles
Miss rate = 0.01
Hit time = 10 cycles Miss time = 10 cycles
DRAM Latency
30 cycles
AMAT in cycles
2 x 0.9 + 0.1 x (2 +
5 x 0.98 + 0.02 x (5 +
10 x 0.99 + 0.01 x (10 +
30) ) ) = 2.52 cycles = 3 cycles

## Slide 50: Computing the AMAT – 2/5/10/30 80% hits
Miss rate = 0.2
Access time = 2 cycles Miss time = 2 cycles
Miss rate = 0.02 Access time = 5 cycles Miss time = 5 cycles
Miss rate = 0.01
Hit time = 10 cycles Miss time = 10 cycles
DRAM Latency
30 cycles
AMAT in cycles
2 x 0.8 + 0.2 x (2 +
5 x 0.98 + 0.02 x (5 +
10 x 0.99 + 0.01 x (10 +
30) ) ) = 3.04 cycles = 4 cycles = 2 x L1 latency!

## Slide 51: The ABCs of Optimizing a Cache

## Slide 52: Associativity vs. Block Size vs Cache Size
Associativity
Many complex inter-dependent factors determine cache performance
Associativity
Block Size
Cache Size
Replacement Policy
Write allocation policy
Write propagation policy
Best option depends on workload!
Factors will sometimes work against one another, where improving degrades another. (we will study this next week)

## Slide 53: Replacement Policies

## Slide 54: Replacement Policies
L3$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,0,0x7fff00,…
ache ontroller
0011
fset
9
Byte 2
Byte 1
Byte 0
. . .
Byte M
. . .
32 Byte Block
@ 0x7fff0000
Which block in the set should we
evict
to make space for the new block?

## Slide 55: Replacement Policies – Round Robin
L3$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,0,0x7fff00,…
ache ontroller
0011
fset
9
Byte 2
Byte 1
Byte 0
. . .
Byte M
. . .
32 Byte Block
@ 0x7fff0000
Evict
Next

## Slide 56: Replacement Policies – Round Robin
L3$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,0,0x7fff00,…
ache ontroller
0011
fset
9
Byte 2
Byte 1
Byte 0
. . .
Byte M
. . .
32 Byte Block
@ 0x7fff0000
Evict
Next

## Slide 57: Replacement Policies – Round Robin
L3$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,0,0x7fff00,…
ache ontroller
0011
fset
9
Byte 2
Byte 1
Byte 0
. . .
Byte M
. . .
32 Byte Block
@ 0x7fff0000
Evict
Next

## Slide 58: Replacement Policies – Round Robin
L3$
Set 0
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,0,0x7fff00,…
ache ontroller
0011
fset
9
Byte 2
Byte 1
Byte 0
. . .
Byte M
. . .
32 Byte Block
@ 0x7fff0000
Evict
Next

## Slide 59: Replacement Policies – Round Robin
L3$
Set 1
Set 2
Set 3
Way 0
Way 1
Way 2
Way 3
Line
lb x6 0x7fff0053
1,0,0x7fff10,…
1,0,0x000000,…
1,1,0x001e00,…
0,0,0x7fff00,…
ache ontroller
0011
fset
9
Byte 2
Byte 1
Byte 0
. . .
Byte M
. . .
32 Byte Block
@ 0x7fff0000
Set 0
Evict
NNeexxtt

## Slide 60: Replacement Policies – Round-Robin Analysis
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa
Set 0
b
a
c
d
Evict Next
Advantage: Simple to implement and understand
Disadvantage: Hopefully the next to evict isn’t going to be the next to be accessed…

## Slide 61: Replacement Policies – Round-Robin Analysis
Set 0
e
a
c
d
Evict
Next
Advantage: Simple to implement and understand
Disadvantage: Hopefully the next to evict isn’t going to be the next to be accessed…
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa

## Slide 62: Replacement Policies – Round-Robin Analysis
Set 0
e
a
b
d
Evict
Next
Advantage: Simple to implement and understand
Disadvantage: Hopefully the next to evict isn’t going to be the next to be accessed…
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa

## Slide 63: Replacement Policies – Round-Robin Analysis
Set 0
e
a
b
c
Evict Next
Advantage: Simple to implement and understand
Disadvantage: Hopefully the next to evict isn’t going to be the next to be accessed…
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa

## Slide 64: Replacement Policies – Round-Robin Analysis
Set 0
e
d
b
c
Evict Next
Advantage: Simple to implement and understand
Disadvantage: Hopefully the next to evict isn’t going to be the next to be accessed…
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa

## Slide 65: Replacement Policies – Round-Robin Analysis
Set 0
a
d
b
c
Evict
Next
Advantage: Simple to implement and understand
Disadvantage: Hopefully the next to evict isn’t going to be the next to be accessed…
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa

## Slide 66: Minimum Number of Misses?
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa
Set 0
b
a
c
d
What is the best replacement strategy to minimize misses & why?

## Slide 67: Minimum Number of Misses?
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa
Set 0
b
a
c
d
Evict
Next

## Slide 68: When are we going to re-use cached data?
lb | x6 | 0xe
lb | x6 | 0xb
lb | x6 | 0xc
lb | x6 | 0xd
lb | x6 | 0xa
Set 0
b
e
c
d
Miss Hit
Hit
Hit Miss
Replacement decisions must be informed by the next reuse of a block of data.
Think: what is an optimal policy? How far in the future is something going to be used again?

## Slide 69: What did we just learn?
Memory has a high access cost; memory hierarchy mitigates that cost
Caches make locality exploitable to optimize for data reuse
Review of the basics of cache operation, address decomposition, set associative caches
Miss types
The costs of associativity & tag storage arrays
What to do about writes?
The replacement problem

## Slide 70: What to think about next?
More caches (next time)
  Replacement from the ground up
  Caching optimizations: victim caches, write buffers & lockup-free caches, prefetching, way partitioning, banking & bank conflicts
  Scratchpads vs. Caches & their relation to the HW/SW interface
Performance Evaluation (next next time)
  Design spaces, Pareto Frontiers, and design space exploration
Miscellaneous (micro)architectural tricks & optimizations (future)
  Vector processors, SIMD/SIMT, dataflow

## Slide 71: What to think about next?
Caches as a microarchitectural optimization (next time)
  Implementation of cache hierarchies
  Cache design tradeoffs
Performance Evaluation (next next time)
  Design spaces, Pareto Frontiers, and design space exploration
Miscellaneous (micro)architectural tricks & optimizations (future)
  Vector processors, SIMD/SIMT, dataflow