## Slide 1: CMU 18-344: Computer Systems and the Hardware/Software Interface
Fall 2023
(Fall 2026 Lecture 2)
LECTURE 2

## Slide 2: What is the hardware/software boundary?
An ISA or Computer Architecture?
A division of labor between Computer Engineers and Programmers?
A split between what you can change and what you cannot change?
Python vs. Verilog?

## Slide 3: The 213 view of the world
ISA is the immutable
foundation of the system
High-level language compiles to ISA
Linux (or other) OS provides important low-level services
Low-level optimization: know HW structure to make smart code changes

## Slide 4: The 240 view of the world
What’s an ISA? (RISC-240 not withstanding)
SystemVerilog describes your hardware
What’s an OS? What is
*software* even?
Implement through simulation, ASIC fabrication or FPGA configuration

## Slide 5: Relative Mutability/Non-Recurring Eng. (NRE) Cost?

## Slide 6: Relative Observability?

## Slide 7: Relative Optimizability?

## Slide 8: Today: Thinking Like a Computer Architect

## Slide 9: Our first hw/sw interface: The Von Neumann Computing Model
Program
Data
Unified Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
John von Neumann’s Big Idea:
Programs are data.

## Slide 10: The Von Neumann / Stored-Program Computing Model
Program
Data
Unified Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Let’s optimize! Where is there a bottleneck in the Von Neumann abstract machine?

## Slide 11: The Von Neumann / Stored-Program Computing Model
Program
Data
Unified Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Data & Program share a bus into the CPU. Need to time multiplex access to the bus.

## Slide 12: The Von Neumann / Stored-Program Computing Model
Program
Data
Unified Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
I1: | x | = | y | + | z
I2: | a | = | b | * | c
I3: | r | = | s | + | t

## Slide 13: The Von Neumann / Stored-Program Computing Model
Program
Data
Unified Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
I1:
x
=
y
+
z
I2: a = b * c
I3: r = s + t
32bits
64bits
Need to
write 8 bytes output data, read 16 bytes bits input data, read 4 bytes instruction
per arithmetic operation

## Slide 14: The Von Neumann / Stored-Program Computing Model
Program
Data
8 byte unified bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
I1:
x
=
y
+
z
I2: a = b * c
I3: r = s + t
32bits
64bits
With a one word (8 byte) bus:
1 data write cycle,
2 data read cycles,
1 instruction read cycle
per arithmetic operation
4 cycles per instruction!

## Slide 15: Alternative to von Neumann: the Harvard Architecture
Program
Data
Instruction Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Data Bus
Split bus architecture provides simultaneous access to program and to data

## Slide 16: Alternative to von Neumann: the Harvard Architecture
Program
Data
Instruction Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Data Bus
I1:
x
=
y
+
z
I2: a = b * c
I3: r = s + t
32bits
64bits
With a one word (8 byte) bus:
data write cycle,
data read cycles, simultaneous with 1 instruction read cycle
per arithmetic operation
3 cycles per instruction!

## Slide 17: Optimizing our Harvard Architecture
Program
Data
Instruction Bus
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(1 read port, 1 write port)
I1:
x
=
y
+
z
I2: a = b * c
I3: r = s + t
32bits
64bits
With a one word (8 byte) bus:
1 data write cycle simultaneous with 2 data read cycles simultaneous with 1 instruction read cycle
per arithmetic operation
2 cycles per instruction!

## Slide 18: Optimizing our Harvard Architecture
Program
Data
Instruction Bus
(32-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1:
x
=
y
+
z
I2: a = b * c
I3: r = s + t
32bits
64bits
With a one word (8 byte) bus:
1 data write cycle simultaneous with 1 data read cycles simultaneous with 1 instruction read cycle
per arithmetic operation
1 cycle per instruction!

## Slide 19: Thinking about the costs of HW optimization
Program
Data
Instruction Bus
(32-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
Program
Data
Unified Bus
Memory
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data Manipulation (“ALU”)
Is this free?

## Slide 20
4-byte Memory Interface: Read Latency = 0.289ns Write Latency = 0.212ns
16-byte Memory Interface: Read Latency = 0.289ns Write Latency = 0.212ns
Program
Data
Unified Bus
Memory
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data Manipulation (“ALU”)
Program
Data
Instruction Bus
(32-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
$ ./destiny config/SRAM_128_1_32.cfg
$ ./destiny config/SRAM_128_1_128.cfg
Free Lunch!

## Slide 21
Program
Data
Unified Bus
Memory
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data Manipulation (“ALU”)
Program
Data
Instruction Bus
(32-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
$ ./destiny config/SRAM_128_1_32.cfg
$ ./destiny config/SRAM_128_1_128.cfg
4-byte Memory Interface: Read Energy = 0.836pJ Write Energy = 0.738pJ
16-byte Memory Interface:
Read Energy = 1.51pJ
Write Energy = 1.30pJ
There is No Free Lunch!

## Slide 22: How about optimizing instruction supply?
Program
Data
Instruction Bus
(32-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1: | x | = | y | + | z
I2: | a | = | b | * | c
I3: | r | = | s | + | t
I4: | q | = | n | + | m
128bits
These four instructions take four cycles to fetch sequentially on our instruction bus

## Slide 23: How about optimizing instruction supply?
Program
Data
Instruction Bus
(128-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1: | x | = | y | + | z
I2: | a | = | b | * | c
I3: | r | = | s | + | t
I4: | q | = | n | + | m
128bits
16 byte instruction bus:
1 instruction read cycle every 4 operations

## Slide 24: Is this optimization a good tradeoff?
Program
Data
Instruction Bus
(128-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1: | x | = | y | + | z
I2: | a | = | b | * | c
I3: | r | = | s | + | t
I4: | q | = | n | + | m
128bits
16 byte instruction bus:
1 instruction read cycle every 4 operations
4B Read Energy = 0.836pJ 16B Read Energy = 1.51pJ

## Slide 25: Is this optimization a good tradeoff?
Program
Data
Instruction Bus
(128-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1:
I2:
I3:
I4:
x = y + z a = b * c r = s + t q = n + m
128bits
16 byte instruction bus:
1 instruction read cycle every 4 operations
4x fewer instruction fetches
4B Read Energy = 0.836pJ
16B Read Energy = 1.51pJ
~2x more energy / fetch
E_old = n x EpF
E_new = (n/4) x (EpF x 2) = ½(n x EpF)
2x savings in total instruction fetch energy!

## Slide 26: Is this optimization a good tradeoff?
Program
Data
Instruction Bus
(128-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1: | x | = | y | + | z
I2: | a | = | b | * | c
I3: | r | = | s | + | t
I4: | q | = | n | + | m
128bits
16 byte instruction bus:
1 instruction read cycle every 4 operations
4x fewer instruction fetches
4B Read Energy = 0.836pJ
16B Read Energy = 1.51pJ
~2x more energy / fetch
When might this optimization *not* pay off?

## Slide 27: Is this optimization always a good tradeoff?
Program
Data
Instruction Bus
(128-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1:
I2:
I3:
I4:
if (x==0) a = b * c y = z + w q = n + m
128bits
1 instruction read cycle every 4 operations
4x fewer reads, if we execute the operations!
OR: 4x more useless fetching if x!=0
(more on this branching topic in a future lecture)
4B Read Energy = 0.836pJ
16B Read Energy = 1.51pJ
~2x more energy / fetch

## Slide 28: How about changing the code?
Program
Data
Instruction Bus
(128-bit read)
Memory
CPU
Control & Instruction
Sequencing (“Control”)
Arithmetic, Logic, and Data
Manipulation (“ALU”)
Dual-ported Data Bus
(2x64-bit read, 64-bit write port)
I1:
I2:
I3:
I4:
if (x==0) a = b * 2 y = z + w q = n + m
Restructure code, increase likelihood to execute
Avoid needless fetch of non-executing code
Q: What if x is most often non-zero?
I5: //else
I6: a = b * 4 I7: y = z + w I8: q = n + m
Compiler!
I1:
I2:
I3:
I4:
I5:
I6:
I7:
I8:
y = z + w q = n + m if (x==0) a = b * 2
//else
a = b * 4
//other
//stuff

## Slide 29: A key Law of the HW/SW Universe

## Slide 30: Amdahl’s Law
Let’s revisit the proposition that we should optimize instruction supply
How do we decide if this part of the system is really worth optimizing?

## Slide 31: Amdahl’s Law
100% of execution time

## Slide 32: Amdahl’s Law
100% of execution time
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
What can we say about optimizing instruction supply (fetch) if this is our situation?
Imagine we have a perfectly precise measurement
tool to break down execution time…

## Slide 33: Amdahl’s Law
100% of execution time
10 seconds
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
We have 45% + 20% + 17.5% + 5% = 87.5% of the execution running at its original speed (ie 87.5% of 10 seconds = 8.75s)
What if we make fetch 4x faster?
We have 12.5% of the execution running 4x faster. Originally, we had 12.5% of 10 units of time = 1.25s. If 4x faster, fetch takes 0.31s. Savings of 0.94s

## Slide 34: Amdahl’s Law
100% of execution time
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
(0.875 x 10)/1 + (0.125 x 10)/4 = 9.06
What does 0.906 mean?
What if we make fetch 4x faster?

## Slide 35: Amdahl’s Law
100% of execution time
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
4x improvement in fetch means execution takes 9.0625s instead of 10s Saved 0.94s overall. 0.94s / 10s * 100 = 9.4% time savings
What if we make fetch 4x faster?
<10% improvement overall, despite 4x improvement on one part of the system!

## Slide 36: Amdahl’s Law
100% of execution time
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
What if we make memory accesses 4x faster?

## Slide 37: Amdahl’s Law
100% of execution time
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
55% of 10s + (45% of 10s) / 4 = 6.625s
Evidently, we should optimize the memory part before fetch!
What if we make memory accesses 4x faster?

## Slide 38: Amdahl’s Law
100% of execution time
45% - Memory Accesses 20% - Control Flow 17.5% - Integer
Amdahl’s Law:
if fraction p can be optimized:
Optimized Time = [ (1-p) * t / 1 ] + [ (p * t) / speedup ]
12.5% - Fetch
5% - Floating
Point

## Slide 39: Amdahl’s Law
100% of execution time
45% - Memory Accesses
Amdahl’s Law:
Overall Speedup = ?
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point

## Slide 40: Amdahl’s Law
100% of execution time
45% - Memory Accesses
Amdahl’s Law:
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
Overall Speedup = T_orig / T_opt
Overall Speedup = 1 / (1 – p + p / s)

## Slide 41: Amdahl’s Law
100% of execution time
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
By how much do we have to improve the memory part of the system to get a 2x total speedup?

## Slide 42: Amdahl’s Law
100% of execution time
45% - Memory Accesses 20% - Control Flow
0.55 x 10s + (0.45 x 10s)/speedup = 10s / 2 = 5s
4.5s / speedup = 5s – 5.5s speedup = -9x
Well that’s a strange amount by which to speed up
a program… conclusion?
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
By how much do we have to improve the memory part of the system to get a 2x total speedup?

## Slide 43: Limit Cases for Amdahl’s Law
100% of execution time
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
Let’s try again:
What if we completely optimize away the optimizable part?

## Slide 44: Limit Cases for Amdahl’s Law
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
0% - Fetch
5% - Floating Point
What if we completely optimize away the optimizable part? (How much is left over here?)
100% of original execution time
IIddeeaallllyy ooppttiimmiizzeedd eexeex ccuuttiioonn ttiimmee

## Slide 45: Limit Cases for Amdahl’s Law
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
0% - Fetch
5% - Floating Point
What if we completely optimize away the optimizable part?
8.75s optimized execution time
100% of original execution time
IIddeeaallllyy ooppttiimmiizzeedd eexeex ccuuttiioonn ttiimmee

## Slide 46: Limit Cases for Amdahl’s Law
100% of original execution time
Ideally optimized execution time
20% - Control Flow 17.5% - Integer 12.5% - Fetch
5% - Floating Point
0% - Memory Accesses
What if we completely optimize away the memory part?
5.5s optimized execution time

## Slide 47: Limit Cases for Amdahl’s Law
100% of original execution time
Ideally optimized execution time
0% - Fetch
5% - Floating Point
45% - Memory Accesses 20% - Control Flow 17.5% - Integer
Amdahl’s Law:
optimized time = [ 1-p x time / 1.0 ] + [ p x time / s ] Overall speedup = 1 / (1 - p + p / s)

## Slide 48: Limit Cases for Amdahl’s Law
100% of original execution time
Ideally optimized execution time
45% - Memory Accesses 20% - Control Flow 17.5% - Integer
0% - Fetch
5% - Floating Point
Amdahl’s Law with infinite speedup:
optimized time with infinite speedup of p = [ 1-p x time / 1.0 ] Overall speedup with infinite speedup of p = 1 / (1 - p)

## Slide 49: Amdahl’s Law Speedup
optimizable
part (p)
Optimized speedup for optimizable part
>100x
optimized part speedup?
80%
optimizable? max speedup 5x!

## Slide 50: Amdahl’s Law is Extremely Versatile
100% of execution energy
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
Works for any optimization problem and goal. Always
focus on the biggest slice & the rest doesn’t matter.

## Slide 51: Using Amdahl’s Law to push the bottleneck around
100% of execution energy
45% - Memory Accesses
20% - Control Flow
17.5% - Integer
12.5% - Fetch
5% - Floating
Point
Bottleneck: memory accesses

## Slide 52: Using Amdahl’s Law to push the bottleneck around
100% of execution energy
Memory Accesses
Control Flow
Integer
Fetch
Floating Point
New bottleneck: control flow

## Slide 53: Using Amdahl’s Law to push the bottleneck around
100% of execution energy
Memory Accesses
Control Flow
Integer
Fetch
Floating
Point
New bottleneck: memory accesses (again!)

## Slide 54: Using Amdahl’s Law to push the bottleneck around
100% of execution energy
Memory Accesses
Control Flow
Integer
Fetch
Floating
Point
Remember: Amdahl tells us to optimize the biggest slice

## Slide 55: Another view of the world: Gustafson’s Law
85% - Memory Accesses
“The speedup we experience is equal to the amount of parallelization, except for the percentage of the problem which isn’t parallelizable and needs to be done sequentially”.
Gustafson’s Law says the scaled speedup S with P processors is:
S(P)=P−α⋅(P−1)
Where:
P = number of processors
α = fraction of time spent on the part of the program that is inherently sequential (cannot be parallelized)
Intuition:
Work tends to be time limited, and as we all know, work tends to fill the time.
So, for many problems, the amount of work we do grows alongside our ability to do it.
We need to judge the real-world impact by what we will do, not what we once did.

## Slide 56: Another view of the world: Gustafson’s Law
Gustafson’s Law: Sequential part does not grow as optimizable part grows. Can always add more optimizable part and make sequential part matter less
Assume that we can scale up # of parallel memory accesses, N
Assume we can scale input up to use all N parallel accesses
data_size = 10 data[data_size] = {…} if(…){ }
…//18 more of these conditionals if(…){ }
for d in 0..data_size{ d++ }
data_size = 100000 data[data_size] = {…} if(…){ }
…//18 more of these conditionals if(…){ }
#parallel[N=1000]
for d in 0..data_size{ d++ }
Gustafson!

## Slide 57: Another view of the world:
85% - Memory Accesses
Gustafson’s Law for overall speedup with speedup factor of N:
(assume) Optimized time = T = 1
Unoptimized time = T’ = (1-p)T + pT*N = (1-p) + pN
Scaled Speedup = T’ / T = (1-p) + pN
Scale parallel memory accesses, N, up to 1000? Scaled Speedup = 1-p + 1000p = 999p + 1 Scaled Speedup = 999 * 0.85 + 1 = 850x

## Slide 58: Amdahl’s Law vs Gustafson’s Law
4x
Parallelizable
1x (Not)
Parallelizable
1=1/4*4
4=1*4
16=4*4 units of work
4 units of work
Hold work constant
Scale time
Gustafson’s Law
Original Situation
8 units of time, 8 units of work
P=50%, NP=50%
What before took 8 units of time now takes 5 units of time
8/5x speedup = 1.6x speedup
Amdahl’s Law
Hold time constant
Scale work
Before we could do 8 units of work in 8 units of time
Now we can do 20 units of work in 8 units of time.
20/8x speedup – 2.5x speedup

## Slide 59: What did we just learn?
Two high-level architectural models
Identify performance bottlenecks
Develop optimizations to mitigate bottlenecks
Analyze resulting improvement from mitigating bottlenecks
Identifying persistent performance limiters (e.g., branches)
Optimize in software or hardware
(Almost) never bet against Gene Amdahl in an optimization contest!

## Slide 60: What to think about next?
What is a computer architecture?
What matters when defining a HW/SW interface?
What is above the ISA and what is below the ISA?
What is hidden from the programmer and what is exposed?