## Slide 1: 18-447 Computer Architecture Lecture 16: SIMD Processing (Vector and Array Processors)
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2014, 2/24/2014

## Slide 2: Lab 4 Reminder
Lab 4a out
  Branch handling and branch predictors
Lab 4b out
  Fine-grained multithreading
Due March 21st
You have 4 weeks!
Get started very early – Exam and S. Break are on the way
Finish Lab 4a first and check off
Finish Lab 4b next and check off
Do the extra credit

## Slide 3: Readings for Today
SIMD Processing
Basic GPU Architecture
Other execution models: VLIW, Dataflow
Lindholm et al., "NVIDIA Tesla: A Unified Graphics and Computing Architecture," IEEE Micro 2008.
Fatahalian and Houston, “A Closer Look at GPUs,” CACM 2008.
Stay tuned for more readings…

## Slide 4: SIMD Processing: Exploiting Regular (Data) Parallelism

## Slide 5: Flynn’s Taxonomy of Computers
Mike Flynn, “Very High-Speed Computing Systems,” Proc. of IEEE, 1966
SISD: Single instruction operates on single data element
SIMD: Single instruction operates on multiple data elements
  Array processor
  Vector processor
MISD: Multiple instructions operate on single data element
  Closest form: systolic array processor, streaming processor
MIMD: Multiple instructions operate on multiple data elements (multiple instruction streams)
  Multiprocessor
  Multithreaded processor

## Slide 6: Data Parallelism
Concurrency arises from performing the same operations on different pieces of data
  Single instruction multiple data (SIMD)
  E.g., dot product of two vectors
Contrast with data flow
  Concurrency arises from executing different operations in parallel (in a data driven manner)
Contrast with thread (“control”) parallelism
  Concurrency arises from executing different threads of control in parallel
SIMD exploits instruction-level parallelism
  Multiple “instructions” (more appropriately, operations) are concurrent: instructions happen to be the same

## Slide 7: SIMD Processing
Single instruction operates on multiple data elements
  In time or in space
Multiple processing elements
Time-space duality
  Array processor: Instruction operates on multiple data elements at the same time
  Vector processor: Instruction operates on multiple data elements in consecutive time steps

## Slide 8: Array vs. Vector Processors
ARRAY PROCESSOR
VECTOR PROCESSOR
LD VR  A[3:0]
ADD VR  VR, 1
MUL VR  VR, 2
ST A[3:0]  VR
Instruction Stream
Time
LD0
LD1
LD2
LD3
AD0
AD1
AD2
AD3
MU0
MU1
MU2
MU3
ST0
ST1
ST2
ST3
LD0
LD1
AD0
LD2
AD1
MU0
LD3
AD2
MU1
ST0
AD3
MU2
ST1
MU3
ST2
ST3
Space
Space
Same op @ same time
Different ops @ same space
Different ops @ time
Same op @ space

## Slide 9: SIMD Array Processing vs. VLIW
VLIW

## Slide 10: SIMD Array Processing vs. VLIW
Array processor

## Slide 11: Vector Processors
A vector is a one-dimensional array of numbers
Many scientific/commercial programs use vectors
    for (i = 0; i<=49; i++)
    C[i] = (A[i] + B[i]) / 2
A vector processor is one whose instructions operate on vectors rather than scalar (single data) values
Basic requirements
  Need to load/store vectors  vector registers (contain vectors)
  Need to operate on vectors of different lengths  vector length register (VLEN)
  Elements of a vector might be stored apart from each other in memory  vector stride register (VSTR)
    Stride: distance between two elements of a vector

## Slide 12: Vector Processors (II)
A vector instruction performs an operation on each element in consecutive cycles
  Vector functional units are pipelined
  Each pipeline stage operates on a different data element
Vector instructions allow deeper pipelines
  No intra-vector dependencies  no hardware interlocking within a vector
  No control flow within a vector
  Known stride allows prefetching of vectors into cache/memory

## Slide 13: Vector Processor Advantages
+ No dependencies within a vector
  Pipelining, parallelization work well
  Can have very deep pipelines, no dependencies!
+ Each instruction generates a lot of work
  Reduces instruction fetch bandwidth
+ Highly regular memory access pattern
  Interleaving multiple banks for higher memory bandwidth
  Prefetching
+ No need to explicitly code loops
  Fewer branches in the instruction sequence

## Slide 14: Vector Processor Disadvantages
-- Works (only) if parallelism is regular (data/SIMD parallelism)
++ Vector operations
-- Very inefficient if parallelism is irregular
-- How about searching for a key in a linked list?
Fisher, “Very Long Instruction Word architectures and the ELI-512,” ISCA 1983.

## Slide 15: Vector Processor Limitations
-- Memory (bandwidth) can easily become a bottleneck, especially if
1. compute/memory operation balance is not maintained
2. data is not mapped appropriately to memory banks

## Slide 16: Vector Processing in More Depth

## Slide 17: Vector Registers
Each vector data register holds N M-bit values
Vector control registers: VLEN, VSTR, VMASK
Maximum VLEN can be N
  Maximum number of elements stored in a vector register
Vector Mask Register (VMASK)
  Indicates which elements of vector to operate on
  Set by vector test instructions
    e.g., VMASK[i] = (Vk[i] == 0)
V0,0
V0,1
V0,N-1
V1,0
V1,1
V1,N-1
M-bit wide
M-bit wide

## Slide 18: Vector Functional Units
Use deep pipeline (=> fast clock) to execute element operations
Simplifies control of deep pipeline because elements in vector are independent
V1
V2
V3
V3 <- v1 * v2
Six stage multiply pipeline
Slide credit: Krste Asanovic

## Slide 19: Vector Machine Organization (CRAY-1)
CRAY-1
Russell, “The CRAY-1 computer system,” CACM 1978.
Scalar and vector modes
8 64-element vector registers
64 bits per element
16 memory banks
8 64-bit scalar registers
8 24-bit address registers

## Slide 20: Memory Banking
Memory is divided into banks that can be accessed independently; banks share address and data buses
Can start and complete one bank access per cycle
Can sustain N parallel accesses if they go to different banks
Bank
0
Bank
1
MDR
MAR
Bank
2
Bank
15
MDR
MAR
MDR
MAR
MDR
MAR
Data bus
Address bus
CPU
Slide credit: Derek Chiou

## Slide 21: Vector Memory System
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator
Slide credit: Krste Asanovic

## Slide 22: Scalar Code Example
For I = 0 to 49
  C[i] = (A[i] + B[i]) / 2
Scalar code (instruction and its latency)
  MOVI R0 = 50 1
  MOVA R1 = A 1
  MOVA R2 = B 1
  MOVA R3 = C 1
  X: LD R4 = MEM[R1++] 11 ;autoincrement addressing
  LD R5 = MEM[R2++] 11
  ADD R6 = R4 + R5 4
  SHFR R7 = R6 >> 1 1
  ST MEM[R3++] = R7 11
  DECBNZ --R0, X 2 ;decrement and branch if NZ
304 dynamic instructions

## Slide 23: Scalar Code Execution Time
Scalar execution time on an in-order processor with 1 bank
  First two loads in the loop cannot be pipelined: 2*11 cycles
  4 + 50*40 = 2004 cycles
Scalar execution time on an in-order processor with 16 banks (word-interleaved: consecutive words are stored in consecutive banks)
  First two loads in the loop can be pipelined
  4 + 50*30 = 1504 cycles
Why 16 banks?
  11 cycle memory access latency
  Having 16 (>11) banks ensures there are enough banks to overlap enough memory operations to cover memory latency

## Slide 24: Vectorizable Loops
A loop is vectorizable if each iteration is independent of any other
For I = 0 to 49
  C[i] = (A[i] + B[i]) / 2
Vectorized loop:
  MOVI VLEN = 50 1
  MOVI VSTR = 1 1
  VLD V0 = A 11 + VLN - 1
  VLD V1 = B 11 + VLN – 1
  VADD V2 = V0 + V1 4 + VLN - 1
  VSHFR V3 = V2 >> 1 1 + VLN - 1
  VST C = V3 11 + VLN – 1
7 dynamic instructions

## Slide 25: Basic Vector Code Performance
Assume no chaining (no vector data forwarding)
  i.e., output of a vector functional unit cannot be used as the direct input of another
  The entire vector register needs to be ready before any element of it can be used as part of another operation
One memory port (one address generator)
16 memory banks (word-interleaved)
285 cycles

## Slide 26: Vector Chaining
Vector chaining: Data forwarding from one vector functional unit to another
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
LV v1
MULV v3,v1,v2
ADDV v5, v3, v4
Slide credit: Krste Asanovic

## Slide 27: Vector Code Performance - Chaining
Vector chaining: Data forwarding from one vector functional unit to another
182 cycles
These two VLDs cannot be
pipelined. WHY?
VLD and VST cannot be
pipelined. WHY?
Strict assumption:
Each memory bank
has a single port
(memory bandwidth
bottleneck)

## Slide 28: Vector Code Performance – Multiple Memory Ports
Chaining and 2 load ports, 1 store port in each bank
79 cycles

## Slide 29: Questions (I)
What if # data elements > # elements in a vector register?
  Need to break loops so that each iteration operates on # elements in a vector register
    E.g., 527 data elements, 64-element VREGs
    8 iterations where VLEN = 64
    1 iteration where VLEN = 15 (need to change value of VLEN)
  Called vector stripmining
What if vector data is not stored in a strided fashion in memory? (irregular memory access to a vector)
  Use indirection to combine/pack elements into vector registers
  Called scatter/gather operations

## Slide 30: Gather/Scatter Operations
Want to vectorize loops with indirect accesses:
  for (i=0; i<N; i++)
  A[i] = B[i] + C[D[i]]
Indexed load instruction (Gather)
  LV vD, rD # Load indices in D vector
  LVI vC, rC, vD # Load indirect from rC base
  LV vB, rB # Load B vector
  ADDV.D vA,vB,vC # Do add
  SV vA, rA # Store result

## Slide 31: Gather/Scatter Operations
Gather/scatter operations often implemented in hardware to handle sparse matrices
Vector loads and stores use an index vector which is added to the base register to generate the addresses
Index Vector Data Vector Equivalent
0 3.14 3.14
2 6.5 0.0
6 71.2 6.5
7 2.71 0.0
0.0
0.0
71.2
2.71

## Slide 32: Conditional Operations in a Loop
What if some operations should not be executed on a vector (based on a dynamically-determined condition)?
  loop: if (a[i] != 0) then b[i]=a[i]*b[i]
  goto loop
Idea: Masked operations
  VMASK register is a bit mask determining which data element should not be acted upon
  VLD V0 = A
  VLD V1 = B
  VMASK = (V0 != 0)
  VMUL V1 = V0 * V1
  VST B = V1
  Does this look familiar? This is essentially predicated execution.

## Slide 33: Another Example with Masking
for (i = 0; i < 64; ++i)
if (a[i] >= b[i]) then c[i] = a[i]
else c[i] = b[i]
A B VMASK
1 2 0
2 2 1
3 2 1
4 10 0
-5 -4 0
0 -3 1
6 5 1
-7 -8 1
Steps to execute loop
1. Compare A, B to get
VMASK
2. Masked store of A into C
3. Complement VMASK
4. Masked store of B into C

## Slide 34: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask
Slide credit: Krste Asanovic

## Slide 35: Some Issues
Stride and banking
  As long as they are relatively prime to each other and there are enough banks to cover bank access latency, consecutive accesses proceed in parallel
Storage of a matrix
  Row major: Consecutive elements in a row are laid out consecutively in memory
  Column major: Consecutive elements in a column are laid out consecutively in memory
  You need to change the stride when accessing a row versus column

## Slide 37: Array vs. Vector Processors, Revisited
Array vs. vector processor distinction is a “purist’s” distinction
Most “modern” SIMD processors are a combination of both
  They exploit data parallelism in both time and space

## Slide 38: Remember: Array vs. Vector Processors
ARRAY PROCESSOR
VECTOR PROCESSOR
LD VR  A[3:0]
ADD VR  VR, 1
MUL VR  VR, 2
ST A[3:0]  VR
Instruction Stream
Time
LD0
LD1
LD2
LD3
AD0
AD1
AD2
AD3
MU0
MU1
MU2
MU3
ST0
ST1
ST2
ST3
LD0
LD1
AD0
LD2
AD1
MU0
LD3
AD2
MU1
ST0
AD3
MU2
ST1
MU3
ST2
ST3
Space
Space
Same op @ same time
Different ops @ same space
Different ops @ time
Same op @ space

## Slide 39: Vector Instruction Execution
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units
Slide credit: Krste Asanovic

## Slide 40: Vector Unit Structure
Lane
Functional Unit
Vector
Registers
Memory Subsystem
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …
Slide credit: Krste Asanovic

## Slide 41: Vector Instruction Level Parallelism
Can overlap execution of multiple vector instructions
  example machine has 32 elements per vector register and 8 lanes
  Complete 24 operations/cycle while issuing 1 short instruction/cycle
load
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue
Slide credit: Krste Asanovic

## Slide 42: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a compile-time reordering of operation sequencing
 requires extensive loop dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time
Slide credit: Krste Asanovic

## Slide 43: Vector/SIMD Processing Summary
Vector/SIMD machines are good at exploiting regular data-level parallelism
  Same operation performed on many data elements
  Improve performance, simplify design (no intra-vector dependencies)
Performance improvement limited by vectorizability of code
  Scalar operations limit vector machine performance
  Amdahl’s Law
  CRAY-1 was the fastest SCALAR machine at its time!
Many existing ISAs include (vector-like) SIMD operations
  Intel MMX/SSEn/AVX, PowerPC AltiVec, ARM Advanced SIMD

## Slide 44: SIMD Operations in Modern ISAs

## Slide 45: Intel Pentium MMX Operations
Idea: One instruction operates on multiple data elements simultaneously
  Ala array processing (yet much more limited)
  Designed with multimedia (graphics) operations in mind
Peleg and Weiser, “MMX Technology
Extension to the Intel Architecture,”
IEEE Micro, 1996.
No VLEN register
Opcode determines data type:
8 8-bit bytes
4 16-bit words
2 32-bit doublewords
1 64-bit quadword
Stride always equal to 1.

## Slide 46: MMX Example: Image Overlaying (I)

## Slide 47: MMX Example: Image Overlaying (II)