## Slide 1: 18-447 Computer Architecture Lecture 19: High-Performance Caches
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2015, 3/2/2015

## Slide 2: Assignment and Exam Reminders
Lab 4: Due March 6 (this Friday!)
  Control flow and branch prediction
Lab 5: Due March 22
  Data cache
HW 4: March 18
Exam: March 20
Advice: Finish the labs early
  You have almost a month for Lab 5
Advice: Manage your time well

## Slide 3: Lab 3 Grade Distribution
Chart: Number of Students
| 0-10 | 10-20 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 80-90 | 90-100
Series 1
Column1 | 7 | 0 | 0 | 4 | 2 | 2 | 4 | 2 | 2 | 15
Column2
Average 63.17
Median 69
Stddev 37.19
Max 100
Min 34

## Slide 4: Lab 3 Extra Credits
Stay tuned!

## Slide 5: Agenda for the Rest of 447
The memory hierarchy
Caches, caches, more caches
Virtualizing the memory hierarchy
Main memory: DRAM
Main memory control, scheduling
Memory latency tolerance techniques
Non-volatile memory
Multiprocessors
Coherence and consistency
Interconnection networks
Multi-core issues

## Slide 6: Readings for Today and Next Lecture
Memory Hierarchy and Caches
Required
Cache chapters from P&H: 5.1-5.3
Memory/cache chapters from Hamacher+: 8.1-8.7
Required + Review:
  Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.
Qureshi et al., “A Case for MLP-Aware Cache Replacement,“ ISCA 2006.

## Slide 7: How to Improve Cache Performance
Three fundamental goals
Reducing miss rate
  Caveat: reducing miss rate can reduce performance if more costly-to-refetch blocks are evicted
Reducing miss latency or miss cost
Reducing hit latency or hit cost

## Slide 8: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 9: Cheap Ways of Reducing Conflict Misses
Instead of building highly-associative caches:
Victim Caches
Hashed/randomized Index Functions
Pseudo Associativity
Skewed Associative Caches
…

## Slide 10: Victim Cache: Reducing Conflict Misses
Jouppi, “Improving Direct-Mapped Cache Performance by the Addition of a Small Fully-Associative Cache and Prefetch Buffers,” ISCA 1990.
Idea: Use a small fully associative buffer (victim cache) to store evicted blocks
  + Can avoid ping ponging of cache blocks mapped to the same set (if two cache blocks continuously accessed in nearby time conflict with each other)
  -- Increases miss latency if accessed serially with L2; adds complexity
Direct Mapped Cache
Next Level
Cache
Victim cache

## Slide 11: Hashing and Pseudo-Associativity
Hashing: Use better “randomizing” index functions
  + can reduce conflict misses
    by distributing the accessed memory blocks more evenly to sets
    Example of conflicting accesses: strided access pattern where stride value equals number of sets in cache
  -- More complex to implement: can lengthen critical path
Pseudo-associativity (Poor Man’s associative cache)
  Serial lookup: On a miss, use a different index function and access cache again
  Given a direct-mapped array with K cache blocks
    Implement K/N sets
    Given address Addr, sequentially look up: {0,Addr[lg(K/N)-1: 0]}, {1,Addr[lg(K/N)-1: 0]}, … , {N-1,Addr[lg(K/N)-1: 0]}

## Slide 12: Skewed Associative Caches
Idea: Reduce conflict misses by using different index functions for each cache way
Seznec, “A Case for Two-Way Skewed-Associative Caches,” ISCA 1993.

## Slide 13: Skewed Associative Caches (I)
Basic 2-way associative cache structure
Way 0
Way 1
Tag Index Byte in Block
Same index function
for each way
=?
=?

## Slide 14: Skewed Associative Caches (II)
Skewed associative caches
  Each bank has a different index function
Way 0
Way 1
tag index byte in block
f0
same index
same set
same index
redistributed to
different sets
=?
=?

## Slide 15: Skewed Associative Caches (III)
Idea: Reduce conflict misses by using different index functions for each cache way
Benefit: indices are more randomized (memory blocks are better distributed across sets)
  Less likely two blocks have same index
    Reduced conflict misses
Cost: additional latency of hash function
Seznec, “A Case for Two-Way Skewed-Associative Caches,” ISCA 1993.

## Slide 16: Software Approaches for Higher Hit Rate
Restructuring data access patterns
Restructuring data layout
Loop interchange
Data structure separation/merging
Blocking
…

## Slide 17: Restructuring Data Access Patterns (I)
Idea: Restructure data layout or data access patterns
Example: If column-major
  x[i+1,j] follows x[i,j] in memory
  x[i,j+1] is far away from x[i,j]
This is called loop interchange
Other optimizations can also increase hit rate
  Loop fusion, array merging, …
What if multiple arrays? Unknown array size at compile time?
Poor code
for i = 1, rows
for j = 1, columns
sum = sum + x[i,j]
  Better code
  for j = 1, columns
  for i = 1, rows
  sum = sum + x[i,j]

## Slide 18: Restructuring Data Access Patterns (II)
Blocking
  Divide loops operating on arrays into computation chunks so that each chunk can hold its data in the cache
  Avoids cache conflicts between different chunks of computation
  Essentially: Divide the working set so that each piece fits in the cache
But, there are still self-conflicts in a block
  1. there can be conflicts among different arrays
  2. array sizes may be unknown at compile/programming time

## Slide 19: Restructuring Data Layout (I)
Pointer based traversal (e.g., of a linked list)
Assume a huge linked list (1M nodes) and unique keys
Why does the code on the left have poor cache hit rate?
  “Other fields” occupy most of the cache line even though rarely accessed!
struct Node {
struct Node* node;
int key;
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access other fields of node
}
node = nodenext;
}

## Slide 20: Restructuring Data Layout (II)
Idea: separate frequently-used fields of a data structure and pack them into a separate data structure
Who should do this?
  Programmer
  Compiler
    Profiling vs. dynamic
  Hardware?
  Who can determine what is frequently used?
struct Node {
struct Node* node;
int key;
struct Node-data* node-data;
}
struct Node-data {
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access nodenode-data
}
node = nodenext;
}

## Slide 21: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 22: Miss Latency/Cost
What is miss latency or miss cost affected by?
  Where does the miss get serviced from?
    Local vs. remote memory
    What level of cache in the hierarchy?
    Row hit versus row miss
    Queueing delays in the memory controller and the interconnect
    …
  How much does the miss stall the processor?
    Is it overlapped with other latencies?
    Is the data immediately needed?
    …

## Slide 23: Memory Level Parallelism (MLP)
Memory Level Parallelism (MLP) means generating and servicing multiple memory accesses in parallel [Glew’98]
Several techniques to improve MLP (e.g., out-of-order execution)
MLP varies. Some misses are isolated and some parallel
How does this affect cache replacement?
time
A
B
C
isolated miss
parallel miss
Notes: Processors are fast, Memory is slow. One way to bridge this gap is to service the memory accesses in parallel. If misses are serviced in parallel, the processor incurs only one long latency stall for all the parallel misses. The notion of generating and servicing off-chip accesses in parallel is termed as Memory Level Parallelism or MLP. Out of order processors improve MLP by continuing processing of independent instructions till the instruction window is full. If there is a miss during the processing of independent instructions, the miss is serviced concurrently with the stalling miss. There are several techniques, such as Runahead, CFP, to improve the MLP of out-of-order processors. MLP is not uniform for all cache misses. Some misses, such as pointer chasing loads, are typically serviced with low MLP while other misses, such as array accesses are serviced with high MLP. Current cache management techniques are not aware of this variation in MLP.

## Slide 24: Traditional Cache Replacement Policies
Traditional cache replacement policies try to reduce miss count
Implicit assumption: Reducing miss count reduces memory-related stall time
Misses with varying cost/MLP breaks this assumption!
Eliminating an isolated miss helps performance more than eliminating a parallel miss
Eliminating a higher-latency miss could help performance more than eliminating a lower-latency miss

## Slide 25: An Example
Misses to blocks P1, P2, P3, P4 can be parallel
Misses to blocks S1, S2, and S3 are isolated
Two replacement algorithms:
  Minimizes miss count (Belady’s OPT)
  Reduces isolated miss (MLP-Aware)
For a fully associative cache containing 4 blocks
S1
P4 P3 P2 P1
P1 P2 P3 P4
S2
S3
Notes: There are 11 memory access instructions in the loop. The accesses to cache blocks P1, P2, P3, P4 occur in the instruction window at same time. If these accesses result in more than 1 miss, then those misses are serviced in parallel. Conversely, misses to the S blocks are spaced far apart in time to misses to the S blocks are always serviced in isolation. This loop executes many time. I will analyze the cache behavior of this loop for two replacement algorithms. The first minimizes the number of misses. The well known Belady's opt algorithm provides a theoretical lower bound on the number of misses. The other is MLP-aware replacement, which tries to reduce the number of isolated miss.

## Slide 26: Fewest Misses = Best Performance
P3
P2
P1
P4
H H H H
M
H H H M
Hit/Miss
Misses=4 Stalls=4
S1
P4 P3 P2 P1
P1 P2 P3 P4
S2
S3
Time
stall
Belady’s OPT replacement
M
M
MLP-Aware replacement
Hit/Miss
P3
P2
S1
P4
P3
P2
P1
P4
P3
P2
S2
P4
P3
P2
S3
P4
S1
S2
S3
P1
P3
P2
S3
P4
S1
S2
S3
P4
H H H
S1
S2
S3
P4
H M M M
H M M M
Time
stall
Misses=6Stalls=2
Saved cycles
Cache
Notes: Although Belady’s OPT minimizes misses, it is impossible to implement it in a real processor as it requires knowledge of the future. We employ the commonly used LRU policy in our experiments

## Slide 27: MLP-Aware Cache Replacement
How do we incorporate MLP into replacement decisions?
Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2006.
  Required reading for this week

## Slide 28: Enabling Multiple Outstanding Misses

## Slide 29: Handling Multiple Outstanding Accesses
Question: If the processor can generate multiple cache accesses, can the later accesses be handled while a previous miss is outstanding?
Goal: Enable cache access when there is a pending miss
Goal: Enable multiple misses in parallel
  Memory-level parallelism (MLP)
Solution: Non-blocking or lockup-free caches
  Kroft, “Lockup-Free Instruction Fetch/Prefetch Cache Organization," ISCA 1981.

## Slide 30: Handling Multiple Outstanding Accesses
Idea: Keep track of the status/data of misses that are being handled in Miss Status Handling Registers (MSHRs)
  A cache access checks MSHRs to see if a miss to the same block is already pending.
    If pending, a new request is not generated
    If pending and the needed data available, data forwarded to later load
  Requires buffering of outstanding miss requests

## Slide 31: Miss Status Handling Register
Also called “miss buffer”
Keeps track of
  Outstanding cache misses
  Pending load/store accesses that refer to the missing cache block
Fields of a single MSHR entry
  Valid bit
  Cache block address (to match incoming accesses)
  Control/status bits (prefetch, issued to memory, which subblocks have arrived, etc)
  Data for each subblock
  For each pending load/store
    Valid, type, data size, byte in block, destination register or store buffer entry address

## Slide 32: Miss Status Handling Register Entry

## Slide 33: MSHR Operation
On a cache miss:
  Search MSHRs for a pending access to the same block
    Found: Allocate a load/store entry in the same MSHR entry
    Not found: Allocate a new MSHR
    No free entry: stall
When a subblock returns from the next level in memory
  Check which loads/stores waiting for it
    Forward data to the load/store unit
    Deallocate load/store entry in the MSHR entry
  Write subblock in cache or MSHR
  If last subblock, dellaocate MSHR (after writing the block in cache)

## Slide 34: Non-Blocking Cache Implementation
When to access the MSHRs?
  In parallel with the cache?
  After cache access is complete?
MSHRs need not be on the critical path of hit requests
  Which one below is the common case?
    Cache miss, MSHR hit
    Cache hit

## Slide 35: Enabling High Bandwidth Memories

## Slide 36: Multiple Instructions per Cycle
Can generate multiple cache/memory accesses per cycle
How do we ensure the cache/memory can handle multiple accesses in the same clock cycle?
Solutions:
  true multi-porting
  virtual multi-porting (time sharing a port)
  multiple cache copies
  banking (interleaving)

## Slide 37: Handling Multiple Accesses per Cycle (I)
True multiporting
  Each memory cell has multiple read or write ports
  + Truly concurrent accesses (no conflicts on read accesses)
  -- Expensive in terms of latency, power, area
  What about read and write to the same location at the same time?
    Peripheral logic needs to handle this

## Slide 38: Peripheral Logic for True Multiporting

## Slide 39: Peripheral Logic for True Multiporting

## Slide 40: Handling Multiple Accesses per Cycle (II)
Virtual multiporting
  Time-share a single port
  Each access needs to be (significantly) shorter than clock cycle
  Used in Alpha 21264
  Is this scalable?

## Slide 41: Handling Multiple Accesses per Cycle (III)
Cache
Copy 1
Multiple cache copies
  Stores update both caches
  Loads proceed in parallel
Used in Alpha 21164
Scalability?
  Store operations form a bottleneck
  Area proportional to “ports”
Port 1
Load
Store
Port 1
Data
Cache
Copy 2
Port 2
Load
Port 2
Data

## Slide 42: Handling Multiple Accesses per Cycle (III)
Banking (Interleaving)
  Bits in address determines which bank an address maps to
    Address space partitioned into separate banks
    Which bits to use for “bank address”?
  + No increase in data store area
  -- Cannot satisfy multiple accesses
  to the same bank
  -- Crossbar interconnect in input/output
Bank conflicts
  Two accesses are to the same bank
  How can these be reduced?
    Hardware? Software?
Bank 0:
Even
addresses
Bank 1:
Odd
addresses

## Slide 43: General Principle: Interleaving
Interleaving (banking)
  Problem: a single monolithic memory array takes long to access and does not enable multiple accesses in parallel
  Goal: Reduce the latency of memory array access and enable multiple accesses in parallel
  Idea: Divide the array into multiple banks that can be accessed independently (in the same cycle or in consecutive cycles)
    Each bank is smaller than the entire memory storage
    Accesses to different banks can be overlapped
  A Key Issue: How do you map data to different banks? (i.e., how do you interleave data across banks?)

## Slide 44: Further Readings on Caching and MLP
Required: Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2006.
Glew, “MLP Yes! ILP No!,” ASPLOS Wild and Crazy Ideas Session, 1998.
Mutlu et al., “Runahead Execution: An Effective Alternative to Large Instruction Windows,” IEEE Micro 2003.

## Slide 45: Multi-Core Issues in Caching

## Slide 46: Caches in Multi-Core Systems
Cache efficiency becomes even more important in a multi-core/multi-threaded system
  Memory bandwidth is at premium
  Cache space is a limited resource
How do we design the caches in a multi-core system?
Many decisions
  Shared vs. private caches
  How to maximize performance of the entire system?
  How to provide QoS to different threads in a shared cache?
  Should cache management algorithms be aware of threads?
  How should space be allocated to threads in a shared cache?

## Slide 47: Private vs. Shared Caches
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 48: Resource Sharing Concept and Advantages
Idea: Instead of dedicating a hardware resource to a hardware context, allow multiple contexts to use it
  Example resources: functional units, pipeline, caches, buses, memory
Why?
+ Resource sharing improves utilization/efficiency  throughput
  When a resource is left idle by one thread, another thread can use it; no need to replicate shared data
+ Reduces communication latency
  For example, shared data kept in the same cache in multithreaded processors
+ Compatible with the shared memory model

## Slide 49: Resource Sharing Disadvantages
Resource sharing results in contention for resources
  When the resource is not idle, another thread cannot use it
  If space is occupied by one thread, another thread needs to re-occupy it
- Sometimes reduces each or some thread’s performance
- Thread performance can be worse than when it is run alone
- Eliminates performance isolation  inconsistent performance across runs
- Thread performance depends on co-executing threads
- Uncontrolled (free-for-all) sharing degrades QoS
- Causes unfairness, starvation
Need to efficiently and fairly utilize shared resources

## Slide 50: Private vs. Shared Caches
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 51: Shared Caches Between Cores
Advantages:
  High effective capacity
  Dynamic partitioning of available cache space
    No fragmentation due to static partitioning
  Easier to maintain coherence (a cache block is in a single location)
  Shared data and locks do not ping pong between caches
Disadvantages
  Slower access
  Cores incur conflict misses due to other cores’ accesses
    Misses due to inter-core interference
    Some cores can destroy the hit rate of other cores
  Guaranteeing a minimum level of service (or fairness) to each core is harder (how much space, how much bandwidth?)

## Slide 52: Shared Caches: How to Share?
Free-for-all sharing
  Placement/replacement policies are the same as a single core system (usually LRU or pseudo-LRU)
  Not thread/application aware
  An incoming block evicts a block regardless of which threads the blocks belong to
Problems
  Inefficient utilization of cache: LRU is not the best policy
  A cache-unfriendly application can destroy the performance of a cache friendly application
  Not all applications benefit equally from the same amount of cache: free-for-all might prioritize those that do not benefit
  Reduced performance, reduced fairness

## Slide 53: Example: Utility Based Shared Cache Partitioning
Goal: Maximize system throughput
Observation: Not all threads/applications benefit equally from caching  simple LRU replacement not good for system throughput
Idea: Allocate more cache space to applications that obtain the most benefit from more space
The high-level idea can be applied to other shared resources as well.
Qureshi and Patt, “Utility-Based Cache Partitioning: A Low-Overhead, High-Performance, Runtime Mechanism to Partition Shared Caches,” MICRO 2006.
Suh et al., “A New Memory Monitoring Scheme for Memory-Aware Scheduling and Partitioning,” HPCA 2002.

## Slide 54: The Multi-Core System: A Shared Resource View
Shared
Storage

## Slide 55: Need for QoS and Shared Resource Mgmt.
Why is unpredictable performance (or lack of QoS) bad?
Makes programmer’s life difficult
  An optimized program can get low performance (and performance varies widely depending on co-runners)
Causes discomfort to user
  An important program can starve
  Examples from shared software resources
Makes system management difficult
  How do we enforce a Service Level Agreement when hardware resources are sharing is uncontrollable?

## Slide 56: Resource Sharing vs. Partitioning
Sharing improves throughput
  Better utilization of space
Partitioning provides performance isolation (predictable performance)
  Dedicated space
Can we get the benefits of both?
Idea: Design shared resources such that they are efficiently utilized, controllable and partitionable
  No wasted resource + QoS mechanisms for threads

## Slide 57: Shared Hardware Resources
Memory subsystem (in both multithreaded and multi-core systems)
  Non-private caches
  Interconnects
  Memory controllers, buses, banks
I/O subsystem (in both multithreaded and multi-core systems)
  I/O, DMA controllers
  Ethernet controllers
Processor (in multithreaded systems)
  Pipeline resources
  L1 caches