## Slide 1: 18-447 Computer Architecture Lecture 26: Prefetching & Emerging Memory Technologies
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2015, 4/3/2015

## Slide 2: Lab 5 Honors (Critical Path)
Zhipeng Zhao 4.48ns 1%
Raghav Gupta 4.52ns 1%
Amanda Marano 6.37ns 0.8%
Elena Feldman 7.67ns 0.7%
Prin Oungpasuk 8.55ns 0.5%
Derek Tzeng 9.58ns 0.3%
Abhijith Kashyap 9.75ns 0.3%

## Slide 3: Lab 5 Honors (4-Way Cache Design)
Jared Choi 1.5%
Kais Kudrolli 1.25%
Junhan Zhou 1.25%
Raghav Gupta 1.25%
Pete Ehrett 0.6%
Xiaofan Li 0.1%

## Slide 4: Where We Are in Lecture Schedule
The memory hierarchy
Caches, caches, more caches
Virtualizing the memory hierarchy: Virtual Memory
Main memory: DRAM
Main memory control, scheduling
Memory latency tolerance techniques
Non-volatile memory
Multiprocessors
Coherence and consistency
Interconnection networks
Multi-core issues (e.g., heterogeneous multi-core)

## Slide 5: Required Reading
Onur Mutlu, Justin Meza, and Lavanya Subramanian, "The Main Memory System: Challenges and Opportunities" Invited Article in Communications of the Korean Institute of Information Scientists and Engineers (KIISE), 2015.
http://users.ece.cmu.edu/~omutlu/pub/main-memory-system_kiise15.pdf

## Slide 6: Prefetching

## Slide 7: Review: Outline of Prefetching Lecture(s)
Why prefetch? Why could/does it work?
The four questions
  What (to prefetch), when, where, how
Software prefetching
Hardware prefetching algorithms
Execution-based prefetching
Prefetching performance
  Coverage, accuracy, timeliness
  Bandwidth consumption, cache pollution
Prefetcher throttling
Issues in multi-core (if we get to it)

## Slide 8: Review: How to Prefetch More Irregular Access Patterns?
Regular patterns: Stride, stream prefetchers do well
More irregular access patterns
  Indirect array accesses
  Linked data structures
  Multiple regular strides (1,2,3,1,2,3,1,2,3,…)
  Random patterns?
  Generalized prefetcher for all patterns?
Correlation based prefetchers
Content-directed prefetchers
Precomputation or execution-based prefetchers

## Slide 9: Address Correlation Based Prefetching (I)
Consider the following history of cache block addresses
  A, B, C, D, C, E, A, C, F, F, E, A, A, B, C, D, E, A, B, C, D, C
After referencing a particular address (say A or E), are some addresses more likely to be referenced next
A
B
C
D
E
F
1.0
.33
.5
.2
1.0
.6
.2
.67
.6
.5
.2
Markov
Model

## Slide 10: Address Correlation Based Prefetching (II)
Idea: Record the likely-next addresses (B, C, D) after seeing an address A
  Next time A is accessed, prefetch B, C, D
  A is said to be correlated with B, C, D
Prefetch up to N next addresses to increase coverage
Prefetch accuracy can be improved by using multiple addresses as key for the next address: (A, B)  (C)
(A,B) correlated with C
Joseph and Grunwald, “Prefetching using Markov Predictors,” ISCA 1997.
  Also called “Markov prefetchers”
Cache Block Addr |  | Prefetch | Confidence | …. | Prefetch | Confidence
(tag) |  | Candidate 1 |  | …. | Candidate N | 
……. |  | ……. | …… | .… | ……. | ……
 |  |  |  | …. |  | 
Cache
Block
Addr

## Slide 11: Address Correlation Based Prefetching (III)
Advantages:
  Can cover arbitrary access patterns
    Linked data structures
    Streaming patterns (though not so efficiently!)
Disadvantages:
  Correlation table needs to be very large for high coverage
    Recording every miss address and its subsequent miss addresses is infeasible
  Can have low timeliness: Lookahead is limited since a prefetch for the next access/miss is initiated right after previous
  Can consume a lot of memory bandwidth
    Especially when Markov model probabilities (correlations) are low
  Cannot reduce compulsory misses

## Slide 12: Content Directed Prefetching (I)
A specialized prefetcher for pointer values
Idea: Identify pointers among all values in a fetched cache block and issue prefetch requests for them.
  Cooksey et al., “A stateless, content-directed data prefetching mechanism,” ASPLOS 2002.
+ No need to memorize/record past addresses!
+ Can eliminate compulsory misses (never-seen pointers)
-- Indiscriminately prefetches all pointers in a cache block
How to identify pointer addresses:
  Compare address sized values within cache block with cache block’s address  if most-significant few bits match, pointer

## Slide 13: Content Directed Prefetching (II)
x40373551
L2
DRAM
…
…
=
=
=
=
=
=
=
=
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
[31:20]
x80011100
Generate Prefetch
Virtual Address Predictor
X80022220
22220
X800
11100
x800

## Slide 14: Execution-based Prefetchers (I)
Idea: Pre-execute a piece of the (pruned) program solely for prefetching data
  Only need to distill pieces that lead to cache misses
Speculative thread: Pre-executed program piece can be considered a “thread”
Speculative thread can be executed
    On a separate processor/core
    On a separate hardware thread context (think fine-grained multithreading)
    On the same thread context in idle cycles (during cache misses)

## Slide 15: Execution-based Prefetchers (II)
How to construct the speculative thread:
  Software based pruning and “spawn” instructions
  Hardware based pruning and “spawn” instructions
  Use the original program (no construction), but
    Execute it faster without stalling and correctness constraints
Speculative thread
  Needs to discover misses before the main program
    Avoid waiting/stalling and/or compute less
  To get ahead, uses
    Perform only address generation computation, branch prediction, value prediction (to predict “unknown” values)
  Purely speculative so there is no need for recovery of main program if the speculative thread is incorrect

## Slide 16: Thread-Based Pre-Execution
Dubois and Song, “Assisted Execution,” USC Tech Report 1998.
Chappell et al., “Simultaneous Subordinate Microthreading (SSMT),” ISCA 1999.
Zilles and Sohi, “Execution-based Prediction Using Speculative Slices”, ISCA 2001.

## Slide 17: Thread-Based Pre-Execution Issues
Where to execute the precomputation thread?
  1. Separate core (least contention with main thread)
  2. Separate thread context on the same core (more contention)
  3. Same core, same context
    When the main thread is stalled
When to spawn the precomputation thread?
  1. Insert spawn instructions well before the “problem” load
    How far ahead?
      Too early: prefetch might not be needed
      Too late: prefetch might not be timely
  2. When the main thread is stalled
When to terminate the precomputation thread?
  1. With pre-inserted CANCEL instructions
  2. Based on effectiveness/contention feedback (recall throttling)

## Slide 18: Thread-Based Pre-Execution Issues
What, when, where, how
  Luk, “Tolerating Memory Latency through Software-Controlled Pre-Execution in Simultaneous Multithreading Processors,” ISCA 2001.
  Many issues in software-based pre-execution discussed

## Slide 19: An Example

## Slide 20: Example ISA Extensions

## Slide 21: Results on a Multithreaded Processor

## Slide 22: Problem Instructions
Zilles and Sohi, “Execution-based Prediction Using Speculative Slices”, ISCA 2001.
Zilles and Sohi, ”Understanding the backward slices of performance degrading instructions,” ISCA 2000.

## Slide 23: Fork Point for Prefetching Thread

## Slide 24: Pre-execution Thread Construction

## Slide 25: Review: Runahead Execution
A simple pre-execution method for prefetching purposes
When the oldest instruction is a long-latency cache miss:
  Checkpoint architectural state and enter runahead mode
In runahead mode:
  Speculatively pre-execute instructions
  The purpose of pre-execution is to generate prefetches
  L2-miss dependent instructions are marked INV and dropped
Runahead mode ends when the original miss returns
  Checkpoint is restored and normal execution resumes
Mutlu et al., “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors,” HPCA 2003.

## Slide 26: Review: Runahead Execution (Mutlu et al., HPCA 2003)
Compute
Compute
Load 1 Miss
Miss 1
Stall
Compute
Load 2 Miss
Miss 2
Stall
Load 1 Miss
Runahead
Load 2 Miss
Load 2 Hit
Miss 1
Miss 2
Compute
Load 1 Hit
Saved Cycles
Small Window:
Runahead:

## Slide 27: Runahead as an Execution-based Prefetcher
Idea of an Execution-Based Prefetcher: Pre-execute a piece of the (pruned) program solely for prefetching data
Idea of Runahead: Pre-execute the main program solely for prefetching data
Advantages and disadvantages of runahead vs. other execution-based prefetchers?
Can you make runahead even better by pruning the program portion executed in runahead mode?

## Slide 28: Taking Advantage of Pure Speculation
Runahead mode is purely speculative
The goal is to find and generate cache misses that would otherwise stall execution later on
How do we achieve this goal most efficiently and with the highest benefit?
Idea: Find and execute only those instructions that will lead to cache misses (that cannot already be captured by the instruction window)
How?

## Slide 29: Where We Are in Lecture Schedule
The memory hierarchy
Caches, caches, more caches
Virtualizing the memory hierarchy: Virtual Memory
Main memory: DRAM
Main memory control, scheduling
Memory latency tolerance techniques
Non-volatile memory
Multiprocessors
Coherence and consistency
Interconnection networks
Multi-core issues (e.g., heterogeneous multi-core)

## Slide 30: Emerging Memory Technologies

## Slide 31: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processor
and caches
Main Memory
Storage (SSD/HDD)

## Slide 32: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 33: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 34: An Example of The Scaling Problem
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Hammered Row
Repeatedly opening and closing a row induces disturbance errors in adjacent rows in most real DRAM chips [Kim+ ISCA 2014]
Opened
Closed

## Slide 35: Most DRAM Modules Are At Risk
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.

## Slide 36: Errors vs. Vintage
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 37: Security Implications
http://googleprojectzero.blogspot.com/2015/03/exploiting-dram-rowhammer-bug-to-gain.html
http://users.ece.cmu.edu/~omutlu/pub/dram-row-hammer_isca14.pdf

## Slide 38: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 39: How Can We Fix the Memory Problem & Design (Memory) Systems of the Future?

## Slide 40: How Do We Solve The Problem?
Tolerate it: Make DRAM and controllers more intelligent
  New interfaces, functions, architectures: system-DRAM codesign
Eliminate or minimize it: Replace or (more likely) augment DRAM with a different technology
  New technologies and system-wide rethinking of memory & storage
Embrace it: Design heterogeneous-reliability memories that map error-tolerant data to less reliable portions
  New usage and execution models
…
Solutions (to memory scaling) require
software/hardware/device cooperation

## Slide 41: Trends: Problems with DRAM as Main Memory
Need for main memory capacity increasing
  DRAM capacity hard to scale
Main memory energy/power is a key system design concern
  DRAM consumes high power due to leakage and refresh
DRAM technology scaling is ending
  DRAM capacity, cost, and energy/power hard to scale

## Slide 42: Solutions to the DRAM Scaling Problem
Two potential solutions
  Tolerate DRAM (by taking a fresh look at it)
  Enable emerging memory technologies to eliminate/minimize DRAM
Do both
  Hybrid memory systems

## Slide 43: Solution 1: Tolerate DRAM
Overcome DRAM shortcomings with
  System-DRAM co-design
  Novel DRAM architectures, interface, functions
  Better waste management (efficient utilization)
Key issues to tackle
  Reduce energy
  Enable reliability at low cost
  Improve bandwidth and latency
  Reduce waste
  Enable computation close to data

## Slide 44: Solution 1: Tolerate DRAM
Liu+, “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.
Kim+, “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices,” ISCA 2013.
Seshadri+, “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.
Pekhimenko+, “Linearly Compressed Pages: A Main Memory Compression Framework,” MICRO 2013.
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Luo+, “Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost,” DSN 2014.
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.
Qureshi+, “AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems,” DSN 2015.
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field,” DSN 2015.
Kim+, “Ramulator: A Fast and Extensible DRAM Simulator,” IEEE CAL 2015.
Avoid DRAM:
  Seshadri+, “The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing,” PACT 2012.
  Pekhimenko+, “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.
  Seshadri+, “The Dirty-Block Index,” ISCA 2014.
  Pekhimenko+, “Exploiting Compressed Block Size as an Indicator of Future Reuse,” HPCA 2015.

## Slide 45: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Expected to scale to 9nm (2022 [ITRS])
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have shortcomings as well
  Can they be enabled to replace/augment/surpass DRAM?
Lee+, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA’09, CACM’10, Micro’10.
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters 2012.
Yoon, Meza+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012.
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Lu+, “Loose Ordering Consistency for Persistent Memory,” ICCD 2014.
Zhao+, “FIRM: Fair and High-Performance Memory Control for Persistent Memory Systems,” MICRO 2014.
Yoon, Meza+, “Efficient Data Mapping and Buffering Techniques for Multi-Level Cell Phase-Change Memories,” ACM TACO 2014.
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 46: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 47: Requirements from an Ideal Memory System
Traditional
  Higher capacity
  Continuous low cost
  High system performance (higher bandwidth, low latency)
New
  Technology scalability: lower cost, higher capacity, lower energy
  Energy (and power) efficiency
  QoS support and configurability (for consolidation)
Emerging, resistive memory technologies (NVM) can help

## Slide 48: The Promise of Emerging Technologies
Likely need to replace/augment DRAM with a technology that is
  Technology scalable
  And at least similarly efficient, high performance, and fault-tolerant
    or can be architected to be so
Some emerging resistive memory technologies appear promising
  Phase Change Memory (PCM)?
  Spin Torque Transfer Magnetic Memory (STT-MRAM)?
  Memristors?
  And, maybe there are other ones
  Can they be enabled to replace/augment/surpass DRAM?

## Slide 49: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 50: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 51: Emerging Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 52: What is Phase Change Memory?
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
PCM cell can be switched between states reliably and quickly

## Slide 53: How Does PCM Work?
Write: change phase via current injection
  SET: sustained current to heat cell above Tcryst
  RESET: cell heated above Tmelt and quenched
Read: detect phase via material resistance
  Amorphous vs. crystalline
Large
Current
SET (cryst)
Low resistance
103-104 W
Small
Current
RESET (amorph)
High resistance
Access
Device
Memory
Element
106-107 W
Photo Courtesy: Bipin Rajendran, IBM
Slide Courtesy: Moinuddin Qureshi, IBM

## Slide 54: Opportunity: PCM Advantages
Scales better than DRAM, Flash
  Requires current pulses, which scale linearly with feature size
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
Can be denser than DRAM
  Can store multiple bits per cell due to large resistance range
  Prototypes with 2 bits/cell in ISSCC’08, 4 bits/cell by 2012
Non-volatile
  Retain data for >10 years at 85C
No refresh needed, low idle power

## Slide 55: Phase Change Memory Properties
Surveyed prototypes from 2003-2008 (ITRS, IEDM, VLSI, ISSCC)
Derived PCM parameters for F=90nm
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 57: Phase Change Memory Properties: Latency
Latency comparable to, but slower than DRAM
Read Latency
  50ns: 4x DRAM, 10-3x NAND Flash
Write Latency
  150ns: 12x DRAM
Write Bandwidth
  5-10 MB/s: 0.1x DRAM, 1x NAND Flash

## Slide 58: Phase Change Memory Properties
Dynamic Energy
  40 uA Rd, 150 uA Wr
  2-43x DRAM, 1x NAND Flash
Endurance
  Writes induce phase change at 650C
  Contacts degrade from thermal expansion/contraction
  108 writes per cell
  10-8x DRAM, 103x NAND Flash
Cell Size
  9-12F2 using BJT, single-level cells
  1.5x DRAM, 2-3x NAND (will scale with feature size)

## Slide 59: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system
  Ensure secure and fault-tolerant PCM operation

## Slide 60: PCM-based Main Memory: Some Questions
Where to place PCM in the memory hierarchy?
  Hybrid OS controlled PCM-DRAM
  Hybrid OS controlled PCM and hardware-controlled DRAM
  Pure PCM main memory
How to mitigate shortcomings of PCM?
How to take advantage of (byte-addressable and fast) non-volatile main memory?

## Slide 61: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09, Meza+ IEEE CAL’12]:
  How to partition/migrate data between PCM and DRAM

## Slide 62: Hybrid Memory Systems: Challenges
Partitioning
  Should DRAM be a cache or main memory, or configurable?
  What fraction? How many controllers?
Data allocation/movement (energy, performance, lifetime)
  Who manages allocation/movement?
  What are good control algorithms?
  How do we prevent degradation of service due to wearout?
Design of cache hierarchy, memory controllers, OS
  Mitigate PCM shortcomings, exploit PCM advantages
Design of PCM/DRAM chips and modules
  Rethink the design of PCM/DRAM with new requirements

## Slide 63: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 64: Aside: STT-RAM Basics
Magnetic Tunnel Junction (MTJ)
  Reference layer: Fixed
  Free layer: Parallel or anti-parallel
Cell
  Access transistor, bit/sense lines
Read and Write
  Read: Apply a small voltage across bitline and senseline; read the current.
  Write: Push large current through MTJ. Direction of current determines new orientation of the free layer.
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 65: Aside: STT MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 66: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 67: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 68: Architecting PCM to Mitigate Shortcomings
Idea 1: Use multiple narrow row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 69: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 70: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 71: One Option: DRAM as a Cache for PCM
PCM is main memory; DRAM caches memory rows/blocks
  Benefits: Reduced latency on DRAM cache hit; write filtering
Memory controller hardware manages the DRAM cache
  Benefit: Eliminates system software overhead
Three issues:
  What data should be placed in DRAM versus kept in PCM?
  What is the granularity of data movement?
  How to design a huge (DRAM) cache at low cost?
Two solutions:
  Locality-aware data placement [Yoon+ , ICCD 2012]
  Cheap tag stores and dynamic granularity [Meza+, IEEE CAL 2012]

## Slide 72: DRAM vs. PCM: An Observation
Row buffers are the same in DRAM and PCM
Row buffer hit latency same in DRAM and PCM
Row buffer miss latency small in DRAM, large in PCM
Accessing the row buffer in PCM is fast
What incurs high latency is the PCM array access  avoid this
CPU
DRAMCtrl
PCM Ctrl
Bank
Bank
Bank
Bank
Row buffer
DRAM Cache
PCM Main Memory
N ns row hit
Fast row miss
N ns row hit
Slow row miss

## Slide 73: Row-Locality-Aware Data Placement
Idea: Cache in DRAM only those rows that
  Frequently cause row buffer conflicts  because row-conflict latency is smaller in DRAM
  Are reused many times  to reduce cache pollution and bandwidth waste
Simplified rule of thumb:
  Streaming accesses: Better to place in PCM
  Other accesses (with some reuse): Better to place in DRAM
Yoon et al., “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.

## Slide 74: Row-Locality-Aware Data Placement: Results
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.9552 | 1.0469 | 1
FREQ-Dyn | 1.0502 | 1.1074 | 1.0784
RBLA | 1.0713 | 1.0997 | 1.0854
RBLA-Dyn | 1.1204 | 1.1511 | 1.1356
10%
14%
17%
Memory energy-efficiency and fairness also improve correspondingly

## Slide 75: Hybrid vs. All-PCM/DRAM
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
31% better performance than all PCM,
within 29% of all DRAM performance
31%
29%
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 76: Other Opportunities with Emerging Technologies
Merging of memory and storage
  e.g., a single interface to manage all data
New applications
  e.g., ultra-fast checkpoint and restore
More robust system design
  e.g., reducing data loss
Processing tightly-coupled with memory
  e.g., enabling efficient search and filtering

## Slide 77: Coordinated Memory and Storage with NVM (I)
The traditional two-level storage model is a bottleneck with NVM
  Volatile data in memory  a load/store interface
  Persistent data in storage  a file system interface
  Problem: Operating system (OS) and file system (FS) code to locate, translate, buffer data become performance and energy bottlenecks with fast NVM stores
Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …
Persistent (e.g., Phase-Change)
Memory

## Slide 78: Coordinated Memory and Storage with NVM (II)
Goal: Unify memory and storage management in a single unit to eliminate wasted work to locate, transfer, and translate data
  Improves both energy and performance
  Simplifies programming model as well
Unified Memory/Storage
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 79: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 80: The Persistent Memory Manager (PMM)
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Persistent objects
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 81: Performance Benefits of a Single-Level Store
Results for PostMark
~5X
~24X

## Slide 82: Energy Benefits of a Single-Level Store
Results for PostMark
~5X
~16X

## Slide 83: Enabling and Exploiting NVM: Issues
Many issues and ideas from technology layer to algorithms layer
Enabling NVM and hybrid memory
  How to tolerate errors?
  How to enable secure operation?
  How to tolerate performance and power shortcomings?
  How to minimize cost?
Exploiting emerging tecnologies
  How to exploit non-volatility?
  How to minimize energy consumption?
  How to exploit NVM on chip?
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 84: Three Principles for (Memory) Scaling
Better cooperation between devices and the system
  Expose more information about devices to upper layers
  More flexible interfaces
Better-than-worst-case design
  Do not optimize for the worst case
  Worst case should not determine the common case
Heterogeneity in design (specialization, asymmetry)
  Enables a more efficient design (No one size fits all)
These principles are related and sometimes coupled

## Slide 85: Security Challenges of Emerging Technologies
1. Limited endurance  Wearout attacks
2. Non-volatility  Data persists in memory after powerdown
 Easy retrieval of privileged or private information
3. Multiple bits per cell  Information leakage (via side channel)

## Slide 86: Securing Emerging Memory Technologies
1. Limited endurance  Wearout attacks
Better architecting of memory chips to absorb writes
Hybrid memory system management
Online wearout attack detection
2. Non-volatility  Data persists in memory after powerdown
 Easy retrieval of privileged or private information
Efficient encryption/decryption of whole main memory
Hybrid memory system management
3. Multiple bits per cell  Information leakage (via side channel)
System design to hide side channel information

## Slide 87: Summary of Emerging Memory Technologies
Key trends affecting main memory
  End of DRAM scaling (cost, capacity, efficiency)
  Need for high capacity
  Need for energy efficiency
Emerging NVM technologies can help
  PCM or STT-MRAM more scalable than DRAM and non-volatile
  But, they have shortcomings: latency, active energy, endurance
We need to enable promising NVM technologies by overcoming their shortcomings
Many exciting opportunities to reinvent main memory at all layers of computing stack