## Slide 1: INTRODUCTION TO THE SHORT-TIME FOURIER TRANSFORM (STFT)
Richard M. Stern
18-491 lecture
April 22, 2020
Department of Electrical and Computer Engineering
Carnegie Mellon University
Pittsburgh, Pennsylvania 15213

## Slide 2: Why consider short-time Fourier transforms?
Conventional DTFT sums over all time:
An example: “Welcome to DSP-I”
The DTFT averages frequency components over time
  (from the creation of the universe until ???}

## Slide 3: “Welcome to DSP-I” in time and frequency
Notes: DTFT provides long-term average but says nothing about temporal evolution.

## Slide 4: Why we want the STFT …
We are more interested in how the frequency components of real sounds like speech and music vary over time
Example: the spectrogram of “Welcome to DSP-I”
Notes: Discuss how phonemes of the utterance are evident in the STFT

## Slide 5: The direct (Fourier transform) approach to STFTs
Multiply the time function and by a sliding window, and take the DTFT of the product:
Comments:
  Note that m is a dummy variable and that the window is time-reversed
    Notation is consistent with chapter by Nawab and Quatieri in book edited by Lim and Oppenheim; OSPY notation is a little different
  Results are plotted as a vector function of n, which is called the index of the analysis frame
  Windows most commonly used are Hamming, rectangular, and exponential
Notes: NOTE unusual combination of delimiters

## Slide 6: An example with exponential windowing

## Slide 7: Impact of window size and shape
The DTFT of the window is
Letting l = m–n and m = n–l, we obtain
Hence …
The STFT can be thought of as the circular convolution in frequency of the DTFT of x[m] with the DTFT of w[n–m]

## Slide 8: Effect of window duration
The window duration mediates the tradeoff between resolution in time and frequency:
Short-duration window: Long-Duration window:
Best choice of window duration depends on the application

## Slide 9: Can the STFT be inverted?
Yes, but ….
Consider the STFT as the transform of the windowed time function:
For n=m we can write
Or, of course
So the only absolute constraint for inversion is

## Slide 10: The discrete STFT
Normally we would like the STFT to be discrete in frequency as well as time (for practical reasons)
We use
which is evaluated at

## Slide 11: Summary: the Fourier transform implementation of the STFT
The Fourier transform implementation of the STFT:
  Window input function
  Take Fourier transform
  Repeat, after shifting window

## Slide 12: There are other ways of computing the STFT!
Again, the STFT equation is
Rearranging the terms, we obtain the convolution
This can expressed as the lowpass implementation of the STFT:

## Slide 13: The lowpass implementation of the STFT
Note that the frequency response of practical windows w[n] is almost invariably that of a lowpass filter
The lowpass implementation translates the spectrum of x[n] to the left by radians and passes through a lowpass filter

## Slide 14: The Hamming window as a lowpass filter
The width of the main lobe of a Hamming window is
We will think of it as if it were an ideal LPF with the same bandwidth
Spectrum of
Hamming window, M = 40
Approximated ideal
rectangular spectrum
Single-sided BW is 4π/M

## Slide 15: Also, the bandpass implementation of the STFT
The original STFT equation remains
Pre-multiplying and post-multiplying by produces
Which can be expressed as the bandpass implementation of the SFFT:

## Slide 16: The bandpass implementation of the STFT
The bandpass implementation can be thought of as passing the signal through a (single-channel) bandpass filter and then shifting the output down to “baseband”
All three implementations are mathematically equivalent representations of the STFT
The signal at the output of the BPF has the same magnitude as X[n,k] but different phase
Notes: Note that the BP implementation is more computationally than the LP if only the magnitude of the STFT is needed.

## Slide 17: Some additional comments on implementations
In the Fourier transform implementation will develop the STFT on a column-by-column (or time frame by time frame) basis
In the LP and BP implementations we work on a row-by-row (or frequency-by-frequency) basis
Because the STFT is lowpass in nature, it can be downsampled. The downsampling ratio depends on the size and shape of the window.

## Slide 18: Reconstructing the time function
Two major methods used:
  Filterbank summation (FBS), based on LP and BP implementations
  Overlap-add (OLA), based on the Fourier transform implementation

## Slide 19: Reconstructing the time function using FBS
Filterbank summation:
Multiply each channel by
Add channels together and
multiply by a constant
This will work if all filters
add to a constant in frequency

## Slide 20: The overlap-add (OLA) method of reconstruction
Procedure:
  Compute the IDTFT for each column of the STFT
  Add the IDTFTs together in the locations of the original window locations
The OLA resynthesis approach will work if all of the windows add up to a constant. Two (of many) solutions:
  Abutting rectangular windows
  Hamming windows spaced by 50% of their length

## Slide 21: How many numbers do we need to keep?
The answer depends on the method used for analysis and synthesis.
For the Fourier transform STFT analysis with OLA resynthesis:
  Need at least N samples in frequency for windows of length N (as is always true for DFTs)
  The analysis frames can be separated by N samples for rectangular windows or N/2 samples for Hamming windows
  This means that the total number of STFT coefficients per second needed will be NFs/N = Fs for rectangular windows or NFs/(N/2) for Hamming windows
Hence, the STFT requires the same or double the number of numbers in the original waveform. (And these numbers are complex!) We accept this for the benefits that STFTs provide

## Slide 22: Summary
Short-time Fourier transforms enable us to analyze how frequency components evolve over time. The most straightforward approach is to window the time function and compute the DFT
The duration of the window mediates temporal versus spectral resolution
The original waveform can be resynthesized from the STFT representation
The number of numbers needed for the representation is somewhat greater, but that is a small price to pay for the ability to analyze and manipulate the input.