## Slide 1: Robust Speech Recognition in the 21st Century
Richard Stern
(with Chanwoo Kim, Yu-Hsiang Chiu, Evandro Gouvea,
Amir Moghimi, Anjali Menon, Bhiksha Raj, Rita Singh,
and many others)
Robust Speech Recognition Group
Carnegie Mellon University
Telephone: +1 412 268-2535
Fax: +1 412 268-3890
rms@cs.cmu.edu
http://www.ece.cmu.edu/~rms
18-491/691 Final Lecture
April 27, 2022

## Slide 2: Introduction
Today is our last regular class (!)
I will begin with a few general remarks about 18-491/691
Most of the class will involve a discussion of DSP technologies to robust speech recognition

## Slide 3: Some reminders
Take the final exam!
  Tuesday 5/3, 1:00 to 4:00 pm, HH B131
  Open book (but the book won’t be very useful in limited time; compiling notes is encouraged)
  Coverage through Problem Set 10
  MATLAB may be used for calculations, but not filterDesigner or other design algorithms
Regular office hours this week (with some modifications); NO recitation Friday
18-691 final project due Sunday evening 5:00 pm Gradescope
Quiz review Sunday evening 7:30 pm (use Recitation Zoom ID)
Complete the faculty course evaluations
  Do it for other courses, too!

## Slide 4: Some of the big themes of 18-491/691
Multiple ways of representing signals and systems
  Time domain / sample response
  Difference equations (+ initial conditions)
  DT Fourier transforms
  Z-transforms (+ ROC)
  Pole/zero representation (+ gain)
Representation of signals in time and frequency
  Continuous time / discrete time
  Aperiodic / periodic

## Slide 5: More big topics
Sampling in time
  Basic C/D and D/C conversion
  Change in sampling rate
The discrete Fourier transform (DFT) / sampling in frequency
  Circular v linear convolution
  Implementation of overlap-add and overlap-save algorithms
The Fast Fourier transform (FFT)
  FFT structures: decimation in time and frequency, non radix-2 FFTs
Implementation of filter structures for IIR, FIR filters
Digital filter design for IIR, FIR filters

## Slide 6: Signal processing is very broad!
Some of the things I have worked on in my career:
  Musical sound synthesis and timbre perception
  Fundamental studies of auditory perception / binaural hearing
  Medical instrumentation (Eustacian tube sonometry)
  Signal processing for robust speech recognition
  Sound manipulation for medical transcription
  Detection and classification of brain activity for “silent speech”
  Music information retrieval
  Applications as a consultant in
    Low-bitrate vocoding (via phonetic analysis/synthesis)
    Reverberation suppression for stadiums
    Handheld translators and humanoid robots
    Expert witness testimony (clients range from startups to Apple/Dell/IBM/GM etc.)

## Slide 7: Robust speech recognition
As speech recognition is transferred from the laboratory to the marketplace, robust recognition is becoming increasingly important
“Robustness” in 1985:
  Recognition in a quiet room using desktop microphones
Robustness in 2022:
  Recognition ….
    over a cell phone
    in a car
    with the windows down
    and the radio playing
    at highway speeds
Notes: COMMENTS:
1. Sea change w DNNs. DNNs unquestionably improve WER w in-domain training; Limits
2. KB v statistically-based ASR

## Slide 8: The source-filter model of speech production
A useful model for representing the generation of speech sounds:
Pitch
Pulse train source
Noise source
Vocal tract model
Amplitude
p[n]

## Slide 9: Signal manipulation: separating excitation from acoustical filtering in speech
Original speech:
Speech with 75-Hz excitation:
Speech with 150-Hz excitation:
Speech with noise excitation:

## Slide 10: The importance of frequency analysis
We produce and perceive speech and other sounds according to their frequency components:
An example …. sine waves and square waves

## Slide 11: Building square waves from sine waves …

## Slide 12: The anatomy of speech production
Important components:
  Sound production in lungs
  Shaping of sound by articulators

## Slide 13: The vocal tract has its own resonant frequencies
Boundary conditions:
Glottis
Lips

## Slide 14: Vowel production in the vocal tract

## Slide 15: Sound propagation through a more realistic non-uniform tube
Comment: Resonant frequencies now non-uniform
Glottis
Lips

## Slide 16: Vowels are produced by changing the resonant frequencies of the vocal tract

## Slide 17: Speech recognition as pattern classification
Major functional components:
  Signal processing to extract features from speech waveforms
  Comparison of features to pre-stored representations
Important design choices:
  Choice of features
  Specific method of comparing features to stored representations
Feature extraction
Decision making
procedure
Speech features
Phoneme
hypotheses

## Slide 18: Robust speech recognition: what we will discuss
Review background and motivation for current work:
  Sources of environmental degradation
Discuss selected approaches and their performance:
  Traditional statistical parameter estimation
  Missing-feature/multiband approaches
  Microphone arrays
  Physiologically- and perceptually-motivated signal processing
Comment on current progress for the hardest problems
Notes: Removing:
  Combination of information sources
  Signal separation based on scene analysis

## Slide 19: Some of the hard problems in ASR
Speech in background music
Speech in background speech
“Operational” data (from RATS devset)
Spontaneous speech
Reverberated speech
Vocoded speech

## Slide 20: Challenges in robust recognition
Additive noise combined with linear filtering
Transient degradations
Highly spontaneous speech
Reverberated speech
Speech masked by other speech and/or music
Speech subjected to nonlinear degradation
And ….. how does the emergence of deep neural networks change things?

## Slide 21: Solutions to classical problems: joint statistical compensation for noise and filtering
Approach of Acero, Liu, Moreno, and Raj, et al. (1990-1997)…
Compensation achieved by estimating parameters of noise and filter and applying inverse operations
Interaction is nonlinear:
“Clean” speech
x[m]
h[m]
n[m]
z[m]
Linear filtering
Degraded speech
Additive noise

## Slide 22: “Classical” combined compensation improves accuracy in stationary environments
Threshold shifts by ~7 dB
Accuracy still poor for low SNRs
Chart: SNR (dB)
| 0 | 2.5 | 5 | 7.5 | 10 | 12.5 | 15 | 20 | 25 | 30
Retrained | 53.1 | 81.1 | 85.8 | 88.2 | 89.5
VTS | 12.9 | 26.9 | 47.3 | 66.6 | 77.4 | 81.9 | 85.2 | 88.8 | 89.2 | 89.7
CDCN | 6.7 | 0 | 20.2 | 59.3 | 81.5 | 88.2 | 89.1 | 89.6
CMN | 0 | 0.2 | 1.6 | 6.2 | 22.6 | 47.5 | 68.3 | 83.7 | 88.5 | 89.6
CMN (baseline)
Complete retraining
VTS (1997)
CDCN (1990)
–5 dB 5 dB 15 dB
Original
“Recovered”

## Slide 23: But model-based compensation does not improve accuracy (much) in transient noise
Possible reasons: nonstationarity of background music and its speechlike nature

## Slide 24: Summary: traditional methods
The effects of additive noise and linear filtering are nonlinear
Methods such as CDCN and VTS can be quite effective, but …
… these methods require that the statistics of the received signal remain stationary over an interval of several hundred ms

## Slide 25: Introduction: Missing-feature recognition
Speech is quite intelligible, even when presented only in fragments
Procedure:
  Determine which time-frequency time-frequency components appear to be unaffected by noise, distortion, etc.
  Reconstruct signal based on “good” components
A monaural example using “oracle” knowledge:
  Mixed signals -
  Separated signals -

## Slide 26: Missing-feature recognition
General approach:
  Determine which cells of a spectrogram-like display are unreliable (or “missing”)
  Ignore missing features or make best guess about their values based on data that are present
Comment:
  Most groups (following the University of Sheffield) modify the internal representations to compensate for missing features
  We attempt to infer and replace missing components of input vector

## Slide 27: Example: an original speech spectrogram

## Slide 28: Spectrogram corrupted by noise at SNR 15 dB
Some regions are affected far more than others

## Slide 29: Ignoring regions in the spectrogram that are corrupted by noise
All regions with SNR less than 0 dB deemed missing (dark blue)
Recognition performed based on colored regions alone

## Slide 30: Recognition accuracy using compensated cepstra, speech in white noise (Raj, 1998)
Large improvements in recognition accuracy can be obtained by reconstruction of corrupted regions of noisy speech spectrograms
A priori knowledge of locations of “missing” features needed
SNR (dB)
Accuracy (%)
Cluster Based Recon.
Temporal Correlations
Spectral Subtraction
Baseline

## Slide 31: Recognition accuracy using compensated cepstra, speech corrupted by music
Recognition accuracy increases from 7% to 69% at 0 dB with cluster-based reconstruction
SNR (dB)
Accuracy (%)
Cluster Based Recon.
Temporal Correlations
Spectral Subtraction
Baseline

## Slide 32: Practical recognition error: white noise (Seltzer, 2000)
Speech plus white noise:

## Slide 33: Practical recognition error: background music
Speech plus music:

## Slide 34: Summary: Missing features
Missing feature approaches can be valuable in dealing with the effects of transient distortion and other disruptions that are localized in the spectro-temporal display
The approach can be effective, but it is limited by the need to determine correctly which cells in the spectrogram are missing, which can be difficult in practice

## Slide 35: Multi-band recognition (Hermanksy, Bourlard et al.)
Original approach:
  Decompose speech into several adjacent frequency bands
  Train separate recognizers to process each band
  Recombine information
Comment:
  Motivated by observation of Fletcher (and Allen) that the auditory system processes speech in separate frequency bands
Some implementation decisions:
  How many bands?
  At what level to split and merge?
  How to recombine and weight separate contributions?

## Slide 36: Missing features versus multi-band recognition: advantages and disadvanages
Multi-band approaches are typically implemented with a relatively small number of channels while ….
…. with missing feature approaches, every time-frequency point can be considered or ignored
Various techniques developed to choose “best” channels fairly well (as examined in PIRE ‘14 workshop):
  But “quantization” of representation due to limited number of channels
Missing-feature approaches:
  Finer partitioning of the observation space than multi-band method
  But errors made in identifying degraded pixels

## Slide 37: Generalizations of multiband analysis: Information fusion
Partitioning of information does not need to be on a frequency-by-frequency basis
Combination of information can take place at various levels of a speech recognition system
Information fusion is presently a fairly active area of research

## Slide 38: Information fusion
Performance can be improved by combining information extracted from different complementary knowledge sources
Sources of information may be from
  Different frequency channels (original implementation)
  Different input modalities (such as speech and video)
  Different feature sets from a single modality

## Slide 39: Combination of information streams: Independent recognition

## Slide 40: Combination of information streams: Feature combination

## Slide 41: Combination of information streams: State combination

## Slide 42: Combination of information streams: Output combination

## Slide 43: Application of hypothesis combination to NRL SPINE 2000 evaluation (Singh)
Combination of parallel hypotheses derived from complementary feature sets or compensation approaches can dramatically lower word error rate
Data
Decode
MFC
Decode
PLP
Decode
Bernoulli
WER = 35.1%
38.0
47.4
+
32.8
Adapt
MFC
Adapt
PLP
Adapt
Bernoulli
32.9
34.7
38.7
+
28.4
Adapt
PLP
Adapt
MFC
Adapt
Bernoulli
40.1
33.3
34.8
Combined
Hypothesis
+
30.3

## Slide 44: An example of output combination: hypothesis combination (Singh)
Confirmed
Southwest
</s>
<s>
South
0
4
16
46
76
79
-1
-7
-9
-8
-4
Southwest
Fire
and
go
<s>
</s>
0
6
16
46
54
76
79
-8
-3
-4
-5
-2
-6
Likelihoods
Frame number of transition point
Confirmed
Southwest
</s>
<s>
South
0
4
16
46
76
-1
-7
-7.68
-8
Fire
and
go
<s>
6
16
46
54
76
79
-3
-4
-3.68
-2
-6

## Slide 45: Combining features improves error rates
Results from NRL SPINE 2000 task (using output combination):
Chart: Word Error Rate (%)
| Filtered MFCC | PLP | MFCC | Combined
47.4 | 47.4 | 38 | 35.1 | 32.8

## Slide 46: Combining compensation schemes improves accuracy, too
Chart: Word Error Rate (%)
| None | KLT | SVD | VTS | CDCN | Combined
 | 35.1 | 34.4 | 33.4 | 32.2 | 31.1 | 29.3
Further results from SPINE 2000:

## Slide 47: Comparing different types of information fusion [RM task] (Li, 2005)
Baseline
Output Comb
Feature Comb
Natural
Features
Optimized
Features

## Slide 48: The problem of reverberation
High levels of reverberation are extremely detrimental to recognition accuracy
  In reverberant environments, the “noise” is actually reflected copies of the target speech signals
  Noise-canceling strategies (like the LMS algorithm) based on uncorrelated noise sources fail
  Frame-based compensation strategies also fail because effects of reverberation can be spread over several frames

## Slide 49: The problem of reverberation
Comparison of single channel and delay-and-sum beamforming (WSJ data passed through measured impulse responses):
Single channel
Delay and sum

## Slide 50: Use of microphone arrays: motivation
Microphone arrays can provide directional response, accepting speech from some directions but suppressing others

## Slide 51: Another reason for microphone arrays …
Microphone arrays can focus attention on the direct field in a reverberant environment

## Slide 52: Options in the use of multiple microphones…
There are many ways we can use multiple microphones to improve recognition accuracy:
  Fixed delay-and-sum beamforming
  Microphone selection techniques
  Traditional adaptive filtering based on minimizing waveform distortion
  Feature-driven adaptive filtering (LIMABEAM)
  Statistically-driven separation approaches (ICA/BSS)
  Binaural processing based on selective reconstruction (e.g. PDCW)
  Binaural processing for correlation-based emphasis (e.g. Polyaural)
  Binaural processing using precedence-based emphasis (peripheral or central, e.g. SSF)

## Slide 53: Delay-and-sum beamforming
Simple processing based on equalizing delays to sensors and summing responses
High directivity can be achieved with many sensors
Baseline algorithm for any multi-microphone experiment

## Slide 54: Adaptive array processing
MMSE-based methods (e.g. LMS, RLS ) falsely assume independence of signal and noise; not true in reverberation
  Not as much of an issue with modern methods using objective functions based on kurtosis or negative entropy
Methods reduce signal distortion, not error rate

## Slide 55: Speech recognition using microphone arrays
Speech recognition using microphone arrays has been always been performed by combining two independent systems.
ASR
Feature
extraction
Array
processing
MIC1
MIC2
MIC3
MIC4
This is not ideal:
  Systems have different objectives
  Each system does not exploit information available to the other
Notes: Say “But for recognition, our criteria are different – not SNR, but WER, retrieval accuracy, semantic content, task completion, etc.
Also, we don’t care what is sounds like, nor do we need to the signal after processing.

## Slide 56: Feature-based optimal filtering (Seltzer 2004)
ASR
Feature
extraction
Array
processing
MIC1
MIC2
MIC3
MIC4
Consider array processing and speech recognition as part of a single system that shares information
Develop array processing algorithms specifically designed to improve speech recognition

## Slide 57: Multi-microphone compensation for speech recognition based on cepstral distortion
Multi-mic compensation based on optimizing speech features rather than signal distortion
Array
Proc
ASR
Front
End
Delay
and Sum
Optimal
Comp
Speech
in Room

## Slide 58: Sample results
WER vs. SNR for WSJ with added white noise:
  Constructed 50-point filters from calibration utterance using transcription only
  Applied filters to all utterances
Chart: SNR (dB)
| 0 | 5 | 10 | 15 | 20 | 25
Closetalk | 16.515 | 16.515 | 16.515 | 16.515 | 16.515 | 16.515
Optim-Calib | 69.993 | 40.208 | 27.793 | 24.351 | 23.942 | 24.876
Delay-Sum | 88.349 | 64.479 | 36.428 | 24.689 | 21.327 | 20.482
1 Mic | 96.131 | 93.837 | 86.642 | 61.953 | 40.173 | 31.741

## Slide 59: “Nonlinear beamforming” – reconstructing sound from fragments
Procedure:
  Determine which time-frequency components appear to be dominated by the desired signal
  Recognize based on subset of features that are “good”
  OR
  Reconstruct signal based on “good” components and recognize using traditional signal processing
  In binaural processing determination of “good” components is based on estimated ITD

## Slide 60: Binaural processing for selective reconstruction (e.g. ZCAE, PDCW processing)
Assume two sources with known azimuths
Extract ITDs in TF rep (using zero crossings, cross-correlation, or phase differences in frequency domain)
Estimate signal amplitudes based on observed ITD (in binary or continuous fashion)
(Optionally) fill in missing TF segments after binary decisions

## Slide 61: Audio samples using selective reconstruction
RT60 (ms) 300
No Proc
Delay-sum
PDCW

## Slide 62: Selective reconstruction from two mics helps
Examples using the PDCW algorithm (Kim et al. 2009):
  Speech in “natural” noise: Reverberated speech:
Comment: Use of two mics provides substantial improvement that is typically independent of what is obtained using other methods

## Slide 63: Comparing linear and “nonlinear” beamforming
“Nonlinear beampatterns: Linear beampattern:
SNR = 0 dB SNR = 20 dB
Comments:
  Performance depends on SNR as well as source locations
  More consistent over frequency than linear beamforming
(Moghimi and Stern, ICASSP 2014)

## Slide 64: Linear and nonlinear beamforming as a function of the number of sensors
(Moghimi & Stern, Interspeech 2014)

## Slide 65: The binaural precedence effect
Basic stimuli of the precedence effect:
Localization is typically dominated by the first arriving pair
Precedence effect believed by some (e.g. Blauert) to improve speech intelligibility
Generalizing, we might say that onset enhancement helps at any level

## Slide 66: Effects of onset enhancement (SSF)
RT60 =
500 ms
Before
SSF
After
SSF

## Slide 67: Performance of onset enhancement in the SSF algorithm (Kim and Stern, Interspeech 2010)
Background music:
Reverberation:
Comment: Onset enhancment using SSF processing is especially effective in dealing with reverberation

## Slide 68: Combining onset enhancement with two-microphone processing:
Comment: the use of both SSF onset enhancement and binaural comparison is especially helpful for improving WER for reverberated speech
(Park et al.,
Interspeech
2014)

## Slide 69: Summary: use of multiple mics
Microphone arrays provide directional response which can help interfering sources and in reverberation
Delay-and-sum beamforming is very simple and somewhat effective
Adaptive beamforming provides better performance but not in reverberant environments with MMSE-based objective functions
Adaptive beamforming based on minimizing feature distortion can be very effective but is computationally costly
For only two mics, “nonlinear” beamforming based on selective reconstruction is best
Onset enhancement helps a great deal as well in reverberance

## Slide 70: Auditory-based representations
An original spectrogram: Spectrum “recovered” from MFCC:
What the speech recognizer sees:

## Slide 71: Comments on MFCC representation
It’s very “blurry” compared to a wideband spectrogram!
Aspects of auditory processing represented:
  Frequency selectivity and spectral bandwidth (but using a constant analysis window duration!)
    Wavelet schemes exploit time-frequency resolution better
  Nonlinear amplitude response (via log transformation only)
Aspects of auditory processing NOT represented:
  Detailed timing structure
  Lateral suppression
  Enhancement of temporal contrast
  Other auditory nonlinearities

## Slide 72: Basic auditory anatomy
Structures involved in auditory processing:

## Slide 73: Excitation along the basilar membrane (courtesy James Hudspeth, HHMI)
Notes: FIND SOURCE AND CREDIT!!

## Slide 74: Central auditory pathways
There is a lot going on!
For the most part, we only consider the response of the auditory nerve
  It is in series with everything else

## Slide 75: Some aspects of peripheral neural processing
Bandpass filtering
Rectification and log compression
Enhancement of onsets and offsets in time in each band
Lateral suppression of weaker signals in adjacent bands
Binaural interaction for localization and reverberation suppression

## Slide 76: Speech representation using mean rate
Representation of vowels by Young and Sachs using mean rate:
Mean rate representation does not preserve spectral information

## Slide 77: Speech representation using average localized synchrony measure
Representation of vowels by Young and Sachs using ALSR:

## Slide 78: Physiologically-motivated signal processing: the Zhang-Carney-Zilany model of the periphery
We used the “synapse output” as the basis for further processing

## Slide 79: An early evaluation by Kim et al. (Interspeech 2006)
Synchrony response is smeared across frequency to remove pitch effects
Higher frequencies represented by mean rate of firing
Synchrony and mean rate combined additively
Much more processing than MFCCs, but will simplify if results are useful

## Slide 80: Comparing auditory processing with cepstral analysis: clean speech

## Slide 81: Comparing auditory processing with cepstral analysis: 20-dB SNR

## Slide 82: Comparing auditory processing with cepstral analysis: 10-dB SNR

## Slide 83: Comparing auditory processing with cepstral analysis: 0-dB SNR

## Slide 84: Auditory processing is more effective than MFCCs at low SNRs, especially in white noise
Curves are shifted by 10-15 dB (greater improvement than obtained with VTS or CDCN)
[Results from Kim et al., Interspeech 2006]
Accuracy in background noise: Accuracy in background music:

## Slide 85: But do auditory models really need to be so complex?
Model of Zhang et al. 2001: A much simpler model:

## Slide 86: Comparing simple and complex auditory models
Comparing MFCC processing, a trivial (filter–rectify–compress) auditory model, and the full Carney-Zhang model:

## Slide 87: Aspects of auditory processing we have found to be important in improving WER in noise/reberb
The shape of the peripheral filters
The shape of the auditory nonlinearity
The use of “medium-time” analysis for noise and reverberation compensation
The use of nonlinear filtering to obtain noise suppression and general separation of speechlike from non-speechlike signals (a form of modulation filtering)
The use of nonlinear approaches to effect onset enhancement
Binaural processing for further enhancement of target signals

## Slide 88: PNCC processing (Kim and Stern, 2010,2014)
A pragmatic implementation of a number of the principles described:
  Gammatone filterbanks
  Nonlinearity shaped to follow auditory processing
  “Medium-time” environmental compensation using nonlinear cepstral highpass filtering in each channel
  Enhancement of envelope onsets
  Computationally-efficient implementation

## Slide 89: PNCC: an integrated front end based on auditory processing
MFCC RASTA-PLP PNCC
Initial processing
Environmental compensation
Final processing

## Slide 90: Computational complexity of front ends
Chart: 
| MFCC | PLP | PNCC | Truncated PNCC
Mults & Divs per Frame | 10742 | 12448 | 21292 | 12809

## Slide 91: Speech in noise after PNCC processing
Speech in white noise”
SNR Original speech Processed speech
∞
10
5
0
–5

## Slide 92: Performance of PNCC in white noise (RM)

## Slide 93: Performance of PNCC in white noise (WSJ)

## Slide 94: Performance of PNCC in background music

## Slide 95: Performance of PNCC in reverberation

## Slide 96: Contributions of PNCC components: white noise (WSJ)
+ Temporal masking
+ Noise protection
+ Medium-time time/freq anal
Baseline MFCC with CMN
+ Temporal masking
+ Noise suppression
+ Medium-duration processing
Baseline MFCC + CMN

## Slide 97: Contributions of PNCC components: background music (WSJ)
+ Temporal masking
+ Noise protection
+ Medium-time time/freq anal
Baseline MFCC with CMN
+ Temporal masking
+ Noise suppression
+ Medium-duration processing
Baseline MFCC + CMN

## Slide 98: Contributions of PNCC components: reverberation (WSJ)
+ Temporal masking
+ Noise protection
+ Medium-time time/freq anal
Baseline MFCC with CMN
+ Temporal masking
+ Noise suppression
+ Medium-duration processing
Baseline MFCC + CMN

## Slide 99: The binaural precedence effect
Basic stimuli of the precedence effect:
Localization is typically dominated by the first arriving pair
Precedence effect believed by some (e.g. Blauert) to improve speech intelligibility
Generalizing, we might say that onset enhancement helps at any level

## Slide 100: Performance of onset enhancement in the SSF algorithm (Kim and Stern, Interspeech 2010)
Background music:
Reverberation:
Comment: Onset enhancment using SSF processing is especially effective in dealing with reverberation

## Slide 101: The SSF algorithm: suppression after onsets
Impact of suppression:
Suppression after onsets causes responses to clean and reverberated speech to become more similar

## Slide 102: Effects of SSF processing
RT60 =
500 ms
Before
SSF
After
SSF

## Slide 103: Effectiveness of PDCW and SSF with an interfering speaker and reverberation
No reverberation Reverberation present
Comments:
• PDCW is effective in dealing with additive interference
• SSF is effective in dealing with reverberation

## Slide 104: Effects of onset enhancement/temporal masking (SSF processing, Kim ‘10)

## Slide 105: Performance with deep neural nets: PNCC and SSF @Google

## Slide 106: Summary: auditory processing
Exploiting knowledge of the auditory system can improve ASR accuracy. Important aspects include:
  Consideration of filter shapes
  Consideration of rate-intensity function
  Onset enhancement
  Nonlinear modulation filtering
  Temporal suppression

## Slide 107: General summary: Robust recognition in the 21st century
Low SNRs, reverberated speech, speech maskers, and music maskers are difficult challenges for robust speech recognition
Robustness algorithms based on classical statistical estimation fail in the presence of transient degradation
Some more recent techniques that can be effective:
  Missing-feature reconstruction
  Microphone array processing in several forms
  Processing motivated by monaural and binaural physiology and perception
More information about our work (and code!) may be found at
http://www.cs.cmu.edu/~robust

## Slide 108: www.cs.cmu.edu/~robust