## Slide 1: Advances in On-Chip Networks
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAA
Thomas Moscibroda
Microsoft Research
Footnote 1: Results presented are very biased towards my own research
during the last couple.
Footnote 2: Most results are joint work with Onur Mutlu (CMU). Other collaborators include Reetu Das (Intel), Chita Das (Penn State),
Chris Fallin (CMU) and George Nychis (CMU).
1
,2

## Slide 2: Why Networks On-Chip…?
More and more components on a single chip
  CPUs, caches, memory controllers, accelerators, etc…
  ever-larger chip multiprocessors (CMPs)
Communication critical CMP’s performance
  Between cores, cache banks, DRAM controllers,…
  Servicing L1 misses quickly is crucial
  Delays in information can stall the pipeline
Traditional architectures won’t scale:
  Common bus does not scale: electrical loading on the bus significantly reduces its speed
  Shared bus cannot support bandwidth demand

## Slide 3: Why Networks On-Chip…?
(Energy-) cost of global wires increases
  Idea: connect components using local wires
Traditional architectures won’t scale:
  Common bus does not scale: electrical loading on the bus significantly reduces its speed
  Shared bus cannot support bandwidth demand
Idea: Use on-chip network to interconnect components!
Single-chip cloud computer … 48 cores
Tilera corperation TILE-G … 100 cores
etc

## Slide 4: Overview
Why On-Chip Networks (NoC)…?
Traditional NoC design
Application-Aware NoC design
Bufferless NoC design
Theory of Bufferless NoC Routing
Conclusions, Open Problems & Bibliography

## Slide 5: Network On-Chip (NOC)
Many different topologies have been proposed
Different routing mechanisms
Different router architectures
Etc…
Design goals in NoC design:
  High throughput, low latency
  Fairness between cores, QoS, …
  Low complexity, low cost
  Power, low energy consumption

## Slide 6: Networks On-Chip (NoC)
Multi-core Chip
CPU+L1
CPU+L1
CPU+L1
CPU+L1
CPU+L1
CPU+L1
CPU+L1
CPU+L1
Cache-Bank
Cache-Bank
Cache-Bank
Cache-Bank
Cache-Bank
Cache-Bank
Cache-Bank
Cache-Bank
Memory
Controller
Accelerator,
etc…

## Slide 7: A Typical Router
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar (5x5)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Routers
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(RC)
VC Allocator (VA)
Switch
Allocator (SA)

## Slide 8: Virtual Channels & Wormhole Routing
Conceptual
View
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
VC
0
VC
1
VC
2
From East
From West
From North
From South
From PE
Routing Unit
(RC)
VC Allocator (VA)
Switch
Allocator (SA)
Buffers partitioned into “virtual channels” (VC)
for efficiency and to avoid deadlocks
Scheduler

## Slide 9: Virtual Channels & Wormhole Routing
Packets consist of multiple flits
Wormhole routing:
  Flits of a packet are routed through the network as a “worm”  all flits take the same route.
  Worm goes from a virtual channel in one router, to virtual channel in the next router, etc.
  Virtual Channel Allocator (VA) allocates which virtual channel a head-flit (and hence, the worm) goes to next.
Switch Allocator (SA) decides – for each physical link – which flit is being sent  Arbitration.
  In traditional networks, simple arbitration policies are used (round robin or age-based (oldest-first))

## Slide 10: Virtual Channels & Wormhole Routing
From E
From W
From N
From S
From PE
From E
From W
From N
From S
From PE
From E
From W
From N
From S
From PE
From E
From W
From N
From S
From PE
head-flit
of the packet
Arbitration:
Switch allocator (SA) decides which flit is sent over physical link

## Slide 11: Virtual Channels & Wormhole Routing
Advantages of wormhole routing:
  Only head-flit needs routing information
  Packet arrives at destination faster than if every flit is routed independently
  Clever allocation of virtual channels can guarantee freedom of deadlocks

## Slide 12: Overview
Why On-Chip Networks (NoC)…?
Traditional NoC design
Application-Aware NoC design
Bufferless NoC design
Theory of Bufferless NoC Routing
Conclusions, Open Problems & Bibliography

## Slide 13: Overview
Network-on-Chip
L2$
L2$
L2$
L2$
Bank
mem cont
Memory Controller
P
Accelerator
L2$
Bank
L2$
Bank
P
P
P
P
P
P
P
App1
App2
App N
App N-1
Network-on-Chip
Network-On-Chip (NOC) is a critical resource that is shared by multiple applications (like DRAM or caches).

## Slide 14: Virtual Channels & Wormhole Routing
Conceptual
View
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
VC
0
VC
1
VC
2
From East
From West
From North
From South
From PE
Routing Unit
(RC)
VC Allocator (VA)
Switch
Allocator (SA)
Scheduler

## Slide 15: Packet Scheduling in NoC
Existing switch allocation (scheduling) policies
  Round robin
  Age
Problem
  Treat all packets equally
  Application-oblivious
Packets have different criticality
  Packet is critical if latency of a packet affects application’s performance
  Different criticality due to memory level parallelism (MLP)
All packets are not the same…!!!

## Slide 16: MLP Principle
Latency ( )
Stall
Compute
St.
Latency ( )
Latency ( )
Stall ( ) = large
Packet Latency != Network Stall Time
Different Packets have different criticality due to MLP
Criticality( ) >
Criticality( ) >
Criticality( )
Stall ( ) = 0
Stall ( ) = small

## Slide 17: Slack of Packets
What is slack of a packet?
  Slack of a packet is number of cycles it can be delayed in a router without reducing application’s performance
  Local network slack
Source of slack: Memory-Level Parallelism (MLP)
  Latency of an application’s packet hidden from application due to overlap with latency of pending cache miss requests
Prioritize packets with lower slack

## Slide 18: Concept of Slack
Instruction
Window
Stall
Network-on-Chip
Load Miss
causes
1
returns earlier than necessary
2
1
2
2
1
Compute
Slack ( ) = Latency ( ) – Latency ( ) = 26 – 6 = 20 hops
2
1
2
Execution Time
Packet( ) can be delayed for available slack cycles
without reducing performance!
2
causes
Load Miss
2
Latency ( )
1
Latency ( )
2
Slack
Slack

## Slide 19: Slack-based Routing
Core A
Core B
Packet | Latency | Slack
 | 13 hops | 0 hops
 | 3 hops | 10 hops
 | 10 hops | 0 hops
 | 4 hops | 6 hops
Causes
Causes
Load Miss
Load Miss
1
2
1
2
Load Miss
Load Miss
Causes
Causes
3
4
4
3
Interference at 3 hops
1
Packet has higher slack than packet
 Prioritize packet
4
1
Slack-based NoC routing: When arbitrating in a router, the switch allocator (SA) prioritizes packet with lower slack  Aérgia.

## Slide 20: What is Aérgia?
Aérgia is the spirit of laziness in Greek mythology
Some packets can afford to slack!

## Slide 21: Slack in Applications
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
50% of packets have 350+ slack cycles
10% of packets have <50 slack cycles
Non-critical
critical

## Slide 22: Slack in Applications
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
art | 67.34 | 78.35 | 86.47 | 91.15 | 93.69 | 95.3 | 96.4 | 97.21 | 97.89 | 98.49 | 98.96
68% of packets have zero slack cycles

## Slide 23: Diversity in Slack
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
omnet | 18.26 | 22.6 | 27.38 | 31.83 | 35.94 | 39.76 | 43.34 | 46.76 | 50.07 | 53.29 | 56.34
tpcw | 24.84 | 32.69 | 39.43 | 43.74 | 47.01 | 49.78 | 52.44 | 55.46 | 59.42 | 64.22 | 68.83
mcf | 20.8 | 22.89 | 25.4 | 27.69 | 29.83 | 31.93 | 34.03 | 36.17 | 38.44 | 40.85 | 43.29
bzip2 | 16.61 | 26.43 | 43.7 | 52.13 | 57.33 | 61.22 | 64.5 | 67.73 | 71.62 | 75.76 | 79.07
sjbb | 31.97 | 44.81 | 54.63 | 59.02 | 61.71 | 63.81 | 65.95 | 69.02 | 74.12 | 80.2 | 84.77
sap | 20.91 | 33.4 | 44.4 | 49.94 | 53.68 | 56.65 | 59.47 | 62.87 | 67.63 | 73.04 | 77.64
sphinx | 33.8 | 46.89 | 57 | 62.2 | 65.55 | 68.25 | 70.75 | 73.51 | 77.02 | 81.17 | 84.85
deal | 48.38 | 63.98 | 81.27 | 87.3 | 89.68 | 91.16 | 92.32 | 93.4 | 94.56 | 95.75 | 96.79
barnes | 32.96 | 46.61 | 59.39 | 63.48 | 66.27 | 68.54 | 70.7 | 73.35 | 78.04 | 83.37 | 86.99
astar | 43.04 | 58.09 | 71.63 | 76.95 | 79.84 | 81.87 | 83.49 | 85.5 | 88.22 | 91.38 | 94.29
calculix | 55.87 | 78.45 | 90.5 | 91.95 | 92.54 | 93 | 93.43 | 93.89 | 94.58 | 95.4 | 96.12

## Slide 24: Diversity in Slack
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
omnet | 18.26 | 22.6 | 27.38 | 31.83 | 35.94 | 39.76 | 43.34 | 46.76 | 50.07 | 53.29 | 56.34
tpcw | 24.84 | 32.69 | 39.43 | 43.74 | 47.01 | 49.78 | 52.44 | 55.46 | 59.42 | 64.22 | 68.83
mcf | 20.8 | 22.89 | 25.4 | 27.69 | 29.83 | 31.93 | 34.03 | 36.17 | 38.44 | 40.85 | 43.29
bzip2 | 16.61 | 26.43 | 43.7 | 52.13 | 57.33 | 61.22 | 64.5 | 67.73 | 71.62 | 75.76 | 79.07
sjbb | 31.97 | 44.81 | 54.63 | 59.02 | 61.71 | 63.81 | 65.95 | 69.02 | 74.12 | 80.2 | 84.77
sap | 20.91 | 33.4 | 44.4 | 49.94 | 53.68 | 56.65 | 59.47 | 62.87 | 67.63 | 73.04 | 77.64
sphinx | 33.8 | 46.89 | 57 | 62.2 | 65.55 | 68.25 | 70.75 | 73.51 | 77.02 | 81.17 | 84.85
deal | 48.38 | 63.98 | 81.27 | 87.3 | 89.68 | 91.16 | 92.32 | 93.4 | 94.56 | 95.75 | 96.79
barnes | 32.96 | 46.61 | 59.39 | 63.48 | 66.27 | 68.54 | 70.7 | 73.35 | 78.04 | 83.37 | 86.99
astar | 43.04 | 58.09 | 71.63 | 76.95 | 79.84 | 81.87 | 83.49 | 85.5 | 88.22 | 91.38 | 94.29
calculix | 55.87 | 78.45 | 90.5 | 91.95 | 92.54 | 93 | 93.43 | 93.89 | 94.58 | 95.4 | 96.12
Slack varies between packets of different applications
Slack varies between packets of a single application

## Slide 25: Estimating Slack Priority
Slack (P) = Max (Latencies of P’s Predecessors) – Latency of P
  Predecessors(P) are the packets of outstanding cache miss requests when P is issued
Packet latencies not known when issued
Predicting latency of any packet Q
  Higher latency if Q corresponds to an L2 miss
  Higher latency if Q has to travel farther number of hops

## Slide 26: Estimating Slack Priority
Slack of P = Maximum Predecessor Latency – Latency of P
Slack(P) =
  PredL2: Number of predecessor packet that are servicing an L2 miss.
  MyL2: Set if P is NOT servicing an L2 miss
  HopEstimate: Max (# of hops of Predecessors) – hops of P
PredL2
(2 bits)
MyL2
(1 bit)
HopEstimate
(2 bits)

## Slide 27: Estimating Slack Priority
How to predict L2 hit or miss at core?
  Global Branch Predictor based L2 Miss Predictor
    Use Pattern History Table and 2-bit saturating counters
  Threshold based L2 Miss Predictor
    If #L2 misses in “M” misses >= “T” threshold then next load is a L2 miss.
Number of miss predecessors?
  List of outstanding L2 Misses
Hops estimate?
  Hops => ∆X + ∆ Y distance
  Use predecessor list to calculate slack hop estimate

## Slide 28: Starvation Avoidance
Problem: Starvation
  Prioritizing packets can lead to starvation of lower priority packets
Solution: Time-Based Packet Batching
  New batches are formed at every T cycles
  Packets of older batches are prioritized over younger batches
Similar to batch-based DRAM scheduling.

## Slide 29: Putting it all together
Tag header of the packet with priority bits before injection
Priority(P)?
  P’s batch (highest priority)
  P’s Slack
  Local Round-Robin (final tie breaker)
PredL2
(2 bits)
MyL2
(1 bit)
HopEstimate
(2 bits)
Batch
(3 bits)
Priority (P) =

## Slide 30: Evaluation Methodology
64-core system
  x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  32KB private L1 and 1MB per core shared L2 caches, 32 miss buffers
  4GB DRAM, 320 cycle access latency, 4 on-chip DRAM controllers
Detailed Network-on-Chip model
  2-stage routers (with speculation and look ahead routing)
  Wormhole switching (8 flit data packets)
  Virtual channel flow control (6 VCs, 5 flit buffer depth)
  8x8 Mesh (128 bit bi-directional channels)
Benchmarks
  Multiprogrammed scientific, server, desktop workloads (35 applications)
  96 workload combinations

## Slide 31: Qualitative Comparison
Round Robin & Age
  Local and application oblivious
  Age is biased towards heavy applications
Globally Synchronized Frames (GSF) [Lee et al., ISCA 2008]
  Provides bandwidth fairness at the expense of system performance
  Penalizes heavy and bursty applications
Application-Aware Prioritization Policies (SJF) [Das et al., MICRO 2009]
  Shortest-Job-First Principle
  Packet scheduling policies which prioritize network sensitive applications which inject lower load
  Application-aware, but not slack-based! Does not take into account intra-application variation of slack.

## Slide 32: System Performance
SJF provides 8.9% improvement in weighted speedup
Aérgia improves system throughput by 10.3%
Aérgia+SJF improves system throughput by 16.1%
Chart: Normalized System Speedup
Age | 1
RR | 1.0046
GSF | 0.88979
SJF | 1.0949
Aergia | 1.1084
SJF+Aergia | 1.1668

## Slide 33: Network Unfairness
SJF does not imbalance network fairness
Aergia improves network unfairness by 1.5X
SJF+Aergia improves network unfairness by 1.3X
Chart: Network Unfairness
Age | 10.21
RR | 10.64
GSF | 10.4794
SJF | 9.8747
Aergia | 6.78
SJF+Aergia | 7.9

## Slide 34: Conclusions
Packets have different criticality, yet existing packet scheduling policies treat all packets equally
We propose a new approach to packet scheduling in NoCs
  We define Slack as a key measure that characterizes the relative importance of a packet.
  We propose Aergia a novel architecture to accelerate low slack critical packets
Result
  Improves system performance: 16.1%
  Improves network fairness: 30.8%

## Slide 35: Overview
Why On-Chip Networks (NoC)…?
Traditional NoC design
Application-Aware NoC design
Bufferless NoC design
Theory of Bufferless NoC Routing
Conclusions, Open Problems & Bibliography

## Slide 36: Network On-Chip (NOC)
Many different topologies have been proposed
Different routing mechanisms
Different router architectures
Etc…
Design goals in NoC design:
  High throughput, low latency
  Fairness between cores, QoS, …
  Low complexity, low cost
  Power, low energy consumption
Energy/Power in On-Chip Networks
Power is a key constraint in the design
of high-performance processors
NoCs consume substantial portion of system
power
  ~30% in Intel 80-core Terascale [IEEE Micro’07]
  ~40% in MIT RAW Chip [ISCA’04]
NoCs estimated to consume 100s of Watts [Borkar, DAC’07]

## Slide 37: Current NoC Approaches
Existing approaches differ in numerous ways:
  Network topology [Kim et al, ISCA’07, Kim et al, ISCA’08 etc]
  Flow control [Michelogiannakis et al, HPCA’09, Kumar et al, MICRO’08, etc]
  Virtual Channels [Nicopoulos et al, MICRO’06, etc]
  QoS & fairness mechanisms [Lee et al, ISCA’08, etc]
  Routing algorithms [Singh et al, CAL’04]
  Router architecture [Park et al, ISCA’08]
  Broadcast, Multicast [Jerger et al, ISCA’08, Rodrigo et al, MICRO’08]
Existing work assumes existence of
buffers in routers!

## Slide 38: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Injection Rate
Avg. packet latency
large buffers
medium buffers
small buffers

## Slide 39: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Buffers consume significant energy/power
  Dynamic energy when read/write
  Static energy even when not occupied
Buffers add complexity and latency
  Logic for buffer management
  Virtual channel allocation
  Credit-based flow control
Buffers require significant chip area
  E.g., in TRIPS prototype chip, input buffers occupy 75% of total on-chip network area [Gratz et al, ICCD’06]

## Slide 40: Going Bufferless…?
How much throughput do we lose?
   How is latency affected?
Up to what injection rates can we use bufferless routing?
 Are there realistic scenarios in which NoC is operated at injection rates below the threshold?
Can we achieve energy reduction?
   If so, how much…?
Can we reduce area, complexity, etc…?
Injection Rate
latency
buffers
no buffers

## Slide 41: BLESS: Bufferless Routing
Packet creation: L1 miss, L1 service, write-back, …
Injection: A packet can be injected whenever at least one output port is available (i.e., when <4 incoming flits in a grid)
Always forward all incoming flits to some output port
If no productive direction is available, send to another direction
 packet is deflected
 Hot-potato routing [Baran’64, etc]

## Slide 42: BLESS: Bufferless Routing
Example: Two flits come in, both want to go North
Traditional, buffered network: One flit is sent North, the other is buffered
In a bufferless network: One flit is sent North, the other is sent to some other direction

## Slide 43: BLESS: Bufferless Routing
Routing
VC Arbiter
Switch Arbiter
Flit-Ranking
Port-Prioritization
arbitration policy
Flit-Ranking
Create a ranking over all incoming flits
Port-Prioritization
For a given flit in this ranking, find the best free output-port
Apply to each flit in order of ranking

## Slide 44: FLIT-BLESS: Flit-Level Routing
Each flit is routed independently.
Oldest-first arbitration (other policies evaluated in paper)
Network Topology:  Can be applied to most topologies (Mesh, Torus, Hypercube, Trees, …) 1) #output ports ¸ #input ports at every router 2) every router is reachable from every other router
Flow Control & Injection Policy:
   Completely local, inject whenever input port is free
Absence of Deadlocks: every flit is always moving
Absence of Livelocks: with oldest-first ranking
Flit-Ranking
Oldest-first ranking
Port-Prioritization
Assign flit to productive port, if possible. Otherwise, assign to non-productive port.

## Slide 45: WORM-BLESS: Wormhole Routing
Potential downsides of FLIT-BLESS
  Not-energy optimal (each flits needs header information)
  Increase in latency (different flits take different path)
  Increase in receive buffer size
BLESS with wormhole routing…?
Problems:
  Injection Problem (how can I know when it is safe to inject…? a new worm could arrive anytime, blocking me from injecting...)
  Livelock Problem (packets can be deflected forever)
new worm!
[Dally, Seitz’86]

## Slide 46: WORM-BLESS: Wormhole Routing
Flit-Ranking
Oldest-first ranking
Port-Prioritization
If flit is head-flit
a) assign flit to unallocated, productive port b) assign flit to allocated, productive port c) assign flit to unallocated, non-productive port d) assign flit to allocated, non-productive port else, a) assign flit to port that is allocated to worm
Deflect worms if necessary!
Truncate worms if necessary!
Head-flit: West
This worm is truncated!
& deflected!
At low congestion, packets
travel routed as worms
allocated to North
allocated to West
Body-flit turns into head-flit

## Slide 47: BLESS with Small Buffers
BLESS without buffers is extreme end of a continuum
BLESS can be integrated with buffers
  FLIT-BLESS with Buffers
  WORM-BLESS with Buffers
Whenever a buffer is full, it’s first flit becomes must-schedule
must-schedule flits must be deflected if necessary

## Slide 48: BLESS: Advantages & Disadvantages
Advantages
No buffers
Purely local flow control
Simplicity - no credit-flows - no virtual channels - simplified router design
No deadlocks, livelocks
Adaptivity - packets are deflected around congested areas!
Router latency reduction
Area savings
Disadvantages
Increased latency
Reduced bandwidth
Increased buffering at receiver
Header information at each flit
Impact on energy…?

## Slide 49: Reduction of Router Latency
BLESS gets rid of input buffers and virtual channels
BW RC
VA SA
ST
LT
BW
SA
ST
LT
RC
ST
LT
RC
ST
LT
LA LT
BW: Buffer Write
RC: Route Computation
VA: Virtual Channel Allocation
SA: Switch Allocation ST: Switch Traversal
LT: Link Traversal
LA LT: Link Traversal of Lookahead
Baseline Router
(speculative)
head flit
body flit
BLESS Router
(standard)
RC
ST
LT
RC
ST
LT
Router 1
Router 2
Router 1
Router 2
BLESS Router
(optimized)
Router Latency = 3
Router Latency = 2
Router Latency = 1
Can be improved to 2.
[Dally, Towles’04]

## Slide 50: BLESS: Advantages & Disadvantages
Advantages
No buffers
Purely local flow control
Simplicity - no credit-flows - no virtual channels - simplified router design
No deadlocks, livelocks
Adaptivity - packets are deflected around congested areas!
Router latency reduction
Area savings
Disadvantages
Increased latency
Reduced bandwidth
Increased buffering at receiver
Header information at each flit
Impact on energy…?

## Slide 51: Evaluation Methodology
2D mesh network, router latency is 2 cycles
  4x4, 8 core, 8 L2 cache banks (each node is a core or an L2 bank)
  4x4, 16 core, 16 L2 cache banks (each node is a core and an L2 bank)
  8x8, 16 core, 64 L2 cache banks (each node is L2 bank and may be a core)
  128-bit wide links, 4-flit data packets, 1-flit address packets
  For baseline configuration: 4 VCs per physical input port, 1 packet deep
Benchmarks
  Multiprogrammed SPEC CPU2006 and Windows Desktop applications
  Heterogeneous and homogenous application mixes
  Synthetic traffic patterns: UR, Transpose, Tornado, Bit Complement
x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  64Kbyte private L1 caches
  Total 16Mbyte shared L2 caches; 16 MSHRs per bank
  DRAM model based on Micron DDR2-800

## Slide 52: Evaluation Methodology
2D mesh network, router latency is 2 cycles
  4x4, 8 core, 8 L2 cache banks (each node is a core or an L2 bank)
  4x4, 16 core, 16 L2 cache banks (each node is a core and an L2 bank)
  8x8, 16 core, 64 L2 cache banks (each node is L2 bank and may be a core)
  128-bit wide links, 4-flit data packets, 1-flit address packets
  For baseline configuration: 4 VCs per physical input port, 1 packet deep
Benchmarks
  Multiprogrammed SPEC CPU2006 and Windows Desktop applications
  Heterogeneous and homogenous application mixes
  Synthetic traffic patterns: UR, Transpose, Tornado, Bit Complement
x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  64Kbyte private L1 caches
  Total 16Mbyte shared L2 caches; 16 MSHRs per bank
  DRAM model based on Micron DDR2-800
Evaluations with perfect L2 caches
 Puts maximal stress on NoC
Simulation is cycle-accurate
Models stalls in network and processors
Self-throttling behavior
Aggressive processor model

## Slide 53: Evaluation Methodology
Energy model provided by Orion simulator [MICRO’02]
  70nm technology, 2 GHz routers at 1.0 Vdd
For BLESS, the following is modeled
  Additional energy to transmit header information
  Additional buffers needed on the receiver side
  Additional logic to reorder flits of individual packets at receiver
Network energy is partitioned into buffer energy, router energy, and link energy, each having static and dynamic components.
Comparisons against non-adaptive and aggressive adaptive buffered routing algorithms (DO, MIN-AD, ROMM)

## Slide 54: Evaluation – Synthethic Traces
First, the bad news 
Uniform random injection
BLESS has significantly lower saturation throughput compared to buffered baseline.
Chart: Injection Rate (flits per cycle per node)
| 0 | 8.0000000000000043E-2 | 0.16 | 7.0000000000000021E-2 | 8.0000000000000043E-2 | 9.0000000000000024E-2 | 0.1 | 0.11 | 0.12000000000000002 | 0.13 | 0.14000000000000001 | 0.15000000000000022 | 0.16 | 0.17 | 0.18000000000000022 | 0.19 | 0.2 | 0.21000000000000021 | 0.22 | 0.23 | 0.24000000000000021 | 0.25 | 0.26 | 0.27 | 0.28000000000000008 | 0.29000000000000031 | 0.30000000000000032 | 0.31000000000000044 | 0.32000000000000051 | 0.33000000000000057 | 0.34 | 0.35000000000000031 | 0.36000000000000032 | 0.37000000000000038 | 0.3800000000000005 | 0.39000000000000051 | 0.4 | 0.41000000000000031 | 0.42000000000000032 | 0.43000000000000038 | 0.44 | 0.45 | 0.46 | 0.47000000000000008 | 0.48000000000000032 | 0.49000000000000032
FLIT-2 | 29.0347 | 29.0347 | 29.0347 | 29.0347 | 29.0347 | 29.3142 | 29.5848 | 29.8829 | 30.2641 | 30.6478 | 31.0371 | 31.5291 | 32.0485 | 32.514 | 33.0424 | 33.6214 | 34.2454 | 34.8647 | 35.5349 | 36.3327 | 37.1874 | 38.0545 | 39.1327 | 40.2686 | 41.8595 | 43.8418 | 48.2112 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
WORM-2 | 29.1135 | 29.1135 | 29.1135 | 29.1135 | 29.1135 | 29.3889 | 29.6607 | 29.9602 | 30.3294 | 30.7091 | 31.1068 | 31.6101 | 32.1665 | 32.6453 | 33.3123 | 33.9411 | 34.7541 | 35.5301 | 36.508 | 37.6649 | 38.9475 | 40.364 | 42.0965 | 44.2469 | 47.7519 | 57.8451 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
FLIT-1 | 22.2481 | 22.2481 | 22.2481 | 22.2481 | 22.2481 | 22.4505 | 22.6682 | 22.8838 | 23.1614 | 23.4459 | 23.7382 | 24.1268 | 24.5155 | 24.8599 | 25.261 | 25.6915 | 26.1454 | 26.6054 | 27.1534 | 27.7909 | 28.4923 | 29.2033 | 30.0413 | 31.1505 | 32.5742 | 34.4702 | 39.8047 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
WORM-1 | 22.3647 | 22.3647 | 22.3647 | 22.3647 | 22.3647 | 22.585 | 22.8079 | 23.0303 | 23.3201 | 23.6314 | 23.9379 | 24.3375 | 24.7663 | 25.1396 | 25.6411 | 26.1686 | 26.7838 | 27.4439 | 28.2236 | 29.1584 | 30.2441 | 31.4552 | 32.9357 | 35.035 | 38.7007 | 61.9914 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
MIN-AD | 28.3699 | 28.3699 | 28.3699 | 28.3699 | 28.3699 | 28.5388 | 28.6459 | 28.864 | 29.0263 | 29.2029 | 29.4106 | 29.6055 | 29.7855 | 30.0568 | 30.2965 | 30.5566 | 30.8537 | 31.067 | 31.3404 | 31.6329 | 31.9691 | 32.281 | 32.5873 | 33.0224 | 33.3879 | 33.7872 | 34.2208 | 34.6467 | 35.2042 | 35.8494 | 36.3318 | 36.9534 | 37.7887 | 38.4606 | 39.5018 | 40.4692 | 41.6397 | 43.0612 | 44.6159 | 46.6269 | 49.5462 | 54.2782 | 61.2888 | 82.5748 | 101 | 101
BLESS
Best Baseline
Is BLESS doomed…?

## Slide 55: Evaluation – Homogenous Case Study
milc benchmarks
(moderately intensive)
Perfect caches!
Very little performance degradation with BLESS
(less than 4% in dense network)
With router latency 1, BLESS can even outperform baseline (by ~10%)
Significant energy improvements (almost 40%)
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.991 | 7.9907 | 7.9892 | 7.9789 | 7.9802 | 7.9918 | 7.9907 | 15.6268 | 15.7797 | 15.6253 | 15.2216 | 15.0442 | 15.3638 | 15.2073 | 14.8309 | 14.7752 | 14.7082 | 14.7206 | 14.6774 | 16.2317 | 16.1992
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.40464 | 0.40495 | 0.40517 | 0.42894 | 0.4223 | 0.42804 | 0.42107 | 0.38681 | 0.38681 | 0.391 | 0.43437 | 0.44217 | 0.43081 | 0.43834 | 0.40835 | 0.41014 | 0.41114 | 0.43191 | 0.42337 | 0.37773 | 0.37158
LinkEnergy | 0.12364 | 0.12368 | 0.1237 | 0.14 | 0.14077 | 0.14024 | 0.14058 | 0.1871 | 0.1871 | 0.1874 | 0.23441 | 0.24339 | 0.23441 | 0.24365 | 0.1164 | 0.11652 | 0.11642 | 0.12893 | 0.12753 | 0.12452 | 0.12405
BufferEnergy | 0.47171 | 0.47418 | 0.47432 | 0.045804 | 0.041356 | 0.041234 | 0.043464 | 0.42609 | 0.42609 | 0.42825 | 0.039818 | 0.040263 | 0.039354 | 0.039719 | 0.47526 | 0.48429 | 0.48088 | 0.043196 | 0.038642 | 0.032973 | 0.031075
Baseline
BLESS
RL=1

## Slide 56: Evaluation – Homogenous Case Study
milc benchmarks
(moderately intensive)
Perfect caches!
Very little performance degradation with BLESS
(less than 4% in dense network)
With router latency 1, BLESS can even outperform baseline (by ~10%)
Significant energy improvements (almost 40%)
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.991 | 7.9907 | 7.9892 | 7.9789 | 7.9802 | 7.9918 | 7.9907 | 15.6268 | 15.7797 | 15.6253 | 15.2216 | 15.0442 | 15.3638 | 15.2073 | 14.8309 | 14.7752 | 14.7082 | 14.7206 | 14.6774 | 16.2317 | 16.1992
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.40464 | 0.40495 | 0.40517 | 0.42894 | 0.4223 | 0.42804 | 0.42107 | 0.38681 | 0.38681 | 0.391 | 0.43437 | 0.44217 | 0.43081 | 0.43834 | 0.40835 | 0.41014 | 0.41114 | 0.43191 | 0.42337 | 0.37773 | 0.37158
LinkEnergy | 0.12364 | 0.12368 | 0.1237 | 0.14 | 0.14077 | 0.14024 | 0.14058 | 0.1871 | 0.1871 | 0.1874 | 0.23441 | 0.24339 | 0.23441 | 0.24365 | 0.1164 | 0.11652 | 0.11642 | 0.12893 | 0.12753 | 0.12452 | 0.12405
BufferEnergy | 0.47171 | 0.47418 | 0.47432 | 0.045804 | 0.041356 | 0.041234 | 0.043464 | 0.42609 | 0.42609 | 0.42825 | 0.039818 | 0.040263 | 0.039354 | 0.039719 | 0.47526 | 0.48429 | 0.48088 | 0.043196 | 0.038642 | 0.032973 | 0.031075
Baseline
BLESS
RL=1
Observations:
Injection rates not extremely high on average  self-throttling!
For bursts and temporary hotspots, use network links as buffers!

## Slide 57: Evaluation – Homogenous Case Study
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.9415 | 7.9702 | 7.9561 | 7.9434 | 7.9242 | 7.9846 | 7.9176 | 13.3279 | 15.2097 | 13.8681 | 12.9915 | 12.7008 | 13.1024 | 12.7729 | 14.8411 | 15.3992 | 14.9538 | 15.3975 | 15.2995 | 15.9073 | 15.8975
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.38973 | 0.38898 | 0.3901 | 0.41286 | 0.4116 | 0.41134 | 0.4112 | 0.38109 | 0.35032 | 0.37054 | 0.43916 | 0.45683 | 0.43939 | 0.45819 | 0.39215 | 0.37893 | 0.38554 | 0.40714 | 0.40839 | 0.38335 | 0.3841
LinkEnergy | 0.16946 | 0.16956 | 0.16956 | 0.19429 | 0.19682 | 0.19447 | 0.1957 | 0.21934 | 0.2179 | 0.21792 | 0.29761 | 0.31243 | 0.29993 | 0.31527 | 0.17002 | 0.1568 | 0.17002 | 0.19798 | 0.2022 | 0.1897 | 0.1938
BufferEnergy | 0.44081 | 0.44722 | 0.44412 | 0.060498 | 0.055111 | 0.058364 | 0.051494 | 0.39957 | 0.36842 | 0.38584 | 0.054662 | 0.049922 | 0.048412 | 0.046704 | 0.43783 | 0.42462 | 0.43122 | 0.05787 | 0.047417 | 0.049107 | 0.037555
Matlab benchmarks
(most intensive)
Perfect caches!
 Worst-case for BLESS
Performance loss is within 15% for most dense configuration
Even here, more than 15% energy savings in densest network!

## Slide 58: Evaluation – Further Results
BLESS increases buffer requirement at receiver by at most 2x  overall, energy is still reduced
Impact of memory latency
 with real caches, very little slowdown! (at most 1.5%)
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.7417 | 7.7492 | 7.7292 | 7.7059 | 7.7181 | 8.0128 | 7.9959 | 15.0683 | 15.1571 | 15.0648 | 14.9256 | 14.9115 | 15.4871 | 15.381 | 15.2257 | 15.2105 | 15.1846 | 15.2005 | 15.1758 | 16.1669 | 16.1562

## Slide 59: Evaluation – Further Results
BLESS increases buffer requirement at receiver by at most 2x  overall, energy is still reduced
Impact of memory latency
 with real caches, very little slowdown! (at most 1.5%)
Heterogeneous application mixes
(we evaluate several mixes of intensive and non-intensive applications)
 little performance degradation
 significant energy savings in all cases
 no significant increase in unfairness across different applications
Area savings: ~60% of network area can be saved!

## Slide 60: Evaluation – Aggregate Results
Aggregate results over all 29 applications
Sparse Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -39.4% | -28.1% | -46.4% | -41.0%
∆ System Performance | -0.5% | -3.2% | -0.15% | -0.55%
Chart: Energy (normalized)
| Mean | Worst-Case
RouterEnergy | 0.41542 | 0.44748 | 0.44 | 0.38395 | 0.43429 | 0.44348
LinkEnergy | 0.076955 | 0.094334 | 0.097193 | 0.1754 | 0.22557 | 0.23775
BufferEnergy | 0.50763 | 0.073091 | 0.062562 | 0.44066 | 0.058704 | 0.055516
FLIT
WORM
BASE
Chart: W-Speedup
| Mean | Worst-Case
WeightedSpeedup | 7.9295 | 7.8761 | 7.8588 | 7.8079 | 7.5574 | 7.4834
FLIT
WORM
BASE
Mean
Mean
Worst-Case
Worst-Case

## Slide 61: Evaluation – Aggregate Results
Aggregate results over all 29 applications
Sparse Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -39.4% | -28.1% | -46.4% | -41.0%
∆ System Performance | -0.5% | -3.2% | -0.15% | -0.55%
Dense Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -32.8% | -14.0% | -42.5% | -33.7%
∆ System Performance | -3.6% | -17.1% | -0.7% | -1.5%

## Slide 62: Summary
For a very wide range of applications and network settings, buffers are not needed in NoC
  Significant energy savings (32% even in dense networks and perfect caches)
  Area-savings of 60%
  Simplified router and network design (flow control, etc…)
  Performance slowdown is minimal (can even increase!)
A strong case for a rethinking of NoC design!

## Slide 63: Overview
Why On-Chip Networks (NoC)…?
Traditional NoC design
Application-Aware NoC design
Bufferless NoC design
Theory of Bufferless NoC Routing
Conclusions, Open Problems & Bibliography

## Slide 64: Optimal Bufferless Routing…?
BLESS uses age-based arbitration in combination with XY-routing  this may be sub-optimal
Same packets (flits) could collide many times on the way to their destination
Is there a provably optimal arbitration & routing mechanism for bufferless networks…?

## Slide 65: Optimal Bufferless Routing…?
Optimal Bufferless “Greedy-Home-Run” Routing
The following arbitration policy is provably optimal for an m x m Mesh network (asymptotically at least)
1 - Packets move greedily towards their destination if possible (if there are 2 good links, any of them is fine)
2 - If a packet is deflected, it gets “excited” with probability 1/p,
where p = £(1/m).
3 - When a packet is excited, it has higher priority than non-excited packets
4 - When being excited, a packet tries to reach the destination on the “home-run” path (row-column XY-path)
5 - When two excited packets contend, the one that goes straight (i.e., keeps its direction) has priority
6 - If an excited packet is deflected  it becomes normal again

## Slide 66: Optimal Bufferless Routing…?
1
2
Packet 1 wants to go to [7,7]
Packet 2 wants to go to [2,7]
say, Packet 1 gets deflected
with probability p, it gets excited
if excited, it is routed strictly on the home-run path
if it is deflected on the home-run path, it becomes non-excited again.
this can only happen at the first hop or at the turn (only 2 possibilities!)
[0,0]
[7,7]
home-run path

## Slide 67: Optimal Bufferless Routing…?
Proof-sketch:
An excited packet can only be deflected at its start node, or when trying to turn.
In both cases, the probability to be deflected is a small constant (because there needs to be another excited packet starting at exactly the right instant at some other node)
Thus, whenever a packet gets excited, it reaches its destination with constant probability.
Thus, on average, a packet needs to become excited only O(1) times to reach its destination.
Since a packet becomes excited every p’th time it gets deflected, it only gets deflected O(1/p)=O(m) times in expectation.
Finally, whenever a packet is NOT deflected, it gets close to its destination.

## Slide 68: Optimal Bufferless Routing…?
Proof-sketch:
An excited packet can only be deflected at its start node, or when trying to turn.
In both cases, the probability to be deflected is a small constant (because there needs to be another excited packet starting at exactly the right instant at some other node)
Thus, whenever a packet gets excited, it reaches its destination with constant probability.
Thus, on average, a packet needs to become excited only O(1) times to reach its destination.
Since a packet becomes excited every p’th time it gets deflected, it only gets deflected O(1/p)=O(m) times in expectation.
Finally, whenever a packet is NOT deflected, it gets close to its destination.
Notice that even with buffers, O(m) is optimal.
Hence, asymptotically, having no buffers does not harm the time-bounds of routing (in expectation) !

## Slide 69: Bibliography
“Principles and Practices of Interconnection Networks”, W. Dally and B. Towles, Morgan Kaufmann Publishers, Inc, 2003.
“A Case for Bufferless Routing in On-Chip Networks”, T. Moscibroda and O. Mutlu, ISCA 2009.
“Application-Aware Prioritization Mechanism for On-Chip Networks”, R. Das, O. Mutlu, T. Moscibroda, and C. Das, MICRO 2009.
“Aergia: Exploiting Packet-Latency Slack in On-Chip Networks”, R. Das, O. Mutlu, T. Moscibroda, and C. Das, ISCA 2010.
“Next Generation On-Chip Networks: What Kind of Congestion Control do we Need?”, G. Nychis, C. Fallin, T. Moscibroda, O. Mutlu, Hotnets 2010.
“Randomized Greedy Hot-Potato Routing”, C. Busch, M. Herlihy, and R. Wattenhofer, SODA 2000