## Slide 1: Computer Architecture: Memory Interference and QoS (Part II)
Prof. Onur Mutlu
Carnegie Mellon University

## Slide 2: Memory Interference and QoS Lectures
These slides are from a lecture delivered at INRIA (July 8, 2013)
Similar slides were used at the ACACES 2013 course
  http://users.ece.cmu.edu/~omutlu/acaces2013-memory.html

## Slide 3: QoS-Aware Memory Systems (Wrap Up)
Onur Mutlu
onur@cmu.edu
July 9, 2013
INRIA

## Slide 4: Slides for These Lectures
Architecting and Exploiting Asymmetry in Multi-Core
  http://users.ece.cmu.edu/~omutlu/pub/onur-INRIA-lecture1-asymmetry-jul-2-2013.pptx
A Fresh Look At DRAM Architecture
  http://www.ece.cmu.edu/~omutlu/pub/onur-INRIA-lecture2-DRAM-jul-4-2013.pptx
QoS-Aware Memory Systems
  http://users.ece.cmu.edu/~omutlu/pub/onur-INRIA-lecture3-memory-qos-jul-8-2013.pptx
QoS-Aware Memory Systems and Waste Management
  http://users.ece.cmu.edu/~omutlu/pub/onur-INRIA-lecture4-memory-qos-and-waste-management-jul-9-2013.pptx

## Slide 5: Videos for Similar Lectures
Basics (of Computer Architecture)
  http://www.youtube.com/playlist?list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ
Advanced (Longer versions of these lectures)
  http://www.youtube.com/playlist?list=PLVngZ7BemHHV6N0ejHhwOfLwTr8Q-UKXj

## Slide 6: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12][Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 7: ATLAS Pros and Cons
Upsides:
  Good at improving overall throughput (compute-intensive threads are prioritized)
  Low complexity
  Coordination among controllers happens infrequently
Downsides:
  Lowest/medium ranked threads get delayed significantly  high unfairness

## Slide 8: TCM: Thread Cluster Memory Scheduling
Yoongu Kim, Michael Papamichael, Onur Mutlu, and Mor Harchol-Balter, "Thread Cluster Memory Scheduling:
Exploiting Differences in Memory Access Behavior" 43rd International Symposium on Microarchitecture (MICRO),
pages 65-76, Atlanta, GA, December 2010. Slides (pptx) (pdf)
TCM Micro 2010 Talk

## Slide 9: Previous Scheduling Algorithms are Biased
No previous memory scheduling algorithm provides both the best fairness and system throughput
Chart: Weighted Speedup
| 7.21 | 8.166 | 8.26 | 8.527000000000001 | 8.778
FCFS | 8.513
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
System throughput bias
Fairness bias
Ideal
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
Notes: The problem is that previously proposed scheduling algorithms are biased.
Shown here is a plot, where the x-axis is weighted speedup, a metric of system throughput and system throughput increases as you move towards the right on the x-axis.
The y-axis is maximum slowdown, which is the slowdown of the most unfairly treated thread within a workload. Correspondingly, fairness increases as you move downwards on the y-axis.
Ideally, a memory scheduling algorithm would be situated towards the lower right part of the graph where fairness and system throughput are both high.
However, some previous algorithms are biased towards system throughput, whereas some are biased towards fairness, while others are optimized for neither.
The takeaway is that no previous memory scheduling algorithm provides both the best fairness and system throughput.

## Slide 10: Throughput vs. Fairness
  Take turns accessing memory
Fairness biased approach
thread C
thread B
thread A
less memory intensive
higher
priority
  Prioritize less memory-intensive threads
Throughput biased approach
  Good for throughput
starvation  unfairness
thread C
thread B
thread A
  Does not starve
not prioritized 
reduced throughput
Single policy for all threads is insufficient
Notes: So why do previous algorithms fail?
On the one hand there is the throughput biased approach that prioritizes less memory-intensive threads.
Servicing memory requests from such threads allow them to make progress in the processor, increasing throughput.
However, the most memory-intensive thread, thread C, remains persistently deprioritized and and becomes prone to starvation causing large slowdowns and, ultimately, unfairness.
On the other hand there is the fairness biased approach where threads take turns accessing the memory.
In this case, the most memory-intensive thread does not starve.
However, the least memory-intensive thread, thread A, is not prioritized, leading to reduced throughput.
As you can see, a single policy applied to all threads is insufficient since different threads have different memory access needs.

## Slide 11: Achieving the Best of Both Worlds
thread
thread
higher
priority
thread
thread
thread
thread
thread
thread
  Prioritize memory-non-intensive threads
For Throughput
  Unfairness caused by memory-intensive being prioritized over each other
    Shuffle thread ranking
  Memory-intensive threads have different vulnerability to interference
    Shuffle asymmetrically
For Fairness
thread
thread
thread
thread
Notes: So how do we achieve the best of both worlds? Our algorithm is based on the following insights:
First, we would like to prioritize the memory-non-intensive threads to increase system throughput.
Doing so does not degrade unfairness, since memory-non-intensive threads are inherently “light” and rarely cause interference for the memory-intensive threads.
For fairness, we discovered that unfairness is usually caused when one memory-intensive thread is prioritized over another.
As we’ve seen, the most deprioritized thread can starve.
To address this problem, we would like to shuffle their priority so that no single thread is persistently prioritized over another thread.
However, memory-intensive threads are not created equal.
They have different vulnerability to memory interference.
To address their differences, shuffling should be performed in an asymmetric manner.

## Slide 12: Thread Cluster Memory Scheduling [Kim+ MICRO’10]
Group threads into two clusters
Prioritize non-intensive cluster
Different policies for each cluster
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness
Notes: Our algorithm, Thread Cluster Memory Scheduling, first groups threads into two clusters.
Among the threads executing in the system, some are memory-non-intensive whereas some are memory-intensive.
We isolate the memory-non-intensive threads into the non-intensive cluster and the memory-intensive threads into the intensive cluster.
This is so that we can apply different policies for different threads.
Subsequently, we prioritize the non-intensive cluster over the intensive cluster since the non-intensive threads have greater potential for making progress IN THEIR CORES [ONUR].
Finally, we apply different policies within each cluster, one optimized for throughput and the other for fairness.

## Slide 13: Clustering Threads
Step1 Sort threads by MPKI (misses per kiloinstruction)
thread
thread
thread
thread
thread
thread
higher
MPKI
T
α < 10% ClusterThreshold
Intensive
cluster
αT
Non-intensive
cluster
T = Total memory bandwidth usage
Step2 Memory bandwidth usage αT divides clusters
Notes: To group threads into two clusters, we first sort threads according to their MPKI, which stands for last-level cache-misses per kiloinstruction and is a metric of memory intensity.
After sorting, the leftmost thread is the thread with the lowest MPKI.
We then define a quantity called T, which is the total memory bandwidth usage across all threads.
Second, we form the non-intensive cluster by including threads whose bandwidth usage sums up to a certain fraction of the memory bandwidth usage.
That fraction is defined by a parameter called the ClusterThreshold. I will show later in the presentation how adjusting this parameter we can trade off between throughput and fairness.
Lastly, the remaining threads become the intensive cluster.

## Slide 14: Prioritization Between Clusters
  Prioritize non-intensive cluster
Increases system throughput
  Non-intensive threads have greater potential for making progress
Does not degrade fairness
  Non-intensive threads are “light”
  Rarely interfere with intensive threads
>
priority
Notes: Between the two clusters, we statically prioritize the non-intensive cluster [ONUR: fixed plural  singular] so that non-intensive threads’ [ONUR: fixed wording] memory requests are serviced first.
This increases system throughput because non-intensive threads have greater potential for making progress BY QUICKLY RETURNING TO COMPUTE PERIODS IN THEIR CORES [ONUR].
Doing so does not degrade fairness, since non-intensive threads are “light” and consequently rarely interfere with intensive threads. [ONUR: removed “by design”… can be confusing if the listener is not in the right mindset]

## Slide 15: Non-Intensive Cluster
Prioritize threads according to MPKI
Increases system throughput
  Least intensive thread has the greatest potential for making progress in the processor
thread
thread
thread
thread
higher
priority
lowest MPKI
highest MPKI
Notes: Within the memory non-intensive cluster, threads are prioritized according to their memory intensity where the least intensive thread receives the highest priority. [ONUR: replaced latency-sensitive]
This is, again, to increase system throughput. The least intensive thread has the greatest potential for making progress.

## Slide 16: Intensive Cluster
Periodically shuffle the priority of threads
Is treating all threads equally good enough?
BUT: Equal turns ≠ Same slowdown
thread
thread
thread
  Increases fairness
  Most prioritized
higher
priority
thread
thread
thread
Notes: Within the intensive cluster, we periodically shuffle the priority of threads.
By shuffling, we can increase fairness, since every thread is given a fair chance of being the most prioritized.
Treating all threads in an such an equal manner may be good enough in some cases.
But we noticed that in other cases, giving each thread equal turns does not necessarily lead to equal slowdowns.
Specifically, threads are not created equal and some threads are more easily slowed down than others.

## Slide 17: Case Study: A Tale of Two Threads
Chart: Slowdown
| random-access | streaming
Series 1 | 11 | 1
Case Study: Two intensive threads contending
  random-access
  streaming
Prioritize random-access
Prioritize streaming
random-access thread is more easily slowed down
Chart: Slowdown
| random-access | streaming
Series 1 | 1 | 7
7x
prioritized
1x
11x
prioritized
1x
Which is slowed down more easily?
Notes: We illustrate how some threads are more easily slowed down than others using a case study, where two memory-intensive threads are contending for memory: a random-access thread and a streaming thread.
Which of these two threads is slowed down more easily?
In the first case, we prioritize the random-access thread and see that the streaming thread is slowed down by a factor of 7.
In the second case, we prioritize the streaming thread and see that the random-access thread is slowed down by a factor of 11.
Clearly, comparing the two cases, we see that the random-access threads is more easily slowed down.

## Slide 18: Why are Threads Different?
random-access
streaming
req
req
req
req
Bank 1
Bank 2
Bank 3
Bank 4
Memory
rows
All requests parallel
High bank-level parallelism
All requests  Same row
High row-buffer locality
req
req
req
req
activated row
req
req
req
req
req
req
req
req
stuck
Vulnerable to interference
Notes: ONUR: Again, if you prefer, you can use “vulnerable” instead of “susceptible.”
So why are these two threads different?
To explain their difference, we must examine their memory access behavior.
First, the memory comprises multiple memory banks which can be accessed in parallel. [ONUR: removed structurally]
Additionally, each bank is basically a two-dimensional bit-array and comprises multiple rows.
The random access thread distributes its memory requests, to different banks.
Across the banks, the requests are serviced concurrently and their individual latencies are overlapped.
Therefore, the random-access thread has high bank-level parallelism.
On the other hand, the streaming thread sends its memory requests to the same bank.
There it is serviced at the same row over and over again.
When consecutive requests are serviced at the same row, it is called a row-buffer hit and has a lower latency.
Therefore, the streaming thread has higher row-buffer locality.
What would happen if we put those threads together?
For the purpose of illustration, we will assume that the streaming thread is prioritized.
You can see that the random-access thread’s request becomes stuck behind those of the streaming thread at Bank 3.
This breaks the bank-level parallelism of the random-access thread and serializes its latency, leading to reduced performance.
This is why, the random-access thread is more susceptible to interference.
If the two threads were prioritized the other way around, the streaming thread would not be interfered with as much, since the random-access thread has only a single request to Bank 3.

## Slide 19: Niceness
How to quantify difference between threads?
  Vulnerability to interference
Bank-level parallelism
  Causes interference
Row-buffer locality
+
Niceness
-
Niceness
High
Low

## Slide 20: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
GOOD: Each thread prioritized once
 What can go wrong?
A
B
C
D
D
A
B
C
D

## Slide 21: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
 What can go wrong?
A
B
C
D
D
A
B
C
D
A
B
D
C
B
C
A
D
C
D
B
A
D
A
C
B
BAD: Nice threads receive lots of interference
GOOD: Each thread prioritized once

## Slide 22: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
GOOD: Each thread prioritized once
A
B
C
D
D
C
B
A
D

## Slide 23: Shuffling: Round-Robin vs. Niceness-Aware
Round-Robin shuffling
Niceness-Aware shuffling
Most prioritized
ShuffleInterval
Priority
Time
Nice thread
Least nice thread
A
B
C
D
D
C
B
A
D
D
A
C
B
B
A
C
D
A
D
B
C
D
A
C
B
GOOD: Each thread prioritized once
GOOD: Least nice thread stays
mostly deprioritized

## Slide 24: TCM Outline
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
1. Clustering
2. Between
Clusters
3. Non-Intensive
Cluster
4. Intensive
Cluster
Fairness
Throughput

## Slide 25: TCM: Quantum-Based Operation
Time
Previous quantum (~1M cycles)
During quantum:
Monitor thread behavior
Memory intensity
Bank-level parallelism
Row-buffer locality
Beginning of quantum:
Perform clustering
Compute niceness of intensive threads
Current quantum
(~1M cycles)
Shuffle interval
(~1K cycles)
Notes: Clustering is performed at regular time intervals called quanta.
THIS IS DONE [ONUR] to account for phase changes in threads’ memory access behavior.
During A [ONUR] quantum, TCM monitors each thread’s memory access behavior:
memory intensity, bank-level parallelism, and row-buffer locality.
At the beginning of the next quantum, TCM is invoked to perform clustering and calculate niceness for the intensive threads.
Throughout the quantum, shuffling of the intensive threads is performed periodically.

## Slide 26: TCM: Scheduling Algorithm
Highest-rank: Requests from higher ranked threads prioritized
    Non-Intensive cluster > Intensive cluster
    Non-Intensive cluster: lower intensity  higher rank
    Intensive cluster: rank shuffling
Row-hit: Row-buffer hit requests are prioritized
Oldest: Older requests are prioritized
Notes: To bring it all together, TCM comprises three simple request prioritization rules.
The first is the highest-rank rule, where requests from higher ranked threads are prioritized.
The intensive cluster is prioritized over the non-intensive cluster TO IMPROVE SYSTEM [ONUR] throughput.
Within the intensive cluster, threads are assigned higher rank in the order of decreasing intensity. This, again, is to increase SYSTEM [ONUR] throughput.
Within the non-intensive cluster, the rank of threads are periodically shuffled and does not stay constant, TO ACHIEVE FAIRNESS [ONUR].
As a tie-breaker, the second rule is row-hit where row-buffer hitting requests are prioritized.
Lastly, all else being the same, we prioritize the oldest request.

## Slide 27: TCM: Implementation Cost
Required storage at memory controller (24 cores)
No computation is on the critical path
Thread memory behavior | Storage
MPKI | ~0.2kb
Bank-level parallelism | ~0.6kb
Row-buffer locality | ~2.9kb
Total | < 4kbits
Notes: ONUR: Have a separate bullet saying “No computation is on the processor critical path; Can be approximated.”
Basically, DRAM latency is very long so we can afford to do this computation especially since we are doing it over intervals.
You can have 4 cores in the first bullet and remove the subbullet.

## Slide 28: Previous Work
FRFCFS [Rixner et al., ISCA00]: Prioritizes row-buffer hits
  Thread-oblivious  Low throughput & Low fairness
STFM [Mutlu et al., MICRO07]: Equalizes thread slowdowns
  Non-intensive threads not prioritized  Low throughput
PAR-BS [Mutlu et al., ISCA08]: Prioritizes oldest batch of requests while preserving bank-level parallelism
  Non-intensive threads not always prioritized  Low throughput
ATLAS [Kim et al., HPCA10]: Prioritizes threads with less memory service
  Most intensive thread starves  Low fairness

## Slide 29: TCM: Throughput and Fairness
Chart: Weighted Speedup
| 8.166 | 8.26 | 8.527000000000001 | 8.778 | 9.179
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
TCM | 7.074
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
TCM, a heterogeneous scheduling policy,
provides best fairness and system throughput
Notes: This figure shows the performance of the four previous scheduling algorithms in addition to TCM, averaged over 96 workloads.
FRFCFS has low system throughput and fairness.
STFM and PAR-BS is biased towards fairness, while ATLAS is biased towards system throughput.
TCM lies towards the lower right part of the figure and provides the best fairness and system throughput.
Compared to ATLAS, TCM provides approx 5% better throughput and 39% better fairness.
Compared to PAR-BS, TCM provides approx 5% better fairness and 8% better throughput.

## Slide 30: TCM: Fairness-Throughput Tradeoff
Chart: Weighted Speedup
| 12.73 | 13.0 | 13.03 | 13.04 | 12.97 | 12.81 | 12.66 | 12.48 | 13.11 | 13.21 | 13.21 | 13.19 | 13.16 | 13.06 | 13.6 | 13.76 | 13.61 | 13.68 | 13.65 | 13.62 | 14.49 | 14.58 | 14.8 | 14.84 | 14.83 | 14.43 | 14.04 | 14.4 | 14.63 | 14.79 | 14.92
FRFCFS | 9.825 | 6.73 | 5.84 | 5.38 | 5 | 5.07 | 5.5 | 5.73
STFM | 5.949 | 6.215 | 6.423 | 6.923 | 6.953 | 7.263
PAR-BS | 5.999 | 5.449 | 5.423 | 5.075 | 4.905 | 4.82
ATLAS | 7.018 | 7.139 | 7.422 | 7.501 | 7.552 | 7.458
TCM | 4.843 | 4.952 | 5.258 | 5.503 | 5.727
When configuration parameter is varied…
Adjusting ClusterThreshold
TCM allows robust fairness-throughput tradeoff
STFM
PAR-BS
ATLAS
TCM
Better system throughput
Better fairness
FRFCFS

## Slide 31: Operating System Support
ClusterThreshold is a tunable knob
  OS can trade off between fairness and throughput
Enforcing thread weights
  OS assigns weights to threads
  TCM enforces thread weights within each cluster

## Slide 32: Conclusion
No previous memory scheduling algorithm provides both high system throughput and fairness
  Problem: They use a single policy for all threads
TCM groups threads into two clusters
  Prioritize non-intensive cluster  throughput
  Shuffle priorities in intensive cluster  fairness
  Shuffling should favor nice threads  fairness
TCM provides the best system throughput and fairness

## Slide 33: TCM Pros and Cons
Upsides:
  Provides both high fairness and high performance
Downsides:
  Scalability to large buffer sizes?
  Effectiveness in a heterogeneous system?

## Slide 34: Staged Memory Scheduling
Rachata Ausavarungnirun, Kevin Chang, Lavanya Subramanian, Gabriel Loh, and Onur Mutlu, "Staged Memory Scheduling: Achieving High Performance
and Scalability in Heterogeneous Systems” 39th International Symposium on Computer Architecture (ISCA),
Portland, OR, June 2012.
SMS ISCA 2012 Talk

## Slide 35: SMS: Executive Summary
Observation: Heterogeneous CPU-GPU systems require memory schedulers with large request buffers
Problem: Existing monolithic application-aware memory scheduler designs are hard to scale to large request buffer sizes
Solution: Staged Memory Scheduling (SMS)
  decomposes the memory controller into three simple stages:
  1) Batch formation: maintains row buffer locality
  2) Batch scheduler: reduces interference between applications
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness
Notes: We observe that Heterogeneous CPU-GPU systems require memory schedulers with large request buffers and this becomes a problem for existing monolithic application-aware memory scheduler designs because they are hard to scale to large request buffer size
Our Solution, staged memory scheduling, decomposes MC into three simpler stages:
  1) Batch formation: maintains row buffer locality by forming batches of row-hitting requests.
  2) Batch scheduler: reduces interference between applications by picking the next batch to prioritize.
  3) DRAM command scheduler: issues requests to DRAM
Compared to state-of-the-art memory schedulers:
  SMS is significantly simpler and more scalable
  SMS provides higher performance and fairness, especially in heterogeneous CPU-GPU systems.

## Slide 36: SMS: Staged Memory Scheduling
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Batch Scheduler
Stage 1
Stage 2
Stage 3
Req
Monolithic Scheduler
Batch Formation
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through <click> stage 1, the batch formation, <click> stage 2, the batch scheduler, <click> stage 3, the DRAM command scheduler

## Slide 37: SMS: Staged Memory Scheduling
Stage 1
Stage 2
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Batch Scheduler
Batch Formation
Stage 3
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: Now, let me explain how the batch formation works …

## Slide 38: Putting Everything Together
Current Batch Scheduling Policy
SJF
Current Batch Scheduling Policy
RR
Batch Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Core 1
Core 2
Core 3
Core 4
Stage 1:
Batch
Formation
Stage 3: DRAM Command Scheduler
GPU
Stage 2:
Notes: In this example, the system consist of 4 CPU cores and a GPU, and the color represent a row the request wants to access. Similar color means these requests want to access the same row.
In the batch formation stage, memory requests that access the same row will be batched.
<click>
One criteria that a batch becomes ready to be scheduled is when the next request is going to a different row, as illustrated in this example at core 2 and core 3. <click click>
Another criteria is when the timeout for the batch formation expires.
This batching process will happen across all cores including the GPU
<click>
<click> and how the batch scheduler will select one of these front batch to send to <click> the DRAM command scheduler.
The scheduler can either use a shortest job poilcy
<click> which will pick this purple request because it is from an application with the fewest number of requests.
Or a round-robin policy
<click>
Whenever the bank is ready to schedule a next request. DRAM command scheduler will schedule the requests in an in-order manner.
<click>
Now that I told you about how SMS works, let me tell you about the complexity of SMS
<click … transition>

## Slide 39: Complexity
Compared to a row hit first scheduler, SMS consumes*
  66% less area
  46% less static power
Reduction comes from:
  Monolithic scheduler  stages of simpler schedulers
  Each stage has a simpler scheduler (considers fewer properties at a time to make the scheduling decision)
  Each stage has simpler buffers (FIFO instead of out-of-order)
  Each stage has a portion of the total buffer size (buffering is distributed across stages)
* Based on a Verilog model using 180nm library
Notes: <transition from the previous slide>
Now that I told you about how SMS works, let me tell you about the complexity of SMS.
Compared to a row hit first scheduler, which is the one of the simplest memory scheduling algorithm that has been proposed, SMS consumes 66% less area and 46% less static power
The reduction in area and static power comes from:
  Decoupling the monolithic scheduler into stages of simpler schedulers
  Each stage has simpler scheduler, which considers fewer properties at a time to make the scheduling decision
  Each stage has simpler buffers, which is a FIFO instead of out-of-order buffers
  Each stage has a portion of the total buffer size and buffering is distributed across stages

## Slide 40: Performance at Different GPU Weights
Chart: GPUweight
Best Previous
Scheduler
ATLAS
TCM
FR-FCFS
Notes: In this plot, we show the performance of SMS, compared to the best performing scheduler. Note that the best previous algorithm is different for different weights. We vary the GPU weight of 0.001 to 1000. The Y-Axis shows the system performance measured by dividing the CPU-GPU weighted speedup by the total weight to make sure it is bound between 0 and 1.

## Slide 41: Performance at Different GPU Weights
At every GPU weight, SMS outperforms the best previous scheduling algorithm for that weight
Chart: GPUweight
SMS
Best Previous
Scheduler
Notes: We found that at every GPU weight, we can configure the probablity of using shortest job first batch scheduling policy such that SMS outperforms the best previous mechanism for that weight

## Slide 42: Stronger Memory Service Guarantees
Lavanya Subramanian, Vivek Seshadri, Yoongu Kim, Ben Jaiyen, and Onur Mutlu, "MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA),
Shenzhen, China, February 2013. Slides (pptx)

## Slide 43: Strong Memory Service Guarantees
Goal: Satisfy performance bounds/requirements in the presence of shared main memory, prefetchers, heterogeneous agents, and hybrid memory
Approach:
  Develop techniques/models to accurately estimate the performance of an application/agent in the presence of resource sharing
  Develop mechanisms (hardware and software) to enable the resource partitioning/prioritization needed to achieve the required performance levels for all applications
  All the while providing high system performance

## Slide 44: MISE: Providing Performance Predictability in Shared Main Memory Systems
Lavanya Subramanian, Vivek Seshadri,
Yoongu Kim, Ben Jaiyen, Onur Mutlu
Notes: Hello everyone. My name is Lavanya Subramanian.
Today, I will present “MISE: Providing perfomance …”.
This is work done in collaboration with my co-authors Vivek ….

## Slide 45: Unpredictable Application Slowdowns
Chart: Slowdown
| leslie3d (core 0) | gcc (core 1)
Slowdown | 1.9 | 1.1
Chart: Slowdown
| leslie3d (core 0) | mcf (core 1)
Slowdown | 5.4 | 2.1
An application’s performance depends on
which application it is running with
Notes: This graph shows two applications from the SPEC CPU 2006 suite, leslie3d and gcc. These applications are run on either core of a two core system and share main memory. The y-axis shows each application’s slowdown as compared to when the application is run standalone on the same system.
Now, let’s look at leslie3d. It slows down by 2x when run with gcc.
Let’s look at another case when leslie3d is run with another application, mcf. Leslie now slows down by 5.5x, while it slowed down by 2x when run with gcc. Leslie experiences different slowdowns when run with different applications.
More generally, an application’s performance depends on which applications it is running with. Such performance unpredictability is undesirable….

## Slide 46: Need for Predictable Performance
There is a need for predictable performance
  When multiple applications share resources
  Especially if some applications require performance guarantees
Example 1: In mobile systems
  Interactive applications run with non-interactive applications
  Need to guarantee performance for interactive applications
Example 2: In server systems
  Different users’ jobs consolidated onto the same server
  Need to provide bounded slowdowns to critical jobs
Our Goal: Predictable performance
in the presence of memory interference
Notes: …because there is a need for predictable performance
When multiple applications share resources and
Especially when some applications require guarantees on performance.
For example, in mobile systems, interactive applications are run with non-interactive ones.
And there is a need to provide guarantees on performance to the interactive applications.
In server systems, different users’ jobs are heavily consolidated onto the same server.
In such a scenario, there is a need to achieve bounded slowdowns for critical jobs of users.
These are a couple of examples of systems that need predictable performance.
There are many other systems (such as …) in which performance predictability is necessary.
Therefore, our goal in this work is to provide predictable performance in the presence of memory interference.

## Slide 47: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: First, let me describe the key observations that enable us to estimate application slowdowns.

## Slide 48: Slowdown: Definition
Notes: Slowdown of an application is its performance when it is run stand alone on a system to its performance when it is sharing the system with other applications.
An application’s performance when it is sharing the system with other applications can be measured in a straightforward manner. However, measuring an application’s alone performance, without actually running it alone is harder.
This is where are first observation comes in.

## Slide 49: Key Observation 1
For a memory bound application,
Performance  Memory request service rate
Chart: Normalized Request Service Rate
| 0.358607859 | 0.408507739 | 0.532531575 | 0.580993121999996 | 0.632877307000005 | 0.690879954000007 | 0.726945501000005 | 0.796354682 | 0.837558983 | 0.938360254 | 0.948305607000005 | 1.0
omnetpp | 0.34972 | 0.39891 | 0.5217 | 0.56944 | 0.61954 | 0.67835 | 0.71425 | 0.78346 | 0.8265 | 0.928 | 0.94883 | 1
mcf | 0.34876 | 0.39942 | 0.4869 | 0.53653 | 0.54337 | 0.55102 | 0.58278 | 0.61457 | 0.65149 | 0.74316 | 0.84741 | 0.93386 | 0.9689 | 1
astar | 0.41586 | 0.48052 | 0.66786 | 0.72536 | 0.77686 | 0.79876 | 0.84877 | 0.88035 | 0.92559 | 0.95012 | 0.98596 | 1
Easy
Harder
Intel Core i7, 4 cores
Mem. Bandwidth: 8.5 GB/s
Notes: We observe that for a memory bound application, its performance is roughly proportional to the rate at which its memory requests are serviced.
This plot shows the results of our experiment on an Intel, 4-core system. We run omnetpp, a SPEC CPU 2006 benchmark along with another memory hog, whose memory intensity can be varied. This, in turn, lets us vary the rate at which the memory requests of omnetpp are serviced.
The x-axis shows the normalized request service rate of omnetpp, normalized to when it is run alone.
The y-axis shows the performance of omnetpp, normalized to when it is run alone.
As can be seen, there is a very strong, y=x like correlation between request service rate and performance.
We observe the same trend for various memory bound applications. Here are a couple of more examples.
Therefore, memory request service rate can be used as a proxy for performance.
Now, going back to the slowdown equation. We can replace performance by request service rate, based on our first observation, enabling us to express slowdown as the ratio of alone to shared request service rates.
Shared request service rate can be measured in a relatively straightforward manner when an application is run along with other applications.
Measuring alone request service rate, without actually running an application alone is harder. This is where our second observation comes into play.

## Slide 50: Key Observation 2
Request Service Rate Alone (RSRAlone) of an application can be estimated by giving the application highest priority in accessing memory
Highest priority  Little interference
(almost as if the application were run alone)
Notes: We observe that an application’s alone request service rate can be estimated by giving the application highest priority in accessing memory.
Because, when an application has highest priority, it receives little interference from other applications, almost as though the application were run alone.

## Slide 51: Key Observation 2
Request Buffer State
Main Memory
1. Run alone
Time units
Service order
Main Memory
1
2
Request Buffer State
Main Memory
2. Run with another application
Service order
Main Memory
1
2
3
Request Buffer State
Main Memory
3. Run with another application: highest priority
Service order
Main Memory
1
2
3
Time units
Time units
3
Notes: Here is an example.
An application, let’s call it the red application, is run by itself on a system. Two of its requests are queued at the memory controller request buffers. Since these are the only two requests queued up for main memory at this point, the memory controller schedules them back to back and they are serviced in two time units.
Now, the red application is run with another application, the blue application. The blue application’s request makes its way between two of the red application’s requests. A naïve memory scheduler could potentially schedule the requests in the order in which they arrived, delaying the red application’s second request by one time unit, as compared to when the application was run alone.
Next, let’s consider running the red and blue applications together, but give the red application highest priority. In this case, the memory scheduler schedules the two requests of the red application back to back, servicing them in two time units. Therefore, when the red application is given highest priority, its requests are serviced as though the application were run alone.

## Slide 52
Memory Interference-induced Slowdown Estimation (MISE) model for memory bound applications
Notes: Based on these two observations, our memory interference induced slowdown estimation (MISE) model for memory bound applications is as follows. Now, let’s analyze why this request service rate ratio based model holds for memory bound applications

## Slide 53: Key Observation 3
Memory-bound application
No interference
Compute Phase
Memory Phase
With interference
Memory phase slowdown dominates overall slowdown
time
time
Req
Req
Req
Req
Req
Req
Notes: A memory-bound application spends significant fraction of its execution time waiting for memory.
Let’s first look at the case when a memory-bound application is not receiving any interference.
The application does a small amount of compute at the core and then sends out a bunch of memory requests. The application cannot do any more compute until these requests are serviced.
Now, when this application experiences interference, the length of its compute phase does not change. However, the time taken to service the memory requests increases. In essence, since the application spends most of its time in the memory phase, the memory induced slowdown of the application dominates the overall slowdown of the application.

## Slide 54: Key Observation 3
Non-memory-bound application
time
time
No interference
Compute Phase
Memory Phase
With interference
Only memory fraction ( ) slows down with interference
Memory Interference-induced Slowdown Estimation (MISE) model for non-memory bound applications
Notes: However, this is not the case for a non-memory-bound application.
A non-memory-bound application spends a sizeable fraction of its time doing compute at the core and a smaller fraction of time waiting for memory. When the application experiences interference, the length of the compute phase does not change, whereas the memory phase slows down with interference.
Specifically, if alpha is the fraction of time the application spends in the memory phase, then 1 – alpha is the fraction of time it spends in the compute phase. The 1 – alpha fraction does not change with memory interference, however the alpha fraction slows down as the ratio of request service rate alone to request service rate shared.
We augment the MISE model to take this into account. Slowdown for non-memory-bound applications can be expressed as the sum of two quantities - 1 – alpha, the compute fraction that does not change with interference and the memory induced slowdown.

## Slide 55: Measuring RSRShared and α
Request Service Rate Shared (RSRShared)
  Per-core counter to track number of requests serviced
  At the end of each interval, measure
Memory Phase Fraction ( )
  Count number of stall cycles at the core
  Compute fraction of cycles stalled for memory
Notes: Shared request service rate can be measured using per-core counters to track the number of requests serviced during each interval.
At the end of the interval, SRSR can be computed as the number of requests serviced divided by the length of the interval.
Memory phase fraction of each application can be computed by counting the number of cycles the core stalls waiting for memory and then computing what fraction are these cycles of the interval length.
Measuring SRSR and alpha is the straightforward part. Now, for the more interesting part, estimating alone request service rate.

## Slide 56: Estimating Request Service Rate Alone (RSRAlone)
Divide each interval into shorter epochs
At the beginning of each epoch
  Memory controller randomly picks an application as the highest priority application
At the end of an interval, for each application, estimate
Goal: Estimate RSRAlone
How: Periodically give each application highest priority in accessing memory
Notes: Our goal is to estimate alone request service rate. To do this, we periodically give each application the highest priority in accessing memory, based on observation 2.
How exactly do we do this. First, each interval is divided into shorter epochs. At the beginning of each epoch, the memory controller picks one application at random and designates it the highest priority application. This way each application is given highest priority at different epochs during the interval.
At the end of the interval, ARSR is estimated for each application as the ratio of the number of requests of the application serviced during the high priority epochs to the number of cycles the application was given highest priority.
Now, is this an accurate way of estimating ARSR. It turns out not. We have been ignoring an inaccuracy all along.

## Slide 57: Inaccuracy in Estimating RSRAlone
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
When an application has highest priority
  Still experiences some interference
Request Buffer
State
Main Memory
Time units
Service order
Main Memory
1
2
3
Time units
Service order
Main Memory
1
2
3
Interference Cycles
High Priority
Main Memory
Time units
Service order
Main Memory
1
2
3
Request Buffer
State
Notes: That is, even when an application has highest priority, it still experiences some interference from other applications.
Here is an example showing why.
The red application has highest priority and is run along with another application, the blue application. First, there is just one request in the request buffer and it is from the red application. Since this is the only request, it is scheduled by the memory controller and completes in one time unit.
While this request is being serviced, there comes another request from the blue application. Our memory controller is work conserving and schedules another application’s request, if there is no request from the red application. So, it schedules the blue application’s request next.
However, just as the blue application’s request is being scheduled comes another request from the red application. Ideally, we would like to pre-empt the blue application’s request. However, because of the way DRAM operates, preempting the blue application’s request incurs overhead. Therefore, the red application’s request would have to wait until the blue application’s request completes and only then is it serviced. These extra cycles that the red application spent waiting for the blue application’s request to complete are interference cycles that it would not have experienced had it been running alone.

## Slide 58: Accounting for Interference in RSRAlone Estimation
Solution: Determine and remove interference cycles from RSRAlone calculation
A cycle is an interference cycle if
  a request from the highest priority application is waiting in the request buffer and
  another application’s request was issued previously
Notes: The solution to account for this interference is to determine and remove such interference cycles from the ARSR computation.
How we do this is to subtract these cycles from the number of high priority epoch cycles.
Now, the question is how do we determine which cycles are interference cycles.
We deem a cycle an interference cycle if …. (read from slide)

## Slide 59: Outline
1. Estimate Slowdown
  Key Observations
  Implementation
  MISE Model: Putting it All Together
  Evaluating the Model
2. Control Slowdown
  Providing Soft Slowdown Guarantees
  Minimizing Maximum Slowdown
Notes: Having described the key observations behind our model and its implementation, we will put it all together

## Slide 60: MISE Model: Putting it All Together
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure RSRShared,
Estimate RSRAlone
Measure RSRShared,
Estimate RSRAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 61: Previous Work on Slowdown Estimation
Previous work on slowdown estimation
  STFM (Stall Time Fair Memory) Scheduling [Mutlu+, MICRO ‘07]
  FST (Fairness via Source Throttling) [Ebrahimi+, ASPLOS ‘10]
  Per-thread Cycle Accounting [Du Bois+, HiPEAC ‘13]
Basic Idea:
Hard
Easy
Count number of cycles application receives interference
Notes: The most relevant previous works on slowdown estimation are STFM, stall time fair memory scheduling and FST, fairness via source throttling.
FST employs similar mechanisms as STFM for memory-induced slowdown estimation, therefore, I will focus on STFM for the rest of the evaluation.
STFM estimates slowdown as the ratio of alone to shared stall times.
Stall time shared is easy to measure, analogous to shared request service rate
Stall time alone is harder and STFM estimates it by counting the number of cycles an application receives interference from other applications.

## Slide 62: Two Major Advantages of MISE Over STFM
Advantage 1:
  STFM estimates alone performance while an application is receiving interference  Hard
  MISE estimates alone performance while giving an application the highest priority  Easier
Advantage 2:
  STFM does not take into account compute phase for non-memory-bound applications
  MISE accounts for compute phase  Better accuracy
Notes: Let me now present the two major advantages of MISE over STFM, qualitatively.
First, STFM estimates alone performance of an application while it is receiving interference. This is hard because of BLP effects.
MISE addresses this difficulty by giving an application highest priority and then estimating its alone performance.
Second, STFM does not take into account compute phase for non-mem-bound applications. MISE accounts for compute phase and hence achieves better accuracy.

## Slide 63: Methodology
Configuration of our simulated system
  4 cores
  1 channel, 8 banks/channel
  DDR3 1066 DRAM
  512 KB private cache/core
Workloads
  SPEC CPU2006
  300 multi programmed workloads
Notes: Next, I will quantitatively compare MISE and STFM. Before that, let me present our methodology.
We carry out our evaluations on a 4-core, 1-channel DDR3 1066 DRAM system.
Our workloads are composed of SPEC CPU 2006 applications. We build 300 multiprogrammed workloads from these applications.

## Slide 64: Quantitative Comparison
Chart: Million Cycles
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 2.7467 | 2.8146 | 2.981 | 2.6916 | 3.5156 | 2.4446 | 3.3601 | 3.2667 | 2.8783 | 2.9401 | 2.7229 | 2.9719 | 2.71 | 2.1736 | 2.0285 | 2.4098 | 2.0056 | 2.2585 | 2.1279 | 2.4625
STFM | 1.8517 | 1.9219 | 1.8786 | 1.8294 | 1.9487 | 1.8759 | 1.7936 | 1.7677 | 1.83 | 1.817 | 1.7232 | 1.7709 | 1.704 | 1.6746 | 1.6715 | 1.7352 | 1.6427 | 1.7084 | 1.6918 | 1.7477
MISE | 2.6655 | 2.8713 | 2.8244 | 2.6053 | 3.1741 | 2.6867 | 3.5471 | 3.4317 | 3.3 | 2.6747 | 2.8604 | 3.0821 | 2.8909 | 2.235 | 2.1161 | 2.3639 | 1.999 | 2.0667 | 2.1632 | 2.3161
SPEC CPU 2006 application
leslie3d
Notes: This graph shows the actual slowdown of leslie3d, a memory-bound application, with time (in million cycles).
Here are slowdown estimates from STFM and here are slowdown estimates from MISE. As can be seen, MISE’s slowdown estimates are much closer to the actual slowdowns. This is because MISE estimates leslie’s alone performance while giving it highest priority, whereas STFM tries to estimate it while leslie receives interference from other applications.

## Slide 65: Comparison to STFM
cactusADM
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.495 | 1.5295 | 1.6709 | 1.5475 | 1.6605 | 1.5731 | 1.9783 | 1.7095 | 1.5337 | 1.5256 | 1.4754 | 1.5235 | 1.5214 | 1.7913 | 1.6855 | 1.6301 | 1.5933 | 1.6732 | 1.5495 | 1.6973
STFM | 1.25 | 1.3555 | 1.3435 | 1.3721 | 1.3293 | 1.3149 | 1.2341 | 1.3128 | 1.3228 | 1.3579 | 1.3509 | 1.344 | 1.4008 | 1.3967 | 1.5397 | 1.5867 | 1.5517 | 1.5683 | 1.5638 | 1.3614
MISE | 1.5723 | 1.5685 | 1.6897 | 1.5829 | 1.73 | 1.6866 | 2.1706 | 1.8114 | 1.5947 | 1.5898 | 1.5347 | 1.5537 | 1.6001 | 1.8673 | 1.7348 | 1.6758 | 1.6313 | 1.7322 | 1.6362 | 1.7298
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.7536 | 1.697 | 1.8734 | 1.7248 | 1.9225 | 1.6413 | 1.9296 | 2.1339 | 2.0504 | 1.9754 | 1.8732 | 2.1705 | 2.0085 | 2.239 | 2.2425 | 2.2469 | 1.9042 | 2.3715 | 2.0927 | 2.5902
STFM | 1.3661 | 1.3843 | 1.3635 | 1.3908 | 1.3589 | 1.35 | 1.3746 | 1.5894 | 1.5811 | 1.5995 | 1.5987 | 1.5832 | 1.5771 | 2.0246 | 1.9878 | 1.9883 | 1.9797 | 1.9406 | 1.9709 | 1.9629
MISE | 1.8607 | 1.9645 | 1.9765 | 1.8835 | 2.5202 | 1.8326 | 2.2231 | 2.3347 | 2.178 | 2.097 | 2.1736 | 2.1054 | 2.0591 | 2.3181 | 2.2502 | 2.3946 | 2.1703 | 2.5387 | 2.2735 | 2.6647
GemsFDTD
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.9414 | 2.1412 | 2.406 | 2.0632 | 2.7223 | 2.6572 | 3.1068 | 3.1879 | 2.6035 | 2.4937 | 2.4704 | 2.8774 | 2.6478 | 2.6947 | 2.7804 | 2.9653 | 2.8228 | 2.5796 | 2.6027 | 2.7846
STFM | 1.5023 | 1.4705 | 1.8931 | 1.4971 | 1.6676 | 1.6306 | 1.8055 | 1.7004 | 1.5827 | 1.7021 | 1.7571 | 1.8054 | 1.974 | 2.2827 | 2.3098 | 2.107 | 1.6316 | 2.0168 | 2.0447 | 2.0375
MISE | 1.916 | 2.3469 | 2.5021 | 2.481 | 2.7434 | 2.413 | 3.2611 | 3.5557 | 2.6948 | 2.6542 | 3.0171 | 2.4489 | 2.5681 | 2.7574 | 3.1405 | 3.0343 | 2.527 | 2.8438 | 3.1033 | 3.2769
soplex
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0179 | 1.0228 | 1.5311 | 1.2016 | 1.0185 | 1.0121 | 1.0059 | 1.0071 | 1.1261 | 1.5714 | 1.0808 | 1.0167 | 1.0097 | 1.2303 | 1.0956 | 1.0308 | 1.0187 | 1.3242 | 1.3257 | 1.0134
STFM | 2.6564 | 2.8136 | 2.323 | 1.9913 | 2.1243 | 2.8472 | 2.9844 | 2.4594 | 2.5397 | 2.2388 | 3.0174 | 2.8437 | 3.3951 | 3.9402 | 2.5308 | 2.8686 | 3.3191 | 2.5052 | 2.3033 | 2.0445
MISE | 1.0005 | 1.0032 | 1.7563 | 1.0691 | 0.99707 | 1.0011 | 1.0016 | 0.99869 | 1.0593 | 1.3748 | 1.0555 | 1.0003 | 1.0006 | 1.0639 | 1.0105 | 0.98886 | 1.0009 | 0.9221 | 1.0907 | 1.0039
wrf
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0394 | 1.0432 | 1.0258 | 1.0358 | 1.031 | 1.0316 | 1.0304 | 1.0232 | 1.0226 | 1.0158 | 1.0543 | 1.0328 | 1.0751 | 1.0632 | 1.0517 | 1.053 | 1.029 | 1.0322 | 1.031 | 1.0246
STFM | 2.1276 | 2.0414 | 1.9127 | 1.8201 | 2.3708 | 1.9609 | 1.9559 | 2.062 | 2.2477 | 2.173 | 3.9673 | 2.3084 | 2.4138 | 2.5477 | 2.8093 | 2.6087 | 2.1795 | 1.9627 | 1.8871 | 2.0011
MISE | 1.0191 | 1.0068 | 1.0168 | 0.98223 | 1.031 | 0.96844 | 1.0017 | 1.0177 | 0.99417 | 1.0091 | 1.0383 | 1.0293 | 1.0276 | 1.0128 | 1.0242 | 1.0231 | 0.99687 | 1.0223 | 0.89507 | 1.0191
calculix
Chart: Slowdown
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 70.0 | 75.0 | 80.0 | 85.0 | 90.0 | 95.0 | 100.0
Actual | 1.0008 | 1.0011 | 1.0029 | 1.0014 | 1.0016 | 1.0015 | 1.0038 | 1.0016 | 1.0011 | 1.0034 | 1.0391 | 1.1297 | 1.0014 | 1.0018 | 1.0019 | 1.002 | 1.0012 | 1.0008 | 1.0011 | 1.0012
STFM | 2.5587 | 2.6401 | 2.5897 | 1.8924 | 2.9635 | 3.1523 | 2.659 | 2.2124 | 3.2205 | 2.9929 | 3.5898 | 2.7107 | 2.1336 | 3.0915 | 3.0289 | 3.0638 | 3.0873 | 2.3554 | 2.7464 | 2.2834
MISE | 1.0002 | 1.0002 | 1.0015 | 1.0003 | 1.0007 | 0.99984 | 1.0012 | 0.99949 | 0.99671 | 1.0015 | 0.99044 | 0.86466 | 1.0003 | 1.0004 | 1.0006 | 0.99474 | 0.99903 | 0.99882 | 1.0001 | 1.0004
povray
Average error of MISE: 8.2%
Average error of STFM: 29.4%
(across 300 workloads)
Notes: Several more applications. For most applications, MISE’s slowdown estimates are more accurate.
On average, MISE’s error is 8.2%, while STFM’s error is 29.4%, across our 300 workloads.

## Slide 66: Providing “Soft” Slowdown Guarantees
Goal
  1. Ensure QoS-critical applications meet a prescribed slowdown bound
  2. Maximize system performance for other applications
Basic Idea
  Allocate just enough bandwidth to QoS-critical application
  Assign remaining bandwidth to other applications
Notes: The goal of this mechanism is to .. <read off slide>.
The basic idea is to allocate just enough bandwidth the QoS-critical application, while assigning the remaining bandwidth among the other applications.

## Slide 67: MISE-QoS: Mechanism to Provide Soft QoS
Assign an initial bandwidth allocation to QoS-critical application
Estimate slowdown of QoS-critical application using the MISE model
After every N intervals
  If slowdown > bound B +/- ε, increase bandwidth allocation
  If slowdown < bound B +/- ε, decrease bandwidth allocation
When slowdown bound not met for N intervals
  Notify the OS so it can migrate/de-schedule jobs
Notes: SLIDE NEEDS WORK

## Slide 68: Methodology
Each application (25 applications in total) considered the QoS-critical application
Run with 12 sets of co-runners of different memory intensities
Total of 300 multiprogrammed workloads
Each workload run with 10 slowdown bound values
Baseline memory scheduling mechanism
  Always prioritize QoS-critical application
  [Iyer+, SIGMETRICS 2007]
  Other applications’ requests scheduled in FRFCFS order
  [Zuravleff +, US Patent 1997, Rixner+, ISCA 2000]
Notes: Read off slide

## Slide 69: A Look at One Workload
Chart: Slowdown
| leslie3d | hmmer | lbm | omnetpp
AlwaysPrioritize | 1.9301 | 2.511 | 2.8159 | 2.7346
MISE-QoS-10/1 | 2.8374 | 2.2769 | 2.0523 | 2.0142
MISE-QoS-10/3 | 2.6976 | 2.3196 | 2.1221 | 2.084
MISE-QoS-10/5 | 2.0128 | 2.5056 | 2.6593 | 2.5534
MISE-QoS-10/7 | 1.9063 | 2.508 | 2.8014 | 2.6609
MISE-QoS-10/9 | 1.9063 | 2.508 | 2.8014 | 2.6609
QoS-critical
non-QoS-critical
MISE is effective in
meeting the slowdown bound for the QoS-critical application
improving performance of non-QoS-critical applications
Slowdown Bound = 10
Slowdown Bound = 3.33
Slowdown Bound = 2

## Slide 70: Effectiveness of MISE in Enforcing QoS
 | Predicted Met | Predicted Not Met
QoS Bound Met | 78.8% | 2.1%
QoS Bound Not Met | 2.2% | 16.9%
Across 3000 data points
MISE-QoS meets the bound for 80.9% of workloads
AlwaysPrioritize meets the bound for 83% of workloads
MISE-QoS correctly predicts whether or not the bound is met for 95.7% of workloads

## Slide 71: Performance of Non-QoS-Critical Applications
Chart: Number of Memory Intensive Applications
| 0 | 1 | 2 | 3 | Avg
AlwaysPrioritize | 1.2932 | 0.92684 | 0.63783 | 0.47247 | 0.83259
MISE-QoS-10/1 | 1.3105 | 1.0515 | 0.75708 | 0.556 | 0.91875
MISE-QoS-10/3 | 1.3105 | 1.0471 | 0.75276 | 0.54982 | 0.91504
MISE-QoS-10/5 | 1.3104 | 1.0268 | 0.71476 | 0.51722 | 0.89229
MISE-QoS-10/7 | 1.3101 | 0.96233 | 0.65406 | 0.47556 | 0.85051
MISE-QoS-10/9 | 1.2966 | 0.92898 | 0.64287 | 0.47149 | 0.83499
Higher performance when bound is loose
When slowdown bound is 10/3
MISE-QoS improves system performance by 10%

## Slide 72: Other Results in the Paper
Sensitivity to model parameters
  Robust across different values of model parameters
Comparison of STFM and MISE models in enforcing soft slowdown guarantees
  MISE significantly more effective in enforcing guarantees
Minimizing maximum slowdown
  MISE improves fairness across several system configurations

## Slide 73: Summary
Uncontrolled memory interference slows down applications unpredictably
Goal: Estimate and control slowdowns
Key contribution
  MISE: An accurate slowdown estimation model
  Average error of MISE: 8.2%
Key Idea
  Request Service Rate is a proxy for performance
  Request Service Rate Alone estimated by giving an application highest priority in accessing memory
Leverage slowdown estimates to control slowdowns
  Providing soft slowdown guarantees
  Minimizing maximum slowdown

## Slide 74: MISE: Providing Performance Predictability in Shared Main Memory Systems
Lavanya Subramanian, Vivek Seshadri,
Yoongu Kim, Ben Jaiyen, Onur Mutlu

## Slide 75: Memory Scheduling for Parallel Applications
Eiman Ebrahimi, Rustam Miftakhutdinov, Chris Fallin,
Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Parallel Application Memory Scheduling" Proceedings of the 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 76: Handling Interference in Parallel Applications
Threads in a multithreaded application are inter-dependent
Some threads can be on the critical path of execution due to synchronization; some threads are not
How do we schedule requests of inter-dependent threads to maximize multithreaded application performance?
  Idea: Estimate limiter threads likely to be on the critical path and prioritize their requests; shuffle priorities of non-limiter threads to reduce memory interference among them [Ebrahimi+, MICRO’11]
  Hardware/software cooperative limiter thread estimation:
    Thread executing the most contended critical section
    Thread that is falling behind the most in a parallel for loop
PAMS Micro 2011 Talk

## Slide 77: Aside: Self-Optimizing Memory Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA),
pages 39-50, Beijing, China, June 2008. Slides (pptx)

## Slide 78: Why are DRAM Controllers Difficult to Design?
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers
Need to handle DRAM refresh
Need to optimize for performance (in the presence of constraints)
  Reordering is not simple
  Predicting the future?

## Slide 79: Many DRAM Timing Constraints
From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.

## Slide 80: More on DRAM Operation and Constraints
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 81: Self-Optimizing DRAM Controllers
Problem: DRAM controllers difficult to design  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: Design a memory controller that adapts its scheduling policy decisions to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent that dynamically and continuously learns and employs the best scheduling policy.

## Slide 82: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 83: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 84: Performance Results

## Slide 85: QoS-Aware Memory Systems: The Dumb Resources Approach

## Slide 86: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 87: Fairness via Source Throttling
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance
Fairness Substrate for Multi-Core Memory Systems" 15th Intl. Conf. on Architectural Support for Programming Languages and Operating Systems (ASPLOS),
pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)
FST ASPLOS 2010 Talk

## Slide 88: Many Shared Resources
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM Bank K
...
Shared Memory
Resources
Chip Boundary
On-chip
Off-chip
88

## Slide 89: The Problem with “Smart Resources”
Independent interference control mechanisms in caches, interconnect, and memory can contradict each other
Explicitly coordinating mechanisms for different resources requires complex implementation
How do we enable fair sharing of the entire memory system by controlling interference in a coordinated manner?

## Slide 90: An Alternative Approach: Source Throttling
Manage inter-thread interference at the cores, not at the shared resources
Dynamically estimate unfairness in the memory system
Feed back this information into a controller
Throttle cores’ memory access rates accordingly
  Whom to throttle and by how much depends on performance target (throughput, fairness, per-thread QoS, etc)
  E.g., if unfairness > system-software-specified target then throttle down core causing unfairness & throttle up core that was unfairly treated
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS’10, TOCS’12.

## Slide 91: Fairness via Source Throttling (FST) [ASPLOS’10]
91
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
(limit injection rate and parallelism)
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
⎪
⎨
⎪
⎧
⎩
Slowdown Estimation
Time
Interval 1
Interval 2
Interval 3
Runtime Unfairness
Evaluation
Dynamic
Request Throttling

## Slide 92: System Software Support
Different fairness objectives can be configured by system software
  Keep maximum slowdown in check
    Estimated Max Slowdown < Target Max Slowdown
  Keep slowdown of particular applications in check to achieve a particular performance target
    Estimated Slowdown(i) < Target Slowdown(i)
Support for thread priorities
  Weighted Slowdown(i) = Estimated Slowdown(i) x Weight(i)

## Slide 93: Source Throttling Results: Takeaways
Source throttling alone provides better performance than a combination of “smart” memory scheduling and fair caching
  Decisions made at the memory scheduler and the cache sometimes contradict each other
Neither source throttling alone nor “smart resources” alone provides the best performance
Combined approaches are even more powerful
  Source throttling and resource-based interference control

## Slide 94: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12] [Subramanian+, HPCA’13]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 95: Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via
Application-Aware Memory Channel Partitioning” 44th International Symposium on Microarchitecture (MICRO),
Porto Alegre, Brazil, December 2011. Slides (pptx)
MCP Micro 2011 Talk

## Slide 96: Another Way to Reduce Memory Interference
Memory Channel Partitioning
  Idea: System software maps badly-interfering applications’ pages to different channels [Muralidhara+, MICRO’11]
Separate data of low/high intensity and low/high row-locality applications
Especially effective in reducing interference of threads with “medium” and “heavy” memory intensity
  11% higher performance over existing systems (200 workloads)
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Channel 1
Bank 0
Bank 1
Bank 0
Conventional Page Mapping
Time Units
1
2
3
4
5
Channel Partitioning
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Bank 0
Bank 1
Bank 0
Time Units
1
2
3
4
5
Channel 1

## Slide 97: Memory Channel Partitioning (MCP) Mechanism
1. Profile applications
2. Classify applications into groups
3. Partition channels between application groups
4. Assign a preferred channel to each application
5. Allocate application pages to preferred channel
Hardware
System Software

## Slide 98: 2. Classify Applications
Test MPKI
High Intensity
High
Low
Low Intensity
Test RBH
High Intensity
Low Row-Buffer Locality
Low
High Intensity
High Row-Buffer Locality
High

## Slide 99: Summary: Memory QoS
Technology, application, architecture trends dictate new needs from memory system
A fresh look at (re-designing) the memory hierarchy
  Scalability: DRAM-System Codesign and New Technologies
  QoS: Reducing and controlling main memory interference: QoS-aware memory system design
  Efficiency: Customizability, minimal waste, new technologies
QoS-unaware memory: uncontrollable and unpredictable
Providing QoS awareness improves performance, predictability, fairness, and utilization of the memory system

## Slide 100: Summary: Memory QoS Approaches and Techniques
Approaches: Smart vs. dumb resources
  Smart resources: QoS-aware memory scheduling
  Dumb resources: Source throttling; channel partitioning
  Both approaches are effective in reducing interference
  No single best approach for all workloads
Techniques: Request/thread scheduling, source throttling, memory partitioning
  All approaches are effective in reducing interference
  Can be applied at different levels: hardware vs. software
  No single best technique for all workloads
Combined approaches and techniques are the most powerful
  Integrated Memory Channel Partitioning and Scheduling [MICRO’11]
MCP Micro 2011 Talk

## Slide 101: Computer Architecture: Memory Interference and QoS (Part II)
Prof. Onur Mutlu
Carnegie Mellon University