## Slide 1: Computer Architecture: Runahead Execution
Prof. Onur Mutlu
Carnegie Mellon University

## Slide 2: A Note on This Lecture
  These slides are partly from 18-447 Spring 2013, Computer Architecture, Lecture 28: Runahead Execution
Video of that lecture:
  http://www.youtube.com/watch?v=z8YpjqXQJIA

## Slide 3: Readings
Required
  Mutlu et al., “Runahead execution”, HPCA 2003.
  Srinath et al., “Feedback directed prefetching”, HPCA 2007.
Optional
  Mutlu et al., “Efficient Runahead Execution: Power-Efficient Memory Latency Tolerance,” ISCA 2005, IEEE Micro Top Picks 2006.
  Mutlu et al., “Address-Value Delta (AVD) Prediction,” MICRO 2005.
  Armstrong et al., “Wrong Path Events,” MICRO 2004.

## Slide 4: Tolerating Memory Latency

## Slide 5: Latency Tolerance
An out-of-order execution processor tolerates latency of multi-cycle operations by executing independent instructions concurrently
  It does so by buffering instructions in reservation stations and reorder buffer
  Instruction window: Hardware resources needed to buffer all decoded but not yet retired/committed instructions
What if an instruction takes 500 cycles?
  How large of an instruction window do we need to continue decoding?
  How many cycles of latency can OoO tolerate?

## Slide 6: Stalls due to Long-Latency Instructions
When a long-latency instruction is not complete, it blocks instruction retirement.
  Because we need to maintain precise exceptions
Incoming instructions fill the instruction window (reorder buffer, reservation stations).
Once the window is full, processor cannot place new instructions into the window.
  This is called a full-window stall.
A full-window stall prevents the processor from making progress in the execution of the program.

## Slide 7: Full-window Stall Example
ADD R2  R2, 64
STOR mem[R2]  R4
ADD R4  R4, R5
MUL R4  R4, R3
LOAD R3  mem[R2]
ADD R2  R2, 8
BEQ R1, R0, target
LOAD R1  mem[R5]
Oldest
L2 Miss! Takes 100s of cycles.
8-entry instruction window:
Independent of the L2 miss,
executed out of program order,
but cannot be retired.
Younger instructions cannot be executed
because there is no space in the instruction window.
The processor stalls until the L2 Miss is serviced.
L2 cache misses are responsible for most full-window stalls.
LOAD R3  mem[R2]

## Slide 8: Cache Misses Responsible for Many Stalls
512KB L2 cache, 500-cycle DRAM latency, aggressive stream-based prefetcher
Data averaged over 147 memory-intensive benchmarks on a high-end x86 processor model
L2 Misses

## Slide 9: How Do We Tolerate Stalls Due to Memory?
Two major approaches
  Reduce/eliminate stalls
  Tolerate the effect of a stall when it happens
Four fundamental techniques to achieve these
  Caching
  Prefetching
  Multithreading
  Out-of-order execution
Many techniques have been developed to make these four fundamental techniques more effective in tolerating memory latency

## Slide 10: Memory Latency Tolerance Techniques
Caching [initially by Wilkes, 1965]
  Widely used, simple, effective, but inefficient, passive
  Not all applications/phases exhibit temporal or spatial locality
Prefetching [initially in IBM 360/91, 1967]
  Works well for regular memory access patterns
  Prefetching irregular access patterns is difficult, inaccurate, and hardware-intensive
Multithreading [initially in CDC 6600, 1964]
  Works well if there are multiple threads
  Improving single thread performance using multithreading hardware is an ongoing research effort
Out-of-order execution [initially by Tomasulo, 1967]
  Tolerates irregular cache misses that cannot be prefetched
  Requires extensive hardware resources for tolerating long latencies
  Runahead execution alleviates this problem (as we will see in a later lecture)

## Slide 11: Runahead Execution

## Slide 12: Small Windows: Full-window Stalls
ADD R2  R2, 64
STOR mem[R2]  R4
ADD R4  R4, R5
MUL R4  R4, R3
LOAD R3  mem[R2]
ADD R2  R2, 8
BEQ R1, R0, target
LOAD R1  mem[R5]
Oldest
L2 Miss! Takes 100s of cycles.
8-entry instruction window:
Independent of the L2 miss,
executed out of program order,
but cannot be retired.
Younger instructions cannot be executed
because there is no space in the instruction window.
The processor stalls until the L2 Miss is serviced.
L2 cache misses are responsible for most full-window stalls.
LOAD R3  mem[R2]

## Slide 13: Impact of L2 Cache Misses
512KB L2 cache, 500-cycle DRAM latency, aggressive stream-based prefetcher
Data averaged over 147 memory-intensive benchmarks on a high-end x86 processor model
L2 Misses

## Slide 14: Impact of L2 Cache Misses
500-cycle DRAM latency, aggressive stream-based prefetcher
Data averaged over 147 memory-intensive benchmarks on a high-end x86 processor model
L2 Misses

## Slide 15: The Problem
Out-of-order execution requires large instruction windows to tolerate today’s main memory latencies.
As main memory latency increases, instruction window size should also increase to fully tolerate the memory latency.
Building a large instruction window is a challenging task if we would like to achieve
  Low power/energy consumption (tag matching logic, ld/st buffers)
  Short cycle time (access, wakeup/select latencies)
  Low design and verification complexity

## Slide 16: Efficient Scaling of Instruction Window Size
One of the major research issues in out of order execution
How to achieve the benefits of a large window with a small one (or in a simpler way)?
How do we efficiently tolerate memory latency with the machinery of out-of-order execution (and a small instruction window)?

## Slide 17: Memory Level Parallelism (MLP)
Idea: Find and service multiple cache misses in parallel so that the processor stalls only once for all misses
  Enables latency tolerance: overlaps latency of different misses
How to generate multiple misses?
  Out-of-order execution, multithreading, runahead, prefetching
time
A
B
C
isolated miss
parallel miss

## Slide 18: Runahead Execution (I)
A technique to obtain the memory-level parallelism benefits of a large instruction window
When the oldest instruction is a long-latency cache miss:
  Checkpoint architectural state and enter runahead mode
In runahead mode:
  Speculatively pre-execute instructions
  The purpose of pre-execution is to generate prefetches
  L2-miss dependent instructions are marked INV and dropped
Runahead mode ends when the original miss returns
  Checkpoint is restored and normal execution resumes
Mutlu et al., “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors,” HPCA 2003.

## Slide 19: Runahead Example
Compute
Compute
Compute
Load 1 Miss
Miss 1
Stall
Compute
Load 2 Miss
Miss 2
Stall
Load 1 Hit
Load 2 Hit
Compute
Load 1 Miss
Runahead
Load 2 Miss
Load 2 Hit
Miss 1
Miss 2
Compute
Load 1 Hit
Saved Cycles
Perfect Caches:
Small Window:
Runahead:

## Slide 20: Benefits of Runahead Execution
Instead of stalling during an L2 cache miss:
Pre-executed loads and stores independent of L2-miss instructions generate very accurate data prefetches:
  For both regular and irregular access patterns
Instructions on the predicted program path are prefetched into the instruction/trace cache and L2.
Hardware prefetcher and branch predictor tables are trained using future access information.

## Slide 21: Runahead Execution Mechanism
Entry into runahead mode
  Checkpoint architectural register state
Instruction processing in runahead mode
Exit from runahead mode
  Restore architectural register state from checkpoint

## Slide 22: Instruction Processing in Runahead Mode
Compute
Load 1 Miss
Runahead
Miss 1
Runahead mode processing is the same as normal instruction processing, EXCEPT:
It is purely speculative: Architectural (software-visible) register/memory state is NOT updated in runahead mode.
L2-miss dependent instructions are identified and treated specially.
  They are quickly removed from the instruction window.
  Their results are not trusted.

## Slide 23: L2-Miss Dependent Instructions
Compute
Load 1 Miss
Runahead
Miss 1
Two types of results produced: INV and VALID
INV = Dependent on an L2 miss
INV results are marked using INV bits in the register file and store buffer.
INV values are not used for prefetching/branch resolution.

## Slide 24: Removal of Instructions from Window
Compute
Load 1 Miss
Runahead
Miss 1
Oldest instruction is examined for pseudo-retirement
  An INV instruction is removed from window immediately.
  A VALID instruction is removed when it completes execution.
Pseudo-retired instructions free their allocated resources.
  This allows the processing of later instructions.
Pseudo-retired stores communicate their data to dependent loads.
Notes: Exceptions ignored. I/O operations that modify the state of the I/O devices are not performed. Uncacheable blocks are not fetched.

## Slide 25: Store/Load Handling in Runahead Mode
Compute
Load 1 Miss
Runahead
Miss 1
A pseudo-retired store writes its data and INV status to a dedicated memory, called runahead cache.
Purpose: Data communication through memory in runahead mode.
A dependent load reads its data from the runahead cache.
Does not need to be always correct  Size of runahead cache is very small.

## Slide 26: Branch Handling in Runahead Mode
Compute
Load 1 Miss
Runahead
Miss 1
INV branches cannot be resolved.
  A mispredicted INV branch causes the processor to stay on the wrong program path until the end of runahead execution.
VALID branches are resolved and initiate recovery if mispredicted.

## Slide 27: Runahead Execution Pros and Cons
Advantages:
  + Very accurate prefetches for data/instructions (all cache levels)
  + Follows the program path
  + Simple to implement, most of the hardware is already built in
  + Versus other pre-execution based prefetching mechanisms:
  + Uses the same thread context as main thread, no waste of context
  + No need to construct a pre-execution thread
Disadvantages/Limitations:
  -- Extra executed instructions
  -- Limited by branch prediction accuracy
  -- Cannot prefetch dependent cache misses. Solution?
  -- Effectiveness limited by available “memory-level parallelism” (MLP)
  -- Prefetch distance limited by memory latency
Implemented in IBM POWER6, Sun “Rock”

## Slide 28: Performance of Runahead Execution

## Slide 29: Runahead Execution vs. Large Windows

## Slide 30: Runahead vs. A Real Large Window
When is one beneficial, when is the other?
Pros and cons of each

## Slide 31: Runahead on In-order vs. Out-of-order

## Slide 32: Effect of Runahead in Sun ROCK
Shailender Chaudhry talk, Aug 2008.

## Slide 33: Runahead Enhancements

## Slide 34: Readings
Required
  Mutlu et al., “Runahead Execution”, HPCA 2003, Top Picks 2003.
Recommended
  Mutlu et al., “Efficient Runahead Execution: Power-Efficient Memory Latency Tolerance,” ISCA 2005, IEEE Micro Top Picks 2006.
  Mutlu et al., “Address-Value Delta (AVD) Prediction,” MICRO 2005.
  Armstrong et al., “Wrong Path Events,” MICRO 2004.

## Slide 35: Limitations of the Baseline Runahead Mechanism
Energy Inefficiency
  A large number of instructions are speculatively executed
  Efficient Runahead Execution [ISCA’05, IEEE Micro Top Picks’06]
Ineffectiveness for pointer-intensive applications
  Runahead cannot parallelize dependent L2 cache misses
  Address-Value Delta (AVD) Prediction [MICRO’05]
Irresolvable branch mispredictions in runahead mode
  Cannot recover from a mispredicted L2-miss dependent branch
  Wrong Path Events [MICRO’04]

## Slide 36: The Efficiency Problem
22%
27%
Notes: Mem latency 500
L2 cache 1 MB

## Slide 37: Causes of Inefficiency
Short runahead periods
Overlapping runahead periods
Useless runahead periods
Mutlu et al., “Efficient Runahead Execution: Power-Efficient Memory Latency Tolerance,” ISCA 2005, IEEE Micro Top Picks 2006.

## Slide 38: Short Runahead Periods
Processor can initiate runahead mode due to an already in-flight L2 miss generated by
  the prefetcher, wrong-path, or a previous runahead period
Short periods
  are less likely to generate useful L2 misses
  have high overhead due to the flush penalty at runahead exit
Compute
Load 1 Miss
Runahead
Load 2 Miss
Load 2 Miss
Miss 1
Miss 2
Load 1 Hit

## Slide 39: Overlapping Runahead Periods
Compute
Load 1 Miss
Miss 1
Runahead
Load 2 Miss
Miss 2
Load 2 INV
Load 1 Hit
OVERLAP
OVERLAP
Two runahead periods that execute the same instructions
Second period is inefficient

## Slide 40: Useless Runahead Periods
Periods that do not result in prefetches for normal mode
They exist due to the lack of memory-level parallelism
Mechanism to eliminate useless periods:
  Predict if a period will generate useful L2 misses
  Estimate a period to be useful if it generated an L2 miss that cannot be captured by the instruction window
    Useless period predictors are trained based on this estimation
Compute
Load 1 Miss
Runahead
Miss 1
Load 1 Hit

## Slide 41: Overall Impact on Executed Instructions
26.5%
6.2%

## Slide 42: Overall Impact on IPC
22.6%
22.1%

## Slide 43: Taking Advantage of Pure Speculation
Runahead mode is purely speculative
The goal is to find and generate cache misses that would otherwise stall execution later on
How do we achieve this goal most efficiently and with the highest benefit?
Idea: Find and execute only those instructions that will lead to cache misses (that cannot already be captured by the instruction window)
How?

## Slide 44: Limitations of the Baseline Runahead Mechanism
Energy Inefficiency
  A large number of instructions are speculatively executed
  Efficient Runahead Execution [ISCA’05, IEEE Micro Top Picks’06]
Ineffectiveness for pointer-intensive applications
  Runahead cannot parallelize dependent L2 cache misses
  Address-Value Delta (AVD) Prediction [MICRO’05]
Irresolvable branch mispredictions in runahead mode
  Cannot recover from a mispredicted L2-miss dependent branch
  Wrong Path Events [MICRO’04]

## Slide 45: The Problem: Dependent Cache Misses
Runahead execution cannot parallelize dependent misses
  wasted opportunity to improve performance
  wasted energy (useless pre-execution)
Runahead performance would improve by 25% if this limitation were ideally overcome
Compute
Load 1 Miss
Miss 1
Load 2 Miss
Miss 2
Load 2
Load 1 Hit
Runahead: Load 2 is dependent on Load 1
Runahead
Cannot Compute Its Address!
INV

## Slide 46: Parallelizing Dependent Cache Misses
Idea: Enable the parallelization of dependent L2 cache misses in runahead mode with a low-cost mechanism
How: Predict the values of L2-miss address (pointer) loads
    Address load: loads an address into its destination register, which is later used to calculate the address of another load
    as opposed to data load
Read:
  Mutlu et al., “Address-Value Delta (AVD) Prediction,” MICRO 2005.

## Slide 47: Parallelizing Dependent Cache Misses
Compute
Load 1 Miss
Miss 1
Load 2 Hit
Miss 2
Load 2
Load 1 Hit
Value Predicted
Runahead
Saved Cycles
Can Compute Its Address
Compute
Load 1 Miss
Miss 1
Load 2 Miss
Miss 2
Load 2 INV
Load 1 Hit
Runahead
Cannot Compute Its Address!
Saved Speculative Instructions
Miss
Notes: As I showed before, traditional runahead execution cannot parallelize dependent cache misses due to load 1 and load 2, because load 2 cannot compute its address in runahead mode. However, if the value of Load 1 is predicted, Load 2 would be able to compute its address and it would generate its miss in runahead mode.

## Slide 48: AVD Prediction [MICRO’05]
Address-value delta (AVD) of a load instruction defined as:
AVD = Effective Address of Load – Data Value of Load
For some address loads, AVD is stable
An AVD predictor keeps track of the AVDs of address loads
When a load is an L2 miss in runahead mode, AVD predictor is consulted
If the predictor returns a stable (confident) AVD for that load, the value of the load is predicted
Predicted Value = Effective Address – Predicted AVD
Notes: Say that predictor does not need to be large!

## Slide 49: Why Do Stable AVDs Occur?
Regularity in the way data structures are
  allocated in memory AND
  traversed
Two types of loads can have stable AVDs
  Traversal address loads
    Produce addresses consumed by address loads
  Leaf address loads
    Produce addresses consumed by data loads

## Slide 50: Traversal Address Loads
Regularly-allocated linked list:
A
A+k
A+2k
A+3k
...
A traversal address load loads the pointer to next node:
node = nodenext
Effective Addr
Data Value
AVD
A
A+k
-k
A+k
A+2k
-k
A+2k
A+3k
-k
Stable AVD
Striding data value
AVD = Effective Addr – Data Value

## Slide 51: Leaf Address Loads
Sorted dictionary in parser: Nodes point to strings (words) String and node allocated consecutively
A+k
A
C+k
C
B+k
B
D+k
E+k
F+k
G+k
D
E
F
G
Dictionary looked up for an input word.
A leaf address load loads the pointer to the string of each node:
Effective Addr
Data Value
AVD
A+k
A
k
C+k
C
k
F+k
F
k
lookup (node, input) { // ... ptr_str = nodestring; m = check_match(ptr_str, input); // … }
Stable AVD
No stride!
AVD = Effective Addr – Data Value
string
node

## Slide 52: Identifying Address Loads in Hardware
Insight:
  If the AVD is too large, the value that is loaded is likely not an address
Only keep track of loads that satisfy:
-MaxAVD ≤ AVD ≤ +MaxAVD
This identification mechanism eliminates many loads from consideration
  Enables the AVD predictor to be small

## Slide 53: Performance of AVD Prediction
runahead
14.3%
15.5%
Notes: 16-entry predictor, baseline: runahead processor
In contrast, a 16-entry stride value predictor reduces exec time by only 2.7% and exec inst by 3.5%
A 4K-entry stride VP reduces exec time by 4.7% and exec inst by 6.1%

## Slide 54: Readings
Required
  Mutlu et al., “Runahead Execution”, HPCA 2003, Top Picks 2003.
Recommended
  Mutlu et al., “Efficient Runahead Execution: Power-Efficient Memory Latency Tolerance,” ISCA 2005, IEEE Micro Top Picks 2006.
  Mutlu et al., “Address-Value Delta (AVD) Prediction,” MICRO 2005.
  Armstrong et al., “Wrong Path Events,” MICRO 2004.

## Slide 55: We did not cover the following slides in lecture. They are for your benefit.

## Slide 56: More on Runahead Enhancements

## Slide 57: Eliminating Short Periods
Mechanism to eliminate short periods:
  Record the number of cycles C an L2-miss has been in flight
  If C is greater than a threshold T for an L2 miss, disable entry into runahead mode due to that miss
  T can be determined statically (at design time) or dynamically
T=400 for a minimum main memory latency of 500 cycles works well

## Slide 58: Eliminating Overlapping Periods
Overlapping periods are not necessarily useless
  The availability of a new data value can result in the generation of useful L2 misses
But, this does not happen often enough
Mechanism to eliminate overlapping periods:
  Keep track of the number of pseudo-retired instructions R during a runahead period
  Keep track of the number of fetched instructions N since the exit from last runahead period
  If N < R, do not enter runahead mode

## Slide 59: Properties of Traversal-based AVDs
Stable AVDs can be captured with a stride value predictor
Stable AVDs disappear with the re-organization of the data structure (e.g., sorting)
Stability of AVDs is dependent on the behavior of the memory allocator
  Allocation of contiguous, fixed-size chunks is useful
A
A+k
A+2k
A+3k
A+3k
A+k
A
A+2k
Sorting
Distance between
nodes NOT constant!


## Slide 60: Properties of Leaf-based AVDs
Stable AVDs cannot be captured with a stride value predictor
Stable AVDs do not disappear with the re-organization of the data structure (e.g., sorting)
Stability of AVDs is dependent on the behavior of the memory allocator
A+k
A
B+k
B
C
C+k
Sorting
Distance between
node and string
still constant!
C+k
C
A+k
A
B
B+k


## Slide 61: An Implementable AVD Predictor
Set-associative prediction table
Prediction table entry consists of
  Tag (Program Counter of the load)
  Last AVD seen for the load
  Confidence counter for the recorded AVD
Updated when an address load is retired in normal mode
Accessed when a load misses in L2 cache in runahead mode
Recovery-free: No need to recover the state of the processor or the predictor on misprediction
  Runahead mode is purely speculative

## Slide 62: AVD Update Logic

## Slide 63: AVD Prediction Logic

## Slide 64: Baseline Processor
Execution-driven Alpha simulator
8-wide superscalar processor
128-entry instruction window, 20-stage pipeline
64 KB, 4-way, 2-cycle L1 data and instruction caches
1 MB, 32-way, 10-cycle unified L2 cache
500-cycle minimum main memory latency
32 DRAM banks, 32-byte wide processor-memory bus (4:1 frequency ratio), 128 outstanding misses
  Detailed memory model
Pointer-intensive benchmarks from Olden and SPEC INT00

## Slide 65: AVD vs. Stride VP Performance
5.1%
2.7%
6.5%
5.5%
4.7%
8.6%
16 entries
4096 entries

## Slide 66: Wrong Path Events

## Slide 67: An Observation and A Question
In an out-of-order processor, some instructions are executed on the mispredicted path (wrong-path instructions).
Is the behavior of wrong-path instructions different from the behavior of correct-path instructions?
  If so, we can use the difference in behavior for early misprediction detection and recovery.
Notes:   17% of all executed instructions are on the wrong path

## Slide 68: What is a Wrong Path Event?
An instance of illegal or unusual behavior that is more likely to occur on the wrong path than on the correct path.
Wrong Path Event = WPE
Probability (wrong path | WPE) ~ 1

## Slide 69: Why Does a WPE Occur?
A wrong-path instruction may be executed before the mispredicted branch is executed.
  Because the mispredicted branch may be dependent on a long-latency instruction.
The wrong-path instruction may consume a data value that is not properly initialized.

## Slide 70: WPE Example from eon: NULL pointer dereference
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 71: Beginning of the loop
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
i = 0
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 72: First iteration
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
i = 0
ptr = x8ABCD0
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 73: First iteration
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
i = 0
ptr = x8ABCD0
*ptr
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 74: Loop branch correctly predicted
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
i = 1
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 75: Second iteration
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
i = 1
ptr = xEFF8B0
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 76: Second iteration
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
i = 1
ptr = xEFF8B0
*ptr
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 77: Loop exit branch mispredicted
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
i = 2
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 78: Third iteration on wrong path
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
i = 2
ptr = 0
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }

## Slide 79: Wrong Path Event
xEFF8B0
x8ABCD0
x0
x0
Array boundary
Array of pointers
to structs
NULL pointer dereference!
i = 2
ptr = 0
*ptr
1 : for (int i=0 ; i< length(); i++) {
2 : structure *ptr = array[i];
3 : if (ptr->x) {
4 : // . . .
5 : }
6 : }
Notes: This event would not have happened if the branch was correctly predicted.
Happens because pointer is dereferenced before the mispredicted branch is executed. Mispredicted branch is dependent on a long-latency operation.

## Slide 80: Types of WPEs
Due to memory instructions
  NULL pointer dereference
  Write to read-only page
  Unaligned access (illegal in the Alpha ISA)
  Access to an address out of segment range
  Data access to code segment
  Multiple concurrent TLB misses

## Slide 81: Types of WPEs (continued)
Due to control-flow instructions
  Misprediction under misprediction
    If three branches are executed and resolved as mispredicts while there are older unresolved branches in the processor, it is almost certain that one of the older unresolved branches is mispredicted.
  Return address stack underflow
  Unaligned instruction fetch address (illegal in Alpha)
Due to arithmetic instructions
  Some arithmetic exceptions
    e.g. Divide by zero

## Slide 82: Two Empirical Questions
How often do WPEs occur?
When do WPEs occur on the wrong path?