## Slide 1: Computer Architecture: Interconnects (Part II)
Michael Papamichael
Carnegie Mellon University
Material partially based on Onur Mutlu’s 18-742 lecture slides from Spring 2010

## Slide 2: Announcements
Reviews due today (November 1)
  Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.
  Fallin et al., “CHIPPER: A Low-Complexity Bufferless Deflection Router,” HPCA 2011.
Project milestones on November 6

## Slide 3: Readings
Required
  Dally, “Route Packets, Not Wires: On-Chip Interconnection Networks,” DAC 2001.
  Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.
  Chang et al., “HAT: Heterogeneous Adaptive Throttling for On-Chip Networks,” SBAC-PAD 2012.
  Fallin et al., “MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect,” NOCS 2012.
Please see website for more recommended readings

## Slide 4: Agenda
Terminology review
More on interconnection networks
  Network properties and performance metrics
  Buffering and flow control
  Router design and pipeline options
Research on NoCs
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack-based packet scheduling
  Bufferless networks

## Slide 5: Basic Terminology (review)
Topology
  Specifies way switches are wired
Routing (algorithm)
  How does a message get from source to destination
Buffering and Flow Control
  Managing and communicating buffer space
Switch/router
  Connects fixed set of inputs to fixed set of outputs
Channel
  A single logical connection between routers/switches

## Slide 6: Basic Terminology (review)
Node
  A switch/router or client/endpoint that is part of the network
Message
  Unit of transfer for network’s clients (processors, memory)
Packet
  Unit of transfer for network
Flit
  Flow control digit
  Unit of flow control within network
Packet
F
F
F
F
F
F
Flits
T
Head Flit
Tail Flit
H

## Slide 7: Agenda
Terminology review
More on interconnection networks
  Network properties and performance metrics
  Buffering and flow control
  Router design and pipeline options
Research on NoCs
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack-based packet scheduling
  Bufferless networks

## Slide 8: Properties of a Topology/Network
Regular or Irregular
  Regular if topology is regular graph (e.g. ring, mesh).
Routing Distance
  Number of links/hops along route
Diameter
  Maximum routing distance
Average Distance
  Average number of hops across all valid routes
diameter = 6
Notes: Example of irregular network? Internet

## Slide 9: Properties of a Topology/Network
  Direct or Indirect Networks
  Endpoints sit “inside” (direct) or “outside” (indirect) the network
  E.g. mesh is direct; every node is both endpoint and switch
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
Router (switch), Radix of 2 (2 inputs, 2 outputs)
Abbreviation: Radix-ary
These routers are 2-ary
Indirect
Direct
Notes: What type of network is the one on the right

## Slide 10: Properties of a Topology/Network
Bisection Bandwidth
  Often used to describe network performance
  Cut network in half and sum bandwidth of links severed
    (Min # channels spanning two halves) * (BW of each channel)
  Meaningful only for recursive topologies
  Can be misleading, because does not account for switch and routing efficiency
Blocking vs. Non-Blocking
  If connecting any permutation of sources & destinations is possible, network is non-blocking; otherwise network is blocking.
  Rearrangeable non-blocking: Same as non-blocking but might require rearranging connections when switching from one permutation to another.

## Slide 11: Blocking vs. Non-Blocking Example
What type of topology/network is this?
  Multistage Logarithmic (Omega)
Is this blocking or non-blocking?
  Blocking
conflict
Notes: Can a rearrangeable non-blocking network only have a single path from each source to each destination?

## Slide 12: Interconnection Network Performance
Load-Latency behavior
  Can heavily depend on traffic pattern
Latency
Load - Offered Traffic (bits/sec)
Min latency given by topology
Min latency given by routing algorithm
Zero load or idle latency
(topology+routing+flow control)
Throughput given by topology
Throughput given by routing
Saturation throughput (given by flow control)

## Slide 13: Ideal Latency
Ideal latency
  Solely due to wire delay between source and destination
  D = Manhattan distance
  L = packet size
  b = channel bandwidth
  v = propagation velocity
Notes: What’s the best we can do?

## Slide 14: Actual Latency
Dedicated wiring impractical
  Long wires segmented with insertion of routers
  D = Manhattan distance
  L = packet size
  b = channel bandwidth
  v = propagation velocity
  H = hops
  Trouter = router latency
  Tc = latency due to contention

## Slide 15: Review
Direct
Topology
Crossbar
Mesh
Indirect
Direct/Indirect
Blocking/ Non-blocking
Non-blocking
Blocking
(this particular one)
Blocking
Multistage Logarith.
Indirect
Cost
Latency
O(N2)
O(NlogN)
O(N)
O(sqrt(N))
O(1)
O(logN)
2
1
0
3
2
1
0
3
1
0
3
2
5
4
7
6
1
0
3
2
5
4
7
6

## Slide 16: Agenda
Terminology review
More on interconnection networks
  Network properties and performance metrics
  Buffering and flow control
  Router design and pipeline options
Research on NoCs
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack-based packet scheduling
  Bufferless networks

## Slide 17: Circuit vs. Packet Switching (review)
Circuit switching sets up full path
  Establish route then send data
  (no one else can use those links)
  faster and higher bandwidth
  setting up and bringing down links slow
Packet switching routes per packet
  Route each packet individually (possibly via different paths)
  if link is free can use
  potentially slower (must dynamically switch)
  no setup, bring down time

## Slide 18: Packet Switched Networks: Packet Format
Header
  routing and control information
  at start so router can start forwarding early
Payload/Body
  carries data (non HW specific information)
  can be further divided (framing, protocol stacks…)
Tail
  contains control information, e.g. error code
  at end of packet so it can be generated on the way out
F
H
F
F
F
T
Head Flit
Body Flits
Tail Flit

## Slide 19: Handling Contention
Two packets trying to use the same link at the same time
What do you do?
  Buffer one
  Drop one
  Misroute one (deflection)
Assume buffering for now

## Slide 20: Flow Control Methods
Circuit switching
Store and forward (Packet based)
Virtual cut through (Packet based)
Wormhole (Flit based)

## Slide 21: Circuit Switching Revisited
Resource allocation granularity is high
Idea: Pre-allocate resources across multiple switches for a given “flow”
Need to send a probe to set up the path for pre-allocation
+ No need for buffering
+ No contention (flow’s performance is isolated)
+ Can handle arbitrary message sizes
- Lower link utilization: two flows cannot use the same link
- Handshake overhead to set up a “circuit”

## Slide 22: Store and Forward Flow Control
Packet based flow control
Store and Forward
  Packet copied entirely into network router before moving to the next node
  Flow control unit is the entire packet
Leads to high per-packet latency
Requires buffering for entire packet in each node
Can we do better?
S
D

## Slide 23: Cut through Flow Control
Another form of packet based flow control
Start forwarding as soon as header is received and resources (buffer, channel, etc) allocated
  Dramatic reduction in latency
Still allocate buffers and channel bandwidth for full packets
What if packets are large?
S
D

## Slide 24: Cut through Flow Control
What to do if output port is blocked?
Lets the tail continue when the head is blocked, absorbing the whole message into a single switch.
  Requires a buffer large enough to hold the largest packet.
Degenerates to store-and-forward with high contention
Can we do better?

## Slide 25: Wormhole Flow Control
Packets broken into (potentially) smaller flits (buffer/bw allocation unit)
Flits are sent across the fabric in a wormhole fashion
  Body follows head, tail follows body
  Pipelined
  If head blocked, rest of packet stops
  Routing (src/dest) information only in head
How does body/tail know where to go?
Latency almost independent of distance for long messages

## Slide 26: Wormhole Flow Control
Advantages over “store and forward” flow control
  + Lower latency
  + More efficient buffer utilization
Limitations
  - Occupies resources across multiple routers
  - Suffers from head of line blocking
  - if head flit cannot move due to contention, another worm cannot proceed even though links may be idle
1
2
1
2
1
2
Switching Fabric
Input Queues
Outputs
1
2
1
2
HOL Blocking
Idle!

## Slide 27: Head of Line Blocking
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until read proceeds

## Slide 28: Head of Line Blocking
A worm can be before another in the router input buffer
Due to FIFO nature, the second worm cannot be scheduled even though it may need to access another output port
Karo et al., “Input Versus Output Queuing on a Space-Division Packet Switch,” IEEE Transactions on Communications 1987

## Slide 29: Virtual Channel Flow Control
Idea: Multiplex multiple channels over one physical channel
Divide up the input buffer into multiple buffers sharing a single physical channel
Dally, “Virtual Channel Flow Control,” ISCA 1990.

## Slide 30: Virtual Channel Flow Control
Idea: Multiplex multiple channels over one physical channel
Divide up the input buffer into multiple buffers sharing a single physical channel
Dally, “Virtual Channel Flow Control,” ISCA 1990.

## Slide 31: Virtual Channel Flow Control
Blocked by other packets
Buffer full: blue cannot proceed

## Slide 32: A Modern Virtual Channel Based Router

## Slide 33: Other Uses of Virtual Channels
Deadlock avoidance
  Enforcing switching to a different set of virtual channels on some “turns” can break the cyclic dependency of resources
    Enforce order on VCs
  Escape VCs: Have at least one VC that uses deadlock-free routing. Ensure each flit has fair access to that VC.
  Protocol level deadlock: Ensure address and data packets use different VCs  prevent cycles due to intermixing of different packet classes
Prioritization of traffic classes
  Some virtual channels can have higher priority than others

## Slide 34: Communicating Buffer Availability
Credit-based flow control
  Upstream knows how many buffers are downstream
  Downstream passes back credits to upstream
  Significant upstream signaling (esp. for small flits)
On/Off (XON/XOFF) flow control
  Downstream has on/off signal to upstream
Ack/Nack flow control
  Upstream optimistically sends downstream
  Buffer cannot be deallocated until ACK/NACK received
  Inefficiently utilizes buffer space

## Slide 35: Credit-based Flow Control
Round-trip credit delay:
  Time between when buffer empties and when next flit can be processed from that buffer entry
Significant throughput degradation if there are few buffers
Important to size buffers to tolerate credit turn-around
Node 1
Node 2
Flit departs
router
t1
Credit
Process
t2
t3
Credit
Flit
Process
t4
t5
Credit round trip delay

## Slide 36: On/Off (XON/XOFF) Flow Control
Downstream has on/off signal to upstream
Process
Node 1
Node 2
t1
Flit
Flit
Flit
Flit
t2
Foffthreshold reached
Off
Flit
Flit
Flit
Flit
Flit
On
Process
Flit
Flit
Flit
Flit
Flit
t3
t4
t5
t6
t7
t8
Foffset to prevent flits arriving before t4 from overflowing
Fonthreshold reached
Fonset so that Node 2 does not run out of flits between t5 and t8

## Slide 37: Review: Flow Control
Store and Forward
S
D
Cut Through / Wormhole
S
D
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until read proceeds
Shrink Buffers
Reduce latency
Any other issues?
Head-of-Line
Blocking
Use Virtual
Channels

## Slide 38: Review: Flow Control
Store and Forward
S
D
Cut Through / Wormhole
S
D
Shrink Buffers
Reduce latency
Any other issues?
Head-of-Line
Blocking
Use Virtual
Channels
Blocked by other packets
Buffer full: blue cannot proceed

## Slide 39: Agenda
Terminology review
More on interconnection networks
  Network properties and performance metrics
  Buffering and flow control
  Router design and pipeline options
Research on NoCs
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack-based packet scheduling
  Bufferless networks

## Slide 40: On-chip Networks
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Router
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)

## Slide 41: Router Design: Functions of a Router
Buffering (of flits)
Route computation
Arbitration of flits (i.e. prioritization) when contention
  Called packet scheduling
Switching
  From input port to output port
Power management
  Scale link/router frequency

## Slide 42: Router Pipeline
Five logical stages
  BW: Buffer Write
  RC: Route computation
  VA: Virtual Channel Allocation
  SA: Switch Allocation
  ST: Switch Traversal
  LT: Link Traversal
BW
RC
VA
SA
ST
LT

## Slide 43: Wormhole Router Timeline
Route computation performed once per packet
Virtual channel allocated once per packet
Body and tail flits inherit this information from head flit
BW
RC
VA
SA
ST
LT
BW
BW
BW
SA
ST
LT
SA
ST
LT
SA
ST
LT
Head
Body 1
Body 2
Tail
1
2
3
4
5
6
7
8
9

## Slide 44: Dependencies in a Router
Dependence between output of one module and input of another
  Determine critical path through router
  Cannot bid for switch port until routing performed
Decode + Routing
Switch Arbitration
Crossbar Traversal
Wormhole Router
Decode + Routing
Switch Arbitration
Crossbar Traversal
Virtual Channel Router
VC Allocation
Decode + Routing
Speculative Switch Arbitration
Crossbar Traversal
Speculative Virtual Channel Router
VC Allocation

## Slide 45: Pipeline Optimizations: Lookahead Routing
At current router perform routing computation for next router
  Overlap with BW
  Precomputing route allows flits to compete for VCs immediately after BW
  RC decodes route header
  Routing computation needed at next hop
    Can be computed in parallel with VA
Galles, “Spider: A High-Speed Network Interconnect,” IEEE Micro 1997.
BW
RC
VA
SA
ST
LT

## Slide 46: Pipeline Optimizations: Speculation
Assume that Virtual Channel Allocation stage will be successful
  Valid under low to moderate loads
Entire VA and SA in parallel
If VA unsuccessful (no virtual channel returned)
  Must repeat VA/SA in next cycle
Prioritize non-speculative requests
BW
RC
VA
SA
ST
LT

## Slide 47: Pipeline Optimizations: Bypassing
When no flits in input buffer
  Speculatively enter ST
  On port conflict, speculation aborted
  In the first stage, a free VC is allocated, next routing is performed and the crossbar is setup
VA
RC
Setup
ST
LT

## Slide 48: Agenda
Terminology review
More on interconnection networks
  Network properties and performance metrics
  Buffering and flow control
  Router design and pipeline options
Research on NoCs
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack-based packet scheduling
  Bufferless networks

## Slide 49: Packet Scheduling
Which packet to choose for a given output port?
  Router needs to prioritize between competing flits
  Which input port?
  Which virtual channel?
  Which application’s packet?
Common strategies
  Round robin across virtual channels
  Oldest packet first (or an approximation)
  Prioritize some virtual channels over others
Better policies in a multi-core environment
  Use application characteristics

## Slide 50: The Problem: Packet Scheduling
Network-on-Chip
L2$
L2$
L2$
L2$
Bank
mem cont
Memory Controller
P
Accelerator
L2$
Bank
L2$
Bank
P
P
P
P
P
P
P
Network-on-Chip
Network-on-Chip is a critical resource
shared by multiple applications
App1
App2
App N
App N-1

## Slide 51: The Problem: Packet Scheduling
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Routers
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)

## Slide 52: The Problem: Packet Scheduling
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
VC
1
VC
2
From East
From West
From North
From South
From PE

## Slide 53: The Problem: Packet Scheduling
Conceptual
View
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
VC
1
VC
2
From East
From West
From North
From South
From PE
Allocator
(SA)

## Slide 54
Scheduler
Conceptual
View
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
VC
1
VC
2
From East
From West
From North
From South
From PE
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
Which packet to choose?
The Problem: Packet Scheduling

## Slide 55: The Problem: Packet Scheduling
Existing scheduling policies
  Round Robin
  Age
Problem 1: Local to a router
  Lead to contradictory decision making between routers: packets from one application may be prioritized at one router, to be delayed at next.
Problem 2: Application oblivious
  Treat all applications packets equally
  But applications are heterogeneous
Solution : Application-aware global scheduling policies.

## Slide 56: Agenda
Terminology review
More on interconnection networks
  Network properties and performance metrics
  Buffering and flow control
  Router design and pipeline options
Research on NoCs
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack-based packet scheduling
  Bufferless networks

## Slide 57: Motivation: Stall Time Criticality
Applications are not homogenous
Applications have different criticality with respect to the network
  Some applications are network latency sensitive
  Some applications are network latency tolerant
Application’s Stall Time Criticality (STC) can be measured by its average network stall time per packet (i.e. NST/packet)
  Network Stall Time (NST) is number of cycles the processor stalls waiting for network transactions to complete

## Slide 58: Motivation: Stall Time Criticality
Why applications have different network stall time criticality (STC)?
  Memory Level Parallelism (MLP)
    Lower MLP leads to higher STC
  Shortest Job First Principle (SJF)
    Lower network load leads to higher STC
  Average Memory Access Time
    Higher memory access time leads to higher STC

## Slide 59
Observation 1: Packet Latency != Network Stall Time
STALL
STALL
STALL of Red Packet = 0
LATENCY
LATENCY
LATENCY
Application with high MLP
STC Principle 1 {MLP}
Compute

## Slide 60
Observation 1: Packet Latency != Network Stall Time
Observation 2: A low MLP application’s packets have higher criticality than a high MLP application’s
STALL
STALL
STALL of Red Packet = 0
LATENCY
LATENCY
LATENCY
Application with high MLP
STALL
LATENCY
STALL
LATENCY
STALL
LATENCY
Application with low MLP
STC Principle 1 {MLP}

## Slide 61: STC Principle 2 {Shortest-Job-First}
4X network slow down
1.2X network slow down
1.3X network slow down
1.6X network slow down
Overall system throughput{weighted speedup} increases by 34%
Running ALONE
Baseline (RR) Scheduling
SJF Scheduling
Light Application
Heavy Application
Compute

## Slide 62: Solution: Application-Aware Policies
Idea
  Identify stall time critical applications (i.e. network sensitive applications) and prioritize their packets in each router.
Key components of scheduling policy:
  Application Ranking
  Packet Batching
Propose low-hardware complexity solution

## Slide 63: Component 1 : Ranking
Ranking distinguishes applications based on Stall Time Criticality (STC)
Periodically rank applications based on Stall Time Criticality (STC).
Explored many heuristics for quantifying STC (Details & analysis in paper)
  Heuristic based on outermost private cache Misses Per Instruction (L1-MPI) is the most effective
  Low L1-MPI => high STC => higher rank
Why Misses Per Instruction (L1-MPI)?
  Easy to Compute (low complexity)
  Stable Metric (unaffected by interference in network)

## Slide 64: Component 1 : How to Rank?
Execution time is divided into fixed “ranking intervals”
  Ranking interval is 350,000 cycles
At the end of an interval, each core calculates their L1-MPI and sends it to the Central Decision Logic (CDL)
  CDL is located in the central node of mesh
CDL forms a ranking order and sends back its rank to each core
  Two control packets per core every ranking interval
Ranking order is a “partial order”
Rank formation is not on the critical path
  Ranking interval is significantly longer than rank computation time
  Cores use older rank values until new ranking is available

## Slide 65: Component 2: Batching
Problem: Starvation
  Prioritizing a higher ranked application can lead to starvation of lower ranked application
Solution: Packet Batching
  Network packets are grouped into finite sized batches
  Packets of older batches are prioritized over younger batches
Alternative batching policies explored in paper
Time-Based Batching
  New batches are formed in a periodic, synchronous manner across all nodes in the network, every T cycles

## Slide 66: Putting it all together
Before injecting a packet into the network, it is tagged by
  Batch ID (3 bits)
  Rank ID (3 bits)
Three tier priority structure at routers
  Oldest batch first (prevent starvation)
  Highest rank first (maximize performance)
  Local Round-Robin (final tie breaker)
Simple hardware support: priority arbiters
Global coordinated scheduling
  Ranking order and batching order are same across all routers

## Slide 67: STC Scheduling Example
Injection Cycles
1
2
3
4
5
6
7
8
2
2
3
Batch 0
Packet Injection Order at Processor
Core1 Core2 Core3
Batching interval length = 3 cycles
Ranking order =
Batch 1
Batch 2

## Slide 68: STC Scheduling Example
4
8
5
1
7
2
1
6
2
1
3
Router
Scheduler
Injection Cycles
1
2
3
4
5
6
7
8
2
2
3
Batch 2
Batch 1
Batch 0
Applications

## Slide 69: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
3
2
8
7
6
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age |  |  |  | 
STC |  |  |  | 
Time

## Slide 70: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
5
4
3
1
2
2
3
2
8
7
6
Age
3
3
5
4
6
7
8
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age | 4 | 6 | 11 | 7.0
STC |  |  |  | 
Time
Time

## Slide 71: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
5
4
3
1
2
2
3
2
8
7
6
Age
2
3
3
5
4
6
7
8
1
2
2
STC
3
5
4
6
7
8
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age | 4 | 6 | 11 | 7.0
STC | 1 | 3 | 11 | 5.0
Ranking order
Time
Time
Time

## Slide 72: Qualitative Comparison
Round Robin & Age
  Local and application oblivious
  Age is biased towards heavy applications
    heavy applications flood the network
    higher likelihood of an older packet being from heavy application
Globally Synchronized Frames (GSF) [Lee et al., ISCA 2008]
  Provides bandwidth fairness at the expense of system performance
  Penalizes heavy and bursty applications
    Each application gets equal and fixed quota of flits (credits) in each batch.
    Heavy application quickly run out of credits after injecting into all active batches & stall till oldest batch completes and frees up fresh credits.
    Underutilization of network resources

## Slide 73: System Performance
Chart: Normalized System Speedup
| weighted
LocalRR | 1
LocalAge | 1.0015
GSF | 0.88571
STC | 1.0922
Chart: Network Unfairness
| unfairness
LocalRR | 8.646
LocalAge | 7.6077
GSF | 8.4794
STC | 7.0747
STC provides 9.1% improvement in weighted speedup over the best existing policy{averaged across 96 workloads}
Detailed case studies in the paper
Notes: This graph compares the system performance provided by the four polices.
Performance is normalized to that of the baseline RR scheduler.
STC also improves system performance compared to the best previous scheduler, on all systems.
It provides an 9.1% performance improvement.
For the unfairness graph lower value is better

## Slide 74: Agenda
Terminology review
More on interconnection networks
  Network properties and performance metrics
  Buffering and flow control
  Router design and pipeline options
Research on NoCs
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack-based packet scheduling
  Bufferless networks

## Slide 75: Today
Review (Topology & Flow Control)
More on interconnection networks
  Routing
  Router design
  Network performance metrics
  On-chip vs. off-chip differences
Research on NoCs and packet scheduling
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack based packet scheduling

## Slide 76: What is Aérgia?
Aérgia is the spirit of laziness in Greek mythology
Some packets can afford to slack!

## Slide 77: Slack of Packets
What is slack of a packet?
  Slack of a packet is number of cycles it can be delayed in a router without reducing application’s performance
  Local network slack
Source of slack: Memory-Level Parallelism (MLP)
  Latency of an application’s packet hidden from application due to overlap with latency of pending cache miss requests
Prioritize packets with lower slack

## Slide 78: Concept of Slack
Instruction
Window
Stall
Network-on-Chip
Load Miss
Causes
returns earlier than necessary
Compute
Slack ( ) = Latency ( ) – Latency ( ) = 26 – 6 = 20 hops
Execution Time
Packet( ) can be delayed for available slack cycles without reducing performance!
Causes
Load Miss
Latency ( )
Latency ( )
Slack
Slack
Notes: We have two cores, core A colored green and core B colored red

## Slide 79: Prioritizing using Slack
Core A
Core B
Packet | Latency | Slack
 | 13 hops | 0 hops
 | 3 hops | 10 hops
 | 10 hops | 0 hops
 | 4 hops | 6 hops
Causes
Causes
Load Miss
Load Miss
Prioritize
Load Miss
Load Miss
Causes
Causes
Interference at 3 hops
Slack( ) > Slack ( )
Notes: Now the packets B-1 and A-0 interfere in the network for 3 hops, and we can choose one over the other
A-0 has slack of 0 hops and B-1 has a slack of 6 hops
So we can Prioritize A-0 over B-1 to reduce stall cycles of Core-A without increasing stall cycles of Core-B

## Slide 80: Slack in Applications
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
50% of packets have 350+ slack cycles
10% of packets have <50 slack cycles
Non-critical
critical

## Slide 81: Slack in Applications
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
art | 67.34 | 78.35 | 86.47 | 91.15 | 93.69 | 95.3 | 96.4 | 97.21 | 97.89 | 98.49 | 98.96
68% of packets have zero slack cycles

## Slide 82: Diversity in Slack
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
omnet | 18.26 | 22.6 | 27.38 | 31.83 | 35.94 | 39.76 | 43.34 | 46.76 | 50.07 | 53.29 | 56.34
tpcw | 24.84 | 32.69 | 39.43 | 43.74 | 47.01 | 49.78 | 52.44 | 55.46 | 59.42 | 64.22 | 68.83
mcf | 20.8 | 22.89 | 25.4 | 27.69 | 29.83 | 31.93 | 34.03 | 36.17 | 38.44 | 40.85 | 43.29
bzip2 | 16.61 | 26.43 | 43.7 | 52.13 | 57.33 | 61.22 | 64.5 | 67.73 | 71.62 | 75.76 | 79.07
sjbb | 31.97 | 44.81 | 54.63 | 59.02 | 61.71 | 63.81 | 65.95 | 69.02 | 74.12 | 80.2 | 84.77
sap | 20.91 | 33.4 | 44.4 | 49.94 | 53.68 | 56.65 | 59.47 | 62.87 | 67.63 | 73.04 | 77.64
sphinx | 33.8 | 46.89 | 57 | 62.2 | 65.55 | 68.25 | 70.75 | 73.51 | 77.02 | 81.17 | 84.85
deal | 48.38 | 63.98 | 81.27 | 87.3 | 89.68 | 91.16 | 92.32 | 93.4 | 94.56 | 95.75 | 96.79
barnes | 32.96 | 46.61 | 59.39 | 63.48 | 66.27 | 68.54 | 70.7 | 73.35 | 78.04 | 83.37 | 86.99
astar | 43.04 | 58.09 | 71.63 | 76.95 | 79.84 | 81.87 | 83.49 | 85.5 | 88.22 | 91.38 | 94.29
calculix | 55.87 | 78.45 | 90.5 | 91.95 | 92.54 | 93 | 93.43 | 93.89 | 94.58 | 95.4 | 96.12

## Slide 83: Diversity in Slack
Chart: Slack in cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
omnet | 18.26 | 22.6 | 27.38 | 31.83 | 35.94 | 39.76 | 43.34 | 46.76 | 50.07 | 53.29 | 56.34
tpcw | 24.84 | 32.69 | 39.43 | 43.74 | 47.01 | 49.78 | 52.44 | 55.46 | 59.42 | 64.22 | 68.83
mcf | 20.8 | 22.89 | 25.4 | 27.69 | 29.83 | 31.93 | 34.03 | 36.17 | 38.44 | 40.85 | 43.29
bzip2 | 16.61 | 26.43 | 43.7 | 52.13 | 57.33 | 61.22 | 64.5 | 67.73 | 71.62 | 75.76 | 79.07
sjbb | 31.97 | 44.81 | 54.63 | 59.02 | 61.71 | 63.81 | 65.95 | 69.02 | 74.12 | 80.2 | 84.77
sap | 20.91 | 33.4 | 44.4 | 49.94 | 53.68 | 56.65 | 59.47 | 62.87 | 67.63 | 73.04 | 77.64
sphinx | 33.8 | 46.89 | 57 | 62.2 | 65.55 | 68.25 | 70.75 | 73.51 | 77.02 | 81.17 | 84.85
deal | 48.38 | 63.98 | 81.27 | 87.3 | 89.68 | 91.16 | 92.32 | 93.4 | 94.56 | 95.75 | 96.79
barnes | 32.96 | 46.61 | 59.39 | 63.48 | 66.27 | 68.54 | 70.7 | 73.35 | 78.04 | 83.37 | 86.99
astar | 43.04 | 58.09 | 71.63 | 76.95 | 79.84 | 81.87 | 83.49 | 85.5 | 88.22 | 91.38 | 94.29
calculix | 55.87 | 78.45 | 90.5 | 91.95 | 92.54 | 93 | 93.43 | 93.89 | 94.58 | 95.4 | 96.12
Slack varies between packets of different applications
Slack varies between packets of a single application

## Slide 84: Estimating Slack Priority
Slack (P) = Max (Latencies of P’s Predecessors) – Latency of P
  Predecessors(P) are the packets of outstanding cache miss requests when P is issued
Packet latencies not known when issued
Predicting latency of any packet Q
  Higher latency if Q corresponds to an L2 miss
  Higher latency if Q has to travel farther number of hops
Notes: Difficult to predict packet latency
Predicting Max (Predecessors’ Latencies)
  Number of predecessors
  Higher predecessor latency if predecessor is L2 miss
Predicting latency of a packet P
  Higher latency if P corresponds to an L2 miss
  Higher latency if P has to travel farther number of hops

## Slide 85: Estimating Slack Priority
Slack of P = Maximum Predecessor Latency – Latency of P
Slack(P) =
  PredL2: Set if any predecessor packet is servicing L2 miss
  MyL2: Set if P is NOT servicing an L2 miss
  HopEstimate: Max (# of hops of Predecessors) – hops of P
PredL2
(2 bits)
MyL2
(1 bit)
HopEstimate
(2 bits)

## Slide 86: Estimating Slack Priority
How to predict L2 hit or miss at core?
  Global Branch Predictor based L2 Miss Predictor
    Use Pattern History Table and 2-bit saturating counters
  Threshold based L2 Miss Predictor
    If #L2 misses in “M” misses >= “T” threshold then next load is a L2 miss.
Number of miss predecessors?
  List of outstanding L2 Misses
Hops estimate?
  Hops => ∆X + ∆ Y distance
  Use predecessor list to calculate slack hop estimate

## Slide 87: Starvation Avoidance
Problem: Starvation
  Prioritizing packets can lead to starvation of lower priority packets
Solution: Time-Based Packet Batching
  New batches are formed at every T cycles
  Packets of older batches are prioritized over younger batches

## Slide 88: Qualitative Comparison
Round Robin & Age
  Local and application oblivious
  Age is biased towards heavy applications
Globally Synchronized Frames (GSF) [Lee et al., ISCA 2008]
  Provides bandwidth fairness at the expense of system performance
  Penalizes heavy and bursty applications
Application-Aware Prioritization Policies (SJF) [Das et al., MICRO 2009]
  Shortest-Job-First Principle
  Packet scheduling policies which prioritize network sensitive applications which inject lower load
Notes:     Age
    heavy applications flood the network
    higher likelihood of an older packet being from heavy application
GSF
    Each application gets equal and fixed quota of flits (credits) in each batch.
    Heavy application quickly run out of credits after injecting into all active batches & stall till oldest batch completes and frees up fresh credits.
    Underutilization of network resources

## Slide 89: System Performance
SJF provides 8.9% improvement in weighted speedup
Aérgia improves system throughput by 10.3%
Aérgia+SJF improves system throughput by 16.1%
Chart: Normalized System Speedup
Age | 1
RR | 1.0046
GSF | 0.88979
SJF | 1.0949
Aergia | 1.1084
SJF+Aergia | 1.1668

## Slide 90: Agenda
Terminology review
More on interconnection networks
  Network properties and performance metrics
  Buffering and flow control
  Router design and pipeline options
Research on NoCs
  The problem with packet scheduling
  Application-aware packet scheduling
  Aergia: Latency slack-based packet scheduling
  Bufferless networks

## Slide 91: On-Chip Networks (NoC)
Connect cores, caches, memory controllers, etc…
Examples:
  Intel 80-core Terascale chip
  MIT RAW chip
Design goals in NoC design:
  High throughput, low latency
  Fairness between cores, QoS, …
  Low complexity, low cost
  Power, low energy consumption

## Slide 92: On-Chip Networks (NoC)
Connect cores, caches, memory controllers, etc…
Examples:
  Intel 80-core Terascale chip
  MIT RAW chip
Design goals in NoC design:
  High throughput, low latency
  Fairness between cores, QoS, …
  Low complexity, low cost
  Power, low energy consumption
Energy/Power in On-Chip Networks
Power is a key constraint in the design
of high-performance processors
NoCs consume substantial portion of system
power
  ~30% in Intel 80-core Terascale [IEEE Micro’07]
  ~40% in MIT RAW Chip [ISCA’04]
NoCs estimated to consume 100s of Watts [Borkar, DAC’07]

## Slide 93: Current NoC Approaches
Existing approaches differ in numerous ways:
  Network topology [Kim et al, ISCA’07, Kim et al, ISCA’08 etc]
  Flow control [Michelogiannakis et al, HPCA’09, Kumar et al, MICRO’08, etc]
  Virtual Channels [Nicopoulos et al, MICRO’06, etc]
  QoS & fairness mechanisms [Lee et al, ISCA’08, etc]
  Routing algorithms [Singh et al, CAL’04]
  Router architecture [Park et al, ISCA’08]
  Broadcast, Multicast [Jerger et al, ISCA’08, Rodrigo et al, MICRO’08]
Existing work assumes existence of
buffers in routers!

## Slide 94: A Typical Router
Routing Computation
VC Arbiter
Switch Arbiter
VC1
VC2
VCv
VC1
VC2
VCv
Input Port N
Input Port 1
N x N Crossbar
Input Channel 1
Input Channel N
Scheduler
Output Channel 1
Output Channel N
Credit Flow to upstream router
Buffers are integral part of existing NoC Routers
Credit Flow to upstream router

## Slide 95: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Injection Rate
Avg. packet latency
large buffers
medium buffers
small buffers

## Slide 96: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Buffers consume significant energy/power
  Dynamic energy when read/write
  Static energy even when not occupied
Buffers add complexity and latency
  Logic for buffer management
  Virtual channel allocation
  Credit-based flow control
Buffers require significant chip area
  E.g., in TRIPS prototype chip, input buffers occupy 75% of total on-chip network area [Gratz et al, ICCD’06]
Can we get rid of buffers…?

## Slide 97: Going Bufferless…?
How much throughput do we lose?
   How is latency affected?
Up to what injection rates can we use bufferless routing?
 Are there realistic scenarios in which NoC is operated at injection rates below the threshold?
Can we achieve energy reduction?
   If so, how much…?
Can we reduce area, complexity, etc…?
Injection Rate
latency
buffers
no buffers
Answers in our paper!

## Slide 98: Overview
Introduction and Background
Bufferless Routing (BLESS)
  FLIT-BLESS
  WORM-BLESS
  BLESS with buffers
Advantages and Disadvantages
Evaluations
Conclusions

## Slide 99: BLESS: Bufferless Routing
Always forward all incoming flits to some output port
If no productive direction is available, send to another direction
 packet is deflected
 Hot-potato routing [Baran’64, etc]
Buffered
BLESS
Deflected!

## Slide 100: BLESS: Bufferless Routing
Routing
VC Arbiter
Switch Arbiter
Flit-Ranking
Port-Prioritization
arbitration policy
Flit-Ranking
Create a ranking over all incoming flits
Port-Prioritization
For a given flit in this ranking, find the best free output-port
Apply to each flit in order of ranking

## Slide 101: FLIT-BLESS: Flit-Level Routing
Each flit is routed independently.
Oldest-first arbitration (other policies evaluated in paper)
Network Topology:  Can be applied to most topologies (Mesh, Torus, Hypercube, Trees, …) 1) #output ports ¸ #input ports at every router 2) every router is reachable from every other router
Flow Control & Injection Policy:
   Completely local, inject whenever input port is free
Absence of Deadlocks: every flit is always moving
Absence of Livelocks: with oldest-first ranking
Flit-Ranking
Oldest-first ranking
Port-Prioritization
Assign flit to productive port, if possible. Otherwise, assign to non-productive port.

## Slide 102: WORM-BLESS: Wormhole Routing
Potential downsides of FLIT-BLESS
  Not-energy optimal (each flits needs header information)
  Increase in latency (different flits take different path)
  Increase in receive buffer size
BLESS with wormhole routing…?
Problems:
  Injection Problem (not known when it is safe to inject)
  Livelock Problem (packets can be deflected forever)
new worm!
[Dally, Seitz’86]

## Slide 103: WORM-BLESS: Wormhole Routing
Flit-Ranking
Oldest-first ranking
Port-Prioritization
If flit is head-flit
a) assign flit to unallocated, productive port b) assign flit to allocated, productive port c) assign flit to unallocated, non-productive port d) assign flit to allocated, non-productive port else, a) assign flit to port that is allocated to worm
Deflect worms if necessary!
Truncate worms if necessary!
Head-flit: West
This worm is truncated!
& deflected!
At low congestion, packets
travel routed as worms
allocated to North
allocated to West
Body-flit turns into head-flit
See paper for details…

## Slide 104: BLESS with Buffers
BLESS without buffers is extreme end of a continuum
BLESS can be integrated with buffers
  FLIT-BLESS with Buffers
  WORM-BLESS with Buffers
Whenever a buffer is full, it’s first flit becomes must-schedule
must-schedule flits must be deflected if necessary
See paper for details…

## Slide 105: Overview
Introduction and Background
Bufferless Routing (BLESS)
  FLIT-BLESS
  WORM-BLESS
  BLESS with buffers
Advantages and Disadvantages
Evaluations
Conclusions

## Slide 106: BLESS: Advantages & Disadvantages
Advantages
No buffers
Purely local flow control
Simplicity - no credit-flows - no virtual channels - simplified router design
No deadlocks, livelocks
Adaptivity - packets are deflected around congested areas!
Router latency reduction
Area savings
Disadvantages
Increased latency
Reduced bandwidth
Increased buffering at receiver
Header information at each flit
Impact on energy…?

## Slide 107: Reduction of Router Latency
BLESS gets rid of input buffers and virtual channels
BW RC
VA SA
ST
LT
BW
SA
ST
LT
RC
ST
LT
RC
ST
LT
LA LT
BW: Buffer Write
RC: Route Computation
VA: Virtual Channel Allocation
SA: Switch Allocation ST: Switch Traversal
LT: Link Traversal
LA LT: Link Traversal of Lookahead
Baseline Router
(speculative)
head flit
body flit
BLESS Router
(standard)
RC
ST
LT
RC
ST
LT
Router 1
Router 2
Router 1
Router 2
BLESS Router
(optimized)
Router Latency = 3
Router Latency = 2
Router Latency = 1
Can be improved to 2.
[Dally, Towles’04]
our evaluations

## Slide 108: BLESS: Advantages & Disadvantages
Advantages
No buffers
Purely local flow control
Simplicity - no credit-flows - no virtual channels - simplified router design
No deadlocks, livelocks
Adaptivity - packets are deflected around congested areas!
Router latency reduction
Area savings
Disadvantages
Increased latency
Reduced bandwidth
Increased buffering at receiver
Header information at each flit
Impact on energy…?
Extensive evaluations in the paper!

## Slide 109: Evaluation Methodology
2D mesh network, router latency is 2 cycles
  4x4, 8 core, 8 L2 cache banks (each node is a core or an L2 bank)
  4x4, 16 core, 16 L2 cache banks (each node is a core and an L2 bank)
  8x8, 16 core, 64 L2 cache banks (each node is L2 bank and may be a core)
  128-bit wide links, 4-flit data packets, 1-flit address packets
  For baseline configuration: 4 VCs per physical input port, 1 packet deep
Benchmarks
  Multiprogrammed SPEC CPU2006 and Windows Desktop applications
  Heterogeneous and homogenous application mixes
  Synthetic traffic patterns: UR, Transpose, Tornado, Bit Complement
x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  64Kbyte private L1 caches
  Total 16Mbyte shared L2 caches; 16 MSHRs per bank
  DRAM model based on Micron DDR2-800
Most of our evaluations with perfect L2 caches
 Puts maximal stress on NoC
Simulation is cycle-accurate
Models stalls in network and processors
Self-throttling behavior
Aggressive processor model

## Slide 110: Evaluation Methodology
Energy model provided by Orion simulator [MICRO’02]
  70nm technology, 2 GHz routers at 1.0 Vdd
For BLESS, we model
  Additional energy to transmit header information
  Additional buffers needed on the receiver side
  Additional logic to reorder flits of individual packets at receiver
We partition network energy into buffer energy, router energy, and link energy, each having static and dynamic components.
Comparisons against non-adaptive and aggressive adaptive buffered routing algorithms (DO, MIN-AD, ROMM)

## Slide 111: Evaluation – Synthethic Traces
First, the bad news 
Uniform random injection
BLESS has significantly lower saturation throughput compared to buffered baseline.
Chart: Injection Rate (flits per cycle per node)
| 0 | 8.0000000000000043E-2 | 0.16 | 7.0000000000000021E-2 | 8.0000000000000043E-2 | 9.0000000000000024E-2 | 0.1 | 0.11 | 0.12000000000000002 | 0.13 | 0.14000000000000001 | 0.15000000000000011 | 0.16 | 0.17 | 0.1800000000000001 | 0.19 | 0.2 | 0.2100000000000001 | 0.22 | 0.23 | 0.2400000000000001 | 0.25 | 0.26 | 0.27 | 0.28000000000000008 | 0.2900000000000002 | 0.30000000000000021 | 0.31000000000000022 | 0.32000000000000023 | 0.33000000000000035 | 0.34 | 0.3500000000000002 | 0.36000000000000021 | 0.37000000000000022 | 0.38000000000000023 | 0.39000000000000024 | 0.4 | 0.4100000000000002 | 0.42000000000000021 | 0.43000000000000022 | 0.44 | 0.45 | 0.46 | 0.47000000000000008 | 0.4800000000000002 | 0.49000000000000021
FLIT-2 | 29.0347 | 29.0347 | 29.0347 | 29.0347 | 29.0347 | 29.3142 | 29.5848 | 29.8829 | 30.2641 | 30.6478 | 31.0371 | 31.5291 | 32.0485 | 32.514 | 33.0424 | 33.6214 | 34.2454 | 34.8647 | 35.5349 | 36.3327 | 37.1874 | 38.0545 | 39.1327 | 40.2686 | 41.8595 | 43.8418 | 48.2112 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
WORM-2 | 29.1135 | 29.1135 | 29.1135 | 29.1135 | 29.1135 | 29.3889 | 29.6607 | 29.9602 | 30.3294 | 30.7091 | 31.1068 | 31.6101 | 32.1665 | 32.6453 | 33.3123 | 33.9411 | 34.7541 | 35.5301 | 36.508 | 37.6649 | 38.9475 | 40.364 | 42.0965 | 44.2469 | 47.7519 | 57.8451 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
FLIT-1 | 22.2481 | 22.2481 | 22.2481 | 22.2481 | 22.2481 | 22.4505 | 22.6682 | 22.8838 | 23.1614 | 23.4459 | 23.7382 | 24.1268 | 24.5155 | 24.8599 | 25.261 | 25.6915 | 26.1454 | 26.6054 | 27.1534 | 27.7909 | 28.4923 | 29.2033 | 30.0413 | 31.1505 | 32.5742 | 34.4702 | 39.8047 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
WORM-1 | 22.3647 | 22.3647 | 22.3647 | 22.3647 | 22.3647 | 22.585 | 22.8079 | 23.0303 | 23.3201 | 23.6314 | 23.9379 | 24.3375 | 24.7663 | 25.1396 | 25.6411 | 26.1686 | 26.7838 | 27.4439 | 28.2236 | 29.1584 | 30.2441 | 31.4552 | 32.9357 | 35.035 | 38.7007 | 61.9914 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
MIN-AD | 28.3699 | 28.3699 | 28.3699 | 28.3699 | 28.3699 | 28.5388 | 28.6459 | 28.864 | 29.0263 | 29.2029 | 29.4106 | 29.6055 | 29.7855 | 30.0568 | 30.2965 | 30.5566 | 30.8537 | 31.067 | 31.3404 | 31.6329 | 31.9691 | 32.281 | 32.5873 | 33.0224 | 33.3879 | 33.7872 | 34.2208 | 34.6467 | 35.2042 | 35.8494 | 36.3318 | 36.9534 | 37.7887 | 38.4606 | 39.5018 | 40.4692 | 41.6397 | 43.0612 | 44.6159 | 46.6269 | 49.5462 | 54.2782 | 61.2888 | 82.5748 | 101 | 101
BLESS
Best Baseline
Is BLESS doomed…?

## Slide 112: Evaluation – Homogenous Case Study
milc benchmarks
(moderately intensive)
Perfect caches!
Very little performance degradation with BLESS
(less than 4% in dense network)
With router latency 1, BLESS can even outperform baseline (by ~10%)
Significant energy improvements (almost 40%)
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.991 | 7.9907 | 7.9892 | 7.9789 | 7.9802 | 7.9918 | 7.9907 | 15.6268 | 15.7797 | 15.6253 | 15.2216 | 15.0442 | 15.3638 | 15.2073 | 14.8309 | 14.7752 | 14.7082 | 14.7206 | 14.6774 | 16.2317 | 16.1992
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.40464 | 0.40495 | 0.40517 | 0.42894 | 0.4223 | 0.42804 | 0.42107 | 0.38681 | 0.38681 | 0.391 | 0.43437 | 0.44217 | 0.43081 | 0.43834 | 0.40835 | 0.41014 | 0.41114 | 0.43191 | 0.42337 | 0.37773 | 0.37158
LinkEnergy | 0.12364 | 0.12368 | 0.1237 | 0.14 | 0.14077 | 0.14024 | 0.14058 | 0.1871 | 0.1871 | 0.1874 | 0.23441 | 0.24339 | 0.23441 | 0.24365 | 0.1164 | 0.11652 | 0.11642 | 0.12893 | 0.12753 | 0.12452 | 0.12405
BufferEnergy | 0.47171 | 0.47418 | 0.47432 | 0.045804 | 0.041356 | 0.041234 | 0.043464 | 0.42609 | 0.42609 | 0.42825 | 0.039818 | 0.040263 | 0.039354 | 0.039719 | 0.47526 | 0.48429 | 0.48088 | 0.043196 | 0.038642 | 0.032973 | 0.031075
Baseline
BLESS
RL=1

## Slide 113: Evaluation – Homogenous Case Study
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.991 | 7.9907 | 7.9892 | 7.9789 | 7.9802 | 7.9918 | 7.9907 | 15.6268 | 15.7797 | 15.6253 | 15.2216 | 15.0442 | 15.3638 | 15.2073 | 14.8309 | 14.7752 | 14.7082 | 14.7206 | 14.6774 | 16.2317 | 16.1992
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.40464 | 0.40495 | 0.40517 | 0.42894 | 0.4223 | 0.42804 | 0.42107 | 0.38681 | 0.38681 | 0.391 | 0.43437 | 0.44217 | 0.43081 | 0.43834 | 0.40835 | 0.41014 | 0.41114 | 0.43191 | 0.42337 | 0.37773 | 0.37158
LinkEnergy | 0.12364 | 0.12368 | 0.1237 | 0.14 | 0.14077 | 0.14024 | 0.14058 | 0.1871 | 0.1871 | 0.1874 | 0.23441 | 0.24339 | 0.23441 | 0.24365 | 0.1164 | 0.11652 | 0.11642 | 0.12893 | 0.12753 | 0.12452 | 0.12405
BufferEnergy | 0.47171 | 0.47418 | 0.47432 | 0.045804 | 0.041356 | 0.041234 | 0.043464 | 0.42609 | 0.42609 | 0.42825 | 0.039818 | 0.040263 | 0.039354 | 0.039719 | 0.47526 | 0.48429 | 0.48088 | 0.043196 | 0.038642 | 0.032973 | 0.031075
Baseline
BLESS
RL=1
milc benchmarks
(moderately intensive)
Perfect caches!
Very little performance degradation with BLESS
(less than 4% in dense network)
With router latency 1, BLESS can even outperform baseline (by ~10%)
Significant energy improvements (almost 40%)
Observations:
Injection rates not extremely high on average  self-throttling!
For bursts and temporary hotspots, use network links as buffers!

## Slide 114: Evaluation – Further Results
BLESS increases buffer requirement at receiver by at most 2x  overall, energy is still reduced
Impact of memory latency
 with real caches, very little slowdown! (at most 1.5%)
See paper for details…
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.7417 | 7.7492 | 7.7292 | 7.7059 | 7.7181 | 8.0128 | 7.9959 | 15.0683 | 15.1571 | 15.0648 | 14.9256 | 14.9115 | 15.4871 | 15.381 | 15.2257 | 15.2105 | 15.1846 | 15.2005 | 15.1758 | 16.1669 | 16.1562

## Slide 115: Evaluation – Further Results
BLESS increases buffer requirement at receiver by at most 2x  overall, energy is still reduced
Impact of memory latency
 with real caches, very little slowdown! (at most 1.5%)
Heterogeneous application mixes
(we evaluate several mixes of intensive and non-intensive applications)
 little performance degradation
 significant energy savings in all cases
 no significant increase in unfairness across different applications
Area savings: ~60% of network area can be saved!
See paper for details…

## Slide 116: Evaluation – Aggregate Results
Aggregate results over all 29 applications
Sparse Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -39.4% | -28.1% | -46.4% | -41.0%
∆ System Performance | -0.5% | -3.2% | -0.15% | -0.55%
Chart: Energy (normalized)
| Mean | Worst-Case
RouterEnergy | 0.41542 | 0.44748 | 0.44 | 0.38395 | 0.43429 | 0.44348
LinkEnergy | 0.076955 | 0.094334 | 0.097193 | 0.1754 | 0.22557 | 0.23775
BufferEnergy | 0.50763 | 0.073091 | 0.062562 | 0.44066 | 0.058704 | 0.055516
FLIT
WORM
BASE
FLIT
WORM
BASE
Chart: W-Speedup
| Mean | Worst-Case
WeightedSpeedup | 7.9295 | 7.8761 | 7.8588 | 7.8079 | 7.5574 | 7.4834
FLIT
WORM
BASE

## Slide 117: Evaluation – Aggregate Results
Aggregate results over all 29 applications
Sparse Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -39.4% | -28.1% | -46.4% | -41.0%
∆ System Performance | -0.5% | -3.2% | -0.15% | -0.55%
Dense Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -32.8% | -14.0% | -42.5% | -33.7%
∆ System Performance | -3.6% | -17.1% | -0.7% | -1.5%

## Slide 118: Conclusion
For a very wide range of applications and network settings, buffers are not needed in NoC
  Significant energy savings (32% even in dense networks and perfect caches)
  Area-savings of 60%
  Simplified router and network design (flow control, etc…)
  Performance slowdown is minimal (can even increase!)
A strong case for a rethinking of NoC design!
We are currently working on future research.
  Support for quality of service, different traffic classes, energy-management, etc…