## Slide 1: 18-740/640 Computer Architecture Lecture 9: Emerging Memory Technologies
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015, 9/30/2015

## Slide 2: Required Readings
Required Reading Assignment:
  Lee et al., “Phase Change Technology and the Future of Main Memory,” IEEE Micro, Jan/Feb 2010.
Recommended References:
  M. Qureshi et al., “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
  H. Yoon et al., “Row buffer locality aware caching policies for hybrid memories,” ICCD 2012.
  J. Zhao et al., “FIRM: Fair and High-Performance Memory Control for Persistent Memory Systems,” MICRO 2014.

## Slide 3: Self-Optimizing DRAM Controllers
Problem: DRAM controllers difficult to design  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: Design a memory controller that adapts its scheduling policy decisions to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent that dynamically and continuously learns and employs the best scheduling policy.
Ipek+, “Self Optimizing Memory Controllers: A Reinforcement Learning Approach,” ISCA 2008.

## Slide 4: Self-Optimizing DRAM Controllers
Dynamically adapt the memory scheduling policy via interaction with the system at runtime
  Associate system states and actions (commands) with long term reward values: each action at a given state leads to a learned reward
  Schedule command with highest estimated long-term reward value in each state
  Continuously update reward values for <state, action> pairs based on feedback from system

## Slide 5: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 6: States, Actions, Rewards
Reward function
  +1 for scheduling Read and Write commands
  0 at all other times
  Goal is to maximize data bus utilization
State attributes
  Number of reads, writes, and load misses in transaction queue
  Number of pending writes and ROB heads waiting for referenced row
  Request’s relative ROB order
Actions
  Activate
  Write
  Read - load miss
  Read - store miss
  Precharge - pending
  Precharge - preemptive
  NOP

## Slide 7: Performance Results

## Slide 8: Self Optimizing DRAM Controllers
Advantages
  + Adapts the scheduling policy dynamically to changing workload behavior and to maximize a long-term target
  + Reduces the designer’s burden in finding a good scheduling policy. Designer specifies:
  1) What system variables might be useful
  2) What target to optimize, but not how to optimize it
Disadvantages and Limitations
  -- Black box: designer much less likely to implement what she cannot easily reason about
  -- How to specify different reward functions that can achieve different objectives? (e.g., fairness, QoS)
  -- Hardware complexity?

## Slide 9: More on Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 10: Evaluating New Ideas for Future (Memory) Architectures

## Slide 11: Simulation: The Field of Dreams

## Slide 12: Dreaming and Reality
An architect is in part a dreamer, a creator
Simulation is a key tool of the architect
Simulation enables
  The exploration of many dreams
  A reality check of the dreams
  Deciding which dream is better
Simulation also enables
  The ability to fool yourself with false dreams

## Slide 13: Why High-Level Simulation?
Problem: RTL simulation is intractable for design space exploration  too time consuming to design and evaluate
  Especially over a large number of workloads
  Especially if you want to predict the performance of a good chunk of a workload on a particular design
  Especially if you want to consider many design choices
    Cache size, associativity, block size, algorithms
    Memory control and scheduling algorithms
    In-order vs. out-of-order execution
    Reservation station sizes, ld/st queue size, register file size, …
    …
Goal: Explore design choices quickly to see their impact on the workloads we are designing the platform for

## Slide 14: Different Goals in Simulation
Explore the design space quickly and see what you want to
  potentially implement in a next-generation platform
  propose as the next big idea to advance the state of the art
  the goal is mainly to see relative effects of design decisions
Match the behavior of an existing system so that you can
  debug and verify it at cycle-level accuracy
  propose small tweaks to the design that can make a difference in performance or energy
  the goal is very high accuracy
Other goals in-between:
  Refine the explored design space without going into a full detailed, cycle-accurate design
  Gain confidence in your design decisions made by higher-level design space exploration

## Slide 15: Tradeoffs in Simulation
Three metrics to evaluate a simulator
  Speed
  Flexibility
  Accuracy
Speed: How fast the simulator runs (xIPS, xCPS)
Flexibility: How quickly one can modify the simulator to evaluate different algorithms and design choices?
Accuracy: How accurate the performance (energy) numbers the simulator generates are vs. a real design (Simulation error)
The relative importance of these metrics varies depending on where you are in the design process

## Slide 16: Trading Off Speed, Flexibility, Accuracy
Speed & flexibility affect:
  How quickly you can make design tradeoffs
Accuracy affects:
  How good your design tradeoffs may end up being
  How fast you can build your simulator (simulator design time)
Flexibility also affects:
  How much human effort you need to spend modifying the simulator
You can trade off between the three to achieve design exploration and decision goals

## Slide 17: High-Level Simulation
  Key Idea: Raise the abstraction level of modeling to give up some accuracy to enable speed & flexibility (and quick simulator design)
Advantage
  + Can still make the right tradeoffs, and can do it quickly
  + All you need is modeling the key high-level factors, you can omit corner case conditions
  + All you need is to get the “relative trends” accurately, not exact performance numbers
Disadvantage
  -- Opens up the possibility of potentially wrong decisions
  -- How do you ensure you get the “relative trends” accurately?

## Slide 18: Simulation as Progressive Refinement
High-level models (Abstract, C)
…
Medium-level models (Less abstract)
…
Low-level models (RTL with eveything modeled)
…
Real design
As you refine (go down the above list)
  Abstraction level reduces
  Accuracy (hopefully) increases (not necessarily, if not careful)
  Speed and flexibility reduce
  You can loop back and fix higher-level models

## Slide 19: Making The Best of Architecture
A good architect is comfortable at all levels of refinement
  Including the extremes
A good architect knows when to use what type of simulation

## Slide 20: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 21: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 22: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 23: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 24: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 25: Extra Credit Assignment
Review the Ramulator paper
  Send your reviews to me (omutlu@gmail.com)
Download and run Ramulator
  Compare DDR3, DDR4, SALP, HBM for the libquantum benchmark (provided in Ramulator repository)
  Send your brief report to me

## Slide 26: Emerging Memory Technologies

## Slide 27: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
Conclusions
Discussion

## Slide 28: Major Trends Affecting Main Memory (I)
Need for main memory capacity and bandwidth increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 29: Trends: Problems with DRAM as Main Memory
Need for main memory capacity and bandwidth increasing
  DRAM capacity hard to scale
Main memory energy/power is a key system design concern
  DRAM consumes high power due to leakage and refresh
DRAM technology scaling is ending
  DRAM capacity, cost, and energy/power hard to scale

## Slide 30: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
Conclusions
Discussion

## Slide 31: Requirements from an Ideal Memory System
Traditional
  Enough capacity
  Low cost
  High system performance (high bandwidth, low latency)
New
  Technology scalability: lower cost, higher capacity, lower energy
  Energy (and power) efficiency
  QoS support and configurability (for consolidation)

## Slide 32: Requirements from an Ideal Memory System
Traditional
  Higher capacity
  Continuous low cost
  High system performance (higher bandwidth, low latency)
New
  Technology scalability: lower cost, higher capacity, lower energy
  Energy (and power) efficiency
  QoS support and configurability (for consolidation)
Emerging, resistive memory technologies (NVM) can help

## Slide 33: How Do We Solve The Memory Problem?
Fix it: Make DRAM and controllers more intelligent
  New interfaces, functions, architectures: system-DRAM codesign
Eliminate or minimize it: Replace or (more likely) augment DRAM with a different technology
  New technologies and system-wide rethinking of memory & storage
Embrace it: Design heterogeneous memories (none of which are perfect) and map data intelligently across them
  New models for data management and maybe usage
…
Solutions (to memory scaling) require
software/hardware/device cooperation
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 34: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Expected to scale to 9nm (2022 [ITRS])
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have shortcomings as well
  Can they be enabled to replace/augment/surpass DRAM?
Lee+, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA’09, CACM’10, Micro’10.
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters 2012.
Yoon, Meza+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012.
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Lu+, “Loose Ordering Consistency for Persistent Memory,” ICCD 2014.
Zhao+, “FIRM: Fair and High-Performance Memory Control for Persistent Memory Systems,” MICRO 2014.
Yoon, Meza+, “Efficient Data Mapping and Buffering Techniques for Multi-Level Cell Phase-Change Memories,” ACM TACO 2014.
Ren+, “Dual-Scheme Checkpointing: “A Software-Transparent Mechanism for Supporting Crash Consistency in Persistent Memory Systems,” MICRO 2015.
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 35: Solution 3: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Technology X (e.g., PCM)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 36: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
Conclusions
Discussion

## Slide 37: The Promise of Emerging Technologies
Likely need to replace/augment DRAM with a technology that is
  Technology scalable
  And at least similarly efficient, high performance, and fault-tolerant
    or can be architected to be so
Some emerging resistive memory technologies appear promising
  Phase Change Memory (PCM)?
  Spin Torque Transfer Magnetic Memory (STT-MRAM)?
  Memristors? RRAM? ReRAM?
  And, maybe there are other ones
  Can they be enabled to replace/augment/surpass DRAM?

## Slide 38: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
Conclusions
Discussion

## Slide 39: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 40: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 41: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 42: What is Phase Change Memory?
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
PCM cell can be switched between states reliably and quickly

## Slide 43: How Does PCM Work?
Write: change phase via current injection
  SET: sustained current to heat cell above Tcryst
  RESET: cell heated above Tmelt and quenched
Read: detect phase via material resistance
  amorphous/crystalline
Large
Current
SET (cryst)
Low resistance
103-104 W
Small
Current
RESET (amorph)
High resistance
Access
Device
Memory
Element
106-107 W
Photo Courtesy: Bipin Rajendran, IBM
Slide Courtesy: Moinuddin Qureshi, IBM

## Slide 44: Opportunity: PCM Advantages
Scales better than DRAM, Flash
  Requires current pulses, which scale linearly with feature size
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
Can be denser than DRAM
  Can store multiple bits per cell due to large resistance range
  Prototypes with 2 bits/cell in ISSCC’08, 4 bits/cell by 2012
Non-volatile
  Can retain data for >10 years at 85C
No refresh needed, low idle power

## Slide 45: PCM Resistance → Value
Cell resistance
1
0
Cell value:

## Slide 46: Multi-Level Cell PCM
Multi-level cell: more than 1 bit per cell
  Further increases density by 2 to 4x [Lee+,ISCA'09]
But MLC-PCM also has drawbacks
  Higher latency and energy than single-level cell PCM

## Slide 47: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Bit 1
Bit 0

## Slide 48: MLC-PCM Resistance → Value
Cell resistance
1
1
0
0
0
1
1
0
Cell value:
Less margin between values
→ need more precise sensing/modification of cell contents
→ higher latency/energy (~2x for reads and 4x for writes)

## Slide 49: Phase Change Memory Properties
Surveyed prototypes from 2003-2008 (ITRS, IEDM, VLSI, ISSCC)
Derived PCM parameters for F=90nm
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 51: Phase Change Memory Properties: Latency
Latency comparable to, but slower than DRAM
Read Latency
  50ns: 4x DRAM, 10-3x NAND Flash
Write Latency
  150ns: 12x DRAM
Write Bandwidth
  5-10 MB/s: 0.1x DRAM, 1x NAND Flash

## Slide 52: Phase Change Memory Properties
Dynamic Energy
  40 uA Rd, 150 uA Wr
  2-43x DRAM, 1x NAND Flash
Endurance
  Writes induce phase change at 650C
  Contacts degrade from thermal expansion/contraction
  108 writes per cell
  10-8x DRAM, 103x NAND Flash
Cell Size
  9-12F2 using BJT, single-level cells
  1.5x DRAM, 2-3x NAND (will scale with feature size, MLC)

## Slide 53: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system
  Ensure secure and fault-tolerant PCM operation

## Slide 54: PCM-based Main Memory: Challenges
Where to place PCM in the memory hierarchy?
  Hybrid OS controlled PCM-DRAM
  Hybrid OS controlled PCM and hardware-controlled DRAM
  Pure PCM main memory
How to mitigate shortcomings of PCM?
How to minimize amount of DRAM in the system?
How to take advantage of (byte-addressable and fast) non-volatile main memory?
Can we design specific-NVM-technology-agnostic techniques?

## Slide 55: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09, Meza+ IEEE CAL’12]:
  How to partition/migrate data between PCM and DRAM

## Slide 56: Hybrid Memory Systems: Challenges
Partitioning
  Should DRAM be a cache or main memory, or configurable?
  What fraction? How many controllers?
Data allocation/movement (energy, performance, lifetime)
  Who manages allocation/movement?
  What are good control algorithms?
  How do we prevent degradation of service due to wearout?
Design of cache hierarchy, memory controllers, OS
  Mitigate PCM shortcomings, exploit PCM advantages
Design of PCM/DRAM chips and modules
  Rethink the design of PCM/DRAM with new requirements

## Slide 57: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 58: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ) device
  Reference layer: Fixed magnetic orientation
  Free layer: Parallel or anti-parallel
Magnetic orientation of the free layer determines logical state of device
  High vs. low resistance
Write: Push large current through MTJ to change orientation of free layer
Read: Sense current flow
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 59: Aside: STT MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 60: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
Conclusions
Discussion

## Slide 61: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 62: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 63: Architecting PCM to Mitigate Shortcomings
Idea 1: Use multiple narrow row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 64: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 65: More on PCM As Main Memory
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)

## Slide 66: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
Conclusions
Discussion

## Slide 67: Hybrid Memory Systems
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 68: One Option: DRAM as a Cache for PCM
PCM is main memory; DRAM caches memory rows/blocks
  Benefits: Reduced latency on DRAM cache hit; write filtering
Memory controller hardware manages the DRAM cache
  Benefit: Eliminates system software overhead
Three issues:
  What data should be placed in DRAM versus kept in PCM?
  What is the granularity of data movement?
  How to design a low-cost hardware-managed DRAM cache?
Two idea directions:
  Locality-aware data placement [Yoon+ , ICCD 2012]
  Cheap tag stores and dynamic granularity [Meza+, IEEE CAL 2012]

## Slide 69: DRAM as a Cache for PCM
Goal: Achieve the best of both DRAM and PCM/NVM
  Minimize amount of DRAM w/o sacrificing performance, endurance
  DRAM as cache to tolerate PCM latency and write bandwidth
  PCM as main memory to provide large capacity at good cost and power
DATA
PCM Main Memory
DATA
T
DRAM Buffer
PCM Write Queue
T=Tag-Store
Processor
Flash
Or
HDD
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 70: Write Filtering Techniques
Lazy Write: Pages from disk installed only in DRAM, not PCM
Partial Writes: Only dirty lines from DRAM page written back
Page Bypass: Discard pages with poor reuse on DRAM eviction
Qureshi et al., “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Processor
DATA
PCM Main Memory
DATA
T
DRAM Buffer
Flash
Or
HDD

## Slide 71: Results: DRAM as PCM Cache (I)
Simulation of 16-core system, 8GB DRAM main-memory at 320 cycles, HDD (2 ms) with Flash (32 us) with Flash hit-rate of 99%
Assumption: PCM 4x denser, 4x slower than DRAM
DRAM block size = PCM page size (4kB)
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Notes: Workloads:
Database workloads & Data parallel kernels
1. Database workloads: db1 and db2
2. Unix utilities: qsort and binary search
3. Data Mining : K-means and Gauss Seidal
4. Streaming: DAXPY and Vector Dot Product

## Slide 72: Results: DRAM as PCM Cache (II)
PCM-DRAM Hybrid performs similarly to similar-size DRAM
Significant energy savings with PCM-DRAM Hybrid
Average lifetime: 9.7 years (no guarantees)
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 73: More on DRAM-PCM Hybrid Memory
Scalable High-Performance Main Memory System Using Phase-Change Memory Technology. Moinuddin K. Qureshi, Viji Srinivasan, and Jude A. Rivers Appears in the International Symposium on Computer Architecture (ISCA) 2009.

## Slide 74: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
    Row-Locality Aware Data Placement
    Efficient DRAM (or Technology X) Caches
Conclusions
Discussion

## Slide 75: Hybrid Memory
Key question: How to place data between the heterogeneous memory devices?
DRAM
PCM
CPU
MC
MC
Notes: One key question in the design of a hybrid memory system is: How to place data between the heterogeneous memory devices?
Our goal in this work is to answer this question.

## Slide 76: Hybrid Memory: A Closer Look
MC
MC
DRAM
(small capacity cache)
PCM (large capacity store)
CPU
Memory channel
Bank
Bank
Bank
Bank
Row buffer
Notes: Here’s a closer look at a hybrid memory system employing both DRAM and PCM.
Typically, the DRAM is used as a small capacity cache, and the PCM is used as a large capacity store.
When the processor needs data, it will first look to see if the data is in DRAM. If the data is indeed in DRAM, the processor will retrieve the data from there. If the data is not in DRAM, the processor will retrieve the data from PCM.
Both DRAM and PCM are organized into banks that are capable of operating independently. Also, in each bank, there are peripheral circuitries known as the row buffers.

## Slide 77: Row Buffers and Latency
Row (buffer) hit: Access data from row buffer  fast
Row (buffer) miss: Access data from cell array  slow
LOAD X
LOAD X+1
LOAD X+1
LOAD X
ROW ADDRESS
ROW DATA
Row buffer miss!
Row buffer hit!
Bank
Row buffer
CELL ARRAY
Notes: Row buffers affect memory latency is a profound way.
Row buffers effectively store the most recently accessed row in memory.
They are typically 2 to 8KB in length, for a single rank.
When data is requested in memory, it is first checked to see if the data is in the row buffer. If the data is not in the row buffer, this is called a row buffer miss. In this case, we need to read a row full of data from the memory cell array into the row buffer, and the memory request is served. In a subsequent memory request, if the requested data is already latched in the row buffer, this is called a row buffer hit, and the data can be retrieved without having to access the memory cell array, which in the case of PCM, is a high latency operation.
In summary, on a row hit, data is accessed from the row buffer, which is fast. On a row miss, data is accessed from the cell array, which is slow.

## Slide 78: Key Observation
Row buffers exist in both DRAM and PCM
  Row hit latency similar in DRAM & PCM [Lee+ ISCA’09]
  Row miss latency small in DRAM, large in PCM
Place data in DRAM which
  is likely to miss in the row buffer (low row buffer locality) miss penalty is smaller in DRAM
  AND
  is reused many times  cache only the data worth the movement cost and DRAM space
Notes: Our key observation is that row buffers exist in both DRAM and PCM.
Row hit latency, which does not access the memory cell array, is similar in DRAM and PCM.
It is for a row miss that the memory access latency is small in DRAM and large in PCM.
Therefore we would like to place data in DRAM which:
Is likely to miss in the row buffer, which we call as having low row buffer locality, since the row buffer miss penalty is small in DRAM than it is in PCM.
And we would like to place data in DRAM which is reused many times, so that we cache only the data that is worth the movement cost.

## Slide 79: System Performance
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.9552 | 1.0469 | 1
FREQ-Dyn | 1.0502 | 1.1074 | 1.0784
RBLA | 1.0713 | 1.0997 | 1.0854
RBLA-Dyn | 1.1204 | 1.1511 | 1.1356
10%
14%
Benefit 1: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM
17%
Benefit 1: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM
Benefit 2: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 2: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 3: Balanced memory request load between DRAM and PCM
Notes: Here are the system performance results of the different hybrid memory caching policies.
RBLA-Dyn achieves 17% performance improvement over frek in server workloads, 10% in cloud, and 14% overall.
This is due to a number of reasons.
The first is that RBLA-Dyn increases row buffer locality in PCM by moving low row buffer locality data to DRAM.
The second is that RBLA-Dyn reduces memory bandwidth consumption due its stricter caching criteria.
And RBLA-Dyn also has the effect of balancing the memory request load between DRAM and PCM by letting rows with high row buffer locality remain in PCM, instead of fetching all accessed data to DRAM.

## Slide 80: Compared to All-PCM/DRAM
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
Our mechanism achieves 31% better performance than all PCM, within 29% of all DRAM performance
31%
29%
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 81: For More on Hybrid Memory Data Placement
HanBin Yoon, Justin Meza, Rachata Ausavarungnirun, Rachael Harding, and Onur Mutlu, "Row Buffer Locality Aware Caching Policies for Hybrid Memories" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (pptx) (pdf)

## Slide 82: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
    Row-Locality Aware Data Placement
    Efficient DRAM (or Technology X) Caches
Conclusions
Discussion

## Slide 83: The Problem with Large DRAM Caches
A large DRAM cache requires a large metadata (tag + block-based information) store
How do we design an efficient DRAM cache?
DRAM
PCM
CPU
(small, fast cache)
(high capacity)
Mem Ctlr
Mem Ctlr
LOAD X
Access X
Metadata:
X  DRAM
X

## Slide 84: Idea 1: Tags in Memory
Store tags in the same row as data in DRAM
  Store metadata in same row as their data
  Data and metadata can be accessed together
Benefit: No on-chip tag storage overhead
Downsides:
  Cache hit determined only after a DRAM access
  Cache hit requires two DRAM accesses
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 85: Idea 2: Cache Tags in SRAM
Recall Idea 1: Store all metadata in DRAM
  To reduce metadata storage overhead
Idea 2: Cache in on-chip SRAM frequently-accessed metadata
  Cache only a small amount to keep SRAM size small

## Slide 86: Idea 3: Dynamic Data Transfer Granularity
Some applications benefit from caching more data
  They have good spatial locality
Others do not
  Large granularity wastes bandwidth and reduces cache utilization
Idea 3: Simple dynamic caching granularity policy
  Cost-benefit analysis to determine best DRAM cache block size
  Group main memory into sets of rows
  Some row sets follow a fixed caching granularity
  The rest of main memory follows the best granularity
    Cost–benefit analysis: access latency versus number of cachings
    Performed every quantum

## Slide 87: TIMBER Tag Management
A Tag-In-Memory BuffER (TIMBER)
  Stores recently-used tags in a small amount of SRAM
Benefits: If tag is cached:
  no need to access DRAM twice
  cache hit determined quickly
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Row Tag
LOAD X
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 88: TIMBER Tag Management Example (I)
Case 1: TIMBER hit
Bank
Bank
Bank
Bank
CPU
Mem Ctlr
Mem Ctlr
LOAD X
TIMBER: X  DRAM
X
Access X
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Our proposal

## Slide 89: TIMBER Tag Management Example (II)
Case 2: TIMBER miss
CPU
Mem Ctlr
Mem Ctlr
LOAD Y
Y  DRAM
Bank
Bank
Bank
Bank
Access Metadata(Y)
Y
1. Access M(Y)
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Miss
M(Y)
2. Cache M(Y)
Row143
3. Access Y (row hit)

## Slide 90
Metadata Storage Performance
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
(Ideal)

## Slide 91
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
-48%
Performance degrades due to increased metadata lookup access latency
(Ideal)

## Slide 92
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
36%
Increased row locality reduces average memory access latency
(Ideal)

## Slide 93
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
23%
Data with locality can access metadata at SRAM latencies
(Ideal)

## Slide 94
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
Dynamic Granularity Performance
10%
Reduced channel contention and improved spatial locality

## Slide 95
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
TIMBER Performance
-6%
Reduced channel contention and improved spatial locality
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 96
Chart: Normalized Performance per Watt (for Memory System)
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.73082 | 0.75384 | 0.89249 | 1.1769
TIMBER Energy Efficiency
Fewer migrations reduce transmitted data and channel contention
18%
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 97: More on Large DRAM Cache Design
Justin Meza, Jichuan Chang, HanBin Yoon, Onur Mutlu, and Parthasarathy Ranganathan, "Enabling Efficient and Scalable Hybrid Memories Using Fine-Granularity DRAM Cache Management" IEEE Computer Architecture Letters (CAL), February 2012.

## Slide 98: STT-MRAM As Main Memory

## Slide 99: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ) device
  Reference layer: Fixed magnetic orientation
  Free layer: Parallel or anti-parallel
Magnetic orientation of the free layer determines logical state of device
  High vs. low resistance
Write: Push large current through MTJ to change orientation of free layer
Read: Sense current flow
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 100: STT-MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 101: Architected STT-MRAM as Main Memory
4-core, 4GB main memory, multiprogrammed workloads
~6% performance loss, ~60% energy savings vs. DRAM
Chart: Performance vs. DRAM
STT-RAM (base) | 0.95574 | 0.91812 | 0.93435 | 0.95579 | 0.95738 | 0.92083 | 0.95404 | 0.93019 | 0.95413 | 0.94507 | 0.92103 | 0.94061
STT-RAM (opt) | 0.96014 | 0.91453 | 0.9443 | 0.95632 | 0.95951 | 0.92092 | 0.95948 | 0.93564 | 0.96003 | 0.94574 | 0.93546 | 0.94473
Chart: Energy vs. DRAM
| mpmix0 | mpmix1 | mpmix2 | mpmix3 | mpmix4 | mpmix5 | mpmix6 | mpmix7 | mpmix8 | mpmix9 | mpmix10 | Average
ACT+PRE | 0.30175 | 0.27646 | 0.37425 | 0.32119 | 0.33973 | 0.34883 | 0.36197 | 0.2603 | 0.33524 | 0.39385 | 0.32655 | 0.33092
WB | 0.018529 | 0.027397 | 0.013518 | 0.015979 | 0.022233 | 0.018649 | 0.015872 | 0.025826 | 0.01687 | 0.016362 | 0.015008 | 0.018749
RB | 0.01752 | 0.014162 | 0.010281 | 0.018781 | 0.023665 | 0.010148 | 0.024161 | 0.016986 | 0.013315 | 0.012743 | 0.010166 | 0.01563
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 102: More on STT-MRAM as Main Memory
Emre Kultursay, Mahmut Kandemir, Anand Sivasubramaniam, and Onur Mutlu, "Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative" Proceedings of the 2013 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), Austin, TX, April 2013. Slides (pptx) (pdf)

## Slide 103: Other Opportunities with Emerging Technologies
Merging of memory and storage
  e.g., a single interface to manage all data
New applications
  e.g., ultra-fast checkpoint and restore
More robust system design
  e.g., reducing data loss
Processing tightly-coupled with memory
  e.g., enabling efficient search and filtering

## Slide 104: Merging of Memory and Storage: Persistent Memory Managers

## Slide 105: Coordinated Memory and Storage with NVM (I)
The traditional two-level storage model is a bottleneck with NVM
  Volatile data in memory  a load/store interface
  Persistent data in storage  a file system interface
  Problem: Operating system (OS) and file system (FS) code to locate, translate, buffer data become performance and energy bottlenecks with fast NVM stores
Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …
Persistent (e.g., Phase-Change)
Memory

## Slide 106: Coordinated Memory and Storage with NVM (II)
Goal: Unify memory and storage management in a single unit to eliminate wasted work to locate, transfer, and translate data
  Improves both energy and performance
  Simplifies programming model as well
Unified Memory/Storage
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 107: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 108: The Persistent Memory Manager (PMM)
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Persistent objects
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 109: Efficient Data Mapping among Heterogeneous Devices
A persistent memory exposes a large, persistent address space
  But it may use many different devices to satisfy this goal
  From fast, low-capacity volatile DRAM to slow, high-capacity non-volatile HDD or Flash
  And other NVM devices in between
Performance and energy can benefit from good placement of data among these devices
  Utilizing the strengths of each device and avoiding their weaknesses, if possible
  For example, consider two important application characteristics: locality and persistence

## Slide 110: Efficient Data Mapping among Heterogeneous Devices
Notes: Here, we’ve plotted these two important characteristics as axes on a graph. On the bottom is persistence, from temporary – the data does not need to be saved across program executions – on the left to persistent – the data must remain across executions for correct operation – on the right. From bottom to top we have data that has more locality – and is accessed very frequently in a short amount of time or space – to data that has less locality – which may predominantly be accessed in a random manner.
Let’s take a look at two examples of data and how they map onto this space.

## Slide 111: Efficient Data Mapping among Heterogeneous Devices
X
Columns in a column store that are scanned through only infrequently
 place on Flash
Notes: First we have some data that requires high persistence but has little locality. Such data might be the columns in a column store that are only scanned through infrequently. While it is essential that this data remain persistent across runs of the program, it may not be accessed that frequently, and therefore may be more beneficial to place on slightly slower, persistent memory devices, such as Flash.

## Slide 112: Efficient Data Mapping among Heterogeneous Devices
X
Columns in a column store that are scanned through only infrequently
 place on Flash
X
Frequently-updated index for a Content Delivery Network (CDN)  place in DRAM
Applications or system software can provide hints for data placement
Notes: On the other end of the perspective is data that has high locality but is only ephemeral and not needed between executions. Data in a Content Delivery Network that is cached as it is accessed and is constantly being updated and replaced, is a great candidate for placing in DRAM on such systems.

## Slide 113: Performance Benefits of a Single-Level Store
~5X
~24X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 114: Energy Benefits of a Single-Level Store
~5X
~16X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 115: More on Single-Level Stores
Justin Meza, Yixin Luo, Samira Khan, Jishen Zhao, Yuan Xie, and Onur Mutlu, "A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory" Proceedings of the 5th Workshop on Energy-Efficient Design (WEED), Tel-Aviv, Israel, June 2013. Slides (pptx) Slides (pdf)

## Slide 116: Enabling and Exploiting NVM: Issues
Many issues and ideas from technology layer to algorithms layer
Enabling NVM and hybrid memory
  How to tolerate errors?
  How to enable secure operation?
  How to tolerate performance and power shortcomings?
  How to minimize cost?
Exploiting emerging technologies
  How to exploit non-volatility?
  How to minimize energy consumption?
  How to exploit NVM on chip?
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 117: Security Challenges of Emerging Technologies
1. Limited endurance  Wearout attacks
2. Non-volatility  Data persists in memory after crash/poweroff
 Inconsistency and retrieval of privileged information
3. Multiple bits per cell  Information leakage (via side channel)

## Slide 118: Securing Emerging Memory Technologies
1. Limited endurance  Wearout attacks
Better architecting of memory chips to absorb writes
Hybrid memory system management
Online wearout attack detection
2. Non-volatility  Data persists in memory after crash/poweroff
 Inconsistency and retrieval of privileged information Efficient encryption/decryption of whole main memory
Hybrid memory system management
3. Multiple bits per cell  Information leakage (via side channel)
System design to hide side channel information

## Slide 119: Agenda
Major Trends Affecting Main Memory
Requirements from an Ideal Main Memory System
Opportunity: Emerging Memory Technologies
  Background
  PCM (or Technology X) as DRAM Replacement
  Hybrid Memory Systems
Conclusions
Discussion

## Slide 120: Summary: Memory Scaling (with NVM)
Main memory scaling problems are a critical bottleneck for system performance, efficiency, and usability
Solution 1: Tolerate DRAM
Solution 2: Enable emerging memory technologies
  Replace DRAM with NVM by architecting NVM chips well
  Hybrid memory systems with automatic data management
An exciting topic with many other solution directions & ideas
  Hardware/software/device cooperation essential
  Memory, storage, controller, software/app co-design needed
  Coordinated management of persistent memory and storage
  Application and hardware cooperative management of NVM

## Slide 121: 18-740/640 Computer Architecture Lecture 9: Emerging Memory Technologies
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015, 9/30/2015