## Slide 1: 18-740/640 Computer Architecture Lecture 14: Memory Resource Management I
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015, 10/26/2015

## Slide 2: Required Readings
Required Reading Assignment:
  Qureshi and Patt, “Utility-Based Cache Partitioning: A Low-Overhead, High-Performance, Runtime Mechanism to Partition Shared Caches,” MICRO 2006.
Recommended References:
  Seshadri et al., “The Evicted-Address Filter: A Unified Mechanism to Address both Cache Pollution and Thrashing,” PACT 2012.
  Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.
  Lin et al., “Gaining Insights into Multi-Core Cache Partitioning: Bridging the Gap between Simulation and Real Systems,” HPCA 2008.

## Slide 3: Shared Resource Design for Multi-Core Systems

## Slide 4: Memory System: A Shared Resource View
Storage

## Slide 5: Resource Sharing Concept
Idea: Instead of dedicating a hardware resource to a hardware context, allow multiple contexts to use it
  Example resources: functional units, pipeline, caches, buses, memory
Why?
+ Resource sharing improves utilization/efficiency  throughput
  When a resource is left idle by one thread, another thread can use it; no need to replicate shared data
+ Reduces communication latency
  For example, shared data kept in the same cache in SMT processors
+ Compatible with the shared memory model

## Slide 6: Resource Sharing Disadvantages
Resource sharing results in contention for resources
  When the resource is not idle, another thread cannot use it
  If space is occupied by one thread, another thread needs to re-occupy it
- Sometimes reduces each or some thread’s performance
- Thread performance can be worse than when it is run alone
- Eliminates performance isolation  inconsistent performance across runs
- Thread performance depends on co-executing threads
- Uncontrolled (free-for-all) sharing degrades QoS
- Causes unfairness, starvation
Need to efficiently and fairly utilize shared resources

## Slide 7: Example: Problem with Shared Caches
L2 $
L1 $
……
Processor Core 1
L1 $
Processor Core 2
←t1
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.

## Slide 8: Example: Problem with Shared Caches
L1 $
Processor Core 1
L1 $
Processor Core 2
L2 $
……
t2→
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.

## Slide 9: Example: Problem with Shared Caches
L1 $
L2 $
……
Processor Core 1
Processor Core 2
←t1
L1 $
t2→
t2’s throughput is significantly reduced due to unfair cache sharing.
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.

## Slide 10: Need for QoS and Shared Resource Mgmt.
Why is unpredictable performance (or lack of QoS) bad?
Makes programmer’s life difficult
  An optimized program can get low performance (and performance varies widely depending on co-runners)
Causes discomfort to user
  An important program can starve
  Examples from shared software resources
Makes system management difficult
  How do we enforce a Service Level Agreement when hardware resources are sharing is uncontrollable?

## Slide 11: Resource Sharing vs. Partitioning
Sharing improves throughput
  Better utilization of space
Partitioning provides performance isolation (predictable performance)
  Dedicated space
Can we get the benefits of both?
Idea: Design shared resources such that they are efficiently utilized, controllable and partitionable
  No wasted resource + QoS mechanisms for threads

## Slide 12: Shared Hardware Resources
Memory subsystem (in both Multi-threaded and Multi-core)
  Non-private caches
  Interconnects
  Memory controllers, buses, banks
I/O subsystem (in both Multi-threaded and Multi-core)
  I/O, DMA controllers
  Ethernet controllers
Processor (in Multi-threaded)
  Pipeline resources
  L1 caches

## Slide 13: Multi-core Issues in Caching
How does the cache hierarchy change in a multi-core system?
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 14: Shared Caches Between Cores
Advantages:
  High effective capacity
  Dynamic partitioning of available cache space
    No fragmentation due to static partitioning
  Easier to maintain coherence (a cache block is in a single location)
  Shared data and locks do not ping pong between caches
Disadvantages
  Slower access
  Cores incur conflict misses due to other cores’ accesses
    Misses due to inter-core interference
    Some cores can destroy the hit rate of other cores
  Guaranteeing a minimum level of service (or fairness) to each core is harder (how much space, how much bandwidth?)

## Slide 15: Shared Caches: How to Share?
Free-for-all sharing
  Placement/replacement policies are the same as a single core system (usually LRU or pseudo-LRU)
  Not thread/application aware
  An incoming block evicts a block regardless of which threads the blocks belong to
Problems
  Inefficient utilization of cache: LRU is not the best policy
  A cache-unfriendly application can destroy the performance of a cache friendly application
  Not all applications benefit equally from the same amount of cache: free-for-all might prioritize those that do not benefit
  Reduced performance, reduced fairness

## Slide 16: Handling Shared Caches
Controlled cache sharing
  Approach 1: Design shared caches but control the amount of cache allocated to different cores
  Approach 2: Design “private” caches but spill/receive data from one cache to another
More efficient cache utilization
  Minimize the wasted cache space
    by keeping out useless blocks
    by keeping in cache blocks that have maximum benefit
    by minimizing redundant data

## Slide 17: Controlled Cache Sharing: Examples
Utility based cache partitioning
  Qureshi and Patt, “Utility-Based Cache Partitioning: A Low-Overhead, High-Performance, Runtime Mechanism to Partition Shared Caches,” MICRO 2006.
  Suh et al., “A New Memory Monitoring Scheme for Memory-Aware Scheduling and Partitioning,” HPCA 2002.
Fair cache partitioning
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.
Shared/private mixed cache mechanisms
  Qureshi, “Adaptive Spill-Receive for Robust High-Performance Caching in CMPs,” HPCA 2009.
  Hardavellas et al., “Reactive NUCA: Near-Optimal Block Placement and Replication in Distributed Caches,” ISCA 2009.

## Slide 18: Efficient Cache Utilization: Examples
Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2005.
Seshadri et al., “The Evicted-Address Filter: A Unified Mechanism to Address both Cache Pollution and Thrashing,” PACT 2012.
Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.

## Slide 19: Controlled Shared Caching

## Slide 20: Hardware-Based Cache Partitioning

## Slide 21: Utility Based Shared Cache Partitioning
Goal: Maximize system throughput
Observation: Not all threads/applications benefit equally from caching  simple LRU replacement not good for system throughput
Idea: Allocate more cache space to applications that obtain the most benefit from more space
The high-level idea can be applied to other shared resources as well.
Qureshi and Patt, “Utility-Based Cache Partitioning: A Low-Overhead, High-Performance, Runtime Mechanism to Partition Shared Caches,” MICRO 2006.
Suh et al., “A New Memory Monitoring Scheme for Memory-Aware Scheduling and Partitioning,” HPCA 2002.

## Slide 22: Marginal Utility of a Cache Way
Utility Uab = Misses with a ways – Misses with b ways
Low Utility
High Utility
Saturating Utility
Num ways from 16-way 1MB L2
Misses per 1000 instructions

## Slide 23: Utility Based Shared Cache Partitioning Motivation
Num ways from 16-way 1MB L2
Misses per 1000 instructions (MPKI)
equake
vpr
LRU
UTIL
Improve performance by giving more cache to the application that benefits more from cache

## Slide 24: Utility Based Cache Partitioning (III)
Three components:
Utility Monitors (UMON) per core
Partitioning Algorithm (PA)
Replacement support to enforce partitions
I$
D$
Core1
I$
D$
Core2
Shared
L2 cache
Main Memory
UMON1
UMON2
PA

## Slide 25: Utility Monitors
For each core, simulate LRU policy using ATD
Hit counters in ATD to count hits per recency position
LRU is a stack algorithm: hit counts  utility E.g. hits(2 ways) = H0+H1
MTD
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
ATD
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
+
+
+
+
(MRU)H0 H1 H2…H15(LRU)

## Slide 26: Utility Monitors

## Slide 27: Dynamic Set Sampling
Extra tags incur hardware and power overhead
Dynamic Set Sampling reduces overhead [Qureshi, ISCA’06]
32 sets sufficient (analytical bounds)
Storage < 2kB/UMON
MTD
ATD
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
+
+
+
+
(MRU)H0 H1 H2…H15(LRU)
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
Set B
Set E
Set G
UMON (DSS)
Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2005.

## Slide 28: Partitioning Algorithm
Evaluate all possible partitions and select the best
With a ways to core1 and (16-a) ways to core2:
Hitscore1 = (H0 + H1 + … + Ha-1) ---- from UMON1 Hitscore2 = (H0 + H1 + … + H16-a-1) ---- from UMON2
Select a that maximizes (Hitscore1 + Hitscore2)
Partitioning done once every 5 million cycles

## Slide 29: Way Partitioning
Way partitioning support: [Suh+ HPCA’02, Iyer ICS’04]
  Each line has core-id bits
  On a miss, count ways_occupied in set by miss-causing app
ways_occupied < ways_given
Yes
No
Victim is the LRU line from other app
Victim is the LRU line from miss-causing app

## Slide 30: Performance Metrics
Three metrics for performance:
Weighted Speedup (default metric)  perf = IPC1/SingleIPC1 + IPC2/SingleIPC2  correlates with reduction in execution time
Throughput  perf = IPC1 + IPC2  can be unfair to low-IPC application
Hmean-fairness  perf = hmean(IPC1/SingleIPC1, IPC2/SingleIPC2)  balances fairness and performance

## Slide 31: Weighted Speedup Results for UCP

## Slide 32: IPC Results for UCP
UCP improves average throughput by 17%

## Slide 33: Any Problems with UCP So Far?
- Scalability to many cores
- Non-convex curves?
Time complexity of partitioning low for two cores (number of possible partitions ≈ number of ways)
Possible partitions increase exponentially with cores
For a 32-way cache, possible partitions:
  4 cores  6545
  8 cores  15.4 million
Problem NP hard  need scalable partitioning algorithm

## Slide 34: Greedy Algorithm [Stone+ ToC ’92]
Greedy Algorithm (GA) allocates 1 block to the app that has the max utility for one block. Repeat till all blocks allocated
Optimal partitioning when utility curves are convex
Pathological behavior for non-convex curves
Stone et al., “Optimal Partitioning of Cache Memory,” IEEE ToC 1992.

## Slide 35: Problem with Greedy Algorithm
Problem: GA considers benefit only from the immediate block. Hence, it fails to exploit large gains from looking ahead
In each iteration, the utility for 1 block:
U(A) = 10 misses U(B) = 0 misses
Blocks assigned
Misses
All blocks assigned to A, even if B has same miss reduction with fewer blocks

## Slide 36: Lookahead Algorithm
Marginal Utility (MU) = Utility per cache resource
  MUab = Uab/(b-a)
GA considers MU for 1 block.
LA (Lookahead Algorithm) considers MU for all possible allocations
Select the app that has the max value for MU. Allocate it as many blocks required to get max MU
Repeat until all blocks are assigned

## Slide 37: Lookahead Algorithm Example
  Time complexity ≈ ways2/2 (512 ops for 32-ways)
Iteration 1:
MU(A) = 10/1 block MU(B) = 80/3 blocks
B gets 3 blocks
Result: A gets 5 blocks and B gets 3 blocks (Optimal)
Next five iterations:
MU(A) = 10/1 block
MU(B) = 0
A gets 1 block
Blocks assigned
Misses

## Slide 38: UCP Results
Four cores sharing a 2MB 32-way L2
Mix2
(swm-glg-mesa-prl)
Mix3
(mcf-applu-art-vrtx)
Mix4
(mcf-art-eqk-wupw)
Mix1
(gap-applu-apsi-gzp)
LA performs similar to EvalAll, with low time-complexity
LRU
UCP(Greedy)
UCP(Lookahead)
UCP(EvalAll)

## Slide 39: Utility Based Cache Partitioning
Advantages over LRU
  + Improves system throughput
  + Better utilizes the shared cache
Disadvantages
  - Fairness, QoS?
Limitations
  - Scalability: Partitioning limited to ways. What if you have numWays < numApps?
  - Scalability: How is utility computed in a distributed cache?
  - What if past behavior is not a good predictor of utility?

## Slide 40: Fair Shared Cache Partitioning
Goal: Equalize the slowdowns of multiple threads sharing the cache
Idea: Dynamically estimate slowdowns due to sharing and assign cache blocks to balance slowdowns
  Approximate slowdown with change in miss rate
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.

## Slide 41: Dynamic Fair Caching Algorithm
P1:
P2:
P1:
P2:
Target Partition
MissRate alone
P1:
P2:
MissRate shared
Repartitioning
interval

## Slide 42: Dynamic Fair Caching Algorithm
1st Interval
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:
P2:
MissRate shared
P1:20%
P2:15%
MissRate shared
P1:256KB
P2:256KB
Target Partition
Notes: At the very beginning, the static profiling obtained miss rate of 20% for P1 and 5% for P2.
Initially, target partitions are equal to P1 and P2.
After the 1st interval, we get shared miss rate by dynamic profiling and it has 20% and 15% miss rate.

## Slide 43: Dynamic Fair Caching Algorithm
Repartition!
Evaluate Slowdown
P1: 20% / 20%
P2: 15% / 5%
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:15%
MissRate shared
P1:256KB
P2:256KB
Target Partition
P1:192KB
P2:320KB
Target Partition
Partition granularity: 64KB
Notes: At repartitioning, we evaluate M3. It equalize the increase in miss rate. P1 has no increase while P2 has 3 times increase.
In this case, we increase partition size for P2. We used 64KB partition granularity.

## Slide 44: Dynamic Fair Caching Algorithm
2nd Interval
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:15%
MissRate shared
P1:20%
P2:15%
MissRate shared
P1:20%
P2:10%
MissRate shared
P1:192KB
P2:320KB
Target Partition
Notes: In second interval, new target partition is applied. After the execution, we get new shared miss rate. same 20% and 10%. We have 5% reduction in miss rate.

## Slide 45: Dynamic Fair Caching Algorithm
Repartition!
Evaluate Slowdown
P1: 20% / 20%
P2: 10% / 5%
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:15%
MissRate shared
P1:20%
P2:10%
MissRate shared
P1:192KB
P2:320KB
Target Partition
P1:128KB
P2:384KB
Target Partition
Notes: When we evaluate M3, again P2 requires more cache space. So we increase it.

## Slide 46: Dynamic Fair Caching Algorithm
3rd Interval
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:10%
MissRate shared
P1:128KB
P2:384KB
Target Partition
P1:20%
P2:10%
MissRate shared
P1:25%
P2: 9%
MissRate shared
Notes: After third interval, dynamic profiling get the miss rate for P1 25% and 9% for P2.

## Slide 47: Dynamic Fair Caching Algorithm
Repartition!
Do Rollback if:
P2: Δ<Trollback
Δ=MRold-MRnew
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:10%
MissRate shared
P1:25%
P2: 9%
MissRate shared
P1:128KB
P2:384KB
Target Partition
P1:192KB
P2:320KB
Target Partition
Notes: There is a hidden step of rollback phase.
In this step, we check whether P2’s miss rate is reduced more than rollback threshold.
Because we increased cache partition, we expected to see reduction in miss rate.
In our example, P2 only reduced 1% miss rate which is smaller than rollback threshold.
So, we cancel our previous decision and go back to the previous partition.

## Slide 48: Advantages/Disadvantages of the Approach
Advantages
  + Reduced starvation
  + Better average throughput
  + Block granularity partitioning
Disadvantages and Limitations
  - Alone miss rate estimation can be incorrect
  - Scalable to many cores?
  - Is this the best (or a good) fairness metric?
  - Does this provide performance isolation in cache?

## Slide 49: Software-Based Shared Cache Partitioning

## Slide 50: Software-Based Shared Cache Management
Assume no hardware support (demand based cache sharing, i.e. LRU replacement)
How can the OS best utilize the cache?
Cache sharing aware thread scheduling
  Schedule workloads that “play nicely” together in the cache
    E.g., working sets together fit in the cache
    Requires static/dynamic profiling of application behavior
    Fedorova et al., “Improving Performance Isolation on Chip Multiprocessors via an Operating System Scheduler,” PACT 2007.
Cache sharing aware page coloring
  Dynamically monitor miss rate over an interval and change virtual to physical mapping to minimize miss rate
    Try out different partitions

## Slide 51: OS Based Cache Partitioning
Lin et al., “Gaining Insights into Multi-Core Cache Partitioning: Bridging the Gap between Simulation and Real Systems,” HPCA 2008.
Cho and Jin, “Managing Distributed, Shared L2 Caches through OS-Level Page Allocation,” MICRO 2006.
Static cache partitioning
  Predetermines the amount of cache blocks allocated to each program at the beginning of its execution
  Divides shared cache to multiple regions and partitions cache regions through OS page address mapping
Dynamic cache partitioning
  Adjusts cache quota among processes dynamically
  Page re-coloring
  Dynamically changes processes’ cache usage through OS page address re-mapping

## Slide 52: Page Coloring
Physical memory divided into colors
Colors map to different cache sets
Cache partitioning
  Ensure two threads are allocated
  pages of different colors
Thread A
Thread B
Cache
Way-1
Way-n
…………
Memory page

## Slide 53: Page Coloring
virtual page number
Virtual address
page offset
physical page number
Physical address
Page offset
Address translation
Cache tag
Block offset
Set index
Cache address
Physically indexed cache
page color bits
… …
OS control
=
Physically indexed caches are divided into multiple regions (colors).
All cache lines in a physical page are cached in one of those regions (colors).
OS can control the page color of a virtual page through address mapping
(by selecting a physical page with a specific value in its page color bits).
Notes: Let me introduce page coloring technique first.
1. A virtual address can be divide into two parts: Virtual page number and page offset
(In our experimental system, the page size is 4KB, so length of page offset bits are 12)
2. The virtual address is converted to physical address by address translation controlled by OS.
Virtual page number is mapped to a physical page number and page offset remain same.
3. The physical address is used in a physically indexed cache. The cache address is divided into tag, set index and block offset.
4. The common bits between physical page number and set index are referred as page color bits.
5. The physically indexed cache is then divided into multiple regions. Each OS page will cached in one of those regions. Indexed by the page color.
In a summary, 1) 2)…

## Slide 54: Static Cache Partitioning using Page Coloring
… …
...
……
…
……
…
Physically indexed cache
…
……
……
…
Physical pages are grouped to page bins
according to their page color
1
2
3
4
…
i+2
i
i+1
…
Process 1
1
2
3
4
…
i+2
i
i+1
…
Process 2
OS address mapping
Shared cache is partitioned between two processes through address mapping.
Cost: Main memory space needs to be partitioned, too.
Notes: 1. This slide shows an example how we enhance page coloring to partition shared cache between two processes.
2. Physical pages are grouped into page bins according to their page color. The pages in a same bin will be cached in same cache region or cache color in a physically indexed cache.
3. Suppose there are two processes running on a dual-core processor. Each processor has a set of pages need to be mapped to physical pages.
4. If we limit that pages from one process can only be mapped to a subset of page bins. Then pages from a process will only use part of the cache.
In a summary,
… We call this restriction co-partitioning.

## Slide 55: Dynamic Cache Partitioning via Page Re-Coloring
Allocated color
page color table
……
N - 1
0
1
2
3
Page re-coloring:
  Allocate page in new color
  Copy memory contents
  Free old page
Allocated colors
Pages of a process are organized into linked lists by their colors.
Memory allocation guarantees that pages are evenly distributed into all the lists (colors) to avoid hot points.
Notes: This slides show how we mange the pages and how we design the dynamic cache partitioning.
1. We link all the pages allocated to a process by their page colors. A page links table is added to each working process. And Memory allocation guarantees that pages are evenly distributed into all the cache colors to avoid hot points. 2. Suppose at the beginning of execution, 3 colors was assigned to the process: red, green and yellow. Pages are allocated in a round-robin fashion among those 3 colors.
3. If a policy decide to expand number of colors from 3 to 4, for example, the blue color is allocated to the process
4. one of every 4 pages are selected for migration. And we re-coloring those pages to the new color.
The re-coloring procedure includes three steps:
1. Allocate a physical page in new color
2. Copy memory contents from old page to new page
3. Free old page.
We execute these three steps for all pages that need to be re-colored.

## Slide 56: Dynamic Partitioning in a Dual-Core System
Init: Partition the cache as (8:8)
Run current partition (P0:P1) for one epoch
finished
Try one epoch for each of the two neighboring
partitions: (P0 – 1: P1+1) and (P0 + 1: P1-1)
Choose next partitioning with best policy
metrics measurement (e.g., cache miss rate)
No
Yes
Exit
Notes: Next, I will present a simple dynamic partition policy we used for performance.
1. Initially, half cache capacity is allocated to each program.
2. We then enter the loops of trying to find optimal partitioning regarding a policy metrics M.
3. We first run one period for current partitioning, then try one period for each of the two neighboring partitionings.
4. We choosing best partition for the next epoch based on their policy metrics measurement.
We repeat this loop until the completion of the workload.
This is a simple greedy policy which emulate the policy of a HPCA’02 paper

## Slide 57: Experimental Environment
Dell PowerEdge1950
  Two-way SMP, Intel dual-core Xeon 5160
  Shared 4MB L2 cache, 16-way
  8GB Fully Buffered DIMM
Red Hat Enterprise Linux 4.0
  2.6.20.3 kernel
  Performance counter tools from HP (Pfmon)
  Divide L2 cache into 16 colors
Notes: We conducted our experiment on a two-way SMP machine that has two intel dual-core Xeon processors. Each processor has a 4MB 16-way L2 cache shared by two processor cores. The machine has 4 2GB Fully buffered DIMM as main memory.
We install RHEL 4.0 on the machine and use 2.6 kernel and patched the kernel with hardware Performance counter tools from HP.
And we extend linux kernel to support both static and dynamic cache partitioning. The L2 cache is divided into 16 colors.

## Slide 58: Performance – Static & Dynamic
Aim to minimize combined miss rate
For RG-type, and some RY-type:
  Static partitioning outperforms dynamic partitioning
For RR- and RY-type, and some RY-type
  Dynamic partitioning outperforms static partitioning
Notes: This figures shows the comparison between the performance of best static partitioning and the performance by the dynamic partitioning policies, using combined miss rates as policy metrics.
It is worth noting that we assume full profiling information is available for the static partitioning. Without such profiling information, the dynamic partitioning perform comparable with static partitioning.
If we look into the workload individually, some workloads perform better by static partitioning
while some other workload performance better by dynamic partitioning.

## Slide 59: Software vs. Hardware Cache Management
Software advantages
  + No need to change hardware
  + Easier to upgrade/change algorithm (not burned into hardware)
Disadvantages
  - Large granularity of partitioning (page-based versus way/block)
  - Limited page colors  reduced performance per application (limited physical memory space!), reduced flexibility
  - Changing partition size has high overhead  page mapping changes
  - Adaptivity is slow: hardware can adapt every cycle (possibly)
  - Not enough information exposed to software (e.g., number of misses due to inter-thread conflict)

## Slide 60: Private/Shared Caching

## Slide 61: Private/Shared Caching
Example: Adaptive spill/receive caching
Goal: Achieve the benefits of private caches (low latency, performance isolation) while sharing cache capacity across cores
Idea: Start with a private cache design (for performance isolation), but dynamically steal space from other cores that do not need all their private caches
  Some caches can spill their data to other cores’ caches dynamically
Qureshi, “Adaptive Spill-Receive for Robust High-Performance Caching in CMPs,” HPCA 2009.

## Slide 62: Revisiting Private Caches on CMP
Private caches avoid the need for shared interconnect
++ fast latency, tiled design, performance isolation
Core A
I$
D$
CACHE A
Core B
I$
D$
CACHE B
Core C
I$
D$
CACHE C
Core D
I$
D$
CACHE D
Memory
Problem: When one core needs more cache and other core
has spare cache, private-cache CMPs cannot share capacity

## Slide 63: Cache Line Spilling
Spill evicted line from one cache to neighbor cache
- Co-operative caching (CC) [ Chang+ ISCA’06]
Problem with CC:
Performance depends on the parameter (spill probability)
All caches spill as well as receive  Limited improvement
Cache A
Cache B
Cache C
Cache D
Spill
Goal: Robust High-Performance Capacity Sharing with Negligible Overhead
Chang and Sohi, “Cooperative Caching for Chip Multiprocessors,” ISCA 2006.

## Slide 64: Spill-Receive Architecture
Each Cache is either a Spiller or Receiver but not both
- Lines from spiller cache are spilled to one of the receivers
- Evicted lines from receiver cache are discarded
What is the best N-bit binary string that maximizes the performance of Spill Receive Architecture  Dynamic Spill Receive (DSR)
Cache A
Cache B
Cache C
Cache D
Spill
S/R =1
(Spiller cache)
S/R =0
(Receiver cache)
S/R =1
(Spiller cache)
S/R =0
(Receiver cache)
Qureshi, “Adaptive Spill-Receive for Robust High-Performance Caching in CMPs,” HPCA 2009.

## Slide 65: Efficient Cache Utilization

## Slide 66: Efficient Cache Utilization: Examples
Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2005.
Seshadri et al., “The Evicted-Address Filter: A Unified Mechanism to Address both Cache Pollution and Thrashing,” PACT 2012.
Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.

## Slide 67: Cache Utilization is Important
Core
Last-Level Cache
Memory
Core
Core
Core
Core
Increasing contention
Effective cache utilization is important
Large latency
Notes: All high-performance processors employ on-chip caches.
In most modern systems, multiple cores share the last-level cache.
With the large latency of main memory access and increasing contention between multiple cores, effective cache utilization is critical for system performance.
For effective cache utilization, the cache should be filled with blocks that are likely to be reused.

## Slide 68: Reuse Behavior of Cache Blocks
A
B
C
A
B
C
S
T
U
V
W
X
Y
A
B
C
Different blocks have different reuse behavior
Access Sequence:
High-reuse block
Low-reuse block
Z
Ideal Cache
A
B
C
.
.
.
.
.
Notes: However, different blocks have different reuse behaviors.
For example, consider the following access sequence.
Blocks A, B and C are accessed repeatedly.
We refer to such blocks as High reuse blocks.
On the other hand, the remaining blocks are not reused. We refer to such blocks as low-reuse blocks.
Ideally, the cache should be filled with high-reuse blocks such as A, B and C.
But traditional cache management policies such as LRU suffer from two problems.

## Slide 69: Cache Pollution
H
G
F
E
D
C
B
A
S
H
G
F
E
D
C
B
T
S
H
G
F
E
D
C
U
T
S
H
G
F
E
D
MRU
LRU
LRU Policy
Idea: Predict reuse behavior of missed blocks. Insert low-reuse blocks at LRU position.
H
G
F
E
D
C
B
A
S
T
U
MRU
LRU
A
B
A
C
B
A
A
S
A
T
S
A
Cache
Problem: Low-reuse blocks evict high-reuse blocks
Notes: The first problem, referred to as cache pollution, is one where blocks with low-reuse evict blocks with high-reuse from the cache.
Consider the following example of a cache following the LRU policy. Although the cache is filled with high–reuse blocks, the LRU policy inserts even blocks with low-reuse at the MRU position, evicting more useful blocks from the cache. So the future accesses to blocks A, B and C will miss in the cache.
To address this problem, prior work proposed the idea of predicting the reuse behavior of missed cache blocks and inserting low-reuse blocks at the LRU position. This mitigates the impact of pollution as shown in the example.

## Slide 70: Cache Thrashing
H
G
F
E
D
C
B
A
I
H
G
F
E
D
C
B
J
I
H
G
F
E
D
C
K
J
I
H
G
F
E
D
MRU
LRU
LRU Policy
A
B
C
D
E
F
G
H
I
J
K
A
B
A
C
B
A
Idea: Insert at MRU position with a very low probability (Bimodal insertion policy)
Cache
H
G
F
E
D
C
B
A
I
J
K
MRU
LRU
A
I
A
J
I
A
A fraction of working set stays in cache
Cache
Problem: High-reuse blocks evict each other
Qureshi+, “Adaptive insertion policies for high performance caching,” ISCA 2007.
Notes: The second problem, referred to as thrashing, occurs when the number of high-reuse blocks is more than what the cache can handle, as shown in the example.
In this case, the LRU policy leads to these high-reuse blocks evicting each other from the cache, leading to zero cache hits.
Prior work proposed to achieve this using the bimodal insertion policy, which inserts blocks at the MRU position with a very low probability.
As a result, majority of the blocks are inserted at the LRU position.
For a thrashing working set, this results in a fraction of the working set to be retained in the cache, leading to cache hits for at least that fraction.

## Slide 71: Handling Pollution and Thrashing
Need to address both pollution and thrashing concurrently
Cache Thrashing
Need to control the number of blocks inserted with high priority into the cache
Cache Pollution
Need to distinguish high-reuse blocks from low-reuse blocks
Notes: The motivation behind this work is that prior works do not address both pollution and thrashing concurrently.
Prior works on pollution do not have control over the number of high-reuse blocks. As a result, if there are more high-reuse blocks than what the cache can handle, these approaches can suffer from thrashing.
On the other hand, prior works on cache thrashing have no mechanism to distinguish high-reuse blocks from low-reuse blocks. As a result, when a working set is not thrashing, these approaches can suffer from pollution.
Our goal in this work is to design a mechanism to address both cache pollution and thrashing. In this talk, I will present our mechanism, the Evicted-address filter, that achieves our goal.

## Slide 72: Reuse Prediction
Miss
Missed-block
High reuse
Low reuse
?
Keep track of the reuse behavior of every cache block in the system
Impractical
High storage overhead
Look-up latency
Notes: The reuse prediction problem asks the following question. On a cache miss, does the missed cache block have high reuse or low reuse?
One possible way to answer this question is to keep track of the reuse behavior of every block in the system.
But such an approach is impractical due to its high storage overhead and look-up latency.
So, how do prior works address this problem?

## Slide 73: Approaches to Reuse Prediction
Use program counter or memory region information.
B
A
T
S
PC 1
PC 2
B
A
T
S
PC 1
PC 2
PC 1
PC 2
C
C
U
U
1. Group Blocks
2. Learn group behavior
3. Predict reuse
Same group → same reuse behavior
No control over number of high-reuse blocks
Notes: Previous approaches proposed to predict the reuse behavior of missed blocks indirectly using program-counter or memory-region information. At a high level, the program-counter based mechanism operates in three steps.
First, the mechanism groups blocks based on the program counter that caused their cache miss.
Second, the mechanism learns the reuse behavior of each group based on the blocks that were previously accessed by the program counter.
Third, the learned behavior of each group is used to predict the reuse behavior of future blocks accessed by the corresponding program counter.
Such an approach has two shortcomings.
First, blocks belonging to the same program counter may not have the same reuse behavior.
Second, the mechanism has no control over the number of blocks predicted to have high reuse. As a result, this approach can potentially suffer from thrashing.

## Slide 74: Per-block Reuse Prediction
Use recency of eviction to predict reuse
A
Time
Time of eviction
A
Accessed soon after eviction
S
Time
S
Accessed long time after eviction
Notes: In this work, we propose a mechanism to predict the reuse behavior of a block based on its own past behavior.
The key idea behind our mechanism is to use the recency of eviction of a block to predict its reuse on its next access.
More specifically, if a block is accessed soon after getting evicted, our mechanism concludes that the block was prematurely evicted and predicts it to have high reuse.
On the other hand, if a block is accessed a long time after eviction, our mechanism concludes that the block is unlikely to be accessed in the near future and predicts it to have low reuse.
The above idea suggests that it is sufficient to keep track of a small number of recently evicted blocks to distinguish between high-reuse blocks and low-reuse blocks.

## Slide 75: Evicted-Address Filter (EAF)
Cache
EAF
(Addresses of recently evicted blocks)
Evicted-block address
Miss
Missed-block address
In EAF?
Yes
No
MRU
LRU
High Reuse
Low Reuse
Notes: Based on this observation, our mechanism augments the cache with a structure called the Evicted-address filter that keeps track of addresses of recently evicted blocks.
When a block is evicted from the cache, our mechanism inserts its address into the EAF.
On a cache miss, if the missed block address is present in the EAF, then the block was evicted recently. Therefore, our mechanism predicts that the block has high reuse and inserts it at the MRU position. It also removes the block address from the EAF to create space for more evicted addresses.
On the other hand, if the missed block address is not present in the EAF, there is one of two possibilities: either the block was accessed before and evicted a long time ago or the block is accessed for the first time. In both cases, our mechanism predicts that the block has low reuse and inserts it at the LRU position.
Although the EAF is a simple mechanism to predict the reuse behavior of missed blocks, one natural question is how to implement it in hardware?

## Slide 76: Naïve Implementation: Full Address Tags
EAF
1. Large storage overhead
2. Associative lookups – High energy
Recently evicted address
Need not be 100% accurate
?
Notes: A naïve implementation of the EAF would be to implement it as a tag store where each tag entry corresponds to the address or a recently evicted block.
However, such an implementation suffers from two problems: 1) it has a large storage overhead and 2) it requires associative lookups which consume high energy.
But notice that the EAF need not be 100% accurate as it is just a prediction structure. This raises the possibility of implementing EAF using a more compact structure which doesn’t have the two shortcomings. So, we consider implementing the EAF using a Bloom filter.

## Slide 77: Low-Cost Implementation: Bloom Filter
EAF
Implement EAF using a Bloom Filter
Low storage overhead + energy
Need not be 100% accurate
?
Notes: A naïve implementation of the EAF would be to implement it as a tag store where each tag entry corresponds to the address or a recently evicted block.
However, such an implementation suffers from two problems: 1) it has a large storage overhead and 2) it requires associative lookups which consume high energy.
But notice that the EAF need not be 100% accurate as it is just a prediction structure. This raises the possibility of implementing EAF using a more compact structure which doesn’t have the two shortcomings. So, we consider implementing the EAF using a Bloom filter.

## Slide 78: Bloom Filter
Y
Compact representation of a set
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1. Bit vector
2. Set of hash functions
H1
H2
H1
H2
X
1
1
1
Insert
Test
Z
W
Remove
X
Y
May remove multiple addresses
Clear


False positive
Inserted Elements:
X
Y
Notes: Let me give you a quick overview of a Bloom filter. A Bloom filter is a compact representation of a set, in this case, a set of addresses.
It consists of a bit vector and a set of hash functions.
All the bits in the bit-vector are initialized to zero.
To insert an address X into the set, the Bloom filter computes the values of the two hash functions and sets the corresponding elements in the filter.
To insert another address Y, the Bloom filter repeats the process.
To test if an address is present in the filter, the Bloom filter computes the values of the hash functions and checks if all the corresponding bits are set. If yes, the Bloom filter concludes that the address is present in the set. This is the case for the address X.
However, even if one of the bits is not set, the Bloom filter concludes that the address is not present in the set.
When we test for the address W, the Bloom filter will conclude that W is present in the set. But W was never inserted. The left bit was set due to the insertion of X and the right bit was set due to the insertion of Y. This situation is referred to as a false positive. The false positive rate of a Bloom filter can be made low by controlling the parameters of the Bloom filter.
Since multiple addresses can map to the same bits, a Bloom filter does not support removing individual addresses from the set.
However, all the addresses can be cleared from the set by simply resetting all the bits in the Bloom filter.
Now, let us look at how we can implement EAF using a Bloom filter.

## Slide 79: EAF using a Bloom Filter
EAF
Insert
Test
Evicted-block address
Remove
FIFO address
Missed-block address
Bloom Filter
Remove
If present
when full
Clear




1
2
when full
Bloom-filter EAF: 4x reduction in storage overhead, 1.47% compared to cache size
Notes: Let us quickly revisit the operations performed on the EAF.
First, on a cache eviction, the evicted block address is inserted into the EAF.
Second, on a cahce miss, our mechanism tests if the missed block address is present in the EAF. If yes, the address is also removed from the EAF.
Finally, when the EAF is full, an address is removed in a FIFO manner to create space for more recently evicted addresses.
A Bloom filter based implementation of EAF will support the insert and the test operations.
However, as we saw in the previous slide, the Bloom filter does not support the remove operations. So we need to somehow eliminate these remove operations. For this purpose, we propose two changes to the EAF design.
First, on a cache miss, if the missed block address is present in the EAF, we choose to retain the block address in the EAF instead of removing it.
Second, when the EAF becomes full, we propose to clear the EAF completely instead of removing an address in a FIFO manner.
With these changes, we can implement the EAF using a Bloom filter.
Doing so can reduce the storage overhead of EAF by 4x, to around 1.47% compared to the cache size.

## Slide 80: EAF-Cache: Final Design
Cache
Bloom Filter
Counter
1
2
3
Cache eviction
Cache miss
Counter reaches max
Insert address into filter
Increment counter
Test if address is present in filter
Yes, insert at MRU. No, insert with BIP
Clear filter and counter
Notes: Lets take a look at the final design of our mechanism, the EAF-cache.
It augments the cache with a Bloom filter and a counter that keeps track of the number of addresses inserted into the Bloom filter.
On a cache eviction, the evicted address is inserted into the filter and the counter is incremented.
On a cache miss, if the missed block address is present in the Bloom filter, the block is inserted at the MRU position. Otherwise it is inserted with the bimodal insertion policy.
Finally, when the counter reaches a maximum, both the filter and the counter are cleared.

## Slide 81: EAF: Advantages
Cache
Bloom Filter
Counter
1. Simple to implement
2. Easy to design and verify
3. Works with other techniques (replacement policy)
Cache eviction
Cache miss
Notes: Apart from its ability to mitigate both pollution and thrashing, EAF has three other advantages.
First, it adds only a Bloom filter and a counter. Hardware implementations of the Bloom filter are well studied. So, EAF-cache is simple to implement.
Second, both the Bloom filter and the counter are outside the cache. As a result, our mechanism is easy to design and verify on top of existing cache implementations.
Finally, all operations on the EAF happen on a cache miss. As a result, EAF can work well with other techniques that monitor cache hits to improve performance, for example, the cache replacement policy.

## Slide 82: EAF Performance – Summary
Chart: Performance Improvement over LRU
| 1-Core | 2-Core | 4-Core
TA-DIP | 0.01 | 0.04 | 0.02
TA-DRRIP | 0.05 | 0.08 | 0.11
RTB | 0.01 | 0.06 | 0.07
MCT | 0.01 | 0.1 | 0.06
SHIP | 0.04 | 0.1 | 0.13
EAF | 0.05 | 0.15 | 0.21
D-EAF | 0.07 | 0.15 | 0.205
Notes: This slide presents the summary of our performance results for systems with different number of cores.
As shown, our mechanisms outperform all prior approaches for all the three systems. Also, the multicore results are significantly better than the single core results. This is because, in a multicore system, pollution or thrashing caused by an application will affect useful blocks of other concurrently running applications.
SAY THAT LAST TWO BARS ARE EAF AND D-EAF

## Slide 83: Cache Compression

## Slide 84: Motivation for Cache Compression
Significant redundancy in data:
0x00000000
How can we exploit this redundancy?
  Cache compression helps
  Provides effect of a larger cache without making it physically larger
0x0000000B
0x00000003
0x00000004
…

## Slide 85: Background on Cache Compression
Key requirements:
  Fast (low decompression latency)
  Simple (avoid complex hardware changes)
  Effective (good compression ratio)
CPU
L2 Cache
Uncompressed
Compressed
Decompression
Uncompressed
L1 Cache
Hit

## Slide 86: Summary of Major Works
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 

## Slide 87: Summary of Major Works
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 

## Slide 88: Summary of Major Works
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 
Frequent Pattern |  | / | 

## Slide 89: Summary of Major Works
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 
Frequent Pattern |  | / | 
BΔI |  |  | 

## Slide 90: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region

## Slide 91: How Common Are These Patterns?
Chart: Cache Coverage (%)
| libquantum | lbm | mcf | tpch17 | sjeng | omnetpp | tpch2 | sphinx3 | xalancbmk | bzip2 | tpch6 | leslie3d | apache | gromacs | astar | gobmk | soplex | gcc | hmmer | wrf | h264ref | zeusmp | cactusADM | GemsFDTD | Average
Zero | 1.2e-05 | 7e-06 | 0.008911 | 0.033323 | 0.032362 | 2.7e-05 | 0.065765 | 0.022031 | 0.000272 | 0.000176 | 0.12314 | 0.16955 | 0.072498 | 0.065675 | 0.016314 | 0.34373 | 0.26863 | 0.30068 | 0.003261 | 0.81434 | 0.00837 | 0.83736 | 0.66632 | 0.99428 | 0.20196
Repeated Values | 0.0001 | 6.5e-05 | 0.0001 | 0.000508 | 0.000146 | 0.0001 | 0.000529 | 0.008812 | 2e-06 | 0.036901 | 0.002005 | 0.095993 | 0.005072 | 0.010873 | 0.005914 | 0.020917 | 0.29969 | 0.038812 | 0.031345 | 0.083856 | 0.006414 | 0.13684 | 0.32178 | 0.001628 | 0.046184
Other Patterns | 0.000177 | 0.000138 | 0.060209 | 0.045394 | 0.070763 | 0.11701 | 0.075432 | 0.1168 | 0.21336 | 0.18863 | 0.12998 | 0.016265 | 0.23912 | 0.24082 | 0.42076 | 0.086109 | 0.18536 | 0.45647 | 0.84697 | 0.017818 | 0.91843 | 0.000306 | 0.000699 | 0.000345 | 0.18531
SPEC2006, databases, web workloads, 2MB L2 cache
“Other Patterns” include Narrow Values
  43% of the cache lines belong to key patterns

## Slide 92: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region
  Low Dynamic Range:
  Differences between values are significantly smaller than the values themselves

## Slide 93: Key Idea: Base+Delta (B+Δ) Encoding
32-byte Uncompressed Cache Line
0xC04039C0
0xC04039C8
0xC04039D0
…
0xC04039F8
4 bytes
0xC04039C0
Base
0x00
1 byte
0x08
1 byte
0x10
1 byte
…
0x38
12-byte
Compressed Cache Line
  20 bytes saved
   Fast Decompression: vector addition
   Simple Hardware:
  arithmetic and comparison
   Effective: good compression ratio

## Slide 94: Can We Do Better?
Uncompressible cache line (with a single base):
Key idea:
Use more bases, e.g., two instead of one
Pro:
  More cache lines can be compressed
Cons:
  Unclear how to find these bases efficiently
  Higher overhead (due to additional bases)
0x00000000
0x09A40178
0x0000000B
0x09A4A838
…

## Slide 95: B+Δ with Multiple Arbitrary Bases
Chart: Compression Ratio
| GeoMean
1 | 1.3961
2 | 1.5113
3 | 1.4982
4 | 1.4326
8 | 1.3118
10 | 1.2742
16 | 1.2242
   2 bases – the best option based on evaluations

## Slide 96: How to Find Two Bases Efficiently?
  First base - first element in the cache line
  Second base - implicit base of 0
Advantages over 2 arbitrary bases:
  Better compression ratio
  Simpler compression logic
   Base+Delta part
   Immediate part
  Base-Delta-Immediate (BΔI) Compression

## Slide 97: B+Δ (with two arbitrary bases) vs. BΔI
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
B+Δ (2 bases) | 1.0625 | 1.0125 | 1.0254 | 1.1979 | 1.1332 | 1.375 | 1.7477 | 1.5346 | 1.3347 | 1.2446 | 1.5238 | 1.447 | 1.2608 | 1.4753 | 1.7447 | 1.3954 | 1.9793 | 1.7868 | 1.9739 | 1.9919 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5113
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
  Average compression ratio is close, but BΔI is simpler

## Slide 98: BΔI Cache Compression Implementation
Decompressor Design
  Low latency
Compressor Design
  Low cost and complexity
BΔI Cache Organization
  Modest complexity

## Slide 99: BΔI Decompressor Design
Δ0
B0
Δ1
Δ2
Δ3
Compressed Cache Line
V0
V1
V2
V3
+
+
Uncompressed Cache Line
+
+
B0
Δ0
B0
B0
B0
B0
Δ1
Δ2
Δ3
V0
V1
V2
V3
  Vector addition

## Slide 100: BΔI Compressor Design
32-byte Uncompressed Cache Line
8-byte B0
1-byte Δ
CU
8-byte B0
2-byte Δ
CU
8-byte B0
4-byte Δ
CU
4-byte B0
1-byte Δ
CU
4-byte B0
2-byte Δ
CU
2-byte B0
1-byte Δ
CU
Zero
CU
Rep.
Values
CU
Compression Selection Logic (based on compr. size)
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
Compression Flag & Compressed Cache Line
CFlag &
CCL
Compressed Cache Line

## Slide 101: BΔI Compression Unit: 8-byte B0 1-byte Δ
32-byte Uncompressed Cache Line
V0
V1
V2
V3
8 bytes
-
-
-
-
B0=
V0
V0
B0
B0
B0
B0
V0
V1
V2
V3
Δ0
Δ1
Δ2
Δ3
Within 1-byte range?
Within 1-byte range?
Within 1-byte range?
Within 1-byte range?
Is every element within 1-byte range?
Δ0
B0
Δ1
Δ2
Δ3
B0
Δ0
Δ1
Δ2
Δ3
Yes
No

## Slide 102: BΔI Cache Organization
Tag0
Tag1
…
…
…
…
Tag Storage:
Set0
Set1
Way0
Way1
Data0
…
…
Set0
Set1
Way0
Way1
…
Data1
…
32 bytes
Data Storage:
Conventional 2-way cache with 32-byte cache lines
BΔI: 4-way cache with 8-byte segmented data
Tag0
Tag1
…
…
…
…
Tag Storage:
Way0
Way1
Way2
Way3
…
…
Tag2
Tag3
…
…
Set0
Set1
Twice as many tags
C - Compr. encoding bits
C
Set0
Set1
…
…
…
…
…
…
…
…
S0
S0
S1
S2
S3
S4
S5
S6
S7
…
…
…
…
…
…
…
…
8 bytes
Tags map to multiple adjacent segments
2.3% overhead for 2 MB cache

## Slide 103: Qualitative Comparison with Prior Work
Zero-based designs
  ZCA [Dusser+, ICS’09]: zero-content augmented cache
  ZVC [Islam+, PACT’09]: zero-value cancelling
  Limited applicability (only zero values)
FVC [Yang+, MICRO’00]: frequent value compression
  High decompression latency and complexity
Pattern-based compression designs
  FPC [Alameldeen+, ISCA’04]: frequent pattern compression
    High decompression latency (5 cycles) and complexity
  C-pack [Chen+, T-VLSI Systems’10]: practical implementation of FPC-like algorithm
    High decompression latency (8 cycles)

## Slide 104: Cache Compression Ratios
BΔI achieves the highest compression ratio
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
ZCA | 1 | 1.0125 | 1.0002 | 1.0055 | 1.0288 | 1 | 1.1561 | 1.0914 | 1.0241 | 1 | 1.0005 | 1.1898 | 1 | 1.1083 | 1.0549 | 1 | 1.0013 | 1.2794 | 1.9738 | 1.5235 | 1.5406 | 1.801 | 1.9951 | 1.9966 | 1.2005
FVC | 1.0297 | 1.0125 | 1.0012 | 1.017 | 1.1457 | 1.4988 | 1.1857 | 1.1438 | 1.4157 | 1.3573 | 1.0143 | 1.4596 | 1.3574 | 1.3745 | 1.1968 | 1.3874 | 1.9381 | 1.7894 | 1.9738 | 1.9859 | 1.9598 | 1.9947 | 1.995 | 1.9966 | 1.4212
FPC | 1.004 | 1.0125 | 1.0225 | 1.0568 | 1.2307 | 1.3121 | 1.1774 | 1.4064 | 1.4705 | 1.5235 | 1.5442 | 1.5994 | 1.5763 | 1.7269 | 1.2651 | 1.6749 | 1.9072 | 1.9167 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5149
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
1.53
SPEC2006, databases, web workloads, 2MB L2

## Slide 105: Single-Core: IPC and MPKI
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 1.0859 | 1.1498 | 1.1819 | 1.2753 | 1.3788
BΔI | 1.0817 | 1.1425 | 1.2085 | 1.2401 | 1.346 | 1.4285
8.1%
5.2%
5.1%
4.9%
5.6%
3.6%
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 0.819 | 0.59143 | 0.46593 | 0.37544 | 0.27527
BΔI | 0.84292 | 0.62368 | 0.466 | 0.40552 | 0.30364 | 0.23666
16%
24%
21%
13%
19%
14%
BΔI achieves the performance of a 2X-size cache
Performance improves due to the decrease in MPKI

## Slide 106: Multi-Core Workloads
Application classification based on
  Compressibility: effective cache size increase
  (Low Compr. (LC) < 1.40, High Compr. (HC) >= 1.40)
  Sensitivity: performance gain with more cache
  (Low Sens. (LS) < 1.10, High Sens. (HS) >= 1.10; 512kB -> 2MB)
Three classes of applications:
  LCLS, HCLS, HCHS, no LCHS applications
For 2-core - random mixes of each possible class pairs (20 each, 120 total workloads)

## Slide 107: Multi-Core: Weighted Speedup
BΔI performance improvement is the highest (9.5%)
Chart: Normalized Weighted Speedup
| LCLS - LCLS | LCLS - HCLS | HCLS - HCLS | LCLS - HCHS | HCLS - HCHS | HCHS - HCHS | Low Sensitivity | High Sensitivity | GeoMean
ZCA | 1.0268 | 1.0154 | 1.0259 | 1.0182 | 1.1193 | 1.01 | 1.0353
FVC | 1.0277 | 1.0179 | 1.0345 | 1.0727 | 1.1468 | 1.08 | 1.0624
FPC | 1.0312 | 1.0197 | 1.0276 | 1.1 | 1.1495 | 1.176 | 1.0822
BΔI | 1.0446 | 1.0342 | 1.0431 | 1.1091 | 1.1651 | 1.18 | 1.0944
If at least one application is sensitive, then the performance improves

## Slide 108: Readings for Lecture 15 (Next Monday)
Required Reading Assignment:
  Mutlu and Moscibroda, “Parallelism-Aware Batch Scheduling: Enhancing both Performance and Fairness of Shared DRAM Systems,” ISCA 2008.
Recommended References:
  Muralidhara et al., “Reducing Memory Interference in Multicore Systems via Application-Aware Memory Channel Partitioning,” MICRO 2011.
  Ebrahimi et al., “Parallel Application Memory Scheduling,” MICRO 2011.
  Wang et al., “A-DRM: Architecture-aware Distributed Resource Management of Virtualized Clusters,” VEE 2015.

## Slide 109: Guest Lecture on Wednesday (10/28)
Bryan Black, AMD
  3D die stacking technology

## Slide 110: 18-740/640 Computer Architecture Lecture 14: Memory Resource Management I
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015, 10/26/2015