## Slide 1: 18-740/640 Computer Architecture Lecture 16: Interconnection Networks
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015, 11/4/2015

## Slide 2: Required Readings
Required Reading Assignment:
  Dubois, Annavaram, Stenstrom, Chapter 6.
Recommended References:
  Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.
  Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.

## Slide 3: Interconnection Network Basics

## Slide 4: Where Is Interconnect Used?
To connect components
Many examples
  Processors and processors
  Processors and memories (banks)
  Processors and caches (banks)
  Caches and caches
  I/O devices
Interconnection network

## Slide 5: Why Is It Important?
Affects the scalability of the system
  How large of a system can you build?
  How easily can you add more processors?
Affects performance and energy efficiency
  How fast can processors, caches, and memory communicate?
  How long are the latencies to memory?
  How much energy is spent on communication?

## Slide 6: Interconnection Network Basics
Topology
  Specifies the way switches are wired
  Affects routing, reliability, throughput, latency, building ease
Routing (algorithm)
  How does a message get from source to destination
  Static or adaptive
Buffering and Flow Control
  What do we store within the network?
    Entire packets, parts of packets, etc?
  How do we throttle during oversubscription?
  Tightly coupled with routing strategy

## Slide 7: Terminology
Network interface
  Module that connects endpoints (e.g. processors) to network
  Decouples computation/communication
Link
  Bundle of wires that carry a signal
Switch/router
  Connects fixed number of input channels to fixed number of output channels
Channel
  A single logical connection between routers/switches

## Slide 8: More Terminology
Node
  A router/switch within a network
Message
  Unit of transfer for network’s clients (processors, memory)
Packet
  Unit of transfer for network
Flit
  Flow control digit
  Unit of flow control within network

## Slide 9: Some More Terminology
  Direct or Indirect Networks
  Endpoints sit “inside” (direct) or “outside” (indirect) the network
  E.g. mesh is direct; every node is both endpoint and switch
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
Router (switch), Radix of 2 (2 inputs, 2 outputs)
Abbreviation: Radix-ary
These routers are 2-ary
Indirect
Direct
Notes: What type of network is the one on the right

## Slide 10: Interconnection Network Topology

## Slide 11: Properties of a Topology/Network
Regular or Irregular
  Regular if topology is regular graph (e.g. ring, mesh).
Routing Distance
  number of links/hops along a route
Diameter
  maximum routing distance within the network
Average Distance
  Average number of hops across all valid routes
Notes: Example of irregular network? Internet

## Slide 12: Properties of a Topology/Network
Bisection Bandwidth
  Often used to describe network performance
  Cut network in half and sum bandwidth of links severed
    (Min # channels spanning two halves) * (BW of each channel)
  Meaningful only for recursive topologies
  Can be misleading, because does not account for switch and routing efficiency (and certainly not execution time)
Blocking vs. Non-Blocking
  If connecting any permutation of sources & destinations is possible, network is non-blocking; otherwise network is blocking.
  Rearrangeable non-blocking: Same as non-blocking but might require rearranging connections when switching from one permutation to another.

## Slide 13: Topology
Bus (simplest)
Point-to-point connections (ideal and most costly)
Crossbar (less costly)
Ring
Tree
Omega
Hypercube
Mesh
Torus
Butterfly
…

## Slide 14: Metrics to Evaluate Interconnect Topology
Cost
Latency (in hops, in nanoseconds)
Contention
Many others exist you should think about
  Energy
  Bandwidth
  Overall system performance

## Slide 15: Bus
All nodes connected to a single link
+ Simple + Cost effective for a small number of nodes
+ Easy to implement coherence (snooping and serialization)
- Not scalable to large number of nodes (limited bandwidth, electrical loading  reduced frequency)
- High contention  fast saturation
0
1
2
3
4
5
6
7

## Slide 16: Point-to-Point
Every node connected to every other
with direct/isolated links
+ Lowest contention
+ Potentially lowest latency
+ Ideal, if cost is no issue
-- Highest cost
O(N) connections/ports
per node
O(N2) links
-- Not scalable
-- How to lay out on chip?
0
1
2
3
4
5
6
7

## Slide 17: Crossbar
Every node connected to every other with a shared link for each destination
Enables concurrent transfers to non-conflicting destinations
Could be cost-effective for small number of nodes
+ Low latency and high throughput
- Expensive
- Not scalable  O(N2) cost
- Difficult to arbitrate as N increases
Used in core-to-cache-bank
networks in
- IBM POWER5
- Sun Niagara I/II
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 18: Another Crossbar Design
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 19: Sun UltraSPARC T2 Core-to-Cache Crossbar
High bandwidth interface between 8 cores and 8 L2 banks & NCU
4-stage pipeline: req, arbitration, selection, transmission
2-deep queue for each src/dest pair to hold data transfer request

## Slide 20: Bufferless and Buffered Crossbars
Output
Arbiter
Output
Arbiter
Output
Arbiter
Output
Arbiter
Flow
Control
Flow
Control
Flow
Control
Flow
Control
NI
NI
NI
NI
Buffered
Crossbar
0
1
2
3
NI
NI
NI
NI
Bufferless
Crossbar
0
1
2
3
+ Simpler arbitration/ scheduling
+ Efficient support for variable-size packets
- Requires N2 buffers

## Slide 21: Can We Get Lower Cost than A Crossbar?
Yet still have low contention compared to a bus?
Idea: Multistage networks

## Slide 22: Multistage Logarithmic Networks
Idea: Indirect networks with multiple layers of switches between terminals/nodes
Cost: O(NlogN), Latency: O(logN)
Many variations (Omega, Butterfly, Benes, Banyan, …)
Omega Network:
conflict
Blocking
or
Non-blocking?

## Slide 23: Multistage Networks (Circuit Switched)
A multistage network has more restrictions on feasible concurrent Tx-Rx pairs vs a crossbar
But more scalable than crossbar in cost, e.g., O(N logN) for Butterfly
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 crossbar

## Slide 24: Multistage Networks (Packet Switched)
Packets “hop” from router to router, pending availability of the next-required switch and buffer
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 router

## Slide 25: Aside: Circuit vs. Packet Switching
Circuit switching sets up full path before transmission
  Establish route then send data
  Noone else can use those links while “circuit” is set
  + faster arbitration
  + no buffering
  -- setting up and bringing down “path” takes time
Packet switching routes per packet in each router
  Route each packet individually (possibly via different paths)
  If link is free, any packet can use it
  -- potentially slower --- must dynamically switch
  -- need buffering
  + no setup, bring down time
  + more flexible, does not underutilize links

## Slide 26: Switching vs. Topology
Circuit/packet switching choice independent of topology
It is a higher-level protocol on how a message gets sent to a destination
However, some topologies are more amenable to circuit vs. packet switching

## Slide 27: Another Example: Delta Network
Single path from source to destination
Each stage has different routers
Proposed to replace costly crossbars as processor-memory interconnect
Janak H. Patel,“Processor-Memory Interconnections for Multiprocessors,” ISCA 1979.
8x8 Delta network

## Slide 28: Another Example: Omega Network
Single path from source to destination
All stages are the same
Used in NYU Ultracomputer
Gottlieb et al. “The NYU Ultracomputer - Designing an MIMD Shared Memory Parallel Computer,” IEEE Trans. On Comp., 1983.

## Slide 29: Combining Operations in the Network
Idea: Combine multiple operations on a shared memory location
Example: Omega network switches combine fetch-and-add operations in NYU Ultracomputer
Fetch-and-add(M, I): return M, replace M with M+I
  Common when parallel processors modify a shared variable, e.g. obtain a chunk of the array
Combining reduces synchronization latency

## Slide 30: Butterfly
Equivalent to Omega Network
Indirect
Used in BBN Butterfly
Conflicts can cause “tree saturation”
  Randomization of route selection helps
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14

## Slide 31: Review: Topologies
Direct
Topology
Crossbar
Mesh
Indirect
Direct/Indirect
Blocking/ Non-blocking
2
1
0
3
2
1
0
3
1
0
3
2
5
4
7
6
1
0
3
2
5
4
7
6
Non-blocking
Blocking
Blocking
Multistage Logarith.
Indirect
Cost
Latency
O(N2)
O(NlogN)
O(N)
O(sqrt(N))
O(1)
O(logN)

## Slide 32: Ring
Each node connected to exactly two other nodes. Nodes form a continuous pathway such that packets can reach any node.
+ Cheap: O(N) cost
- High latency: O(N)
- Not easy to scale
- Bisection bandwidth remains constant
Used in Intel Haswell,
Intel Larrabee, IBM Cell,
many commercial systems today
Notes: KSR machine, Hector

## Slide 33: Unidirectional Ring
Single directional pathway
Simple topology and implementation
  Reasonable performance if N and performance needs (bandwidth & latency) still moderately low
  O(N) cost
  N/2 average hops; latency depends on utilization
R
0
R
1
R
N-2
R
N-1
2
2x2 router

## Slide 34: Bidirectional Rings
Multi-directional pathways, or multiple rings
+ Reduces latency
+ Improves scalability
- Slightly more complex injection policy (need to select which ring to inject a packet into)

## Slide 35: Hierarchical Rings
+ More scalable
+ Lower latency
- More complex

## Slide 36: More on Hierarchical Rings
Ausavarungnirun et al., “Design and Evaluation of Hierarchical Rings with Deflection Routing,” SBAC-PAD 2014.
  http://users.ece.cmu.edu/~omutlu/pub/hierarchical-rings-with-deflection_sbacpad14.pdf
Discusses the design and implementation of a mostly-bufferless hierarchical ring

## Slide 37: Mesh
Each node connected to 4 neighbors (N, E, S, W)
O(N) cost
Average latency: O(sqrt(N))
Easy to layout on-chip: regular and equal-length links
Path diversity: many ways to get from one node to another
Used in Tilera 100-core
And many on-chip network
prototypes
Notes: e.g. Tile64

## Slide 38: Torus
Mesh is not symmetric on edges: performance very sensitive to placement of task on edge vs. middle
Torus avoids this problem
+ Higher path diversity (and bisection bandwidth) than mesh
- Higher cost
- Harder to lay out on-chip
- Unequal link lengths

## Slide 39: Torus, continued
Weave nodes to make inter-node latencies ~constant

## Slide 40: Trees
Planar, hierarchical topology
Latency: O(logN)
Good for local traffic
+ Cheap: O(N) cost
+ Easy to Layout
- Root can become a bottleneck
Fat trees avoid this problem (CM-5)
Fat Tree

## Slide 41: CM-5 Fat Tree
Fat tree based on 4x2 switches
Randomized routing on the way up
Combining, multicast, reduction operators supported in hardware
  Thinking Machines Corp., “The Connection Machine CM-5 Technical Summary,” Jan. 1992.

## Slide 42: Hypercube
“N-dimensional cube” or “N-cube”
Latency: O(logN)
Radix: O(logN)
#links: O(NlogN)
+ Low latency
- Hard to lay out in 2D/3D
0000
0101
0100
0001
0011
0010
0110
0111
1000
1101
1100
1001
1011
1010
1110
1111
Notes: Popular in early message-passing computers (e.g., intel iPSC, NCUBE)

## Slide 43: Caltech Cosmic Cube
64-node message passing machine
Seitz, “The Cosmic Cube,” CACM 1985.

## Slide 44: Routing

## Slide 45: Routing Mechanism
Arithmetic
  Simple arithmetic to determine route in regular topologies
  Dimension order routing in meshes/tori
Source Based
  Source specifies output port for each switch in route
  + Simple switches
    no control state: strip output port off header
  - Large header
Table Lookup Based
  Index into table for output port
  + Small header
  - More complex switches
Notes: Any advantages of Table Lookup Based? Easier to support fault tolerance. E.g. can bypass faulty links

## Slide 46: Routing Algorithm
Three Types
  Deterministic: always chooses the same path for a communicating source-destination pair
  Oblivious: chooses different paths, without considering network state
  Adaptive: can choose different paths, adapting to the state of the network
How to adapt
  Local/global feedback
  Minimal or non-minimal paths

## Slide 47: Deterministic Routing
All packets between the same (source, dest) pair take the same path
Dimension-order routing
  First traverse dimension X, then traverse dimension Y
  E.g., XY routing (used in Cray T3D, and many on-chip networks)
+ Simple
+ Deadlock freedom (no cycles in resource allocation)
- Could lead to high contention
- Does not exploit path diversity

## Slide 48: Deadlock
No forward progress
Caused by circular dependencies on resources
Each packet waits for a buffer occupied by another packet downstream

## Slide 49: Handling Deadlock
Avoid cycles in routing
  Dimension order routing
    Cannot build a circular dependency
  Restrict the “turns” each packet can take
Avoid deadlock by adding more buffering (escape paths)
Detect and break deadlock
  Preemption of buffers

## Slide 50: Turn Model to Avoid Deadlock
Idea
  Analyze directions in which packets can turn in the network
  Determine the cycles that such turns can form
  Prohibit just enough turns to break possible cycles
Glass and Ni, “The Turn Model for Adaptive Routing,” ISCA 1992.

## Slide 51: Oblivious Routing: Valiant’s Algorithm
Goal: Balance network load
Idea: Randomly choose an intermediate destination, route to it first, then route from there to destination
  Between source-intermediate and intermediate-dest, can use dimension order routing
+ Randomizes/balances network load
- Non minimal (packet latency can increase)
Optimizations:
  Do this on high load
  Restrict the intermediate node to be close (in the same quadrant)

## Slide 52: Adaptive Routing
Minimal adaptive
  Router uses network state (e.g., downstream buffer occupancy) to pick which “productive” output port to send a packet to
  Productive output port: port that gets the packet closer to its destination
  + Aware of local congestion
  - Minimality restricts achievable link utilization (load balance)
Non-minimal (fully) adaptive
  “Misroute” packets to non-productive output ports based on network state
  + Can achieve better network utilization and load balance
  - Need to guarantee livelock freedom

## Slide 53: More on Adaptive Routing
Can avoid faulty links/routers
Idea: Route around faults
+ Deterministic routing cannot handle faulty components
- Need to change the routing table to disable faulty routes
- Assuming the faulty link/router is detected
One recent example:
Fattah et al., "A Low-Overhead, Fully-Distributed, Guaranteed-Delivery Routing Algorithm for Faulty Network-on-Chips", NOCS 2015.

## Slide 54: Buffering and Flow Control

## Slide 55: Recall: Circuit vs. Packet Switching
Circuit switching sets up full path before transmission
  Establish route then send data
  Noone else can use those links while “circuit” is set
  + faster arbitration
  -- setting up and bringing down “path” takes time
Packet switching routes per packet in each router
  Route each packet individually (possibly via different paths)
  If link is free, any packet can use it
  -- potentially slower --- must dynamically switch
  + no setup, bring down time
  + more flexible, does not underutilize links

## Slide 56: Packet Switched Networks: Packet Format
Header
  routing and control information
Payload
  carries data (non HW specific information)
  can be further divided (framing, protocol stacks…)
Error Code
  generally at tail of packet so it can be generated on the way out
Header
Payload
Error Code

## Slide 57: Handling Contention
Two packets trying to use the same link at the same time
What do you do?
  Buffer one
  Drop one
  Misroute one (deflection)
Tradeoffs?

## Slide 58: Flow Control Methods
Circuit switching
Bufferless (Packet/flit based)
Store and forward (Packet based)
Virtual Cut Through (Packet based)
Wormhole (Flit based)

## Slide 59: Circuit Switching Revisited
Resource allocation granularity is high
Idea: Pre-allocate resources across multiple switches for a given “flow”
Need to send a probe to set up the path for pre-allocation
+ No need for buffering
+ No contention (flow’s performance is isolated)
+ Can handle arbitrary message sizes
- Lower link utilization: two flows cannot use the same link
- Handshake overhead to set up a “circuit”

## Slide 60: Bufferless Deflection Routing
Destination
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.1
1Baran, “On Distributed Communication Networks.” RAND Tech. Report., 1962 / IEEE Trans.Comm., 1964.
New traffic can be injected
whenever there is a free
output link.

## Slide 61: Bufferless Deflection Routing
Input buffers are eliminated: packets are buffered in pipeline latches and on network links
North
South
East
West
Local
North
South
East
West
Local
Deflection Routing Logic
Input Buffers

## Slide 62: Store and Forward Flow Control
Packet based flow control
Store and Forward
  Packet copied entirely into network router before moving to the next node
  Flow control unit is the entire packet
Leads to high per-packet latency
Requires buffering for entire packet in each node
Can we do better?
S
D

## Slide 63: Cut through Flow Control
Another form of packet based flow control
Start forwarding as soon as header is received and resources (buffer, channel, etc) allocated
  Dramatic reduction in latency
Still allocate buffers and channel bandwidth for full packets
What if packets are large?
S
D

## Slide 64: Cut through Flow Control
What to do if output port is blocked?
Lets the tail continue when the head is blocked, absorbing the whole message into a single switch.
  Requires a buffer large enough to hold the largest packet.
Degenerates to store-and-forward with high contention
Can we do better?

## Slide 65: Wormhole Flow Control
Packets broken into (potentially) smaller flits (buffer/bw allocation unit)
Flits are sent across the fabric in a wormhole fashion
  Body follows head, tail follows body
  Pipelined
  If head blocked, rest of packet stops
  Routing (src/dest) information only in head
How does body/tail know where to go?
Latency almost independent of distance for long messages

## Slide 66: Wormhole Flow Control
Advantages over “store and forward” flow control
  + Lower latency
  + More efficient buffer utilization
Limitations
  - Suffers from head of line blocking
  - If head flit cannot move due to contention, another worm cannot proceed even though links may be idle
1
2
1
2
1
2
Switching Fabric
Input Queues
Outputs
1
2
1
2
HOL Blocking
Idle!

## Slide 67: Head of Line Blocking
A worm can be before another in the router input buffer
Due to FIFO nature, the second worm cannot be scheduled even though it may need to access another output port

## Slide 68: Head of Line Blocking
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until read proceeds

## Slide 69: Virtual Channel Flow Control
Idea: Multiplex multiple channels over one physical channel
Divide up the input buffer into multiple buffers sharing a single physical channel
Dally, “Virtual Channel Flow Control,” ISCA 1990.

## Slide 70: Virtual Channel Flow Control
Idea: Multiplex multiple channels over one physical channel
Divide up the input buffer into multiple buffers sharing a single physical channel
Dally, “Virtual Channel Flow Control,” ISCA 1990.

## Slide 71: Virtual Channel Flow Control
Blocked by other packets
Buffer full: blue cannot proceed

## Slide 72: A Modern Virtual Channel Based Router

## Slide 73: Other Uses of Virtual Channels
Deadlock avoidance
  Enforcing switching to a different set of virtual channels on some “turns” can break the cyclic dependency of resources
    Enforce order on VCs
  Escape VCs: Have at least one VC that uses deadlock-free routing. Ensure each flit has fair access to that VC.
  Protocol level deadlock: Ensure address and data packets use different VCs  prevent cycles due to intermixing of different packet classes
Prioritization of traffic classes
  Some virtual channels can have higher priority than others

## Slide 74: Review: Flow Control
Store and Forward
S
D
Cut Through / Wormhole
S
D
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until read proceeds
Shrink Buffers
Reduce latency
Any other issues?
Head-of-Line
Blocking
Use Virtual
Channels

## Slide 75: Review: Flow Control
Store and Forward
S
D
Cut Through / Wormhole
S
D
Shrink Buffers
Reduce latency
Any other issues?
Head-of-Line
Blocking
Use Virtual
Channels
Blocked by other packets
Buffer full: blue cannot proceed

## Slide 76: Communicating Buffer Availability
Credit-based flow control
  Upstream knows how many buffers are downstream
  Downstream passes back credits to upstream
  Significant upstream signaling (esp. for small flits)
On/Off (XON/XOFF) flow control
  Downstream has on/off signal to upstream
Ack/Nack flow control
  Upstream optimistically sends downstream
  Buffer cannot be deallocated until ACK/NACK received
  Inefficiently utilizes buffer space

## Slide 77: Credit-based Flow Control
Round-trip credit delay:
  Time between when buffer empties and when next flit can be processed from that buffer entry
Significant throughput degradation if there are few buffers
Important to size buffers to tolerate credit turn-around
Node 1
Node 2
Flit departs
router
t1
Credit
Process
t2
t3
Credit
Flit
Process
t4
t5
Credit round trip delay

## Slide 78: On/Off (XON/XOFF) Flow Control
Downstream has on/off signal to upstream
Process
Node 1
Node 2
t1
Flit
Flit
Flit
Flit
t2
Foffthreshold reached
Off
Flit
Flit
Flit
Flit
Flit
On
Process
Flit
Flit
Flit
Flit
Flit
t3
t4
t5
t6
t7
t8
Foffset to prevent flits arriving before t4 from overflowing
Fonthreshold reached
Fonset so that Node 2 does not run out of flits between t5 and t8

## Slide 79: Interconnection Network Performance

## Slide 80: Interconnection Network Performance
Latency
Injection rate into network
Min latency given by topology
Min latency given by routing algorithm
Zero load latency
(topology+routing+flow control)
Throughput given by topology
Throughput given by routing
Throughput given by flow control

## Slide 81: Ideal Latency
Ideal latency
  Solely due to wire delay between source and destination
  D = Manhattan distance
  L = packet size
  b = channel bandwidth
  v = propagation velocity
Notes: What’s the best we can do?

## Slide 82: Actual Latency
Dedicated wiring impractical
  Long wires segmented with insertion of routers
  D = Manhattan distance
  L = packet size
  b = channel bandwidth
  v = propagation velocity
  H = hops
  Trouter = router latency
  Tc = latency due to contention

## Slide 83: Latency and Throughput Curve
Chart: Injected load (fraction of capacity)
| 0.01 | 0.02 | 0.05 | 0.1 | 0.12 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.60000000000000098 | 0.65000000000000102 | 0.70000000000000095 | 0.750000000000001 | 0.76000000000000101 | 0.85000000000000098 | 0.9 | 0.95000000000000095 | 1
Ideal | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13
On-chip Network | 20 | 20 | 20 | 20 | 20.1 | 20.3 | 20.4 | 20.7 | 21 | 21.6 | 22.5 | 23.8 | 25 | 27 | 29 | 33 | 39 | 50 | 60 | 100 | 100 | 100 | 100

## Slide 84: Network Performance Metrics
Packet latency
Round trip latency
Saturation throughput
Application-level performance: system performance
  Affected by interference among threads/applications

## Slide 85: Buffering and Routing in On-Chip Networks

## Slide 86: On-Chip Networks
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc
  Buses and crossbars are not scalable
Packet switched
2D mesh: Most commonly used topology
Primarily serve cache misses and memory requests
Notes: One commonly proposed solution is on-chip network (NoC), which allows cores to communicate with a packet switched substrate.
Here is a figure showing an on-chip network that uses a 2d-mesh topology which
is commonly used due to its low layout complexity.
This is also the topology we used for our evaluations, but our mechanism is also applicable to other topologies.
In most multi-core systems, NoC primarily serves cache misses and memory requests.

## Slide 87: On-chip Networks
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Router
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)

## Slide 88: On-Chip vs. Off-Chip Interconnects
On-chip advantages
  Low latency between cores
  No pin constraints
  Rich wiring resources
  Very high bandwidth
  Simpler coordination
On-chip constraints/disadvantages
  2D substrate limits implementable topologies
  Energy/power consumption a key concern
  Complex algorithms undesirable
  Logic area constrains use of wiring resources

## Slide 89: On-Chip vs. Off-Chip Interconnects (II)
Cost
  Off-chip: Channels, pins, connectors, cables
  On-chip: Cost is storage and switches (wires are plentiful)
  Leads to networks with many wide channels, few buffers
Channel characteristics
  On chip short distance  low latency
  On chip RC lines  need repeaters every 1-2mm
    Can put logic in repeaters
Workloads
  Multi-core cache traffic vs. supercomputer interconnect traffic

## Slide 90: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Injection Rate
Avg. packet latency
large buffers
medium buffers
small buffers

## Slide 91: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Buffers consume significant energy/power
  Dynamic energy when read/write
  Static energy even when not occupied
Buffers add complexity and latency
  Logic for buffer management
  Virtual channel allocation
  Credit-based flow control
Buffers require significant chip area
  E.g., in TRIPS prototype chip, input buffers occupy 75% of total on-chip network area [Gratz et al, ICCD’06]
Can we get rid of buffers…?

## Slide 92: Going Bufferless…?
How much throughput do we lose?
   How is latency affected?
Up to what injection rates can we use bufferless routing?
 Are there realistic scenarios in which NoC is operated at injection rates below the threshold?
Can we achieve energy reduction?
   If so, how much…?
Can we reduce area, complexity, etc…?
Injection Rate
latency
buffers
no buffers
Answers in our paper!

## Slide 93: Bufferless Routing in NoCs
Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.
  https://users.ece.cmu.edu/~omutlu/pub/bless_isca09.pdf

## Slide 94: Packet Scheduling
Which packet to choose for a given output port?
  Router needs to prioritize between competing flits
  Which input port?
  Which virtual channel?
  Which application’s packet?
Common strategies
  Round robin across virtual channels
  Oldest packet first (or an approximation)
  Prioritize some virtual channels over others
Better policies in a multi-core environment
  Use application characteristics

## Slide 95: Application-Aware Packet Scheduling
  Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.

## Slide 96: The Problem: Packet Scheduling
Network-on-Chip
L2$
L2$
L2$
L2$
Bank
mem cont
Memory Controller
P
Accelerator
L2$
Bank
L2$
Bank
P
P
P
P
P
P
P
Network-on-Chip
Network-on-Chip is a critical resource
shared by multiple applications
App1
App2
App N
App N-1

## Slide 97: The Problem: Packet Scheduling
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Routers
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)

## Slide 98: The Problem: Packet Scheduling
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
VC
1
VC
2
From East
From West
From North
From South
From PE

## Slide 99: The Problem: Packet Scheduling
Conceptual
View
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
VC
1
VC
2
From East
From West
From North
From South
From PE
Allocator
(SA)

## Slide 100
Scheduler
Conceptual
View
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
VC
1
VC
2
From East
From West
From North
From South
From PE
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
Which packet to choose?
The Problem: Packet Scheduling

## Slide 101: The Problem: Packet Scheduling
Existing scheduling policies
  Round Robin
  Age
Problem 1: Local to a router
  Lead to contradictory decision making between routers: packets from one application may be prioritized at one router, to be delayed at next.
Problem 2: Application oblivious
  Treat all applications packets equally
  But applications are heterogeneous
Solution : Application-aware global scheduling policies.

## Slide 102: STC Scheduling Example
Injection Cycles
1
2
3
4
5
6
7
8
2
2
3
Batch 0
Packet Injection Order at Processor
Core1 Core2 Core3
Batching interval length = 3 cycles
Ranking order =
Batch 1
Batch 2

## Slide 103: STC Scheduling Example
4
8
5
1
7
2
1
6
2
1
3
Router
Scheduler
Injection Cycles
1
2
3
4
5
6
7
8
2
2
3
Batch 2
Batch 1
Batch 0
Applications

## Slide 104: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
3
2
8
7
6
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age |  |  |  | 
STC |  |  |  | 
Time

## Slide 105: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
5
4
3
1
2
2
3
2
8
7
6
Age
3
3
5
4
6
7
8
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age | 4 | 6 | 11 | 7.0
STC |  |  |  | 
Time
Time

## Slide 106: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
5
4
3
1
2
2
3
2
8
7
6
Age
2
3
3
5
4
6
7
8
1
2
2
STC
3
5
4
6
7
8
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age | 4 | 6 | 11 | 7.0
STC | 1 | 3 | 11 | 5.0
Ranking order
Time
Time
Time

## Slide 107: Bufferless Routing in NoCs
Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.
  https://users.ece.cmu.edu/~omutlu/pub/app-aware-noc_micro09.pdf

## Slide 108: 18-740/640 Computer Architecture Lecture 16: Interconnection Networks
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015, 11/4/2015