## Slide 1
18-740: Computer Architecture Recitation 3:
Rethinking Memory System Design
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015
September 15, 2015
Notes: 1

## Slide 2: Agenda
Review Assignments for Next Week
Rethinking Memory System Design (Continued)
  With a lot of discussion, hopefully

## Slide 3: Review Assignments for Next Week

## Slide 4: Required Reviews
Due Tuesday Sep 22 @ 3pm
Enter your reviews on the review website
Please discuss ideas and thoughts on Piazza

## Slide 5: Review Paper 1 (Required)
Yu Cai, Yixin Luo, Saugata Ghose, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]
Related
  Yu Cai, Yixin Luo, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)]

## Slide 6: Review Paper 2 (Required)
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)
Related
  Benjamin C. Lee, Ping Zhou, Jun Yang, Youtao Zhang, Bo Zhao, Engin Ipek, Onur Mutlu, and Doug Burger, "Phase Change Technology and the Future of Main Memory" IEEE Micro, Special Issue: Micro's Top Picks from 2009 Computer Architecture Conferences (MICRO TOP PICKS), Vol. 30, No. 1, pages 60-70, January/February 2010.

## Slide 7: Review Paper 3 (Required)
Jose A. Joao, M. Aater Suleman, Onur Mutlu, and Yale N. Patt, "Bottleneck Identification and Scheduling in Multithreaded Applications" Proceedings of the 17th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), London, UK, March 2012. Slides (ppt) (pdf)
Related
  M. Aater Suleman, Onur Mutlu, Moinuddin K. Qureshi, and Yale N. Patt, "Accelerating Critical Section Execution with Asymmetric Multi-Core Architectures" Proceedings of the 14th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), pages 253-264, Washington, DC, March 2009. Slides (ppt)

## Slide 8: Review Paper 4 (Optional)
Eiman Ebrahimi, Chang Joo Lee, Onur Mutlu, and Yale N. Patt, "Fairness via Source Throttling: A Configurable and High-Performance Fairness Substrate for Multi-Core Memory Systems" Proceedings of the 15th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), pages 335-346, Pittsburgh, PA, March 2010. Slides (pdf)

## Slide 9: Project Proposal
Due next week
  September 25, 2015

## Slide 10: Another Possible Project
GPU Warp Scheduling Championship
http://adwaitjog.github.io/gpu_scheduling.html

## Slide 11: Rethinking Memory System Design

## Slide 12: Some Promising Directions
New memory architectures
  Rethinking DRAM and flash memory
  A lot of hope in fixing DRAM
Enabling emerging NVM technologies
  Hybrid memory systems
  Single-level memory and storage
  A lot of hope in hybrid memory systems and single-level stores
System-level memory/storage QoS
  A lot of hope in designing a predictable system

## Slide 13: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
How Can We Do Better?
Summary

## Slide 14: Rethinking DRAM
In-Memory Computation
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 15: Recap: The DRAM Scaling Problem

## Slide 16: Takeaways So Far
DRAM Scaling is getting extremely difficult
  To the point of threatening the foundations of secure systems
Industry is very open to “different” system designs and “different” memories
  Cost-per-bit is not the sole driving force any more

## Slide 17: Why In-Memory Computation Today?
Push from Technology Trends
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
Pull from Systems and Applications Trends
  Data access is a major system and application bottleneck
  Systems are energy limited
  Data movement much more energy-hungry than computation

## Slide 18: A Computing System
Three key components
Computation
Communication
Storage/memory

## Slide 19: Today’s Computing Systems
Are overwhelmingly processor centric
Processor is heavily optimized and is considered the master
Many system-level tradeoffs are constrained or dictated by the processor – all data processed in the processor
Data storage units are dumb slaves and are largely unoptimized (except for some that are on the processor die)

## Slide 20: Traditional Computing Systems
Data stored far away from computational units
Bring data to the computational units
Operate on the brought data
Cache it as much as possible
Send back the results to data storage
This may not be an efficient approach given three key systems trends

## Slide 21: Three Key Systems Trends
1. Data access from memory is a major bottleneck
  Limited pin bandwidth
  High energy memory bus
  Applications are increasingly data hungry
2. Energy consumption is a key limiter in systems
3. Data movement is much more expensive than computation
  Especially true for off-chip to on-chip movement
Dally, HiPEAC 2015

## Slide 22: The Problem
Today’s systems overwhelmingly move data towards computation, exercising the three bottlenecks
This is a huge problem when the amount of data access is huge relative to the amount of computation
  The case with many data-intensive workloads
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos

## Slide 23: In-Memory Computation: Goals and Approaches
Goals
  Enable computation capability where data resides (e.g., in memory, in caches)
  Enable system-level mechanisms to exploit near-data computation capability
    E.g., to decide where it makes the most sense to perform the computation
Approaches
  1. Minimally change DRAM to enable simple yet powerful computation primitives
  2. Exploit the control logic in 3D-stacked memory to enable more comprehensive computation near memory

## Slide 24: Why This is Not All Déjà Vu
Past approaches to PIM (e.g., logic-in-memory, NON-VON, Execube, IRAM) had little success due to three reasons:
1. They were too costly. Placing a full processor inside DRAM technology is still not a good idea today.
2. The time was not ripe:
  Memory scaling was not pressing. Today it is critical.
  Energy and bandwidth were not critical scalability limiters. Today they are.
  New technologies were not as prevalent, promising or needed. Today we have 3D stacking, STT-MRAM, etc. which can help with computation near data.
3. They did not consider all issues that limited adoption (e.g., coherence, appropriate partitioning of computation)

## Slide 25: Two Approaches to In-Memory Processing
1. Minimally change DRAM to enable simple yet powerful computation primitives
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
2. Exploit the control logic in 3D-stacked memory to enable more comprehensive computation near memory

## Slide 26: Approach 1: Minimally Changing DRAM
DRAM has great capability to perform bulk data movement and computation internally with small changes
  Can exploit internal bandwidth to move data
  Can exploit analog computation capability
  …
Examples: RowClone and In-DRAM AND/OR
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  …

## Slide 27: Today’s Memory: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 28: Future: RowClone (In-Memory Copy)
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
90ns, 0.04uJ

## Slide 29: DRAM Subarray Operation (load one byte)
Row Buffer (8 Kbits)
Data Bus
8 bits
DRAM array
8 Kbits
Step 1: Activate row
Transfer row
Step 2: Read
Transfer byte onto bus
Notes: say you want a byte

## Slide 30: RowClone: In-DRAM Row Copy
Row Buffer (8 Kbits)
Data Bus
8 bits
DRAM array
8 Kbits
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
0.01% area cost
Notes: copy

## Slide 31: Generalized RowClone
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Intra Subarray
Copy (2 ACTs)
Inter Bank Copy
(Pipelined
Internal RD/WR)
Inter Subarray Copy
(Use Inter-Bank Copy Twice)

## Slide 32: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 33: RowClone: Application Performance
Chart: % Compared to Baseline
| bootup | compile | forkbench | mcached | mysql | shell
IPC Improvement | 15 | 9 | 43 | 4 | 4 | 40
Energy Reduction | 40 | 32 | 60 | 15 | 17 | 67

## Slide 34: RowClone: Multi-Core Performance
Chart: 50 Workloads (4-core)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RowClone | 1.02 | 1.04 | 1.07 | 1.07 | 1.08 | 1.08 | 1.08 | 1.08 | 1.08 | 1.09 | 1.09 | 1.09 | 1.1 | 1.1 | 1.11 | 1.11 | 1.12 | 1.12 | 1.12 | 1.12 | 1.13 | 1.15 | 1.16 | 1.16 | 1.18 | 1.2 | 1.2 | 1.2 | 1.2 | 1.21 | 1.21 | 1.21 | 1.21 | 1.23 | 1.23 | 1.23 | 1.23 | 1.24 | 1.26 | 1.27 | 1.27 | 1.27 | 1.28 | 1.3 | 1.31 | 1.32 | 1.32 | 1.34 | 1.34 | 1.39

## Slide 35: End-to-End System Design
DRAM (RowClone)
Microarchitecture
ISA
Operating System
Application
How to communicate occurrences of bulk copy/initialization across layers?
How to maximize latency and energy savings?
How to ensure cache coherence?
How to handle data reuse?

## Slide 36: Goal: Ultra-Efficient Processing Near Data
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 37: Enabling In-Memory Search
What is a flexible and scalable memory interface?
What is the right partitioning of computation capability?
What is the right low-cost memory substrate?
What memory technologies are the best enablers?
How do we rethink/ease search algorithms/applications?
Cache
Processor
Core
Interconnect
Memory
Database
Query vector
Results

## Slide 38: Enabling In-Memory Computation
Virtual Memory Support
Cache Coherence
DRAM Support
RowClone
(MICRO 2013)
Dirty-Block Index
(ISCA 2014)
Page Overlays
(ISCA 2015)
In-DRAM Gather Scatter
In-DRAM Bitwise Operations
(IEEE CAL 2015)
?
?
Non-contiguous Cache lines
Gathered Pages

## Slide 39: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 40: In-DRAM Bulk Bitwise AND/OR Operation
BULKAND A, B  C
Semantics: Perform a bitwise AND of two rows A and B and store the result in row C
R0 – reserved zero row, R1 – reserved one row
D1, D2, D3 – Designated rows for triple activation
1. RowClone A into D1
2. RowClone B into D2
3. RowClone R0 into D3
4. ACTIVATE D1,D2,D3
5. RowClone Result into C

## Slide 41: In-DRAM AND/OR Results
20X improvement in AND/OR throughput vs. Intel AVX
50.5X reduction in memory energy consumption
At least 30% performance improvement in range queries
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.
Size of Vectors to be ANDed
Throughput of AND operations (GB/s)
In-DRAM AND (2 banks)
In-DRAM AND (1 bank)
Intel AVX

## Slide 42: Going Forward
A bulk computation model in memory
New memory & software interfaces to enable bulk in-memory computation
New programming models, algorithms, compilers, and system designs that can take advantage of the model
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 43: Two Approaches to In-Memory Processing
1. Minimally change DRAM to enable simple yet powerful computation primitives
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
2. Exploit the control logic in 3D-stacked memory to enable more comprehensive computation near memory
  PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture (Ahn et al., ISCA 2015)
  A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing (Ahn et al., ISCA 2015)

## Slide 44: Two Key Questions in 3D Stacked PIM
What is the minimal processing-in-memory support we can provide ?
  without changing the system significantly
  while achieving significant benefits of processing in 3D-stacked memory
How can we accelerate important applications if we use 3D-stacked memory as a coarse-grained accelerator?
  what is the architecture and programming model?
  what are the mechanisms for acceleration?

## Slide 45: PIM-Enabled Instructions: A Low-Overhead, Locality-Aware PIM Architecture
  PIM-Enabled Instructions: A Low-Overhead,
  Locality-Aware Processing-in-Memory Architecture
  (Ahn et al., ISCA 2015)

## Slide 46: Challenges in Processing-in-Memory
DRAM die
Cost-effectiveness
Programming Model
Coherence & VM
DRAM die
Complex Logic
Host Processor
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
In-Memory Processors
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Host Processor
3
3
4
5
C
C

## Slide 47: Challenges in Processing-in-Memory
DRAM die
Cost-effectiveness
Programming Model
Coherence & VM
DRAM die
Complex Logic
Host Processor
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
In-Memory Processors
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Host Processor
3
3
4
5
C
C
(Partially) Solved by
3D-Stacked DRAM
Still Challenging even in Recent PIM Architectures
(e.g., AC-DIMM, NDA, NDC, TOP-PIM, Tesseract, …)

## Slide 48: Simple PIM Programming, Coherence, VM
Objectives
  Provide an intuitive programming model for PIM
  Full support for cache coherence and virtual memory
  Minimize implementation overhead of PIM units
Solution: simple PIM operations as ISA extensions
  PIM operations as host processor instructions: intuitive
    Preserves sequential programming model
    Avoids the need for virtual memory support in memory
  Leads to low-overhead implementation
  PIM-enabled instructions can be executed on the host-side or the memory side (locality-aware execution)

## Slide 49: Simple PIM Operations as ISA Extensions (I)
Example: Parallel PageRank computation
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}
for (v: graph.vertices) {
v.rank = v.next_rank; v.next_rank = alpha;
}

## Slide 50: Simple PIM Operations as ISA Extensions (II)
Main Memory
w.next_rank
w.next_rank
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}
Host Processor
w.next_rank
w.next_rank
64 bytes in
64 bytes out
Conventional Architecture

## Slide 51: Simple PIM Operations as ISA Extensions (III)
Main Memory
w.next_rank
w.next_rank
Host Processor
value
8 bytes in
0 bytes out
In-Memory Addition
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pim.add r1, (r2)

## Slide 52: Always Executing in Memory? Not A Good Idea
Chart: Speedup
| p2p-Gnu tella31 | soc-Slash dot0811 | web- Stanford | amazon- 2008 | frwiki- 2013 | wiki- Talk | cit- Patents | soc-Live Journal1 | ljournal- 2008
계열 1 | -0.19828 | -0.072364 | -0.11014 | -0.0073164 | 0.015521 | 0.30554 | 0.53667 | 0.50416 | 0.18676
More Vertices
Increased
Memory Bandwidth Consumption
Caching very effective
Reduced Memory Bandwidth
Consumption due to
In-Memory Computation

## Slide 53: Two Key Questions for Simple PIM
How should simple PIM operations be interfaced to conventional systems?
  PIM-enabled Instructions (PEIs): Expose PIM operations as cache-coherent, virtually-addressed host processor instructions
  No changes to the existing sequential programming model
What is the most efficient way of exploiting such simple PIM operations?
  Locality-aware PEIs: Dynamically determine the location of PEI execution based on data locality without software hints

## Slide 54: PIM-Enabled Instructions
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}

## Slide 55: PIM-Enabled Instructions
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pim.add r1, (r2)
Executed either in memory or in the host processor
Cache-coherent, virtually-addressed
Atomic between different PEIs
Not atomic with normal instructions (use pfence)

## Slide 56: PIM-Enabled Instructions
Executed either in memory or in the host processor
Cache-coherent, virtually-addressed
Atomic between different PEIs
Not atomic with normal instructions (use pfence)
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pfence();
pim.add r1, (r2)
pfence

## Slide 57: PIM-Enabled Instructions
Key to practicality: single-cache-block restriction
  Each PEI can access at most one last-level cache block
  Similar restrictions exist in atomic instructions
Benefits
  Localization: each PEI is bounded to one memory module
  Interoperability: easier support for cache coherence and virtual memory
  Simplified locality monitoring: data locality of PEIs can be identified simply by the cache control logic

## Slide 58: PEI Architecture
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
3D-stacked Memory (HMC)
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
Proposed PEI Architecture

## Slide 59: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
x
y
y

## Slide 60: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
y
Address Translation for PEIs
Done by the host processor TLB
(similar to normal instructions)
No modifications to existing HW/OS
No need for in-memory TLBs

## Slide 61: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
x
y
y
Wait until x is writable

## Slide 62: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
x
y
Wait until x is writable
Reader-writer lock #0
Reader-writer lock #1
Reader-writer lock #N-1
Reader-writer lock #2
…
Address
XOR-Hash
(Inexact, but Conservative)

## Slide 63: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
x
Wait until x is writable
Check the data locality of x
y

## Slide 64: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
Wait until x is writable
Check the data locality of x
y
Hit: High locality
Miss: Low locality
Tag
Tag
Tag
Tag
…
Tag
Tag
Tag
Tag
…
Tag
Tag
Tag
Tag
…
…
Address
Partial Tag Array
Updated on
Each LLC access
Each issue of a PIM operation to memory

## Slide 65: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
y
x
Low locality
Wait until x is writable
Check the data locality of x

## Slide 66: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
y
x
Low locality
Back-invalidation for cache coherence
No modifications to existing cache coherence protocols

## Slide 67: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
y
x
x+y
y
x+y
Low locality

## Slide 68: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM
Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
y
x+y
x+y
Completely Localized
PIM Memory Accesses
without Special Data Mapping

## Slide 69: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
y
x
x+y
x+y
Completion Notification

## Slide 70: Host-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
x
y
y
Wait until x is writable
Check the data locality of x

## Slide 71: Host-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
x
y
Wait until x is writable
Check the data locality of x
x
High locality
x
x+y
x
x+y

## Slide 72: Host-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
x+y
x
x
x+y
No Cache Coherence Issues

## Slide 73: Host-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level
Cache
HMC Controller
Crossbar Network
DRAM
Controller
DRAM
Controller
DRAM
Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM
Directory
Locality Monitor
PMU
pim.add y, &x
x
y
x+y
x
x
x+y
Completion Notification

## Slide 74: PEI Execution Summary
Atomicity of PEIs
  PIM directory implements reader-writer locks
Locality-aware PEI execution
  Locality monitor simulates cache replacement behavior
Cache coherence for PEIs
  Memory-side: back-invalidation/back-writeback
  Host-side: no need for consideration
Virtual memory for PEIs
  Host processor performs address translation before issuing a PEI

## Slide 75: Evaluation: Simulation Configuration
In-house x86-64 simulator based on Pin
  16 out-of-order cores, 4GHz, 4-issue
  32KB private L1 I/D-cache, 256KB private L2 cache
  16MB shared 16-way L3 cache, 64B blocks
  32GB main memory with 8 daisy-chained HMCs (80GB/s)
PCU (PIM Computation Unit, In Memory)
  1-issue computation logic, 4-entry operand buffer
  16 host-side PCUs at 4GHz, 128 memory-side PCUs at 2GHz
PMU (PIM Management Unit, Host Side)
  PIM directory: 2048 entries (3.25KB)
  Locality monitor: similar to LLC tag array (512KB)

## Slide 76: Evaluated Data-Intensive Applications
Ten emerging data-intensive workloads
  Large-scale graph processing
    Average teenage followers, BFS, PageRank, single-source shortest path, weakly connected components
  In-memory data analytics
    Hash join, histogram, radix partitioning
  Machine learning and data mining
    Streamcluster, SVM-RFE
Three input sets (small, medium, large) for each workload to show the impact of data locality

## Slide 77: PEI Performance Delta: Large Data Sets
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.53918 | 0.31004 | 0.50416 | 0.45845 | 0.47598 | 0.66307 | 0.6314 | 0.44904 | 0.15358 | 0.33671 | 0.4446
Locality-Aware | 0.60067 | 0.34622 | 0.55934 | 0.51064 | 0.5286 | 0.65698 | 0.60316 | 0.44327 | 0.2149 | 0.3438 | 0.47446
(Large Inputs, Baseline: Host-Only)

## Slide 78: PEI Performance: Large Data Sets
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.53918 | 0.31004 | 0.50416 | 0.45845 | 0.47598 | 0.66307 | 0.6314 | 0.44904 | 0.15358 | 0.33671 | 0.4446
Locality-Aware | 0.60067 | 0.34622 | 0.55934 | 0.51064 | 0.5286 | 0.65698 | 0.60316 | 0.44327 | 0.2149 | 0.3438 | 0.47446
(Large Inputs, Baseline: Host-Only)
Chart: Normalized Amount of Off-chip Transfer
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM
Host-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Only | 0.57082 | 0.75659 | 0.68201 | 0.74528 | 0.69303 | 0.7343 | 0.66669 | 0.82187 | 1.066 | 1.0402
Locality-Aware | 0.53033 | 0.70259 | 0.58305 | 0.62293 | 0.61429 | 0.73496 | 0.66669 | 0.82173 | 1.0575 | 0.9762

## Slide 79: PEI Performance Delta: Small Data Sets
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | -0.22001 | -0.17526 | -0.072364 | -0.074298 | -0.090338 | -0.20025 | 0.54727 | -0.50008 | -0.40915 | -0.43574 | -0.20283
Locality-Aware | 0.050393 | 0.033552 | 0.00024264 | 0.0089585 | 0.0094162 | -0.013054 | 0.51424 | -0.0057565 | -0.0011447 | -0.0029887 | 0.05049
(Small Inputs, Baseline: Host-Only)

## Slide 80: PEI Performance: Small Data Sets
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | -0.22001 | -0.17526 | -0.072364 | -0.074298 | -0.090338 | -0.20025 | 0.54727 | -0.50008 | -0.40915 | -0.43574 | -0.20283
Locality-Aware | 0.050393 | 0.033552 | 0.00024264 | 0.0089585 | 0.0094162 | -0.013054 | 0.51424 | -0.0057565 | -0.0011447 | -0.0029887 | 0.05049
(Small Inputs, Baseline: Host-Only)
Chart: Normalized Amount of Off-chip Transfer
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM
Host-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Only | 2.2436 | 2.8887 | 3.1716 | 6.4881 | 3.6498 | 3.5416 | 0.67043 | 16.241 | 501.6688 | 408.0847
Locality-Aware | 1.1309 | 1.1806 | 1.0027 | 1.123 | 1.0907 | 1.1189 | 0.67043 | 1.038 | 1.7717 | 2.5209

## Slide 81: PEI Performance Delta: Medium Data Sets
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.016737 | -0.013893 | 0.015521 | 0.03812 | 0.0073854 | 0.22636 | 0.62757 | 0.2138 | 0.077582 | -0.034224 | 0.1038
Locality-Aware | 0.13541 | 0.1263 | 0.11073 | 0.12106 | 0.13711 | 0.17555 | 0.59989 | 0.21386 | 0.13909 | 0.0445 | 0.17268
(Medium Inputs, Baseline: Host-Only)

## Slide 82: PEI Energy Consumption
Chart: 
| Small | Medium | Large
Cache | 0.27613 | 0.22974 | 0.2138
HMC Link | 0.50415 | 0.51297 | 0.51397
DRAM | 0.21457 | 0.25453 | 0.26887
Host-side PCU | 0.0043662 | 0.0036967 | 0.0030358
Memory-side PCU | 0 | 0 | 0
PMU | 7.7323e-05 | 6.4146e-05 | 5.4225e-05
계열 7 | 0.29322 | 0.18897 | 0.14107
계열 8 | 0.68428 | 0.4834 | 0.36147
계열 9 | 0.46391 | 0.35056 | 0.26204
계열 10 | 0 | 0 | 0
계열 11 | 0.015795 | 0.011518 | 0.0085371
계열 12 | 0.0053637 | 0.0036921 | 0.0027686
Host-Only
PIM-Only
Locality-Aware

## Slide 83: Summary: Simple Processing-In-Memory
PIM-enabled Instructions (PEIs): Expose PIM operations as cache-coherent, virtually-addressed host processor instructions
  No changes to the existing sequential programming model
  No changes to virtual memory
  Minimal changes for cache coherence
Locality-aware PEIs: Dynamically determine the location of PEI execution based on data locality without software hints
PEI performance and energy results are promising
  47%/32% speedup over Host/PIM-Only in large/small inputs
  25% node energy reduction in large inputs
  Good adaptivity across randomly generated workloads

## Slide 84: Two Key Questions in 3D Stacked PIM
What is the minimal processing-in-memory support we can provide ?
  without changing the system significantly
  while achieving significant benefits of processing in 3D-stacked memory
How can we accelerate important applications if we use 3D-stacked memory as a coarse-grained accelerator?
  what is the architecture and programming model?
  what are the mechanisms for acceleration?