## Slide 1
18-740: Computer Architecture Recitation 5:
Main Memory Scaling Wrap-Up
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015
September 29, 2015
Notes: 1

## Slide 2: Review Assignments for Next Week

## Slide 3: Required Reviews
Due Tuesday Oct 6 @ 3pm
Enter your reviews on the review website
Please discuss ideas and thoughts on Piazza

## Slide 4: Review Paper 1 (Required)
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015.
Related paper
  Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 5: Review Paper 2 (Required)
Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Error Analysis and Retention-Aware Error Management for NAND Flash Memory" Intel Technology Journal (ITJ) Special Issue on Memory Resiliency, Vol. 17, No. 1, May 2013.

## Slide 6: Review Paper 3 (Required)
Edmund B. Nightingale, John R. Douceur, Vince Orgovan, “Cycles, cells and platters: an empirical analysisof hardware failures on a million consumer PCs,” Eurosys 2011.
  http://eurosys2011.cs.uni-salzburg.at/pdf/eurosys2011-nightingale.pdf

## Slide 7: General Feedback on Project Proposals

## Slide 8: Overall Feedback on Project Proposals
Drive for becoming more concrete in the ideas
And, be more ambitious
And, be more thorough in related work (do not limit yourself only the papers we suggest)
You will get more detailed, per-proposal feedback from us

## Slide 9: Next Steps in Projects
Next steps are:
  1. Do a thorough literature search in your area
  Go deeper. Find and cite the seminal works as well as recent works. Increase the scholarship.
  2. Make the ideas and mechanisms more concrete
  3. Develop and understand the means for testing your ideas

## Slide 10: Next Week Recitation Plan
Present your revised proposal to get more feedback
10 minutes per group max

## Slide 11: General Feedback on Reviews

## Slide 12: Feedback on Reviews
Many reviews are very good quality
Avoid being
  Too terse: show the depth of your thinking
  Too critical: evaluate the positive contribution of each paper
Evaluate each paper considering when it was written
  Example: The first cache paper did not consider alternative replacement policies
    A paper cannot do everything: there is no perfect paper
Develop more ideas after reading each paper

## Slide 13: Rethinking Memory System Design (Continued)

## Slide 14: Solution 3: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 15: One Option: DRAM as a Cache for PCM
PCM is main memory; DRAM caches memory rows/blocks
  Benefits: Reduced latency on DRAM cache hit; write filtering
Memory controller hardware manages the DRAM cache
  Benefit: Eliminates system software overhead
Three issues:
  What data should be placed in DRAM versus kept in PCM?
  What is the granularity of data movement?
  How to design a low-cost hardware-managed DRAM cache?
Two idea directions:
  Locality-aware data placement [Yoon+ , ICCD 2012]
  Cheap tag stores and dynamic granularity [Meza+, IEEE CAL 2012]

## Slide 16: DRAM as a Cache for PCM
Goal: Achieve the best of both DRAM and PCM/NVM
  Minimize amount of DRAM w/o sacrificing performance, endurance
  DRAM as cache to tolerate PCM latency and write bandwidth
  PCM as main memory to provide large capacity at good cost and power
DATA
PCM Main Memory
DATA
T
DRAM Buffer
PCM Write Queue
T=Tag-Store
Processor
Flash
Or
HDD
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 17: Write Filtering Techniques
Lazy Write: Pages from disk installed only in DRAM, not PCM
Partial Writes: Only dirty lines from DRAM page written back
Page Bypass: Discard pages with poor reuse on DRAM eviction
Qureshi et al., “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Processor
DATA
PCM Main Memory
DATA
T
DRAM Buffer
Flash
Or
HDD

## Slide 18: Results: DRAM as PCM Cache (I)
Simulation of 16-core system, 8GB DRAM main-memory at 320 cycles, HDD (2 ms) with Flash (32 us) with Flash hit-rate of 99%
Assumption: PCM 4x denser, 4x slower than DRAM
DRAM block size = PCM page size (4kB)
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.
Notes: Workloads:
Database workloads & Data parallel kernels
1. Database workloads: db1 and db2
2. Unix utilities: qsort and binary search
3. Data Mining : K-means and Gauss Seidal
4. Streaming: DAXPY and Vector Dot Product

## Slide 19: Results: DRAM as PCM Cache (II)
PCM-DRAM Hybrid performs similarly to similar-size DRAM
Significant power and energy savings with PCM-DRAM Hybrid
Average lifetime: 9.7 years (no guarantees)
Qureshi+, “Scalable high performance main memory system using phase-change memory technology,” ISCA 2009.

## Slide 20: Hybrid Memory: A Closer Look
MC
MC
DRAM
(small capacity cache)
PCM (large capacity store)
CPU
Memory channel
Bank
Bank
Bank
Bank
Row buffer
Notes: Here’s a closer look at a hybrid memory system employing both DRAM and PCM.
Typically, the DRAM is used as a small capacity cache, and the PCM is used as a large capacity store.
When the processor needs data, it will first look to see if the data is in DRAM. If the data is indeed in DRAM, the processor will retrieve the data from there. If the data is not in DRAM, the processor will retrieve the data from PCM.
Both DRAM and PCM are organized into banks that are capable of operating independently. Also, in each bank, there are peripheral circuitries known as the row buffers.

## Slide 21: Key Observation
Row buffers exist in both DRAM and PCM
  Row hit latency similar in DRAM & PCM [Lee+ ISCA’09]
  Row miss latency small in DRAM, large in PCM
Place data in DRAM which
  is likely to miss in the row buffer (low row buffer locality) miss penalty is smaller in DRAM
  AND
  is reused many times  cache only the data worth the movement cost and DRAM space
Notes: Our key observation is that row buffers exist in both DRAM and PCM.
Row hit latency, which does not access the memory cell array, is similar in DRAM and PCM.
It is for a row miss that the memory access latency is small in DRAM and large in PCM.
Therefore we would like to place data in DRAM which:
Is likely to miss in the row buffer, which we call as having low row buffer locality, since the row buffer miss penalty is small in DRAM than it is in PCM.
And we would like to place data in DRAM which is reused many times, so that we cache only the data that is worth the movement cost.

## Slide 22: Hybrid vs. All-PCM/DRAM [ICCD’12]
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
31% better performance than all PCM,
within 29% of all DRAM performance
31%
29%
Yoon+, “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 23: For More on Hybrid Memory Data Placement
HanBin Yoon, Justin Meza, Rachata Ausavarungnirun, Rachael Harding, and Onur Mutlu, "Row Buffer Locality Aware Caching Policies for Hybrid Memories" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (pptx) (pdf)

## Slide 24: The Problem with Large DRAM Caches
A large DRAM cache requires a large metadata (tag + block-based information) store
How do we design an efficient DRAM cache?
DRAM
PCM
CPU
(small, fast cache)
(high capacity)
Mem Ctlr
Mem Ctlr
LOAD X
Access X
Metadata:
X  DRAM
X

## Slide 25: Idea 1: Tags in Memory
Store tags in the same row as data in DRAM
  Store metadata in same row as their data
  Data and metadata can be accessed together
Benefit: No on-chip tag storage overhead
Downsides:
  Cache hit determined only after a DRAM access
  Cache hit requires two DRAM accesses
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 26: Idea 2: Cache Tags in SRAM
Recall Idea 1: Store all metadata in DRAM
  To reduce metadata storage overhead
Idea 2: Cache in on-chip SRAM frequently-accessed metadata
  Cache only a small amount to keep SRAM size small

## Slide 27: Idea 3: Dynamic Data Transfer Granularity
Some applications benefit from caching more data
  They have good spatial locality
Others do not
  Large granularity wastes bandwidth and reduces cache utilization
Idea 3: Simple dynamic caching granularity policy
  Cost-benefit analysis to determine best DRAM cache block size
  Group main memory into sets of rows
  Some row sets follow a fixed caching granularity
  The rest of main memory follows the best granularity
    Cost–benefit analysis: access latency versus number of cachings
    Performed every quantum

## Slide 28: TIMBER Tag Management
A Tag-In-Memory BuffER (TIMBER)
  Stores recently-used tags in a small amount of SRAM
Benefits: If tag is cached:
  no need to access DRAM twice
  cache hit determined quickly
Tag0
Tag1
Tag2
Row0
Tag0
Tag1
Tag2
Row27
Row Tag
LOAD X
Cache block 2
Cache block 0
Cache block 1
DRAM row
Tag0
Tag1
Tag2

## Slide 29
Metadata Storage Performance
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
(Ideal)

## Slide 30
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
-48%
Performance degrades due to increased metadata lookup access latency
(Ideal)

## Slide 31
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
36%
Increased row locality reduces average memory access latency
(Ideal)

## Slide 32
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER
 | 1 | 0.51631 | 0.70016 | 0.85785
Metadata Storage Performance
23%
Data with locality can access metadata at SRAM latencies
(Ideal)

## Slide 33
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
Dynamic Granularity Performance
10%
Reduced channel contention and improved spatial locality

## Slide 34
Chart: Normalized Weighted Speedup
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.51631 | 0.70016 | 0.85785 | 0.94487
TIMBER Performance
-6%
Reduced channel contention and improved spatial locality
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 35
Chart: Normalized Performance per Watt (for Memory System)
| SRAM | Region | TIM | TIMBER | TIMBER-Dyn
 | 1 | 0.73082 | 0.75384 | 0.89249 | 1.1769
TIMBER Energy Efficiency
Fewer migrations reduce transmitted data and channel contention
18%
Meza, Chang, Yoon, Mutlu, Ranganathan, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.

## Slide 36: More on Large DRAM Cache Design
Justin Meza, Jichuan Chang, HanBin Yoon, Onur Mutlu, and Parthasarathy Ranganathan, "Enabling Efficient and Scalable Hybrid Memories Using Fine-Granularity DRAM Cache Management" IEEE Computer Architecture Letters (CAL), February 2012.

## Slide 37: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ) device
  Reference layer: Fixed magnetic orientation
  Free layer: Parallel or anti-parallel
Magnetic orientation of the free layer determines logical state of device
  High vs. low resistance
Write: Push large current through MTJ to change orientation of free layer
Read: Sense current flow
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 38: STT-MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 39: Architected STT-MRAM as Main Memory
4-core, 4GB main memory, multiprogrammed workloads
~6% performance loss, ~60% energy savings vs. DRAM
Chart: Performance vs. DRAM
STT-RAM (base) | 0.95574 | 0.91812 | 0.93435 | 0.95579 | 0.95738 | 0.92083 | 0.95404 | 0.93019 | 0.95413 | 0.94507 | 0.92103 | 0.94061
STT-RAM (opt) | 0.96014 | 0.91453 | 0.9443 | 0.95632 | 0.95951 | 0.92092 | 0.95948 | 0.93564 | 0.96003 | 0.94574 | 0.93546 | 0.94473
Chart: Energy vs. DRAM
| mpmix0 | mpmix1 | mpmix2 | mpmix3 | mpmix4 | mpmix5 | mpmix6 | mpmix7 | mpmix8 | mpmix9 | mpmix10 | Average
ACT+PRE | 0.30175 | 0.27646 | 0.37425 | 0.32119 | 0.33973 | 0.34883 | 0.36197 | 0.2603 | 0.33524 | 0.39385 | 0.32655 | 0.33092
WB | 0.018529 | 0.027397 | 0.013518 | 0.015979 | 0.022233 | 0.018649 | 0.015872 | 0.025826 | 0.01687 | 0.016362 | 0.015008 | 0.018749
RB | 0.01752 | 0.014162 | 0.010281 | 0.018781 | 0.023665 | 0.010148 | 0.024161 | 0.016986 | 0.013315 | 0.012743 | 0.010166 | 0.01563
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 40: Other Opportunities with Emerging Technologies
Merging of memory and storage
  e.g., a single interface to manage all data
New applications
  e.g., ultra-fast checkpoint and restore
More robust system design
  e.g., reducing data loss
Processing tightly-coupled with memory
  e.g., enabling efficient search and filtering

## Slide 41: Coordinated Memory and Storage with NVM (I)
The traditional two-level storage model is a bottleneck with NVM
  Volatile data in memory  a load/store interface
  Persistent data in storage  a file system interface
  Problem: Operating system (OS) and file system (FS) code to locate, translate, buffer data become performance and energy bottlenecks with fast NVM stores
Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …
Persistent (e.g., Phase-Change)
Memory

## Slide 42: Coordinated Memory and Storage with NVM (II)
Goal: Unify memory and storage management in a single unit to eliminate wasted work to locate, transfer, and translate data
  Improves both energy and performance
  Simplifies programming model as well
Unified Memory/Storage
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 43: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 44: The Persistent Memory Manager (PMM)
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Persistent objects
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 45: Performance Benefits of a Single-Level Store
~5X
~24X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 46: Energy Benefits of a Single-Level Store
~5X
~16X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 47: Some Principles for Memory Scaling

## Slide 48: Principles for Memory Scaling (So Far)
Better cooperation between devices and the system
  Expose more information about devices to upper layers
  More flexible interfaces
Better-than-worst-case design
  Do not optimize for the worst case
  Worst case should not determine the common case
Heterogeneity in design (specialization, asymmetry)
  Enables a more efficient design (No one size fits all)
These principles are coupled

## Slide 49: Summary: Memory Scaling
Memory scaling problems are a critical bottleneck for system performance, efficiency, and usability
New memory architectures
  A lot of hope in fixing DRAM
Enabling emerging NVM technologies
  A lot of hope in hybrid memory systems and single-level stores
System-level memory/storage QoS
  A lot of hope in designing a predictable system
Three principles are essential for scaling
  Software/hardware/device cooperation
  Better-than-worst-case design
  Heterogeneity (specialization, asymmetry)

## Slide 50
18-740: Computer Architecture Recitation 5:
Main Memory Scaling Wrap-Up
Prof. Onur Mutlu
Carnegie Mellon University
Fall 2015
September 29, 2015
Notes: 50

## Slide 51: Another Discussion: NAND Flash Scaling
Onur Mutlu, "Error Analysis and Management for MLC NAND Flash Memory" Technical talk at Flash Memory Summit 2014 (FMS), Santa Clara, CA, August 2014. Slides (ppt) (pdf)
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.

## Slide 52: Experimental Infrastructure (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
3x-nm
NAND Flash
[Cai+, DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015]