## Slide 1
Timothy G. Rogers
Daniel R. Johnson
Mike O’Connor
Stephen W. Keckler
A Variable Warp-Size Architecture

## Slide 2: Contemporary GPU
Massively Multithreaded
10,000’s of threads concurrently executing on 10’s of Streaming Multiprocessors (SM)

## Slide 3: Contemporary Streaming Multiprocessor (SM)
1,000’s of schedulable threads
Amortize front end and memory overheads by grouping threads into warps.
  Size of the warp is fixed based on the architecture

## Slide 4: Contemporary GPU Software
Regular structured computation
Predictable access and control flow patterns
Can take advantage of HW amortization for increased performance and energy efficiency
Execute Efficiently on a GPU Today
Graphics Shaders
Matrix Multiply
…

## Slide 5: Forward-Looking GPU Software
Still Massively Parallel
Less Structured
  Memory access and control flow patterns are less predictable
Execute efficiently on a GPU today
Graphics Shaders
Matrix Multiply
…
Less efficient on today’s GPU
Raytracing
Molecular Dynamics
Object Classification
…

## Slide 6: Divergence: Source of Inefficiency
Regular hardware that amortizes front end and overhead
Irregular software with many different control flow paths and less predicable memory accesses.
Branch Divergence
Memory Divergence
…
if (…) {
…
}
…
Load R1, 0(R2)
Can cut function unit utilization to 1/32.
32- Wide
32- Wide
Main Memory
Instruction may wait for 32 cache lines

## Slide 7: Irregular “Divergent” Applications: Perform better with a smaller warp size
…
if (…) {
…
}
…
Allows more threads to proceed concurrently
Branch Divergence
Memory Divergence
Load R1, 0(R2)
Increased function unit utilization
Main Memory
Each instruction waits on fewer accesses

## Slide 8: Negative effects of smaller warp size
Less front end amortization
  Increase in fetch/decode energy
Negative performance effects
  Scheduling skew increases pressure on the memory system

## Slide 9: Regular “Convergent” Applications: Perform better with a wider warp
32- Wide
Load R1, 0(R2)
Load R1, 0(R2)
Main Memory
GPU memory coalescing
One memory system request can service all 32 threads
Smaller warps: Less coalescing
Main Memory
8 redundant memory accesses – no longer occurring together

## Slide 10: Performance vs. Warp Size
Chart: IPC normalized to warp size 32
Convergent Applications
Warp-Size Insensitive Applications
Divergent Applications
165 Applications

## Slide 11: Goals
Convergent Applications
  Maintain wide-warp performance
  Maintain front end efficiency
Warp Size Insensitive Applications
  Maintain front end efficiency
Divergent Applications
  Gain small warp performance
Set the warp size based on the executing application

## Slide 12: Sliced Datapath + Ganged Scheduling
Split the SM datapath into narrow slices.
  Extensively studied 4-thread slices
Gang slice execution to gain efficiencies of wider warp.
Slices can execute independently
Slices share an L1
I-Cache and Memory Unit

## Slide 13: Initial operation
Slices begin execution in ganged mode
  Mirrors the baseline 32-wide warp system
Question: When to break the gang?
Ganging unit drives the slices
Instructions are fetched and decoded once

## Slide 14: Breaking Gangs on Control Flow Divergence
PCs common to more than one slice form a new gang
Slices that follow a unique PC in the gang are transferred to independent control
Unique PCs: no longer controlled by ganging unit
Observes different PCs from each slice

## Slide 15: Breaking Gangs on Memory Divergence
Latency of accesses from each slice can differ
Evaluated several heuristics on breaking the gang when this occurs
Hits in L1
Goes to memory

## Slide 16: Gang Reformation
Performed opportunistically
  Ganging unit checks for gangs or independent slices at the same PC
  Forms them into a gang
Independent BUT at the same PC
Ganging unit re-gangs them
More details in the paper

## Slide 17: Methodology
In House, Cycle-Level Streaming Multiprocessor Model
  1 In-order core
  64KB L1 Data cache
  128KB L2 Data Cache (One SM’s worth)
  48KB Shared Memory
  Texture memory unit
  Limited BW memory system
  Greedy-Then-Oldest (GTO) Issue Scheduler

## Slide 18: Configurations
Warp Size 32 (WS 32)
Warp Size 4 (WS 4)
Inelastic Variable Warp Sizing (I-VWS)
  Gangs break on control flow divergence
  Are not reformed
Elastic Variable Warp Sizing (E-VWS)
  Like I-VWS, except gangs are opportunistically reformed
Studied 5 applications from each category in detail
Paper Explores Many More Configurations

## Slide 19: Divergent Application Performance
Chart: IPC normalized to warp size 32
| CoMD | Lighting | GamePhysics | ObjClassifier | Raytracing | HMEAN-DIV | Divergent Applications
WS 32 | 1 | 1 | 1 | 1 | 1 | 1
WS 4 | 1.28 | 1.32 | 1.2 | 1.63 | 1.62 | 1.3878
I-VWS | 1.27 | 1.28 | 1.13 | 1.57 | 1.6 | 1.3457
E-VWS | 1.17 | 1.16 | 1.13 | 1.54 | 1.51 | 1.2777
Warp Size 4
I-VWS: Break on CF Only
E-VWS: Break + Reform

## Slide 20: Divergent Application Fetch Overhead
Chart: Avg. Fetches Per Cycle
| CoMD | Lighting | GamePhysics | ObjClassifier | Raytracing | AVG-DIV | Divergent Applications
WS 32 | 0.8 | 1 | 0.9 | 1 | 0.5 | 0.84
WS 4 | 5.3 | 7.3 | 6.5 | 5.5 | 3.8 | 5.68
I-VWS | 4.9 | 2.6 | 1.1 | 1.6 | 2 | 2.44
E-VWS | 1.3 | 1.1 | 1.1 | 1.1 | 1 | 1.12
Warp Size 4
I-VWS: Break on CF Only
Used as a proxy for energy consumption
E-VWS: Break + Reform

## Slide 21: Convergent Application Performance
Chart: IPC normalized to warp size 32
| Game 1 | MatrixMultiply | Game 2 | FeatureDetect | Radix Sort | HMEAN-CON | Convergent Applications
WS 32 | 1 | 1 | 1 | 1 | 1 | 1
WS 4 | 0.79 | 0.81 | 0.58 | 0.82 | 0.75 | 0.73775
I-VWS | 1.01 | 1 | 1 | 0.99 | 0.99 | 0.99794
E-VWS | 1 | 1 | 1 | 0.99 | 0.99 | 0.99598
Warp Size 4
I-VWS: Break on CF Only
Warp-Size Insensitive Applications Unaffected
E-VWS: Break + Reform

## Slide 22: Convergent/Insensitive Application Fetch Overhead
Chart: Avg. Fetches Per Cycle
| Image Proc. | Game 3 | Convolution | Game 4 | FFT | AVG-WSI | Game 1 | MatrixMultiply | Game 2 | FeatureDetect | Radix Sort | AVG-CON | Warp-Size Insensitive Applications | Convergent Applications
WS 32 | 1 | 0.9 | 1 | 1 | 0.9 | 0.96 | 1 | 0.8 | 0.6 | 0.8 | 0.9 | 0.82
WS 4 | 8 | 6.9 | 7.9 | 8 | 7.2 | 7.6 | 6.1 | 5.1 | 2.8 | 5.1 | 5.6 | 4.94
I-VWS | 1 | 0.9 | 1 | 1 | 0.9 | 0.96 | 1.1 | 0.8 | 0.6 | 0.8 | 1.1 | 0.88
E-VWS | 1 | 0.9 | 1 | 1 | 0.9 | 0.96 | 1 | 0.8 | 0.6 | 0.8 | 1.1 | 0.86
Warp Size 4
I-VWS: Break on CF Only
E-VWS: Break + Reform

## Slide 23: 165 Application Performance
Convergent Applications
Divergent Applications
Chart: IPC normalized to warp size 32
Warp-Size Insensitive Applications

## Slide 24: Related Work
Compaction/Formation
Subdivision/Multipath
Improve Function Unit Utilization
Decrease Thread Level Parallelism
Decreased Function Unit Utilization
Increase Thread Level Parallelism
Variable Warp Sizing
Improve Function Unit Utilization
Increase Thread Level Parallelism
Area Cost
Area Cost
Area Cost
VWS Estimate:
5% for 4-wide slices
2.5% for 8-wide slices

## Slide 25: Conclusion
Explored space surrounding warp size and perfromance
Vary the size of the warp to meet the depends of the workload
  35% performance improvement on divergent apps
  No performance degradation on convergent apps
Narrow slices with ganged execution
  Improves both SIMD efficiency and thread-level parallelism
Questions?

## Slide 26: Managing DRAM Latency Divergence in Irregular GPGPU Applications
Niladrish Chatterjee
Mike O’Connor
Gabriel H. Loh
Nuwan Jayasena
Rajeev Balasubramonian

## Slide 27: Irregular GPGPU Applications
Conventional GPGPU workloads access vector or matrix-based data structures
  Predictable strides, large data parallelism
Emerging Irregular Workloads
  Pointer-based data-structures & data-dependent memory accesses
  Memory Latency Divergence on SIMT platforms
  Warp-aware memory scheduling to reduce DRAM latency divergence

## Slide 28: SIMT Execution Overview
GDDR5
Channel
L1
Warp 1
Warp Scheduler
SIMD Lanes
Memory Port
Warp 2
Warp 3
Warp N
SIMT Core
SIMT Core
SIMT Core
I
N
T
E
R
C
O
N
N
E
C
T
L2 Slice
Memory Controller
GDDR5
Channel
Memory Partition
THREADS
Memory Partition
Warps
GDDR5
GDDR5
L2 Slice
Memory Controller
Lockstep execution
Warp stalled on memory access

## Slide 29: Memory Latency Divergence
Coalescer has limited efficacy in irregular workloads
Partial hits in L1 and L2
  1st source of latency divergence
DRAM requests can have varied latencies
  Warp stalled for last request
DRAM Latency Divergence
Load Inst
SIMD Lanes (32)
Access Coalescing Unit
L1
L2
GDDR5

## Slide 30: GPU Memory Controller (GMC)
Optimized for high throughput
Harvest channel and bank parallelism
  Address mapping to spread cache-lines across channels and banks.
Achieve high row-buffer hit rate
  Deep queuing
  Aggressive reordering of requests for row-hit batching
Not cognizant of the need to service requests from a warp together
  Interleave requests from different warps leading to latency divergence

## Slide 31: Warp-Aware Scheduling
SM 1
SM 2
A: LD
A
A
A
A
B
B
B
B
MC
A: Use
Baseline
GMC Scheduling
A
B
A
A
A
B: Use
B
B
B
Stall Cycles
Stall Cycles
Warp-Aware Scheduling
A
A
A
B
B
A
B
B
A: Use
Stall Cycles
B: LD
Reduced Average Memory Stall Time

## Slide 32: Impact of DRAM Latency Divergence
If all requests from a warp were to be returned in perfect sequence from the DRAM –
~40% improvement.
If there was only 1 request per warp – 5X improvement.

## Slide 33: Key Idea
Form batches of requests from each warp
  warp-group
Schedule all requests from a warp-group together
Scheduling algorithm arbitrates between warp-groups to minimize average stall-time of warps

## Slide 34: Controller Design

## Slide 35: Controller Design

## Slide 36: Warp-Group Scheduling : Single Channel
Pending Warp-Groups
Warp-group priority table
Transaction Scheduler
# of reqs in warp-group
Row hit/miss status of reqs
Queuing delay in cmd queues
Pick warp-group with lowest runtime
Each Warp-Group assigned a priority
  Reflects completion time of last request
Higher Priority to
  Few requests
  High spatial locality
  Lightly loaded banks
Priorities updated dynamically
Transaction Scheduler picks warp-group with lowest run-time
  Shortest-job-first based on actual service time

## Slide 37: WG-scheduling
Latency Divergence
Ideal
Bandwidth Utilization
GMC Baseline
WG

## Slide 38: Multiple Memory Controllers
Channel level parallelism
  Warp’s requests sent to multiple memory channels
  Independent scheduling at each controller
Subset of warp’s requests can be delayed at one or few memory controllers
Coordinate scheduling between controllers
  Prioritize warp-group that has already been serviced at other controllers
  Coordination message broadcast to other controllers on completion of a warp-group.

## Slide 39: Warp-Group Scheduling : Multi-Channel
Pending Warp-Groups
Priority Table
Transaction Scheduler
# of reqs in warp-group
Row hit/miss status of reqs
Queuing delay in cmd queues
Pick warp-group with lowest runtime
Status of Warp-group in other channels
Periodic messages to other channels about completed warp-groups

## Slide 40: WG-M Scheduling
Latency Divergence
Ideal
Bandwidth Utilization
GMC Baseline
WG
WG-M

## Slide 41: Bandwidth-Aware Warp-Group Scheduling
Warp-group scheduling negatively affects bandwidth utilization
  Reduced row-hit rate
Conflicting objectives
  Issue row-miss request from current warp-group
  Issue row-hit requests to maintain bus utilization
Activate and Precharge idle cycles
  Hidden by row-hits in other banks
Delay row-miss request to find the right slot

## Slide 42: Bandwidth-Aware Warp-Group Scheduling
The minimum number of row-hits needed in other banks to overlap (tRTP+tRP+tRCD)
  Determined by GDDR timing parameters
  Minimum efficient row burst (MERB)
Stored in a ROM looked up by Transaction Scheduler
More banks with pending row-hits
  smaller MERB
Schedule row-miss after MERB row-hits have been issued to bank

## Slide 43: WG-Bw Scheduling
Latency Divergence
Ideal
Bandwidth Utilization
GMC Baseline
WG
WG-M
WG-Bw

## Slide 44: Warp-Aware Write Draining
Writes drained in batches
  starts at High_Watermark
Can stall small warp-groups
When WQ reaches a threshold (lower than High_Watermark)
  Drain singleton warp-groups only
Reduce write-induced latency

## Slide 45: WG-scheduling
Latency Divergence
Ideal
Bandwidth Utilization
GMC Baseline
WG
WG-M
WG-Bw
WG-W

## Slide 46: Methodology
GPGPUSim v3.1 : Cycle Accurate GPGPU simulator
USIMM v1.3 : Cycle Accurate DRAM Simulator
  modified to model GMC-baseline & GDDR5 timings
Irregular and Regular workloads from Parboil, Rodinia, Lonestar, and MARS.
SM Cores | 30
Max Threads/Core | 1024
Warp Size | 32 Threads/warp
L1 / L2 | 32KB / 128 KB
DRAM | 6Gbps GDDR5
DRAM Channels Banks | 6 Channels 16 Banks/channel

## Slide 47: Performance Improvement
Chart: IPC Normalized to Baseline
| WG | WG-M | WG-Bw | WG-W
Column1 | 0.034 | 0.062 | 0.084 | 0.101
Reduced Latency Divergence
Restored Bandwidth Utilization

## Slide 48: Impact on Regular Workloads
Effective coalescing
High spatial locality in warp-group
WG scheduling works similar to GMC-baseline
  No performance loss
WG-Bw and WG-W provide
  Minor benefits

## Slide 49: Energy Impact of Reduced Row Hit-Rate
Scheduling Row-misses over Row-hits
  Reduces the row-buffer hit rate 16%
In GDDR5, power consumption dominated by I/O.
Increase in DRAM power negligible compared to execution speed-up
  Net improvement in system energy
Chart: GDDR5 Energy/bit
| Baseline | WG-Bw
I/O | 18.1 | 18.1
Row | 8.4151 | 9.7615
Column | 6.21 | 6.21
Control | 0.31 | 0.31
DLL | 0.44 | 0.44
Background | 0.88 | 0.88

## Slide 50: Conclusions
Irregular applications place new demands on the GPU’s memory system
Memory scheduling can alleviate the issues caused by latency divergence
Carefully orchestrating the scheduling of commands can help regain the bandwidth lost by warp-aware scheduling
Future techniques must also include the cache-hierarchy in reducing latency divergence

## Slide 51: Thanks !

## Slide 52: Backup Slides

## Slide 53: Performance Improvement : IPC

## Slide 54: Average Warp Stall Latency

## Slide 55: DRAM Latency Divergence

## Slide 56: Bandwidth Utilization

## Slide 57: Memory Controller Microarchitecture

## Slide 58: Warp-Group Scheduling
Every batch assigned a priority-score
  completion time of the longest request
Higher priority to warp groups with
  Few requests
  High spatial locality
  Lightly loaded banks
Priorities updated after each warp-group scheduling
Warp-group with lowest service time selected
  Shortest-job-first based on actual service time, not number of requests

## Slide 59: Priority-Based Cache Allocation in Throughput Processors
Dong Li*†, Minsoo Rhu*§†, Daniel R. Johnson§, Mike O’Connor§†, Mattan Erez†, Doug Burger‡ , Donald S. Fussell† and Stephen W. Keckler§†
*First authors Li and Rhu have made equal contributions to this work and are listed alphabetically
†
§
‡

## Slide 60: Introduction
Graphics Processing Units (GPUs)
  General purpose throughput processors
  Massive thread hierarchy, warp=32 threads
Challenge:
  Small caches + many threads  contention + cache thrashing
Prior work: throttling thread level parallelism (TLP)
  Problem 1: under-utilized system resources
  Problem 2: unexplored cache efficiency

## Slide 61: Motivation: Case Study (CoMD)
Best Throttled
max TLP (default)
Throttling improves performance
Observation 2:
Unexplored cache efficiency
Observation 1:
Resource under-utilized
Throttling
Throttling
Throttling

## Slide 62: Motivation
    Throttling
      Tradeoff between cache efficiency and parallelism.
      # Active Warps = # Warps Allocating Cache
    Idea
  Decoupling cache efficiency from parallelism
# Active Warps
# Warps Allocating Cache
Throttling
Baseline
Unexplored

## Slide 63: Our Proposal: Priority Based Cache Allocation (PCAL)

## Slide 64: Baseline
Standard operation
Regular threads: threads have all capabilities, operate as usual (full access to the L1 cache)
Regular
Threads
Warp 0
Warp 1
Warp 2
Warp 3
Warp 4
Warp n-1
Notes: Baseline line

## Slide 65: TLP Throttling
TLP reduced to improve performance
Regular threads: threads have all capabilities, operate as usual (full access to the L1 cache)
Second subset: prevented from polluting L1 cache (fills bypass)
Throttled threads: throttled (not runnable)
Regular
Threads
Throttled Threads
Warp 0
Warp 1
Warp 2
Warp 3
Warp 4
Warp n-1
Notes: Throttling

## Slide 66: Proposed Solution: PCAL
Three subsets of threads
Regular threads: threads have all capabilities, operate as usual (full access to the L1 cache)
Regular
Threads
Non-polluting Threads
Throttled Threads
Warp 0
Warp 1
Warp 2
Warp 3
Warp 4
Warp n-1
Non-polluting threads: runnable, but prevented from polluting L1 cache
Throttled threads: throttled (not runnable)

## Slide 67: Proposed Solution: PCAL
Tokens for privileged cache access
Tokens grant capabilities or privileges to some threads
Threads with tokens are allowed to allocate and evict L1 cache lines
Threads without tokens can read and write, but not allocate or evict, L1 cache lines
Regular
Threads
Non-polluting Threads
Throttled Threads
Warp 0
Warp 1
Warp 2
Warp 3
Warp 4
Warp n-1
1
1
0
0
0
Priority Token Bit

## Slide 68: Proposed solution: Static PCAL
HW implementation: simplicity
  Scheduler manages per-warp token bits
  Token bits sent with memory requests
Policies: token assignment
  Assign at warp launch, release at termination
  Re-assigned to oldest token-less warp
Parameters supplied by software prior to kernel launch
Enhanced scheduler operation
Regular
Threads
Non-polluting Threads
Throttled Threads
Warp 0
Warp 1
Warp 2
Warp 3
Warp 4
Warp n-1
Warp Scheduler
Token Assignment
1
1
0
0
0
Priority Token Bit
Scheduler Status Bits

## Slide 69: Two Optimization Strategies to exploit the 2-D (#Warps, #Tokens) search space
# Active Warps (#Warps)
# Warps Allocating Cache
(#Tokens)
Throttling
(#Warps = #Tokens )
Baseline
1. Increasing TLP (ITLP)
  Adding non-polluting warps
  Without hurting regular warps
Resource under-utilized
ITLP
Unexplored cache efficiency
MTLP
2. Maintaining TLP (MTLP)
  Reduce #Token to increase the efficiency
  Without decreasing TLP

## Slide 70: Proposed Solution: Dynamic PCAL
Decide parameters at run time
  Choose MTLP/ITLP based on resource usage performance counter
  For MTLP: search #Tokens in parallel
  For ITLP: search #Warps in sequential
Please refer to our paper for more details

## Slide 71: Evaluation
Simulation: GPGPU-Sim
  Open source academic simulator, configured similar to Fermi (full-chip)
Benchmarks
  Open source GPGPU suites: Parboil, Rodinia, LonestarGPU. etc
  Selected benchmark subset shows sensitivity to cache size

## Slide 72: MTLP Example (CoMD)
MTLP: reducing #Tokens, keeping #Warps =6
Best Throttled
PCAL with MTLP
MTLP
MTLP
MTLP

## Slide 73: ITLP Example (Similarity-Score)
ITLP: increasing #Warps, keeping #Tokens=2
Best Throttled
PCAL with ITLP
ITLP
ITLP
ITLP

## Slide 74: PCAL Results Summary
Baseline: best throttled results
Performance improvement: Static-PCAL: 17%, Dynamic-PCAL: 11%

## Slide 75: Conclusion
Existing throttling approach may lead to two problems:
  Resources underutilization
  Unexplored cache efficiency
We propose PCAL, a simple mechanism to rebalance cache efficiency and parallelism
  ITLP: increases parallelism without hurting regular warps
  MTLP: alleviates cache thrashing while maintaining parallelism
Throughput improvement over best throttled results
  Static PCAL: 17%
  Dynamic PCAL: 11%

## Slide 76: Questions

## Slide 77: Unlocking bandwidth for GPUS in cc-numa systems
Neha Agarwal*
David Nellans
Mike O’Connor
Stephen W. Keckler
Thomas F. Wenisch*
NVIDIA
University of Michigan*
(Major part of this work was done when Neha Agarwal was an intern at NVIDIA)
HPCA-2015
Notes: Hi everyone, I am Neha. Today I will talk about techniques for exploiting memory BW for upcoming GPU memory architectures.

## Slide 78: Evolving gpu memory system
CUDA 1.0-5.x
CUDA 6.0+: Current
Future
cudaMemcpy
Programmer controlled copying to GPU memory
Unified virtual memory
Run-time controlled copying  Better productivity
CPU-GPU cache-coherent
high BW interconnect
How to best exploit full BW while maintaining programmability?
Roadmap
GDDR5
GPU
CPU
200 GB/s
80 GB/s
80 GB/s
NVLink
(Cache Coherent)
PCI-E
15.8 GB/s
DDR4
HPCA-2015
Notes: Let me first take you through the evolution of GPU memory system via a roadmap.
A typical CPU-GPU system today is connected by a PCI-E link. The GPU is connected to high bandwidth GDDR memory and CPU is connected to high-capacity but lower-bandwidth DDR memory.
Example system
In the legacy systems from first generation of CUDA uptill CUDA 5, programming model was such that GPU could only access the GDDR memory attached to it. Programmer was responsible to identify the data accessed by the GPU and manually transfer it to the GDDR memory using cudaMemcpy calls. Such a programming model demands high effort on part of the programmer.
Moving forward CUDA 6.0 onwards Unified virtual memory was introduced, wherein the programmer is no longer required to make explicit data copies. Using the same hardware as in the legacy systems runtime software performs on-demand data copying to the GPU memory. Although this memory abstraction had a significant impact on improving programmer productivity still on-demand copying slows down the running program.
Moving further ahead, we anticipate that CPU & GPU will become cache coherent. As announced by the GPU vendors CPU & GPU will be connected via a high BW interconnect such as NVIDIA’s NVLink. For the first time GPU will be able to transparently access the CPU memory. This future system provides various opportunities for performance enhancement as GPU can now use BW from both CPU and GPU memories. The big question here is how to exploit the full system BW in the best possible way without burdening the programmer to worry about the data placement or copying decisions.

## Slide 79: Design goals & Opportunities
Simple programming model:
  No need for explicit data copying
Exploit full DDR + GDDR BW
  Additional 30% BW via NVLink
  Crucial to BW sensitive GPU apps
Legacy CUDA
UVM
PCI-E
Target
80
200
280
Total Bandwidth (GB/s)
NVLink
CC-NUMA BW
15.8
Design intelligent dynamic page migration policies
to achieve both these goals
HPCA-2015
Notes: Let us look at the design goals and opportunities of this future anticipated CPU-GPU system.
The key design goal is to have a simple programming model where programmer is not responsible to manage the memory. Programmer should simply be able to declare the data structures in the CPU memory and should not have to worry about exploiting different properties of the memory system to get performance. Underlying system should make decisions on how to best utilize BW and capacity of different types of memory technologies available in the system.
GPUs are designed to hide memory latency but demand good BW utilization to achieve high throughput. Hence, the second important design goal is to exploit full BW from both the DDR + GDDR memory, as GPU applications are highly sensitive to the memory BW. When CPU and GPU are connected through PCI-E link the additional interconnect BW is just 8% of the total BW. But in the future as CPU and GPU will be connected via high BW interconnect such as NVLink this additional BW will be increased to be 30% of the total BW, which is a significant fraction to leave on the table. As a programmer I would like to be able to utilize both 200GB/s form the GDDR memory and 80GB/s from the cache coherent link without have to actually worry about how to do it.
So, for programmability data allocation starts from the CPU memory and for performance we need to design an intelligent dynamic page migration policy which will exploit full DDR + GDDR BW
Let us try to understand the challenges posed by this future GPU memory system. Cache-coherence enables GPU to transparently access the data residing in the CPU memory. It frees programmer/SW runtime system from making explicit data copies. Its a big advantage from the programming model perspective. At the same time cache coherence enable finer-grained sharing between CPU & GPU.
However, data placement into DDR vs GDDR memories drastically impact GPU throughput, as GPU workloads are highly sensitive to memory BW.
Can static placement solve the problem of making data placement decisions? But wait, do we need some a-priori information from the programmer to make effective decisions of placing what data where? I will talk more about it in our ASPLOS 2015 paper in Istanbul
The goal of this paper is to come with automated dynamic page migration schemes where GPU throughput is maximized by exploiting full DDR + GDDR BW without demanding programmer involvement. Programmer should be able to declare data structures in the CPU memory and forget about data management. An intelligent runtime system would be able to determine what and when to migrate pages among GDDR and DDR memories, which takes us to the contributions of this work.

## Slide 80: Bandwidth utilization
DDR4
GDDR5
GPU
CPU
200 GB/s
80 GB/s
NVLink
80 GB/s
Coherence-based accesses, no page migration
Wastes GPU memory BW
80
200
280
BW from CC
GPU Memory BW
Total System Memory BW
% of Migrated Pages to GPU Memory
Total Bandwidth (GB/s)
0
100
HPCA-2015
Notes: Now, let us look at the BW utilization as we start running an application on this system. On the left we will see how GPU accesses the data from the memory system and on the right we will see the BW utilization for those accesses.
For the sake of the programmability, all the data is allocated in the CPU memory to begin with. GPU can access this data from the CPU memory via cache coherence. Hence, the best BW utilization in such topology can be only 80GB/s, which is only 30% of the total system BW. We are not able to use 70% of the system BW which a a big lose from performance perspective.
With no page migrations this system will end up wasting high BW GPU memory.
Next, we move onto the future CC-NUMA system where CPU and GPU are connected through a high BW interconnect of 80GB/s. For the sake of programmability all the data structures reside in the CPU memory to start with. GPU can do coherence-based accesses and thus the total BW utilizes in this system will be 80GB/s. Clearly, with no page migration enabled from DDR to GDDR memory this system will end up wasting high BW GPU memory.

## Slide 81: Bandwidth utilization
DDR4
GDDR5
Dynamic migration can exploit the full system memory BW
GPU
CPU
200 GB/s
80 GB/s
NVLink
80 GB/s
Static Oracle: Place data in the ratio of memory bandwidths [ASPLOS’15]
80
200
280
Additional BW from CC
GPU Memory BW
Total System Memory BW
% of Migrated Pages to GPU Memory
Total Bandwidth (GB/s)
0
100
HPCA-2015
Notes: Remember, our goal here is to reach the peak BW as soon as possible. As pages are migrated to the GPU memory BW utilization will go up. We have observed that the best bandwidth utilization happens when the application data is spread across the GDDR and DDR memories in the ratio of their bandwidths. In our ASPLOS 2015 paper we will discuss more about the static placement policies. The goal of this work however is to dynamically migrate pages so that data is divided in the ratio of memory BW and thus GPU can concurrently access both the memories.
Distinguish ASPLOS from HPCA
Correct animation
How can we utilize both the CPU and the GPU memory BW? In our ASPLOS 2015 paper we will discuss about the static oracle placement that achieves the goal of maximizing BW utilization from both the memories. By placing data in the ratio of memory BW here it being 70:30% GPU can saturate both the memories and thus achieve the cumulative BW of 280GB/s. The goal of this work is to achieve this static oracle performance by dynamically migrating pages among DDR and GDDR memories.

## Slide 82: Bandwidth Utilization
Excessive migration leads to under-utilization of DDR BW
GDDR5
GPU
CPU
200 GB/s
80 GB/s
NVLink
80 GB/s
DDR4
80
200
280
Additional BW from CC
GPU Memory BW
Total System Memory BW
% of Migrated Pages to GPU Memory
Total Bandwidth (GB/s)
0
100
Migrate pages for optimal BW utilization
HPCA-2015
Notes: As more and more migration happen, a point comes where all the data is transferred to the GPU memory. In such a case GPU memory requests can only be served from GDDR memory. Excessive page migration leads to under-utilization of the CPU memory BW. Hence page migration policy should only migrate pages to unlock memory BW of both the DDR and the GDDR memories.
So, the take away from the above discussion is that we want to utilize both 200GB/s from GDDR memory and 80GB/s from DDR memory at the same time we do not programmer to worry about these decisions.
Let us try to understand how BW is utilized in the Legacy/Current CPU-GPU systems where either programmer/SW runtime copies data accessed by the GPU to the GDDR memory.
On the left we can see a GPU attached to the CPU through low BW PCI-E link. Any data accessed by the GPU has to be placed in the GDDR memory as this system is not CC, which means that DDR BW will not be used by the GPU. All the GPU accesses happen through 200GB/s attached memory. Therefore, the total BW utilization of this topology can be 200GB/s.

## Slide 83: contributions
Aggressively migrate pages upon First-Touch to GDDR memory
Pre-fetch neighbors of touched pages to reduce TLB shootdowns
Throttle page migrations when nearing peak BW
Intelligent Dynamic Page Migration
Dynamic page migration performs 1.95x better than no migration
Comes within 28% of the static oracle performance
6% better than Legacy CUDA
HPCA-2015
Notes: In this work, we have developed intelligent dynamic page migration policies that demands no programmer involvement. We aggressively migrate pages to the GDDR memory after a page has been accessed. We employ a technique to pre-fetch neighbors of already accessed pages to reduce TLB shootdowns. Finally, we throttle page migrations when BW utilization peaks as more migration lead to under-utilization of the CPU memory BW.
Our dynamic page migration policy performs 1.95 times better than no migration case, is within 28% of the static oracle performance and is 6% better than the Legacy CUDA.

## Slide 84: Outline
Page Migration Techniques
  First-Touch page migration
  Range-Expansion to save TLB shootdowns
  BW balancing to stop excessive migrations
Results & Conclusions
HPCA-2015
Notes: In rest of the talk I will discuss 3 complementary page migration techniques that we experimented with in this work. Then we will see the results followed by conclusions.

## Slide 85: First-touch Page Migration
Chart: Throughput Relative to No Migration
| No Migration | First-Touch | Best Threshold | Legacy CUDA | Static Oracle
Throughput | 1 | 1.714 | 1.8919 | 1.8583 | 2.7444
Naive: Migrate pages that are touched
First-Touch migration approaches Legacy CUDA
1
1
CPU memory
GPU memory
First-Touch migration is cheap, no hardware counters required
1
1
1
1
HPCA-2015
Notes: Talk about it being similar to UVM but every access is not stalled because of copying. Instead we migrate a page after first-touch happens
The naive approach is to migrate pages as they are touched.
First-Touch migration policy is similar to Unified virtual memory model which copies data on-demand. However, in our policy migration happens after the first-access has been served from the CPU memory, hence first-accesses to a page are not stalled unlike UVM.
We also experimented with a variation of the first-touch page migration where we varied the number of accesses to a page before migrating it to the GPU memory. We show the average performance of the best threshold per application with Best-Threshold bar on the graph here.
To understand the performance gap between first-touch and static oracle let us look into the problems that first-touch migration encounters.
Explain other bars
Use First-Touch page migration further on
----- Meeting Notes (2/7/15 18:41) -----

## Slide 86: Problems with first-touch migration
TLB shootdowns may negate benefits of page migration
How to migrate pages without incurring shootdown cost?
CPU TLB
GPU TLB
VA
PA
VA
PA
V1
P1
V1
P1
…
…
Send
Invalidate
GPU
…
…
CPU
Migrate V1
Ack
Invalidate
P2
P2
Chart: Throughput Relative To No Migration
| backprop | needle | pathfinder
No overhead | 1.3374 | 1.66 | 1.1628
TLB shootdown | 1.0758 | 1.3454 | 0.92018
HPCA-2015
Notes: In this animation we will see how page migrations lead to stalls in the GPU pipeline, which directly impacts the GPU throughput.

## Slide 87: Pre-fetch to avoid tlb shootdowns
No shootdown cost for pre-fetched pages
Intuition: Hot virtual addresses are clustered
Pre-fetch pages before access by the GPU
Max
Min
Hot pages, consume 80% BW
Min
HPCA-2015
Notes: Hot pages are clustered in the virtual address space
We can see on the right in the graph where we have plotted virtual page addresses against their relative hotness, where hotness is the number of accesses to a page. The x-axis shows hottest on the left and coldest pages on the right. The y-axis shows their corresponding virtual addresses as they are laid out in the memory. We observed that the distinct red boxes correspond to the data structures in this application.
The pages that have not been accessed yet would not have any TLB mapping. Hence. Pre-fetching them before even they are accessed would not incur any TLB shootdown cost as there is no TLB mapping to invalidate. Another cool thing about this prefetching technique is that it is based on the virtual address space, so even if the physical layout of the addresses change, still we would be able to exploit the hotness locality present in the application data structures.

## Slide 88: Migration using Range-Expansion
Pre-fetch pages in spatially contiguous range
Chart: Throughput Relative to No Migration
| No overhead | TLB shootdown | No overhead | TLB shootdown | No overhead | TLB shootdown | backprop | needle | pathfinder
No range expansion | 1.3374 | 1.0758 | 1.66 | 1.3454 | 1.1628 | 0.92018
Range:128 | 0 | 0.006975 | 0 | 0 | 0 | 0.068356
X
X
X
X
CPU memory
GPU memory
X
Accessed, shootdown required
Pre-fetched, shootdown not required
HPCA-2015
Notes: With previous
Tell why furthest are migrated first?

## Slide 89: Migration using Range-Expansion
CPU memory
GPU memory
X
X
Chart: Throughput Relative to No Migration
| No overhead | TLB shootdown | No overhead | TLB shootdown | No overhead | TLB shootdown | backprop | needle | pathfinder
No range expansion | 1.3374 | 1.0758 | 1.66 | 1.3454 | 1.1628 | 0.92018
Range:16 | 0 | 0.17818 | 0 | 0.26766 | 0 | 0
Range:64 | 0 | 0.077485 | 0 | 0 | 0 | 0.073731
Range:128 | 0 | 0.006975 | 0 | 0 | 0 | 0.068356
X
Accessed, shootdown required
Pre-fetched, shootdown not required
Range-Expansion hides TLB shootdown overhead
Pre-fetch pages in spatially contiguous range
HPCA-2015
Notes: With previous
Tell why furthest are migrated first?

## Slide 90: Revisiting Bandwidth utilization
First-Touch + Range-Expansion aggressively unlocks GDDR BW
First-Touch migration
Excessive
migration
How to avoid excessive page migrations?
80
200
280
BW from CC
GPU Memory BW
Total System Memory BW
% of Migrated Pages to GPU Memory
Total Bandwidth (GB/s)
0
100
HPCA-2015
Notes: ----- Meeting Notes (2/3/15 10:09) -----
Let us revisit the BW util curve to see where we stand in terms of utilizing full system BW using previous policies

## Slide 91: Bandwidth balancing
Throttle migrations when nearing peak BW
Chart: Time
80
200
280
Total Bandwidth (GB/s)
First-Touch migrations
Excessive
migrations
Target
% of Migrated Pages to GPU Memory
0
100
70
Start
End
HPCA-2015
Notes: Static oracle page access ratio
Talk about that this ends up not utlizing the DDR BW and is away from the target line

## Slide 92: Bandwidth balancing
Throttle migrations when nearing peak BW
Chart: Time
80
200
280
Total Bandwidth (GB/s)
First-Touch migrations
Excessive
migrations
Target
% of Migrated Pages to GPU Memory
0
100
70
Start
End
HPCA-2015
Notes: Static oracle page access ratio

## Slide 93: Simulation Environment
Simulator: GPGPU-Sim 3.x
Heterogeneous 2-level memory
  GDDR5 (200GB/s, 8-channels)
  DDR4 (80GB/s, 4-channels)
GPU-CPU interconnect
  Latency: 100 GPU core cycles
Workloads:
  Rodinia applications [Che’IISWC2009]
  DoE mini apps [Villa’SC2014]
GDDR5
GPU
CPU
200 GB/s
80 GB/s
100 clks additional latency
DDR4
80 GB/s
HPCA-2015

## Slide 94: Results
Chart: Throughput Relative to No Migration
| backprop | bfs | cns | comd | kmeans | minife | mummer | needle | pathfinder | srad_v1 | xsbench | geo-mean
Legacy CUDA | 1.2456 | 3.0805 | 1.7139 | 1.4954 | 2.525 | 1.7619 | 2.7028 | 1.3362 | 0.91416 | 1.9765 | 3.1966 | 1.8583
First-Touch + Range Exp + BW Balancing | 1.3384 | 4.14 | 2.588 | 1.4709 | 2.67 | 0.97576 | 2.0535 | 1.7 | 1.0729 | 2.1574 | 3.5 | 1.9505
ORACLE | 2.4175 | 4.577 | 3.23 | 1.5124 | 2.9669 | 2.9856 | 3.3718 | 1.7567 | 1.65 | 2.5326 | 5.6126 | 2.7444
Static Oracle
HPCA-2015
Notes: Static Oracle

## Slide 95: Results
Chart: Throughput Relative to No Migration
| backprop | bfs | cns | comd | kmeans | minife | mummer | needle | pathfinder | srad_v1 | xsbench | geo-mean
Legacy CUDA | 1.2456 | 3.0805 | 1.7139 | 1.4954 | 2.525 | 1.7619 | 2.7028 | 1.3362 | 0.91416 | 1.9765 | 3.1966 | 1.8583
First-Touch + Range Exp + BW Balancing | 1.3384 | 4.14 | 2.588 | 1.4709 | 2.67 | 0.97576 | 2.0535 | 1.7 | 1.0729 | 2.1574 | 3.5 | 1.9505
ORACLE | 2.4175 | 4.577 | 3.23 | 1.5124 | 2.9669 | 2.9856 | 3.3718 | 1.7567 | 1.65 | 2.5326 | 5.6126 | 2.7444
First-Touch + Range-Expansion + BW Balancing outperforms Legacy CUDA
Static Oracle
HPCA-2015

## Slide 96: Results
Chart: Throughput Relative to No Migration
| backprop | bfs | cns | comd | kmeans | minife | mummer | needle | pathfinder | srad_v1 | xsbench | geo-mean
Legacy CUDA | 1.2456 | 3.0805 | 1.7139 | 1.4954 | 2.525 | 1.7619 | 2.7028 | 1.3362 | 0.91416 | 1.9765 | 3.1966 | 1.8583
First-Touch + Range Exp + BW Balancing | 1.3384 | 4.14 | 2.588 | 1.4709 | 2.67 | 0.97576 | 2.0535 | 1.7 | 1.0729 | 2.1574 | 3.5 | 1.9505
ORACLE | 2.4175 | 4.577 | 3.23 | 1.5124 | 2.9669 | 2.9856 | 3.3718 | 1.7567 | 1.65 | 2.5326 | 5.6126 | 2.7444
Streaming accesses, no-reuse after migration
Static Oracle
HPCA-2015
Notes: Migration is not able to keep up the pace with the access sequence

## Slide 97: Results
Chart: Throughput Relative to No Migration
| backprop | bfs | cns | comd | kmeans | minife | mummer | needle | pathfinder | srad_v1 | xsbench | geo-mean
Legacy CUDA | 1.2456 | 3.0805 | 1.7139 | 1.4954 | 2.525 | 1.7619 | 2.7028 | 1.3362 | 0.91416 | 1.9765 | 3.1966 | 1.8583
First-Touch + Range Exp + BW Balancing | 1.3384 | 4.14 | 2.588 | 1.4709 | 2.67 | 0.97576 | 2.0535 | 1.7 | 1.0729 | 2.1574 | 3.5 | 1.9505
ORACLE | 2.4175 | 4.577 | 3.23 | 1.5124 | 2.9669 | 2.9856 | 3.3718 | 1.7567 | 1.65 | 2.5326 | 5.6126 | 2.7444
Dynamic page migration performs 1.95x better than no migration
Comes within 28% of the static oracle performance
6% better than Legacy CUDA
Static Oracle
HPCA-2015
Notes: Nevertheless

## Slide 98: Conclusions
Developed migration policies without any programmer involvement
First-Touch migration is cheap but has high TLB shootdowns
First-Touch + Range-Expansion technique unlocks GDDR memory BW
BW balancing maximizes BW utilization, throttles excessive migrations
These 3 complementary techniques effectively unlock full system BW
HPCA-2015
Notes: So, to wrap up

## Slide 99: Thank you
HPCA-2015

## Slide 100: Effectiveness of Range-Expansion
Benchmark | Execution Overhead of TLB Shootdown | % Migrations Without Shootdown | Execution Runtime Saved
Backprop | 29.1% | 26% | 7.6%
Pathfinder | 25.9% | 10% | 2.6%
Needle | 24.9% | 55% | 2.75%
Mummer | 21.15% | 13% | 2.75%
Bfs | 6.7% | 12% | 0.8%
Range-Expansion can save up to 45% TLB shootdowns
HPCA-2015

## Slide 101: Data transfer ratio
Performance is low when GDDR/DDR ratio is away from optimal
HPCA-2015

## Slide 102: GPU workloads: BW Sensitivity
GPU workloads are highly BW sensitive
HPCA-2015

## Slide 103: Results
Chart: Throughput Relative to No Migration
| backprop | bfs | cns | comd | kmeans | minife | mummer | needle | pathfinder | srad_v1 | xsbench | geo-mean
Legacy CUDA | 1.2456 | 3.0805 | 1.7139 | 1.4954 | 2.525 | 1.7619 | 2.7028 | 1.3362 | 0.91416 | 1.9765 | 3.1966 | 1.8583
First-Touch | 1.0758 | 3.2007 | 2.4264 | 1.4611 | 2.4112 | 0.84084 | 2.0334 | 1.3454 | 0.91859 | 2.1512 | 2.9239 | 1.7206
First-Touch + Range Exp | 1.3384 | 3.2264 | 2.588 | 1.4709 | 2.4863 | 0.97576 | 2.0305 | 1.5699 | 1.0729 | 2.1581 | 3.1239 | 1.8596
First-Touch + Range Exp + BW Balancing | 1.3384 | 4.14 | 2.588 | 1.4709 | 2.67 | 0.97576 | 2.0535 | 1.7 | 1.0729 | 2.1574 | 3.5 | 1.9505
ORACLE | 2.4175 | 4.577 | 3.23 | 1.5124 | 2.9669 | 2.9856 | 3.3718 | 1.7567 | 1.65 | 2.5326 | 5.6126 | 2.7444
Oracle
Dynamic page migration performs 1.95x better than no migration
Comes within 28% of the static oracle performance
6% better than Legacy CUDA
HPCA-2015