## Slide 1: Paper Discussion for 18-742
Kevin Hsieh
Sep 9, 2014

## Slide 2: Paper to Discuss (1/3)
Seshadri et al., "The Dirty-Block Index", ISCA 2014.
  Introducing a cache organization to achieve better performance and cost.
Ausavarungnirun et al., "Staged Memory Scheduling: Achieving High Performance and Scalability in Heterogeneous Systems", ISCA 2012.
  Introducing a memory controller which is simpler and works better in heterogeneous system.
Chang et al., "Improving DRAM Performance by Parallelizing Refreshes with Accesses", HPCA 2014.
  Introducing a few parallelism schemes for refresh commands.

## Slide 3: Background and Problem
Traditionally, the metadata of the cache is organized according to cache block (or cache line)
  Each cache block has a corresponding cache metadata, which maintains all the attributes for this cache block (valid, dirty, tag address, etc.)
  It’s intuitive, simple, and scalable.
However, there are shortcomings
  All metadata query is relatively expensive
  It makes some cache improvement difficult to implement
    DRAM-Aware Writeback [TR-HPS-2010-2]
    Bypassing Cache Lookups [HPCA 2003, PACT 2012]

## Slide 4: Block-Oriented Metadata Organization (Vivek’s Slide)
Valid Bit
Dirty Bit
(Writeback cache)
Sharing Status
(Multi-cores)
Error Correction
(Reliability)
V
Block Address
D
Sh
Repl
ECC
Replacement Policy
(Set-associative cache)

## Slide 5: DRAM-Aware Writeback (Vivek’s slide)
Last-Level Cache
Memory Controller
DRAM
Channel
Write Buffer
1. Buffer writes and flush them in a burst
2. Row buffer hits are faster and more efficient than row misses
Row Buffer
Virtual Write Queue [ISCA 2010], DRAM-Aware Writeback [TR-HPS-2010-2]

## Slide 6: DRAM-Aware Writeback (Vivek’s slide)
Dirty Block
Proactively write back
all other dirty blocks from
the same DRAM row
Last-Level Cache
Significantly increases the DRAM write row hit rate
Get all dirty blocks of DRAM row ‘R’
Memory Controller
R
R
R
R
R
Virtual Write Queue [ISCA 2010], DRAM-Aware Writeback [TR-HPS-2010-2]

## Slide 7: Query to Tag Store for a DRAM row
Tag
Index
Offset
Address
Row offset
A DRAM row can be distributed into a lot of sets.
It is very inefficient if we want to query all cache blocks for a certain DRAM row
Tag Store

## Slide 8: The Dirty-Block Index
Key Idea
  Decouple dirty bits from main tag store and indexed them by DRAM row. This separated structure makes query for dirty bit (especially in terms of DRAM row) much more efficient.
V
Block Address
D
Sh
Repl
ECC
DRAM Address
V
D
D
D
D
…...
D
Tag Store
DBI

## Slide 9: Benefit of DBI
DRAM-aware writeback
  With DBI, a single query can know all the dirty block in a DRAM row
  No more tag store contention
Bypassing cache lookups
  The idea was to bypass cache lookup if it’s very likely to miss. However it must not bypass dirty cache block.
  With DBI, it can check the dirty status much faster to seamlessly enable this optimization.
Reducing ECC overhead
  The idea was only dirty block requires error correction, others only requires detection.
  With DBI, it’s much easier to track the error correction codes

## Slide 10: Operation of DBI

## Slide 11: Evaluated Mechanism
Baseline (LRU, Least Recently Used)
TA-DIP (Thread-aware dynamic insertion policy)
DAWB (DRAM aware writeback)
VWQ (Virtual write queue)
CLB (cache lookup bypass)
DBI
  No optimization
  +DAWB
  +CLB
  +AWB+DBI

## Slide 12: System Configuration

## Slide 13: Effect on Writes and Tag Lookups (Vivek’s slide)
Chart: Normalized to Baseline
| Memory Writes | Write Row Hits | Tag Lookups
Baseline | 1 | 1 | 1
DAWB | 1.14 | 2.51 | 1.95
DBI
+AWB
+CLB
DBI+Both | 1.17 | 2.31 | 0.86
DBI achieves almost all the benefits of DAWB
with significantly lower tag store contention

## Slide 14: System Performance (Vivek’s slide)
Chart: System Performance
| 1-Core | 2-Core | 4-Core | 8-Core
Baseline | 1 | 1.46 | 1.8 | 2.62
DAWB | 1.13 | 1.73 | 2.29 | 3.17
DBI
+AWB
+CLB
DBI+Both | 1.13 | 1.8 | 2.43 | 3.36
13%
0%
23%
4%
35%
6%
28%
6%
Reduced tag store contention due to DBI
translates to significant performance improvement

## Slide 15: Area and Power
Bit cost reduction of cache
Power increase in cache (not including memory)

## Slide 16: DBI design consideration
Major design considerations
  DBI size (number of total blocks tracked by DBI, α, in ratio of total cache blocks)
  DBI granularity (number of blocks tracked by a single DBI entry)
  DBI replacement policy
    5 policies evaluated, better policy gives better performance

## Slide 17: Conclusion
Dirty-Block Index is a new cache organization, which decouples dirty bit information from main tag store. All dirty bits are indexed by DRAM row at a separate, much smaller store.
By doing so, it’s much faster to
  Query all dirty bits for a DRAM row (makes AWB much easier)
  Query whether certain cache line is dirty (makes CLB much easier)
  Organize correction bits for dirty cache line (hybrid ECC)
Evaluation results showed
  6% performance improvement over best previous mechanism
  8% overall cache area reduction (with ECC)

## Slide 18: Open Discussion
What are the major strengths?
What are the major weakness?
Any other ideas from this paper?

## Slide 19: My 2 cents - Strength
This paper proposed a novel cache organization which can improve both performance and cost of cache at the same time.
The analysis of design consideration was comprehensive and solid. The authors not only mentioned most of major considerations, but also rigorously evaluated the sensitivity of them (granularity, size, replacement policy)

## Slide 20: My 2 cents - Weakness
The DBI eviction induces some unnecessary write back traffics when handling write request. The worst case is all DBI-associated cache lines have to be written back.
The evaluation was done on a system with L1/L2/L3 caches and specific 2-core, 4-core, 8-core workloads. Some analysis should be done to prove it works on different memory hierarchy and different workload/core combinations.
One of the major weakness of DBI is that its structure is limited to DRAM row (though it can be adjusted by granularity). If the dirty lines are sparsely distributed in different DRAM row, this structure will be inefficient and keep thrashing DBI cache.

## Slide 21: My 2 cents - Ideas
Investigate the possibility of moving other bits out of tag store, such as cache coherency bits or even ECC bits.
Try if DRAM-oriented cache structure works better, not just dirty bits. We can have smaller α and a vector to manage cache lines by DRAM row tag address.
Evaluate the density of DRAM rows in cache for various workloads. Also evaluate DBI with different memory hierarchies to show whether it can be applied to different systems.

## Slide 22: Paper to Discuss (2/3)
Seshadri et al., "The Dirty-Block Index", ISCA 2014.
  Introducing a cache organization to achieve better performance and cost.
Ausavarungnirun et al., "Staged Memory Scheduling: Achieving High Performance and Scalability in Heterogeneous Systems", ISCA 2012.
  Introducing a memory controller which is simpler and works better in heterogeneous system.
Chang et al., "Improving DRAM Performance by Parallelizing Refreshes with Accesses", HPCA 2014.
  Introducing a few parallelism schemes for refresh commands.

## Slide 23: Background and Problem
In multi-core CPU-GPU systems, the memory requests from GPUs can overwhelm that from CPUs.
  The nature of GPU makes it be able to issue much more outstanding requests than CPU
  GPU is much more (4x-20x) memory-intensive than CPU
The memory controller with centralized request buffer will become very complex and costly for such system.
  Unless it has a lot of buffer, it can’t see enough pending requests from CPUs as buffers are overwhelmed by those from GPU
  But a lot of buffer can make the design very complicated

## Slide 24: Prior Memory Scheduling Schemes
FR-FCFS (First ready, First Come First Serve) [Rixner+, ISCA’00]
  Totally memory throughput driven
  Can lead to serious fairness problem
PAR-BS (Parallelism-aware Batch Scheduling) [Mutlu and Moscibroda, MICRO’07]
  Batches request based on arrival time, oldest first.
  Minimize fairness issue
ATLAS (Adaptive per-Thread Least- Attained-Service memory scheduling) [Kim+, HPCA’10]
  Prioritize applications with least memory service. But high memory intensity application can be slowed down significantly.
TCM (Thread Cluster Memory Scheduling) [Kim+, MICRO’10]
  Cluster threads into high or low memory-intensity buckets and apply different approaches
Most schemes need certain visibility to requests from all applications to be effective

## Slide 25: Introducing the GPU into the System (Rachata’s slide)
GPU occupies a significant portion of the request buffers
  Limits the MC’s visibility of the CPU applications’ differing memory behavior  can lead to a poor scheduling decision
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
Req
Req
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Notes: When GPU is introduced into the system <click>, because the GPU is memory-intensive, requests from cores contend heavily with request from the GPU, as you can see from this example
<click>
The memory-intensive GPU application will send a lot of request to the memory request buffer
<click>
As a result, some of the requests are unable to be inject into the request buffer, as illustrated by this blue request from core 2.
<click>
When only some of the memory requests can inject into the request buffer, memory scheduler cannot observe full applications behavior. This can lead to a poor scheduling decision
<click… transition>
A naïve solution to this problem is to increase the size of the monolithic request buffer…

## Slide 26: The performance of memory schedulers in CPU-GPU systems
Results showed it’s highly dependent on buffer size

## Slide 27: Problems with Large Monolithic Buffer (Rachata’s slide)
A large buffer requires more complicated logic to:
  Analyze memory requests (e.g., determine row buffer hits)
  Analyze application characteristics
  Assign and enforce priorities
This leads to high complexity, high power, large die area
Memory Scheduler
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
More Complex Memory Scheduler
Notes: <However (continue from the previous slide) a large buffer requires more complicated logic to analyze memory requests (for example, to determine if each request is a row hit), analyze application characteristics, assign and enforce priorities.
<click>
This leads to high complexity, high power, and large die area
<click, the big Mem sched. Appears>
<click, transition>
Our goal in this project is…

## Slide 28: Key Idea: Staged Memory Scheduler
Decouple the memory controller’s three major tasks into three significantly simpler structures
Stage 1: Group requests by locality
  The requests to the same row from the same source are grouped as a batch
  No out-of-order batch
Stage 2: Prioritize inter-application requests
  Schedule batches based on SJF (shortest job first) or RR (round-robin)
  The probability of applying SJF is based on a configurable parameter p
  Always pick from the head of FIFO from each source
Stage 3: Schedule low-level DRAM commands
  Issue batches to DRAM, no reorder

## Slide 29: SMS: Staged Memory Scheduling (Rachata’s slide)
Memory Scheduler
Core 1
Core 2
Core 3
Core 4
To DRAM
GPU
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Batch Scheduler
Stage 1
Stage 2
Stage 3
Req
Monolithic Scheduler
Batch Formation
DRAM Command Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Notes: With these key observations, we will show how we can decouple a monolithic schedulers into a simpler design through <click> stage 1, the batch formation, <click> stage 2, the batch scheduler, <click> stage 3, the DRAM command scheduler

## Slide 30: Stage 1: Batch Formation Example (Rachata’s slide)
Core 1
Core 2
Core 3
Core 4
Row A
Row B
Row B
Row C
Row D
Row D
Row E
Row F
Row E
Batch Boundary
To Stage 2 (Batch Scheduling)
Row A
Time window expires
Next request goes to a different row
Stage 1
Batch Formation
Notes: I will show an example of how the batch formation work
<click>
When there is an incoming requests that access the same row as an earlier requests. (This yellow request that accesses row B), they will be batched. And a batch will become ready to be scheduled under two conditions. First, it will become ready when a subsequent request wants to access a different row, in this case row C. The earlier request to row B will become ready to be scheduled.
A batch can become ready to be scheduled under another condition, which is when the time window for the batch formation expires, which is shown in this example in core 1. this batch formation will happen across all the cores including the GPU.

## Slide 31: Stage 2: SJF vs RR
Aside from simplicity, SMS provided another major advantage: Configurable probability p for SJF
SJF (Shortest Job First)
  Good for low memory intensive applications (mostly from CPUs)
  The price is overall system bandwidth
RR (Round Robin)
  Good for high memory intensive applications (mostly from GPUs)
  The price is the fairness of low memory intensive applications
Make it as a configurable parameter provides flexibility. The system can adjust p to reach best tradeoff between GPU performance and CPU fairness.

## Slide 32: Putting Everything Together (Rachata’s slide)
Current Batch Scheduling Policy
SJF
Current Batch Scheduling Policy
RR
Batch Scheduler
Bank 1
Bank 2
Bank 3
Bank 4
Core 1
Core 2
Core 3
Core 4
Stage 1:
Batch
Formation
Stage 3: DRAM Command Scheduler
GPU
Stage 2:
Notes: In this example, the system consist of 4 CPU cores and a GPU, and the color represent a row the request wants to access. Similar color means these requests want to access the same row.
In the batch formation stage, memory requests that access the same row will be batched.
<click>
One criteria that a batch becomes ready to be scheduled is when the next request is going to a different row, as illustrated in this example at core 2 and core 3. <click click>
Another criteria is when the timeout for the batch formation expires.
This batching process will happen across all cores including the GPU
<click>
<click> and how the batch scheduler will select one of these front batch to send to <click> the DRAM command scheduler.
The scheduler can either use a shortest job poilcy
<click> which will pick this purple request because it is from an application with the fewest number of requests.
Or a round-robin policy
<click>
Whenever the bank is ready to schedule a next request. DRAM command scheduler will schedule the requests in an in-order manner.
<click>
Now that I told you about how SMS works, let me tell you about the complexity of SMS
<click … transition>

## Slide 33: Evaluation
Power and Area (in 110nm, compared to FR-FCFS)
  66% less area
  46% less static power
Performance Metrics
  GPU Weight means how important GPU performance is for a system
  If it’s important, SMS can use smaller p value to reach best overall performance

## Slide 34: Results – CPU Speedup
SMS0.9 worked very well for low memory intensity applications, but not so well for high ones.
SMS0 performed inversely.

## Slide 35: Results – GPU frame rate
SMS0.9 was the worst in terms of GPU frame rate.
But SMS0 gave a comparable GPU frame rate with FR-FCFS.

## Slide 36: Results – Combined CPU and GPU speed up
If sticking with a constant p, SMS may be good at some GPU weight but very bad at the others
If choosing p wisely, SMS can reach best combined CPU+GPU speedup

## Slide 37: Conclusion
Prior memory scheduling scheme can’t handle CPU-GPU systems effectively because the memory intensity from GPU is much higher.
The proposed SMS (Stage Memory Scheduling) decouples the memory scheduler into 3 stages
  Batch formation, batch scheduling, DRAM command scheduling
Evaluation result
  66% less area
  46% less static power
  Flexible parameter p to reach optimal tradeoff between fairness and system throughput (or best combined CPU+GPU performance, according to system goal)

## Slide 38: Open Discussion
What are the major strengths?
What are the major weakness?
Any other ideas from this paper?

## Slide 39: My 2 cents - Strength
Presented an important challenge to memory controller scheduling with very good data analysis.
The discussion of SMS rationale was pretty thorough. It’s the key to make the mechanism much simpler than previous schedulers.
The experimental evaluation was pretty solid. It included a lot of metrics and also evaluated on the sensitivity of parameters of SMS.
The proposed scheduler was simpler and more flexible than state-of-art ones. The rigorous evaluation also showed that SMS had better potential to fulfill different needs

## Slide 40: My 2 cents - Weakness
The tunable parameter p provided a flexibility to fulfill different needs (either fairness or performance). However that can be a problem as an incorrect parameter can cause severe performance or fairness degradation.
This memory scheduler was very simple but gave up some important optimization opportunity. For example, it gave up cross-source row buffer locality. It didn’t try to prevent row conflict either.
The workload used unrelated workloads between CPU and GPU for evaluation, which may not represent the system performance goal very well.

## Slide 41: My 2 cents - Ideas
Research on inter-dependent, state-of-art benchmark for CPU-GPU multicore system. Use it to validate state-of-art memory controllers and maybe come out a more efficient scheduling mechanism.
Research other mechanism which can do better tradeoff between performance and fairness by considering more optimization opportunities. It shouldn’t limit to CPU-GPU only and should take more system configurations into account.

## Slide 42: Paper to Discuss (3/3)
Seshadri et al., "The Dirty-Block Index", ISCA 2014.
  Introducing a cache organization to achieve better performance and cost.
Ausavarungnirun et al., "Staged Memory Scheduling: Achieving High Performance and Scalability in Heterogeneous Systems", ISCA 2012.
  Introducing a memory controller which is simpler and works better in heterogeneous system.
Chang et al., "Improving DRAM Performance by Parallelizing Refreshes with Accesses", HPCA 2014.
  Introducing a few parallelism schemes for refresh commands.

## Slide 43: Background – DRAM Refresh
DRAM stores data in capacitors, which leaks charge over time
  So all DRAM cells need to be refreshed for a certain period of time (tREFI)
Because all cells need to be refreshed, the time to do refresh (tRFC) depends on the capacity of DRAM cells
tRefPeriod (tREFI): Remains constant
tRefLatency (tRFC): Varies based on DRAM chip density (e.g., 350ns)
Timeline
Read/Write: roughly 50ns
*From Kevin’s slide

## Slide 44: Refresh Overhead: Performance

## Slide 45: Refresh Problem
During refresh, DRAM is not accessible
  All bank refresh (REFab): all banks can’t be accessed
  Per bank refresh (REFpb): the refreshing bank can’t be accessed
As DRAM capacity grows, the refresh overhead will take too much time and makes performance unacceptable
  Even with per bank refresh, it still takes too much time
  Besides, the total time spent on REFpb is more than REFab
    tRFCpb*banknum > tRFCab
    That is because all bank refresh are done on multiple banks simultaneously.

## Slide 46: Idea one - DARP
DARP - Dynamic Access Refresh Parallelization
  Currently, the order of per bank refresh is round-robin and controlled by DRAM chip.
  The key idea of DARP is to let memory controller fully control which bank to refresh
Out-of-Order Per-Bank Refresh
  Memory controller can do optimal scheduling based on the command queue
  It can schedule the refresh to the banks with least pending commands (within timing constraint)
Write-refresh Parallelism
  Most memory controller will have burst write mode to save read-write turnaround overhead
  Memory controller can schedule more refresh during burst write mode, as write latency generally won’t be at critical path of system performance.

## Slide 47: 1) Out-of-Order Per-Bank Refresh (Kevin’s slide)
Bank 1
Bank 0
Our mechanism: DARP
Refresh
Read
Timeline
Bank 1
Bank 0
Refresh
Read
Refresh
Read
Baseline: Round robin
Refresh
Read
Saved cycles
Delayed by refresh
Saved cycles
Read
Request queue (Bank 0)
Request queue (Bank 1)
Read
Reduces refresh penalty on demand requests by refreshing idle banks first in a flexible order

## Slide 48: 2) Write-Refresh Parallelization (Kevin’s slide)
Proactively schedules refreshes when banks are serving write batches
Timeline
Bank 1
Bank 0
Turnaround
Refresh
Read
Read
Baseline
Delayed by refresh
Write
Write
Write
Write-refresh parallelization
Timeline
Bank 1
Bank 0
Read
Turnaround
Read
Write
Write
Write
Refresh
1. Postpone refresh
Refresh
2. Refresh during writes
Saved cycles
Avoids stalling latency-critical read requests by refreshing with non-latency-critical writes

## Slide 49: Idea two - SARP
SARP – Subarray Access Refresh Parallelization
  Each subarray has its own row buffer.
  With some modification, we can parallelize refresh and access of different subarrays in the same bank

## Slide 50: Our Second Approach: SARP (Kevin’s slide)
Subarray Access-Refresh Parallelization (SARP):
  Parallelizes refreshes and accesses within a bank
Very modest DRAM modifications: 0.71% die area overhead
Bank 7
Bank 1
Bank 0
…
Subarray
Bank I/O
Timeline
Subarray 1
Subarray 0
Bank 1
Data
Refresh
Refresh
Read
Read

## Slide 51: Evaluation
Evaluated schemes
  REFab : All bank refresh (baseline)
  REFpb : Per-bank refresh
  Elastic : Try to schedule refresh when memory idle
  DARP : The first idea, out-of-order per-bank refresh
  SARPpb : The second idea, subarray level parallism and works on REFpb
  DSARP : The combination of DARP and SARP
  No REF : Ideal case, no refresh required

## Slide 52: Results (1/3)
When memory capacity grows to 32Gb, the benefit of DARP is decreasing
  That is because the refresh time is too long and no way to hide it any more
But with SARP, the performance gain is increasing with memory capacity
  That is because SARP parallelize access and refresh to subarray level.

## Slide 53: Results (2/3)
REFpb can’t improve too much when memory capacity grows
Surprisingly, DSARP can be almost as good as ideal no-refresh memory

## Slide 54: Results (3/3)

## Slide 55: Conclusion
To mitigate the deteriorating DRAM refresh overhead, this paper proposed two mechanisms to parallelize refresh with access
DARP enables memory controller to fully control the order and timing of per-bank refresh
SARP enables memory controller to issue access and refresh to different subarrays in the same bank
The performance improvement is significant and consistent, and close to ideal no-refresh memory
  7.9% for 8Gb DRAM
  20.2% for 32Gb DRAM
  With only 0.71% DRAM die area cost

## Slide 56: Open Discussion
What are the major strengths?
What are the major weakness?
Any other ideas from this paper?

## Slide 57: My 2 cents - Strength
The statement of the refresh problem was very clear with a good background introduction. The explanation of all-bank refresh and per-bank refresh gave enough details to understand the optimizations.
The proposed mechanism tackled the refresh problem with several novel ideas on DRAM architecture modification. The idea of parallelizing and fined-grained control on refreshes provided promising direction to mitigate refresh overhead.
The evaluation mechanisms and results were solid. The best among them is the comparison to ideal non-refresh case, which showed how good DARP and SARP are. The sensitivity analysis on workloads, core count, timing, and DRAM architecture was comprehensive, too.

## Slide 58: My 2 cents - Weakness
SARP can make the scheduling of refresh very complicated. This paper didn’t discuss how complicated it can be or how to do it efficiently.
This paper didn’t discuss in detail about the scheduling policy of REFab and REFpb. Elastic refresh should be applied to REFpb, too. By considering this, the performance improvement may not be that significant
The energy data didn’t include memory controller, where significant complexity was added by DARP and SARP. The algorithm of out-of-order per-bank refresh may cost too much energy, as it has to make a complex decision on every cycle

## Slide 59: My 2 cents - Ideas
As an extensive work, the energy of memory controller could be a concern. If it is, it will be interesting to find a better algorithm to exploit DARP/SARP with competitive power consumption.
  Or better refresh scheduling to achieve better performance.
Another idea is to research more aggressive parallelism.
  Is it possible to parallel REFpb with another REFpb?
  Is it possible to optimize the DRAM timing with more understand on its limitation?